OMB Approval 2700-0042

|  | 1. CONTRACT ID CODE | PAGE OF PAGES |
| --- | --- | --- |
| AMENDMENT OF SOLICITATION/MODIFICATION OF CONTRACT |  | 1 | 4 |
| 2. AMENDMENT/MODIFICATION NO. | 3. EFFECTIVE DATE | 4. REQUISITION/PURCHASE REQ. NO. | 5. PROJECT NO. (If applicable) |
| 1 | See Block 16C |  |  |
| 6. ISSUED BY | CODE |  | 7. ADMINISTERED BY (If other than Item 6) | CODE |  |
| NASA Procurement Office Code DA20 John C. Stennis Space Center Stennis Space Center, MS 39529-6000 ATTN: Rob Harris (robert.harris@ssc.NASA.gov, (228)-688-3862) | Same as block #6 |
| 8. NAME AND ADDRESS OF CONTRACTOR (No. Street, county, State and ZIP: Code) | (() | 9A. AMENDMENT OF SOLICITATION NO. |
|  |  | 13-SSC-O-02-37 |
| TO ALL PROSPECTIVE BIDDERS | X | 9B. DATED (SEE ITEM 11) |
|  |  | July 3, 2002 |
|  |  | 10A. MODIFICATION OF CONTRACT/ORDER NO. |
|  |  | 10B. DATED (SEE ITEM 13) |
| CODE | FACILITY CODE |  |  |
| 11. THIS ITEM ONLY APPLIES TO AMENDMENTS OF SOLICITATIONS |
| The above numbered solicitation is amended as set forth in Item 14. The hour and date specified for receipt of Offers is extended, is not extended. Offers must acknowledge receipt of this amendment prior to the hour and date specified in the solicitation or as amended, by one of the following methods:(a) By completing Items 8 and 15, and returning one (1) copy of the amendment; (b) By acknowledging receipt of this amendment on each copy of the offer submitted; or (c) By separate letter or telegram which includes a reference to the solicitation and amendment numbers. FAILURE OF YOUR ACKNOWLEDGMENT TO BE RECEIVED AT THE PLACE DESIGNATED FOR THE RECEIPT OF OFFERS PRIOR TO THE HOUR AND DATA SPECIFIED MAY RESULT IN REJECTION OF YOUR OFFER. If by virtue of this amendment you desire to change an offer already submitted, such change may be made by telegram or letter, provided each telegram or letter makes reference to the solicitation and this amendment, and is received prior to the opening hour and data specified. |
| 12. ACCOUNTING AND APPROPRIATION DATA (If required) |
| N/A |
| 13. THIS ITEM APPLIES ONLY TO MODIFICATIONS OF CONTRACTS/ORDERS, IT MODIFIES THE CONTRACT/ORDER NO. AS DESCRIBED IN ITEM 14. |
| (() | A. THIS CHANGE ORDER IS ISSUED PURSUANT TO: (Specify authority) THE CHANGES SET FORTH IN ITEM 14 ARE MADE IN THE CONTRACT ORDER NO. IN ITEM 10A. |
|  | B. THE ABOVE NUMBERED CONTRACT/ORDER IS MODIFIED TO REFLECT THE ADMINISTRATIVE CHANGES (such as changes in paying office, appropriation date, etc.) SET FORTH IN ITEM 14, PURSUANT TO THE AUTHORITY OF FAR 43.103(b). |
|  | C. THIS SUPPLEMENTAL AGREEMENT IS ENTERED INTO PURSUANT TO AUTHORITY OF: |
|  | D. OTHER Specify type of modification and authority) |
| E. IMPORTANT: Contractor is required to sign this document and return _1_ copy to the issuing office. |
| 14. DESCRIPTION OF AMENDMENT/MODIFICATION (Organized by UCF section headings, including solicitation/contract subject matter where feasible.) SEE CONTINUATION PAGES |
| Except at provided herein, all terms and conditions of the document referenced in Item 9A or 10A, as heretofore changed, remains unchanged and in full force and effect. |
| 15A. NAME AND TITLE OF SIGNER (Type or print) | 16A. NAME AND TITLE OF CONTRACTING OFFICER (Type or print) |
|  | James D. Huk II Contracting Officer |
| 15B. CONTRACTOR/OFFEROR | 15C. DATE SIGNED | 16B. UNITED STATES OF AMERICA | 16C. DATE SIGNED |
| ________________________________________________ (Signature of person authorized to sign) |  | BY _____________________________________________ (Signature of Contracting Officer) |  |

NSN 7540-01-152-8070		30-105	STANDARD FORM 30 (REV. 10-83)

PREVIOUS EDITION UNUSABLE		Computer Generated	Prescribed by GSA			FAR (48 CFR) 53.243

13-SSC-O-02-37

Amendment 1

Page 2 of 4

A.  The purpose of this amendment is answer contractor’s questions, change the “required delivery

schedule” of line items 0001 and 0002, and extend the bid opening date to July 31, 2002.  Solicitation

13-SSC-O-02-37 is hereby amended as follows:

B.  The following contractor questions were received and the following responses are hereby provided:

1.	Question:  Is ASME BPV “Code Stamping” required on pressure vessel?

Answer:    No

2.	Question:  Paragraph 4.0:  Filter Assembly Materials -   “All pressure containing piece parts shall

be machined forgings.”,  Is bar stock and/ or pierced seamless tubing allowable?

Answer:   Not for the housing or external pressure boundaries.  But ok on internal piece parts.

3.	Question:  Filter Data Sheet #GF-10A2283-GH – Housing Material allows use of  Type TPXM-11

(Nitronic 40) material, Filter Data Sheet #GF-10A2284-GN and #GF-10A2285-GN do

not.  Is this an oversight OR IF NOT can Nitronic 40 be used for these applications as

well?

Answer:    Nitronic 40 is allowed.

- Question:  Design Requirements Para 3.0 page 3 states:  “All welds and brazed joints shall be

accessible to visual inspection and shall be 100% dye penetrant inspected…..”. It is not

desirable to dye penetrant inspect filter elements due to the resultant contamination of

the element and subsequent difficulty in attaining the required cleanliness level of the

deliverable part.

Answer:    The specification requires that the design allow for precision cleaning for LOx service.

The filter design shall enable the removal of all contamination including dye penetrant.

However, alternate methods of weld inspection may be proposed for our consideration.

- Question:  3.2.1 Wire Cloth – Table 1, Wire Cloth as defined per Table 1; i.e., 30x30 Mesh and

.0065” wire diameter as well as 60x60 Mesh and .0060” wire diameter are not available

in a twilled weave pattern configuration.  Manufacturers state that it is not feasible to

produce a  twilled weave pattern at a ratio above 1.3 in terms of opening

dimension/wire diameter; i.e., 30x30x0065 wire diameter would equate to

0.0268/.0065 = 4.12 .  Therefore, both Mesh requirements, 30x30 and 60x60 will have

to be plain square weave configurations.  Also, the 60x60 does not appear to be

available at a 0.0060 wire diameter; it is available at a 0.0065 wire diameter.

Answer:  Plain square weave maybe acceptable provided our concerns with regards to individual

wires shifting around within the weave pattern are addressed.  Using plain square weave

with larger wire diameter is acceptable provided the operating pressure drop conforms to

the specification.

13-SSC-O-02-37

Amendment 1

Page 3 of 4

- Question:  3.2.2 Support Structure  - “The support structure members, screen retainer ring,

supporting wire meshes, and fine wire mesh shall be brazed at all points of

contact……”.  Request option to allow for Resistance and/or TIG welding as applicable

in lieu of brazing.

Answer:  Ok to weld.

- Question:  3.2.4  Screen Retainer Supporting Ring – “If used, the wire cloth retainer support ring

shall be mechanically connected to the screen retainer support ring.  Assume that

“mechanically connected” means that it could also be resistance and/or TIG welded.

Answer:  Yes

- Question:  The solicitation table shown on page 2 identifies Item 0004 as a 4 inch size where as

the specification says it is a 6 inch size. We assume the specification is correct.

Answer:  6 inch is the correct size.

- Question:  Specification 110GK-GMF10 and 110GK-GMH9 data sheets have an asterisk

indicating the manufacture should fill in the "Operating Pressure Drop for each of the

filters/Screen Assemblies. The specification shows a "Maximum allowed" pressure

drop already for the filters covered by these documents. Does Stennis expect the

manufacture to enter the estimated pressure drop for information only?

Answer:  Yes.

- Question:  It appears the contraction and expansion losses from the Connections with no

allowance for screen loss will exceed some of the maximum allowed pressure drop

requirements listed on the data sheets. Does the "Operating Pressure Drop" asterisk

refer to the element only pressure drop?

Answer:  No, the pressure drop was intended to be for inlet to outlet.  However, provide your

predicted delta pressure for us to evaluate.

- Question:  Specification 110GK-GMF10 indicates a Maximum Allowed Housing I.D. of 4.25" for

the gaseous nitrogen filters. We are concerned with the annulus around the element

given this limitation on the I.D. If we make the element smaller the pressure drop

increases even more. Is the 4.25" dimension a hard requirement?

Answer:  No.  Internal volume needs to be minimized as much as possible, especially annulus

region around the element.  Tapering the ID of the housing to minimize internal volume

is an option.  The housing ID should 6.25” or less.

13-SSC-O-02-37

Amendment 1

Page 4 of 4

12.  Question:  Maximum allowed housing I.D. is stated as 4.25”.  Good design practices demand that the

element ID be not less than the outlet line bore.  In this case the line bore is 3.825” per

ACK1 piping specification.  Allowing for a support design suitable for the collapse

pressure, adequate wire area, external protective sleeve and required inlet flow area

around the element, we anticipate that 6.25” ID would be required?

Answer:  Internal volume needs to be minimized as much as possible, especially annulus region

around the element.  Tapering the ID of the housing to minimize internal volume is an

option.  The housing ID should 6.25” or less.

13.  Question:  Request the required delivery of items 1 & 2 be NLT 105 days after issuance of a contract?

Answer:  Approved.  Contract clause 52.211-9, is hereby changed to reflect that line items 0001 and

0002, Required Delivery Schedule, be changed from as reads “84 days” to read: “105 days”.

(Note this change in required delivery schedule only affects line item 0001 and 0002.)

C.  SF1449, Block 8, titled “Offer Due Date/Local Time”, is hereby changed from “July 24, 2002…” to

Read: “July 31, 2002 Not Later Than 3:00pm”.

D.  All other terms and conditions remain the same.