#### 1981 Cessna 182R – N5524H

# Preflight Cabin

- Pilot’s Operating Handbook Available

- Parking Brake	Set

- Hobbs & Tach	Check

- Fire Extinguisher	Charged

- Squawk Sheet	Check

- Documents	AROW in airplane

- Control/Avionics Lock	Remove

- Avionics Power Switch	Off

- Ignition Switch	Off

- Master Switch	On

- Flaps	Full Down

- Fuel Quantity Indicators	Check Quantity

- Low-Vacuum Warning Light	Check On

- Avionics Power Switch	On

- Avionics Cooling Fan	Check Audibly

- Avionics Power Switch	Off

- Pitot Heat 	Check

- Lights	Check

- Master Switch	Off

- Alternate Static	Off

- Fuel Selector	Both

Preflight Empennage

- Baggage Door	Check for security and lock

- Rudder Gust Lock	Remove

- Tail Tie-Down	Disconnect

- Control Surfaces	Check

Preflight Right Wing trailing edge

- Right Flap	Check

- Right Aileron	Check

- Right Wingtip & Light	Check

# Preflight Right Wing

- Wing Tie Down	Disconnect

- Right Fuel Vent	Check Clear

- Right Main Wheel Tire & Brake	Check

- Right Fuel Sump(s)	Drain

- Right Fuel Quantity	Visually Check

- Fuel Filler Cap	Secure, vent unobstructed

Nose

- Static Sources	Check (Both sides)

- Prop & Spinner	Check

- Landing Lights	Check

- Carburetor Air Filter	Check

- Nose Wheel, Strut & Tire	Check

- Nose Tie-Down	Disconnect

- Engine Oil Filler Cap	Check Secure

- Engine Oil Dipstick	9-12 Quarts

- Fuel Strainer Drain Knob	Pullout to Drain

- Windscreen	Check/Clean

# Preflight Left Wing

- Left Main Wheel Tire & Brake	Check

- Left Fuel Sump(s)	Drain

- Left Fuel Quantity	Visually Check

- Fuel Filler Cap	Secure

# Preflight Left Wing Leading Edge

- Pitot Tube Cover	Remove

- Left Fuel Vent	Check Clear

- Stall Warning	Check

- Wing Tie-Down	Disconnect

- Left Wingtip & Light	Check

# Preflight Left Wing Trailing Edge

- Left Aileron	Check

- Left Flap	Check

Before Starting Engine

- Preflight Inspection	Complete

- Passenger Brief	Complete

- Seats / Belts / Shoulder Harness	Adjust and Lock

- Fuel Selector Valve	Both

- Brakes	Test & Set

- Avionics Power Switch	Off

Caution

The avionics power switch must be OFF during engine start to prevent possible damage to avionics.

- Electrical Equipment	Off

- Circuit Breakers	Check In

- Autopilot (If installed)	Off

10. Cowl Flaps	Open

##### PASSENGER BRIEF

- Seat Belts / Shoulder Harness

- Personal Electronic Devices off

- Air Vents / Comfort

- Fire Extinguisher Location / Operation

- Emergency Procedures & Exits

##### MISSION BRIEF

- Mission Objective

- Destination, WX, Route, Alt, ETE

- NOTAMS

- Crew Coordination & CRM

- Sterile Cockpit Procedures

- Cockpit Layout

- Intercom & Radio Usage

- Seats, Seatbelts, Doors

- Emergency Action & Equipment

# Starting Engine

- Prime	As Required (Up to 3)

- Carburetor Heat	Cold

- Throttle	Open ½ Inch

- Propeller	High RPM

- Mixture	Rich

- Propeller Area	Clear

- Master Switch	On

- Ignition Switch	Start

Note

If engine has been over primed, start with throttle ¼ to ½ open.  Reduce throttle to idle when engine fires.

- Throttle	800 to 1000 RPM

- Oil Pressure	Check

- Starter	Check Disengaged

- Avionics Power Switch	On

- Beacon & Nav Lights	On

- Taxi Lights	As Required

- Flaps	Up

- Transponder	TEST/STBY

- Radios	On

- ATIS / AWOS	Copy

- Altimeter	 Set (Verify Within 75’ of Fld Elev.)

- Clearance Delivery/Ground Control	Contact

Taxi

- Brakes	Test

- Heat / Vents / Defrost	As Required

- Attitude Indicator	Verify Proper Operation

- Turn Coordinator	Verify Proper Operation

- H.I. & Compass	Verify Proper Operation

- Fuel Selector Valve	Check & Set to Both

Before Takeoff - Run-Up

- Parking Brake	Set

- Seats / Belts / Shoulder Harness	Check Secure

- Cabin Doors	Closed and Locked

- Flight Controls	Free & Correct

- Flight Instruments & H.I.	Check & Set

Caution

The directional indicator should be rechecked during engine run-up to avoid compass deviation errors, which may occur below 1200 RPM.

- Fuel Quantity	Check

- Mixture	Rich

- Fuel Selector Valve	Recheck Both

- Elevator & Rudder Trim	Set for Takeoff

- Cowl Flaps	Recheck Open

- Throttle	1700 RPM

- Magnetos	Max Drop 150 RPM

- Carb Heat	Check for RPM Drop

- Propeller	Cycle

- Suction Gauge	Check

- Engine Inst & Ammeter	Check

- Throttle	Idle Check, then 800 to 1000 RPM

- Throttle Friction Lock	Adjust

- Strobe Lights/Pulse Lights

(If installed)	As Desired

- Radios / Transponder	Set

- Autopilot (If Installed)	Off

- Flaps set for Takeoff	0°-20°

- Primer	In & Locked

- Carb Heat	Cold

- Electric Trim (If Installed)	Test

- Takeoff Briefing	Complete

- Doors & Windows	Latched

- Lights	Set

- Transponder	Set to ALT

- Time	Record

- Parking Brake	Release

Takeoff

- Flaps	0°-20°

- Carb Heat	Cold

- Power	Full Throttle and 2400 RPM

- Mixture	Full Rich or Max Power

- Engine Instruments	In Green

- Rotate	50 KIAS

- Normal Climb Speed	80 KIAS

- Short Field T.O.	20° Flaps / 59 KIAS Until Clear

- Soft Field T.O	20° Flaps / Ground Effect ASAP

6.  Flaps	Retract (above 70 KIAS)

Enroute Climb

- Airspeed	85-95 KIAS Normal

- Throttle	23 Inches or Full (whichever is less)

- Propeller	2400 RPM

- Fuel Selector	Both

- Mixture	Full Rich or Max Power

- Cowl Flaps	Recheck Open

- Engine Instruments	Check

Cruise

- Power	15-23 Inches & 2100-2400 RPM (no more than 75% power).

- Elevator & Rudder Trim	Adjust

- Mixture	Lean

- Cowl Flaps	As required

- Engine Instruments / Fuel	Check

- Heading Indicator (H.I.).	To Compass

- Lights	As Required

- Flight Plan	Activate as Required

Descent

- Heading Indicator.	To Compass

- Altimeter	Set

- Fuel Selector	Both

- Lights	As Required

- Engine Instruments	Check

- Mixture	Enrich

- Power / Carb Heat	As Required

- Cowl Flaps	Closed

- Wing Flaps	As Desired

Before Landing Harness	Secure

- Seat, Seat Belts, Shoulder Harness 	Adjust and Lock

- Fuel Selector	Both

- Mixture	Rich

- Propeller	High RPM

- Carb Heat	On

- Autopilot (If installed)	Off

- Airspeed	70-80 KIAS  (Flaps Up)

- Airspeed	60-70 KIAS (Flaps Down)

- Trim	Adjust

10.Touchdown	Main Wheel First

11. Landing Roll	Lower Nose Wheel Gently

## 12. Braking	Minimum required

## Short Field Landing

- Airspeed	70-80 KIAS  (Flaps Up)

- Flaps	40º (below 95 KIAS)

- Airspeed	Maintain 61 KIAS

- Trim	Adjust

- Power	Reduce to idle as obstacle

is cleared

- Touchdown	Main Wheels First

- Brakes	Apply Heavily

- Flaps	Retract for Max brake effectiveness.

## Balked Landing

- Power	Full Throttle  & 2400 RPM

- Carb Heat	Cold

- Flaps	Retract to 20°

- Climb Speed	55 KIAS

- Flaps	Retract Slowly (above 70 KIAS)

- Cowl Flaps	Open

After Landing (Clear of Runway)

- Flaps	Up

- Carb Heat	Cold

- Cowl Flaps	Open

- Lights	As Required

- Transponder	STBY & 1200

- Mixture	Lean

- Pitot Heat	Off

# Securing Aircraft

- Parking Brake	Set

- Throttle	Idle

- Avionics Power & Switches	Off

- Magnetos	Check for Ground

- Mixture	Idle Cut Off

- Ignition & Master Switch	Off

- Control/Avionics Lock	Install

- Parking Brake 	 Off

- Cowl Flaps 	Closed

- Fuel Selector	Left or Right

- Hobbs & Tach	Record

- Aircraft	Secured & Locked

- Flight Plan	Closed

# V Speeds and Specs

- X-Wind (Max Demo’d)	15 Knots

- Vr  Rotation Speed	50 KIAS

- Vx  Best Angle Climb	59 KIAS

- Vy  Best Rate Climb	81 KIAS

- Vso  Stall w/ Flaps	40 KIAS

- Vs1  Stall w/o Flaps	50 KIAS

- Best Glide (3100 Lbs)	76 KIAS

- Best Glide (2600 Lbs)	70 KIAS

- Best Glide (2000 Lbs)	61 KIAS

- Va  Max Abrupt Ctrl (3100 Lbs)	111 KIAS

- Va  Max Abrupt Ctrl (2600 Lbs)	102 KIAS

- Va Max Abrupt Ctrl (2000 Lbs)	61 KIAS

- Vno  Max Structural Cruise	143 KIAS

- Vne  Never Exceed	179 KIAS

- Vfe  10° Flaps	140 KIAS

- Vfe  10°-Full Flaps	95 KIAS

General...

- EMERGENCY	121.50

- Unicom	122.70-122.80-122.95

123.00-123.05

- Multicom	122.90 (CTAF)

- Flight Service	122.20 (Most Common) 122.10-122.60-123.60

- Flight Watch	122.00

- Air to Air	122.75-122.85-123.45

Transponder Codes

- 1200	VFR

- 7500	HIJACK

- 7600	LOST COMMS

- 7700	EMERGENCY

# Aircraft Information

- Gross Weight Capacity

3100 (Takeoff)	2950 (Landing)

- Engine	Continental  O-470-U

- Max Power	230 BHP

- Fuel Type	100LL (Blue)

- Fuel Capacity (Standard)	88 Gal Usable

- Oil Type	Aeroshell 15W-50

- Oil Capacity	12 Qts (Minimum 9)

- Electrical	24-28 Volt / 60 Amp

- Tire Pressure	Nose-49 PSI / Main-42 PSI

This checklist is a guide to coordinate Pilot Operating Handbook and STC data applicable to this particular aircraft only.  The applicable Pilot Operating Handbook and STC installations remain the official documentation for this aircraft.

The pilot in command is responsible for complying with all items in the Pilot Operating Handbook and applicable STCs.

I certify this checklist has been reviewed for accuracy.

______________________________________

Wing Director of Maintenance              Date

# Text boxes

Warning

When turning on the master switch, using an external power source, or pulling the propeller through by hand, treat the propeller as if the ignition switch were on.  Do not stand, nor allow anyone else to stand, within the arc of the propeller, since a loose or broken wire, or a component malfunction, could cause the propeller to rotate.