Measurement Method:  Single-end deflection of 56 inch long roller-ski bar, with center fulcrum and one lightly-constrained end.

Data:

Free-end

Force

(pounds)

Free-end

Displacement

(inches)

Midpoint

Force

(pounds)

Rel. Mid-point

Displacement

| (inches) |
| --- |
| 0 | 0 | 0 | 0 |
| 20 | .125 | 40 | .0625 |
| 40 | .250 | 80 | .125 |
| 60 | .375 | 120 | .1875 |

Mid-point stiffness: 640 pounds/inch (56 inch fulcrums).

Scaling: 	X= (L/L0)^2 *F/K0,  where

X= Free-end deflection relative to a free-end fulcrum

L= Distance between free-end fulcrums.

F= Force applied to the mid-point of the beam.

K0= Beam stiffness with free-end fulcrums at L= L0.

Note: A beam with periodic fulcrums is 2x stiffer than one having free-ends with the same fulcrum spacing.

D20 Summary:

| Magnet weight: | 14000 pounds. |
| --- | --- |
| # of supports: | 28 wheels. |
| Weight/wheel (average): | 500 pounds/wheel. |
| Contact pressure (.01” x .25”) | 200 Kpsi (avg). |
| Distance between wheels: | 4 inches. |
| Stiffness (scaled to 4”, periodic): | 250 pounds/mil. |
| Wheel displacement (500 pounds): | 0.002 inches. |
| Tolerance required (1500 pounds): | 0.004 inches. |
| Wall tolerance (as-found): | 0.020 |
| Conforming stiffness (1500 pounds): | 50 pounds/mil. |