| x.x.x. Oxomethyl (formyl) radical |  | 2597-44-6 |
| --- | --- | --- |
| HC=O (2A') |  | CS ((ext = 1) |
| (fH((298.15 K) = 42.3 ± 1.0 kJ mol-1 |  | (fH((0 K) = 41.9 ± 1.0 kJ mol-1 |
| C(p(298.15 K) = 34.590 J K-1 mol-1 |  | H((298.15 K) – H((0 K) = 10.001 kJ mol-1 |
| S((298.15 K) = 224.355 J K-1 mol-1 |  | p( = 100 000 Pa (1 bar) |

| Literature Data for the Enthalpy of Formation at 298.15 K |
| --- |
| (fH(/kJ mol-1 | Authors and Reference | Method a | Comments |
| Measurements |
| 41.8 ± 0.8 | Chuang et al. (1987) | KPD | (1a) |
| 42.5 ± 0.5 | Terentis and Kable (1996) | KEPD | (1b) |
| 44.29 ± 0.43 | Bercera et al. (1997) | KFP | (1c) |
| Computations |
| 38.9 ± 7.1 | Zachariah et al. (1996) | BAC-MP4 | (1d) |
| 37.81 | Janoschek (2001) | G3MP2B3 | (1e) |
| 42. | Martin (2001) | W2 | (1f) |
| 42.3 ± 0.8 | Marenich and Boggs (2003) | AI | (1g) |
| Reviews and Evaluations |
| 43.51 ± 8. | Chase (1970) | CDE-TN | (1h) |
| 37.24 ± 5. | McMillen and Golden (1982) | CDE | (1i) |
| 42. ± 5. | Gurvich et al. (1991) | CDE | (1j) |
| 41.7 ± 0.8 | Berkowitz et al. (1994) | CDE | (1k) |
| 42 ± 4 | Tsang (1996) | TT-A | (1l) |
| 41.8 ± 4.2 | JPL (1997) | TT-A | (1m) |
| 41.3 | Atkinson et al. (2000) | TT-A | (1n) |
| 42. ± 0.8 | Burcat (2001) | TT-A | (1o) |
| 43.1 | Kerr (2002) | TT-U | (1p) |
| 43.51 | NIST WebBook(2005) | TT-A | (1q) |

a	KFP: Kinetic flash photolysis reactions; KPD: Kinetic photodissociation; KEPD : Kinetics of Exciting and Population Distribution Change; CDE: Critical data evaluation; TT-A: Annotated tabulation of thermodynamic data; TT-U: Unannotated tabulation of thermodynamic data.

b	The quoted value was either not given explicitly by the author(s) or it was recalculated using auxiliary thermochemical values that differ from those used by the original authors; see individual comments for additional details.

c	The uncertainty was either not given explicitly by the original author(s) or it has been modified; see individual comments for further explanations.

Comments on the Enthalpies of Formation

(1a)  The enthalpy of formation of the formyl radical.was obtained from the measurement of the threshold for the onset of photodissociation of CH2O.

(1b)	The CHO radical was produced from the photolysis of H2CO very near to the energy threshold. Rovibronically resolved excitation of the formaldehyde molecule is followed by high resolution laser-induced fluorescence excitation spectroscopy of the nascent HCO fragment.

(1c)	CHO was generated by flash photolysis of acetaldehyde in order to obtain rate constants for its bimolecular reactions with HI and HBr. Combination with known kinetic data on the reverse reaction leads to the thermodynamic estimate of (fH(298 = 44.29 kJ mol-1 by the third law method. By the second law method the value obtained is 42.76 ± 0.85 – 45.27 ± 0.81 kJ mol-1.

(1d)	Ab initio G2 BAC-MP4 calculations for the C/H/O/F system of molecules and radicals. (fH0 = 38.91 kJ mol-1, the same value as for 298 K.

(1e)	G3(MP2)//B3LYP ab initio calculation. The uncertainty quoted in the table corresponds to twice the average absolute deviation for the G2/97 test set of 0.99 kcal mol-1, which corresponds roughly to 2( or ~95% confidence limits. The (fH(0 = 37.45 kJ mol-1.

(1f)	The value is the W2 calculation. The W1 value is 40.9 kJ mol-1.

(1g)	Ab initio coupled cluster CCSD(T) calculations of equilibrium geometries, anharmonic force fields, and thermodynamic properties of HCO and CHO radicals. The research was performed to elucidate the data for the present report.

(1h)	The values of Chase from 1970 are reprinted in the 1998 edition of JANAF, and these are quoted by NIST.

(1i)	The value is based on old kinetic estimates of Benson.

(1j)	Critical evaluation of all data before 1989. This value is based on two papers of J.G. Calvert J.Chem Phys 29, 954 (1958) and J. Am. Chem. Soc. 30, 1313 (1958) with J.T. Gruver.

(1k)	Based on the bond energy given by Chuang et al.1 D(H-CHO) = (fH(298(HCO)=9.99 kcal mol-1 and the enthalpy of formation of formaldehyde given by Gurvich10 (fH(298(CH2O)=25.98 kcal mol-1.

(1l)	Tsang accepts the value of Gurvich.10

(1m)	Round off in kcal mol-1 of Gurvich’s10/Tsang12 value.

(1n)	Attkinson quotes the values of Becera3 and Chuang.1

(1o)	Thermochemical database for combustion quotes Jacox17 for vibrations and Gurvich10 for the enthalpy of formation.

(1p)	No details given.

(1q)	The data of JANAF8 and Tsang12  are quoted.

### Preferred Value of the Enthalpy of Formation

(fH((298.15 K) = 42.3 ± 1. kJ mol-1

(fH((0 K) = 41.9 ± 1. kJ mol-1

The computational research of Marenich and Boggs7 was undertaken in order to evaluate among the experimental estimated and calculated values quoted here. Their value is within the error limits of the experimental values of Terentis and Kable2 and Chuang.1 This decision is backed up by the former estimates of Gurvich,10 Berkowitz11 and by the recent calculation of Martin.6

| Geometry (distance in Å, angles in degrees)(2a) |
| --- |
| Z-Matrix |  | Cartesian Coordinates |
|  |  |  | x | y | z |
| C |  | C | 0.062574 | 0.589085 | 0.000000 |
| O | 1 1.1827 | O | 0.062574 | -0.593577 | 0.000000 |
| H | 1 1.1277 2 123.660 | H | -0.876042 | 1.214106 | 0.000000 |
| Moments of Inertia in the Electronic Ground State(2b) |
| IA = 1.13968 ( 10-47 kg m2 | IB = 18.68676( 10-47 kg m2 | IC = 19.9521( 10-47 kg m2 |
| Bond Distances (10-10 m) (2b) |
| r(C ( H): 1.117 r(C – O): 1.174 a(HCO): 124.6( (i don’t like removing info, but we don’t usually include these) |
| Vibrational Wavenumbers in the Electronic Ground State ((i / cm-1) (2c) |
| 1097 | 1885 | 2465 |  |  |  |
| Ground State Anharmonicity Constants(2c) |
| x11 = −12.703 | x12 = −1.741 | x13 = −4.409 | x22 = −10.346 |
| x23 = −6.610 | x33 = −124.441 | α1A=2.041 | α2A=−0.0938 |
| α3A= −1.509 | α1B=0.00530 | α2B=−0.0119 | α3B= 0.000372 |
| α1C= −0.00544 | α2C=−0.0110 | α3C=−0.00349 |  |

.

Heat Capacity C(p, Entropy S( and Enthalpy Increment [H((T) -H((0 K)] (2d)

| T/K | C(p(T) (J K-1 mol-1) | S((T) (J K-1 mol-1) | [H((T) -H((0 K)] (kJ mol-1) |
| --- | --- | --- | --- |
| 150 | 33.35 | 201.09 | 4.988 |
| 200 | 33.54 | 210.70 | 6.659 |
| 250 | 34.00 | 218.23 | 8.347 |
| 298.15 | 34.68 | 224.28 | 10.000 |
| 300 | 34.71 | 224.49 | 10.064 |
| 350 | 35.60 | 229.91 | 11.821 |
| 400 | 36.61 | 234.72 | 13.626 |
| 500 | 38.85 | 243.13 | 17.397 |
| 600 | 41.2 | 250.40 | 21.398 |
| 700 | 43.4 | 256.9 | 25.626 |
| 800 | 45.4 | 262.9 | 30.066 |
| 900 | 47.2 | 268.3 | 34.699 |
| 1000 | 48.8 | 273.4 | 39.504 |
| 1500 | 54.5 | 294.4 | 65.473 |
| 2000 | 58.1 | 310.6 | 93.667 |
| 2500 | 61.1 | 323.8 | 123.468 |
| 3000 | 63.8 | 335.2 | 154.687 |

* The pressure at which this table was calculated is p = 101325 Pa.

7-Constant NASA Polynomial

CHO Formyl Rad    IU5/03C  1.H  1.O  1.   0.G   200.000  6000.000     29.01804 1

3.92001542E+00 2.52279324E-03-6.71004164E-07 1.05615948E-10-7.43798261E-15    2

3.65342928E+03 3.58077056E+00 4.23754610E+00-3.32075257E-03 1.40030264E-05    3

-1.34239995E-08 4.37416208E-12 3.87241185E+03 3.30834869E+00 5.08749163E+03    4

9-Constant NASA Polynomial

CHO Formyl Radical  IUPAC Task Group for Selected Radicals

3 IU5/03 C   1.00H   1.00O   1.00    0.00    0.00 0   29.0180400      42300.000

50.000   200.000 7 -2.0 -1.0  0.0  1.0  2.0  3.0  4.0  0.0        10000.000

1.909054361D+02-6.505083940D+00 4.007960170D+00 1.976299520D-03-2.595595158D-05

1.244398772D-07-1.867688014D-10 0.000000000D+00 3.911446940D+03 3.943182620D+00

200.000  1000.000 7 -2.0 -1.0  0.0  1.0  2.0  3.0  4.0  0.0        10000.000

-9.217964230D+02 2.491028603D+01 4.021945390D+00-2.474162328D-03 1.235893571D-05

-1.190013708D-08 3.838988660D-12 0.000000000D+00 3.765811090D+03 4.423377420D+00

1000.000  6000.000 7 -2.0 -1.0  0.0  1.0  2.0  3.0  4.0  0.0        10000.000

2.077147739D+06-8.433987270D+03 1.602453231D+01-5.394244960D-03 1.859525520D-06

-2.779868187D-10 1.457229515D-14 0.000000000D+00 5.509247840D+04-8.065557680D+01

##### Comments on Molecular Data, Heat Capacity, Entropy and Enthalpy Increment

(2a)  The geometry coordinates were calculated by Janoschek.5

(2b) The moments of inertia are equivalent to A0=24.562 cm-1, B0=1.498 cm-1, and C0=1.403 cm-1, and the bond distances were calculated by Marenich and Boggs.7

(2c) The ab initio CCSD(T)/vqz calculated wavenumbers and anharmonicity constants are of Marenich and Boggs.7 The experimental vibrational wavenumbers reported by Jacox17 are Te =0(2), ωe = 2435 cm-1, 1868 cm-1, and 1087 cm-1.  Serrano-Andres et al. calculated with the CAPT2 optimized geometry method for ground state wavenumbers 2713, 1877, 1107 cm-1 and –134, −13, −15, 3, −7, −5 for the x11 x22 x33 x12 x13 x23 respectively. The newer ones,  ab initio G3MP2B3 wavenumbers, were calculated (unscaled) by Janoschek:5 668 cm-1, 1948 cm-1, and 1130 cm-1.

(2d) The NASA polynomials were calculated with McBride and Gordon’s PAC99 program. The values were taken from the tables of Marenich and Boggs7 since they used direct summation methods. The standard heat capacity and entropy values reported in the "Thermochemical Database for Combustion"15 are C(p,298 = 32.459 J mol-1  K-1,  S(298 = 195.638 J mol-1 K-1.

# Endnotes

M. C. Chuang, M. F. Foltzand, and C. B. Moore, J. Chem. Phys. 87, 3855 (1987).

A. C. Terentis and S. H. Kable, Chem. Phys. Lett. 258, 626 (1996).

R. Becerra, I. W. Carpenter, and R. Walsh, J. Phys. Chem. A 101, 4185 (1997).

M. R. Zachariah, P. R. Westmoreland, .R. Burges Jr., W. Tsang, and C. F. Melius, J. Phys. Chem. 100, 8737 (1996).

R. Janoschek, calculations for this database,.Oct. 2001.

S. Parthiban and J. M. L. Martin, J. Chem. Phys. 114, 6014 (2001).

A. V. Marenich and J .E. Boggs, J. Phys. Chem 107 2343 (2003).

M. W. Chase Jr. NIST-JANAF Thermochemical Tables, Fourth Edition, J. Phys. Chem. Ref. Data, Monograph 9. 1998.

D. F. McMillen and D. M. Golden, Ann. Rev. Phys. Chem. 33, 493 (1982).

L. V. Gurvich, I. V. Veyts, and C. B. Alcock, Thermodynamic Properties of Individual Substances, 4th Edition, Vol. 1 & 2, Hemisphere, New York, 1989.

J. Berkowitz, G. B. Ellison, and D. Gutman, J. Phys. Chem. 98, 2744 (1994).

W. Tsang., Heats of Formation of Organic Free Radicals by Kinetic Methods in Energetics of Organic Free Radicals, Martinho Simoes, J.A.; Greenberg, A.; Liebman, J.F., eds., Blackie Academic and Professional, London, p.22-58 (1996).

W. B. DeMore, S. P. Sander, D. M. Golden, R. F. Hampson, M. J. Kurylo, C. J. Howard, A. R. Ravishankara, C. E. Kolb, and M. J. Molina, Chemical Kinetics and Photochemical Data for Use in Stratospheric Modeling, Evaluation No. 12, JPL Publication 97-4, NASA and JPL (January 15, 1997).

R. Atkinson, D. L. Baulch, R. A. Cox, R. F. Hampson, Jr., J. A. Kerr, M. J. Rossi, and J. Troe, J. Phys. Chem. Ref. Data 29, 167 (2000).

A. Burcat, Third Millennium Ideal Gas and Condensed Phase Thermochemical Database for Combustion, TAE Report No.867, Technion, Haifa, 2001. (see also ftp://ftp.technion.ac.il./pub/supported/aetdd/thermodynamics).

J. A. Kerr, CRC Handbook of Chemistry and Physics, 83rd Edition, 2002. CRC Press, Boca Raton.

W. G. Mallard and P. J. Linstrom, Eds., NIST Chemistry WebBook, NIST Standard Reference Database Number 69, February 2000, National Institute of Standards and Technology, Gaithersburg MD, 20899  (http://webbook.nist.gov/chemistry/).

(a) D. M. Golden and S. W. Benson, Chem. Rev. 69, 125 (1969); (b) S. W. Benson and H. E. O’Neal, in Free Radicals, Wiley, N.Y.  2:273, (1973).

L. Serrano-Andres, N. Fosberg, and P. A. Malmqvist, J. Chem. Phys. 108, 7202 (1998).

B. McBride and S. Gordon: “Computer Program for Calculating and Fitting Thermodynamic functions” Report NASA-RP-1271 (1992).