July 22, 1994

Contract #TW0592

SPECIAL STANDARD SPECIFICATION

SECTION 10800-S

TOILET ACCESSORIES

Page

PART 1 - GENERAL

1.01	Description Of Work	2

1.02	References	2

1.03	Submittals	3

1.04	Quality Assurance	3

1.05	Project Conditions	3

PART 2 - PRODUCTS

2.01	Manufacturers	3

2.02	Materials	3

2.03	Paper Towel Dispensers	4

2.04	Toilet Tissue Dispensers	4

2.05	Waste Receptacles	4

2.06	Combination Towel Dispenser/Waste Receptacle Units	5

2.07	Grab Bars	5

2.08	Sanitary Napkin Vendors	5

2.09	Sanitary Napkin Disposal Units	5

2.10	Soap Dispensers	6

2.11	Seat Cover Dispensers	6

2.12	Miscellaneous Items Fabrication	6

2.13	Fabrication	6

PART 3 - EXECUTION

3.01	Installation	76

3.02	Adjusting And Cleaning	76

SPECIAL STANDARD SPECIFICATION

SECTION 10800

TOILET ACCESSORIES-S

PART 1 - GENERAL

1.01	DESCRIPTION OF WORK

A.	Toilet accessory items included in this section:

1.	Paper towel dispenser

2.	Toilet tissue dispenser

3. 	Waste receptacle

4.	Combination towel dispenser/waste receptacle unit

5. 	Grab bars

6. 	Sanitary napkin vendor

7. 	Sanitary napkin disposal unit

8. 	Soap dispenser

9. 	Seat cover dispenser

B.	Mounting heights are specified in the Toilet Accessory Schedule or shown on interior elevations.

C.	Related Section:  Mirrored glass is specified in Division 8, Section "Glass and Glazing".

1.02	references

A.	American Iron and Steel Institute (AISI)

B.	American Society of Testing and Materials (ASTM)

A153	Specification for Zinc Coating (Hot-Dip) on Iron and Steel Hardware

A366	Specification for Steel Sheet, Carbon, Cold-Rolled, Commercial Quality

A527	Specification for Steel Sheet, Zinc-Coated (Galvanized) by the Hot-Dip Process, Commercial Quality

B16	Specification for Free-Cutting Brass Rod, Bar, and Shapes for Use in Screw Machines

B19	Specification for Cartridge Brass Sheet, Strip, Plate, Bar, and Disks (Blanks)

B30	Specification for Copper-Base Alloys in Ingot Form

B456	Specification for Electrodeposited Coatings of Copper Plus Nickel Plus Chromium and Nickel Plus Chromium

1.03	SUBMITTALS

Product Data:  Submit product data for each toilet accessory item shown on drawings or schedule, including details of construction relative to materials, dimensions, gages, profiles, method of mounting, specified options, and finishes.

1.04	QUALITY ASSURANCE

A.	Inserts and Anchorage:  Furnish inserts and anchoring devices as recommended by the manufacturer.

B.	Single-Source Responsibility:  Provide products of same manufacturer for each type of accessory unit and for units exposed to view in same areas.

1.05	PROJECT CONDITIONS

Coordination:  Coordinate accessory locations, installation, and sequencing with other work to avoid interference and to assure proper installation, operation, adjustment, cleaning, and servicing of toilet accessory items.

PART 2 - PRODUCTS

2.01	MANUFACTURERS

Available Manufacturers:  Subject to compliance with requirements, manufacturers offering toilet accessories that may be incorporated in the work include, but are not limited to, the following:

A & J Washroom Accessories

American Specialties, Inc.

Bobrick Washroom Equipment, Inc.

Bradley Corporation

2.02	MATERIALS

A.	Stainless Steel:  AISI Type 302/304, with polished No. 4 finish, 0.034 inch (22 gage) minimum thickness, unless otherwise indicated.

B.	Brass:  Leaded and unleaded, flat products, ASTM B19; rods, shapes, forgings, and flat products with finished edges, ASTM B16, castings, ASTM B30.

C.	Sheet Steel:  Cold-rolled, commercial quality ASTM A366, 0.040 inch (20 gage) minimum, unless otherwise indicated.  Surface preparation and metal pretreatment as required for applied finish.

D.	Galvanized Steel Sheet:  ASTM A527, G60.

E.	Chromium Plating:  Nickel and chromium electro-deposited on base metal, ASTM B456, Type SC 2.

F.	Baked Enamel Finish:  Factory-applied, gloss white, baked acrylic enamel coating.

G.	Galvanized Steel Mounting Devices:  ASTM A153, hot-dip galvanized after fabrication.

H.	Fasteners:  Screws, bolts, and other devices of same material as accessory unit or of galvanized steel where concealed.

2.03	PAPER TOWEL DISPENSERS

Surface-Mounted Towel Dispensers:  Fabricate of stainless steel with hinged front equipped with tumbler lockset.  Provide pierced slots at sides as refill indicator.

Capacity:  Not less than either 300 C-fold or 500 multi-fold paper towels without need for special adapters.

2.04	TOILET TISSUE DISPENSERS

A.	Roll-In-Reserve Dispenser:  Fabricate of stainless steel for mountings indicated below, sized to store and dispense either 4-1/2-inch (110 mm)  or 5-inch (130 mm) diameter core tissue rolls, with reserve roll placed in service by automatic release or by action of manual release bar.  Hinge front of unit with pivot hinge.

1.	Mounting:  Surface-mounted, concealed anchorage.

2.	Mounting:  Partition-mounted, designed to service two adjacent toilet compartments, two rolls for each.

B.	Double-Roll Dispenser:  Size to accommodate two separate rolls of core-type tissue to 5-inch (130 mm) diameter.

Mounting:  Surface-mounted, concealed anchorage.

2.05	WASTE RECEPTACLES

Open-Top, Semi-Recessed Waste Receptacle:  Fabricate of stainless steel with seamless exposed flange, removable receptacle with seamless exposed walls, 4-inch (100 mm) projection from wall surface and  hemmed edges.  Furnish heavy-duty vinyl removable liner, secured to receptacle at not less than 4 points by means of grommets, stainless steel hooks; 12-gallon (45 L) capacity.

2.06	COMBINATION TOWEL DISPENSER/WASTE RECEPTACLE UNITS

Recessed Unit with Projecting Receptacle:  Stainless steel combination unit fabricated for nominal 4-inch (100 mm) wall depth and with continuous seamless 1-inch (25 mm) wide wall flange.  Provide towel compartment in upper portion of unit, designed to dispense not less than 400 C-fold or 700 multi-fold paper towels; double-panel door with continuous piano hinge.  Waste receptacle in lower portion of unit provided with reusable heavy-duty vinyl liner, minimum 12-gallon (45 L) capacity.

2.07	GRAB BARS

Stainless Steel Type:  Provide grab bars with wall thickness not less than 0.050 inch (18 gage) and as follows:

A.	Mounting:  Concealed, manufacturer's standard flanges and anchorages, adequate to support a 250 lb (113 kg) load applied in any direction for a period of five minutes.

B.	Clearance:  1-1/2 inches (38 mm) clearance between wall surface and inside face of bar.

C.	Gripping Surfaces:  Smooth, satin finish.

D.	Heavy-Duty Size:  Outside diameter of 1-1/2 inches (38 mm).

2.08	SANITARY NAPKIN VENDORS

General:  Fabricate cabinet of stainless steel, not less than 0.034 inch (22 gage), all welded construction.  Provide door of seamless stainless steel, minimum 0.050 inch (18 gage), with returned edges.  Provide identification reading "Napkins" and "Tampons"; brand name advertising is not allowed.  Capacity not less than 15 napkins and 72 tampons.

A.	Mounting:  Fully recessed type for nominal 6-inch (150 mm) thick wall.

B.	Mounting:  Semi-recessed type, with stainless steel collar to extend unit from nominal 4-inch (100 mm) thick wall cavity.

C.	Mounting:  Surface-mounted type for CMU wall.

D.	Operation:  No coin (free) operation.

2.09	SANITARY NAPKIN DISPOSAL UNITS

A.	Partition-Mounted Dual-Access Type:  Fabricate of stainless steel equipped with adjustable flanges to permit partition mounting to service two toilet compartments.  Provide self-closing door and all-welded stainless steel receptacle removable from one side.

B.	Surface-Mounted Type:  Fabricate of stainless steel with seamless exposed walls, tightly self-closing top cover and locking bottom panel with continuous stainless steel piano hinge.

2.10	SOAP DISPENSERS

Liquid Soap Dispenser, Wall-Mounted:  Furnished by Sandia National Laboratories (SNL).

2.11	SEAT COVER DISPENSERS

A.	Surface-Mounted Type:  Fabricate of stainless steel with concealed opening at bottom for filling; capacity not less than 250 seat covers.

B.	Partition-Mounted, Dual-Access Type:  Fabricate of stainless steel and provide adjustable 1-inch (25 mm) wide seamless wall flanges for installation in cutout in toilet partition to service two compartments.  Provide hinged access door for servicing from one side.

2.12	MISCELLANEOUS ITEMS

A.	Mop and Broom Holder/Utility Shelf:  Combination unit with 0.05-inch (18-gage), Type 304, stainless steel shelf with 1/2-inch returns, 0.062-inch (16-gage) support brackets for wall mounting.  Provide 0.062-inch (16-gage) stainless steel hooks for wiping rags on front of shelf, together with spring-loaded, rubber hat, cam-type mop/broom holders; 1/4-inch-diameter stainless steel drying rod suspended beneath shelf.  Provide unit 36 inches long and complete with four mop/broom holders and three hooks.

B.	Double-Prong Robe Hook:  Heavy-duty satin finished stainless steel double-prong robe hook; rectangular wall bracket with backplate for concealed mounting.

C.	Towel Bar:  24-inch-long, satin-finished, Type 304 stainless steel tubular (3/4-inch-square) bar and rectangular end brackets.  Provide galvanized backplates for concealed mounting.

2.1312	FABRICATION

A.	Surface-Mounted Toilet Accessories:  Except where otherwise indicated, fabricate units with tight seams and joints, exposed edges rolled.  Hang doors or access panels with continuous stainless steel piano hinge.  Provide concealed anchorage wherever possible.

B.	Recessed Toilet Accessories:  Except where otherwise indicated, fabricate units of all welded construction, without mitered corners.  Hang doors or access panels with full-length stainless steel piano hinge.  Provide anchorage that is fully concealed when unit is closed.

PART 3 - EXECUTION

3.01	INSTALLATION

A.	Install toilet accessory units in accordance with manufacturers' instructions, using fasteners appropriate to substrate and recommended by manufacturer of unit.  Install units plumb and level, firmly anchored in locations and at heights indicated.

B.	Install SNL-furnished soap dispensers in locations indicated on drawings.

3.02	ADJUSTING AND CLEANING

A.	Adjust toilet accessories for proper operation and verify that mechanisms function smoothly.  Replace damaged or defective items.

B.	Clean and polish all exposed surfaces in strict accordance with manufacturer's recommendations after removing temporary labels and protective coatings.

END OF SECTION