Silage/Feedstock Storage Area Evaluation

Not to be used for vertical silos and silo bags.

- Does the feed storage area have appropriate separation to wells?  (See back of sheet.)

Yes     No (Does not meet NR-812; Check with DNR)

- Is there evidence of leachate in the feed storage area (brown stain or pools of discolored liquid, concrete surface with cement missing, or burned-out vegetation downstream)?

No (0 pts)     Yes (15 pts)	   points

- Is the feed in the storage area entirely covered to exclude rainfall from the feedstock?

Yes (0 pts)     No (20 pts)	   points

- How much of the “first flush” of runoff is captured and stored from the feed storage area?

0.2 inches (0 pts)     0.05 inches (10 pts)     None (20 pts)	   points

- What feedstock is stored?

Haylage (0 pts)     Field Corn Silage (5 pts)     Sweet Corn Silage(10 pts)	   points

- Does runoff from the feed storage area discharge directly (< 100’) to a concentrated 
flow channel or to surface water?

No (0 pts)     Yes (10 pts)	   points

- Is the feed storage area within a WQMA? (<300 feet to a solid or dashed blue line on a USGS 
7.5 quad map or site that is susceptible to groundwater contamination, or that has the potential
to be a direct conduit for contamination to reach groundwater or <1000 feet to a lake)

No (0 pts)     Yes (5 pts)	   points

- What is the size of the feedstock storage area?

0 - 1/4 ac. (5 pts)     1/4 - 1/2 ac. (10 pts)     1/2 - 1 ac. (15 pts)     >1 ac. (20 pts)	   points

- Are soils map units (immediately down-slope of the feed storage area) listed on the 
Wisconsin Conservation Planning Technical Note WI-1 appendix 1 “List of Soils with 
High Potential for Leaching to Groundwater?”

No (0 pts)     Yes (5 pts)	   points

- Is loose or spoiled feed uncovered and stacked on the feed storage area?

No (0 pts)     Yes (10 pts)	   points

- Does the feed storage area have 2 feet of separation to RHWT and Bedrock?

Yes (0 pts)     No (10 pts)	   points

- What is the floor surface and soils directly below the floor?

(See back side of sheet.)	   points

Total Points from Evaluation: points

Rating of the Silage/Feed Storage Area (from back side of the sheet): Not a resource concern Probably a resource concern Not likely a resource concern A resource concern exists

Well Separation Criteria (Applies to #1 on front.)

| Silage Storage System (NR-812) | Current Separation to Well |
| --- | --- |
| Silage Storage, Earthen Trench or Pit | 250 feet |
| Silage Storage Structure (Fabricated liquid-tight) (In-ground or surface) | 100 feet |
| Silage Storage - Surface, Uncovered | 100 feet |
| Silage Storage Tube (Plastic) | 8 feet |
| Silo With Pit | 50 feet |
| Silo Without Pit But With Concrete Floor and Drain | 50 feet |

Floor and Soils Assessment (Applies to #12 - Transfer score to the front.)

| Total Points | System Rating |
| --- | --- |
| < 25 | Not a resource concern |
| 26 to 45 | Not likely a resource concern |
| 46 to 65 | Probably a resource concern |
| > 66 | A resource concern exists |

# Text boxes

The feed storage area has a hard nonporous floor with some cracks.

The feed storage area has a porous floor or no hard surface

(Earthen)

The feed storage area has a hard semi-porous floor with lots of cracks.

The feed storage area has a hard nonporous floor, free of cracks.

(0 points)

Start floor scoring

>20 % fines  and > 7 PI

(5 points)

<20 % fines  or < 7 PI

(10 points)

> 20% fines  and > 7 PI

(10 points)

< 20 % fines  or < 7 PI

(15 points)

> 40% fines  and > 12 PI

Or

> 50% fines

(15 points)

< 40 % fines  or < 12 PI;

OR

<50% fines

(20 points)