## Statement of Work for Purchase Request Number RCF.1217

## NASA Langley Research Center requires a new control system for its exisiting loadframe dedicated to materials tesing and research.

## A digital controller that would replace the existing Model 458 controller shall provide capabilities or features for the major system components as descibed below:

### 1) A load frame chassis of the system shall provide:

### -digital servo control, function generation, data acquisition, hydraulic control,

###### and digital I/O

###### - Data acquisition reslution and rate of 16 bit and 6 kHz, repectively

###### - Function generation by 32 bit processor, standard haversine, square, and

###### ramp waveforms and downloaded wave shapes

###### - Computer controlled transducer limits

###### - 8 uncommitted channels of digital I/O (4 in, 4 out)

###### - Slots for up to 5 conditioning modules

###### - Automated dynamic control mode switching between any connected

###### transducer.  Any connected transducer or calculation can be selected for

###### control (typically load, strain or displacement) including load limited

###### displacement during specimen loading

###### - 2 Computer-selectable channels of 16 bit resolution analog output for easy access to transducer signals and other critical parameters

###### - Cables for hydraulic control, servovalves, conditioners, and communications

###### to personal computer

### 2) A remote station control panel of the system shall provide:

###### - Local actuator and hydraulic control at the load unit for ease of specimen

###### loading

###### - A display for test specific information

###### - 4 application defined function keys for test specific control

###### - Control of hydraulic pressure

###### - Actuator positioning controller to move actuator during specimen loading and

###### removal

###### - Load limited displacement available as a control mode for safe

###### specimen loading

###### - Test control buttons to stop, start, hold, and resume tests from

###### the load unit

###### - LED indication of interlocks with reset button

###### - Easy to see LED indication of switch status

### 3) A universal conditioner of the system shall provide:

###### - transducer conditioning for AC or DC transducers

###### Normalized with an on board reference for easy portability of

###### calibrations

###### - Low noise, low drift, high accuracy signal conditioning

###### - Computer control of range, transducer zero, excitation, filter

###### - Traceable calibration for each range

###### - Shunt calibration for 100% range

###### - Supports strain gage bridge completion.

###### - Excitation loss detection

###### - Computer controlled limit detection

### 4) A two stage valve driver shall provide:

###### - Servovalve drive signal for 2-stage servovalves

###### - Single or dual MTS Model 252 style servovalves

###### - Computer controlled dither amplitude and frequency

###### - Digitally controlled fault protection logic

###### - 16 bit resolution on valve D/A

## 5) A system control software package shall provide:

###### - A software interface for configuring the controller and the user interface to the test

###### station. The user can enter and save user preferences (units, valve adjustments, loop

###### tuning) for recall at any time

###### - A two channel on-line data display (X vs. Y or Time vs. YY), digital displays, and a

###### function generator for setting up tuning parameters and warming up the system prior

###### to testing

###### - An easy program for simple monotonic and cyclic test execution including data

###### acquisition. Test data may be stored in your choice of ASCII, Lotus, or Excel formats

###### for analysis with your favorite tools

###### - Peak Valley Control (PVC)

###### - Ability to correct for peaks and mean levels in cyclic waveforms.   PVC is our most

###### popular and widely used compensation tool

## 6) Other items to be provided shall include:

### - Floor mounting for remote station control panel

### - Remote emergency stopl cable, 10ft / 3m

### - Ground cable, 25ft / 7.5m

### - Load/Torque cell cable adapter, PT to MS connector

### - Exensometer cable adapter, PT to amphenol connector

- RSC / E-stop cable, 25ft / 7.5m

- Three day installation and user training at NASA LaRC