DESCRIPTION OF PROGRAM TJI95

This software package is self-contained and capable of being compiled and executed on a variety of platforms ranging from a personal computer to large scale "super computers".  The software is written in FORTRAN 77.  The software is designed to efficiently compute the trajectory of an energetic charged particle of a specified momentum per unit charge (rigidity) through a model magnetic field.  For cosmic ray access to the earth, the geocenter becomes the origin of the coordinate system.  All calculations are done in the r, (, ( coordinate system (a right-handed, orthogonal coordinate system).  The magnetic field subroutine included in this software is designed for efficient evaluation of the IGRF95 model of the earth's magnetic field.

In its usual mode of computing the path of cosmic ray trajectories in a model of the earth's magnetic field, we utilize this program to determine the path of a cosmic ray (a positively charged particle) from interplanetary space arriving at the earth at a specified position and direction.  To accomplish this, a negatively charged particle is 'launched' from the 'top' of the atmosphere at a specified position (latitude and longitude) in a specific direction (zenith and azimuth), and its path traced though the model magnetic field until it either (1) reaches a specified radial distance, (2) reenters the atmosphere, or (3) fails to reach either condition by a specified number of iterative steps.  If the negative test particle path penetrates the specified outer boundary (reaches interplanetary space) the direction of the particle velocity vector at the boundary crossing is specified as asymptotic latitude and longitude (in corresponding geocentric coordinates).  If the charged particle re-enters the atmosphere, then the re-entrant coordinates (geocentric latitude and longitude) are given.  In this version of the software, an oxygen nuclei (16O) is used as the test particle.  Since rigidity is a canonical coordinate, the path of any charged particle having the specified rigidity will be the same.

The software can be adapted to trace the path of any particle of a specified rigidity from a specified position and direction through any model magnetic field as long as the magnetic field is expressed as vectors in the r, (, ( coordinate system.

The 'input' to this program is a data line that specifies the initial position (latitude, longitude and altitude above the earth's surface), direction (azimuth and zenith), and rigidity (momentum per unit charge) along with control parameters to do 'N' trajectory calculations at specified rigidity increments beginning at an initial specified rigidity.

The 'output' of the software is in summary files with one line for each trajectory calculation.

The traditional summary output is called TAPE7 and is in an 80-column "card image" format.  This contains the initial conditions (the geodetic latitude, longitude, rigidity, zenith, and azimuth), the final results (asymptotic latitude and longitude), fate of the trajectory, the number of steps in the trajectory calculation, plus a magnetic field identifier.

There is also a second output summary, traditionally called TAPE8, which is in a line printer 132 column format.  This contains more detail; the initial conditions (the geodetic and geocentric latitude, the longitude, rigidity, zenith, and azimuth), the final results (asymptotic latitude and longitude, path length (in earth radii), trajectory transit time, time at altitudes under 100 km, number of maximum and minimum in radial distance along the trajectory, the trajectory fate, the number of steps in the calculation, plus a magnetic field identifier.

This structured FORTRAN 77 software assembly consists of a main program and four associated subroutines.  The software has extensive internal comments to aid the user in understanding the program.  The program and subroutines are:

Program    	TJI95			Main program; primary purpose is control

Subroutine 	GDGC			Conversion from geodetic to geocentric coordinates

Subroutine 	SINGLTJ		Calculates a particle trajectory

Subroutine 	FGRAD		Evaluates the V X B force vectors on the particle

Subroutine 	MAGNEW95		Evaluates the vector magnetic field at position r, (, (

Program Organization:

Each subroutine has a separate unique function.  Critical and often used variables are defined in labeled common blocks.  The important "working" variables are in the common block WRKVLU.  The trigonometric sines and cosines are in common block WRKTSC.  Definitions associated with the shape of the ellipsoid representing the surface of the earth are in common block GEOID.  We have found that some "super computers" do not allow mixing of real and integer variables in the same common block; therefore the are two additional common blocks associated with subroutine SINGLTJ.  These are common block SNGLR (real variables) and common block SNGLI (integer variables)

Accuracy and Precision

It is recommended that the REAL*8 precision always be used.  The primary limitation affecting the results is the accuracy of the magnetic field expansion.  For reasonably simple trajectories the results should be repeatable, independent of the computer platform used.  For long complex trajectories, default compiler options (round off or truncate, and the precision of intrinsic function) begin to affect the result.  The calculation procedure includes automatic error checking.  The particle acceleration terms are monitored in subroutine SINGLTJ.  When significant increases in the force on the particle are noted the step size is reduced and the calculations are continued at smaller step intervals.  The quantity BETA (( = v/c) should be invariant throughout the calculation and is monitored.  Changes of BETA exceeding 1 part in 105 results in an automatic restart and the trajectory is recalculated at smaller step size increments.

On some "main fames" the intrinsic functions are automatically derived in REAL*8 precision; on some other systems the intrinsic functions are evaluated in a REAL*4 mode unless the double precision argument is specified.  In this version intended for the Desktop Computer, all intrinsic functions are specified in the double precision mode; however, we have left a single precision statement "commented out" immediately before each double precision statement.  For simple trajectories the user probably cannot note any difference; however, for long complex trajectories, the differences between the use of single precision intrinsic functions and double precision intrinsic functions will become apparent.  If a specific rigidity and direction is used for comparison and the position of each trajectory step is monitored, the effect of the small differences between REAL*4 and REAL*8 accumulate and eventually the trajectory path will differ is it is a long complex trajectory.

In the interest of computational speed, the magnetic field calculation routine drops the evaluation of the high order terms when they make an "insignificant" contribution to the total magnetic field.  Again for long complex trajectories, these small differences accumulate and the trajectory paths may diverge when different criteria are used for dropping magnetic field expansion.

User Defined Parameters:

Two variables are intended to be user defined.  These are FSTEP and LIMIT.  Default values have been set in the program, LIMIT = 600,000, and FSTEP = 4 x 108.

LIMIT is the number of Runge-Kutta steps allowed before a trajectory is declared failed.

FSTEP is the total number of Runge-Kutta steps allowed before the run is terminated.

Simple high rigidity trajectories often require only several hundred steps.  Simple trajectories above the upper cutoff rigidity often can be completed in a few thousand steps.  Most cosmic ray trajectories will complete in about 10,000 steps.  Some quasi-trapped periodic orbits may require more than 100,000 steps.  Trapped orbits require an infinite number of steps.  Very low rigidity trajectories initiated at high polar latitudes will exhibit the quasi-trapped behavior and probably fail to reach a solution.  (The step size criteria is based on the time to travel about one percent of a gyro-distance.  Therefore trajectories with many loops require many steps to complete.)

Assuming the user wants to operate in a "batch mode" some job control parameters are needed.  This is the quantity FSTEP.  Some estimate of the computer speed is necessary.  For desktop personal computers this can range from a few hundred steps per second on old obsolete 486 chips to the order of 50,000 steps per second obtainable with current Pentium( III chips operating at approximately 1 GHz clock cycle time.  We have found a very significant difference in the program computational speed on the same computer that can be attributed to the efficiency of the object code generated by the compiler.  In our testing on desktop platforms we have found that the executable code generated by the COMPAQ( Visual Fortran operates efficiently on a Microsoft( Windows operating system.  The worst performing executable code (derived from an old, no longer sold system) ran about five times slower on the same test set of trajectory calculation.  It is assumed that workstations will have trajectory computational speeds of the order or at least 10,000 steps per second.  The default FSTEP setting will allow a batch run of the order of 10 hours if the program executes at 10,000 Runge-Kutta steps per second.

Program Operation

This program operates in the  r, (, (  coordinate system.  The variables Y(1), Y(2), and Y(3) are the position vectors in the  r, (, (  coordinate system and the variables Y(4), Y(5), and Y(6) are the velocity vectors.

The program initially defines the physical constants used in the calculation and control parameters.  It then enters a control loop beginning with reading a data line to determine the initial position and direction, the specified starting rigidity and how many trajectories to calculate at specified increments.

For each control line read, a call to subroutine GDGC converts the initial geodetic coordinates (map makers coordinates on the earth's surface) to geocentric  r, (, ( coordinates.  Then the trajectory calculations are done by subroutine SINGLTJ

The control loop continues (read in control line, convert coordinates, do trajectory calculations) until a negative (or zero) value of rigidity is read in.  When this occurs the program terminates.

Labeled Common arguments:

Block name:		/WRKVLU/

Arguments in block	F(6), Y(6), ERAD, EOMC, VEL, BR, BT, BP

F(6)		Array of force and acceleration vectors

Y(6)		Array of position and velocity vectors

ERAD		Average radius of the earth in kilometers

EOMC    	Electronic charge divided by relativistic mass energy equivalent (mixed units)

VEL		Particle velocity in earth radii per second

BP		Value of the B(() magnetic field vector (in units of Gauss)

BR		Value of the B(r) magnetic field vector (in units of Gauss)

BT		Value of the B(() magnetic field vector (in units of Gauss)

Block name:		/WRKTSC/

Arguments in block	TSY2, TCY2, TSY3, TCY3

TSY2		Sine of the Y(2) coordinate (theta coordinate)

TCY2		Cosine of the Y(2) coordinate (theta coordinate)

TSY3		Sine of the Y(3) coordinate (phi coordinate)

TCY3		Cosine of the Y(3) coordinate (phi coordinate)

Block name:		/TRIG/

Arguments in block	PI, RAD, PI02

PI		Value of pi

RAD		Value of degrees in a radian

PI02		Value of pi/2.0

Block name:		/GEOID/

Arguments in block	ERADPL, ERECSQ

ERADPL	Polar radius of the earth in kilometers

ERECSQ	Eccentricity of ellipsoid squared

Block name:		/SNGLR/

Arguments in block	SALT, DISOUT, GCLATD, GDLATD, GLOND, GDAZD, GDZED,

RY1, RY2, RY3, RHT, TSTEP

SALT		Start altitude of trajectory above surface of geoid

DISOUT	Radial distance (in earth radii) for termination of calculation

GCLATD	Geocentric latitude in degree

GDLATD	Geodetic latitude in degrees

GLOND	East longitude in degrees

GDAZD 	Geodetic azimuth in degrees

GDZED	Geodetic zenith in degrees

RY1		Original start position Y(1), (radial component in the  r, (, (  coordinate system)

RY2		Original start position Y(2), (theta component in the  r, (, (  coordinate system)

RY3		Original start position Y(3), (phi component in the  r, (, (  coordinate system)

RHT		Height above geoid where trajectory re-enters the atmosphere

TSTEP		Total number of steps in this run.

Block name:		/SNGLI/

Arguments in block	LIMIT, NTRAJC, IERRPT

LIMIT		Maximum number of steps before 'failed' trajectory

NTRAJC	Number of trajectories calculated in this run

IERRPT	Integer control for printing diagnostics (normally = 0)

Subroutines called:

GCGC (TCD, TSD)

TCD		Cosine of the rotation angle

TSD		Sine of the rotation angle

SINGLTJ (PC, IRSLT, INDXPC, Y1GC, Y2GC, Y3GC)

PC		Particle rigidity (in units of GV)

IRSLT		Integer result of trajectory calculation

(+1 = Allowed, 0 = Failed, -1 = Re-entrant)

INDXPC	Integer value of PC in units of MV

Y1GC		Y(1) position in geocentric coordinates

Y2GC		Y(2) position in geocentric coordinates

Y3GC		Y(3) position in geocentric coordinates

Dimensioned variables: all in labeled common

F(6)		Array of force and acceleration vectors

Y(6)		Array of position and velocity vectors

Data files: none

Output files:

TAPE7 from subroutine SINGTJ (80 character summary)

TAPE8 from subroutine SINGTJ (132 character line printer summary)

TAPE16 (diagnostic output; if desired, set IERRPT to > 0)

Listing of all variables in program TJI95

B    			Magnitude of the magnetic field (in Gauss) [in COMMON /WRKVLU/]

BP  			Value of the B(() magnetic field vector (in Gauss) [in COMMON /WRKVLU/]

BR  			Value of the B(r) magnetic field vector (in Gauss) [in COMMON /WRKVLU/]

BT  			Value of the B(() magnetic field vector (in Gauss) [in COMMON /WRKVLU/]

CF 			Character variable "F"

DELPC   		Increments of rigidity spacing search in control line

DISOUT 		Distance (in earth radii) for trajectory termination [in COMMON /SNGLR/]

ERAD  			Average radius of the earth in kilometers [in COMMOM /WRKVLU/]

ERADPL   		Polar radius of the earth in km [in COMMON /GEOID/]

ERECSQ		Eccentricity of ellipsoid squared [in COMMON /GEOID/]

F(6)			Array of  "F" values (velocity and acceleration in program coordinates)

[in COMMON /WRKVLU/]

GCLATD  		Geocentric latitude in degrees (+ = north, south = -) [in COMMON /SNGLR/]

GDAZ  		Geodetic azimuth in radians (measured clockwise from north)

GDAZD    		Geodetic azimuth in degrees (measured clockwise from north)

GDLATD  		Geodetic latitude in degrees (+ = north, south = -) [in COMMON /SNGLR/]

GDZE  			Geodetic zenith in radians (0 = vertical)

GDZED  		Geodetic zenith in degrees (0 = vertical)

GLOND   		Geodetic East longitude in degrees (from Greenwich meridian)

[in COMMON /SNGLR/]

IDELPC  		Integer value of rigidity change increment in MV (attempt to avoid round off)

IERRPT  		Integer control for printing diagnostics (normally set to 0)

INDEX  		Arbitrary index number of input control line (optional)

INDO  			Integer control of number of trajectories to calculate

INDXPC  		Integer value of rigidity in MV increments (attempt to avoid round off)

IOSTAT 		Integer system argument of status of read

IRSLT 			Internal result of particle trajectory (+1 = allowed, 0 = failed, -1 = re-entrant)

ISALT  		Integer value of start altitude (in km) above geoid surface

LIMIT  		Limit of number of steps before trajectory is declared "Failed"

LSTEP  		Number of times step size control has been reduced to overcome trajectory error

NDO    			Integer control read in (number of trajectories to compute from this control line)

NTRAJC 		Number of trajectories in this computer run

PC  			Rigidity of particle (in units of GV)

PI  			Real value of the quantity Pi (~3.1415926535) [in COMMON /TRIG/]

PIO2   			Real value of Pi divided by 2.0 [in COMMON /TRIG/]

RAD    			Real value of one radian (~57.29578 degrees) [in COMMON /TRIG/]

RHT    			Height above geoid where a trajectory re-entered the atmosphere

RY1    			Real value of the starting position of the  r coordinate in  r, (, ( coordinates

[in COMMON /SNGLR/]]

RY2    			Real value of the starting position of the  theta coordinate in  r, (, ( coordinates

[in COMMON /SNGLR/]

RY3    			Real value of the starting position of the  phi coordinate in  r, (, ( coordinates

[in COMMON /SNGLR/]

SALT   			Real value of the starting altitude above the surface of the geoid

[in COMMON /SNGLR/]

TCD    			Trigonometric cosine of the rotation angle from geodetic to geocentric

TCGDAZ 		Trigonometric cosine of the geodetic azimuth

(Measured clockwise from north) 	 [in COMMON /SNGLR/]

TCGDZE 	Trigonometric cosine of the geodetic zenith (measured clockwise from north)

TCY2   			Trigonometric cosine of the vector theta angle in  r, (, ( coordinates

[in COMMON /SNGLR/]

TCY3   			Trigonometric cosine of the vector phi angle in  r, (, ( coordinates

[in COMMON /SNGLR/]

TSTEP  		Number steps executed in this run

TSY2   			Trigonometric sine of the vector theta (() angle in  r, (, ( coordinates

[in COMMON /SNGLR/]

TSY3   			Value of the trigonometric sine of the vector phi (() angle in  r, (, ( coordinates

[in COMMON /SNGLR/]

VEL    			Particle velocity in earth radii per second [in COMMON /WRKVLU/]

Y(6)  			Array of "Y" values (position and velocity in  r, (, ( coordinates)

[in COMMON /WRKVLU/]

Y1GC   		Starting position  r  component in geocentric coordinates

Y1GD   		Starting position  r  component in geodetic coordinates

Y2GC   		Starting position  (  component in geocentric coordinates

Y2GD   		Starting position  (  component in geodetic coordinates

Y3GC   		Starting position  ( component in geocentric coordinates

Y3GD   		Starting position  (  component in geodetic coordinates

Subroutine GDGC (TCD, TSD)

This subroutine calculates the angle between geodetic and geocentric coordinates.  The arguments TCD and TSD are the trigonometric cosine and sine of the rotation angle from a normal from the surface of the geoid (geodetic coordinates) and a radial from the center of the earth (geocentric coordinates). See Appendix B of NSSDC 72-12)

Arguments in call statement

TCD	Cosine of the rotation angle

TSD	Sine of the rotation angle

Labeled Common arguments:

Block name:		/WRKVLU/

Arguments in block	F(6), Y(6), ERAD, EOMC, VEL, BR, BT, BP

F(6)		Array of force and acceleration vectors

Y(6)		Array of position and velocity vectors

ERAD		Average radius of the earth in kilometers

EOMC    	Electronic charge divided by relativistic mass energy equivalent (mixed units)

VEL		Particle velocity in earth radii per second

BP		Value of the B(() magnetic field vector (in units of Gauss)

BR		Value of the B(r) magnetic field vector (in units of Gauss)

BT		Value of the B(() magnetic field vector (in units of Gauss)

Block name:		/WRKTSC/

Arguments in block	TSY2, TCY2, TSY3, TCY3

TSY2		Sine of the Y(2) coordinate (theta coordinate)

TCY2		Cosine of the Y(2) coordinate (theta coordinate)

TSY3		Sine of the Y(3) coordinate (phi coordinate)

TCY3		Cosine of the Y(3) coordinate (phi coordinate)

Block name:		/TRIG/

Arguments in block	PI, RAD, PI02

PI		Value of pi

RAD		Value of degrees in a radian

PI02		Value of pi/2.0

Block name:		/GEOID/

Arguments in block	ERADPL, ERECSQ

ERADPL	Polar radius of the earth in kilometers

ERECSQ	Eccentricity of ellipsoid squared

Block name:		/SNGLR/

Arguments in block	SALT, DISOUT, GCLATD, GDLATD, GLOND, GDAZD, GDZED,

RY1, RY2, RY3, RHT, TSTEP

SALT		Start altitude of trajectory above surface of geoid

DISOUT	Radial distance (in earth radii) for termination of calculation

GCLATD	Geocentric latitude in degrees

GDLATD	Geodetic latitude in degrees

GLOND	East longitude in degrees

GDAZD 	Geodetic azimuth in degrees

GDZED	Geodetic zenith in degrees

RY1		Original start position Y(1)

RY2		Original start position Y(2)

RY3		Original start position Y(3)

RHT		Height above geoid where trajectory re-enters the atmosphere

TSTEP		Total number of steps in this run.

Block name:		/SNGLI/

Arguments in block	LIMIT, NTRAJC, IERRPT

LIMIT		Maximum number of steps before 'failed' trajectory

NTRAJC	Number of trajectories calculated in this run

IERRPT	Integer control for printing diagnostics (normally = 0)

Dimensioned variables: all in labeled common

F(6)		Array of force and acceleration vectors

Y(6)		Array of position and velocity vectors

Subroutines called:  none

Data files: none

Output files: none

Operation:

The shape of the earth used is not a sphere, but an ellipsoid having a specified polar radius, equatorial radius, and eccentricity.  When this subroutine is called, it defines the shape of an oblate earth from the polar and equatorial radius, and calculates vectors from a normal on the surface of the ellipsoid to the specified position in geodetic coordinates, at the specified latitude, and determines the vector rotation angle between geodetic coordinates and geocentric coordinates.  The sine and cosine of this rotation angle are passed to the calling program.  Geodetic latitude is a measure of latitude in a coordinate system normal to the surface of the earth.  At a position on or above the surface of the ellipsoid, there is a slight difference between a direction normal to the surface of the ellipsoid and a direction to the geocentric.  This difference is latitude dependent.  (It is zero at the equator or poles and can be as large as approximately 1/2 of a degree at mid latitudes.)  The vector rotation angle allows for direction specification in both geodetic (map) coordinates and geocentric coordinates.  This small correction for the direction may be insignificant for some applications, but may be significant for precision calculation in a specific direction at high rigidities.

Data checking: none.  The data to describe the shape of the earth are included in the subroutine.

Listing of all variables used in subroutine GDGC of program TJI95

B    			Magnitude of the magnetic field (in Gauss) [in COMMON /WRKVLU/]

BP  			Value of the B(() magnetic field vector (in Gauss) [in COMMON /WRKVLU/]

BR  			Value of the B(r) magnetic field vector (in Gauss) [in COMMON /WRKVLU/]

BT  			Value of the B(() magnetic field vector (in Gauss) [in COMMON /WRKVLU/]

DISOUT 		Distance (in earth radii) for trajectory termination [in COMMON /SNGLR/]

DISTKM  		Starting position geocentric radial distance from geocenter

EOMC    		Electronic charge divided by relativistic mass energy equivalent (mixed units)

[in COMMON /WRKVLU/]

ERAD  			Average radius of the earth in kilometers [in COMMOM /WRKVLU/]

ERADPL   		Polar radius of the earth in km [in COMMON /GEOID/]

ERECSQ		Eccentricity of ellipsoid squared [in COMMON /GEOID/]

ERPLSQ  		Polar radius of earth (in km) squared

F(6)			Array of  "F" values (velocity and acceleration in program coordinates)

[in COMMON /WRKVLU/]

GCLATD  		Geocentric latitude in degrees (+ = north, south = -) [in COMMON /SNGLR/]

GDAZD    		Geodetic azimuth in degrees (measured clockwise from north)

GDCLT		Geodetic co-latitude (in radians)

GDLATD  		Geodetic latitude in degrees (+ = north, south = -) [in COMMON /SNGLR/]

GDZED  		Geodetic zenith in degrees (0 = vertical)

GLOND   		Geodetic East longitude in degrees (from Greenwich meridian)

[in COMMON /SNGLR/]

ONE 			Intermediate term in computations (see NSSDC ALLMAG description)

PI  			Real value of the quantity Pi (~3.1415926535) [in COMMON /TRIG/]

PIO2   			Real value of Pi divided by 2.0 [in COMMON /TRIG/]

RAD    			Real value of one radian (~57.29578 degrees) [in COMMON /TRIG/]

RHO  			Intermediate term in computations (see NSSDC ALLMAG description)

RHT  			Height above geoid where a trajectory is declared re-entrant

[in COMMON /SNGLR/]

RY1    			Real value of the starting position of the  r coordinate in  r, (, ( coordinates

[in COMMON /SNGLR/]

RY2    			Real value of the starting position of the  theta coordinate in  r, (, ( coordinates

[in COMMON /SNGLR/]

RY3    			Real value of the starting position of the  phi coordinate in  r, (, ( coordinates

[in COMMON /SNGLR/]

SALT   			Real value of the starting altitude above the surface of the geoid

[in COMMON /SNGLR/]

TCD    			Trigonometric cosine of the rotation angle from geodetic to geocentric

TCGDCLT 		Trigonometric cosine of the geocentric co-latitude

TCY2   			Trigonometric cosine of the vector theta angle in  r, (, ( coordinates

[in COMMON /SNGLR/]

TCY3   			Trigonometric cosine of the vector phi angle in  r, (, ( coordinates

[in COMMON /SNGLR/]

THREE  		Intermediate term in computations (see NSSDC ALLMAG description)

TSD    			Trigonometric sine of the rotation angle from geodetic to geocentric

TSGDCLT 		Trigonometric sine of the geocentric co-latitude

TSTEP  		Number steps executed in this run

TSY2   			Trigonometric sine of the vector theta (() angle in  r, (, ( coordinates

[in COMMON /SNGLR/]

TSY3   			Trigonometric sine of the vector phi (() angle in  r, (, ( coordinates

[in COMMON /SNGLR/]

TWO  			Intermediate term in computations (see NSSDC ALLMAG description)

VEL    			Particle velocity in earth radii per second [in COMMON /WRKVLU/]

Y(6)  			Array of "Y" values (position and velocity in  r, (, ( coordinates)

[in COMMON /WRKVLU/]

Reference publication:

ALLMAG, GCAZLMG, LINTRA: Commuter Programs For Geomagnetic Field And Field-Line Calculations, E.G. Stassinopulous and G.D. Mead, NSSDC 72-12, February 1972, NASA, GFSC, Greenbelt MD.

Subroutine SINGLTJ (PC, IRSLT, INDXPC, Y1GC, Y2GC, Y3GC)

This subroutine does the actual trajectory tracing.  When called it initially defines control parameters and constants used in the particle tracing and initializes the Runge-Kutta variables to zero.  It sets up the initial position and direction, and defines the relativistic parameters relating to the particle total energy and speed.

In this version of the subroutine, an oxygen nuclei (16O) is used as the test particle.  By definition a 16O nuclei has a mass of 16 Atomic Mass Units (AMU) and an atomic charge of 8.  The mass-energy conversion for one AMU is 0.93114 GeV.  If it were desired to modify the program for some other nuclei, such as a proton that has an atomic charge of 1 and atomic mass of 1.0081415 AMU, then the rest mass energy for atomic nuclei must be adjusted.

After the initial definitions, the subroutine then chooses an initial starting step length (a relatively small value) and starts the Runge-Kutta process of tracing the particle trajectory.   After each step it goes though an error checking and detection process.  If the checks are satisfactory, it determines the particle location with respect to the atmosphere and the outer boundary.

If the charged particle is between the atmosphere and the outer boundary, it adjusts the size of the next step and continues the trajectory tracing until the LIMIT on the number of steps is reached.

If the charged particle is entering the atmosphere, it terminates the calculation.

If the charged particle is less than 100 km above the earth's surface, it maintains a running sum of the time at low altitudes.

If the charged particle is approaching the outer boundary, it adjusts the step size so it penetrates this boundary at small step lengths.

If the charged particle has penetrated the outer boundary at a small step, it computes the final coordinates.

When the particle has reached a solution (allowed or re-entrant) or reached the step limit, it writes out the result and returns to the calling program.

Arguments in call statement

PC, IRSLT, INDXPC, Y1GC, Y2GC, Y3GC

PC		Particle rigidity

IRSLT		Integer result of trajectory (+1 = allowed, 0 = failed, -1 = re-entrant)

INDXPC	Integer value of PC in MV units

Y1GC		Y(1) position in geocentric coordinates

Y2GC		Y(2) position in geocentric coordinates

Y3GC		Y(3) position in geocentric coordinates

Labeled Common arguments:

Block name:		/WRKVLU/

Arguments in block	F(6), Y(6), ERAD, EOMC, VEL, BR, BT, BP

F(6)		Array of force and acceleration vectors

Y(6)		Array of position and velocity vectors

ERAD		Average radius of the earth in kilometers

EOMC    	Electronic charge divided by relativistic mass energy equivalent (mixed units)

VEL		Particle velocity in earth radii per second

BP		Value of the B(() magnetic field vector (in units of Gauss)

BR		Value of the B(r) magnetic field vector (in units of Gauss)

BT		Value of the B(() magnetic field vector (in units of Gauss

Block name:		/WRKTSC/

Arguments in block	TSY2, TCY2, TSY3, TCY3

TSY2		Sine of the Y(2) coordinate (theta coordinate)

TCY2		Cosine of the Y(2) coordinate (theta coordinate)

TSY3		Sine of the Y(3) coordinate (phi coordinate)

TCY3		Cosine of the Y(3) coordinate (phi coordinate)

Block name:		/TRIG/

Arguments in block	PI, RAD, PI02

PI		Value of pi

RAD		Value of degrees in a radian

PI02		Value of pi/2.0

Block name:		/GEOID/

Arguments in block	ERADPL, ERECSQ

ERADPL	polar radius of the earth in kilometers

ERECSQ	Eccentricity of ellipsoid squared

Block name:		/SNGLR/

Arguments in block	SALT, DISOUT, GCLATD, GDLATD, GLOND, GDAZD, GDZED,

RY1, RY2, RY3, RHT, TSTEP

SALT		Start altitude of trajectory above surface of geoid

DISOUT	Radial distance (in earth radii) for termination of calculation

GCLATD	Geocentric latitude in degrees

GDLATD	Geodetic latitude in degrees

GLOND	East longitude in degrees

GDAZD 	Geodetic azimuth in degrees

GDZED	Geodetic zenith in degrees

RY1		Original start position Y(1), (radial component in the  r, (, (  coordinate system)

RY2		Original start position Y(2) , (theta component in the  r, (, (  coordinate system)

RY3		Original start position Y(3) , (phi component in the  r, (, (  coordinate system)

RHT		Height above geoid where trajectory re-enters the atmosphere

TSTEP		Total number of steps in this run.

Block name:		/SNGLI/

Arguments in block	LIMIT, NTRAJC, IERRPT

LIMIT		Maximum number of steps before 'failed' trajectory

NTRAJC	Number of trajectories calculated in this run

IERRPT	Integer control for printing diagnostics (normally = 0)

Dimension variables: (not in labeled common)

P(6), Q(6), R(6), S(6), YB(6), FOLD(6), YOLD(6)

P(6)		Runge-Kutta variable

Q(6)		Runge-Kutta variable

R(6)		Runge-Kutta variable

S(6)		Runge-Kutta variable

YB(6)		Runge-Kutta variable

FOLD(6)	"F" vectors of previous step

YOLD(6)	"Y" vectors of previous step

Subroutines called:  FGRAD

Data files: none

Output files:

TAPE7 (80 character summary)

TAPE8 (132 character line printer summary)

TAPE16 (diagnostic output; if desired set IERRPT to > 0)

Program Operation:

This program operates in the  r, (, (  coordinate system.  The variables Y(1), Y(2), and Y(3) are the position vectors in the  r, (, (  coordinate system and the variables Y(4), Y(5), and Y(6) are the velocity vectors.

When this subroutine is called, it initially defines control parameters and constants used in the particle path tracing, and initializes the Runge-Kutta variables to zero.  It obtains the particle's height with respect to the surface of an oblate earth.  It sets up the initial position vectors, Y(1), Y(2) and Y(3), and based on the particle rigidity, sets up velocity vectors, Y(4), Y(5), and Y(6).  It then defines the relativistic parameters TENG (total energy), EOMC (charge per relativistic mass/energy equivalent), and GMA (the relativistic parameter of total energy over the rest mass energy).  It defines scalar quantities relating to the particle, BETA (the particle speed with respect to light), PVEL (the particle speed in earth radii per second), and HMAX (a maximum step length allowed for this particle rigidity).

Next it defines an initial starting step length (a relatively small value) and starts the Runge-Kutta process of tracing the particle trajectory.   Comment cards specifically indicate the Runge-Kutta iteration process, which is the coding between FORTRAN statement numbers 130 and 170.  The calls to subroutine FGRAD evaluate the V X B force on the particle during this step.  The logic is very similar to that documented in Ralston and Wilf (1960).  After each Runge-Kutta iteration step there is an extensive error checking and detection process.

The error checking process begins with a check on the particle speed (BETA), which should remain invariant throughout the trajectory.  If the difference between the initial particle speed (BETA) and it's current speed (RCKBETA) is greater than EDIF, then the trajectory tracing process is re-initialized (including the NSTEP variable) and the trajectory re-started at a smaller step size selection criteria.  Up to five re-starts are allowed before the specific trajectory is declared impossible to calculate, evaluated as "failed", and the path length made negative in order to distinguish it from successful trajectories.  In order to attempt to reach a solution the EDIF variable is widened by a factor of two after each successive trajectory failure.

After the error check, then the acceleration of the particle is compared with previous values.  We have found that computational errors are most likely to occur when there are rapid changes in the acceleration.  If the average change in acceleration exceeds a factor of five, or if any component of the acceleration exceeds a factor of three, then the step length for the next Runge-Kutta step is reduced.

Along the particle path the software checks the particle location with respect to the atmosphere and the outer boundary.  If the charged particle is less than 100 km above the earth's surface, it maintains a running sum of the time at low altitudes.  If the charged particle is entering the atmosphere, it terminates the calculation.

The next check determines if the particle has penetrated the outer termination boundary.  The step length can be relatively large at extreme distances from the earth.  If the outer boundary has been penetrated at a large step size, the trajectory is "backed up" and the step size reduced until it penetrates the boundary at a small step size.  This results in a more precise determination of  the penetration location and can significantly affect the computed asymptotic direction.

If there are no errors and the charged particle is between the atmosphere and the outer boundary, the software adjusts the size of the next step appropriate for the magnitude of the magnetic field (the step size is normally about one percent of the gyro-distance) and continues the trajectory tracing.  The basic step length algorithm is:

H = ((2.0*(*33.333*PC)/(B*(*C))/100.0

where "H" is time in seconds, "PC" is the particle rigidity in GV, "B" is the magnitude of the magnetic field in Gauss and "C" is the speed of light in km/sec.

(A handy formula to remember is the gyro-radius is 33 km per GV per Gauss)

The software initially starts at a trajectory calculation at a small step size and the step size is permitted to grow at a maximum of about 20 percent each step.  If the particle trajectory starts to loop to a lower altitude, then the step size is reduced to compensate for the increasing magnitude of the magnetic field.  When a loop in the trajectory develops, the acceleration forces increase and step size adjustments are made in the case of a significant increase in the acceleration forces.

During the trajectory tracing, the software notes the number of maximum and minima the trajectory experiences.  This information is useful in ascertaining the complexity of the trajectory.

When the particle has reached a solution (allowed or re-entrant) or reached the step limit, the subroutine will write out the result and return to the calling program.   The fate is coded in the variable IFATE: (0 = Allowed,   1 = Failed,   2 = Re-entrant,   3 = Failed, but max alt > 6.6 earth radii)

If the trajectory is allowed (penetrates the outer boundary), then the velocity vectors are transformed into asymptotic latitude and longitude.  Asymptotic latitude and longitude are the geocentric coordinates the velocity vector would have at infinity.  If the trajectory re-enters the atmosphere, then the position coordinates are transformed to geocentric latitude and longitude.

The 'output' of the software is in summary files, on one line for each trajectory calculation.

The output files are:

TAPE7   is in an 80-column "card image" format.  This contains the initial conditions (the geodetic latitude, longitude, rigidity, zenith, and azimuth), the final results (asymptotic latitude and longitude, fate and number of steps), and a magnetic field identifier.

TAPE8   is in a line printer 132-column format.  This contains more detail; the initial conditions (the geodetic latitude and the geocentric latitude, the longitude, rigidity, zenith, and azimuth), the final results (asymptotic latitude and longitude, path length, trajectory time, time at altitudes under 100 km, number of maximum and minimum in trajectory, fate, and number of steps), and a magnetic field identifier.

TAPE16   is a diagnostic output, including a record of restarts due to BETA checks 
			or trajectory failures.

See the examples section for samples of the output.

Possible Additions for Trajectory Plotting

If it is desired to plot a trajectory, the position variables Y(1), Y(2), and Y(3) must be stored after each Runge-Kutta step in a suitable array.  The task of adding such a modification should be straightforward and is left to the individual program user.

Listing of all variables in subroutine SINGLTJ

ACCER  		Magnitude of current value of the particle acceleration

ACCOLD 		Magnitude of last value of the particle acceleration

AFOLD  		Absolute value of FOLD

AHLT 			Variable to control step size at high latitude

ANUC 			Atomic number of number of nucleons in atom

ATRG1  		Intermediate value to compute asymptotic latitude (avoid 0/0 problem)

ATRG2  		Intermediate value to compute asymptotic latitude (avoid 0/0 problem)

AZD  			Azimuth angle in degrees (measured clockwise from north)

B    			Magnitude of the magnetic field (in Gauss) [in COMMON /WRKVLU/]

BETA 			Particle speed as fraction of light speed (( = v/c  where c is speed of light)

BETAST 		Control variable for reducing step size if error has occurred

BP  			Value of the B(() magnetic field vector (in Gauss) [in COMMON /WRKVLU/]

BR  			Value of the B(r) magnetic field vector (in Gauss) [in COMMON /WRKVLU/]

BT  			Value of the B(() magnetic field vector (in Gauss) [in COMMON /WRKVLU/]

CF 			Character variable "F"

CNAME  		Character variable (up to 6 characters) identifying magnetic field used

CR  			Character variable "R"

DELACC 		Change in particle acceleration from previous step

DISCK  		Step length control variable to approach boundary at 10 % increments

DISOUT 		Distance (in earth radii) for trajectory termination [in COMMON /SNGLR/]

DISTR  		Radial distance (in earth radii) from current distance to termination boundary

EDIF 			Variation in ( allowed before error declared

EMCSQ  		Mass energy equivalent for a AMU (0.931141 GeV)

EOMC    		Electronic charge divided by relativistic mass energy equivalent (mixed units)

[in COMMON /WRKVLU/]

ERAD  			Average radius of the earth in kilometers [in COMMOM /WRKVLU/]

ERADPL   		Polar radius of the earth in km [in COMMON /GEOID/]

ERECSQ		Eccentricity of ellipsoid squared [in COMMON /GEOID/]

F(6)			Array of  "F" values (velocity and acceleration in program coordinates)

[in COMMON /WRKVLU/]

FOLD(6)		Array of  "F" values (velocity and acceleration)  from previous step

FASLAT  		Asymptotic latitude (in degrees)

FASLON  		Asymptotic longitude (in degrees east of the Greenwich meridian)

GCLATD  		Geocentric latitude in degrees (+ = north, south = -) [in COMMON /SNGLR/]

GDAZD    		Geodetic azimuth in degrees (measured clockwise from north)

GDLATD  		Geodetic latitude in degrees (+ = north, south = -) [in COMMON /SNGLR/]

GDZED  		Geodetic zenith in degrees (0 = vertical)

GLOND   		Geodetic East longitude in degrees (from Greenwich meridian)

[in COMMON /SNGLR/]

GMA 			Relativistic factor (total energy/rest energy)

GRNDKM  		Altitude above surface of earth at this latitude (in km)

H 			Runge-Kutta step size (in seconds)

HB  			Preliminary value of step size for  ( = 1

HCK 			Control to limit step size growth to 20%

HCNG  		Change of step size from previous step

HMAX  		Maximum value of step size allowed

HOLD  		Value of previous  Runge-Kutta step size

HSNEK 		Control to approach 90% of distance to boundary

HSTART  		Starting step size value (deliberately made small)

I 			Index variable in do loops

IAZ 			Integer value of azimuth (measured counter clockwise from north)

ICK 			Index for checking acceleration growth

IERRPT  		Integer control for printing diagnostics (normally set to 0)

IFATE 			Integer fate of particle trajectory ( 0 = Allowed,	1 = Failed, 2 = Re-entrant

3 = Failed, but max alt > 6.6 earth radii)

INDXPC  		Index of particle rigidity in MV

IRT			Integer control for writing results (+1 = Allowed, 0 = Failed, -1 = Re-entrant)

IRSLT 			Internal result of particle trajectory (+1 = Allowed, 0 = Failed, -1 = Re-entrant)

ISALT 			Integer value of start altitude (in km) above earth surface

IZE 			Integer value of zenith angle (in degrees)

KBF  			Number of failed attempts to trace this trajectory

LIMIT  		Limit of number of steps before trajectory declared "Failed"

LSTEP  		Number of times the step size control reduced to overcome trajectory error

NMAX 		Number of maxima in complex trajectory path

NMIN 			Number of minima in complex trajectory path

NSTEP  		Number of steps in current trajectory

NSTEPT 		Temporary variable that can be used to print out first 1000 steps

NTRAJC 		Number of trajectories in this computer run

P(6)			Array of intermediate values used in Runge-Kutta integration

PATH 			Total distance of trajectory path from start to termination

PC  			Rigidity of particle (in units of GV)

PI  			Real value of the quantity Pi (~3.1415926535) [in COMMON /TRIG/]

PIO2   			Real value of Pi divided by 2.0 [in COMMON /TRIG/]

PSALT  		Current particle distance from ground (used for re-entrant calculations)

PTCY2  		Absolute value of cosine Y(2) (used in control of polar step size)

PVEL 			Particle velocity (in earth radii per second)

R(6) 			Array of intermediate values used in Runge-Kutta integration

R100KM 		Y(1) distance of 100 km altitude at this latitude

R120KM 		Y(1) distance of 120 km altitude at this latitude

RAD    			Real value of one radian (~57.29578 degrees) [in COMMON /TRIG/]

RC1O6  		Constant in Runge-Kutta integration (1.0/6.0)

RCKBETA  		Current value of particle ( after this step

RENLAT 		Latitude of re-entrant particle intersection with atmosphere

RENLON 		Longitude of re-entrant particle intersection with atmosphere

RFA  			Ratio of acceleration magnitude between current step and last step

RFCK 			Ratio of acceleration component between current step and last step

RHT    			Height above geoid where a trajectory re-entered the atmosphere

RY1    			Real value of the starting position of the  r coordinate in  r, (, ( coordinates

[in COMMON /SNGLR/]

RY2    			Real value of the starting position of the  theta coordinate in  r, (, ( coordinates

[in COMMON /SNGLR/]

RY3    			Real value of the starting position of the  phi coordinate in  r, (, ( coordinates

[in COMMON /SNGLR/]

S(6) 			Array of intermediate values used in Runge-Kutta integration

SALT   			Real value of the starting altitude above the surface of the geoid

[in COMMON /SNGLR/]

SR2  			Runge-Kutta constant (square root of 2.0)

TAU  			Time (in seconds) for a trajectory transit from start to termination

TBETA  		Difference between current value of  (  and starting value of  (

TCY2   			Trigonometric cosine of the vector theta (() angle in  r, (, ( coordinates

[in COMMON /SNGLR/]

TCY3   			Trigonometric cosine of the vector phi (() angle in  r, (, ( coordinates

[in COMMON /SNGLR/]

TENG 			Total energy of particle (kinetic energy plus rest mass energy)

TMS2O2 		Runge-Kutta constant (2.0 - SR2/2.0)

TPS2O2 		Runge-Kutta constant ((2.0 + SR2/2.0)

TSTEP  		Number steps executed in this run

TSY2   			Trigonometric sine of the vector theta (() angle in  r, (, ( coordinates

[in COMMON /SNGLR/]

TSY2SQ 		Square of TSY2

TSY3   			Value of the trigonometric sine of the vector phi (() angle in  r, (, ( coordinates

[in COMMON /SNGLR/]

TU100  		Time (in seconds) the particle is under 100 km altitude

VEL    			Particle velocity in earth radii per second [in COMMON /WRKVLU/]

Y(6)  			Array of "Y" values (position and velocity in  r, (, ( coordinates)

[in COMMON /WRKVLU/]

YB(6) 			Array of intermediate values used in Runge-Kutta integration

Y10  			Y(1) radial coordinate for re-entrant distance at this latitude

Y1GC   		Starting position  r  component in geocentric coordinates

Y2GC   		Starting position  (  component in geocentric coordinates

Y3GC   		Starting position  ( component in geocentric coordinates

YDA5 			Intermediate value for computing asymptotic latitude

YMAX 		Maximum radial distance attained by trajectory

ZCHARGE		Atomic charge number

ZED  			Zenith angle in degrees

Reference publication:

Ralston, A, and Wilf, S.H., Mathematical Models for Digital Computers, JohnWiley and Sons, New York, 1960.

Subroutine FGRAD

This subroutine calculates the V X B force on the charged particle.

Arguments in call statement:  none.   All in labeled common

Labeled Common arguments:

Block name:		/WRKVLU/

Arguments in block	F(6), Y(6), ERAD, EOMC, VEL, BR, BT, BP

F(6)		Array of force and acceleration vectors

Y(6)		Array of position and velocity vectors

ERAD		Average radius of the earth in kilometers

EOMC    	Electronic charge divided by relativistic mass energy equivalent (mixed units)

VEL		Particle velocity in earth radii per second

BP		Value of the B(() magnetic field vector (in units of Gauss)

BR		Value of the B(r) magnetic field vector (in units of Gauss)

BT		Value of the B(() magnetic field vector (in units of Gauss)

Block name:		/WRKTSC/

Arguments in block	TSY2, TCY2, TSY3, TCY3

TSY2		Sine of the Y(2) coordinate (theta coordinate)

TCY2		Cosine of the Y(2) coordinate (theta coordinate)

TSY3		Sine of the Y(3) coordinate (phi coordinate)

TCY3		Cosine of the Y(3) coordinate (phi coordinate)

Subroutines called:

MAGNEW95

(All arguments are in labeled common /WRKVLU/ and /WRKTSC/)

Data files: none

Output files: none

Program Operation:

When this subroutine is called, the force vectors, ((F(1), F(2), F(3)) are defined.  The sine and cosine of the Y(2) coordinates are determined.  The magnetic field vectors (BR, BT, BP) at the particle position (Y(1), Y(2), Y(3)) are obtained by the call to subroutine MAGNEW95.  Then the acceleration vectors (F(4), F(5), F(6)) are calculated.

Listing of all variables in subroutine FGRAD in program TJI95

B    			Magnitude of the magnetic field (in Gauss) [in COMMON /WRKVLU/]

BP  			Value of the B(() magnetic field vector (in Gauss) [in COMMON /WRKVLU/]

BR  			Value of the B(r) magnetic field vector (in Gauss) [in COMMON /WRKVLU/]

BT  			Value of the B(() magnetic field vector (in Gauss) [in COMMON /WRKVLU/]

EOMC    		Electronic charge divided by relativistic mass energy equivalent (mixed units)

[in COMMON /WRKVLU/]

ERAD  			Average radius of the earth in kilometers [in COMMOM /WRKVLU/]

F(6)			Array of  "F" values (velocity and acceleration in program coordinates)

[in COMMON /WRKVLU/]

SQY6 			Intermediate term (Y6)*Y(6)/Y(1)

TAY2 			Intermediate term TSY2/TSC2

TCY2   			Trigonometric cosine of the vector theta angle in  r, (, ( coordinates

[in COMMON /SNGLR/]

TCY3   			Trigonometric cosine of the vector phi angle in  r, (, ( coordinates

[in COMMON /SNGLR/]

TSY2   			Trigonometric sine of the vector theta (() angle in  r, (, ( coordinates

[in COMMON /SNGLR/]

TSY3   			Trigonometric sine of the vector phi (() angle in  r, (, ( coordinates

[in COMMON /SNGLR/]

VEL    			Particle velocity in earth radii per second [in COMMON /WRKVLU/]

Y(6)  			Array of "Y" values (position and velocity in  r, (, ( coordinates)

[in COMMON /WRKVLU/]

Y5OY1 		Intermediate term Y(5)/Y(1)

Subroutine MAGNEW95

This is the magnetic field evaluation program containing the IGRF95 magnetic field model.  The normalized magnetic field coefficients have been pre-processed and loaded in as data statements.  This is a serial computation designed to repeatedly evaluate the same magnetic field model at different positions in space at optimum efficiency.  Each term of the magnetic field expansion is the derivative of the pervious term.

Arguments in call statement:  none.  (All in labeled common)

Labeled Common arguments:

Block name:		/WRKVLU/

Arguments in block	F(6), Y(6), ERAD, EOMC, VEL, BR, BT, BP

F(6)		Array of force and acceleration vectors

Y(6)		Array of position and velocity vectors

ERAD		Average radius of the earth in kilometers

EOMC    	Electronic charge divided by relativistic mass energy equivalent (mixed units)

VEL		Particle velocity in earth radii per second

BP		Value of the B(() magnetic field vector (in units of Gauss)

BR		Value of the B(r) magnetic field vector (in units of Gauss)

BT		Value of the B(() magnetic field vector (in units of Gauss)

Block name:		/WRKTSC/

Arguments in block	TSY2, TCY2, TSY3, TCY3

TSY2		Sine of the Y(2) coordinate (theta coordinate)

TCY2		Cosine of the Y(2) coordinate (theta coordinate)

TSY3		Sine of the Y(3) coordinate (phi coordinate)

TCY3		Cosine of the Y(3) coordinate (phi coordinate)

Dimensioned variables: (not in labeled common)

G(11,11), BM(11)

G(11,11) 		Normalized coefficients ordered for fast serial computation

BM(11) 		Values to determine if the expansion should terminated at order N

Program Operation:

This subroutine is designed for efficient serial computation of the earth's main magnetic field.  This procedure expands the terms into FORTRAN coding (resulting in pages and pages of FORTRAN code) and then evaluates the normalized field coefficients.  The result of this serial expansion is approximately an order of magnitude speed increase over the recursion method which is much more compact in program size but requires the expansion of the Legender polynomials each time the subroutine is called.

When this subroutine is called it checks the value of the variable JDATA.  If JDATA is not 77, then it loads in the data coefficients; otherwise it proceeds directly to the magnetic field evaluation.  The array G(11,11) contains the pre-processed and normalized  magnetic field model coefficients ordered for fast serial computation.  The array BM(11) contains a set of values that determine if the expansion should be terminated above a specified order because the additional contribution of the magnetic field would not be significant.  (This is an additional technique to speed up the computation.)

At the beginning of the magnetic field determination, the sine and cosine of Y(3) (the phi coordinate) are calculated.  (This has not been done since the completion of the last Runge-Kutta step.)  It then determines the value of the AR variable; AR is reciprocal of the radial distance, (Y(1)) ,in earth radii.  Each order of the field expansion requires an evaluation of ARN where N is the order of the field expansion.  (The N = 1 term, a description of a monopole magnetic field, is zero.)  The first magnetic field evaluation designated by N = 2 is the dipole field component.  Each subsequent order of expansion evaluates the contribution of the next order and adds this to the contribution of the previous orders.  The final computation converts the magnetic field vectors to units of Gauss.  ( One Gauss - 105 Nt).  A more detailed description of the process is given in NSSDC DATA USERS NOTE 68-11.

Listing of all variables in subroutine MAGNEW95

AOR  			Temporary value of radial distance (in earth radii) to the Nth power

AR  			1.0/Radial distance (in earth radii) [AR = 1.0/Y(1)]

B    			Magnitude of the magnetic field (in Gauss) [in COMMON /WRKVLU/]

BERR  			Variable for dropping terms if field magnitude is less than significant value

(set to 0.001 for improved accuracy)

BM(11)			Array of check values for dropping terms of magnetic field expansion

BP  			Value of the B(() magnetic field vector (in Gauss) [in COMMON /WRKVLU/]

BR  			Value of the B(r) magnetic field vector (in Gauss) [in COMMON /WRKVLU/]

BT  			Value of the B(() magnetic field vector (in Gauss) [in COMMON /WRKVLU/]

DP101  		Derivative of the polynomial (10,1) term

DP102  		Derivative of the polynomial (10,2) term

DP103  		Derivative of the polynomial (10,3) term

DP104  		Derivative of the polynomial (10,4) term

DP105  		Derivative of the polynomial (10,5) term

DP106  		Derivative of the polynomial (10,6) term

DP107  		Derivative of the polynomial (10,7) term

DP108  		Derivative of the polynomial (10,8) term

DP109  		Derivative of the polynomial (10,9) term

DP111  		Derivative of the polynomial (11,1) term

DP1110  		Derivative of the polynomial (11,10) term

DP1111  		Derivative of the polynomial (11,11) term

DP112  		Derivative of the polynomial (11,2 term

DP113  		Derivative of the polynomial (11,3 term

DP114  		Derivative of the polynomial (11,4) term

DP115  		Derivative of the polynomial (11,5) term

DP116  		Derivative of the polynomial (11,6) term

DP117  		Derivative of the polynomial (11,7) term

DP118  		Derivative of the polynomial (11,8) term

DP119  		Derivative of the polynomial (11,9) term

DP21  			Derivative of the polynomial (2,1) term

DP22  			Derivative of the polynomial (2,2) term

DP31  			Derivative of the polynomial (3,1) term

DP32  			Derivative of the polynomial (3,2) term

DP33  			Derivative of the polynomial (3,3) term

DP41  			Derivative of the polynomial (4,1) term

DP42  			Derivative of the polynomial (4,2) term

DP43  			Derivative of the polynomial (4,3) term

DP44  			Derivative of the polynomial (4,4) term

DP51  			Derivative of the polynomial (5,1) term

DP52  			Derivative of the polynomial (5,2) term

DP53  			Derivative of the polynomial (5,3) term

DP54  			Derivative of the polynomial (5,4) term

DP55  			Derivative of the polynomial (5,5) term

DP61  			Derivative of the polynomial (6,1) term

DP62  			Derivative of the polynomial (6,2) term

DP63  			Derivative of the polynomial (6,3) term

DP64  			Derivative of the polynomial (6,4) term

DP65  			Derivative of the polynomial (6,5) term

DP66  			Derivative of the polynomial (6,6) term

DP71  			Derivative of the polynomial (7,1) term

DP72  			Derivative of the polynomial (7,2) term

DP73  			Derivative of the polynomial (7,3) term

DP74  			Derivative of the polynomial (7,4) term

DP75  			Derivative of the polynomial (7,5) term

DP76  			Derivative of the polynomial (7,6) term

DP77  			Derivative of the polynomial (7,7) term

DP81  			Derivative of the polynomial (8,1) term

DP82  			Derivative of the polynomial (8,2) term

DP83  			Derivative of the polynomial (8,3) term

DP84  			Derivative of the polynomial (8,4) term

DP85  			Derivative of the polynomial (8,5) term

DP86  			Derivative of the polynomial (8,6) term

DP87  			Derivative of the polynomial (8,7) term

DP88  			Derivative of the polynomial (8,8) term

DP91  			Derivative of the polynomial (9,1) term

DP92  			Derivative of the polynomial (9,2) term

DP93  			Derivative of the polynomial (9,3) term

DP94  			Derivative of the polynomial (9,4) term

DP95  			Derivative of the polynomial (9,5) term

DP96  			Derivative of the polynomial (9,6) term

DP97  			Derivative of the polynomial (9,7) term

DP98  			Derivative of the polynomial (9,8) term

DP99  			Derivative of the polynomial (9,9) term

DP1010  		Derivative of the polynomial (10,10) term

EOMC    		Electronic charge divided by relativistic mass energy equivalent (mixed units)

(not used in this subroutine) [in COMMON /WRKVLU/]

ERAD  			Average radius of the earth in kilometers (not used in this subroutine)

[in COMMOM /WRKVLU/]

ERR  			Intermediate term used to evaluate when higher order terms can be dropped

F(6)			Array of  "F" values (velocity and acceleration in program coordinates)

[in COMMON /WRKVLU/]

G(11,11)  		Array of normalized magnetic field coefficients ordered for fast computation

GMSUM  		Check value to assure that proper magnetic field coefficients are loaded

GSUM  		Check data for testing that proper magnetic field coefficients are loaded

JDATA  		Integer test value for loading in data statement for magnetic field coefficients

JMAG  			Integer order of magnetic field expansion (N+1)

L  			Intermediate index for data checking

M  			Intermediate index for data checking

MGNMAX  		Integer value of maximum order of magnetic field expansion

P101  			Polynomial (10,1) term

P1010 			Polynomial (10,10) term

P102  			Polynomial (10,2) term

P103  			Polynomial (10,3) term

P104  			Polynomial (10,4) term

P105  			Polynomial (10,5) term

P106  			Polynomial (10,6) term

P107  			Polynomial (10,7) term

P108  			Polynomial (10,8) term

P109  			Polynomial (10,9) term

P111    			Polynomial (11,1) term

P1110   		Polynomial (11,10) term

P1111 			Polynomial (11,11) term

P112  			Polynomial (11,2 term

P113  			Polynomial (11,3 term

P114  			Polynomial (11,4) term

P115  			Polynomial (11,5) term

P116  			Polynomial (11,6) term

P117  			Polynomial (11,7) term

P118  			Polynomial (11,8) term

P119  			Polynomial (11,9) term

P21  			Polynomial (2,1) term

P22  			Polynomial (2,2) term

P31  			Polynomial (3,1) term

P32  			Polynomial (3,2) term

P33  			Polynomial (3,3) term

P41  			Polynomial (4,1) term

P42  			Polynomial (4,2) term

P43  			Polynomial (4,3) term

P44  			Polynomial (4,4) term

P51  			Polynomial (5,1) term

P52  			Polynomial (5,2) term

P53  			Polynomial (5,3) term

P54  			Polynomial (5,4) term

P55  			Polynomial (5,5) term

P61  			Polynomial (6,1) term

P62  			Polynomial (6,2) term

P63  			Polynomial (6,3) term

P64  			Polynomial (6,4) term

P65  			Polynomial (6,5) term

P66  			Polynomial (6,6) term

P71  			Polynomial (7,1) term

P72  			Polynomial (7,2) term

P73  			Polynomial (7,3) term

P74  			Polynomial (7,4) term

P75  			Polynomial (7,5) term

P76  			Polynomial (7,6) term

P77  			Polynomial (7,7) term

P81  			Polynomial (8,1) term

P82  			Polynomial (8,2) term

P83  			Polynomial (8,3) term

P84  			Polynomial (8,4) term

P85  			Polynomial (8,5) term

P86  			Polynomial (8,6) term

P87  			Polynomial (8,7) term

P88  			Polynomial (8,8) term

P91  			Polynomial (9,1) term

P92  			Polynomial (9,2) term

P93  			Polynomial (9,3) term

P94  			Polynomial (9,4) term

P95  			Polynomial (9,5) term

P96  			Polynomial (9,6) term

P97  			Polynomial (9,7) term

P98  			Polynomial (9,8) term

P99    			Polynomial (9,9) term

RC10  			Intermediate value (N=10) in magnetic field expansion

RC11  			Intermediate value (N=11) in magnetic field expansion

RC2  			Intermediate value (N=2) in magnetic field expansion

RC3  			Intermediate value (N=3) in magnetic field expansion

RC4  			Intermediate value (N=4) in magnetic field expansion

RC5  			Intermediate value (N=5) in magnetic field expansion

RC6  			Intermediate value (N=6) in magnetic field expansion

RC7  			Intermediate value (N=7) in magnetic field expansion

RC8  			Intermediate value (N=8) in magnetic field expansion

RC9  			Intermediate value (N=9) in magnetic field expansion

TCP10  		Trigonometric cosine function for the P10 term

TCP11  		Trigonometric cosine function for the P11 term

TCP2  			Trigonometric cosine function for the P2 term

TCP3  			Trigonometric cosine function for the P3 term

TCP4  			Trigonometric cosine function for the P4 term

TCP5  			Trigonometric cosine function for the P5 term

TCP6  			Trigonometric cosine function for the P6 term

TCP7  			Trigonometric cosine function for the P7 term

TCP8  			Trigonometric cosine function for the P8 term

TCP9  			Trigonometric cosine function for the P9 term

TCY2   			Trigonometric cosine of the vector theta angle in  r, (, ( coordinates

[in COMMON /SNGLR/]

TCY3   			Trigonometric cosine of the vector phi angle in  r, (, ( coordinates

[in COMMON /SNGLR/]

TSP10  			Trigonometric sine function for the P10 term

TSP11  			Trigonometric sine function for the P11 term

TSP2   			Trigonometric sine function for the P2 term

TSP3  			Trigonometric sine function for the P3 term

TSP4  			Trigonometric sine function for the P4 term

TSP5  			Trigonometric sine function for the P5 term

TSP6  			Trigonometric sine function for the P6 term

TSP7  			Trigonometric sine function for the P7 term

TSP8  			Trigonometric sine function for the P8 term

TSP9  			Trigonometric sine function for the P9 term

TSY2   			Trigonometric sine of the vector theta angle in  r, (, ( coordinates

[in COMMON /SNGLR/]

TSY3   			Trigonometric sine of the vector phi angle in  r, (, ( coordinates

[in COMMON /SNGLR/]

VEL    			Particle velocity in earth radii per second (not used in this subroutine)

[in COMMON /WRKVLU/]

Y(6)  			Array of "Y" values (position and velocity in  r, (, ( coordinates)

[in COMMON /WRKVLU/]

Reference publication:

Computation of the Main Geomagnetic Field for Spherical Harmonic Expansion, Data Users Note NSSDC 68-11, February 1968, NSDC, NASA, GFSC, Greenbelt MD.