Intelligent Transportation Systems (ITS)

Commercial Vehicle Operations (CVO)

Procedures for SAFER / CVIEW Electronic
Data Interchange (EDI)
Data Exchange

CVIEW (Version 3.x)

Draft Version D.1

SSD-POR-02-7382

December 2002

Prepared for:

US Department of Transportation

Federal Motor Carrier Safety Administration

400 Seventh Street, SW

Washington, DC  20590

Prepared by:

The Johns Hopkins University

Applied Physics Laboratory

11100 Johns Hopkins Road

Laurel, MD  20723

The Motor Carrier Safety Improvement Act was signed into law on December 9, 1999.  This act established a new Federal Motor Carrier Safety Administration (FMCSA) within the US Department of Transportation (DOT), effective January 1, 2000.  Prior to that, the motor carrier and highway safety program was administered under the Federal Highway Administration (FHWA).

The mission of the FMCSA is to improve truck and commercial passenger carrier safety on our nation’s highways through information technology, targeted enforcement, research and technology, outreach, and partnerships. The FMCSA manages the ITS/Commercial Vehicle Operations (CVO) Program, a voluntary effort involving public and private partnerships that uses information systems, innovative technologies, and business practice reengineering to improve safety, simplify government administrative systems, and provide savings to states and motor carriers. The FMCSA works closely with the FHWA’s ITS JPO to ensure the integration and interoperability of ITS/CVO systems with the national ITS program.

Please note that this is a Draft Issue

It is important to note that this is a draft document.  The document is incomplete and may contain sections that have not been completely reviewed internally.  The material presented herein will undergo several iterations of review and comment before a baseline version is published.

Note: This document and other CVISN-related documentation are available for review and downloading by the ITS/CVO community from the JHU/APL CVISN site on the World Wide Web.  The URL for the CVISN site is: http://www.jhuapl.edu/cvisn/.

Review and comments to this document are welcome.  For more information, please contact:

The Johns Hopkins University

Applied Physics Laboratory

11100 Johns Hopkins Road

Laurel, MD  20723-6099

Ms. Theresa G. Nester

Phone:		(240) 228-8760

Fax:		(240) 228-6149

E-Mail:	theresa.nester@jhuapl.edu

Procedures for SAFER/CVIEW

EDI Data Exchange

CVIEW (Version 3.x)

Table of Contents

1	Introduction	1–1

1.1	Purpose	1–1

1.2	Scope and Applicability	1–1

1.3	Responsible Organizations	1–1

1.4	Document Organization	1–1

2	Download Data From SAFER	2–1

2.1	Approval Process	2–1

2.2	State Mailbox at SAFER	2–2

2.3	Communications	2–2

2.4	Subscription	2–2

2.4.1	Carrier Subscription Properties and Registration Data	2–2

2.4.2	Vehicle Subscription Properties and Registration Data	2–4

2.5	Testing	2–5

2.6	Final Notification and Configuration	2–5

3	Upload Data to SAFER	3–1

3.1	Approval Process	3–1

3.2	SAFER Mailbox at the State System	3–1

3.3	Communications	3–1

3.4	Subscription	3–1

3.4.1	Organization Data	3–2

3.4.2	Carrier Subscription Registration	3–2

3.4.3	Vehicle Subscription Registration	3–3

3.5	Testing	3–3

3.5.1	General Connectivity Tests	3–3

3.5.2	Interface Tests	3–3

3.5.3	E-mail Tests	3–4

3.6	Final Notification and Configuration	3–4

4	Interoperability Testing	4–1

4.1	Preparation	4–1

4.1.1	Mailbox Setup	4–1

4.1.2	Registry Modification	4–1

4.1.3	Subscription Creation	4–2

4.2	Troubleshooting	4–2

4.3	Test Completion	4–3

5	References 	5–1

Appendix A. Contacts	A–1

Appendix B. Process Flow	B–1

B.1	Download from SAFER	B–3

B.2	Upload to SAFER	B–4

Appendix C. Procedures to Create Subscriptions	C–1

C.1	Start OpCon	C–3

C.2	Create an Organization	C–4

C.3	Create a User	C–7

C.4	Register a User for an Existing Carrier Subscription	C–11

C.5	Register a User for an Existing Vehicle Subscription	C–17

C.6	Create a New 'Carrier' Subscription	C–23

C.7	Create a New 'Vehicle' Subscription	C–29

C.8	Show Subscription Properties	C–34

C.9	Show Subscription Registration Properties	C–37

C.10	Subscriptions Needed for Interoperability Testing	C–39

Appendix D. Forms	D–1

List of Tables

Table 2–1. State Organization Data	2–1

Table 2–2. Carrier Subscription Registration Data	2–2

Table 2–3. Carrier Data Views and Versions	2–3

Table 2–4. Vehicle Subscription Registration Data	2–4

Table 2–5. Vehicle Data Views and Versions	2–4

Table 3–1. SAFER Organization Data	3–2

Table 3–2. SAFER Carrier Subscription Registration Data at the State CVIEW	3–2

Table 3–3. SAFER Vehicle Subscription Registration Data at the State CVIEW	3–3

List of Diagrams

Diagram B-1: Download Process	B–3

Diagram B-2: Upload Process	B–4

Diagram C-1: OpCon Control Bar	C–3

Diagram C-2:  Managers Menu	C–4

Diagram C-3: Organization Manager Window	C–4

Diagram C-4: Create New Organization Selection	C–5

Diagram C-5: Create New Organization Window	C–6

Diagram C-6: Added Organization	C–6

Diagram C-7: User Manager Selection	C–7

Diagram C-8: User Manager Window	C–7

Diagram C-9: Create New User Selection	C–8

Diagram C-10: Create New User Window	C–9

Diagram C-11: Network Account Description Window	C–10

Diagram C-12: Added User	C–10

Diagram C-13: Subscription Manager Selection	C–11

Diagram C-14: Subscription Manager Window	C–11

Diagram C-15: Add Registrations Selection	C–12

Diagram C-16: New Subscription Registration Properties Window	C–13

Diagram C-17: Register Accounts to Subscription #1 Window	C–14

Diagram C-18: User Registered	C–15

Diagram C-19: Completed Registration	C–16

Diagram C-20: Subscription Manager Window	C–17

Diagram C-21: Add Registrations Selection	C–18

Diagram C-22: New Subscription Registration Properties Window	C–19

Diagram C-23: Register Accounts to Subscription #2 Window	C–20

Diagram C-24: User Registered for Subscription #2	C–21

Diagram C-25: Completed Registration	C–22

Diagram C-26: Create New Subscription Selection	C–23

Diagram C-27: Create New Subscription Window	C–24

Diagram C-28: Create New Subscription (2 of 3)	C–24

Diagram C-29: Select DOT Numbers Window	C–25

Diagram C-30: Enter DOT Number Window	C–25

Diagram C-31: Select States Window	C–26

Diagram C-32: Create New Subscription (3 of 3)	C–27

Diagram C-33: Completed New Carrier Subscription	C–28

Diagram C-34: Create New Subscription Window	C–29

Diagram C-35: Create New Subscription (2 of 3)	C–30

Diagram C-36: IRP Base States Selection Window	C–31

Diagram C-37: Create New Subscription (3 of 3)	C–32

Diagram C-38: Completed Vehicle Subscription	C–33

Diagram C-39: Select Subscription	C–34

Diagram C-40: Properties of Subscription #1 (1 of 3)	C–35

Diagram C-41: Properties of Subscription #1 (2 of 3)	C–35

Diagram C-42: Properties of Subscription #1 (3 of 3)	C–36

Diagram C-43: Select Subscription	C–37

Diagram C-44: Registrations for Subscription #1 Window	C–37

Diagram C-45: Subscription Registration Properties Window	C–38

# Introduction

## Purpose

This document contains information for states new to the Safety and Fitness Electronic Records (SAFER) System /Commercial Vehicle Information Exchange Window (CVIEW) System data exchange process.  It provides information on setting up CVIEW (Version 3.x) to receive data from, and send data to, SAFER.  The procedures can be used to set up data exchange for both a test environment or for production operations.

## Scope and Applicability

The primary audience for this document is a state CVIEW administrator.

The information contained in this document describes CVIEW (Version 3.x) data exchange with SAFER.  The data format is assumed to be transactions approved by American National Standards Institute (ANSI) Accredited Standards Committee (ASC) X12 Electronic Data Interchange (EDI).

## Responsible Organizations

State CVIEW Administrator – Responsible for state system configuration, and routine and maintenance operations.

Volpe National Transportation Systems Center – Hosts the operational SAFER and creates and maintains user identifiers and subscriptions, provides communications testing.

The Johns Hopkins University Applied Physics Laboratory (JHU/APL) – Developed SAFER and the Federal Motor Carrier Safety Administration (FMCSA) CVIEW and maintains the Commercial Vehicle Information Systems and Networks (CVISN) Test Facility to support initial and on-going interoperability testing activities.  Using this facility, testers verify that products claiming to be compatible with standard interfaces are actually compliant.

## Document Organization

This document is divided into several sections:

The first section, INTRODUCTION, identifies the intended audience for this document and the organizations involved in SAFER data exchange.

The second section, DOWNLOAD DATA FROM SAFER, covers the steps a state must follow to retrieve subscriptions from SAFER.

The third section, UPLOAD DATA TO SAFER, identifies the procedures a state must follow to fulfill subscriptions to SAFER.

The fourth section, INTEROPERABILITY TESTING, provides guidance in preparing to test the state’s ability to retrieve and fulfill subscriptions.

The fifth section, REFERENCES, provides sources for additional information about CVIEW, SAFER, and CVISN.

The document ends with appendices organized as follows:

CONTACTS: provides names and communication numbers of staff members at APL and Volpe

PROCESS FLOW: provides a graphical representations of the download (subscription retrieval) and upload (subscription fulfillment) processes

PROCEDURES TO CREATE SUBSCRIPTIONS: provides an example of the procedures that may be used by a State to create and maintain subscriptions

FORMS: contains paper forms used in sending information to Volpe to set up state user IDs and mailboxes on SAFER, and to register the user for SAFER snapshots.

# Download Data From SAFER

To receive data of interest from SAFER, a state must request an account (Section 2.1), a mailbox (Section 2.2), register for one or more subscriptions (Section 2.4) at Volpe, and successfully perform tests (Section 2.5).  A subscription is a standing query specifying a predefined set of conditions to be stored and re-processed by the data source (SAFER, in this case) to forward data to an external system or user at future times.  Refer to Section B.1 for the activity flow diagram for the download process.

## Approval Process

FMCSA must approve each state’s request for data from SAFER.  The state contacts Volpe to request SAFER data.  The administrator at Volpe will ask FMSCA for the authorization to establish the user and mailbox based on the organizational data provided by the state.  (See Table 2–1 or Appendix D for the necessary data and Appendix A for contact information.)

Table 2–1.
State Organization Data

| Item | Required | Description |
| --- | --- | --- |
| Jurisdiction | Yes | Jurisdiction requesting the subscription |
| Organization Name | Yes | Name of organization, e.g., Maryland Dept. of Transportation |
| Sub-Organization Name | No | Division or sub-unit within the organization, e.g., Commercial Vehicles |
| Sub-Organization Short Name | No | An abbreviated name for the division or sub-unit within the organization, e.g., ComVeh |
| State Contact Name | Yes | First and last name |
| State Contact Address | Yes | Street, City, State, Zip Code, Country |
| State Contact Communication Number | Yes | Phone is required; FAX and e-mail are optional |
| Contractor Name | No | First and last name |
| Contractor Address1 | No | Street, City, State, Zip Code, Country |
| Contractor Communication Number1 | No | If a contractor is supplied, phone is required; FAX and e-mail are optional |

## State Mailbox at SAFER

Volpe will establish the state user ID and mailbox using the configuration instructions provided in Reference [1].  The state mailbox is named CVIEWxx where xx is a two-character jurisdiction code.  This is the mailbox the state accesses to retrieve its subscriptions from SAFER.  The NT user ID is the same as the mailbox.  Password is provided by Volpe.  The state will modify its registry settings to identify the state mailbox on the SAFER system in accordance with Reference [1].  The following table contains information needed to set up an account for a state.

## Communications

See Reference [2] and contact Volpe for additional information on communication options such as AAMVAnet, IPSEC, and FTS2001.  See Reference [2] for details on sending and receiving e-mail from SAFER.  See Section 4 for testing procedures.

## Subscription

To receive data of interest, a subscription must be established at Volpe.  The following sections specify the information to be provided.

### Carrier Subscription Properties and Registration Data

The information in Table 2–2 is required to register a state as a user of a carrier subscription.

Table 2–2.
Carrier Subscription Registration Data

| Item | Description |
| --- | --- |
| Product Type | Specify 'Carrier Snapshot' |
| Periodicity | Frequency to send the data. Your choices are: Next Update Immediately |
| States to monitor | A list of states (carrier’s legal address state). Carrier snapshots for these states will be sent to you if something in the snapshot has changed. User may specify 'All states', or a specific list. |
| Data View | Determines which carrier snapshot fields you will receive. (Refer to Table 2–3, and References [4] and [5].) |
| View Version | A version identifier for the data view. (Refer to Table 2–3, and References [4] and [5].) |
| Data Format | Specify 'EDI' |
| Compression | Specify 'Zip' |

Table 2–3 provides the names and descriptions of the carrier views.  For CVIEW (Version 3.x), the view version is '4' for all views.  The View ID identifies the data elements in the view as given in References [4] and [5].

Table 2–3.
Carrier Data Views and Versions

| Data View | View Version | Description | View ID |
| --- | --- | --- | --- |
| Full | 4 | The full view includes all SAFER snapshot data pertaining to the carrier. | Q105 |
| E-Screening | 4 | Contains the information necessary to register carriers in multiple screening programs and to permit screening by transponder ID across boundaries of jurisdictions and screening programs. | Q104 |
| IFTA | 4 | Contains the information necessary to update International Fuel Tax Agreement (IFTA) credentials information in the carrier snapshot. | Q109 |
| IRP | 4 | Contains the information necessary to update International Registration Program (IRP) credentials information in the carrier snapshot. | Q111 |
| ISS-2 | 4 | Contains the SAFER data required to support the identification of the carrier and the computation of the Inspection Selection System (ISS) score for use in determining vehicles to be inspected. | Q110 |
| L&I (License and Insurance) | 4 | Includes the information from the Licensing and Insurance System obtained from the Interstate Commerce Commission (ICC) and maintained by FMCSA. | Q107 |
| MCMIS | 4 | Details the information supplied to SAFER by the FMCSA Motor Carrier Management Information System (MCMIS) about the safety, safety review, and inspection history of interstate motor carriers. | Q102 |

### Vehicle Subscription Properties and Registration Data

The information in Table 2–4 is required to register a state as a user of a vehicle subscription.

Table 2–4.
Vehicle Subscription Registration Data

| Item | Description |
| --- | --- |
| Product Type | Specify 'Vehicle Snapshot' |
| Periodicity | Specify 'Immediately' |
| IRP Base States to monitor* | A list of IRP base states. Vehicle snapshots from these base states will be sent to you if something in the snapshot has changed. User may specify 'All States', or provide a specific list. |
| States of Operation to monitor* | A list of IRP states of operation. Vehicle snapshots from these states of operation will be sent to you if something in the snapshot has changed. User may specify 'All States', provide a specific list, or specify the user’s state only. |
| Data View | Determines which vehicle snapshot fields you will receive. (Refer to Table 2–5 and References [4] and [5].) |
| View Version | A version identifier for the data view. (Refer to Table 2–5 and References [4] and [5].) |
| Data Format | Specify 'EDI' |
| Compression | Specify 'None' |

Table 2–5 provides the names and descriptions of the vehicle views.  For CVIEW (Version 3.x), the view version is '4' for all views.  The View ID identifies the data elements in the view as given in References [4] and [5].

Table 2–5.
Vehicle Data Views and Versions

| Data View | View Version | Description | View ID |
| --- | --- | --- | --- |
| Full | 4 | Includes all SAFER snapshot data pertaining to the vehicle. | Q303 |
| E-Screening | 4 | Contains the information necessary to register a carrier’s vehicles in multiple screening programs and to permit screening by transponder ID across boundaries of jurisdictions and screening programs. | Q305 |
| INSP (Inspection Overview) | 4 | Contains information provided by an inspector at the roadside. It includes the identification and safety information from an ASPEN inspection report used to update SAFER and CVIEW. This information provides guidance to the inspectors about past problem areas that should be reviewed in future inspections. | Q302 |
| IRP (no TagID) | 4 | To facilitate the update of snapshots with registration IRP information equivalent to what is carried in the vehicle now. | Q306 |

## Testing

States should first test their system with example snapshot (EDI) output from SAFER.  See Reference [3] for candidate interoperability tests for SAFER-CVIEW data exchange.  States may request sample EDI snapshot data from APL.

When these interoperability tests are completed successfully, a state should then retrieve a test snapshot inserted into its mailbox on SAFER by Volpe.  The state’s processing system should correctly process the data.

## Final Notification and Configuration

When the state is ready to receive SAFER data, the state will notify Volpe to turn on the subscription (i.e., register the state for the subscription).  The state must turn on its timer to retrieve snapshots in accordance with Reference [1].

This Page Intentionally Blank

# Upload Data to SAFER

To send data of interest to SAFER, a state must establish a mailbox for SAFER on the state system (Section 3.2) and register SAFER for one or more subscriptions (Section 3.4) at the state level.  Refer to Section C.2 for the activity flow diagram for the upload process.

## Approval Process

Before setting up SAFER to retrieve data from the state, Volpe will require interoperability and communication tests to be conducted.  (See Section 4).

## SAFER Mailbox at the State System

A mailbox named 'SAFER' shall be established on the state system via OpCon.  This is the mailbox SAFER will access to retrieve its subscriptions from the state.  The NT user name for SAFER on the state system is also named 'SAFER'.  The password is provided by the state.  Volpe will modify its registry settings to identify the SAFER mailbox on the state system in accordance with Reference [1].

## Communications

See Reference [2] and contact Volpe for additional information on communication options such as AAMVAnet, IPSEC, and FTS2001.  See Reference [2] for details of sending e-mails to SAFER.

## Subscription

To send data of interest, one or more subscriptions must be established for SAFER at the state system.  The following sections specify the information relevant to SAFER.  See Appendix C for procedures that may be used to set up SAFER subscriptions at a state using OpCon.

### Organization Data

The following table contains the information necessary to establish an account for SAFER at the state.

Table 3–1.
SAFER Organization Data

| Item | Value |
| --- | --- |
| Organization Name | SAFER |
| Sub-Organization Name | None |
| Sub-Organization Short Name | None |
| Contact Name | Dan Coelho |
| Contact Address | Volpe |
| Phone | 617-374-5031 |
| E-mail | Coelho@Volpe.dot.gov |

### Carrier Subscription Registration

Table 3–2 contains the carrier subscriptions to be registered for SAFER at the state CVIEW.

Table 3–2.
SAFER Carrier Subscription Registration Data at the State CVIEW

| Subscription | Item | Description |
| --- | --- | --- |
| Carrier E-Screening | Product Type | Carrier Snapshot |
|  | Periodicity | Immediately |
|  | States to include | (Your state) |
|  | Event Fields | E-Screen View Fields |
|  | Data View - Version | Carrier E-Screen - 4 |
|  | Data Format | EDI |
|  | EDI Version | 4010 |
|  | Compression | None |
|  | Max. Bundling and Status | Use defaults |
| Carrier IFTA | Item | Description |
|  | Product Type | Carrier Snapshot |
|  | Periodicity | Immediately |
|  | States to include | (Your state) |
|  | Event Fields | IFTA View Fields |
|  | Data View - Version | Carrier IFTA - 4 |
|  | Data Format | EDI |
|  | EDI Version | 4010 |
|  | Compression | None |
|  | Max. Bundling and Status | Use defaults |

### Vehicle Subscription Registration

Table 3–3 contains the vehicle subscriptions to be registered for SAFER at the state CVIEW.

Table 3–3.
SAFER Vehicle Subscription Registration Data at the State CVIEW

| Vehicle E-Screening | Item | Description |
| --- | --- | --- |
|  | Product Type | Carrier Snapshot |
|  | Periodicity | Immediately |
|  | IRP Base States to include | (Your state) |
|  | Event Fields | E-Screen View Fields |
|  | Data View - Version | Vehicle E-Screen - 4 |
|  | Data Format | EDI |
|  | EDI Version | 4010 |
|  | Compression | None |
|  | Max. Bundling and Status | Use defaults |
| IRP (no TagID) | Item | Description |
|  | Product Type | Vehicle Snapshot |
|  | Periodicity | Immediately |
|  | IRP Base States to include | (Your state) |
|  | Event Fields | IRP no TagID View Fields |
|  | Data View - Version | IRP no TagID - 4 |
|  | Data Format | EDI |
|  | EDI Version | 4010 |
|  | Compression | None |
|  | Max. Bundling and Status | Use defaults |

## Testing

### General Connectivity Tests

Volpe will perform a system test to verify connectivity between the state server and Volpe (e.g., via telnet).

### Interface Tests

See Reference [3] for candidate interoperability tests for SAFER-CVIEW data exchange and Section 4 of this document for information on setting up tests with APL.  APL will notify Volpe upon successful completion of the interface tests.

### E-mail Tests

To test the state’s ability to send e-mails to SAFER according to SAFER’s packaging requirements:

APL will use the 32-bit MailTool to retrieve contents of SAFER mailbox at the State.

Place contents in a temporary folder.

Alternatively, Volpe executes a test using the mail tool and places the contents of e-mail in a test folder.  The Test tool uses the same software as SAFER for extracting attachments.  This demonstrates that e-mail from the state is well formed.

## Final Notification and Configuration

Volpe will set the timer to read the SAFER mailbox at the state and will notify the state to turn on the subscription for SAFER (i.e., register SAFER for the subscription via OpCon).

# Interoperability Testing

This testing verifies the state’s ability to:

retrieve snapshots from the state’s mailbox at APLINT or Volpe

fulfill subscriptions to SAFER by sending a snapshot to the SAFER mailbox at the state

See Reference [3] for details on interoperability testing.

Before starting, the state should contact the APL (see Appendix A, CONTACTS) and set up a time for testing.  The state should also send APL example snapshot EDI files for testing with CVIEW EDI tools.  APL will provide feedback to the state on the syntax and semantics of the EDI files.

## Preparation

### Mailbox Setup

The state must establish users and mailboxes for SAFER and APLINT on the state CVIEW using configuration instructions provided in Reference [1].  APL will create a user and a mailbox for the state at APLINT.

### Registry Modification

Refer to the following sections of the “CVIEW Version 3.3 Configuration Definition Document” of Reference [1] for details on the modifications of the registry needed for mailbox set up:

Section 4, CVIEW Registry Settings

SMTP Mailbox Settings

Error Mailbox Settings

Subscription Mailbox Settings

Section 5, SENDLIST Registry Settings

SMTP Mailbox Settings

Error Mailbox Settings

### Subscription Creation

APL will register the state for carrier (MCMIS and IFTA views) and vehicle subscriptions (IRP and Inspection views) on the APL test server.  Refer to Appendix C for details.  The state must register SAFER for carrier IFTA and vehicle IRP views.

## Troubleshooting

#### Event Viewer

The Event Viewer is a utility providing information about security events, hardware, software, and system problems.  Software applications may create entries in the 'Application Log' to track significant events or errors in processing.  This utility is available on Windows systems under 'Administrative Tools'.

Problems are identified with a 'red light'.  Mailbox problems will be displayed in the 'Application' with 'IMH' in the 'Source' column.  Double-clicking the entry will provide more information.  EDI outbound translation errors typically have 'IOTSERVER' in the 'Source' column.

#### Temporary Files

All 'temporary' files, such as IOX, IIX, IOE, IOG, IOS, MBX (vehicle snapshot), and ZIP (carrier snapshot) files, are transient.  They appear and then disappear from the C:\TEMP directory.  If they persist, this indicates a problem with queries or subscription processing.  Large numbers of these files cause the 'TEMP' directory to get very large and it should be purged occasionally.

During processing, carrier 'MBX' files are renamed to 'ZIPzzzz.zip'.  If there is a read error, 'MBX' files will remain in the 'TEMP' directory and an entry should appear in the 'Event Viewer' (see Section 4.2.1.1).  The ZIP files are unzipped and each record is extracted to an 'IOEnnnn.tmp' file.  The 'IOE' files are submitted to the EDI translator to produce an 'IIEkkkk.tmp' file.  The 'IIE' is used to update the database.  For vehicles, 'IOXnnnn' files are read and processed.

#### Command Line Prompt

IMH_CMDLN.exe is a command line executable to monitor the processing of a received snapshot.  It is useful to use if no errors are evident but processing is not taking place.  For instance, if an e-mail problem prevents the snapshot from being input to CVIEW, this could be used to troubleshoot.

## Test Completion

When testing is complete, reset subscription registrations and mailbox settings to operational status.  Turn off error logging (set IOTLog=0), and remove APLINT as a registered user of the state subscription.  Delete any messages that were sent during testing to the SAFER mailbox on the state system.  Un-register SAFER for any subscriptions for state data.  When Volpe notifies the state that is has turned on the mailbox timer at SAFER to begin reading its CVIEW data mailbox, re-register SAFER for the subscriptions.

This Page Intentionally Blank

# References

[1]	JHU/APL, CVIEW Version 3.3 Configuration Definition Document, Version 1, dated July 2002.  This document is available from the CVISN Web site at http://www.jhuapl.edu/cvisn/.

[2]	JHU/APL, Safety and Fitness Electronic Records (SAFER) System Interface Control Document, POR-99-7129 Baseline V1.0, dated June 2001.  This document is available from the CVISN Web site at http://www.jhuapl.edu/cvisn/.

[3]	JHU/APL, Commercial Vehicle Information Systems and Networks (CVISN) Operational and Architectural Compatibility Handbook (COACH), Part 5, Interoperability Test Criteria, Baseline Version, POR-98-7126 V1.0, dated July 2001.  This document is available from the CVISN Web site at http://www.jhuapl.edu/cvisn/.

[4]	JHU/APL, Safety and Fitness Electronic Records (SAFER) System and Commercial Vehicle Information Exchange Window (CVIEW), Carrier, Vehicle, and Driver Snapshots, White Paper, Baseline Version, dated August 2001.  This document is available from the CVISN Web site at http://www.jhuapl.edu/cvisn/.

[5]	JHU/APL, CVIEW 3 CD Documentation, Snapshot Definitions and Views.  This documentation is available from the CVISN Web site at http://www.jhuapl.edu/cvisn/.

This Page Intentionally Blank

Contacts

This Page Intentionally Blank

Table A–1.

Contacts

| Organization | Name | Phone | FAX | E-mail | Notes |
| --- | --- | --- | --- | --- | --- |
| APL | Goldfarb, Robert | 240-228-7635 | 240-228-6149 | Robert.Goldfarb@jhuapl.edu | SAFER Project Manager and Technical Support |
| APL | North, Paul | 240-228-6627 |  | Paul.North@jhuapl.edu | Safety Systems Program Manager |
| APL | Stuart, Mary | 240-228-7001 | 240-228-6149 | Mary.Stuart@jhuapl.edu | Deployment Support and Interoperability Testing |
| Volpe | Technical Support | 617-374-5090 |  |  | Account, Mailbox and Subscription setup |

This Page Intentionally Blank

Process Flow

This Page Intentionally Blank

Download from SAFER

Diagram B-1: Download Process

Upload to SAFER

Diagram B-2: Upload Process

Procedures to Create Subscriptions

This Page Intentionally Blank

This appendix provides an example of the procedures that may be used by a State to create and maintain subscriptions using OpCon.  The example covers the typical steps involved in registering a new user for one or more subscriptions.

| Step | Action | Section |
| --- | --- | --- |
| 1 | Start OpCon | C.1 |
| 2 | Create an Organization | C.2 |
| 3 | Create a User | C.3 |
| 4 | Register a User for an Existing Carrier Subscription | C.4 |
| 5 | Register a User for an Existing Vehicle Subscription | C.5 |

Examples for creating new carrier and vehicle subscriptions are in Sections C.6 and C.7, respectively.  Section C.8 provides the steps to review the properties of a subscription and Section C.9 provides the steps to review the properties of a subscription registration.  The subscriptions needed for testing are given in Section C.10.

Start OpCon

- Go to Start/Programs/CVIEW/OpCon.

The 'OpCon Control Bar' will be displayed.

Diagram C-1: OpCon Control Bar

Create an Organization

- From the 'OpCon Control Bar', select 'Organization Manager' from the 'Managers' drop-down menu.

Diagram C-2:  Managers Menu

The current organizations are listed in the 'Organization Manager' window.

Diagram C-3: Organization Manager Window

To add an organization, select the 'Create New Organization' icon -  or select the option from the 'Actions' drop-down menu.  This example will add SAFER as an organization.

Diagram C-4: Create New Organization Selection

On the 'Create New Organization' window:

(Required)  Type the Organization name in the 'Organization name' field.

(Optional)  Type a division or sub-organization name in the 'Sub-Organization Name' field.

(Optional)  Enter Contact information fields.

(Required)  Type an Organization ID in the 'Org. ID' field of the Organization ID section (or select the 'Generate Organization ID' button to let OpCon create the Org. ID automatically).

Select 'Active' in the 'Organization Status' section.

Select 'Finish' to close the 'Create New Organization' window.

Diagram C-5: Create New Organization Window

The new organization will be displayed in the 'Organization Manager' window.

Diagram C-6: Added Organization

See Section C.3 to add a user for the organization just created.

Create a User

- From the 'Organization Manager' window, select 'User Manager' from the 'Managers' drop-down menu or select the 'User Manager' icon -

Diagram C-7: User Manager Selection

The users for all organizations will be displayed.

Diagram C-8: User Manager Window

If the organization does not have a User in the list (i.e., the organization is not in the table under 'Organization Name'), select the 'Create New User' icon -  or select 'Create New User' from the 'Actions' menu.

Diagram C-9: Create New User Selection

From the 'Create New User' window:

Select the User’s Organization from the 'Organization' drop-down list.

To identify the State CVIEW’s account on OpCon for purposes of registering users for subscriptions:

(Required)  Type in the new user ID in the 'First Name' field.  The user ID is not to exceed ten (10) characters, including 'sub' if appended for a second mailbox.

On VOLPE, enter cviewxx, where xx is the state

On the state, it would be 'SAFER'

For testing, enter APLINT

Type @ in the 'Middle Initial' field.

In the 'Last Name' field, type

On Volpe, enter state name

On State, enter 'Volpe'

For testing, enter 'ALPINT'

The 'Fill' button may be used to populate the address and communication numbers fields.

(Required)  Select the 'User Type' drop-down list.  The example uses 'SAFER General'.

Select 'Active' in the 'User Status' section.

In the 'User ID and Password' section:

Type the userid (from First Name) in the 'User ID', 'Password,' and 'Confirm Password' fields.

Do not check the' Create additional "sub" account' box for the subscription mailbox.

Do not select the 'Generate User ID and Password' button to have OpCon automatically create the userid and password.

To print the User information select the 'Print' button in the bottom left corner.

Select the 'Finish' button to create the new user account.

Diagram C-10: Create New User Window

Select 'OK' when the 'Network Account Description' window appears.

Diagram C-11: Network Account Description Window

The new user appears in the 'User Manager' window.  Close the 'User Manager' window.

Diagram C-12: Added User

Register a User for an Existing Carrier Subscription

- Select 'Subscription Manager' from the 'Managers' drop-down menu or select the raised 'Subscription Manager' icon -  to add SAFER to the appropriate carrier subscriptions for testing.

Diagram C-13: Subscription Manager Selection

The available Subscriptions, both carrier and vehicle, are listed in the 'Subscription Manager' window.  Scroll through and highlight the subscription needed for testing.  Select the 'Subscription Registration Properties' icon -  or select 'Subscription Properties' from the 'Actions' menu to be sure it is the subscription required (see Section C.8).  In the example, subscription '1' is highlighted.

Diagram C-14: Subscription Manager Window

After highlighting the subscription, select the 'Show Subscription Registrations' icon  or select 'Show Subscription Registrations' from the 'Actions' menu.  (If a new Carrier subscription needs to be created, go to Section C.6.)

The 'Registrations for Subscription #1' window should be displayed.  Select the 'Add Registrations' icon  or select the 'Add Registrations' from the 'Actions' menu.

Diagram C-15: Add Registrations Selection

The 'New Subscription Registration Properties' window appears for the new registration with default values visible.

Select 'Carrier MCMIS - 4' from the 'Data View – Version' drop-down menu for CVIEW (Version 3.x).  (See Table 2–3 for other carrier data views and versions for CVIEW (Version 3.x).)

Select 'EDI' from the 'Data Format' drop-down menu.

Select '4010' from the 'EDI Version' drop-down menu.

For testing, select 'None' from the 'Compression' drop-down menu.

Accept the defaults for 'Max Bundling' and 'Status'.

Select 'Next'.

Diagram C-16: New Subscription Registration Properties Window

The 'Register Accounts to Subscription #1' window should be displayed.

A list of available organizations and users appears on the left and users to be registered on the right.

Select the box in front of the organization to view the available users.

Highlight the user to be registered.

Select the 'Select to subscribe' right arrow button located between 'Available Accounts' and 'Accounts to be Registered'.

Diagram C-17: Register Accounts to Subscription #1 Window

The userid now appears on the right.  Since there are no more users available in the organization, the organization does not appear on the left anymore.

Diagram C-18: User Registered

Select 'OK'

The user’s CVIEW userid now appears in the 'Registrations for Subscription #1' window.

Diagram C-19: Completed Registration

Close the 'Registrations for Subscription' window.

Register a User for an Existing Vehicle Subscription

- Select 'Subscription Manager' from the 'Managers' drop-down menu or select the raised 'Subscription Manager' icon -  to add SAFER to the appropriate vehicle subscriptions for testing (see Diagram C-13).

The available Subscriptions, both carrier and vehicle, are listed in the 'Subscription Manager' window.  Scroll through and highlight the subscription needed for testing.  Select the 'Subscription Registration Properties' icon -  or select 'Subscription Properties' from the 'Actions' menu to be sure it is the one required (see Section C.8).  In the example, subscription '2' is highlighted.

Diagram C-20: Subscription Manager Window

After highlighting the subscription, select the 'Show Subscription Registrations' icon  or select 'Show Subscription Registrations' from the 'Actions' menu.  (If a new Vehicle subscription needs to be created, go Section C.7.)

The 'Registrations for Subscription #2', should be displayed.  Select the 'Add Registrations' icon  or select the 'Add Registrations' from the 'Actions' menu.

Diagram C-21: Add Registrations Selection

The 'New Subscription Registration Properties' window appears for the new registration with default values visible.

Select 'Vehicle IRP no TagID - 4' from the 'Data View – Version' drop-down menu for CVIEW (Version 3.x).  (See Table 2–5 for vehicle data views and versions and CVIEW (Version 3.x).)

Select 'EDI' from the 'Data Format' drop-down menu.

Select '4010' from the 'EDI Version' drop-down menu.

For testing, select 'None' from the 'Compression' drop-down menu.

Accept the defaults for 'Max Bundling' and 'Status'.

Select 'Next'.

Diagram C-22: New Subscription Registration Properties Window

The 'Register Accounts to Subscription #2' window should be displayed.

A list of available organizations and users appears on the left and users to be registered on the right.

Select the box in front of the State’s organization to view the available users.

Highlight the user to be registered.

Select the 'Select to subscribe' right arrow button located between Available Users and Users to be Registered.

Diagram C-23: Register Accounts to Subscription #2 Window

The userid now appears on the right.  Since there are no more users available in the organization, the organization does not appear on the left anymore.

Diagram C-24: User Registered for Subscription #2

Select 'OK'.

The user’s CVIEW userid now appears in the 'Registrations for Subscription #2' window.

Diagram C-25: Completed Registration

Close the 'Registrations for Subscription' window.

Create a New 'Carrier' Subscription

If the desired carrier subscription is not available in Section C.4, select the 'Create New Subscription' icon  or select 'Create New Subscription' from the 'Actions' menu.  The example uses an IFTA view.

Diagram C-26: Create New Subscription Selection

- The 'Create New Subscription' window should be displayed.

Type in a name for the subscription in the 'Subscription Name' field.  This will be a unique name in the subscription manager.

Type in a description for the subscription in the 'Subscription Description' field.

Select 'Carrier Snapshot' from the 'Product Type' drop-down menu.

Select 'Immediately' from the 'Periodicity' drop-down menu.  (Normally, a Carrier subscription’s periodicity would be 'Next Update' for data received from SAFER.)

Select 'Next'.

Diagram C-27: Create New Subscription Window

The 'Create New Subscription (2 of 3)' should be displayed.  Select Carriers by:

DOT Numbers

States - physical address of the carrier (recommended for production)

Exclude certain DOT Numbers

Diagram C-28: Create New Subscription (2 of 3)

Select the 'Change' button for 'DOT Numbers' to add specific test DOT Numbers to the subscription.  (For production processing, leave blank to receive data from all carriers.)  The DOT Numbers window should appear.

Diagram C-29: Select DOT Numbers Window

Select the 'Add' button and type in the test DOT Number.

Diagram C-30: Enter DOT Number Window

Select 'OK'.

If more DOT Numbers are needed, select 'Add' and type in the additional numbers.

Select 'OK' to return to the 'Create New Subscription (2 of 3)' window.

Select the 'Change' button for 'States'.

Diagram C-31: Select States Window

Do one of the following:

For a new subscription created at the state to send data to SAFER, from the 'States' window, select the 'Clear All' box, then scroll through the states, and select your state.

For a new subscription created at the state to send data to systems within the state, such as roadside operations, select the same states as those specified in your request for data from SAFER.

For a new subscription created at Volpe for SAFER data to go to a state, the Volpe administrator would select those states specified in the state’s request for data from SAFER.

Select 'OK' to return to the 'Create New Subscription (2 of 3)' window.

Select 'Next'.

The 'Create New Subscription (3 of 3)' window should appear.

Select the 'IFTA View Fields' radio button.  Only those fields associated with the IFTA view will be monitored for changes.  If there are any changes to the monitored fields, that record will be added to the subscription.

Select 'Finish'.

Diagram C-32: Create New Subscription (3 of 3)

The new subscription will be displayed in the 'Subscription Manager' window.

Diagram C-33: Completed New Carrier Subscription

Create a New 'Vehicle' Subscription

If the desired vehicle subscription is not available in Section C.5, select the 'Create New Subscription' icon  or select 'Create New Subscription' from the 'Actions' menu.  (See Diagram C-26.)  The example adds an inspection subscription as an example.

- The 'Create New Subscription' window should be displayed.

Type in a Name for the Subscription in the 'Subscription Name' field.  This will be a unique name in the subscription manager.

Type in a Description for the Subscription in the 'Subscription Description' field.

Select 'Vehicle Snapshot' from the 'Product Type' drop-down menu.

Select 'Immediately' from the 'Periodicity' drop-down menu.  A Vehicle subscription always uses 'Immediately'.

Select 'Next'.

Diagram C-34: Create New Subscription Window

The 'Create New Subscription (2 of 3)' should be displayed.  Select Vehicles by:

IRP Base States

States of Operation

Diagram C-35: Create New Subscription (2 of 3)

Select the 'Change' button for 'IRP Base States' to add specific IRP base states to the subscription.  The States window should appear.

Diagram C-36: IRP Base States Selection Window

Do one of the following:

For a new subscription created at the state to send data to SAFER, from the 'States' window, select the 'Clear All' box, then scroll through the states, and select your state.

For a new subscription created at the state to send data to systems within the state, such as roadside operations, select the same states as those specified in your request for data from SAFER.

For a new subscription created at Volpe for SAFER data to go to a state, the Volpe administrator would select those states specified in the state’s request for data from SAFER.

Select 'OK' to return to the 'Create New Subscription (2 of 3)' window.

Select the 'Change' button for 'States of Operations', if desired, and select the state(s).  When finished, select 'OK' to return to the 'Create New Subscription (2 of 3)' window.

Select 'Next'.

The 'Create New Subscription (3 of 3)' window should appear.

Select the 'INSP View Fields' radio button.  Only those fields associated with the INSP (Inspection) view will be monitored for changes.  If there are any changes to the monitored fields, that record will be added to the subscription.

Select 'Finish'.

Diagram C-37: Create New Subscription (3 of 3)

The new subscription will be displayed in the 'Subscription Manager' window.

Diagram C-38: Completed Vehicle Subscription

Show Subscription Properties

To view the current properties of a subscription:

- Select the 'Subscription Manager' icon -  or select the 'Subscription Manager' from the 'Managers' menu from the 'OpCon Control Bar'.  (See Diagram C-13.)

Select a subscription from the 'Subscription Manager' window.  Subscription #1 is highlighted in the example.

Diagram C-39: Select Subscription

Double-click on the subscription, or select the 'Subscription Properties' icon - , or select 'Subscription Properties' from the 'Actions' menu to display the first window of the properties.

Diagram C-40: Properties of Subscription #1 (1 of 3)

Select 'Next' to view the next 'Properties' window.

Diagram C-41: Properties of Subscription #1 (2 of 3)

Select 'Next' to view the last 'Properties' window.

Diagram C-42: Properties of Subscription #1 (3 of 3)

Select 'Finish' to exit.

Show Subscription Registration Properties

To view the current properties of a subscription registration:

- Select the 'Subscription Manager' icon -  or select the 'Subscription Manager' from the 'Managers' menu from the 'OpCon Control Bar'.  (See Diagram C-13.)

Select a subscription from the 'Subscription Manager' window.  Subscription #1 is highlighted in the example.

Diagram C-43: Select Subscription

Select 'Show Subscription Registration' from the 'Action' menu or select the  icon to display the 'Registrations for Subscription #1' window and select an organization (SAFER is highlighted in the diagram.)

Diagram C-44: Registrations for Subscription #1 Window

Double-click on the highlighted organization, or selection 'Registration Properties' from the 'Actions' menu, or select the  icon to display the properties of this registration for the selected subscription.

Diagram C-45: Subscription Registration Properties Window

Select 'OK' to exit.

Subscriptions Needed for Interoperability Testing

| Carrier: | MCMIS View |
| --- | --- |
|  | IFTA View |
| Vehicle: | IRP no TagID View |
|  | INSP View |

More than one subscription may be required for testing.  Repeat the steps in Section C.4 to add the State’s CVIEW userid to another subscription.  When finished with subscriptions and adding users, go to Tools on the menu bar and print the list of new users.  Close OpCon.

This Page Intentionally Blank

Forms

This Page Intentionally Blank

The pages in this section may be used to send the following information to Volpe:

| Data | Form | Section |
| --- | --- | --- |
| State Organization Data | Page D–4 | 2.2 |
| Carrier Subscription Registration Data | Page D–5 | 2.4.1 |
| Carrier Data Views and Versions | Page D–6 | 2.4.1 |
| Vehicle Subscription Registration Data | Page D–7 | 2.4.2 |
| Vehicle Data Views and Versions | Page D–8 | 2.4.2 |

This information is used to:

Request approval from FMCSA for the state (or the state’s representative) to receive data from SAFER

Set up the state as a user and establish a data mailbox on SAFER

Register the user for SAFER carrier/vehicle snapshots as specified

| State Organizational Data |
| --- |
| Item | Required | Description | State Selection for Registration |
| Jurisdiction | Yes | Jurisdiction requesting the subscription. |  |
| Organization Name | Yes | Name of organization, e.g., Maryland Dept. of Transportation |  |
| Sub-Organization Name | No | Division or sub-unit within the organization, e.g., Commercial Vehicles |  |
| Sub-Organization Short Name | No | An abbreviated name for the division or sub-unit within the organization, e.g., ComVeh |  |
| State Contact Name | Yes | First and last name |  |
| State Contact Address | Yes | Street City, State, ZIP code Country |  |
| State Contact Communication Number(s) | Yes | Phone is required. FAX and e-mail are optional. | Phone: FAX: E-mail: |
| Contractor Name | No | First and last name |  |
| Contractor Address8 | No | Street City, State, ZIP code Country |  |
| Contractor Communication Number(s)8 | No | If a Contractor is supplied, Phone is required. FAX and e-mail are optional. | Phone: FAX: E-mail: |

| Carrier Subscription Registration Data |
| --- |
| Item | Required | Description | State Selection for Registration |
| Product Type | Yes | Specify 'Carrier Snapshot' | Carrier Snapshot |
| Periodicity | Yes | Frequency to send the data. Your choices are: Next Update Immediately |  |
| States to Monitor | Yes | A list of states to monitor. This is the state of the carrier's legal address. User may specify 'All states' or provide a specific list of states. |  |
| Data View | Yes | Determines which carrier snapshot fields you will receive. (Refer to Table 2–3, and References [4] and [5].) |  |
| View Version | Yes | A version identifier for the data view. (Refer to Table 2–3, and References [4] and [5].) |  |
| Data Format | Yes | Specify 'EDI' | EDI |
| Compression | Yes | Specify 'Zip' | ZIP |

| Carrier Data Views and Versions |
| --- |
| Data View | View Version | Description | State Selection for Registration (Check to select) |
| Full | 4 | The full view includes all SAFER snapshot data pertaining to the carrier. (This view is equivalent to MCMIS+L&I+IFTA+IRP) |  |
| E-Screening | 4 | Contains the information necessary to register carriers in multiple screening programs and to permit screening by transponder ID across boundaries of jurisdictions and screening programs. |  |
| IFTA | 4 | Contains the information necessary to update International Fuel Tax Agreement (IFTA) credentials information in the carrier snapshot. |  |
| IRP | 4 | Contains the information necessary to update International Registration Program (IRP) credentials information in the carrier snapshot. |  |
| ISS-2 | 4 | Contains the SAFER data required to support the computation of the ISS score for use in determining which vehicles should be inspected. (This is a subset of MCMIS view, and is delivered to ISS-2 clients via other means) |  |
| L&I (License and Insurance) | 4 | Includes the information from the Licensing and Insurance System obtained from the Interstate Commerce Commission (ICC) and being maintained by FMCSA. |  |
| MCMIS | 4 | Details the information supplied to SAFER by the Federal Motor Carrier Safety Administration MCMIS system about the safety, safety review, and inspection history of interstate motor carriers. |  |

| Vehicle Subscription Registration Data |
| --- |
| Item | Required | Description | State Selection for Registration |
| Product Type | Yes | Specify 'Vehicle Snapshot' | Vehicle Snapshot |
| Periodicity | Yes | Specify 'Immediately' | Immediately |
| IRP Base States to Monitor* |  | A list of IRP base states to monitor. User may specify 'All States' or provide a specific list of states. |  |
| States of Operation to Monitor* |  | A list of IRP states of operation. Vehicle snapshots from these states of operation will be sent to you if something in the snapshot has changed. User may specify 'All States', provide a specific list, or specify the user's state only. |  |
| Data View | Yes | Determines which vehicle snapshot fields you will receive. (Refer to Table 2–5 and References [4] and [5].) |  |
| View Version | Yes | A version identifier for the data view. (Refer to Table 2–5 and References [4] and [5].) |  |
| Data Format | Yes | Specify 'EDI' | EDI |
| Compression | Yes | Specify 'None' | None |

| Vehicle Data Views and Versions |
| --- |
| Data View | View Version | Description | State Selection for Registration (Check to select) |
| Full | 4 | Includes all SAFER snapshot data pertaining to the vehicle. (Not to be used with FMCSA CVIEW 3.3.) |  |
| E-Screening | 4 | Contains the information necessary to register a carrier's vehicles in multiple screening programs and to permit screening by transponder ID across boundaries of jurisdictions and screening programs. |  |
| INSP (Inspection Overview) | 4 | Contains information provided by an inspector at the roadside. It includes the identification and safety information from an aspen inspection report that is used to update SAFER and CVIEW. This information provides guidance to the inspectors about past problem areas that should be reviewed in future inspections. |  |
| IRP (No TagID) | 4 | To facilitate the update of snapshots with registration IRP information equivalent to what is carried in the vehicle now. |  |

# Footnotes

Some states have contracted with outside organizations to develop or manage their CVIEW operations.  In these cases, contractor information is also required.

The data view corresponds to the 'Carrier Snapshot Event Fields' in the subscription Properties window as displayed with OpCon.

See References [4] and [5].

* At least one of these is required.

The data view corresponds to the 'Vehicle Snapshot Event Fields' in the subscription Properties window as displayed with OpCon.

See References [4] and [5].

'zzzz', 'nnnn', and  'kkkk' represent randomly generated series of numbers and digits to uniquely identify a file.

See Reference [5] for more information on OpCon.

Some states have contracted with outside organizations to develop or manage their CVIEW operations.  In these cases, contractor information is also required.

The data view corresponds to the 'Carrier Snapshot Event Fields' in the subscription Properties window as displayed with OpCon.

* At least one of these is required.

The data view corresponds to the 'Vehicle Snapshot Event Fields' in the subscription Properties window as displayed with OpCon.

# Text boxes

NOTE: 'Next Update' is normally specified for carrier snapshots from SAFER.

NOTE: if 'sub' account is created, OpCon creates another mailbox with 'sub' appended to User ID.  Total length must not be greater than ten (10) characters.

NOTE: the OpCon operator should insert the same properties (data format, etc.) from an existing user registration, if any, for subscription #1 so that values for all user registration properties match for a given subscription (see Section C.8).  Any changes made to the subscription properties will affect all users.  If this is the first registration, follow the guidance below.

NOTE: the registration process is where data view, view version, and format are specified.  The data view selections will be entity specific based on the subscription properties, i.e., only carrier data views are available for carrier subscriptions.  The user should select the data view that corresponds to the 'Snapshot Event Fields' specified in the 'Properties of Subscription' window (see Diagram C-32).

NOTE: the subscription registration properties (see Section C.8) for the subscription may be viewed by selecting the  icon or selecting the 'Registration Properties' option from the 'Actions' menu.

NOTE: if a registration already exists for the subscription, view the properties before registering a new user to it, to make sure it is what the user wants.

NOTE: the OpCon operator should insert the same values from an existing user registration, if any, for subscription #2 so that values for all user registration properties match for a given subscription (see Section C.8).  Any changes made to the subscription properties will affect all users.  If this is the first registration, follow the guidance below.

NOTE: the registration process is where data view, version, and format are specified.  The data view selections will be entity specific based on the subscription properties, i.e., only vehicle data views are available for vehicle subscriptions.  The user should select the data view that corresponds to the 'Snapshot Event Fields' specified in the 'Properties of Subscription' for subscription #2 (see Diagram C-37).

NOTE: the subscription registration properties (see Section C.8) for the subscription may be viewed by selecting the  icon or selecting the 'Registration Properties' option from the 'Actions' menu.  If a registration exists, view the properties before registering a new user to make sure it is what the user wants.

NOTE: When a user is registered for this subscription, the data view specified in the 'Registration Properties' window (such as Diagram C-16) for this subscription should be the IFTA view.

NOTE: When a user is registered for this subscription, the data view specified in the Registration Properties window (such as Diagram C-22) for this subscription should be the Inspection view.

NOTE: Any changes made in the 'Properties' windows will change the subscription definition.

NOTE: 'Next Update' is normally specified for carrier snapshots from SAFER.