About this resource:

EPA is providing this resource solely for informational purposes. The agency can not attest to the accuracy, effectiveness, legality or usefulness of the information provided, nor does the inclusion or reference of such language constitute an endorsement by EPA.

Document Name:

NY MTA Emission Control Specification

Organization/Agency Responsible:

New York Metropolitan Transportation Authority (NY MTA)

Contact:	Ramesh Raman

New York Metropolitan Transportation Authority (NY MTA)

646-252-3016

Rr2555@columbia.edu

Description:	NY MTA Emission Control Specification

New York Metropolitan Transportation Authority's emissions control specification includes provisions for on-road and nonroad vehicles.  Stipulations include fuel and retrofit technology provisions, truck staging zones, idling restrictions and location considerations for diesel engines.

PART 1 General

1.01	SECTION INCLUDES

- This specification covers requirements for on-road and off-road vehicle emission control for vehicles necessary for the Work of this Contract.

1.02	REFERENCED SECTIONS

A.	 None Cited

  - CITED STANDARDS

A.	None Cited

  - NOTED RESTRICTIONS

A.	None Cited.

1.05	QUALITY CONTROL

A.	None Cited

1.06	SUBMITTALS

A.	Submit a list of non-road diesel powered construction equipment that will be or have been retrofitted. The list shall include

- Contractor name/address/contact person;

- Equipment type, model, serial number;

- Engine serial number, make, model, year of manufacture; and

- Retrofit type, make, model, manufacturer, EPA verification number, and installation date.

- Certificate from original engine manufacturer stating engine serial number and its tier

- Submit monthly log, which lists the non-road diesel equipment details as in ‘B’ above, date on site, date off site, and fuel usage. The monthly log shall be submitted in electronic format and hard copy. Submit fuel log with bar code, equipment make & model, fill date, quantity & quality of fuel.

- Submit digital pictures (four per piece) of equipment showing machine, engine, and retrofit data plates, and fuel bar code.

1.07	DELIVERABLES

A.	None Cited

# PART 2 - PRODUCTS

A. 	None Cited

# PART 3 - EXECUTION

# 3.01	VEHICLE EMISSION CONTROL

A.	All motor vehicles and construction equipment (both on-road and non-road) shall comply with all pertinent State and Federal regulations relative to exhaust emission controls and safety.

B.	Establish truck-staging zones for vehicles waiting to load or unload material at the Work Site.  Such zones shall be located where diesel emissions have the least impact on abutters and the general public.

C.	Idling time shall be limited to three consecutive minutes for delivery and 	dump trucks and all other diesel powered equipment except as follows:

- When a “mobile source” is forced to remain motionless because of traffic conditions or mechanical difficulties over which the operator has no control;

- When it is necessary to operate heating, cooling or auxiliary equipment installed on the “mobile source” when such equipment is necessary to accomplish the intended use of the “mobile source”;

- To bring the “mobile source” to the manufacturer’s recommended operating temperature;

- When the outdoor temperature is below twenty-five (25) degrees Fahrenheit;

- When the “mobile source” is being repaired.

D.	Ensure that diesel emissions do not cause harmful effects to adjacent sensitive receptors.  Sensitive receptors include but are not limited to hospitals, schools, daycare facilities, elderly housing, and convalescent facilities.

E.	Ensure that diesel powered engines are located away from fresh air intakes, air conditioners, and windows.

F.	Equipment shall prominently display a clean exhaust message such as: “Machine is equipped with an air pollution control device and uses Ultra Low Sulfur Diesel fuel”.

G.	All on-road vehicles serving the construction site shall use ultra low sulfur diesel fuel (15ppm sulfur content) and comply with the New York State Environmental Conservation Law amendment 19-0323, which requires not less than 33% of the on-road vehicles to be retrofitted with the best available retrofit technology by 12/31/08, 66% by 12/31/09 and 100% by 12/31/10. The Contractor shall submit fuel delivery slips indicating date, fuel quantity, fuel quality, vehicle VIN number, and details of the retrofit program.

# 3.02	OFF-ROAD VEHICLE EMISSION CONTROL

A.	All Contractor non-road vehicles with auxiliary power source and construction equipment powered by an internal combustion engine with gross engine horse power rating of 50hp and above that are on the Project or are assigned to the Contract shall be Minimum Tier 2 certified diesel engines (emissions meeting Tier 2 standards), fitted with retrofit technology such as Diesel Particulate Filter (DPF) or better that removes greater than 90% particulate matter without increasing NOx, and uses Ultra Low Sulfur diesel fuel with 15 parts per million (ppm) maximum of sulfur.

B.	The retrofit technology / retrofit emission control device shall be US Environmental Protection Agency (EPA) verified or California Air Resources Board (CARB) verified for non road application, or have satisfactorily met all the criteria (level 1, 2 & 3) of VERT and recommended for use on construction equipment.

C.	In the event that Contractor is unable to use DPF technology, Contractor shall request approval of the Engineer to use alternative retrofit technology. Request shall be made in writing 30 days prior to use of equipment. Request shall document efforts made to implement DPF, provide letter from retrofit supplier stating reason for their inability to provide suitable DPF for the specific equipment and application, and demonstrate selected alternative retrofit technology is next best to DPF.

F.	Maintain copies of fuel deliveries identifying source of supply, quantity of fuel, and quality of fuel.  These copies shall be available for review by the Resident Engineer.

G.	Non compliant equipment shall be removed immediately from the job site.

Submittal Approvals

| Item No. | Paragraph No. | Submittal | Approval By |
| --- | --- | --- | --- |
| 1 | 1.06 A | Pre site equipment, engine, retrofit documentation | Engineer |
| 2 | 1.06 B | On site monthly log of equipment, engine, retrofit & fuel | Engineer |
| 3 | 1.06C | Digital pictures (4 per piece) | Engineer |

END OF SECTION