North Shore LRT Connector

Pittsburgh, Pennsylvania

(November 2005)

The Port Authority of Allegheny County (Port Authority) is proposing to design and construct a light rail transit (LRT) extension that would link the Golden Triangle area of downtown Pittsburgh across the Allegheny River to the rapidly developing North Shore and Strip District areas.  The proposed project would be constructed primarily underground, extending 1.2 miles from the existing Gateway LRT station to the North Shore via two bored tunnels below the Allegheny River.  This LRT line would continue through the North Shore area as a mix of below-grade and elevated alignments.  The project as currently scoped also includes a 0.3-mile spur from the existing Steel Plaza LRT station in downtown Pittsburgh to the David L. Lawrence Convention Center.  Four stations would be constructed as part of the total project: a reconfigured and expanded Gateway station to facilitate the tie-in to the existing system; two new stations on the North Shore; and the Convention Center station to be located underground at 11th Street near the Convention Center.  Four new light rail vehicles would be procured through the project.  Service would be provided at better than three-minute frequencies during peak periods.

Pittsburgh’s North Shore is one of the fastest redeveloping areas in the city.  Traffic congestion is prevalent in the area during peak commuter periods, weekends, and before and after events at PNC Park and Heinz Field, which reduces the speed, reliability, and effectiveness of bus transit.  Physical barriers created by the Allegheny River and the surrounding terrain prohibit any feasible roadway expansion.  The proposed project is designed to improve transit service in the area by providing quick, convenient, and reliable LRT connections between key downtown trip generators.  The project is further intended to serve a variety of travel markets, including LRT riders now transferring to buses in the Golden Triangle to continue to the North Shore, commuters using fringe parking on the North Shore to travel to the Golden Triangle, and students of Allegheny County Community College located on the North Shore.

| Summary Description |
| --- |
| Proposed Project: | Light Rail Transit |
|  | 1.5 Miles 4 Stations |
| Total Capital Cost ($YOE): | $393.0 Million (includes $0.2 million in finance charges) |
| Section 5309 New Starts Share ($YOE): | $217.7 Million (55.4%) |
| Annual Forecast Year Operating Cost: | $8.5 Million |
| Ridership Forecast (2025): | 15,800 Average Weekday Boardings |
|  | 4,100 Daily New Riders |
| Opening Year Ridership Forecast (2010): | 10,000 Average Weekday Boardings |
| FY 2007 Finance Rating: | Medium |
| FY 2007 Project Justification Rating: | Medium-High |
| FY 2007 Overall Project Rating: | Medium |

##### FTA expects to execute a Full Funding Grant Agreement (FFGA) for the Pittsburgh North Shore LRT Connector project in FY 2006.  The project was recommended for an FFGA in the FY 2006 President’s Budget; congressional review of the agreement and attendant documents was completed in July 2005.  Execution of an FFGA for the project, however, has been delayed due to an unanticipated cost increase associated with construction of the Allegheny River tunnel.  FTA is working with the Port Authority to reconfigure the project scope to conform to the $393.0 million cost estimate - while delivering the anticipated benefits - on which the FFGA recommendation was based.  Pending completion of this work, a full re-evaluation of the project is not possible; therefore, FTA is reporting for the FY 2007 Annual Report on New Starts information which supported the project’s FY 2006 evaluation and rating and the submitted FFGA, which results in an overall rating of Medium.  Based upon analysis completed by the Port Authority to date, FTA expects that the final project scope, budget, and resulting benefits will continue to support execution of the FFGA.

Project Development History and Current Status

In Fall 1997, the city of Pittsburgh and the Southwestern Pennsylvania Commission (the local metropolitan planning organization) initiated a major investment study to evaluate possible transportation linkages within the North Shore/central business district (CBD) segment of the Spine Line Corridor.  Upon completion of the North Shore Connector Draft Environmental Impact Statement, the Port Authority’s Board of Directors selected the Gateway LRT Alternative as the locally preferred alternative in August 2000.  FTA approved the North Shore LRT Connector for preliminary engineering in January 2001.  FTA issued the NEPA Record of Decision in July 2002 and approved the project’s entry into final design in April 2003.  The project was recommended for an FFGA in the President’s FY 2006 Budget. Due to increases in the project cost estimate, the Port Authority is developing a revised project scope and budget for FTA consideration.

Significant Changes Since FY 2006 Evaluation (November 2004)

The capital cost of the project has increased since last year, requiring additional cost analysis and scope modifications which are continuing at the time of this evaluation.

Project Justification Rating: Medium-High

FTA’s evaluation of the project justification criteria is based upon information submitted by Port Authority in 2004.  Since that time, FTA has revised the breakpoints for assigning ratings for cost effectiveness, resulting in an improvement in the project’s cost effectiveness rating from Medium-Low to Medium, and an improvement in the project’s justification criteria from Medium to Medium-High.    The project received a Medium-High rating for transit-supportive land use.

Cost Effectiveness Rating: Medium

The Medium cost effectiveness rating reflects the travel-time benefits (4,100 weekday hours) relative to the project’s annualized costs.  The cost effectiveness estimate assumes the present scope and cost, both of which are being re-examined; therefore, the current cost effectiveness carries some risk.

| Cost Effectiveness |
| --- |
| Cost per Hour of Transportation System User Benefit Incremental Cost per Incremental Trip | New Start vs. Baseline $21.89* $15.80 |

* Indicates that measure is a component of Cost Effectiveness rating.

The North Shore LRT Connector is expected to provide benefits to a number of downtown-oriented travel markets, including trips between the four major activity centers in Pittsburgh’s urban core: the Golden Triangle, Strip District, North Shore, and Station Square.  Nearly 15 percent of travel-time benefits are anticipated to be accrued by patrons utilizing less-expensive fringe parking facilities on the North Shore for travel to the Golden Triangle.  In addition to improving access within the corridor, the project would provide improved LRT access from various points in the region to the corridor, particularly the North Shore area, which currently requires LRT passengers to transfer to bus.  For example, commuters from Pittsburgh’s South Hills suburban communities bound for the North Shore would benefit from a one-seat ride and experience annual travel-time savings of over 80,000 hours.

Transit-Supportive Land Use Rating: Medium-High

The Medium-High land use rating is based on the Medium-High ratings assigned to each of the subfactors summarized below.

Existing Land Use: Medium-High

- Existing employment within ½ mile of proposed station areas is approximately 150,500.  Population within ½ mile of station areas is approximately 8,100.

- Land use in the downtown area is dense and transit-supportive, with the exception of vacant land on the North Shore that is awaiting redevelopment.

- A new street grid and pedestrian facilities have been established on the North Shore.

Transit-Supportive Plans and Policies: Medium-High

- There are no coordinated regional growth management policies, although efforts are being undertaken to promote transit-oriented development in various parts of the region.

- The Pittsburgh 1998 Downtown Master Plan and the 2002 Master Plan for the North Shore reflect a strong emphasis on development with transit-supportive densities and design.

- Former industrial and warehousing structures are being adapted for retail/entertainment, residential and office use in the Strip District.

- Pittsburgh’s zoning code allows for increased development densities in proximity to transit.

- Off-street parking requirements have been eliminated in the downtown area and reduced by 25 percent in the North Shore area in proximity to transit.

- Emerging policies reflect the view of city officials that LRT is an amenity for potential North Shore tenants and a mechanism to help reduce downtown parking needs.

Performance and Impacts of Policies: Medium-High

- The North Shore is being redeveloped with two major sports facilities, new infrastructure, and high-density, mixed-use development on a reconstructed street grid.   Initial public investments in infrastructure and sports stadiums have been instrumental in leveraging additional private investment in the North Shore area.

- Development proposals for the North Shore are integrated with plans for the LRT project and reflect transit-supportive design principles.

- At least 43 acres of new development are planned or under consideration, in addition to the new development that has already taken place or is underway.

- Port Authority has worked successfully in existing station areas downtown to undertake joint development projects.

Other Project Justification Criteria

| Mobility Improvements Rating: Medium-High |
| --- |
| Within ½-mile radius of boarding areas: Existing Employment Projected Employment (2030) Low Income Households (% of total HH) Average Per Station: Employment Low Income Households Transportation System User Benefit Per Project Passenger Mile (Minutes) | 150,500 162,600 450 (13%) 37,625* 113* New Start vs. Baseline 23.09* |
| Environmental Benefits Rating: High |
| Criteria Pollutant (Reduction in tons) Carbon Monoxide (CO) Nitrogen Oxide (NOx) Volatile Organic Compounds (VOC) Particulate Matter (PM10) Carbon Dioxide (CO2) Criteria Pollutant Status 8-Hour Ozone (O3) Particulate Matter (PM2.5) Annual Energy Savings (million British Thermal Units) | New Start vs. Baseline 33 5 8 0 13,160 EPA Designation Subpart 1* Non-Attainment Area* 22,960 |
| Operating Efficiencies Rating: Medium |
| System Operating Cost per Passenger Mile (current year dollars) | Baseline $0.534* | New Start $0.537* |

* Indicates that measure is a component of rating for each criterion.

N/A indicates information was not available for this entry.

# Local Financial Commitment Rating: Medium

The local financial commitment rating of Medium reflects the FY 2006 New Starts evaluation and rating, as updated for the Port Authority’s most recent FFGA submission.  This rating is based upon a rating of Medium-High for the capital plan, and Medium ratings for the New Starts share of project costs and the project operating plan.

| Locally Proposed Financial Plan |
| --- |
| Source of Funds | Total Funds ($million) | Percent of Total |
| Federal: Section 5309 New Starts Flexible Funds (CMAQ) Section 5309 Fixed Guideway Modernization Funds | $217.7 $76.2 $20.5 | 55.4% 19.4% 5.2% |
| State: Capital Grant | $65.5 | 16.7% |
| Local: Allegheny County Appropriation | $13.1 | 3.3% |
| Total: | $393.0 | 100.0% |

NOTE:  The financial plan reflected in this table has been developed by the project sponsor and does not reflect a commitment by DOT or FTA.  The sum of the figures may differ from the total as listed due to rounding.

Map