POLAR Spacecraft Status As of: Tues, 11 Apr 06, 16:00 EST

(changes from last week in bold border)

| Subsystem/ Component | NOAA-12D AM 16:59=AN STIP data only | NOAA-14J AM: 21:10=AN STIP data only | NOAA-15K AM: 17:49=AN GAC data only | NOAA-16L PM: 15:04=AN GAC&LAC data | NOAA-17M AM: 22:23=AN GAC&LAC data | NOAA-18N PM 13:49=AN GAC & LAC data |
| --- | --- | --- | --- | --- | --- | --- |
| LAUNCHED | 05/14/91 | 12/30/94 | 05/13/98 | 09/21/00 | 6/24/02 | 5/20/05 |
| CNTL OBP | OBP2 Recursive SCT | OBP2 OBP1 inoperative | OBP2 | OBP2 | OBP2 | OBP2 |
| BUS | B-BUS XSU-1 | B-BUS XSU2 (XSU1 inop) | B-BUS XSU-1 | B-BUS XSU-1: TOAR444 | B-BUS XSU-1 | B-BUS XSU-1 |
| BUS VETO | NO | NO | NO | NO | NO | NO |
| ADACS X=Yaw: gas unload mom trigger=70i#s Y=Roll: gas unload mom trigger=70i#s Z=Pitch: gas unload mom trigger=40i#s * | Nominal Mode RGmode=Monitor Gyro chans=XYZ | Nominal Mode Rgmode=Disabled Gyro chans=XYZ | Nominal Mode Rgmode=Monitor Gyro-3 Off 6/26/00 Gyro chans=AAB | RGYRO Mode Estimate ROLL Rgmode=PASSIVE Gyros-1 & 3 Inop/Off TOAR 454 Gyro chans XA-ZB | Nominal Mode Rgmode=Monitor Gyro-3 Off 6/10/04 Gyro chans=AAB | Nominal Mode Gyro-A MIMU-2 Z-wheel -Pitch TOAR 447 |
| RXO | PRI BU random enables daily bias+6.5 mS | PRI BU random enables daily bias–7.0 mS | PRI daily bias -8 mS -500 mS 12/31/05 | PRI Daily Bias –5.5 mS -1500 mS 31Dec05 | PRI Daily Bias –3 mS -1500 mS 31Dec05 | PRI No daily bias -1500 mS 31Dec05 |
| CLOCK DIV | 2 | 2 | 2 | 2 | 2 | 2 |
| MIRP | External Synch Rephase Enabled | External Synch Rephase each orbit | External Synch Rephase 0730 daily | External Sync Rephase each orbit | External Sync Rephase Enabled | External Synch Rephase Enabled |
| TIP SIDE | 1 | 1 | 2 (since 4/3/03) #2 has 3 chans inop | 2 since 4/18/05 | 1 Analog telem drifting | 1 Analog telem drift? |
| Recorders (DTR, SSR) | DTRs 3A, 4, 5B Safestate 5B | DTRs 1, 2B, 5 Safestate- 1B | DTRs 1, 2, 3, 4 Safestate 1B EOT | DTRs 1, 2, 3, 4A Safestate 3A 4B STIP only | DTR 1,3,4 / SSR 2 Safestate=SSR 2B | SSRs 1,2,3,4,5 Safestate=5B Current spikes TOAR 450 |
| VTX (APT data) | #1 ON 137.50 MHZ | OFF (nominal) Since 8/2/05 | #1 ON Turned back on 2 | INOP/Off OFF since 11/15/00 | #2 ON 137.62 MHZ | #1 ON 137.10 MHZ |
| BTX | #1 136.77 MHZ | #2 137.77 MHZ | #1 137.35 MHZ | #2 137.77 MHZ | #2 137.77 MHZ | #1 137.35 MHZ |
| STX 1 = rcp 1698.0 mhz 2 = lcp 1702.5 mhz 3= rcp 1707.0 mhz 4= rcp 2247.5 mhz | 1 – HRPT; 2,3 - Playback | 3 – HRPT 2, 1 – Playback | 2-Omni HRPT 2 omni=rcp Power Drop TOAR 446 4-Playback 1,2,3-Degraded | 2 – HRPT 1– Playback 4 – Playback & MCM usage 3 low power unused | 3 – HRPT TOAR424 low power 2 & 4 Playback 1-Standby STX-1 Power drop TOAR 443. | 1 - HRPT 3 - Playback 2-Playback 4-Test & Standby |
| POWER (Array offset and CANT angle, charge & V/T rates, eclipse states and sun angle) Sun Moon eclipse occurred for all spacecraft 29 Mar. No significant impact. | ArrayOff +60 since 6/23/05 Full Sun Sun Angle 25 uptrend to 35 in mid-June Batts 1&2=LRC Batt 1&2 V/T=4 Shunt degraded Eclipse season starts 29 Apr SA CANT=37 degs | Array Off -50 Batts 1&3V/T=6/9 Batt2 VT=7/9 Since 11/22/05 Eclipse all year Sun angle 54 up trend to 60 in June Batts 1-3= LRC Degraded shunts SA CANT=22 degs PSSS change plan | Array Off -45 Since 1/25/01 Full Sun Sun Angle 20 New uptrend to 32 in mid-June Batts 1-3= LRC V/T=7/9 SA CANT=37 degs Eclipse season starts mid-May | Array Off -40 Since 7/16/02 Eclipse all year Sun Angle 57 Steady Trend Batts 1-3= LRC V/T=4/8 SA CANT=22 degs | Array Off. –40 Since 1/29/04 Eclipse all year Sun Angle at 68 uptrend to 71 at end of May Batts 1-3= LRC V/T= 4/8 SA CANT=37 degs | Array Off. -40 Since 6/6/05 Eclipse all year Sun Angle 66 up trend to 72 mid-Jul Batts 1-3=LRC Batts 1-3 V/T=4/8 SA CANT=22 TOAR 453 on Batt C/D ratio Closed 4/11/06 BVR Phase Control autonomous swap 3/29TOAR submited |
| AVHRR | Nominal | Variable Occasional scan motor current surge Channels 2&4 APT | Nominal Channel 3B only Recent minor scan motor instabilities | Nominal since mid Oct 05 TCE24 OFF 4/14/04 Channel 3B only | Nominal 3A-B switch enabled scan motor current mini surges observed | Nominal Channel 3B only |
| AMSU-A1 |  |  | Operational Ch14 inoperative Ch11 inoperative | Operational Primary PLLO chans 9-14 bias shift. Backup PLLO inop. Channel 9-14 noise | OFF/INOP Since 10/30/03 Survival heat on. | Nominal Full Scan mode |
| AMSU-A2 |  |  | Nominal | Nominal Space Position-2 | Nominal | Nominal Full scan mode |
| AMSU-B |  |  | Operational Bias in All Chans. Motor surges most recent 11/14/04 Degraded Chan-3 since 4/30/05 | Operational Space Position-3 IPD reports channel 8 degradation | Nominal | Replaced by MHS |
| HIRS | OFF/Inop Turned off 6/23/05 For power balance Filter Wheel turned OFF 10/17/02. | NOMINAL Operational Occasional loss of Fwheel synch | NOMINAL FW Abrupt return to nominal 7/12/05 After years of minor and major current surges FW mode=Hi Powr | Operational Imagery high levels radiometric noise TOAR 441 CLOSED Recent momentary FW synch dropouts Occasional major FM surges, most recent 12/9/04 | NOMINAL 1 Pixel cross track misalignment. | Operational LW channel 1-12 noise TOAR 448 Loose LWIR lens. Longwave noise improved 7 Apr but degraded again 11 Apr 06 |
| MHS/MIU |  |  |  |  |  | Nominal Space View=0 Two Turbo anomalies Caused by proton hits over SAA |
| MSU | OFF/Inop Turned off for power balance 6/23/05 | Operational Scan motor and antenna problems EOL test planned |  |  |  |  |
| SSU |  | Nominal |  |  |  |  |
| DCS RFI investigation | Nominal | Nominal | Nominal | Nominal Pseudo message turned on 1/5/06 | Nominal | Nominal DRU’s 1-7 On DRU8 inop/off |
| SARR |  | Nominal | Operational A-Side, AGC Mode Intermittent failures for 243MHz A&B | Operational Mode =AA A-side, AGC Mode (B-side in FG mode) 243 MHz = INOP. | Nominal A-side All AGC Mode | Nominal A-Side All AGC Mode Since 15 Aug 05 |
| SARP |  | OFF Power Failure | Nominal RCVR B/W = 2 | Nominal RCVR B/W = 2 | Nominal | Nominal A-side 23 May05 |
| SEM | ON/Nominal Turned on 8/30/04 Elec-CH-HVPS=4 Prot-CH-HVPS=0 TED level=3 | Operational Elec-CH-HVPS=0 Prot-CH-HVPS=0 1 of 4 Tscopes inop | Nominal E-CDEM-HVPS=2 P-CDEM-HVPS=0 | Nominal E-CDEM-HVPS=5 P-CDEM-HVPS=4 | Nominal E-CDEM-HVPS=2 P-CDEM-HVPS=3 | Nominal Elec-CH-HVPS=0 Prot-CH-HVPS=0 |
| SBUV |  | Degraded Grate motor sticks Flex memory 3 (giant step) ops suspended 12/2/03 Reduced operations Transient anomaly 1 Sept 05 |  | Operational Degraded Ozone data Backup Diffuser inop Primary Diffuser deployment problem TOAR 426 AMSU EMI causing erratic Behavior in PMT cathod, range 3 | Nominal Anode Mode Plan sweep mode Standard Ops Procedure changes forthcoming | Nominal Anode mode since 6 July 13:30z Electronics turnoff taken out of STESM safestate table |
| SADPOS |  |  | N/A | ON Enabled MFactor50% Timer = 12 mins | ON ENABLED Timer = 12mins | ON Enabled Timer =12 mins |
| THERMAL Heaters, louvers TCE’s | Nominal TCE’s back to nominal configuration following 7/25/04 UVtrip. | Nominal | TCE26 & 15H Telem invalid TOAR 432 TCE24L&25L (HIRS & AVHRR) failed 5/13/98 RCE thermostat failed 5/13/98 Spacecraft in thermal uptrend | Nominal TCE24 OFF 4/14 (AVHRR H&L) HIRS Filter heater turned OFF 1/18/05 | TCE3H Batt 2A heater failed ON, turned off 8/26/03 AMSU-A1 survival heaters on 10/29/03 | All TCE’s active TCE3H displaying invalid readings TOAR forthcoming |
|  | N12 | N14 | N15 | N16 | N17 | N18 |

COMMENTS/CHANGES:

NOAA-12:	There were no changes to N12 during the past reporting period although N12 will enter its eclipse season within three

weeks.

NOAA-14:	There were no changes to N14 during the past reporting period.  There were no AVHRR scan motor current spikes

during the past week (illustration 1) and the Power subsystem was generally nominal although battery voltages were falling to seasonal lows as the battery temperatures increased (illustration 2).

.

NOAA-15:	The N15 payload suite was generally nominal (illustration 3 and 4) with the spacecraft thermal trend now firmly to the

upside.  The N15 Attitude Control Subsystem was also nominal and stable last week (illustration 5 and 6). VTX-1 continued to perform nominally since being re-activated on 2 Apr.

NOAA-16:	The N16 payload suite was also generally nominal and stable during the past week (illustration 7 and 8) with the

AVHRR again reaching and sustaining a new historical low scan motor current and all other payloads nominal and stable.  The N16 HIRS filter motor current fell slightly after equaling its all time high value the week previous.

There was no change to the DCS configuration on N16 with pseudo messaging remaining on and expected to remain so indefinitely as it has proven beneficial to European (IJPS) engineers investigating noise and RFI events on N18.

NOAA-17:	The N17 payload suite was generally nominal and stable during the past week (illustrations 12 and 13) although the AVHRR scan motor current experienced yet another mini surge (again equaling an all time high value) and return to nominal during the past week.  There were no reports of degraded imagery received as a result of this event.

The N17 ADACS experienced a minor perturbation during the past week between the gyro spin motor currents and the IMU TCA voltage.  Late on 5 April, both gyro 1 and 2 spin motor currents both abruptly dropped one mA.  At the same time, the IMU TCA abruptly rose by 0.7 volts.  Late on 7 Apr the gyro current rose 1-2 mA and the TCA voltage fell back by approximately 0.6 volts.  This response of the TCA to the gyro motor current was the opposite of what was expected.  As demonstrated on N16 on 13 Mar, when the gyro current goes up the TCA should do likewise and vice versa (illustration 14).  Although there were no apparent peripheral effects on the N17 ADACS system that appear to be attributable to this event (illustration 15 and 16), with so many concerns about the N17 gyros it was agreed at the TOAR board that a new TOAR should be opened up on this situation.

NOAA-18:	Most of the N18 payload suite was nominal and stable during the past week (illustration 18).  In addition, late on 7 Apr

the N18 HIRS long wave channels returned to a more nominal value for the first time since early February.

Accompanying this improvement was improvement in image quality.  However, it did not last. On 11 Apr at approximately 06:09z, the noise again increased significantly and impacted imagery once again (illustrations 19-22).   As has been the case all along, the N18 HIRS hardware was nominal and showed no discernable change either when the channel noise improved or when it again degraded (illustration 23).   Therefore, the HIRS hardware remains nominal but the payload users should know that data can go unstable.

Engineers continue looking into a possible problem with TCE3H on N18 (battery 2A heater) which continued exhibiting unusual readings (illustration 24).  Values that straddle the channel used by TCE3H show no such degradation nor does any other battery TCE.

On 11 Apr the TOAR Board closed TOAR 456 which investigated the turbo anomalies that occurred with the MHS.  The problem was attributed to proton strikes over the South Atlantic Anomaly with no actual resolution possible beyond COP implementation as was performed the previous times this anomaly occurred.  The TOAR Board also closed out TOAR 453 which was concerned with battery charge to discharge ratios.

MISC:	As mentioned in last weeks report, all POES spacecraft experienced a sun-moon eclipse situation on 29 Mar between

07:30 and 14:00z.

Illustration 1:  NOAA-14 AVHRR Health Analysis

(Nominal and stable as it has been for more than a month.)

Illustration 2: N14 Power Subsystem Health Analysis

(Generally nominal and stable with warming batteries and slightly lower battery voltage levels being reached as a consequence of those temps.)

Illustration 3:  N15 AMSU’s Health Analysis

(Nominal and stable last week with an upward trending thermal cycle.)

HIRS								AVHRR

Illustration 4:  N15 HIRS & AVHRR Health Analysis

(Stable and nominal last week with a thermal uptrend.  Synch delta [not shown here] was also stable and nominal.)

Illustration 5:  N15 ADACS Health Analysis

(Nominal and stable last week.  Note the hydrazine plot [upper right] which can be compared to N16 and N17 that appear in later illustrations.)

Illustration 6:  omitted for web release

Illustration 7:  N16 AMSU’s Analysis

(Generally nominal and stable all week.)

ILLUSTRATION 8:  N16 HIRS & AVHRR Health Analysis

(HIRS showed some slight improvement from last week while AVHRR once again achieved and sustained new all time low scan motor current values.)

Illustration 9:  omitted for web release

ILLUSTRATION 10: omitted for web release

ILLUSTRATION 11: omitted for web release

ILLUSTRATION 12:  N17 AMSU’s Health Analysis

(Nominal and stable last week.)

ILLUSTRATION 13:  N17 AVHRR Health Analysis

(Yet another scan motor current “mini-surge and return” event last week with no apparent impact on imagery. Otherwise nominal.)

ILLUSTRATION 14:  N18 Primary Payload Motor Current Analysis

(Nominal and stable across the board.)

N16 Gyro vs. TCA cause-effect		        N17 Gyro vs. TCA cause-effect

ILLUSTRATION 14:  Comparing N16 and N17 Gyro motor current vs. IMU TCA voltage changes, cause and effect.

(As it did on N16 several week ago [left side plots] when N17 gyro motor currents went down, late on JDAY 95 [right side plots] it was expected that the TCA voltage would go down as well, and vice versa.  N17 acted the opposite of what was expected and there is currently no conclusive reason why this occurred.)

ILLUSTRATION 15:   N17 ADACS Analysis

(Nominal and stable last week.  No new perturbations.  and nothing to indicate any correlation with the IMU TCA event.)

ILLUSTRATION 16: N17 Attitude Control Analysis

(Nominal and stable last week and nothing to indicate any correlation with the IMU TCA event.)

ILLUSTRATION 17: omitted for web release

Illustration 18:  N18 Primary Payloads Health Analysis

(Nominal and stable last week.)

Illustration 19:  N18 HIRS Long Wave Channel Health Analysis

(Nominal and stable last week.)

Illustration 20:  N18 HIRS Long Wave Channel Health Comparison THEN and NOW

(Nominal THEN is at a different level then nominal NOW.  Therefore the question is which one is actually nominal?  Something of a moot question now that the channel again went anomalous.)

Illustration 21:  N18 HIRS Long Wave Channel Stability Analysis

Illustration 22:  N18 HIRS Imagery Analysis

(Imagery improved along with the improvement in Channel noise on 7 Apr but degraded once again after the 11 Apr degradation of the channels.  Affected channels are marked by an “X” in the left side images.)

Illustration 23:  N18 HIRS Hardware Analysis

(No noticeable change regardless of long wave channel situation.  Everything looks nominal and stable.)

Illustration 24:  N18 TCE Analysis

(Plot on lower right shows how a TCE that is cycling should look.  The two plots on the left side are on telemetry channels immediately before and immediately after TCE3H which is on the top right.  Comparing these 4 plots it is very apparent that TCE3H is not working or reporting its values correctly.

ILLUSTRATION 25A:  omitted for web release

ILLUSTRATION 25B:  omitted for web release

ILLUSTRATION 25C:  omitted for web release

ILLUSTRATION 25D:  omitted for web release

ILLUSTRATION 25E:  omitted for web release

# POLAR SPACECRAFT TIP CLOCK ERROR

## WEEK ENDING April 7, 2006

| DAY/DATE | NOAA-12 | NOAA-14 | NOAA-15 | NOAA-16 | NOAA-17 | NOAA-18 |
| --- | --- | --- | --- | --- | --- | --- |
| FRI. 03/31 | -080 msec | -146 msec | +048 msec | -041 msec | -174 msec | -185 msec |
| SAT. 04/01 | -080 msec | -147 msec | +048 msec | -037 msec | -172 msec | -185 msec |
| SUN. 04/02 | -082 msec | -147 msec | +047 msec | -037 msec | -170 msec | -183 msec |
| MON. 04/03 | -084 msec | -150 msec | +044 msec | -035 msec | -168 msec | -180 msec |
| TUE. 04/04 | -082 msec | -149 msec | +043 msec | -037 msec | -168 msec | -178 msec |
| WED. 04/05 | -083 msec | -148 msec | +044 msec | -036 msec | -167 msec | -176 msec |
| THU. 04/06 | -082 msec | -148 msec | +042 msec | -035 msec | -165 msec | -175 msec |

NOAA-14:  As of 12/23/03 the TIP clock is corrected daily by –7.0 msec to compensate for drift.

NOAA-15:  As of 04/22/03 the TIP clock is corrected daily by –8.0 msec to compensate for drift.

NOAA-16:  As of 12/23/03 the TIP clock is corrected daily by -5.5 msec to compensate for drift.

NOAA-17:  As of 12/23/03 the TIP clock is corrected daily by –3.0 msec to compensate for drift.

NOAA-12:  As of 12/10/03 the TIP clock is corrected daily by +6.5 msec to compensate for drift.

*    A clock jump of +500 milliseconds on 11/30/05 due to fractional second daily ETCUP. A clock

jump of -500 milliseconds on 02/14/06 due to fractional second daily ETCUP. Alternating +/-

500 millisecond clock jumps will ccur at 76-day intervals as long as fractional second daily

ETCUP is utilized to manage clock drift. The next +500 millisecond jump is expected on 05/01/06.

** TIP Clock corrections were made to compensate for the positive leap second introduced on 12/31/05.