6 Minutes for Safety Topic:  Structural Damage / Controllability Check

Note:  POH / AFM guidance takes precedence over this checklist.  If your specific aircraft POH / AFM has a controllability check, use it instead of this checklist.

Recommend perform this check when structural integrity of the aircraft has been compromised (actual or suspected).  For example:

- Mid-air collision with other aircraft or debris

- Bird strike

- Ground obstacle strike (tree, wire, snag, etc.)

- Control jam / failure

- Lightning strike

- Asymmetric flaps

- Icing

- Hail damage

- Over-G

- Any occurrence that would cast doubt as to the structural integrity / normal flight characteristics of the aircraft

The aircraft may be perfectly controllable at a specific airspeed and / or configuration.  However, acceptable flight characteristics may be an issue at approach and landing speeds.  It is advisable to ascertain this before attempting a normal landing approach (e.g. getting close to the ground).  Upon determining a structural issue exists that is having a negative effect on flight characteristics, recommend accomplishing the following:

- Maintain aircraft control (use trim as required to help control the aircraft / relieve control pressure)

- Load - jettison

- Attain a safe altitude (recommend 2000’ – 3000’ AGL minimum)

- Determine optimum configuration for landing (flap position)

- Slow only to that airspeed which allows acceptable handling qualities for continued flight

- Prior to descent:  Check handling characteristics at approach / landing speeds

- Land at the nearest suitable airport

Note: Suitable airport determination should include evaluation of the following:

- Weather (winds / crosswinds, ceiling / visibility, etc.)

- Runway condition

- Runway length / width

- Facilities (emergency response)

- Pilot experience