309 Customs Manifest

FUNCTIONAL GROUP ID = AQ

This X12 Transaction set contains the format and establishes the data contents of the Customs

Manifest Transaction Set (309) for use within the context of an Electronic Data Interchange (EDI) environment. The  transaction set can be used by  carriers, terminal operators, port authorities, or service centers to provide . Customs  with manifest data on cargo arriving or departing from ocean going vessels, railroad trains,  or other types of conveyances. The transaction set  can also be used by carriers to    provide terminal  operators, port authorities, or service  centers with manifest data on cargo arriving at their facilities via the  above mentioned conveyances.

This message map defines the data elements and structure associated with submitting an electronic Data Interchange (EDI) message highway cargo document to U.S. Customs and Border Protection (CBP)

If a shipper sends in one bill of lading with multiple pieces of equipment, the manifesting carrier will not send one manifest (309) per piece of equipment to CBP. Multiple pieces of equipment may be accommodated within the same 309 manifest. The Manifest Accept/Reject notification (Set 355) will go out to the Trade in response to this message.  Status notifications (350) will go to the carrier as entries are filed and releases obtained.

Table 1

PAGE # POS. # 	SEG. ID   NAME 				REQ. DES. 	MAX USE	                	                 LOOP REPEAT

2         0100 	ST       Transaction Set Header	 	M 	1

3         0200	M10     Manifest Identifying Information    	M 	1

N/U     0210	N9       Extended Reference Information                 O	6

6         0250 	VEH     Vehicle Information 		 	O 	10

12       0225	M7       Seal Numbers			O	5

13       0250 	CII       Conveyance Insurance Information 	O 	3

LOOP ID - NM1 							         999

14       0270 	NM1    Individual or Organizational Name 	O 	1

16       0290	DMG    Demographic Information 		O 	1

N/U     0300	DMA    Additional Demographic Information	O	1

17       0310 	REF     Reference Information 		O 	10

19       0320 	N3       Party Location 			O 	2

20       0330 	N4       Geographic Location 			O 	1

LOOP ID – P4						                            20

21       0400	P4       Port Information 			M 	1

LOOP ID-P4/LX							        9999

22       0600 	LX      Transaction Set Line Number 		M 	1

23       0700 	M13    Manifest Amendment Details 		O 	1

26       0800 	M11    Manifest Bill of Lading Details 		O 	1

30       0850	N9      Extended Reference Identification		O 	999

LOOP ID –P4/LX/ N1 							            25

33       1000	N1      Party Identification 			 O	1

37       1050	N2      Additional Name Information		 O	1

38       1100 	N3      Party Location 			 O	2

39       1200 	N4      Geographic Location 			 O 	1

N/U     1230 	DTM   Date/Time Reference 			 O 	1

40       1250	PER   Administrative Communications Contact	 O	1

N/U     1260	X1      Export License			 O	1

LOOP ID –P4/LX/ M12 							              1

41       1300 	M12   In-bond Identifying Information 		 O 	1

N/U     1350	R4      Port or Terminal			 O	10

LOOP ID – P4/LX/VID 							          999

44       1500 	VID    Vehicle ID 				 O 	1

48       1570 	M7     Seal Numbers 			 O 	5

LOOP ID P4/LX/VID/ N10 						          999

49       1600 	N10    Quantity and Description 		 O 	1

53       1620 	VC     Motor Vehicle Control 			 O             999

N/U     1630 	MAN  Marks and Numbers 			 O 	 999

LOOP ID – P4/LX/VID/N10/H1 						        99

54       1650 	H1      Hazardous Material 			 O 	 1

N/U     1660	H2      Additional Hazardous Material		 O	 99

N/U     1665	PER   Administrative Communications Contact        O 	 1

55       2000 	SE     Transaction Set Trailer 			 M 	 1

Segment: 		ST	 Transaction Set Header

Position:	0100

Loop: 		____

Level:	N/A

Usage: 	Mandatory

Max Use: 	1

Purpose: 	To indicate the start of a transaction set and to assign a control number

Syntax:	N/A

Semantic: 	    1 The transaction set identifier (ST01) is used by the translation routines of the

interchange partners to select the appropriate transaction set definition

(e.g., 810 selects the invoice transaction set).

2 The implementation convention reference (ST03) is used by the translation

routines of the interchange partners to select the appropriate

implementation convention to match the transaction set definition. When

used, this implementation convention reference takes precedence over the

implementation reference specified in the GS08.

Comments:	   N/A

Notes:	1  This segment is used by CBP

Data Element Summary

REF. DES. 	 DATA ELEMENT	NAME 							      ATTRIBUTES

ST01 	143 		Transaction Set Identifier Code 		M 	ID 		3/3

Code uniquely identifying a Transaction Set.

CODE 	DEFINITION

- Customs Manifest

ST02 	329 		Transaction Set Control Number 		M 	AN 		4/9

Identifying control number that must be unique within the transaction set

functional group assigned by the originator for a transaction set

DENTIFYING INFORMATION

Segment: 		M10	Manifest Identifying Information

Position:	0200

Loop: 		___

Level:	N/A

Usage: 	Mandatory

Max Use: 	1

Purpose: 	To transmit manifest identifying information

Syntax: 	   4 P0410

If either M1004 or M1010 is present, then the other is required.

5 R0504

At least one of M1005 or M1004 is required.

15 P1516

If either M1015 or M1016 is present, then the other is required.

Semantic: 	   4 M1004 is Lloyd’s vessel code

7 M1007 is used for the 6-digit Numeric Manifest Sequence Number.

11 M1011 indicates if the transmission involves an in-bond participant. A ‘‘Y’’

indicates it does. A ‘‘N’’ indicates it does not.

12 M1012 is the unique identification number of the manifest described by the

originator of the manifest with a maximum length of 15.

17 M1017 is the type of initial manifest being amended by this transmission.

Comments: 	  A M1003 is the code identifying the country in which the ship (vessel) is

registered.

B 1008 is used for Number of Bills Lading. (Maximum 5 Digits.)

Notes:	 1  For CBP truck manifest: Key information is comprised of M1001, M1006

And M1009

2  This segment is used by CBP

Data Element Summary

REF. DES.	DATA ELEMENT	NAME							     ATTRIBUTES

M1001  140 		Standard Carrier Alpha Code				M    ID	2/4

Standard Carrier Alpha Code

##### For CBP:

##### Truck carrier initiating manifest. (Preferred data  element).

M1002	 91		Transportation Method/Type Code 			M    ID	1/2

Code specifying the method or type of transportation for the shipment.

For CBP.

CODE 	DEFINITION

J 		Truck

M1005  182		Vessel Name						X    AN   2/28

Name of ship as documented in ‘Lloyd’s Register of Ships’

###### For CBP:

###### If trip number not known specify SYSTEM.  For original standard and preferred manifest , this is the trip number.  Truck manifest accepts only 21 positions. Truck manifest accepts only alpha-numerics with no embedded spaces or special characters.

M1006    55 		Flight/Voyage Number 					O    AN	2/10

Identifying designator for the particular flight or voyage on which the cargo travels.

For CBP:

May contain a reference number such as the Julian date (YYDDD) to 		promote uniqueness.  May contain ‘TRUCK’ in preliminary manifest.  If 		nothing is indicated, system will default to ‘TRUCK’.

For CBSA:

M1009  256		Manifest Type Code					O    ID	1/1

Code identifying type of manifest transmitted .

##### One code is required.  (Preferred Data Element)

CODE 	DEFINITION

P 	Preliminary  Manifest from Carrier to Customs

For CBP

W	Original  manifest

For CBP

T 		In-Transit Manifest.

For CBP

Used for US-CAN-US, CAN-US-CAN  traffic where it is not 			consisted on the outbound move. This must be an original 		manifest. This is for future use.

Y		Amendment to Manifest (change)

For CBP:

Used after sending a 358 Trip, or when amending/updating 	manifests or shipments.

- Delete  manifest

For CBP

M1012	  127		Reference Identification					O    AN   1/50

Reference Identification as defined for a particular Transaction Set, or as 				specified by the Reference Identification Qualifier.

For CBP:

This is a unique identifier that will be returned to the carrier in output messages.  CBPTruck manifest accepts only 15 positions.

M1015     580 		Amendment Type Code 					O     ID 	1/1

Code identifying type of manifest amendment.

For CBP:

Required to make changes after submission of  data to CBP.

CODE 	DEFINITION

M		Replace a manifest segment by substituting original manifest 						information

This permits users to substitute trip, conveyance, and crew information in existing manifests without deleting and transmitting a new 309 set.  The segment with the corrected information immediately follows. Segments affected are:  VEH, M7, CII, NM1, DMG, REF, N3, N4, P4. Segments should be transmitted in loops if there is no unique identifier in the segment.  Example: all the segments for crew are required when a change of crew data occurs.

M1016     393 		Amendment Code 					O     ID 	2/2

Code giving the reasons for the amendment of the manifest record.

For CBP

CODE 	DEFINITION

03		Clerical error in manifesting.

18	 	Electronic manifest delayed by communications failure

24		Modification of trip data due to mechanical failure, change in 				schedule, availability, or other unforeseen reason.  Reason 				documented and on file.

This code is required when code ‘3’ is supplied in M1009.  Also required when  code ‘Y’ is supplied in M1009 after a 353 set with an ‘end of manifest’ message has been transmitted, or a code ‘Y’ is used to amend an manifest with an original manifest type code of ‘W’.

M1017     256		Manifest Type Code 					O    AN	1/1

Code identifying the type of manifest transmitted .

For CBP

CODE 	DEFINITION

8		Standard Manifest from Carrier to CBP

- Preferred Manifest from Carrier to CBP

Segment:     		VEH	Vehicle Information

Position:	0250

Loop: 		____

Level:	N/A

Usage: 	Optional

Max Use: 	10

Purpose: 	To provide descriptions that identify a specific vehicle

Syntax:       4  L040507

If VEH04 is present, then at least one of VEH05 or VEH07 is required.

5 C0504

If VEH05 is present, then VEH04 is required.

6 C060405

If VEH06 is present, then VEH04 and VEH05 are required.

7 C0704

If VEH07 is present, then VEH04 is required.

10 E1026

Only one of VEH10 or VEH26 may be present

10 C1017

If VEH10 is present, then VEH17 is required

18 P1819

If either VEH18 or VEH19 is present, then the other is required.

20 L200221

If VEH20 is present, then at least one of  VEH02 or VEH21 is required.

21 P2122

If either VEH21 or VEH22 is present, then the other is required.

26 C2617

If VEH26 is present then VEH17 is required.

Semantic: 	   4 VEH04 applies to VEH05, VEH06, and VEH07.

5 VEH05 is the vehicle make.

6 VEH06 is the vehicle model.

7 VEH07 is the vehicle style.

8 VEH08 is the length of the vehicle measured in feet.

9 VEH09 is the vehicle reference number.

10 VEH10 is the vehicle registration state or province.

11 VEH11 is used to identify a territory as defined by trading partners.

12 VEH12 is the Used Car Indicator.  A ‘Y’ indicates the vehicle is a used

vehicle; an ‘N’ indicates the vehicle is a new vehicle.  A value of ‘U’

indicating unknown cannot be used.

13 VEH13 is the original cost of the vehicle when it was new (i.e. OCN –

original cost new).

14 VEH14 is the Vehicle Altered Indicator.  A ‘Y’ indicates the vehicle was

altered; an ‘N’ indicates the vehicle was not altered.  A value of ‘U’ indicating

unknown cannot be used.

15 VEH15 is the value of the alterations for a vehicle.

17 VEH17 is the Country of the State in VEH10 or the country subdivision in

VEH26.

18 VEH18 is the Name of the Vehicle Owner.

19 VEH19 is the Residence Country of the Vehicle Owner in VEH18

21 VEH21 is the ACE (Automated Commercial Environment) ID assigned by

U.S. Customs and Border Protection

24 VEH24 is the transponder number of the vehicle.

25 VEH25 is the Department of Transportation (DOT) number of the vehicle.

Comments:	N/A

Notes:	1  If conveyance is pre-registered in ACE, either ACE ID or Conveyance ID 			    or VIN number or Transponder ID to be provided.

2  Only 1 occurrence of conveyance per trip.  However, the VEH segment 		     can be repeated to provide up to 4 license plates/multiple IIT’s of the 		     conveyance.  IF the VEH segment is repeated, supply only element

VEH09, VEH10 and VEH20.

3  This segment is  used by CBP.

Data Element Summary

REF. DES. 	DATA ELEMENT	NAME 							            ATTRIBUTES

VEH02    539 		Vehicle Identification Number 			X     AN 		    1/30

Unique identification number stamped on the vehicle by the manufacturer.

For CBP:

VIN of the conveyance (motorized unit).  If the conveyance is not registered in the carrier’s account, it is required here.

VEH09   127 		Reference Identification 				O/Z  AN 		     1/50

Reference identification as defined for a particular Transaction Set, or as

specified by the Reference Identification Qualifier.

For CBP:

This is the license plate of the truck.  (CBP Truck manifest accepts only 17 positions. Only alphas and numerics are accepted, no special characters).  If the Conveyance is not registered in the carrier’s account,

it is required here.  Maximum of 4 occurrences  will be accepted.

VEH17     26 		Country Code 					X/Z    ID 		       2/3

Code identifying the country.

For CBP:

The  2 alpha ISO country code of the state/province in VEH25.

License plate country of registration.   Required if country is other than US, 	CA, MX...

Valid country codes are found in the Appendix

VEH20	   40		Equipment  Description Code			O     ID		       2/2				Code identifying the type of equipment.

For CBP

This is the Conveyance Type code.  This is required in CBPTruck manifest.

CODE 	DEFINITION		                          Seal Required

‘Y’ = ‘Yes’  ‘?’ = ‘possibly’  ‘(N)’ = ‘likely No’  ‘Y’ = ‘Likely Yes’

AR		Armored Truck			Y

AU		Automobile			Y

BT		Box Truck			Y

BU		Bus				Y

BV		Beverage Truck			Y

BY		Bicycle				Y

CO		Construction Vehicle		Y

(general)

EV		Emergency Vehicle		Y

(general)

FE		Ferry				Y

FM		Farm Tractor			Y

GB		Garbage Truck			Y

MC		Motorcycle			Y

OC		Other				Y

PM		Pick-up Truck with 		Y

Camper

PN		Panel Truck			Y

PU		Pick-up Truck			Y

PV		Passenger, Van			Y

RV		Recreation Vehicle		Y

TR		Tractor (semi)			Y

TV		Van				Y

VEH21	127		Reference Identification				X    AN                        1/80

Reference identification as defined for a particular Transaction Set, or as

specified by the Reference Identification Qualifier.

In CPB truck manifest this is the ACE ID, or any legitimate carrier account   ID for the conveyance. CPB Truck manifest accepts only 50 positions.

VEH22	128		ID Code Qualifier				X     ID    	         2/3				Code designating the system/method of code structure  used for identification.

CODE 	DEFINITION

AID		ACE ID

CNV		Conveyance ID

VEH23    322		Load/empty Status Code				O     ID  	                       1/1

For CBP:

Code qualifying VEH20

CODE 	DEFINITION

C		Indicates party whose bond is obligated for the release of 				instruments of international traffic- empty IIT’s covered by the 				Carrier’s bond.

In standard  manifests, this indicates shipments 					consisting solely of empty IIT’s covered by Carrier’s bond

I		Indicates party whose bond is obligated for the release of

Instruments of international traffic.- empty IIT’s covered by the 				importer’s bond.

In standard  manifests, this indicates shipments 					consisting solely of empty IIT’s covered by importer’s 				bond

A		Indicates party whose bond is obligated  for the release of 				international traffic – merchandise and IIT’s covered by the 				carrier’s bond.

In standard  manifests,  this indicates a shipment 					consisting of merchandise and 	IIT’s.  IIT’s covered by 				carrier’s bond.

B		Indicates party whose bond is obligated for release of

instruments of international traffic- merchandise and IIT’s 				covered by the importer’s bond.

In standard  manifests, this indicates a shipment 					consisting of merchandise and IIT’s.  IIT’s covered by 				importer’s bond.

VEH24	127		Reference Identification				O/Z   AN		       1/50

Reference identification as defined for a particular Transaction Set, or as

specified by the Reference Identification Qualifier.

For CBP:

This is the transponder number on the conveyance.  Required if conveyance has transponder and  pre-registered conveyance not supplied in VEH21 and VEH22. CBP Truck manifest accepts only 50

Positions.

VEH25  127 		Reference Identification 				O/Z  AN 	                     1/50

Reference identification as defined for a particular Transaction Set, or as

specified by the Reference Identification Qualifier. This is the DOT Number.

For CBP:

Required.  If the carrier has pre-registered the DOT number in his account 		and has	Indicated a Pre-registered Conveyance, this is not required. CBP  		truck manifest accepts only 8 positions.

VEH26	1715		Country Subdivision				X      ID		     1/3				Code identifying the country subdivision

For CBP:

License plate State/Province of registration.  If the conveyance is not 	registered in the carrier’s account information, it is required here

In CBP truck manifest this is used to indicate the1- 3 position  state/province code.

The following codes will be used to designate U.S. and Mexican states and Canadian provinces

CODE	DEFINITION                                                                                                                                                                  U.S. States

This list is used by CBP:

AK	Alaska

AL	Alabama

AR	Arkansas

AZ	Arizona

CA	California

CO	Colorado

CT	Connecticut

DC	District of Columbia

DE	Delaware

FL	Florida

GA	Georgia

GU	Guam

HI	Hawaii

IA	Iowa

ID	Idaho

IL	Illinois

IN	Indiana

KS	Kansas

KY	Kentucky

LA	Louisiana

MA	Massachusetts

MD	Maryland

ME	Maine

MI	Michigan

MN	Minnesota

MO	Missouri

MS	Mississippi

MT	Montana

NC	North Carolina

ND	North Dakota

NE	Nebraska

NH	New Hampshire

NJ	New Jersey

NM	New Mexico

NV	Nevada

NY	New York

OH	Ohio

OK	Oklahoma

OR	Oregon

PA	Pennsylvania

PR	Puerto Rico

RI	Rhode Island

SC	South Carolina

SD	South Dakota

TN	Tennessee

TX	Texas

UT	Utah

VA	Virginia

VI	Virgin Islands

VT	Vermont

WA	Washington

WI	Wisconsin

WV	West Virginia

WY	Wyoming

Mexican States

This list is used by CBP:

AGU	Aguascalientes

BCN	Baja California Nord

BCS	Baja California Sur

CAM	Campeche

CHH	Chihuahua

CHP	Chiapas

COA	Coahuila

COL	Colima

DIF	Distrito Federal

DUR	Durango

GRO	Guerrero

GUA	Guanajuato

HID	Hidalgo

JAL	Jalisco

MEX	Mexico State

MIC	Michoacan

MOR	Morelos

NAY	Nayarit

NLE	Nuevo Leon

OAX	Oaxaca

PUE	Puebla

QUE	Queretaro

ROO	Quintana Roo

SIN	Sinaloa

SLP	San Luis Potosi

SON	Sonora

TAB	Tabasco

TAM	Tamaulipas

TLA	Tlaxcala

VER	Vera Cruz

YUC	Yucatan

ZAC	Zacatecas

Canadian Provinces

This list is used by CBP:

AB	Alberta

BC	British Columbia

MB	Manitoba

NB	New Brunswick

NL	New Foundland and Labrador

NS	Nova Scotia

NT	Northwest Territories

NU	Nunavut

ON	Ontario

PE	Prince Edward Island

QC	Quebec

SK	Saskatchewan

YT	Yukon Territory

Segment:		M7	Seal Numbers

Position:	0225

Loop:		___

Level:	N/A

Usage: 	Optional

Max Use: 	5

Purpose: 	To record seal numbers used and the organization that applied the seals.

Syntax:	  N/A

Semantic:	  N/A

Comments: 	  5 M705 indicates the name of the organization who applied the seal(s)

Notes:	  1 CBP Truck manifest accepts only 1 M7 segment

2 This segment is used by CBP

Data Element Summary

REF. DES. 	DATA ELEMENT 	NAME 							      ATTRIBUTES

M701     225 		Seal Number 				 		M     AN 	2/15

Unique number on seal used to close a shipment.

CBP will accept up to 15 positions.

M702     225 		Seal Number 						O     AN 	2/15

Unique number on seal used to close a shipment.

CBP will accept up to 15 positions.

M703     225 		Seal Number 						O     AN 	2/15

Unique number on seal used to close a shipment.

CBP will accept up to 15 positions.

M704     225 		Seal Number 						O     AN 	2/15

Unique number on seal used to close a shipment.

CBP will accept up to 15 positions.

Segment: 		CII 	Conveyance Insurance Information

Position:	0260

Loop:	____

Level:	N/A

Usage: 	Optional

Max Use: 	3

Purpose: 	Conveyance Insurance Information

Syntax:	N/A

Semantic: 	    1 CII01 is the Name of the Insurance Company

2 CII02 is the Policy Number of the Insurance

3 CII03 is the Year policy in CII02 was Issued

5 CII05 is the Amount of the Insurance on policy in CII02

Notes:	    1 CBP Truck manifest accepts only 1 CII segment

2 This segment is used by CBP

Data Element Summary

REF. DES. 	DATA ELEMENT 	NAME 							       ATTRIBUTES

CII01 	93 		Name 						M     AN		1/60

Free-form name.

The name of the insurance company for the conveyance in VEH.  Required if any shipment on the trip is hazardous – I.E - if H101 is present.  	REF01 code HD is also required.

CII02    127		Reference Identification				M      AN		1/50

Reference identification as defined for a particular Transaction Set, or as

specified by the Reference Identification Qualifier.

This is the policy number issued by the entity in CII01.  Required if H101 is present.  REF01 code HD is also required

CII03  1095 		Year 						M      N0 	 4/4

Four position designation of the year expressed as CCYY.

This is the year of the policy identified in CII02.  Required if H101 is present.  REF01 code HD is also required

CII05    610 		Amount 					M      N2 	 1/15

Monetary amount. Amount of insurance covered in CII02.

Required if H101 is present. REF01 code HD is also required. Default to U.S. dollars. Truck manifest accepts only 12 positions. The last 2 positions are considered to be cents.

Segment: 		NM1 	Individual or Organizational Name

Position:	0270

Loop: 	NM1

Level:	N/A

Usage: 	Optional

Max Use: 	1

Purpose: 	To supply the full name of an individual or organizational entity

Syntax: 	    1 P0809

If either NM108 or NM109 is present, then the other is required.

2 C1110

If NM111 is present, then NM110 is required.

3 C1203

If NM112 is present, then NM103 is required.

Semantic: 	     2 NM102 qualifies NM103.

Comments: 	     A NM110 and NM111 further define the type of entity in NM101.

B NM112 can identify a second surname.

Notes:	     1  If Party is pre-registered in ACE, either ACE ID, legitimate

Party proximity card to be provided in NM109.

2 At least one party to be specified.  If NM1 is provided then DMG, REF, 			         N3, N4 are required.  Only one ‘Person in Charge’ per trip.  Multiple 			         Crew and Passengers allowed.

3 This segment is  used by CBP .

Data Element Summary

REF. DES. 	DATA ELEMENT 	NAME 							      ATTRIBUTES

NM101       98 		Entity Identifier Code 				M     ID 		2/3

Code identifying an organizational entity, a physical location, or an individual

For CBP:

Person in charge, all crew members and/or passengers.    At least one party to be specified.  If NM1 is 	provided then DMG, REF, N3, N4 are required. Only one Person in Charge per Trip, Multiple Crew, and Passengers allowed.

CODE	DEFINITION

EJ		Principal person (Person in Charge)

CRW		Crew Member

QF		Passenger

NM102   1065 		Entity Type Qualifier   				M     ID 		1/1

Code qualifying the type of entity.

Party’s full name

CODE	DEFINITION

1		Person surname (full name)

NM103   1035 		Name Last or Organizational Name 		X     AN 		1/60

Individual last name or organizational name.

CBP truck manifest accepts only 40 positions. Aduana Mexico

NM104   1036 		Name First 					O     AN 		1/35

Individual first name.

For CBP

NM105   1037 		Name Middle 					O     AN 		1/25

Individual middle name or initial.

For CBP

NM108       66 		Identification Code Qualifier 			X      ID 		1/2

Code designating the system/method of code structure used for Identification

For CBP:

Qualifier for Automated Commercial Environment ID, or ACE proximity card to be 	provided in NM109

CODE	DEFINITION

A7		ACEID

CBP Truck manifest only 10 positions are accepted. N3 and N4 are required here

PY		FAST Proximity Card ID

In CBP Truck manifest only 50 positions are accepted. DMG, REF, N3 and N4 are not required.

NM109       67 		Identification Code 				X     AN 		2/80

Code identifying a party or other code.

For CBP:

Required if NM108 is present.  CBP Truck manifest accepts only 10    positions for ACE ID, 17 positions for proximity card.

NM112   1035 		Name Last or Organizational Name 		X     AN 		1/60

Individual last name or organizational name.

Segment: 		DMG 	Demographic Information

Position:	0310

Loop: 	NM1

Usage: 	Optional

Max Use: 	1

Purpose: 	To supply demographic information

Syntax: 	    1 P0102

If either DMG01 or DMG02 is present, then the other is required.

2 P1011

If either DMG10 or DMG11 is present, then the other is required.

3 C1105

If DMG11 is present, then DMG05 is required.

Semantic: 	    2 DMG02 is the date of birth.

7 DMG07 is the country of citizenship.

9 DMG09 is the age in years.

11 DMG11 is used to specify how the information in DMG05, including repeats

of C056 was collected.

Comments:	    N/A

Notes:	   1   All fields are required if the information isn’t pre-registered.

2  This segment is  used by CBP and Aduana Mexico.

Data Element Summary

REF. DES. 	DATA ELEMENT 	NAME 							      ATTRIBUTES

DMG01   1250 		Date Time Period Format Qualifier 		X     ID 		2/3

Code indicating the date format, time format, or date and time format.

CODE	DEFINITION

DB		Date of birth

For CBP :

DMG02   1251 		Date Time Period 				X     AN 		1/35

Expression of a date, a time, or range of dates, times or dates and times.

CPB truck manifest accepts only CCYYMMDD format.  Person in Charge’s, Crew Member’s, or Passenger’s date of birth expressed as format indicated in DMG01

DMG03   1068 		Gender Code 					O     ID 		1/1

Code indicating the sex of the individual.

CODE	DEFINITION

M		Male

F		Female

For CBP:

DMG06   1066 		Citizenship Status Code 				O     ID 		 1/2

Code indicating the citizenship status.

CODE	DEFINITION

8		Citizen

DMG07       26 		Country Code 					O     ID 		2/3

Code identifying the country.

The 2 alpha ISO code identifying the country of citizenship of the Person in Charge, Crew member or passenger.   Valid country codes are found in the Appendix

Segment:		REF 	Reference Information

Position:	0310

Loop: 	NM1

Level:	N/A

Usage: 	Optional

Max Use: 	10

Purpose: 	To specify identifying information

Syntax: 	  1 R0203

At least one of REF02 or REF03 is required.

2 If either C04003 or C04004 is present, then the other is required.

3 If either C04005 or C04006 is present, then the other is required.

Semantic: 	  4 REF04 contains data relating to the value cited in REF02

Comments:	  N/A

Notes:    1 All fields are required if the information isn’t pre-registered.

2 This segment is  used by CBP

Data Element Summary

REF. DES. 	DATA ELEMENT 	NAME 							      ATTRIBUTES

REF01     128 		Reference Number Qualifier    				M    ID	 2/3

Code qualifying the Reference Identification.

Code identifying  crew member’s or passenger’s travel document. 5J and 	5K are not considered travel documents.   At least one REF01 with 	either

5J or 5K and a travel document is required for trip. All codes are used by CBP as indicated:

CODE	DEFINITION

HD		DOT Hazardous Number

Person in Charge or Crew Member’s Hazmat Endorsement Number.  If this code is used it MUST be listed first, before all others.

AAG		Military ID Document (number)

ACU		Permanent Resident Card C2 (number) (effective June 2009)

ACW		Passport (number)

AEF		U.S. Passport Card (number)

AEW		NEXUS Card (number) (effective June 2009)

AGR		U.S. Alien Registration Card  A1 (number) (effective June 				2009)

AGS		Permanent Resident Card (1998-2003) C1 (number) (effective

June 2009)

AGT		Visa Non-Immigrant (number) (effective June 2009)

ALR		U.S. Alien Registration Card A2 (number)

ALV		Secure Electronic Network for Travelers Rapid Inspection

(SENTRI) Card  (number) (effective June 2009)

ALX		U.S. Merchant Mariner Document ID (number) (effective June 						2009)

ALY		Native American Indian/INAC (number) (effective June 2009)

BCN		Birth Certificate (expires June 2009)

BCP		Laser Visa Border crossing card (number)

CDN		Citizenship Document Number  (Citizenship Card) (expires 						June 2009)

CON		Certificate of Naturalization (Expires June 2009)

OTD		Other Travel Document ID (Expires June 2009)

REP		DHS Re-entry permit (number)

RTP		DHS Refugee Travel Document (number)

- Visa Immigrant (number)

5J		Driver’s License (number)

5K		Commercial Driver’s License (number)

6W		Enhanced Driver’s Licence (EDI) ID (number) (effective June

2009)

REF02     127 		Reference Identification 					X     AN 	1/50

Reference information as defined for a particular Transaction Set, or as

specified by the Reference Identification Qualifier.

For CBP :

The  number of the travel document/license identified in REF01. For hazmat endorsement, if REF01 is ‘HD’ insert state/province hazmat endorsement code.  If the state/province has no hazmat endorsement code, insert ‘Y’

REF03     352 		Description 						X     AN 	1/80

A free-form description to clarify the related data elements and their content.

For CBP :

The 2/3alpha State/Province of Issuance code of 					the travel document identified in REF01: This is required with codes  		‘5J’, ‘5K’ .

REF04	  C040		Reference Identifier					O     ID	    2/3

To identify one or more reference numbers or identification numbers as specified by the reference qualifier.

For CBP :Only the following code will be used.  Required

cODE	DEFINITION

ZZ		Other, mutually defined

REF05       26		Country Code						O     ID       2/3

Code identifying the country

For CBP :

The 2 alpha ISO code of the country of issuance of REF02 or the country in

Which the state/province in REF03 is located.  This is required with codes 	 	‘BCP’, ‘BCN’, ‘CDN’, ‘30’, ‘ACW, OTD.

Valid country codes are found in the Appendix

Segment:		N3	Party Location

Position:	0320

Loop:	NM1

Level:	N/A

Usage: 	Optional

Max Use: 	2

Purpose: 	To specify the location of the named party

Syntax:	N/A

Semantic:	N/A

Comments:	N/A

Notes:     1  Provide one N3 per party specified in NM1.  This is the address to which 			    the person in NM1 is going. If NM108 is ‘PY’ this is not required.

2 This segment is used by CBP

Data Element Summary

REF. DES. 	DATA ELEMENT 	NAME 							       ATTRIBUTES

N301     166 		Address Information 				M     AN 		1/55				Address information

For CBP:

Must be U.S. Address .

N30 2     166 		Address Information 				O     AN 		1/55

Address information

Segment: 		N4 	Geographic Location

Position:	0330

Loop: 	NM1

Level:	N/A

Usage: 	Optional

Max Use: 	1

Purpose: 	To specify the geographic place of the named party

Syntax: 	    1 E0207

Only one of N402 or N407 may be present.

2 C0605

If N406 is present, then N405 is required.

3 C0704

If N407 is present, then N404 is required.

Semantic:	    N/A

Comments: 	    A A combination of either N401 through N404 (or N405 and N406) may be

adequate to specify a location.

B N402 is required only if city name (N401) is in the U.S. or Canada

Notes:        1 This segment is  used by CBP

Data Element Summary

REF. DES. 	DATA ELEMENT 	NAME 							      ATTRIBUTES

N401       19 		City Name 					O     AN 		    2/30

Free-form text for city name.

Must be U.S. address..

N403     116 		Postal Code 					O     ID 		     3/15

Code defining international postal zone code excluding punctuation and blanks

(ZIP code for the United States).  (CBP Truck manifest accepts only 10 	positions).

N404	 26		Country Code					X      ID		     2/3

Code identifying the country

Valid country codes are found in the Appendix

N407   1715		Country Subdivision				X      ID		     1/3				Code identifying the country subdivision

In CBP truck manifest this is used to identify the 1 to 3 position state/province code.  Use the list in VEH26  for acceptable U.S. and Mexican states and Canadian provinces

Segment:		P4	Port Information

Position:	0400

Loop: 	P4

Level:	N/A

Usage: 	Mandatory

Max Use: 	1

Purpose: 	To transmit identifying information for a port

Syntax:     N/A

Semantic: 	    1 P401 is used for CBP port code (Census Schedule D).

2 P402 is the estimated date of arrival.

3 P403 is used for number of bills of lading.

4 P404 is the Facilities Information and Resources Management System

(FIRMS) Code

5 P405 is the Estimated Time of Arrival for P402

6 P406 is the date conveyance departed prior port.

7 P407 is the time conveyance departed prior port.

Notes: 	    1 Only one P4 segment allowed per trip for Truck applications

2  This segment is used by CBP

Data Element Summary

REF. DES. 	DATA ELEMENT 	NAME 							      ATTRIBUTES

P401      310 		Location Identifier 					M     AN	1/30

Code which identifies a specific location.

For CBP:

CPB truck manifest accepts only 4 positions.  Port of expected entry. First US Physical port of arrival in U.S. Census Schedule D code.  In Preferred shipments the word PORT may be substituted for the port of expected arrival code.

P402    373 		Date 							M     DT 	8/8

Date expressed as CCYYMMDD where CC represents the first two digits of the calendar year.

For CBP:

Estimated Date of Arrival.  For Standard shipments,  this is  required.

P403     380		Quantity						O    R     1/15

Numeric value of quantity

Total number of bills

P405     337		Time							O     TM  4/8

Time expressed in 24-hour clock time as follows: HHMM, or HHMMSS, or HHMMSSDD, where H = hours (00-25), M=minutes (00-59),  S = integer seconds, and DD= decimal seconds, decimal seconds are expressed as follows: D = tenths (0-9) and DD = hundredths (00-99).

Fot CBP:

Scheduled/estimated Time of Arrival at First U.S. Port.  Time must be in 		U.S. Eastern Standard/Daylight Time.  In truck manifest, Time is required.

Segment:		LX	Transaction Set Line Number

Position:	0600

Loop: 	LX

Level:	N/A

Usage: 	Mandatory

Max Use: 	1

Purpose: 	To reference a line number in a transaction set.

Syntax:	N/A

Semantic:	N/A

Comments:	N/A

Notes:	    1  Start with one (1), and increment by one (1) for each iteration of the

Loop.

- Only one P4/LX loop is allowed per transaction.

- This segment is used by CBP

Data Element Summary

REF. DES.	DATA ELEMENT 	NAME 							       ATTRIBUTES

LX01      554 		Assigned Number 					M     N0 	1/6

Number assigned for differentiation within a transaction set.

Segment: 		M13 	Manifest Amendment Details

Position:	0700

Loop: 	LX

Level:	N/A

Usage: 	Optional

Max Use: 	1

Purpose: 	To correct a manifest record prior to vessel arrival or to amend a manifest

record after vessel arrival.

Syntax: 	    1 P0810

If either M1308 or M1310 is present, then the other is required.

2 P1112

If either M1311 or M1312 is present, then the other is required.

Semantic: 	    1 M1301 is the Bill of Lading Issuer.

2 M1302 is used for discharge port (4-digit numeric census schedule D).

3  M1305 is new manifest quantity and is used if M1303 = “R”

8 M1308 is used to report individual portions of a consolidated shipment.

9 M1309 is the conveyance operator’s Standard Carrier Alpha Code

10 M1310 is the issuer code for the consolidated shipment.

Comments: 	   N/A

Notes: 	    1 Used to reflect any change. Required if M1009 is ‘Y’.

2 This segment is currently used by CBP

Data Element Summary

REF. DES. 	DATA ELEMENT 	NAME 							      ATTRIBUTES

M1301     140 		Standard Carrier Alpha Code 				M     ID 	2/4

Standard Carrier Alpha Code

For CBP :

This is the Bill Issuer Code of the Bill of Lading/Waybill Number in M1304

Preferred Data Element .

M1302     310 		Location Identifier 					M     AN 	1/30

Code which identifies a specific location.

Same as P401

M1303     580 		Amendment Type Code 					O     ID 	1/1

Code identifying type of manifest amendment.

###### For CBP: Required

CODE 	DEFINITION

A 		Add a Bill of Lading

D 		Delete a Bill of Lading

M		Replace a shipment segment, either adding, deleting, or

Substituting original manifest information

For CBP:

This permits users to substitute information in existing

Manifests without deleting and transmitting a new 309 set.

The segment with the corrected information immediately follows the M13. The segments must be submitted in loops: NM1,DMG, REF, N3, N4; N1  (shipper), N3, N4, N1 (consignee), N3, N4; VID,  M7, N10, VC,H1.  If anything is updated in an N10, all N10 segment in the loop must be submitted.  The M11 segment must be submitted every time the replace submission occurs.  The N1 loops must also be submitted  every time a replace submission occurs.

M1304     598 		Bill of Lading/Waybill Number 				M    AN	1/25

Identification number assigned to the shipment by the carrier or consolidator.

The 12 alphanumeric number  equivalent to the number in the M1101.  This 				number with the DCAC in the M1301 is the unique bill of lading number, or 				shipment control number.  The Customs broker must have this number as well 			for filing an entry.  (preferred data element)

M1306     393 		Amendment Code 					O     ID 	2/2

Code giving the reasons for the amendment of the manifest record.

For CBP:

This segment is required to show changes after submission of complete 	data to CBP

CODE 	DEFINITION

Standard Manifest

01 	Not laden aboard per evidence from foreign shipper, or

amended pro-bill

02	Error in manifesting, not laden on this trip; laden on 				subsequent trip for transportation to United States per

evidence in files.

03 	Clerical error in manifesting per pro-bill in files.

05	Erroneously duplicated by another pro-bill on the same 			manifest

06	Prematurely landed or over carried to another United States

port where proper disposition was made per evidence in  			files

07	Inadvertently delivered without CBP release.  Goods will be

redelivered intact or carrier will pay duty, taxes, and/or 			liquidated damages

11	Overage omitted from manifest through clerical error.

Standard Manifest/Inbond

04 	Pilfered, stolen, or lost while in custody of the carrier,

per signed statement of person in charge or his 	authorized agent, or log extract in files.

18 	Electronic manifest delayed by communications failure

19	Amendment to non-critical field or provision of additional data 	to manifest

27	Short delivery

28	Wrong delivery

29	Merchandise damaged/destroyed during transport.

- Inadvertently delivered without CBP authorization.  Goods will be redelivered intact or carrier will pay duty, taxes, and/or

Liquidated damages

In-bond

- Error in quantity manifested at port of origin.  MDR (Manifest 	Discrepancy Report) will be filed at origin to correct in-bond 	entry

- Merchandise removed from original container and restuffed as 	part of in-bond movement.

- In-bond diversion.  Reason documented and on file.

Amendment Codes are required for bill of lading updates after a 309 set 				with a code ‘W’ in M1009 or after a 353 set with a code ‘Z’ in the M1501 has

been transmitted and accepted. Amendment codes are not required for 				preferred shipments.

M1308    598		Bill of lading/Waybill Number		 		X    AN    1/25

Identification number assigned to the shipment by the carrier or 					consolidator.

For CBP applications, this is a unique 16 position identifier 					made up of the SCAC in M1310 and the 12 alphanumeric number 					found in M1308.  This is the Bill Control  (House Bill) Number.

M1310	140		Standard Carrier Alpha Code				X   ID	2/4

This is the Bill Issuer Code of the Bill of Lading/Waybill Number in 					M1308.  This could be a deconsolidator, freight forwarder, or NVOCC.

Segment: 		M11 	Manifest Bill of Lading Details

Position:	0800

Loop: 	LX

Level:	N/A

Usage: 	Optional

Max Use: 	1

Purpose: 	To transmit bill of lading detail information for a manifest

Syntax: 	    3 P0304

If either M1103 or M1104 is present, then the other is required.

5 P0506

If either M1105 or M1106 is present, then the other is required.

7 P0708

If either M1107 or M1108 is present, then the other is required.

11 P1113

If either M1111 or M1113 is present, then the other is required.

15 C1514

If M1115 is present, then M1114 is required.

18 C1815

If M1118 is present, then M1115 is required.

19 C1918

If M1119 is present, then M1118 is required.

Semantic: 	    1 M1101 is the unique bill of lading number. .

2 M1102 is used for Port of Lading (5-Digit Numeric Census Schedule  K)

3 M1103 is used for total number of pieces on a bill of lading using the

smallest package unit (maximum eight digits).

4 M1104 is the smallest package unit code.

11 M1111 is house bill number for consolidation.

12 M1112 is the unique bill of lading issuer code.

13 M1113 is the issuer code of the consolidated shipment.

14 M1114 is the code of the secondary party nominated to receive bill of

lading status notifications.

15 M1115 is the code of the 2nd secondary party nominated to receive bill of

lading status notifications.

18 M1118 is the Standard Carrier Alpha Code (SCAC) of an additional second

notify carrier.

19 M1119 is the Standard Carrier Alpha Code (SCAC) of an additional second

notify carrier.

20 M1120 is the last place/port prior to loading.

21 M1121 is the first foreign port.

22 M1122 identifies mode of transportation from the last place/port prior to

loading.

23 M1123 is the method of payment for transportation.

24 M1124 is the Maritime Administration Cargo Preference Program Code

(see code source 926).

Comments: 	  A  If identifying the US Customs bill number, the maximum length shall be 12.

.If identifying the Canadian cargo control number, the maximum length shall

be 25.

Notes: 	   1 For CBP:

Unique Identification is composed of the SCAC from M1112 and the

unique identifier in the M1101.

2 U.S. Truck manifest accepts a maximum use of only 999 iterations of  /

the P4/LX loop.

3 This segment is used by CBP

Data Element Summary

REF. DES. 	DATA ELEMENT 	NAME							      ATTRIBUTES

M1101     598 		Bill of Lading/Waybill Number 				M    AN 	1/25

Identification number assigned to the shipment by the carrier or consolidator.

For CBP:

CBP truck manifest accepts only 12 positions.  For CBP applications, this is a unique 16 position identifieris made up of the SCAC in M1112 and the alphanumeric number found in M1101. This is the Shipment Control Number and  must be unique for one year. A Customs Broker must have this number as well for filing an entry.

CBP Truck manifest accepts only alpha-numerics no spaces or special characters (Preferred Data Element) (Required)

M1102     310 		Location Identifier 					M    AN	 1/30

Code which identifies a specific location.

For CBP:

In CBP truck manifest this is the foreign port/point of loading. This is required in standard manifest. This may be a code or a free form name of the foreign location at which the shipment was loaded on the conveyance.  The qualifiers are in M1125.  In preferred shipments  this is required as a Schedule K Code if the port/point of loading is not in Canada.  (Preferred Data element). In in-bond shipments, and shipments designated for broker download only the Schedule K codes will be accepted.

M1109      582 		Bill of Lading Type Code 				O     ID 	2/2

Code identifying the type of bill of lading.

For CBP:

This is a shipment release type code indicating whether a bill of lading is Regular, Preferred, PAPS, or special release category.

Default is ‘00’.  ’33’ or ’34’  required for Preferred Shipments.  (Preferred 		Data Element). Required.

CODE 	DEFINITION

00		Regular Bill

CN		Consolidated Shipment

Required when carrier transmits a master shipment control number expecting bill control numbers associated with it to be transmitted.

- Sec 321 release

N1006 and N1011 are required

14		Intangibles

15		Intransit

Used in USA-Canada-USA, Canada-USA-Canada intransit

Movements. Future use

18 		Goods Astray

M1127 and M1128 are required.

24 		Single Entry Per C4 Line Release

All of the C4 Line Release codes must have the same filer 						and same importer codes.

- Individual Entry for Multiple C4 Line Releases

- Preferred  FAST Shipment

Preferred Shipments that do not have pre-filed entries.

For future use.

- Preferred Pre-Arrival Processing System (PAPS) shipment

Preferred Shipments that do not have pre-filed entries.

For future use.

35		Sec 321 Release

For  release under section 321 with FDA-BTA considerations.

- CF-7523

Not a bill type. Used for statistical purposes only to alert

CBP that a paper CF-7523 is attached requiring clearance.

- CF-3311

Not a bill type. Used for statistical purposes only to alert

CBP that a paper CF-3311 is attached requiring clearance.

- CF-3299

Not a bill type. Used for statistical purposes only to alert

CBP that a paper CF-3299 is attached requiring clearance.

- Release under Sec 321

Release in Courier Manifest Transactions – Future Use

- Release as Intangibles.  No entry is permitted

Used in Courier Manifest Transactions – Future Use

- Gifts

Used in Courier Manifest Transactions – Future Use

- American Goods Returned

Used in Courier Manifest Transactions – Future Use

- Gifts, U.S. Possessions

Used in Courier Manifest Transactions – Future Use

- Personal Shipment

Used in Courier Manifest Transactions – Future Use

M1110	600		Place of Receipt by Pre-carrier 				O     AN 	1/17

The city or country in which the pre-carrier took possession of the cargo.

For CBP:

Alpha name of the city of the bill of lading origin where carrier took possession of the cargo  if different from M1102. Required for truck manifest.

M1111	  598		Bill of Lading/Waybill Number				X    AN	1/25

Identification number assigned to the shipment by the carrier or consolidator.

For CBP:

this is a unique 16 position identifier made up of the SCAC in M1113 and the 12 position alphanumeric number found in M1111.  This is the Bill Control (House Bill) Number. If M1111, then M1101 is required .

M1112     140 		Standard Carrier Alpha Code 				M     ID 	2/4

Standard Carrier Alpha Code

For CBP:

This is the Bill Issuer Code of the Bill of Lading/Waybill Number in M1101.

M1113	  140		Standard Carrier Alpha Code				X     ID	2/4

Standard Carrier Alpha Code

For CBP:

This is the Bill Issuer Code of the Bill of Lading/Waybill Number in M1111.

M1125	  128		Reference Number Qualifier				X     ID    2/3

Code qualifying the reference identifier .

For CBP:

CODE 	DEFINITION

K		Census Schedule K code for foreign ports and inland K codes

For Canadian provinces

In CBP truck manifest it is required to submit as ‘K space’

IA		IATA airport codes

ZZ		Free form name of the port/point of lading

These codes are required for  the port/ point of lading in M1102.   (Only Schedule K is applicable for Preferred Shipments, in-bond movements, and broker downloads).

M1126       284		Service Level Type					O    ID	2/2

Code indicating extent of transportation service requested.

For CBP:

CODE 	DEFINITION

CG		Ground

DS		Door Receive (Door to Door)

CD		Collect on Delivery

DC		Delivery Confirmation

EV		Excess Value Insurance

SD		Saturday Pickup (Delivery)

ON		Overnight

ND		Next Day (1 Day Service)

IZ		International Second Day (2 Day Service)

M1127	   373 		Date 							M     DT 	8/8

Date expressed as CCYYMMDD where CC represents the first two digits of the calendar year.

The date of departure from the U.S. This is required when a shipment is claiming free astray status, or free release without entry under Headnote 1 of the Tariff Act (M1109 code 18).  To qualify for this status the EDA of the shipment  for into the US must not be more that 45 days from the date indicated here.

M1128	1073		Yes/No Condition Response Code		O     ID		1/1

Code indicating a Yes or No condition or response.

This is required when a shipment is claiming free astray status, or free release without entry under Headnote 1 of the Tariff Act (M1109 code 18).  To qualify as free astray the shipment must have been in the custody of foreign Customs while out of the country.  To qualify for free release without entry under Headnote 1 the shipment must have been in the custody of the carrier while out of the country.

Segment:		N9	Extended Reference Identification

Position:	0850

Loop: 	LX

Level:	N/A

Usage: 	Optional

Max Use: 	999

Purpose: 	To transmit information as specified by the reference identification qualifier

Syntax: 	    2 R0203

At least one of N902 or N903 is required.

6 C0605

If N906 is present, then N905 is required.

3 If either C04003 or C04004 is present, then the other is required.

5 If either C04005 or C04006 is present, then the other is required.

Semantic: 	    6 N906 reflects the time zone which the time reflects.

7 N907 contains data relating to the value cited in N902.

Comments:         N/A

Notes:          For CBP:

The use of code ‘BEN’ in N901 and the entry number in N902 is no longer

Valid and should not be used by Truck AMS participants.

This segment is used by CBP

Data Element Summary

REF. DES. 	DATA ELEMENT 	NAME 							      ATTRIBUTES

N901     128 		Reference Number Qualifier				M     ID	 2/3

Code qualifying the Reference Identifier

CODE 	DEFINITION

8S		Broker Identification

For CBP:

Used to pass routing number of the broker identified in

N902.  If 8S is used it must be followed by N1 code ‘CB’

BL		Government Bill of Lading

Future Use

BM		Bill of Lading Number

Future Use

BN		Booking Number

Future Use

CG		Consignee’s Order Number

Future Use

CN		Carrier’s Reference Number (pro/invoice)

Future Use

CO		Customer Order Number

Future Use

CR		Customer Reference Number

Future Use

CX		Consignment Classification ID

Future Use

ED		Export Declaration

Future Use

EP		Softwood Lumber Permit

FN		Forwarder’s Agent’s Reference Number

Future Use

FP		Forestry Permit Number

Future Use

GB		Grain Block Number

Future Use

GR		Grain Order Reference Number

Future Use

HS	Harmonized Code System (Canada) – used when the shipment is not an IE or T&E movement, or if the HS code received from the shipper is greater than 6 digits

Future Use

IN		Consignee’s Invoice Number

Future Use

LT		Lot Number

Future Use

MA	Ship Notice/Manifest number – used for the automotive ASN number

Future Use

MB	Master Bill Of Lading

Future Use

MR		Merchandise Type Code

For CBSA

OB 		Ocean Bill of Lading

Future Use

OM		Ocean Manifest

Future use

OW		Service Order Number

Future Use

PK		Packing List Number

Future Use

PN		Permit Number

Future use

PO		Purchase Order Number

Future Use

RC	Rail Routing Code – Used by Automotive Manufacturers and Brokers

Future Use

S7		Stack Train Identification

Future Use

SI 		Shipper’s Identifying Number for Shipment (SID)

For CBP:

In standard and preferred manifests this is the 			number used by the importer/exporter to reference the 		shipment and is required.  (Preferred Data Element)

SO		Shipper’s Order

Future Use

ST		Store Number

Future Use

SW		Seller’s Sale Number

Future Use

UT		Unit Train

Future Use

VA		Vessel Agent Number

Future Use

WU		Vessel

Future Use

WY		Rail Waybill Number

Future Use

XP		Previous Cargo Control Number

Future Use

ZE		Coal Authority Number

Future Use

ZZ		Mutually Defined

Future Use

FEN		Foreign Entry Number

For CBP and Aduana Mexico:

This is the Mexican Pedimento. When M1201 is ‘63’				for Mexican border Immediate Exports this is required.

N902     127 		Reference Identification 					X      AN	 1/50

Reference identification as defined for a particular Transaction Set, or as

specified by the Reference Identification Qualifier.

For CBP:

Routing Number/ Reference value as per qualifier.

Currently Routing number  is Port (4) + Filer (3) + Office Code (2) = 9

Shipper’s Identifying Number for Shipment – this is for preferred shipments only.

Mexican Pedimento Number:

Maximum/minimum length: 15 digits all numbers (no letters,characters, dashes,hyphens)

Format for Mexican Pedimento: yyppbbbbddddddd

yy = the last 2 years of a year

pp = the Aduana Mexico port code

bbbb = the Mexican broker code

ddddddd = the document number

Segment: 		N1 	Party Identification

Position:	1000

Loop: 	N1

Level:	N/A

Usage: 	Optional

Max Use: 	1

Purpose: 	To identify a party by type of organization, name and code

Syntax: 	 2 R0203

At least one of N102 or N103 is required.

3 P0304

If either N103 or N104 is present, then the other is required.

Semantic:	    N/A

Comments:      A This segment, used alone, provides the most efficient method of providing

organizational identification. To obtain this efficiency the "ID Code" (N104)

must provide a key to the table maintained by the transaction processing

party.

B  N105 and N106 further define the type of entity in N101.

Notes:	      For CBP:

1 There must be at least two occurrences of the N1 loop. One must

contain an N101 of ‘SH’  - Shipper - with the name of the party tendering 	      the shipment to the truck carrier in N102 or the ID in N103. The second 		      occurrence must contain an N101 of ‘CN’ – consignee -  with the party’s 	      name in N102.

2 For a Standard Shipment, Shipper and Consignee required.  For a 	 	      Preferred Shipment, Shipper, Consignee, and C-TPAT Importer (N101 – 		      ‘IM’ are required.  For Preferred Shipments these parties to be pre-		      registered in ACE and hence carrier needs to provide only ID’s in N103, 	 	      N104).

3 For standard shipments, either a legitimate party ID to be provided in		     N104, or full party data is to be provided.

For CBSA

1 The N1 loop is used to identify the following parties:

Mandatory –

  - Shipper (SH)

  - Consignee (CN)

Optional –

  - Notify Party

Data Element Summary

REF. DES. 	DATA ELEMENT 	NAME 							      ATTRIBUTES

N101       98		Entity Identifier Code					    M    	2/3

Code identifying an organizational entity, a physical location, property, or an individual.

For CBP:

CODE 	DEFINITION

B5		Affiliated Company

BK 		Bank

BN 		Beneficial Owner

BO 		Broker or Sales Office

BS 		Bill and Ship To

BT 		Bill-to-Party

BY 		Buying Party (Purchaser)

C1 		In Care Of Party no. 1

C2 		In Care Of Party no. 2

CA 		Carrier

CB 		Customs Broker

This is required if N901 is ‘8S’

CD 		Consignee (To Receive Mail and Small Parcels)

CE 		Consignee (To receive large parcels and freight)

CF 		Subsidiary

CG 		Carnet Issuer

CI 		Consignor

CJ 		Automated Data Processing (ADP) Point A qualifier for an 						address of a location providing ADP support to an entity that is 						the intended recipient of a transmission, but that entity does 						not have its own organic capability to receive the transmission 						directly, relying instead on the support provided by the ADP 						point

CL 		Container Location

CN 		Consignee (For CBP and Aduana Mexico)(Tipo de persona)

CP 		Party to Receive Cert. of Compliance

CQ 		Corporate Office

CR 		Container Return Company

CS 		Consolidator

D8 		Dispatcher

DA 		Delivery Address

DB 		Distributor Branch

DC 		Destination Carrier

DF 		Material Disposition Authorization Location

DH 		Doing Business As

DM 		Destination Mail Facility

DR 		Destination Drayman

DS 		Distributor

DT 		Destination Terminal

DU 		Resale Dealer

DV 		Division

DW 		Downstream Party

DX 		Distiller An entity that manufactures an alcoholic product using 						Bureau of Alcohol, Tobacco and Firearms approved methods 						and formulas

EH 		Exhibitor

EV 		Selling Agent

EX 		Exporter

FN 		Filer Name

FQ 		Pier Name

FS 		Final Scheduled Destination Customs duties, excise taxes, and 					use of bonded fuels are dependent on whether an  aircraft 						flight originated or is destined for an international location, 						these codes would be used to note those occurrences

FW 		Forwarder

HW 		Designated Hazardous Waste Facility

HX 		Transporter of Hazardous Waste

I1 		Interested Party

IC 		Intermediate Consignee

IF 		International Freight Forwarder

IK 		Intermediate Carrier

IM 		Importer

J3		Authorized entity

J6		Power of Attorney

JV		Joint Owner

JW		Joint Venture

LA		Attorney

LL 		Location of Load Exchange (Export) Name of the location at 						which load (trailer) is exchanged with another motor  carrier for 					export

MA 		Party for whom Item is Ultimately Intended

MC 		Motor Carrier

MF 		Manufacturer of Goods

MO 		Release Drayman

MQ 		Delivery Location

NP		Notify Party (For CBSA)

OB		Ordered By

OO 		Order Of (Shippers Orders) - (Transportation)

OP 		Operator of property or unit

OR 		Origin Drayman

OW		Owner of Property or Unit

OY 		Owner of Vehicle

PE 		Payee

PF 		Party to Receive Freight Bill

PJ 		Party to Receive Correspondence

PK 		Party to Receive Copy

PL 		Party to Receive Purchase Order

PM 		Party to receive paper Memo of Invoice

PN 		Party to Receive Shipping Notice

PO 		Party to Receive Invoice for Goods or Services

PR 		Payer

PU 		Party at Pickup Location

PW 		Pickup Address

RD 		Destination Intermodal Ramp

RO		Original Intermodal Ramp

SD 		Sold To and Ship To

SE 		Selling Party

SF 		Ship From

SH		Shipper (For CBP and Aduana Mexico)(Tipo de persona)

SM 		Party to Receive Shipping Manifest

SO 		Sold To If Different From Bill To

SP 		Party filling Shipper's Order

SQ 		Service Bureau A business entity that is responsible for 						providing computer resources to other firms that do not have 						computer resources of their own

SS 		Steamship Company

ST 		Ship To

SU 		Supplier/Manufacturer

T3 		Terminal Location A geographic location where a motor or rail 						or air or water terminal is located

T4 		Transfer Point A geographic location where a shipment is 						transferred or diverted to a new destination

T6 		Terminal Operator

TR 		Terminal

TT 		Transfer To

UC 		Ultimate Consignee

V1 		Surety

XR		Mexican Customs broker

WH 		Warehouse

XU		United States Customs Broker

YE 		Third Party

ZF 		Break Bulk Point

Z1		Party to receive Status

AEB 		Airport Authority

AEE 		Port Authority

IAV		Other Related Party

SNP		Secondary Notify Party

N102       93 		Name						                 X   AN	1/60

Free-form name.

Required for CBSA and Aduana Mexico

N103       66		Identification Code Qualifier			      	   X     ID	1/2

Code designating the system/method of code structure used for Identification

For CBP:

Preferred Data Element

(((CODE 		DEFINITION

- Standard Carrier Alpha Code (SCAC)

For CBP:

For Secondary Notify Party, and authorized entity

A7		ACE ID Number (shipper, consignee, importer)

For CBP

FT		FAST ID (shipper. Consignee)

For CBP

BF		Broker/Filer

For CBP

- The 9 position Dun’s number identifying the shipper,

Consignee, importer

For CBP

FI 	Federal Taxpayer’s Identification Number  (importer, consignee)

For CBP:

To report the Internal Revenue Service identification

Number of the shipper, consignee,  or importer in N101.

FR		Facilities Information Requirements Management System

(FIRMS) code.

For CBP:

For secondary notify party. Future use.

CU		Customs Assigned Importer Number

For CBP:

N104       67 		Identification Code					  X    AN	2/80

Code identifying a party or other code.

For CBP:

Required for any ID in N103.   (Preferred Data Element)

Current  codes and numerical parameters are: 		will accept 3

ACE ID: 	            	 10  AN

Dun’s number:   	 9 (NNNNNNNNN)

IR number:      	 12 (EIN – NN-NNNNNNNNN

SSN – NNN-NN-NNNN)

FAST ID:                7 AN

Filer Code:             3AN

SCAC:                    4 A

FIRMS:		  1 A, 3 N

Customs Assigned 6N – 5N

Importer Number    (6N = year+port code)

Segment:		N2	Additional Name Information

Position:	1050

Loop:	P4/LX/N1

Level:	N/A

Usage: 	Optional

Max Use: 	1

Purpose: 	To specify additional names

Syntax:	N/A

Semantic:	N/A

Comments:	N/A

Notes:     1  Provide additional names to the party listed in N1.  This plus N1 allows

For a maximum of 250 bytes.

Data Element Summary

REF. DES. 	DATA ELEMENT 	NAME 							       ATTRIBUTES

N201      93 		Name 						M     AN 		1/60				Free-form name

N20 2     93 		Name		 				O     AN 		1/60

Free-form name

Segment:     	N3	Party Location

Position:	1100

Loop: 	N1

Level:	N/A

Usage: 	Optional

Max Use: 	2

Purpose: 	To specify the location of the named party

Syntax:     N/A

Semantic:     N/A

Comments:     N/A

Notes:     For CBP:

1 For any ID in N103. Required (Preferred Data Element)

2 One Address occurrence per party in N1.  Required for 					    Shipper/Consignee/Importer if pre-registered party ID not indicated in 		                 N104.

3  This segment is used by CBP

Data Element Summary

REF. DES. 	DATA ELEMENT 	NAME 							       ATTRIBUTES

N301     166 		Address Information 				M     AN 		1/55				Address information

N302     166 		Address Information 				O     AN 		1/55

Address information

Segment: 		N4 	Geographic Location

Position:	1200

Loop: 	N1

Usage: 	Optional

Max Use: 	1

Purpose: 	To specify the geographic place of the named party

Syntax: 	    2 E0207

Only one of N402 or N407 may be present.

6 C0605

If N406 is present, then N405 is required.

7 C0704

If N407 is present, then N404 is required.

Comments: 	    A A combination of either N401 through N404 (or N405 and N406) may be

adequate to specify a location.

B N402 is required only if city name (N401) is in the U.S. or Canada

Notes:	   1    Refer to the N1 loop usage in the Standards Convention chapter

2    One Address occurrence per party in N1.  Required for Shipper/Consignee/

Importer if pre-registered party ID not indicated in N104

3    This segment is used by CBP

Data Element Summary

REF. DES. 	DATA ELEMENT 	NAME 							      ATTRIBUTES

N401       19 		City Name 					O     AN 		    2/30

Free-form text for city name.

For CBP

N403     116 		Postal Code 					O     ID 		     3/15

Code defining international postal zone code excluding punctuation and blanks.

For CBP:

(ZIP code for the United States).  (CBP Truck manifest accepts only 10 	positions).

For CBP

N404	 26		Country Code					X      ID		     2/3

Code identifying the country

Valid country codes are found in the Appendix

N407   1715		Country Subdivision				X      ID		     1/3				Code identifying the country subdivision

For CBP:

In CBP truck manifest this is used to identify the 1 to 3 position state/province code.  Use the list in VEH26  for acceptable U.S. and Mexican states and Canadian provinces.

For CBSA:

CBSA does not currently accept Mexican state codes.

For CBP and CBSA

Segment:		PER	Administrative Communications Contact

Position:	1250

Loop: 	N1

Usage: 	Optional

Max Use: 	1

Semantic:	N/A

Comments:	N/A

Purpose: 	To identify a person or office to whom administrative communications should be

directed

Syntax: 	    3 P0304

If either PER03 or PER04 is present, then the other is required.

5 P0506

If either PER05 or PER06 is present, then the other is required.

7 P0708

If either PER07 or PER08 is present, then the other is required.

Semantic:	N/A

Comments:	N/A

Notes: 	1 Only 1 telephone number of EMAIL identification is allowed per party in 	 	             N1.  Specify if pre-registered party ID not indicated in N104.

2 This segment is used by CBP .

Data Element Summary

REF. DES. 	DATA ELEMENT 	NAME 							      ATTRIBUTES

PER01	  366		Contact Function Code					M    ID    2/2

Code identifying  the major duty or responsibility of the person or group named        				CODE 	DEFINITION

IC		Information Contact

PER03     365 		Communication Number Qualifier 			X     ID	2/2

Code identifying the type of communication number.

CODE 	DEFINITION

TE 		Telephone

EM		Electronic Mail (EMAIL)

PER04     364 		Communication Number 					X    AN	1/256

Complete communications number including country or area code when

applicable.

CBPTruck manifest accepts only 30 positions for ‘TE’ in PER03.  CBP Truck

Manifestr accepts maximum 255 positions for ‘EM’ in PER03.

SS

SSSegment:		M12 	In-bond Identifying Information

Position:	1300

Loop: 	M12

Usage: 	Optional

Max Use: 	1

Purpose: 	To transmit in-bond information.

Syntax: 	    2 E0206

Only one of M1202 or M1206 may be present.

2 C0608

If M1206 is present, then M1208 is required.

3 P0809

If either M1208 or M1209 is present, then the other is required.

4 P1011

If either M1210 or M1211 is present, then the other is required.

Semantic: 	    3 M1203 is a 4-digit numeric census schedule D when identifying a U.S. port,

and three-digit memorandum D when identifying a Canadian port. It is the

port of destination if M1201 is 61. It is the port of export if M1201 is 62 or 63.

4 M1204 is 5-digit numeric census schedule K. It is the foreign port of

destination if M1201 is 62 or 63.

7 M1207 identifies the carrier to whom liability is transferred.

12 M1212 is the US Food and Drug Administration prior notification requirement

indicator.  A “Y” indicates that the shipper has advised the commodity is

subject to the prior notification requirement.  An “N” indicates the

commodity is not subject to the prior notification requirement.  If blank, the

default value is “N”.

13 M1213 is the estimated date of departure of the in-bond shipment from

the U.S.

14 M1214 is the FIRMS (Facilities Information Resources Management

System) code of the location of the in-bond shipment.

Comments: 	    A If M1202 does not contain the paperless entry number, then M1206 is

required when used for US In-Bond information.

B M1205 is the value in whole dollars of the in-bond movement. Use twenty

dollars per kilo if value is unknown.

Notes: 	        For CBP:

- M1206 contains the conventional in-bond number.

- The M12 segment is not used by CBSA.  It is used as a trigger      segment to allow the use of the R4 segment.

- This segment is used by CBP

- Commencing on May , 2007, Truck AMS participants will no longer be able to use the carrier’s shipment control number as inbond control number and must use the CBPF 7512 number or paperless in-bond number (‘V’ number) for in-bond control.  This capability may be restored in the future.

Data Element Summary

REF. DES. 	DATA ELEMENT 	NAME 							      ATTRIBUTES

M1201     581 		Customs Entry Type Code			M     ID 		2/2

Code defining the type of entry assigned by CBP..

CODE 	DEFINITION

- Immediate Transportation

For CBP and CBSA

- Transportation Exportation

For CBP and Aduana Mexico

- Immediate Exportation

For CBP

65		Permit to Proceed  (Permit to Transfer)

For CBP:

This code is used to designate local transfers.  M1207, 		M1208, M1209, M1214 are required for a local transfer.  		Future use

69 		Transit

For CBP:

USA-Canada-USA.  Future use

70 		Transit

For CBP:

Canada-USA-Canada.  Future use

M1202     601 		Customs Entry Number				X     AN 		1/15

Automated Commercial System Code Furnished by U.S. Customs Service.

For CBP

CBP truck manifest accepts only 11 positions.  Carriers authorized to participate in Paperless in-bond will be assigned a 3-position filer identification code beginning with ‘V’. This code is used with a check digit routine to create a paperless in-bond number. Check digit routine is defined by CBP CAMIR document.

In CBP truck manifest, if M1201, M1203 are provided  M1202 may be used to provide the paperless in-bond number

M1203    310 		Location Identifier 				O     AN 		1/30

Code which identifies a specific location.

For CBP:

CBP truck manifest accepts only 4 positions.  Code for the US port of in-bond destination and/or unloading in the US. This is the Customs clearance point.  It may also be the point of exit from the U.S.

This must not be the P4 port of arrival  if the entry type in M1201 is ‘61’ or ‘62’.  This must be the P4 port of arrival if the entry type in M1201 is ‘63’.

Exceptions: New York Seaport, Newark, JFK; Seattle-Tacoma; Los Angeles-Long Beach; San Francisco-Oakland; Miami and its subports are considered technically equivalent for IE movements

M1204     310 		Location Identifier 				O     AN 		1/30

Code which identifies a specific location.

For CBP:

CBP truck manifest accepts only 5 positions.  Code identifying the foreign port of destination for in-bonds exported

From US.  This is required for M1201 codes ‘62’ and ‘63’

M1206     603 		In-bond Control Number 				X     AN 		1/25

Currently assigned control number for in-bond movement.

For CBP:

CBP truck manifest accepts only 9 positions, with check digit. This is

the CBPF 7512 number. In CBP truck, if M1201, M1203 are provided, M1206 may be used as in-bond control number.

M1207	  140		SCAC						O    ID		2/4				Standard Carrier Alpha Code

For CBP:

This is the Standard Carrier Alpha Code of the onward carrier to whom 		an in-bond shipment is transferred beyond the initiating carrier

M1208     128 		Reference Number Qualifier 			X      ID 		2/3

Code qualifying the Reference Identifier

For CBP:

Is required when M1202 or M1206 is present to signify a carrier other 			than the importing carrier assumes liability for the in-bond movement.

If designated carrier has more than one bond, the carrier will have to submit the bond number that is liable. May also be present if M1214 contains a CFS indicator to signify a Permit to Transfer.  This is the transfer carrier.

CODE 	DEFINITION

BI 		Bonded Carrier Internal Revenue Service Identification

Number. Format is NN-NNNNNNNNNXX

TRC		Transfer Carrier Identification Number

This Internal Revenue Service Identification Number 						identifies the carrier assuming liability in a Permit to 						Transfer.  Future use

M1209     127 		Reference Identification 				X     AN 		1/50

Reference information as defined for a particular Transaction Set, or as specified by the Reference Identification Qualifier.

For CBP:

CBP truck manifest accepts only 12 positions.  This is the  Carrier Identification number associated with the code In M1208

M1212	1073		Yes/No Condition Response Code		O     ID		1/1

Code indicating a Yes or No condition or response.

For CBP:

In CBP Truck manifest this is the FDA indicator pointing out that the shipment must be monitored by the FDA under the Bioterrorism Act.  This applies only to Transportation and Exportation (TE) In-bonds.  If ‘Y’ the shipper will provide information to FDA before shipment arrival.

M1213	  373		Date						O     DT   	8/8

Date expressed as CCYYMMDD

For CBP:

Estimated date of departure of in-bond shipment from US.  Required if 		M1201 codes are ‘62’ or ‘63’.

M1214	  310		Location Identifier				O     AN		1/30

Code which identifies a specific location.

For CBP:

In CBP truck manifest this is a Facilities Information Resources Management System (FIRMS) code indicating arrival/transfer facility to which the shipment is going.  Also, this is the Facilities Information Resources Management	Systems (FIRMS) code at destination in-bond port facility (CFS).  If 	destination in-bond port facility code, in-bond data (M1201, M1202, M1203,	M1204, M1206, M1209) are required if applicable. CBP truck manifest accepts only 4 positions.

Segment:		VID	Vehicle ID

Position:	1500

Loop: 	VID

Level:	N/A

Usage: 	Optional

Max Use: 	1

Purpose: 	To identify a conveyance and its attributes.

Syntax:	  14 L141518

If  either VID14 or VID15 (VID18) is present, then the other is required.	        		  15 E1518

Only one of VID15 or VID18 may be present

15 C1516

If VID15 is present then VID16 is required.

16 L161518

If VID16 is present, then at least one of VID15 or VID18 is required.

18 C1816

If VID18 is present, then VID16 is required.

Semantic: 	   12 VID12 is the Census Schedule K Code for the foreign port of loading on a

vessel.

13  VID13 is the Standard Carrier Alpha Code (SCAC) of the Haulage Rights

Carrier.

- VID14 is the license plate of the equipment

- VID15 is the state or province of the license in VID14

- VID16 is the country of the license in the VID15 or VID18

- VID17 is the ACE (Automated Commercial Environment) ID of the

Equipment identified in the VID03

- VID18 is the country subdivision of the license in the VID14

Notes:	         For CBP:

1  Either the ACE ID or Equipment Number or License plate, 		        		        State/Province, Country, or full equipment data is required.

2 CBP will accept 4 occurrences of license plates (Preferred data

element) in the P4/LX/VID loop.  If the VID is repeated in loops, only

the VID03, VID14 and VID18 if applicable, should be supplied.

3 The VID segment is not currently used by CBSA.  It is used as a trigger

segment to allow the use of the N10 loop.

4.This segment is used by CBP

Data Element Summary

REF. DES. 	DATA ELEMENT 	NAME 							      ATTRIBUTES

VID01       40 		Equipment Description Code 				M     ID 	2/2

Code identifying type of equipment used for shipment.

For CBP:

Preferred Data Element

CODE 	DEFINITION		                          Seal Required   license plate required

‘Y’ = ‘Yes’  ‘?’ = ‘possibly’  ‘(N)’ = ‘likely No’  ‘Y’ = ‘Likely Yes’

BI		Beverage rack trailer		Y		N		CB		Gooseneck Trailer		Y		N

CH 		Chassis				Y		N

CL		Other Length Sea			N		N

Container (closed top)

CU		Other Length Sea			N		N

Container (open top)

CZ 		Refrigerated Container		N		N

DD		Double-drop trailer		Y		N

DT		Drop back trailer			Y		N

FH		Flat Bed trailer with headboards 	N		N

FN		Flat Bed trailer with no headboards N		N

FR		Flat Bed Trailer			Y		N

FT		Flatbed/perform Trailer		Y		N

HC		Hopper Car (covered)		Y		N

HE		Horse Trailer			Y		N

HO		Hopper Car (open)		Y		N

HP		Hopper Car  (covered; 		Y		N

pneumatic discharge)

LT		Livestock Trailer			Y		Y

L1		Tank Trailer (liquids)		Y

not heated/not insulated

L2		Tank Trailer (liquids)		Y		N

heated/not insulated

L3		Tank Trailer (liquids) 		Y		N

not heated/insulated

L4		Tank Trailer (liquids) heated/I	Y		N

Insulated

NC		No Equipment

For CBP:

Required if no equipment is used for the trip

OE 		Other				N/A

RD		Fixed Rack, double-drop trailer	Y		Y		RG		Gondola-closed 			Y		Y

RO		Gondola-open			Y		Y

RS		Fixed Rack , single-drop trailer	Y

RT		Controlled temperature		Y		Y

SD		Single-drop trailer			Y		Y

TC		Auto carrier/trailer			Y		Y

TF		Trailer dry freight			Y		Y

TK		Tank trailer (food grade liquids)	Y		Y

TL		Semi-truck trailer			Y		Y

TW		Controlled Temperature Trailer	Y

T1		Tank Trailer (gas)-not heated/	Y		Y

not insulated

T2		Tank Trailer (gas)-heated/		Y		Y

not insulated

T3		Tank Trailer (gas)-not heated/I	Y		Y

insulated

T4		Tank Trailer (gas)-heated/insulated	Y		Y

T5		Tank Trailer (chemicals) – 		Y		Y

not heated/not insulated

T6		Tank Trailer (chemicals) – 		Y		Y

heated/not insulated

T7		Tank Trailer (chemicals) – 		Y		Y

not heated/insulated

T8		Tank Trailer (chemicals) – 		Y		Y

heated/insulated

2B		20 ft. container (closed top)	N		N

sea container

- 20 ft. container (open top)    	N		N

sea container

4B		40 ft. container (closed top) 	N		N

sea container

- 40 ft. container (open top)  	N		N

sea container

VID02	206		Equipment Initial					O     AN  1/4

Prefix or alphabetic part of an equipment unit’s identifying number.

For CBP:

Required in CBP truck manifest if equipment initial precedes the equipment   	number.  Preferred Data Element.

VID03     207 		Equipment Number 					M     AN 	1/15

Sequencing or serial part of an equipment unit’s identifying number (pure numeric

form for equipment number is preferred).

For CBP:

Number required if license plate information not provided.  If license plate information is provided/no Equipment indicated by ‘NC’ in VID01, supply ‘No Number’.  (Preferred Data Element).

VID10	322		Load/Empty Status Indicator				O    ID	1/1

Code which specifies the loaded condition of transportation equipment.

This element is used by CBP and Aduana Mexico

For CBP:

CODE 	DEFINITION

C		Indicates party whose bond is obligated for the release of 				instruments of international traffic- empty IIT’s covered by the 				Carrier’s bond.

In standard and Preferred shipments, 						this indicates shipments consisting solely of empty IIT’s 				covered by Carrier’s bond

I		Indicates party whose bond is obligated for the release of

Instruments of international traffic.- empty IIT’s covered by the 				importer’s bond.

In standard and preferred shipments, 						this indicates shipments consisting solely of empty IIT’s 				covered by importer’s bond

A		Indicates party whose bond is obligated  for the release of 				international traffic – merchandise and IIT’s covered by the 				carrier’s bond.

In standard and preferred shipments, 						this indicates a shipment consisting of merchandise and 				IIT’s.  IIT’s covered by carrier’s bond.

B		Indicates party whose bond is obligated for release of 					instruments of international traffic- merchandise and IIT’s 				covered by the importer’s bond.

In standard and preferred shipments, 						this indicates a shipment consisting of merchandise and 				IIT’s.  IIT’s covered by importer’s bond.

VID14     127		Reference Identification				O/Z    AN  1/80

Reference Identification as defined for a particular Transaction Set, or as

specified  by the Reference Identification Qualifier.

For CBP:

This is the license of the trailer/equipment.  Required in CBP Standard truck shipments if Equipment has license plates.  Required for CBP Preferred Shipments if Equipment Number not reported in VID03. Only alphas and numerics are accepted, no special characters. Truck manifest accepts 4 different licence plates for the same equipment. There may be 4 P4/LX/VID loops to accommodate the license plates.  If there are more than 1P4/LX/ VID loop, the first VID contains  the equipment number or ‘no number’ in VID03.  The subsequent VID segments contain ‘same’ in VID03. This will prevent the equipment from being counted as a new equipment.  CBP Truck manifest accepts only 50 positions.

VID16      26		Country Code						X/Z     ID    2/3

Code identifying the country.  The 2 alpha ISO country code of the state/province 			in VID15

For CBP:

The 2 alpha ISO country code of the state/province in VID18..  Required if license plates are given in VID14 and the country code is other than ‘US’,’CA’, ‘MX’. (Preferred Data Element)

Valid country codes are found in the Appendix

VID17	127		Reference Identification					O/Z   AN  1/80

Reference Identification as defined for a particular Transaction Set, or as

specified  by the Reference Identification Qualifier.

In CBP truck manifest this is the ACE ID for the equipment. CBP Truck	 Manifest accepts only 10 positions

VID18   1715		Country Subdivision					X/Z     ID	     1/3				Code identifying the country subdivision

For CBP, CBSA, Aduana Mexico.

Required if license plate provided in VID14. (Preferred Data Element).  In CBP truck manifest this is used to identify the 1 to 3 position state/province code.  Use the list in VEH26  for acceptable U.S. and Mexican states and Canadian provinces for CBP

Segment:		M7	Seal Numbers

Position:	1570

Loop: 	VID

Level:	N/A

Usage: 	Optional

Max Use: 	5

Purpose: 	To record seal numbers used and the organization that applied the seals.

Comments: 	 A M705 indicates the name of the organization which applied the seal(s)

Notes: 	 1 This segment is used by CBP.  Truck AMS accepts only 1 occurrence.

Data Element Summary

REF. DES. 	DATA ELEMENT 	NAME 							      ATTRIBUTES

M701     225 		Seal Number 				 		M     AN 	2/15

Unique number on seal used to close a shipment.

For CBP:

CBP will accept up to 15 positions.

M702     225 		Seal Number 						O     AN 	2/15

Unique number on seal used to close a shipment.

CBP will accept up to 15 positions.

M703     225 		Seal Number 						O     AN 	2/15

Unique number on seal used to close a shipment.

CBP will accept up to 15 positions.

M704     225 		Seal Number 						O     AN 	2/15

Unique number on seal used to close a shipment.

CBP will accept up to 15 positions.

Segment: 		N10 	Quantity and Description

Position:	1600

Loop: 	N10

Level:	N/A

Usage: 	Optional

Max Use: 	1

Purpose: 	To indicate line item quantity, description, marks and numbers, commodity

code, weight and Customs value

Syntax:         4 P0405

If either N1004 or N1005 is present, then the other is required.

6 P0613

If either N1006 or N1013 is present, then the other is required.

7 P0708

If either N1007 or N1008 is present, then the other is required.

Semantic: 	    9 N1009 is the CBP Bar Code Number for Line Release

11 N1011 is the country of manufacture of the goods

12 N1012 is the country of the final destination of the goods

13 N1013 is the currency of the value of the goods

Comments:	   N/A

Notes:	1  For CBP:

N10 may be repeated for Free-Form Description, Marks and Numbers,

And C4 code.

2 If a commodity requires extra lines of description, send N1002

only.  N1001 may be 0 (zero) or empty.

3 Each new commodity requires a Weight Unit Code (N1007),

Weight, (N1008) and a Manifest Unit Code (N1011).

4 This segment is used by CBP.

Data Element Summary

REF. DES. 	DATA ELEMENT 	NAME							      ATTRIBUTES

N1001     380 		Quantity 						O     R 	1/15

Numeric value of quantity.

For CBP:

Required for a Standard and preferred Manifest.  A minimum of 1 N10 segment is required per container/equipment for a shipment.  If there is more than one line of description for a commodity in a shipment, the first N1001 for each 	commodity will have the quantity for that commodity.  If there is more than one VID per shipment, each VID will have a minimum of one N10 segment, containing the quantity of the commodity in the container .  ACE will compute the total quantity for the bill by adding all the quantities in all the VID’s.  If a carrier transmits a shipment control number (master bill) to which bill control numbers  (house bills) will be associated carri indicates by code ‘CN’ in M1109 and transmits a ‘0’ in this element.  ACE will total the quantities for this bill by adding the quantities of all associated house bills.

N1002     369 		Free-form Description 					O     AN 	1/45

Free-form descriptive text.

For CBP:

Used for commodity description.  Provide commonly used trade terms or

HTS Schedules.  (Preferred data element). At least 1 line of description is

Required.

N1003      87		Marks and Numbers					O    AN	1/48

Marks and Numbers used to identify a shipment or parts of a shipment.

For CBP:

CBP truck manifest accepts only 45 positions

N1004      23 		Commodity Code Qualifier				X      ID 	1/1

Code identifying the commodity coding system used for Commodity Code.

For CBP:

Required if M1201 is ‘62’ or ‘63’

CODE 	DEFINITION

J 		Harmonized Code System (United States)

N1005       22 		Commodity Code 					X     AN 	1/30

Code describing a commodity or group of commodities.

For CBP:

Harmonized Tariff Code number. Truck manifest accepts minimum of 6 maximum 10 digits. Required if M1201 is ‘62’ or ‘63’ .

N1006     602 		Customs Shipment Value 				X     AN 	2/8

Customs value in whole dollars.

For CBP:

Required if M1201 is ‘61’, ‘62’ or ‘63’. Required for Sec 321 Release and if M1109 is ‘13’ or ‘35’, or ‘18’. The dollar value must be greater than ‘0’.

N1007     188 		Weight Unit Code 					X      ID 	1/1

Code specifying the weight unit.

For CBP:

If the description in N1002 is by specific commodities, this is required for each new commodity. This is required if M1201 is ‘62’ or ‘63’ for Corps of Engineers

For CBSA:

Required for a new commodity.

For Aduana Mexico:

Weight unit code (this code not listed here)

Unidad de medida.  Required

CODE 	DEFINITION

G		Grams

For CBP

K 		Kilograms

For CBP and CBSA

L 		Pounds

For CBP and CBSA

O		Ounces

For CBP

T		Tons

For CBP

N1008        81		Weight 							X     R 	1/10

Numeric value of weight .

For CBP:

If the description in N102 is by specific commodities, this is required for each new commodity.  CBP truck manifest accepts only 8 positions.

For CBSA:

Required for a new commodity. Always use gross weight.

For Aduana Mexico:

Weight (net)

Peso neto.  Required

N1009     127 		Reference Identification 					O     AN 	1/50

Reference identification as defined for a particular Transaction Set, or as

specified by the Reference Identification Qualifier.

For CBP:

Used for CBP C4 Line Release number.

If the M1109 equals ‘24’ then all of the C4 Line Release numbers

must have the same filer and same importer codes.

If multiple C4 Line Release numbers are used then each must have

an N1001.

If multiple C4 codes have the same bill of lading/waybill number, the 	importer and filer must be the same.  All C4 codes will be combined into 	one entry.  If a bill of lading/waybill has multiple C4’s but either the 	importer or filer are different, a new entry must be used for those C4’s. 	Truck manifest only accepts 14 positions.

N1010     599 		Manifest Unit Code 					O      ID 	1/3

Code defining the smallest package unit for the bill of lading.

###### For CBP:

CODE 	DEFINITION

BAG 		Bag

BBL 		Barrel

BDL	 	Bundle

BIC 		Bing Chest

BIN	 	Bin

BKT	 	Bucket

BLE 		Bale

BOX 		Box

BSK		Basket

CAN	 	Can

CAR 		Carcass

CAS 		Case

CBC 		Container Bulk Cargo

CBY 		Carboy

CCS	 	Can Case

CHS	 	Chest

COL	 	Coil

COR 		Cord

CRT 		Crate

CSK	 	Cask

CTN	 	Carton

CYL	 	Cylinder

DBK	 	Dry Bulk

DRM 		Drum

DZ		Dozen

FT		Feet

GAL	 	Gallon

HED	 	Heads of Beef

HMP	 	Hamper

KEG	 	Keg

L		Liter

LBK	 	Liquid Bulk

LOG	 	Logs

LUG	 	Lugs

LVN 		Lift Van

M		Meters

PAA		Pairs

PAL 		Pail

PCL 		Parcel

PCS 		Pieces

PKG 		Package

POV 		Private Vehicle

QTR 		Quarters of Beef

REL 		Reel

ROL 		Roll

SFT		Square Feet

SAK 		Sack

SHT 		Sheet

SID 		Sides of Beef

SKD 		Skid

TBE	 	Tube

TBN 		Tote Bin

TIN 		Tin

TNK 		Tank

UNT 		Unit

Used for empty cars and conveying flat cars (TOFC/COFC)

VEH	 	Vehicle

VPK 		Van Pack

WDC	 	Wooden Case

For CBSA:

Required for a new commodity.  For code list see ASC X12 data element 211 – packaging Form Code.

N1011	   26		Country Code						O    ID    2/3

Code identifying the country

For CBP:

Country of origin.  This is required for SEC 321 moves if M1109 is ‘13’,’35’

Valid country codes are found in the Appendix

N1013     100		Currency Code						X    ID    3/3

Code (Standard ISO) for country in whose currency the charges are specified.

For CBP:

In truck, if N1006 is present then N1013 is required.

CODE 	DEFINITION

USD		US Dollars

Segment:   		VC	Motor Vehicle Control

Position:	1620

Loop: 	N10

Usage: 	Optional

Max Length: 	134

Purpose: 	To define motor vehicle identification and logistics.

Syntax:	N/A

Semantic: 	    5 VC05 is the automotive manufacturer route code.

12 VC12 is the direction the headlights of the vehicle point

13 VC13 is the final destination ramp location as assigned by the manufacturer.

Comments:	N/A

Note:        This segment is used by CBP

Data Element Summary

REF. DES. 	DATA ELEMENT 	NAME 							      ATTRIBUTES

VC01     539 		Vehicle Identification Number 				M     AN 	1/30

Unique identification number stamped on the vehicle by the manufacturer.

The VIN number of a vehicle imported as merchandise

Segment: 		H1 	Hazardous Material

Position:	1650

Loop: 	H1

Level:	N/A

Usage: 	Optional

Max Use: 	1

Purpose: 	To specify information relative to hazardous material

Syntax: 	7 P0708

If either H107 or H108 is present, then the other is required.

Semantic:	N/A

Comments: 	1 This segment is required when the shipment contains hazardous material.

2 H107 is lowest temperature for hazardous materials.

Notes:      This segment is used by CBP.

Data Element Summary

REF. DES. 	DATA ELEMENT 	NAME 							      ATTRIBUTES

H101       62 		Hazardous Material Code 				M    AN 	4/10

Code relating to hazardous material code qualifier for regulated hazardous

materials.

For CBP:

UN Code

If UN code is present, CII01, CII02, CII03, CII05, and REF01 code ‘HD’ is 	   required for Standard Manifest.   CBP truck manifest accepts only 4 positions.  (Preferred Data Element)

H102	 209		Hazardous Material Class Code				O    AN	¼

Code specifying the kind of hazard for a material.

H103	 208		Hazardous Material Code Qualifier			O     ID   1/1

Code which qualifies the Hazardous Material Class Code (209)

CODE 	DEFINITION

U		United Nations

H105       63 		Hazardous Material Contact 				O     AN 	1/24

Name of person or department to contact in case of emergency.

For CBP :

This is the free-form name for the HAZMAT contact.

H110  	365      		Communication Number Qualifier 			X     ID 	2/2

Code identifying the type of communications number.

CODE 	  DEFINITION

TE		 Telephone

EM		  Electronic mail (EMAIL)

For CBP:

H110 and H111 will be used to provide Hazardous Material communications information until a PER segment for this purpose is incorporated into the 309 data set.  This is required in truck AMS

H111	   364     		Communication Number 		 			X    AN 	1/256

Complete communications number including country or area code when applicable.

H110 and H111 will be used to provide Hazardous Material communications information until a PER segment for this purpose is incorporated into the 309 data set.  CBP truck manifest accepts only 30 positions in H111.  CBP

Truck manifest accepts maximum 255 positions for ‘EM’ in H111.  This is

Required in truck AMS.

Segment: 		SE 	Transaction Set Trailer

Position:	2000

Loop: 	N/A

Level:	N/A

Usage: 	Mandatory

Max Use: 	1

Purpose: 	To indicate the end of the transaction set and provide the count of the

transmitted segments (including the beginning (ST) and ending (SE) segments).

Syntax:     N/A

Semantic:     N/A

Comments: 	1 SE is the last segment of each transaction set.

Notes:    This segment is used by CBP .

Data Element Summary

REF. DES. 	DATA ELEMENT 	NAME 							      ATTRIBUTES

SE01       96 		Number of Included Segments 				M     N0 	1/10

Total number of segments included in a transaction set including ST and SE

segments.

SE02     329 		Transaction Set Control Number 				M     AN 	4/9

Identifying control number that must be unique within the transaction set

functional group assigned by the originator for a transaction set

APPENDIX

ISO country codes that may be supplied when required in data element  26

Valid Country codes are:					(updated June 28, 2007)

CODE 	DEFINITION

AF	Afganistan

AX	Aland Islands

AL	Albania

DZ	Algeria

AS	American Samoa

AD	Andorra

AO	Angola

AI	Anguilla

AQ	Antarctica

AG	Antigua and Barbuda

AR	Argentina

AM	Armenia

AW	Aruba

AU	Australia

AT	Austria

AZ	Azerbaijan

BS	Bahamas

BH	Bahrain

BD	Bangladesh

BB	Barbados

BY	Belarus

BE	Belgium

BZ	Belize

BJ	Benin

BM	Bermuda

BT	Bhutan

BO	Bolivia

BA	Bosnia-Herzegovina

BW	Botswana

BV	Bouvet Island

BR	Brazil

IO	British Indian Ocean Territory

VG	British Virgin Islands

BN	Brunei

BG	Bulgaria

BF	Burkina Faso

BI	Burundi

KH	Cambodia

CM	Cameroon

CA	Canada

CV	Cape Verde

KY	Cayman Islands

CF	Central African Republic

TD	Chad

CL	Chile

CN	China (mainland)

TW	China (Taiwan)

CX	Christmas Islands

CC	Cocos (Keeling) Islands

CO	Colombia

KM	Comoros

CG	Congo (Brazzaville)

CD	Congo (Kinshasa)

CK	Cook Islands

CR	Costa Rica

CI	Cote d’Ivoire

HR	Croatia

CU	Cuba

CY	Cyprus

CZ	Czech Republic

DK	Denmark

DJ	Djibouti

DM	Dominica

DO	Dominican Republic

TL	East Timor

EC	Ecuador

EG	Egypt

SV	El Salvador

GQ	Equatorial Guinea

ER	Eritrea

EE	Estonia

ET	Ethiopia

FK	Falkland Islands

FO	Faroe Islands

FJ	Fiji

FI	Finland

FR	France

GF	French Guiana

PF	French Polynesia

TF	French Southern and Antarctic Islands

GA	Gabon

GM	Gambia

DE	Germany

GE	Georgia

GG         Guernsey

GH	Ghana

GI	Gibraltar

GR	Greece

GL	Greenland

GD	Grenada

GP	Guadeloupe

GU	Guam

GT	Guatemala

GG	Guernsey

GN	Guinea

GW	Guinea-Bissau

GY	Guyana

HT	Haiti

HM	Heard and McDonald Islands

HN	Honduras

HK	Hong Kong

HU	Hungary

IS	Iceland

IM	Isle of Man

IN	India

ID	Indonesia

IR	Iran

IQ	Iraq

NT	Iraq-Saudi Arabia Neutral Zone

IE	Ireland

IM	Isle of Man

IL	Israel

IT	Italy

CI	Ivory Coast

JM	Jamaica

JP	Japan

JE	Jersey

JO	Jordan

KZ	Kazakhstan

KE	Kenya

KI	Kiribati

KR	Korea

KW	Kuwait

KG	Kyrgyzstan

LA	Laos

LV	Latvia

LB	Lebanon

LS	Lesotho

LR	Liberia

LY	Libya

LI	Liechtenstein

LT	Lithuania

LU	Luxembourg

MO	Macao

MK	Macedonia (Skopje)

MG	Madagascar (Malagasy)

MW	Malawi

MY	Malaysia

MV	Maldives

ML	Mali

MT	Malta and Gozo

MH	Marshall Islands
	MQ	Martinique

MR	Mauritania

MU	Mauritius

YT	Mayotte

MX	Mexico

FM	Micronesia

MD	Moldova

MC	Monaco

MN	Mongolia

ME	Montenegro

MS	Montserrat

MA	Morocco

MZ	Mozambique

MM	Myanmar

NA	Namibia

NR	Nauru

NP	Nepal

NL	Netherlands

AN	Netherlands Antilles

NC	New Caledonia

NZ	New Zealand

NI	Nicaragua

NE	Niger

NG	Nigeria

NU	Niue

NF	Norfolk Island

KP	North Korea

MP	Northern Mariana Islands

NO	Norway

OM	Oman

PK	Pakistan

PW	Palau

PS	Palestinian Territory

PA	Panama

PG	Papua New Guinea

PY	Paraguay

PE	Peru

PH	Philippines

PN	Pitcairn Island

PL	Poland

PT	Portugal

PR	Puerto Rico

QA	Qatar

ZA	Republic of South Africa

YE	Republic of Yemen

RE	Reunion (French)

RO	Romania

RU	Russia

RW	Rwanda

SH	St. Helena

KN	St. Kitts and Nevis

PM	St. Pierre and Miquelon

LC	St. Lucia

VC	St. Vincent and the Grenadines

WS	Samoa

SM	San Marino

ST	Sao Tomes and Principe

SA	Saudi Arabia

SN	Senegal

RS	Serbia

SC	Seychelles

SL	Sierra Leone

SG	Singapore

SK	Slovakia

SI	Slovenia

SB	Solomon Islands

SO	Somalia

GS	South Georgia and South Sandwich Islands

ES	Spain

LK	Sri Lanka

SD	Sudan

SR	Surinam

SJ	Svalbard and Jan Mayen Islands

SZ	Swaziland

SE	Sweden

CH	Switzerland

SY	Syria

TJ	Tajikistan

TZ	Tanzania

TH	Thailand

TG	Togo

TK	Tokelau Islands

TO	Tonga

TT	Trinidad and Tobago

TN	Tunisia

TR	Turkey

TM	Turkmenistan

TC	Turks and Caicos Islands

TV	Tuvulu

UG	Uganda

UA	Ukraine

AE	United Arab Emirates

GB	United Kingdom

US	United States

UM	United States Outlying Islands

UY	Uruguay

UZ	Uzbekistan

VU	Vanuatu

VA	Vatican City

VE	Venezuela

VN	Vietnam

VG	British Virgin Islands

VI	U.S. Virgin Islands

WF	Wallis and Futuna Islands

EH	Western Sahara

ZM	Zambia

ZW	Zimbabwe