TRACK ADVISORY

USER’S GUIDE

FOR DISPATCHERS

REVISED:  April 11, 2007

OAKLAND ARTCC TRAFFIC MANAGEMENT UNIT

ANCHORAGE ARTCC TRAFFIC MANAGEMENT UNIT

TABLE OF CONTENTS

Page

- Background				                              				   	2

- Summary Of User’s Guide Changes	                     				   	2

- Procedures For Track Advisory Tracks C, D, E, F, G and H			   	3

- Procedures For Track Advisory Tracks J and K				   	4

- Addresses for Input Messages							   	5

- Flight Request Messages (TKF)                              				   	6

- Cancel A Request (TKC)                                         				   	7

- Request a Gateway Reservation List (TKL)						7

- Alternate Uses of Request Messages                                                        		8

- Examples of Output Messages				           		   		9

- Slot Availability Message (SAM)                              				   	10

- Slot Availability Message Functionality		                                              10

- Example of Error Messages                                 				  	11

- Reservation Slot Message after 1900 UTC                                              		12

- Sample Aircraft Schedule before Modification         			  		13

- Sample Gateway Reservation List                          			  		14

- Procedures for Computer or Communication Link Failures at Oakland Center       15

- Quick Reference Sheet for Track Advisory for Oakland Center 	  		16

- Track Advisory Daily Procedures Chart for Oakland Center                    		17

- Anchorage Center Track Advisory Procedures                                         		18

- Anchorage Center Reservation Slot Message after 1900 UTC                               19

## Procedures for Computer or Communication Link Failures at Anchorage Center   20

- Quick Reference Sheet for Track Advisory for Anchorage Center    	  	21

- Track Advisory Daily Procedures Chart for Anchorage Center 			22

## BACKGROUND

Track Advisory (TA) is a computer based program, utilizing DOTS Plus, which is designed to assign route of flight, altitude and departure release times for aircraft utilizing either the Westbound Pacific Organized Tracks (PACOTS) which are in Oakland Center’s (ZOA) TA or the Russian Far East Tracks (RFE) route system which are in Anchorage Center’s (ZAN) TA.  Obtaining slots for the same flight in both TA programs is prohibited as it has the potential to create unnecessary delays, secondary altitudes and secondary track options for other participating flights.

## SUMMARY OF USER’S GUIDE CHANGES

The Track Advisory User’s Guide has been updated.  The majority of the changes were editorial other items were updated to reflect current procedures, they are as follows:

- Oakland Center eliminated references to the time change from Standard to Daylight Savings Time.

- Oakland Center updated the Traffic Management Unit FAX number.

- Oakland Center removed references to PACOTS Track I and L, as they are no longer subject to Track Advisory.

- Anchorage Center eliminated references to time change from Standard to Daylight Savings Time.

- Anchorage Center replaced Track letter identification for routes with Gateway Fix names.

- Anchorage Center replaced the fix “YUREE” with “VALDA”.

PROCEDURES FOR TRACK ADVISORY

FOR TRACKS C, D, E, F, G and H

ZOA publishes the Westbound PACOTS by 1100 UTC.  After receipt of the Track Definition Message (TDM) and between 1200 UTC and 1649 UTC, dispatchers may transmit their track request options (TKFs) to ZOA via ARINC or NADIN/AFTN. TKF messages must be submitted for flights crossing the first fix of a Westbound PACOTS track between 1900 UTC and 0100 UTC that depart from KLAX, KSFO, KSJC, KPDX, KSEA, CYVR and other West coast area airports.

At 1650 UTC, ZOA TA will compile the TKF messages into a Gateway Reservation List (GRL).  This list will allow a 10-minute departure window and 10 minutes separation between aircraft at the same altitude, on the same track, at the first fix of the track.

This GRL is sent via ARINC/NADIN/AFTN to the address of all dispatchers that submitted a TKF message.

After 1650 UTC changes can be made electronically by submitting a new TKF.  Any new TKF with the same flight call sign will replace the original TKF if the requested slot is available.  Changes can also be requested by telephone to the ZOA TA Position at 510-745-3771.  The program will use the options within the TKF messages to try and insert fights into the available slots in the GRL.  If a flight does not fit into the GRL, an electronic notification will be sent to the dispatcher and a new TKF message should be submitted.

DISPATCHERS SHOULD USE THE RELEASE TIMES, ALTITUDES AND TRACK ASSIGNMENTS FOR FLIGHT PLANNING PURPOSES.

Flights with an ETA at a Westbound PACOTS gateway fix prior to 1900 UTC or after 0100 UTC do not need a slot reservation and should not send TKF messages.  These flights will be released by the control tower.

PROCEDURES FOR TRACK ADVISORY

FOR TRACKS J and K

ZOA publishes PACOTS tracks J and/or K by 0000 UTC.  Dispatchers may submit TKF messages to ZOA TA via ARINC or NADIN/AFTN between 0200 UTC and 0359 UTC.  TKF messages must be submitted for flights departing KLAX or KSFO with an ETA at the first fix of track J or K between 0600 UTC and 0930 UTC.

At 0400 UTC, ZOA will compile the TKF messages into a GRL.  This list will allow a 10-minute departure window and 10 minutes separation between aircraft at the same altitude, on the same track, at the first fix of the track.  The GRL is sent via ARINC/NADIN/AFTN to the address of all dispatchers that submitted a TKF message. TKF messages submitted after 0400 UTC will be inserted into the remaining available slots based on the requested options.

After 0400 UTC changes can be made electronically by submitting a new TKF.  Any new TKF with the same flight call sign will replace the original TKF if the requested slot time is available.  Changes can also be requested by telephone to the ZOA TA Position at 510-745-3771.  The program will use the options within the TKF messages to try and insert fights into the available slots in the GRL.  If a flight does not fit into the GRL, an electronic notification will be sent to the dispatcher and a new TKF message should be submitted.

DISPATCHERS SHOULD USE THE RELEASE TIMES, ALTITUDES AND TRACK ASSIGNMENTS FOR FLIGHT PLANNING PURPOSES.

Flights with and ETA at the gateway fix prior to 0600 UTC or after 0930 UTC do not need a slot reservation and should not send TKF messages.  These flights will be released by the control tower.

## ADDRESSES FOR INPUT MESSAGES

Messages transmitted to the ZOA TA program via ARINC or NADIN/AFTN must use the following addresses:

# ARINC:	     		OAKDPXA

NADIN/AFTN:  	KZOAZOZD

NOTE: Do not add extra lines of information to the messages, except for more flights on succeeding lines.  Extra lines of information will cause an error message.

FLIGHT REQUEST MESSAGES (TKF)

As shown in the example below, a “TKF” is used on the first line when transmitting your message.  At any time if a new TKF message with the same call sign is received it will replace the previous TKF.  This means if a previously submitted TKF needs to be changed then submit a new TKF with the same call sign and the old TKF is replaced with the new one.  No cancellation message is needed.

Example:

TKF

ZZZ1234.1520.KSFO.RJAA.340.E.1555.15.340.F.1545.15.320.E.1540.25

.320.F.1540.25.300.E.1555.10.300.F.1545.10.340.G.1540.25.320.G.1540.25.REM.

Requirements and limitations of a TKF message:

- Each item is separated by a period “.”.

- Beginning a line with a period indicates that this line is a continuation of the current TKF message.

- A period at the end of a line is optional.

- Up to eight track options are allowed.

- Do not use any other special characters or spaces between options.

- An optional remarks line begins with “.REM.” (“period REM period”).

- The remarks line is limited to 63 characters.

- Spaces may only be used in the remarks section.

- Up to 20 flights may be specified in a single TKF message.

Breakdown of a TKF message:

ZZZ1234 -	Flight Identification - must match the filed flight plan call sign and must be 7 or less characters (any combination of letters or numbers – no symbols)

1520 -		Airport wheels up time – must be 4 numbers and only in UTC time.

# KSFO -		Departure Airport - must be the 4-letter ICAO identifier.

# RJAA -		Destination Airport - must be the 4-letter ICAO identifier.

340 -		1st choice Altitude

E		1st choice Track

1555           1st choice ETA for the gateway fix for this track

15		1st choice Acceptable Delay Time

320		2nd choice Altitude

F		2nd choice Track

1545           2nd choice ETA for the gateway fix for this track

15		2nd choice Acceptable Delay Time

.		.	.	.	.	.	.	.	.	.

.		.	.	.	.	.	.	.	.	.

.		.	.	.	.	.	.	.	.	.

.		.	.	.	.	.	.	.	.	.

320		8th choice Altitude

G		8th choice Track

1540           8th choice ETA for the gateway fix for this track

25		8th choice Acceptable Delay Time

If a slot for the first option cannot be found within the specified delay time, the program will evaluate the second option and succeeding options until a slot is found and assigned. Track options 2 through 8 are not required.  Submitting multiple options is recommended in order to increase chances of obtaining a slot during a congested time period.

If a slot is not found after the last available option is evaluated, the assumption will be that the user will submit another TKF or that they will file their flight plan clear of the Westbound PACOTS tracks.

NOTE:  Dispatchers are reminded that accurate ETEs to a track’s gateway fix affect the release time and altitude.  An inaccurate ETE may cause a flight to arrive at the gateway fix outside of the expected 10-minute window.  If this happens the radar controller may have to assign the flight a less favorable altitude if the flight is in conflict with another flight that is within its window at the affected altitude.

CANCEL A REQUEST (TKC)

Example:  (One line required)

# TKC.UAL1234

This will cause the removal of the flight from the current Track Advisory program.  The TKC call sign must match the original TKF call sign submitted earlier.

REQUEST A GATEWAY RESERVATION LIST (TKL)

Example:

# TKL

Optional:

# TKL.xxxxxxx

“xxxxxxx” is the address of your alternate printer.

- If the Gateway Reservation list is available, one will be transmitted to the address that initiated the request.

- If the Gateway Reservation list is not available, an error message will be transmitted to the address making the request.

ALTERNATE USES OF REQUEST MESSAGES

The TA program allows for consecutive TKF and TKC requests to be included into a single message.  Up to 20 requests can be made in a single message.

For example, a dispatcher may have already requested and received slots for two or more aircraft.  A decision by the dispatcher may be made to swap the slots of two aircraft due to maintenance problems.  The dispatcher would cancel the first flight; change the second flight's slot and the give the first flight the second flights slot.

Original requests:

TKF

AC7.2310.CYVR.RKSS.320.C.2336.30.340.D.2342.30

AC9.2330.CYVR.RKSS.320.C.2356.30.340.D.0002.30.300.C.2356.99

. REM. DISPATCH PHONE XXX-XXX-XXXX

AC3.2240.CYVR.RKSS.300.D2312.15.320.C.2306.99

. REM. B747-400.

Assume that the above requests were accepted for the first option with no delay.  The following message would swap the two flights within the GRL:

TKC.AC7

# TKF

AC9.2310.CYVR.RKSS.320.C.2336.30

.REM.SLOT SWAPPED WITH AC7, DISPATCH XXX-XXX-XXXX

AC7.2330.CYVR.RKSS.320.C.2356.30

.REM.LATE LEAVING FOR ADDITIONAL CARGO

The new remarks would replace the previous remarks as the above message replaces the original TKF message.  If the previous remarks still apply and are needed, include them in the new TKF message.   The computer reads the first line and then executes the instruction before reading the second line.  This sequence of completing each line’s instructions first allows this slot swapping to occur without losing the slot to another user.

EXAMPLES OF OUTPUT MESSAGES

The following output message is for a properly formatted TKF message received before the GRL was transmitted.

# THE FOLLOWING TRACK ADVISORY REQUEST WAS ACCEPTED OK

AC7.2310.CYVR.RKSS.320.C.2336.30.340.D.2347.30

The following output message is for a properly formatted TKF message received after the GRL was transmitted, but not inserted into the GRL because the options submitted were not available.  This message will require the dispatcher to change options and resubmit the request in order to obtain a slot or plan a flight that remains clear of the Westbound PACOTS tracks.

THE FOLLOWING TRACK ADVISORY REQUEST WAS ACCEPTED OK

AC7.2310.KLAX.RKSS.320.F.0002.30.340.G.2355.30

FLIGHT ENTRY WAS NOT INSERTED INTO LIST - CHANGE OPTIONS

The following output message is for a properly formatted TKF message received after the GRL was transmitted and successfully inserted into the listing:

THE FOLLOWING TRACK ADVISORY REQUEST WAS ACCEPTED OK

AC7.2310.KLAX.RKSS.320.F.0023.30.340.G.0010.30

TRACK=G  ALTITUDE=340  DEPARTURE TIME=2317  ALCOA TIME=0017

The above flight did not fit into the first track (F), which used the fix REDWD.  The gateway fix time supplied by the dispatcher for track G was then evaluated and a slot was found with in the allowed maximum delay time.  This flight will take a 7-minute delay and fly on track G at FL340.

SLOT AVAILABILITY MESSAGE

The slot availability message is generated and transmitted to a dispatcher when the assigned departure delay can be shortened or a slot that was previously unavailable has now become available.  The slot is not automatically reserved and the dispatcher must submit a TKF message to reserve the slot.  The slot is available to any dispatcher that can submit TKF request. The following is an example of a slot availability message.

The following slot is currently available for AC4:

Track = E, Alt = 300, Time at ALCOA 2130

This slot corresponds to option number 1 with 0 minutes delay of original TKF message.  You may reserve the slot by submitting a TKF message.

SLOT AVAILABILITY MESSAGE  (SAM) FUNCTIONALITY

The slot availability message function is active when the TA system is in the Negotiation Mode (1650 UTC to 0100 UTC).  Each time a slot reservation is cancelled or changed, a message is automatically sent to the next flight that was delayed or denied a preferred altitude advising them that an earlier departure time or the preferred altitude is currently available.  Only flights that show a delay within 20 minutes of the available gateway time slot are candidates.  The priorities listed below determine which flight the message will be given the SAM:

1.	Flights that are reserved on the same track and at the same altitude as the available slot but only with a time delay.  Flights within this group are prioritized by the order of the ETA at the gateway fix following the available time slot.

2.	Flights that are reserved on the same track but at an altitude that is a secondary requested altitude and the available slot altitude is the preferred option.  If more than one flight is in this category, priority is given to the flight that would get the greatest improvement in the reserved option.  For example, a flight that could switch from the fourth to the second option would have higher priority than a flight that could switch from the second to the first option.  The final tiebreaker is the improvement in delay time gained by using the newly opened slot.  For example, a flight that could reduce its delay from 20 to 10 minutes has a higher priority than a flight that could reduce its delay from 8 to 5 minutes.

3.	Flights not reserved on the same track as the available slot.  If more than one flight is in this category, the same tiebreakers used in item 2 above are used.

## EXAMPLE OF ERROR MESSAGES

The following are error type messages that are output when a request is first received with errors:

THE FOLLOWING TRACK ADVISORY REQUEST CONTAINS AN ERROR

AC4.2325.KLAX.RKSS.320.F.0007.30.330.G.0001.30

INVALID ALTITUDE FOR SECOND OPTION

VALID ALTITUDES ARE FL280,300,320,340

THE FOLLOWING TRACK ADVISORY REQUEST CONTAINS AN ERROR

AC3?.2310.KLAX.RKSS.320.F.0002.30.340.G.2355.30

NO SPECIAL CHARACTERS ALLOWED IN FLIGHT ID

THE FOLLOWING TRACK ADVISORY REQUEST CONTAINS AN ERROR

AC27.2200.KLAX.RKSS.320.F.2245.30.340.G.2237.30

DEPARTURE TIME IS 19 MINUTES FROM NOW

PLEASE PHONE 510-745-3771 FOR MANUAL UPDATE

THE FOLLOWING TRACK ADVISORY REQUEST CONTAINS AN ERROR

AC8.C310.KPDX.RKSS.320.C.0002.30.340.D.0012.30

TIMES MUST BE IN UTC HHMM FORMAT

THE FOLLOWING TRACK ADVISORY REQUEST CONTAINS AN ERROR

AC1.2100.KSEA.RJAA.340.C.2140.320.D.2140.15.340.D.2140.15

SECOND TRACK IS INVALID

(Note: The second track was valid, the request is missing the 1st option delay time.)

THE FOLLOWING TRACK ADVISORY REQUEST CONTAINS AN ERROR

AC2.2000.KLAX.RJAA.340.F.2130.10.320.F.2130.15.340.G.2120.15

UTC FIX TIME IS TOO FAR INTO FUTURE AFTER DEPARTURE TIME

THE FOLLOWING TRACK ADVISORY REQUEST CONTAINS AN ERROR

AC10.2115.KLAX.RCTP.340.F.2145.:10.320.F.2145.15.340.G.2135.15

NO SPECIAL CHARACTERS ALLOWED IN DELAY TIME

NOTE:  The previous error messages will have the following message attached to them:

SEE THE DISPATCHERS USERS GUIDE FOR SAMPLE FORMATS.

## RESERVATION SLOT MESSAGE AFTER 1900 UTC

After 1900 UTC the first flights in the GRL are beginning to depart and Track Advisory switches to a manual mode for slot changes requiring interaction with the ZOA TMC.  When a slot change request is received a window appears on the TMC’s workstation.  This request must be analyzed and then approved or modified.  There may be a short delay in response time if the TMC is coordinating with another dispatcher or with a control tower.  Once the request is acted upon it is sent back to the dispatcher.

Below is an example of a response message for an approved change:

REVISED RESERVATION FOR UAL1 DEPARTING KSFO HAS BEEN APPROVED

# TRACK=F  ALTITUDE=340  DEPARTURE TIME=2040    ALCOA TIME=2110

If the request is not approved and the slot is no longer available a message is returned to the dispatcher requiring a change in flight options.

SAMPLE AIRCRAFT SCHEDULE BEFORE MODIFICATION

The following list is a sample of flights submitted to the Track Advisory program before modification.  This list will not be available to the dispatchers.

OAKLAND ARTCC

TRAFFIC MANAGEMENT

AIRCRAFT SCHEDULE BEFORE MODIFICATION  05-17-2007

WHEEL                   1ST  1ST         2ND  2ND         3RD  3RD

UP              1ST 1ST FIX  MAX 2ND 2ND FIX  MAX 3RD 3RD FIX  MAX

FLIGHT TIME  DEPT DEST ALT TRK TIME DLY ALT TRK TIME DLY ALT TRK TIME DLY

****************************************************************************

FLIGHTS FOR TRACK F

AC15    1850 KSFO RJAA 320  F  1920 30  340  G  1916 30

AC25    1910 KSFO RJOO 320  F  1940 30  340  G  1936 30

AC24    1855 KLAX RJAA 320  F  1952 30  340  G  1948 30

AC27    1900 KLAX RJAA 320  F  1952 30  340  G  1948 30

AC16    1930 KSFO RJAA 320  F  2000 30  340  G  1956 30

AC28    1930 KSFO RJAA 320  F  2000 30  340  G  1956 30  340  F  2000 39

AC21    1945 KSFO RJAA 320  F  2015 30  340  G  2011 30

AC30    1945 KSFO VHHH 320  F  2015 30  340  G  2011 30

AC32    1950 KSFO ZSSS 320  F  2020 30  340  G  2016 30

AC18    1930 KLAX RKSS 320  F  2022 30  340  G  2018 30  340  F  2022 30

AC22    1950 KSJC RJAA 320  F  2025 45  340  G  2021 45

AC29    1950 KLAX RJAA 320  F  2042 30  340  G  2038 30

AC17    2000 KLAX RJAA 320  F  2052 60  340  G  2048 60

AC31    2005 KLAX RJAA 320  F  2057 30  340  G  2053 30

AC11    2015 KLAX RCTP 320  F  2107 40  340  G  2103 40

AC8     2040 KSFO VHHH 320  F  2110 30  340  G  2106 30  340  F  2110 25

AC6     2050 KSFO RJAA 320  F  2120 30  340  G  2116 30  340  F  2120 30

AC5     2055 KSFO RKSS 320  F  2125 50  340  G  2121 50

AC10    2035 KLAX RJAA 320  F  2127 35  340  G  2123 35  340  F  2127 25

AC9     2045 KLAX RJAA 320  F  2127 30  340  G  2123 30  320  G  2123 30

AC7     2100 KLAX RKSS 320  F  2152 30  340  G  2148 30  340  F  2152 25

AC4     2145 KLAX RJAA 320  F  2237 30  340  G  2233 30

AC1     2320 KLAX RKSS 320  F  0002 30  340  G  2358 30

AC20    1910 KLAX RJOO 340  F  2002 99

SAMPLE GATEWAY RESERVATION LIST

The following list is a sample of what dispatchers will receive via ARINC/AFTN/NADIN. This list will be transmitted in multiple parts.

Gateway Reservation List (compiled 05/17/07 16:50)

OAKLAND ARTCC

TRAFFIC MANAGEMENT

OCEANIC TRACK ADVISORY

*REQUESTED*             *RELEASED*

WHEEL CROSS             WHEEL CROSS

UP    FIX               UP    FIX   RELEASED

FLIGHT   TIME  TIME  DEPT  DEST  TIME  TIME  ALT TRK

*****************************************************

FLIGHTS FOR TRACK  E      CROSSING FIX REDWD

AC15     1850  1920  KSFO  RJAA  1850  1920  320  F

AC25     1910  1940  KSFO  RJOO  1910  1940  320  F

AC24     1855  1952  KLAX  RJAA  1903  2000  320  F

AC27     1900  1952  KLAX  RJAA  1908  2020  320  F

AC21     1945  2015  KSFO  RJAA  2010  2040  320  F

AC22     1950  2025  KSJC  RJAA  2025  2100  320  F

AC17     2000  2052  KLAX  RJAA  2028  2120  320  F

AC11     2015  2107  KLAX  RCTP  2048  2140  320  F

AC5      2055  2125  KSFO  RKSS  2130  2200  320  F

AC7      2100  2152  KLAX  RKSS  2128  2220  320  F

AC4      2145  2237  KLAX  RJAA  2148  2240  320  F

AC1      2320  0002  KLAX  RKSS  2320  0002  320  F

AC20     1910  2002  KLAX  RJOO  1910  2002  340  F

AC19     1920  2012  KLAX  RKSS  1930  2022  340  F

AC18     1930  2022  KLAX  RKSS  1950  2042  340  F

AC6      2050  2120  KSFO  RJAA  2050  2120  340  F

AC10     2035  2127  KLAX  RJAA  2048  2140  340  F

*****************************************************

FLIGHTS FOR TRACK  F      CROSSING FIX ALCOA

AC9      2045  2123  KLAX  RJAA  2045  2123  320  G

AC16     1930  1956  KSFO  RJAA  1930  1956  340  G

AC28     1930  1956  KSFO  RJAA  1950  2016  340  G

AC30     1945  2011  KSFO  VHHH  2010  2036  340  G

AC29     1950  2038  KLAX  RJAA  2008  2056  340  G

AC31     2005  2053  KLAX  RJAA  2028  2116  340  G

AC8      2040  2106  KSFO  VHHH  2110  2136  340  G

*****************************************************

THE FOLLOWING FLIGHTS WERE NOT INSERTED INTO THE LIST.

THE MAX ACCEPTABLE DELAY TIME WAS EXCEEDED.

ONLY THE 1ST TWO OF THE EIGHT OPTIONS ARE SHOWN

WHEEL                   1ST  1ST         2ND  2ND

UP              1ST 1ST FIX  MAX 2ND 2ND FIX  MAX

FLIGHT  TIME  DEPT DEST ALT TRK TIME DLY ALT TRK TIME DLY

**********************************************************

AC32    1950  KSFO ZSSS 320  E  2020 30  340  F  2015 30

ANALYSIS OF ABOVE ADVISORY

NUMBER OF FLIGHTS PUT INTO PROGRAM:        29

NUMBER OF FLIGHTS SCHEDULED ON-TIME:       12

NUMBER OF FLIGHTS SCHEDULED WITH DELAY:    17

MINIMUM DELAY:  3   MAXIMUM DELAY:  35

AVERAGE DELAY TIME:   22.9

PROCEDURES FOR COMPUTER OR COMMUNICATION

LINK FAILURES AT OAKLAND CENTER

In the event that the TA system fails, the following procedure will be used until normal service is restored.

Users will be notified to forward TKF requests via Fax (510-745-3339).  If a FAX is unavailable, call in your flight requests or use the alternate NADIN/AFTN address as listed on Quick Reference sheet. Please include your name and phone number with your flight request.  Flight request must be received between 1230 UTC AND 1645 UTC.

After 1650 UTC Oakland Center will compile a listing.  Dispatchers should not expect to receive the Gateway Reservation list until 1730 UTC.

Changes or additions after 1650 UTC must be made by phone (510-745-3771).

In this manual mode of TA, the TKL function to request additional or updated GRLs is not available.

QUICK REFERENCE SHEET FOR TRACK ADVISORY

## FOR OAKLAND CENTER

Normal ARINC address:                         				OAKDPXA

Normal NADIN/AFTN address:                    			KZOAZOZD

Alternate NADIN/AFTN address if line is down: 		KZOAZRZX

Oakland Center TRACK ADVISORY PHONE NUMBER:   	510-745-3771

Oakland Center TMU FAX PHONE NUMBER:          		510-745-3339

TIME     	PROCEDURE

# Z     	PACOTS tracks C, D, E, F, G and H are transmitted to the users.

# Z     	Users start sending TKFs

1650Z     	Oakland Center compiles and transmits the GRL

1900Z to 0100Z TA active for tracks C, D, E, F, G and H.

****************************************************************************

# 0000Z     	PACOTS tracks J and K are transmitted to the users.

# 0200Z     	Track Advisory will accept TKF messages for tracks J and/or K.

0400Z     	Oakland Center complies and transmits GRL.

0500Z		Controlled Departure Times (CDTs) are sent to the towers or

if track volume is low Track Advisory is canceled.

0600Z to 0930Z TA active for tracks J and K.

NOTE:    The ten-minute departure window for flights begins at the CDT.

DISPATCHERS SHOULD USE THE RELEASE TIMES, ALTITUDES AND TRACK ASSIGNMENTS FROM THE GATEWAY RESERVATION LIST FOR FLIGHT PLANNING PURPOSES.

DISPATCHER MESSAGES:

TKF    - Two or more line flight request.

TKC    - Cancel flight request.

TKL    - Request GRL.

TRACK ADVISORY DAILY PROCEDURES CHART

FOR OAKLAND CENTER

OAKLAND ARTCC TMU

#### PLANNING PHASE

# Flexible tracks

### TKF Requests

### GRL

#### NEGOTIATION PHASE

Change Request

New Reservation

Change Request

New Reservation

ANCHORAGE CENTER TRACK ADVISORY PROCEDURES

This section provides specific procedures for westbound flights planning to enter the Russian Far East (RFE) route system.

Dispatchers must transmit daily TKF options to Anchorage Center (ZAN) for all westbound flights planning to enter the RFE tracks according to the following table:

| Trackload Program | File TKF | Compile and Send GRL | Negotiation Period | Archive Time |
| --- | --- | --- | --- | --- |
| 1700Z-0700Z | 0900Z-1430Z | 1430Z | 1430Z-0000Z | 0000Z |
| 0700Z-1700Z | 0000Z-0430Z | 0430Z | 0430Z-0900Z | 0900Z |

1700 UTC – 0700 UTC: GRL is compiled and sent to users at 1430 UTC.

1430 UTC – 0000 UTC: The negotiation period.

0000 UTC – 0700 UTC: All TKF requests must be called in to ZAN - 907-269-1104.

0700 UTC – 1700 UTC: GRL is compiled and sent to users at 0430 UTC.

0430 UTC – 0900 UTC: The negotiation period.

0900 UTC – 1700 UTC:  All TKF requests must be called in to ZAN - 907-269-1104.

TKFs for RFE routes requiring a metric altitude, use the following designator:

| FL = Meters | Designator |
| --- | --- |
| FL280 = 8600 Meters | 86 |
| FL310 = 9600 Meters | 96 |
| FL350 = 10600 Meters | 106 |
| FL380/390 = 11600 Meters | 116 |

Required longitudinal separation and useable altitudes at the gateway fixes:

| Gateway Fix | In-trail Spacing | Useable Altitudes |
| --- | --- | --- |
| DEVID | 25 minutes | 310, 350, 390 |
| RAMEL | 20 minutes | 320, 340, 380 |
| ORVIT | 20 minutes | 320, 340, 380 |
| LISKI | 20 minutes | 96, 106, 116 |
| FRENK | 20 minutes | 86, 96, 106, 116 |
| VALDA | 20 minutes | 86, 96, 106, 116 |
| MARCC | 20 minutes | 96, 106 |

NOTE: Flights must arrive at the gateway fix at the GRL gateway time or no more than 10 minutes later to ensure being assigned the GRL altitude.

Example of ZAN TKF message format:

TKF

Callsign.2000.KSFO.RJAA.106.VALDA.0130.15.96.VALDA.0130.20.REM. DISPATCHER REMARKS GO HERE FOR THE FLIGHT

After the GRL is published, TKF messages will be processed automatically without TMC intervention during the negotiation period.

Transmit  messages to the ZAN TA program via ARINC or NADIN/AFTN using the following addresses:

ARINC:	ANCDPXA

# NADIN/AFTN:	PANCZOZD

## 1430 - 0000 UTC & 0430 - 0900 UTC: Slot availability message function is active.

REVISED RESERVATION FOR UAL1 DEPARTING KSFO HAS BEEN APPROVED

TRACK=VALDA  ALTITUDE=106  DEPARTURE TIME=2040    VALDA TIME=0211

## PROCEDURES FOR COMPUTER OR COMMUNICATION

## LINK FAILURES AT ANCHORAGE CENTER

In the event that the TA system fails, the following procedure will be used until the service is restored:

Users will be notified to forward flight request via alternate AFTN address as listed on the Quick Reference sheet, via FAX, or via phone. Please include your name and phone number with your flight request.

After 1430 UTC ZAN will compile a GRL.  Dispatchers should not expect to receive the GRL until 1530 UTC.

Any changes or additions after 1430 UTC must be made by phone (907-269-1104).

In this manual mode of TA, the TKL function to request additional or updated GRLs is not available.

NOTE: There will not be a GRL compiled for flights between 0700 and 1700 UTC.

QUICK REFERENCE SHEET FOR TRACK ADVISORY

## FOR ANCHORAGE CENTER

Normal ARINC address:        						ANCDPXA

Normal NADIN/AFTN address:              				PANCZOZD

Alternate NADIN/AFTN address if line is down: 		PAZAZQZX

Anchorage Center TRACK ADVISORY PHONE NUMBER:  	907-269-1104

Anchorage Center TMU FAX PHONE NUMBER:          	907-269-1343

DISPATCHERS SHOULD USE THE RELEASE TIMES, ALTITUDES AND ROUTINGS FROM THE GRL FOR FLIGHT PLANNING PURPOSES.

DISPATCHER MESSAGES:

TKF    - Two or more line flight request.

TKC    - Cancel flight request.

TKL    - Request a GRL.

TRACK ADVISORY DAILY PROCEDURES CHART

FOR ANCHORAGE CENTER

ANCHORAGE ARTCC TMU

PLANNING PHASE

Gateway Requests

# Gateway Reservation List

NEGOTIATION PHASE

### Change Request

New Reservation

### Change Request

New Reservation

# Text boxes

##### AIRLINE

DISPATCH

OFFICES

1100 and 0000Z

Flexible Tracks Published

1200-1649Z and 0200-0359Z

TA Accepts TKF messages

1650 and 0400Z

TA compiles and sends the GRL to airlines

1650-0100Z and 0400-0930Z

TA Updates GRL Automatically

1900-0100Z

TKF requests require TMC approval or change.

Response messages are returned to users.

0000-0430Z

TA Processor Accepts

Gateway Requests

0900-1430Z

TA Processor Accepts

Gateway Requests

0430Z TA Processor Builds Gateway Reservation List

1430Z TA Processor Builds Gateway Reservation List

0430-0900Z and

1430-0000Z

TA Processor Updates List Automatically

Automated requests are coordinated before approval.  Automated messages returned to users.

0000-0700Z and

0900-1700Z

Call Anchorage TMU at (907) 269-1104 for Gateway Reservation.

##### AIRLINE

DISPATCH

OFFICES