PPE Descriptions and Design Requirements Standards

BNL’s Definitions & Required Design Specifications for PPE are described for the following types of protection:

1. Body Protection

2. Eye Protection

3. Foot Protection

4. Hand Protection

5. Head Protection

Abbreviations used in this Exhibit:

ANSI:  	American National Standards Institute

ASTM:	ASTM International (formerly American Society for Testing and Materials)

ISEA:	International Safety Equipment Association

NFPA:	National Fire Protection Association

If you have any questions about the appropriate type of Personal Protection Equipment required for your work, contact your Supervisor or the Facility Support Representative, Safety & Health Representative, ESH Coordinator or the PPE Subject Matter Expert.

PPE Descriptions and Design Requirements Standards

- Body Protection

ANSI/ISEA 101: American National Standard for Limited-Use and Disposable Coveralls - Size and Labeling Requirements.

ANSI/ISEA 107: American National Standard for High Visibility Safety Apparel and Headwear.

ANSI/ISEA 207: American National Standard for High-Visibility Public Safety Vests.

NFPA 1992: Standard on Liquid Splash-Protective Ensembles and Clothing for Hazardous Materials Emergencies.

| Body Protective Equipment |
| --- |
| Equipment Title | Description | Illustration |
| Skin covering clothing | Consists of socks, long pants (or long dress or skirt to the ankles) and long sleeve shirt (or short sleeve shirt/dress and lab coat) Provides a minimum protection level for incidental exposure certain physical and chemical hazards. Design Requirements: none |  |
| Lab coat | Cotton or synthetic fiber long-sleeve coat, open at the collar, covering to knee length. Provides initial splash protection, minimal thermal protection, and some abrasion protection. Lab coats with red collars are reserved for work with radiological hazards. Design Requirements: none |  |
| Coveralls | Reusable or disposable one-piece suit. Provides initial splash protection and some thermal protection, and abrasion protection. Design Requirements: none |  |
| Encapsulating suit level B, C, D | Reusable or disposable one-piece suit with polymer coating for chemical permeation resistance. Provide splash and limited protection for sustained chemical contact, thermal sources, and abrasion. Design Requirements: ANSI/ISEA 101 |  |
| Total encapsulating suit level A | Reusable or disposable one-piece suit coated with polymer or constructed of polymer. Provides maximum degree of chemical permeation resistance. Provides some thermal protection and abrasion protection. Requires breathing-grade air be supplied into the suit. Design Requirements: NFPA 1992 |  |
| Laboratory apron | Apron provides protection from abrasion and splash to front of body. Used in conjunction with skin covering clothing. Design Requirements: none |  |
| Flame Resistant Clothing | Fire resistant clothing such as shirts, pants, coveralls, jackets, and parkas for protection from momentary electric arc and related thermal hazards. Layering of Flame resistant and natural fiber garments is used for added protection. A typical layering system may include an undershirt, a shirt and trouser and coverall. Loose fitting clothing provides additional thermal insulation due to air spaces. Design Requirements: NFPA 2112 |  |
| Electrical Flash Suit | Gloves, suit, hood, and face shield constructed to protect from Electrical Flash accidents hazards that create a large fireball, sending hot metal flying through the air. Design Requirements: See Electrical Safety Subject Area |  |
| Gauntlets/ sleeves | Gauntlets provide protection from abrasion to the forearms, for uses where the maximum potential for exposure occurs in that area. Typical uses are chain saws and knife cutting operations. Design Requirements: none |  |
| High-visibility clothing | High-visibility color and reflective material worn to alert vehicle drivers of the presence of workers on roadways and for other applications where high visibility of workers is needed. Design Requirements: ANSI/ISEA 107 or ANSI/ISEA 207 |  |

PPE Descriptions and Design Requirements Standards

2. Eye Protection

ANSI Z87.1: American National Standard for Occupational and Educational Eye and Face Protection

| Eye Protective Equipment |
| --- |
| Equipment Title | Description | Illustration |
| Non-safety eye glasses | Any glasses without impact resistance lenses and safety design features such as specialized lens mounting. Design Requirement: none |  |
| Impact-resistant safety glasses with side shields | Lenses insert into frame from the outside with a solid rim on the inner side of frame smaller than the lens. Design may include the lens and frame as one piece. The material of the lens meets impact resistant standards with built in or add-on clear side shield that guard against impact of flying objects entering from the side of the face. Design Requirement: ANSI Z87.1 |  |
| Prescription Lens safety glasses with side shields | Corrective lenses insert into frame from the outside with a solid rim on the inner side of frame smaller than the lens. Design may include the lens and frame as one piece. On impact with a flying object, the lens will not disengage toward eye. The material of the lens meets impact resistant standards with built in or add-on clear side shield that guard against impact of flying objects entering from the side of the face. Design Requirement: ANSI Z87.1 |  |
| Add-on side shields | Add-on clear side shield that guard against impact of flying objects entering from the side of the face. Design Requirement: ANSI Z87.1 |  |
| Visitor glasses | Impact Resistant Safety Glasses designed to fit over non-safety glasses or be worn without glasses underneath. Design Requirements: ANSI Z87.1 |  |
| Electrical Flash Eye Protection | Safety glasses and goggles with non-conductive frames (plastic) for work with electrical current. Design Requirements: ANSI Z87.1 with Non- conductive Frames |  |
| Vented goggles | Frame makes full contact with the face at all points. Vents in frame allow perspiration to exit goggles helping to reduce fogging. The material of the lens meets impact resistant standards. Design Requirement: ANSI Z87.1 |  |
| Non-vented goggles | Frame makes full contact with the face at all points. No vents in frame prevent entry of hazardous vapors, mists, fumes or aerosols. The material of the lens meets impact resistant standards. Design Requirement: ANSI Z87.1 |  |
| Face shield | High-impact resistant shield. Mounts on harness or hard hat. Provides protection from flying particles and liquid splashes. Design Requirement: ANSI Z87.1 |  |
| Full-face respirator | Face piece makes full contact with the face at all points. The lens meets impact resistant standards. Equivalent to face shield or sfaetry glasses with side siheids or non-vented goggles or vented goggles. Design Requirement: ANSI Z87.1 |  |
| Biohazard face masks | Thin polymer shield provides a minimal droplet barrier for biohazards and bloodborne pathogens splashes. Typically filtering efficiency is 95%. Design Requirement: none |  |
| Combo goggles and face shield (Monoshield) | High-impact resistant face shield attached to goggles as one-piece. Provides protection from flying particles and liquid splashes. Design Requirement: ANSI Z87.1 |  |
| Welding helmet | Impact resistant helment with tinted viewing window that provides protection of eyes and face from certain wavelengths of non-ionizing radiation and hot metal. Equivalent to glasses or face shield. Design Requirement: ANSI Z87.1 |  |
| Combo hard hat and face shield respirator | Impact resistant helmet, face shield, and PAPR loose-fitting respirator. Provides protection to head, respiratory, and face. Equivalent to safety glasses or face shield. Design Requirement: ANSI Z87.1 |  |
| Laser operations | See the Laser Safety Subject Area. |  |

PPE Descriptions and Design Requirements Standards

3. Foot Protection

ASTM 2413 Standard Specification for Performance Requirements for Foot Protection

ANSI Z41 standard (withdrawn). Footwear with this designation is acceptable for use.

ASTM F 1117: Standard Specification for Dielectric Footwear

| Equipment Title | Description | Illustration |
| --- | --- | --- |
| Enclosed footwear (substantial) | No impact resistance. Minimal protection from initial brief contact with chemicals and hot objects. Worn with socks. Design Requirement: none |  |  |
| Safety shoe (impact resistant, safety toe) | Structured steel cap capable of withstanding 2500 lbs. of compression. Designation of (I) for absorbing impact and (C) for compression. Typically leather or vinyl uppers, slip-resistant outsole. Falling object, impact protection, and brief chemical protection. Worn with socks. Design Requirement: ANSI Z41 or ASTM 2413 |  |
| Metatarsal protection | High degree of impact and falling object protection. Provides protection for front and bridge of foot. Worn with socks. Design Requirement: ANSI Z41 or ASTM 2413 |  |
| Chemical-resistant overboot | Offers protection for hazardous and non-hazardous materials. Seamless waterproof covers that provides a layer of chemical protection. To be worn over “enclosed footwear” or safety toe shoe. Worn with socks. Design Requirement: none |  |
| Chemical-resistant boots with safety toe | Neoprene or other polymer boots in a polymer resistant to the chemicals present. Worn with socks. Design Requirements: ANSI Z41 or ASTM 2413 |  |
| Dielectric boot | Dielectric overshoe for electrical insulation. Worn with socks. Design Requirements: See Electrical Safety Subject Area |  |
| Conductive sole shoe | Resistance typically under 10,000 ohms for conduction of electricity to prevent static electric discharge. Worn with socks. Design Requirement: ANSI Z41 or ASTM 2413 |  |
| Conductive shoe covers | Antistatic covers for footwear. Design Requirement: none |  |
| Shoe cover | Contaminant protection worn over “enclosed footwear” or safety toe shoe, as appropriate. Design Requirement: none |  |
| Disposable boot | Boot cover with elastic top, used for particulates such as asbestos, lead and radioactive dusts. Worn over “enclosed footwear” or safety toe shoe, as appropriate. Design Requirement: none |  |

PPE Descriptions and Design Requirements Standards

4. Hand Protection

| Hand Protective Equipment |
| --- |
| Equipment Title | Description | Illustration |
| Splash glove | Disposable, nitrile or natural rubber, ambidextrous gloves slightly resistant to a broad range of chemicals for brief periods. Design Requirement: none |  |
| Sustained contact and immersion glove | Typically embossed grip, flocked or fabric-lined glove. Usually 10- to 20-mil thick. Select material of construction to be impervious to the chemical based on glove selection charts. Design Requirement: none |  |
| Cryogen glove | Thick-insulating fabric provides protection against injury from both cryogenic and hot materials from -160° to 150°C (-260° to 300°F). Not for immersion in liquid cryogens. Design Requirement: none |  |
| Thermal burn- protection glove | Woven fiber gloves for very low to very high temperatures (-70° to 600°C). Aluminized gloves may be present for extra heat reflectivity and molten-splash resistance. Can be used for cryogen liquid handling. Design Requirement: none |  |
| Abrasion resistance (a.k.a. work glove) | Heavy glove resistant to abrasion, typically a split leather palm or fabric with coating. Design Requirements: none |  |
| Cut-resistant glove | Heavyweight cut-resistant fiber (such as Kevlar) knitted gloves. Design Requirement: none |  |
| Electrical Insulating & flash hand protection gloves | Electrically non-conductive glove to prevent electrical shock hazard. Flame resistant to limit arc flash burns. Leather protectors worn over these rubber gloves for mechanical abrasion protection. Design Requirements: See Electrical Safety Subject Area |  |

PPE Descriptions and Design Requirements Standards

5. Head Protection

ANSI Z89.1: American National Standard Requirements for Protective Headwear for Industrial Workers

| Head Protective Equipment |
| --- |
| Equipment Title | Description | Illustration |
| Bump cap | Bump cap is lightweight and features a suspension. Popular where the possibility of a head bump or laceration is possible. Ideal for those working in areas with low head clearance. Four-point easily adjustable plastic suspension with perforated vinyl sweatband. Design Requirement: none |  |
| Hard hat | A safety cap adjusts from head with 4- to 6-point web suspension system. Designs include those that permit Hearing, welding, and face shield accessories to be attached to the helmet. Design Requirement: ANSI Z89.1 |  |
| Helmet respirator | Combination of PAPR respirator built into a safety cap adjusts from head with 4- to 6-point suspension system. Design Requirement: ANSI Z89.1 |  |