ARM AOS Measurements at SGP Central Facility during ARM ACP Aerosol IOP, May 2003

Revision History

2-19-03 Pat Sheridan

2-20-03 Rev Steve Schwartz

2-21-03 Y-N Lee Revs incorp

2-26-03 Schwartz Beginning to populate new rows: Quantities, Technique,Time resolution, References; Cowin particle collector withdrawn; resource requirements specified for AMS; reqmts specified for EC-OC

2-27-03 Sheridan – Adding ARM AOS and ARM IOP surface measurements

2-28-03 Schwartz reorganized order of tables

2-28-03 Sheridan: Added CMDL nephelometer to GIF measurements

03-06-03 small changes and edits by Ferrare, added Table from Ji for NASA GSFC SMART Measurements

ARM AOS Measurements at SGP Central Facility during ARM ACP Aerosol IOP, May 2003
(page 1 of 2)

| Instrument | Integrating Nephelometer | Humidified Integrating Nephelometer | Continuous Filter-based Light Absorption Photometer | Condensation Particle Counter | Optical Particle Counter |
| --- | --- | --- | --- | --- | --- |
|  | TSI Model 3563 Integrating Nephelometer (AOS) | TSI Model 3563 Integrating Nephelometer (AOS) | Radiance Research Model PSAP (AOS) | TSI Model 3010 Condensation Particle Counter (AOS) | Particle Measuring Systems Model PCASP-X optical particle counter (AOS) |
| Operator | John Ogren | John Ogren | John Ogren | John Ogren | John Ogren |
| Contact | John.a.ogren@noaa.gov | John.a.ogren@noaa.gov | John.a.ogren@noaa.gov | John.a.ogren@noaa.gov | John.a.ogren@noaa.gov |
| Quantities to be measured | Total and backwards hemispheric aerosol light scattering coefficient at 450, 550, 700 nm | Total and backwards hemispheric aerosol light scattering coefficient at 450, 550, 700 nm as a function of RH | Aerosol light absorption coefficient (565 nm) | Total particle concentration, 0.01 m < Dp < 3 m | Aerosol size distributions, 31 bins, 0.10 m < Dp < 10 m |
| Measurement Technique or Principle | Integrating nephelometry | Integrating nephelometry | Light attenuation through aerosol deposit on filter | Condensational particle growth and detection w/ laser optics | Particle counting and sizing |
| Time resolution | 1 minute | 1 minute | 1 minute | 1 minute | 1 minute |
| Reference(s) | Sheridan et al., J. Geophys. Res., Vol. 106, 20735-20747, 2001 | Sheridan et al., J. Geophys. Res., Vol. 106, 20735-20747, 2001 | Sheridan et al., J. Geophys. Res., Vol. 106, 20735-20747, 2001 | Sheridan et al., J. Geophys. Res., Vol. 106, 20735-20747, 2001 | Sheridan et al., J. Geophys. Res., Vol. 106, 20735-20747, 2001 |
| Flow rate | 30 slpm | 30 slpm | 0.75 slpm | 1 lpm | 2 cc/sec |
| Pump1 | A | A | A | A | A |
| Sample line1 | A | A | A | A | A |
| duration | Continuous | Continuous | Continuous | Continuous | Continuous |
| Flow control1 | A | A | A | A | A |
| Size µm | Dp < 1 m and Dp < 10 m alternating size cuts | Dp < 1 m and Dp < 10 m alternating size cuts | Dp < 1 m and Dp < 10 m alternating size cuts | 0.01 – 3 m | 0.10-10 m |
| Filter1 | N | N | N | N | N |
| Power1 | A | A | A | A | A |
| Data1 | A | A | A | A | A |
| dimension | In AOS | In AOS | In AOS | In AOS | In AOS |
| Space feet | In AOS | In AOS | In AOS | In AOS | In AOS |
| Desk1 | N | N | N | N | N |
| Internet1 | N | N | N | N | N |
| Additional Requirements | None | None | None | None | None |

1S=self; A=ARM supply; N=no

ARM AOS Measurements at SGP Central Facility during ARM ACP Aerosol IOP, May 2003
(page 2 of 2)

| Instrument | Ozone Monitor | Aerosol Filters |
| --- | --- | --- |
|  | Dasibi Continuous Ozone Monitor Model 1008-RS (AOS) | NOAA/PMEL aerosol filters (permanent addition to AOS) |
| Operator | John Ogren | Trish Quinn |
| Contact | John.a.ogren@noaa.gov | Patricia.K.Quinn@noaa.gov |
| Quantities to be measured | Ozone mixing ratio | Aerosol ionic chemistry |
| Measurement Technique or Principle | UV absorption | Ion chromatography |
| Time resolution | 1 minute | 24 hours |
| Reference(s) | Sheridan et al., J. Geophys. Res., Vol. 106, 20735-20747, 2001 |  |
| Flow rate | 2 lpm | 30 lpm |
| Pump1 | A | A |
| Sample line1 | A | A |
| duration | Continuous | Continuous |
| Flow control1 | A | A |
| Size µm | None | Dp < 1 m |
| Filter1 | N | S, changed once a week |
| Power1 | A | A |
| Data1 | A | A |
| dimension | In AOS | In AOS |
| Space feet | In AOS | In AOS |
| Desk1 | N | N |
| Internet1 | N | N |
| Additional Requirements | None | None |

1S=self; A=ARM supply; N=no

ARM IOP Measurements at SGP Central Facility during ARM ACP Aerosol IOP, May 2003
(page 1 of 3)

| Instrument | 3- Light Absorption | Integrating Nephelometer | Integrating Nephelometer | Integrating Nephelometer |
| --- | --- | --- | --- | --- |
|  | Univ. of Washington modified PSAP (Aerosol Trailer) | DRI integrating sphere nephelometer (GIF Trailer) | Radiance Research Model M-903 integrating nephelometer (GIF Trailer) | TSI Model 3563 Integrating Nephelometer |
| Operator | Dave Covert | Pat Arnott | Pat Arnott | John Ogren |
| Contact | dcovert@u.washington.edu | pat@dri.edu | pat@dri.edu | John.a.ogren@noaa.gov |
| Quantities to be measured | Aerosol light absorption coefficient at 3 visible wavelengths (466, 530, 660 nm) | Aerosol light scattering coefficient at 532 nm | Aerosol light scattering coefficient at 530 nm | Total and backwards hemispheric aerosol light scattering coefficient at 450, 550, 700 nm |
| Measurement Technique or Principle | Light attenuation through aerosol deposit on filter | Integrating nephelometry | Integrating nephelometry | Integrating nephelometry |
| Time resolution | 1 minute | 1 minute | 1 minute | 1 minute |
| Reference(s) |  |  |  | Anderson and Ogren, Aerosol Sci. Technol., Vol. 29, 57-69, 1998. |
| Flow rate | 2 lpm | 10 lpm | 3 lpm | 30 slpm |
| Pump1 | A | S | S | S |
| Sample line1 | A | S | S | S |
| duration | Continuous | Continuous | Continuous | Continuous |
| Flow control1 | A | S | S | S |
| Size µm |  |  |  | Dp < 1 m and Dp < 10 m alternating size cuts |
| Filter1 | S, changed daily | N | N | N |
| Power1 | A |  |  | <100W @ 120 VAC |
| Data1 | A |  |  | S |
| dimension | In AOS |  | 12”x12”x24” | 12”x12”x46” |
| Space feet | In AOS |  |  | 12”x12”x46” |
| Desk1 | N |  |  | N |
| Internet1 | N |  |  | N |
| Additional Requirements | None |  |  | None; In GIF |

1S=self; A=ARM supply; N=no

ARM IOP Measurements at SGP Central Facility during ARM ACP Aerosol IOP, May 2003
(page 2 of 3)

| Instrument | Photoacoustic Light Absorption | 7- Aethalometer | Cavity Ringdown Extinction | TEOM | Dusttrak |
| --- | --- | --- | --- | --- | --- |
|  | DRI photoacoustic instrument (GIF) | Model XXXX Aethalometer (GIF) | DRI cavity ring-down instrument (GIF) | Tapered Element Oscillating Microbalance (GIF) | (GIF) |
| Operator | Pat Arnott | Pat Arnott | Pat Arnott | Pat Arnott | Pat Arnott |
| Contact | pat@dri.edu | pat@dri.edu | pat@dri.edu | pat@dri.edu | pat@dri.edu |
| Quantities to be measured | Aerosol light absorption coefficient at 532 nm | Aerosol light absorption coefficient at 7 wavelengths | Aerosol light extinction coefficient at 532 nm | Total aerosol mass concentration |  |
| Measurement Technique or Principle | Photoacoustic light absorption | Light attenuation through aerosol deposit on filter | Extinction of light through ring-down cell | Based on oscillation frequency dependence on aerosol mass loading |  |
| Time resolution | 1 minute | 2 minutes | 1 minute |  |  |
| Reference(s) |  |  |  |  |  |
| Flow rate | 1 lpm | 1 lpm | 10 lpm | 3 lpm |  |
| Pump1 | S | S | S | S |  |
| Sample line1 | S | S | S | S |  |
| duration | Continuous | Continuous | Continuous | Continuous |  |
| Flow control1 | S | S | S | S |  |
| Size µm |  |  |  |  |  |
| Filter1 | N | N | N | N |  |
| Power1 |  |  |  |  |  |
| Data1 | S | S | S | S |  |
| dimension |  |  |  |  |  |
| Space feet | 3’ x 3’ floor space | Can sit in rack or on desk | 3’ x 5’ floor space | Can sit in rack or on desk |  |
| Desk1 | A | N | N | N |  |
| Internet1 | A | N | N | N |  |
| Additional Requirements |  |  |  |  |  |

1S=self; A=ARM supply; N=no

ARM IOP Measurements at SGP Central Facility during ARM ACP Aerosol IOP, May 2003
(page 3 of 3)

| Instrument | CCN Measurement | CCN Measurement | Size segregated composition |  |
| --- | --- | --- | --- | --- |
|  | DRI CCN spectrometer (GIF Trailer) | CalTech CCN instrument (GIF Trailer) | DELTA Drum sampler, eight size cuts (GIF) |  |
| Operator | Jim Hudson | Tracey Rissman | Tom Cahill |  |
| Contact | hudson@dri.edu | rissman@its.caltech.edu | tacahill@ucdavis.edu |  |
| Quantities to be measured |  | CCN concentration at a still-to-be-determined supersaturation |  |  |
| Measurement Technique or Principle |  | N/A |  |  |
| Time resolution |  | ~ 1 Hz |  |  |
| Reference(s) |  | N/A |  |  |
| Flow rate | 12 lpm | 0.8-0.9 lpm | ~ 17 lpm |  |
| Pump1 | S | S | S |  |
| Sample line1 | S | S | S |  |
| duration | Continuous | Continuous |  |  |
| Flow control1 | S | S | S |  |
| Size µm | Dp < 2 m | N/A |  |  |
| Filter1 | N | S |  |  |
| Power1 | 40A (max) @ 120VAC | 5A @ 120VAC, 2 outlets |  |  |
| Data1 | S | S | S |  |
| dimension | 3 racks of 24”x24”x40” plus a couple of pumps | 15” vertical rack space, plus column that hangs on side of rack |  |  |
| Space feet | 8’ x 8’ | 6’ x 8’ | 2’ x 2’ |  |
| Desk1 | A | A | N |  |
| Internet1 | A | A | N |  |
| Additional Requirements |  | Room for a rack-mounted calibration system to be wheeled in occasionally |  |  |

1S=self; A=ARM supply; N=no

ACP IOP Measurements at SGP Central Facility during ARM ACP Aerosol IOP, May 2003
(page 1 of 3)

| Instrument | AMS | SPLAT-MS | DMA | TDMA |
| --- | --- | --- | --- | --- |
|  | Aerodyne Aerosol Mass Spectrometer | Single Particle Laser Ablation Time-of-flight Mass Spectrometer (GIF) | Differential Mobility Analyzer (GIF) | Tandem Differential Mobility Analyzer (GIF) |
| Operator | Dan Imre | Alla Imre | Jian Wang | Jian Wang |
| Contact | imre@bnl.gov | alla@bnl.gov | jian@bnl.gov | jian@bnl.gov |
| Quantities to be measured |  |  |  |  |
| Measurement Technique or Principle |  |  |  |  |
| Time resolution |  |  |  |  |
| Reference(s) |  |  |  |  |
| Flow rate | 2 cc/sec | 3 cc/s | 7 l/m | 22 l/m |
| Pump1 | s | S | A2 |  |
| Sample line | A | A | A | A |
| duration | Continuous | Continuous | Cont | Cont |
| Flow control | S | S | S | S |
| Size µm | .03 - 3 | 0.05-3 | 0.0035-1 | 0.0035-1 |
| filter | N | N | N | N |
| power | 600w 120 or 240 | 120V, ~80A 8 outlets | 5A 120v 3out | 7A 120v 6out |
| data | S | S |  |  |
| dimension | 45" X 43" X 24" | 300 lb 10" x 4" | 19 x 23 | 40 x 23 |
| Space feet | 6 X 8 | 10' X 20'3 | 6 X 83 |  |
| desk | Y | Y | Y |  |
| internet | Y | Y | Y |  |
| Additional Requirements |  |  |  |  |

1S=self; A=ARM supply; N=no

2 Please provide: 6 LPM critical flow vacuum source

3 Please make sure that spaces assigned for Wang and Imre are contiguous.

ACP IOP Measurements at SGP Central Facility during ARM ACP Aerosol IOP, May 2003
(page 2 of 3)

| Instrument | PILS-IC | PILS-TOC | filter | TEOM |
| --- | --- | --- | --- | --- |
|  | Particle into Liquid Sampler: Ion Chromatograph (GIF) | Particle into Liquid Sampler: Total Organic Carbon (GIF) | Quartz filter to collect 12-hr integrated sample (GIF) | Tapered Element Oscillating Microbalance (GIF) |
| Operator | Yin Nan Lee | Yin Nan Lee | Yin Nan Lee | Yin Nan Lee |
| Contact | ynlee@bnl.gov | ynlee@bnl.gov | ynlee@bnl.gov | ynlee@bnl.gov |
| Quantities to be measured | major cations and anions | total organic carbon | major cations and anions | total aerosol mass concentration |
| Measurement Technique or Principle | sampling using PILS followed by on-line IC analysis | sampling using PILS followed by on-line TOC analysis | filter collection followed by batch IC analysis | based on oscillation frequency dependence on aerosol mass loading |
| Time resolution | 8 min | 4 min | 12 hr | 30 min |
| Reference(s) | A particle-into-liquid collector for rapid measurement of aerosol bulk chemical composition. Weber et al. Aerosol Sci. Technol, 35, 718-727, 2001. | http://www.ionics.com/products/division/Instruments/sievers_instruments.htm#1 | The BNL filter pack system for collection and determination of air pollutants, Leahy et al, BNL report -61730, 1995. | http://www.rpco.com/products/ambprod/amb1400/index.htm |
| Flow rate | 5 l/min | 5 l/min | 5 l/min | 3 l/m |
| Pump1 | A | A | A | A |
| Sample line | A | A | A | A |
| duration | 7am-7pm | 7am-7pm | 7am-7pm | 7am-7pm |
| Flow control | S | S | S | S |
| Size µm | PM2.5 or PM1.0 | PM2.5 or PM1.0 | PM2.5 or PM1.0 | PM2.5 or PM1.0 |
| filter | N | N | S | N |
| power | 3A 120v 2out | 3A 120v 2out | 1A 120v 2out | 1A 120v 2out |
| data | S | S | S |  |
| dimension | 23" w x 18" d | 23" w x 18" d | 18" w x 12" | 18" w x 12" |
| Space feet | 6' X 8' |  |  |  |
| desk | Y |  |  |  |
| internet | N |  |  |  |

1S=self; A=ARM supply; N=no

ACP IOP Measurements at SGP Central Facility during ARM ACP Aerosol IOP, May 2003
(page 3 of3)

| Instrument | EC-OC6 | SP-2 | WITHDRAWN Particle collector5 |  |
| --- | --- | --- | --- | --- |
|  | Elemental and Organic Carbon (aerosol trailer) | (GIF) |  |  |
| Operator | Tom Kirchstetter | Darrel Baumgardner4 | Dan Imre/ Jim Cowin |  |
| Contact | TWKirchstetter@lbl.gov | darrel@servidor.unam.mx | imre@bnl.gov |  |
| Quantities to be measured | TC/OC/BC and 330-900 nm light-transmission |  |  |  |
| Measurement Technique or Principle | thermal analysis and light spectrometer |  |  |  |
| Time resolution | 6 hour |  |  |  |
| Reference(s) |  |  |  |  |
| Flow rate | 30 std L per min | 100 cc/s |  |  |
| Pump1 |  | S |  |  |
| Sample line |  | A |  |  |
| duration |  | Continuous |  |  |
| Flow control | mass flow controller | S |  |  |
| Size µm |  | 0.1-10 |  |  |
| filter |  | N |  |  |
| power | ARM (backup pump is 12A, 120V) | 5A 120V 4 outlets |  |  |
| data |  | S |  |  |
| dimension |  | 66 lb 30" x 30" |  |  |
| Space feet |  | 6' X 8' |  |  |
| desk | need small workspace to change filters | Y |  |  |
| internet | No | N |  |  |
|  | No PVC. Data logger to record flows, technician to log filter changes |  |  |  |
|  | This experiment will be housed in the Aerosol Trailer |  |  |  |

1S=self; A=ARM supply; N=no

4 Not ACP; tentative.

Other ARM Measurements at SGP Central Facility during ARM ACP Aerosol IOP, May 2003

(page 1 of 2)

| Instrument | SMART trailer (Surface Measurements for Atmospheric Radiative Transfer) | S3 photometer | Shadowband radiometer | Broadband radiometers | Micopulse lidar |
| --- | --- | --- | --- | --- | --- |
|  | NASA GSFC | NASA GSFC | Yankee Environmental Systems, Inc. | Eppley, Yankee, Kipp&Zonen, NILU-UV | NASA GSFC |
| Operator | SMART team | Jack Ji | Jack Ji | Jack Ji | Jack Ji |
| Contact | Jack Ji , ji@climate.gsfc.nasa.gov | ji@climate.gsfc.nasa.gov | ji@climate.gsfc.nasa.gov | ji@climate.gsfc.nasa.gov | ji@climate.gsfc.nasa.gov |
| Quantities to be measured | Solar, terrestrial radiation | Solar radiance at 340, 380, 440, 500, 615, 675, 870, 870p1, 870p2, 936, 1030, 1240, 1640, 2130 nm | Solar irradiance at 414, 498, 614, 672, 866, 939, and 300~1000 nm (Global, Diffuse, and Direct radiance) | Solar irradiance at, 0.3~3, 0.4~3, 0.7~3 um (Global and Diffuse); 0.3~3 um (Direct); 4~50 um, also 302, 308, 315, 336, 377, 400~700 nm (Global) | Normalized Relative Backscatter |
| Measurement Technique or Principle | Remote sensing |  |  | Eppley PSP, PIR, NIP; Kipp and Zonen CM21, CG4, CH1 |  |
| Time resolution | Up to 1 min | 15 min | 1 min | 1 min | 1 min |
| Reference(s) | http://smart-commit.gsfc.nasa.gov |  | http://www.yesinc.com/products/data/mfr7/index.html | http://www.eppleylab.com http://www.kippzonen.com/product/index.html http://alomar.rocketrange.no/nilu-uv.html | http://virl.gsfc.nasa.gov |
| Flow rate | No |  |  |  |  |
| Pump1 | N |  |  |  |  |
| Sample line1 | N |  |  |  |  |
| Duration | Continuous |  |  |  |  |
| Flow control1 | N |  |  |  |  |
| Size µm | N |  |  |  |  |
| Filter1 | N |  |  |  |  |
| Power1 | A, 100A@220V |  |  |  |  |
| Data1 | S |  |  |  |  |
| Dimension | 20x17x9 ft |  |  |  |  |
| Space feet | 25x9 ft |  |  |  |  |
| Desk1 | N |  |  |  |  |
| Internet1 | A |  |  |  |  |
| Additional Requirements | Whole sky view |  |  |  |  |

1S=self; A=ARM supply; N=no

Other ARM Measurements at SGP Central Facility during ARM ACP Aerosol IOP, May 2003

(page 2 of 2)

| Instrument | Sky imager | Spectro-radiometer | Interferometer | Scanning microwave radiometer | Rain gage |
| --- | --- | --- | --- | --- | --- |
|  | Yankee Environmental Systems, Inc. | Analytical Spectral Devices, Inc. | ABB Bomem | NASA GSFC | Optical Scientific Inc. |
| Operator | Jack Ji | Jack Ji | Jack Ji | Jack Ji | Jack Ji |
| Contact | ji@climate.gsfc.nasa.gov | ji@climate.gsfc.nasa.gov | ji@climate.gsfc.nasa.gov | ji@climate.gsfc.nasa.gov | ji@climate.gsfc.nasa.gov |
| Quantities to be measured | Sky image | Solar spectral irradiance 0.4~2.5 um, Sampling Interval 2nm | AERI, Sky spectral radiance 500~3000 cm-1, 1 cm-1 resolution | Sky radiance at 23, 23.8, and 36 GHz | Rain rate, measures from .1 to 500 mm/hr |
| Measurement Technique or Principle |  |  |  |  |  |
| Time resolution | 1 min | 1 min | 5 min | 5 min | 5 min |
| Reference(s) | http://www.yesinc.com/products/data/tsi440/index.html | http://www.asdi.com/asdi_t2_pr_sp_fsp.html | http://www.abb.com/global/abbzh/abbzh251.nsf!OpenDatabase&db=/global/seapr/seapr035.nsf&v=6312A&e=us&m=9F2&c=C1E6CB3C346573A385256C61005B3D44 |  | http://www.opticalscientific.com/Org.htm |
| Flow rate |  |  |  |  |  |
| Pump1 |  |  |  |  |  |
| Sample line1 |  |  |  |  |  |
| Duration |  |  |  |  |  |
| Flow control1 |  |  |  |  |  |
| Size µm |  |  |  |  |  |
| Filter1 |  |  |  |  |  |
| Power1 |  |  |  |  |  |
| Data1 |  |  |  |  |  |
| Dimension |  |  |  |  |  |
| Space feet |  |  |  |  |  |
| Desk1 |  |  |  |  |  |
| Internet1 |  |  |  |  |  |
| Additional Requirements |  |  |  |  |  |

1S=self; A=ARM supply; N=no