NOAA NESDIS

CENTER for SATELLITE APPLICATIONS and RESEARCH

The IASI Product Processing System

Interface Control Document

Version 2.0

Title: IASI Product processing system interface CONTROL DOCUMENT VERSION 2.0

AUTHORS:

Larisa Koval (PSGS)

Tom King (PSGS)

APPROVAL SIGNATURES:

_________________________________________March 19, 2008

Walter Wolf (STAR)		                                           Date

Project Development Lead

____________________________________________March 19, 2008___

Hank Drahos (STAR)	                                           Date

Operational Products Development Branch Chief

IASI Product processing system

INTERFACE CONTROL DOCUMENT

Version History SUMMARY

| Version | Description | Revised Sections | Date |
| --- | --- | --- | --- |
| 1.0 | Created by Larisa Koval and Tom King of PSGS | New Document | 08/23/07 |
| 1.1 | Revised after SRR | Sections 2, 4, 5 | 9/21/07 |
| 2.0 | Revised by Larisa Koval to include Level 2 products | All sections | 3/19/2008 |

TABLE OF CONTENTS

Page

LIST OF TABLES	16

LIST OF ACRONYMS	18

1. Introduction	20

2. Input Data Sets	30

2.1. IASI L1C Granule Files	30

2.1.1. Purpose	30

2.1.2. Data File Description	31

2.1.3. Access	33

2.2. GFS Forecast Files	34

2.2.1. Purpose	34

2.2.2. Data File Description	34

2.2.3. Access	35

2.3. GDAS Forecast Files	36

2.3.1. Purpose	36

2.3.2. Data File Description	36

2.3.3. Access	37

2.4. CDL Template Files	38

2.4.1. Purpose	38

2.4.2. Data File Description	38

2.4.3. Access	40

2.5. IASI L1C Granule Metadata Template File	41

2.5.1. Purpose	41

2.5.2. Data File Description	41

2.5.3. Access	43

2.6. Global Grid Metadata Template File	43

2.6.1. Purpose	43

2.6.2. Data File Description	43

2.6.3. Access	44

2.7	L2 Metadata Template	44

2.7.1	Purpose	44

2.7.2	Data File Description	44

2.7.3	Access	45

2.8	IASI CCR Metadata Template	45

2.8.1	Purpose	45

2.8.2	Data File Description	45

2.8.3	Access	46

2.9. Matchup Template File	46

2.9.1	Purpose	46

2.9.2	Data File Description	46

2.9.3	Access	47

2.10. EUMETSAT Level 2 BUFR Files	47

2.10.1	Purpose	47

2.10.2	Data File Description	47

2.10.3	Access	48

2.11. Eigenvector Files	48

2.11.1	Purpose	48

2.11.2	Data File Description	49

2.11.3	Access	49

2.12	Local Angle correction File	49

2.12.1	Purpose	49

2.12.2	Data File Description	50

2.12.3	Access	50

2.13	Retrieval System Files	50

2.13.1	Purpose	51

2.13.2	Data File Description	51

2.13.3	Access	53

2.14	AMSU-A Orbital files	54

2.14.1	Purpose	54

2.14.2	Data File Description	54

2.14.3	Access	55

2.15	MHS Orbital files	55

2.15.1	Purpose	55

2.15.2	Data File Description	56

2.15.3	Access	57

3. Intermediate Data Sets	58

3.1. IASI L1C Full Resolution Subset Files	59

3.1.1	Purpose	59

3.1.2	Data File Description	60

3.1.3	Access	67

3.2. IASI L1CT Thinned Subset Files	68

3.2.1	Purpose	68

3.2.2	Data File Description	69

3.2.3	Access	69

3.3. IASI Daily Full Global File	70

3.3.1	Purpose	70

3.3.2	Data File Description	70

3.3.3	Access	84

3.4. Daily Full Global Location Files	85

3.4.1	Purpose	85

3.4.2	Data File Description	85

3.4.3	Access	85

3.5	AMSU-A Level 1B NetCDF Granule Files	86

3.5.1	Purpose	86

3.5.2	Data File Description	87

3.5.3	Access	91

3.6	MHS Level 1B NetCDF Granule Files	91

3.6.1	Purpose	91

3.6.2	Data File Description	91

3.6.3	Access	95

3.7	Retrieval Input/Output Files	96

3.7.1	Purpose	96

3.7.2	Data File Description	96

3.7.3	Access	98

4. Output Data Sets	99

4.1. IASI L1C Granule Files	100

4.1.1	Purpose	101

4.1.2	Data File Description	101

4.1.3	Intended Users	101

4.1.4	Access	102

4.2. IASI Level 1C Granule-Level Metadata	102

4.2.1	Purpose	102

4.2.2	Data File Description	102

4.2.3	Intended Users	104

4.2.4	Access	104

4.3. IASI L1CT BUFR granule files	105

4.3.1	Purpose	105

4.3.2	Data File Description	105

4.3.3	Intended Users	109

4.3.4	Access	109

4.4. IASI Global 1-Band PC Grid Files	109

4.4.1	Purpose	109

4.4.2	Data File Description	110

4.4.3	Intended Users	111

4.4.4	Access	111

4.5. IASI Global 3-Band PC Grid Files	112

4.5.1	Purpose	112

4.5.2	Data File Description	112

4.5.3	Intended Users	114

4.5.4	Access	114

4.6. IASI Full Global 1-Band PC Grid Files	115

4.6.1	Purpose	115

4.6.2	Data File Description	115

4.6.3	Intended Users	117

4.6.4	Access	117

4.7. IASI Full Global 3-Band PC Grid Files	117

4.7.1	Purpose	117

4.7.2	Data File Description	118

4.7.3	Intended Users	119

4.7.4	Access	119

4.8. IASI Global Thinned Radiances	120

4.8.1	Purpose	120

4.8.2	Data File Description	120

4.8.3	Intended Users	122

4.8.4	Access	122

4.9. IASI Full Global Thinned Radiances	123

4.9.1	Purpose	123

4.9.2	Data File Description	123

4.9.3	Intended Users	125

4.9.4	Access	125

4.10. Full Global Grids Metadata	126

4.10.1	Purpose	126

4.10.2	Data File description	126

4.10.3	Intended Users	127

4.10.4	Access	128

4.11. IASI GFS Forecast Global Grids	128

4.11.1	Purpose	128

4.11.2	Data File Description	128

4.11.3	Intended Users	130

4.11.4	Access	130

4.12. IASI GDAS Forecast Global Grids	131

4.12.1	Purpose	131

4.12.2	Data File Description	131

4.12.3	Intended Users	133

4.12.4	Access	133

4.13	AMSU-A Full Global Grids	134

4.13.1	Purpose	134

4.13.2	Data File Description	134

4.13.3	Intended Users	136

4.13.4	Access	136

4.14	AMSU-A Global Grids	136

4.14.1	Purpose	137

4.14.2	Data File Description	137

4.14.3	Intended Users	138

4.14.4	Access	138

4.15	MHS Full Global Grids	139

4.15.1	Purpose	139

4.15.2	Data File Description	139

4.15.3	Intended Users	141

4.15.4	Access	141

4.16	MHS Global Grids	142

4.16.1	Purpose	142

4.16.2	Data File Description	142

4.16.3	Intended Users	144

4.16.4	Access	144

4.17	IASI L2 Full Global Grids	144

4.17.1	Purpose	144

4.17.2	Data File Description	145

4.17.3	Intended Users	148

4.17.4	Access	148

4.18	IASI L2 Global Grids	148

4.18.1	Purpose	148

4.18.2	Data File Description	149

4.18.3	Intended Users	152

4.18.4	Access	152

4.19	IASI CCR Global Grids	152

4.19.1	Purpose	152

4.19.2	Data File Description	152

4.19.3	Intended Users	154

4.19.4	Access	154

4.20. IASI Matchups	155

4.20.1	Purpose	155

4.20.2	Data File Description	155

4.20.3	Intended Users	161

4.20.4	Access	161

4.21. EUMETSAT Level 2 BUFR Files	162

4.21.1	Purpose	162

4.21.2	Data File Description	162

4.21.3	Intended Users	162

4.21.4	Access	162

4.22. 2-Scan Global File	163

4.22.1	Purpose	163

4.22.2	Data File Description	163

4.22.3	Intended Users	167

4.22.4	Access	167

4.23	AMSU-A Matchups	168

4.23.1	Purpose	168

4.23.2	Data File Description	168

4.23.3	Intended Users	172

4.23.4	Access	172

4.24	MHS Matchups	173

4.24.1	Purpose	173

4.24.2	Data File Description	173

4.24.3	Intended Users	177

4.24.4	Access	177

4.25	IASI L2 Matchups	178

4.25.1	Purpose	178

4.25.2	Data File Description	178

4.25.3	Intended Users	184

4.25.4	Access	184

4.26	IASI L2 NetCDF Files	184

4.26.1	Purpose	184

4.26.2	Data File Description	184

4.26.3	Intended Users	197

4.26.4	Access	197

4.27	IASI CCR NetCDF File	198

4.27.1	Purpose	198

4.27.2	Data File Description	198

4.27.3	Intended Users	207

4.27.4	Access	207

4.28	IASI L2 and CCR Metadata	208

4.28.1	Purpose	208

4.28.2	Data File Discription	208

4.28.3	Intended Users	209

4.28.4	Access	209

4.29	IASI CCR BUFR Files	210

4.29.1	Purpose	210

4.29.2	Data File Description	210

4.29.3	Intended Users	211

4.29.4	Access	211

4.30	IASI NetCDF Principal Component File	212

4.30.1	Purpose	212

4.30.2	Data File Description	212

4.30.3	Intended Users	220

4.30.4	Access	220

5. LIST OF REFERENCES	223

Appendix A -  IASI L1C BUFR Table	225

# LIST OF FIGURES

Page

Figure 1. IASI PPS External Interfaces	22

Figure 2. IASI PPS System Flow	23

Figure 3. Check L1C Unit Flow	24

Figure 4. L1C Subsetter Unit Flow	24

Figure 5. IASI L1B Processing Unit Flow	25

Figure 6. IASI L2 Processing Unit Flow	25

Figure 7. Global Grids Unit Flow (Level 1)	26

Figure 8. Global Grids Unit Flow (Level 2)	27

Figure 9. Global Binaries Unit Flow	28

Figure 10. Global Matchups Unit Flow	29

# LIST OF TABLES

Page

Table 1. IASI L1C Data File-Naming Convention and Format.	31

Table 2 CDL Template File Descriptions	38

Table 3. Retrieval System Files	51

Table 4 .  Intermediate Data Sets	58

Table 5 Full resolution NetCDF header	60

Table 6. Thinned NetCDF File Header	69

Table 7 IASI Global Binariy Header Record Number 1	71

Table 8 IASI Global Binary Header Record Number 2	72

Table 9 IASI Global Binary Data Record	72

Table 10 AMSU-A Global Binary Header Record Number 1	75

Table 11 AMSU-A Global Binary Header Record Number 2	75

Table 12 AMSU-A Global Binary Data Record	75

Table 13 MHS Global Binary Header Record Number 1	77

Table 14 MHS Global Binary Header Record Number 2	78

Table 15 MHS Global Binary Data Record	78

Table 16 IASI L2 Global Binary Header Record Number 1	80

Table 17 IASI L2 Global Binary Data Record	80

Table 18 AMSU-A Level 1B Net CDF File Header	87

Table 19 MHS Level 1B NetCDF File Header	92

Table 20. Output Files	99

Table 21. Metadata File Name Convention and Format	103

Table 22. IASI L1CT Granule Files Subset	105

Table 23. IASI L1C BUFR Granule File Name Structure	106

Table 24. Matchup Header Record Number 1	156

Table 25. Matchup Header Record Number	157

Table 26. Matchup Data Record	157

Table 27. 2-Scan Header Record Number 1	164

Table 28. 2-Scan Header Record Number 2	165

Table 29. 2-Scan Data Record	165

Table 30. AMSU-A Matchup Header Record Number 1	169

Table 31. AMSU-A Matchup Header record Number 2	169

Table 32. AMSU-A Matchup Data record	169

Table 33. MHS Matchup Header Record Number 1	174

Table 34. MHS Matchup Header Record Number 2	174

Table 35. MHS Matchup Data Record	174

Table 36. IASI L2 matchup Header Record Number 1	178

Table 37. IASI L2 Matchup Data record	179

Table 38. IASI L2 NetCDF Header	186

Table 39. IASI CCR NetCDF Header	200

Table 40. IASI NetCDF Principal Component File Header	213

# LIST OF ACRONYMS

| AFWA | Air Force Weather Agency |
| --- | --- |
| AMSU | Advanced Microwave Sounder Unit |
| ASCII | American Standard Code for Information Interchange |
| AVHRR | Advanced Very High Resolution Radiometer |
| BUFR | Binary Universal Form for the Representation of meteorological data |
| CCR | Cloud-Cleared Radiances |
| CDL | Common Data Language |
| CLASS | Comprehensive Large Array-data Stewardship System |
| DDS | Data Distribution Server |
| DOD | Department of Defense |
| EPS | EUMETSAT Polar System |
| ESPC | Environmental Satellite Processing Center |
| EUMETSAT | European Organization for the Exploitation Meteorological Satellites |
| FGDC | Federal Geographic Data Center |
| FNMOC | Fleet Numerical Meteorology and Oceanography Center |
| FOR | Field Of Regard |
| FOV | Field of View |
| GDAS | Global Data Assimilation System |
| GFS | Global Forecast System |
| GFT | Generic File Transfer |
| GMAO | Global Modeling and Assimilation Office |
| GrADS | Grid Analysis and Display System |
| GRIB | Gridded Binary format |
| GTS | Global Transmission System |
| IASI | Infrared Atmospheric Sounding Interferometer |
| MHS | Microwave Humidity Sounder |
| NCEP | National Center for Environmental Prediction |
| NetCDF | Network Common Data Format |
| NESDIS | National Environmental Satellite, Data, and Information Service |
| NOAA | National Oceanic and Atmospheric Administration |
| NRL | Naval Research Lab |
| NRT | Near Realtime Terminal |
| NWS | National Weather Service |
| OPDB | Operations Product Development Branch |
| OSDPD | Office of Satellite Data Processing and Distribution |
| PFS | Product Format Specification |
| PPS | Product Processing System |
| RR | Reconstructed Radiances |
| RSE | Remote Sensing Extension |
| SDD | System Description Document |
| STAR | Center for Satellite Applications and Research |
| XML | eXtensible Markup Language |

# Introduction

The Interface Control Document (ICD), a standard STAR EPL project artifact, is one of six standard SPSRB documents. The purpose of this document is to describe all input, intermediate and output datasets at the level of detail sufficient for the maintenance personnel to be able to locate it and identify processing errors that involve it.  This document specifies the interfaces of the IASI product processing system (PPS). This document provides an overview of the IASI PPS, followed by detailed descriptions of input, intermediate, and output datasets. Data description includes details on format/type, range and special error value, file naming conventions and data content and formats.  For more detailed descriptions of the IASI PPS the reader is referred to the User’s Manual (UM) and System Description Document (SDD). Intended users of this document are operational maintenance personnel.

There are seven main system software units within the IASI product processing system. Each unit is not a single program, but actually a family of related programs. They are numbered roughly in the order in which they process data through the system: (1) Check L1C, (2) L1B Processing Unit, (3) L1C Subsetter, (4) L2 Processing, (5) Global Grids, (6) Global Binaries, and (7) Global Matchups.  Check L1C is the data acquisition, checking, and preprocessing units.  L1C Subsetter is the main product generation unit. L1B Processing handles ingest, collocation to IASI, and preprocessing (for Level 2) of the AMSU-A and MHS data. Global Grids, Global Binaries, and Global Matchups are the products validation and verification units.  Data flows within units are shown in Figures 2 - 10.

This document was developed by the IASI development team under the oversight of the IASI project lead and the IASI project review team.  The review team consists of management and technical staff from both the Center for Satellite Applications and Research (STAR) and the Office of Satellite Data Processing and Distribution (OSDPD).  The document is approved by members of this review team.  It is stored in configuration management as a project artifact, maintained, and disseminated by the IASI development team.  This team resides within the Operational Products Development Branch (OPDB) at STAR.

This document is organized as follows:

Section 1 – provides brief description of IASI PPS.

It also gives the overview of the document.

Section 2 – provides a description of input data files, including function, type, format and naming convention and content.

Section 3 – provides a description of intermediate files including function, type, format and naming convention and content. It also gives an idea by which component of the PPS these datasets are generated and what they are used for. The software units are always shown in italics.

Section 4– provides a description of output data files including function, type, format and naming convention and content. It also gives an idea by which component of the PPS these datasets are generated and what they are used for. The software units are always shown in italics.

Section 5 - provides a list of documents that are referenced in this manual.  Many of these are project artifacts that should be available to the users of this document.

Figure 1. IASI PPS External Interfaces

Figure 1 shows the external system interfaces. The external interfaces refer to the connectivity between the processing system and outside elements such as remote servers. The current system has three external interfaces, the Generic File Transfer (GFT), the Environmental Satellite Processing Center (ESPC) Data Distribution Server (DDS), and the OSDPD 24/7 production monitoring machine (balmy.nesdis.noaa.gov).  The EUMETSAT IASI L1C granule data are pulled from the GFT and the GFS and GDAS forecast files, as well as AMSU-A/MHS L1B data files are pulled from the DDS.  All product files are transferred to the DDS  where customers can retrieve them. The DDS makes products available to the Shared Processing Network (SPN) for Department of Defense (DOD) customers.  The IASI Process_Status file is required by the OSDPD monitoring tool.  Updates of this file’s contents are sent directly to balmy.nesdis.noaa.gov at regular intervals.  The OSDPD monitoring tool is run on this machine by the 24/7 production monitoring staff.  All system files reside within, and are managed by, the system itself.  Access to the GFT and DDS is through ftp.  This is automated using a .netrc file in the home directory of the application ID (/home/iasidev/.netrc).  The IASI L1C data files reside in the GFT directory of entry (when accessing the machine through the user account).  On the DDS all files required as input are pulled from the “pull” directory.   The IASI PPS products are sent to the “push” directory.  Upon entry a user or script must change to the “push” or “pull” directories.  Sent files can be viewed in the neighboring “pull” directory to verify transfer.  Nominally, data reside on the GFT and DDS for 24 hours before being removed.  The DDS handles all the direct external data distribution to customers.  To access the data products on these servers, a customer must have an account.   Retrievals of all data products are through ftp pulls.

Figure 2. IASI PPS System Flow

Figure 2 shows the internal system interfaces. The internal interfaces refer to the relationships (1) between processing units and (2) between processing units and the system itself. Each unit is not a single program, but actually a family of related programs.

Figure 3. Check L1C Unit Flow

Figure 4. L1C Subsetter Unit Flow

Figure 5. IASI L1B Processing Unit Flow

Figure 6. IASI L2 Processing Unit Flow

Figure 7. Global Grids Unit Flow (Level 1)

Figure 8. Global Grids Unit Flow (Level 2)

Figure 9. Global Binaries Unit Flow

Figure 10. Global Matchups Unit Flow

# Input Data Sets

Input datasets used in IASI PPS are described in detail in this section.  To get a sense of where these files fit within the IASI PPS, the reader is referred to the previous section and Figures 1 - 10.

## IASI L1C Granule Files

The EUMETSAT PFC IASI L1C binary granule files.

### Purpose

The EUMETSAT IASI L1C binary granule files in the native Product Format Specification (PFS) format are used for:

- Ingesting and staging the EUMETSAT IASI L1C data for processing.

  - Extracting the contents of the EUMETSAT IASI L1C header for generating metadata.

  - Extracting some additional metadata information from the IASI measurement data records such as bounding box for the granule.)

- Generating spatially and spectrally subset data as well as principal components

- Generating FGDC compliant IASI granule metadata files inthe eXtensible Markup Language (XML) format for the Comprehensive Large Array-data Stewardship System (CLASS) archive in accordance with Producer-Archive  Submission Agreement for IASI Products (CLASS, 2006). These granule files are also used to generate subset data products to be distributed for operational use by the NWS and the Department of Defense (DOD).

These files and their associated metadata are transmitted by the NOAA/NESDIS/STAR near real time processing system to the OSDPD DDS for retrieval by CLASS.

### Data File Description

These are big endian sequential access binary files. The data set consists of granular files 176 seconds in length. Therefore, 480 granules are produced per day. The IASI level 1C PFS files contain:

- The radiances for 8461 channels

- The mean and standard deviation of Advanced Very High Resolution Radiometer (AVHRR) radiances on the IASI fields of view

- Calibrated IASI image for a window channel

- An AVHRR radiance analysis image

- All associated navigational and temporal information for the observations

- Number of quality control flags.

Table 1. IASI L1C Data File-Naming Convention and Format.

| Data file-naming Convention | IASI_xxx_1C_M01_${Sensing_Start}Z_${Sensing_End}Z_${P}_${D}_${Processing_Time_Start}Z_${Unknown_Date_String} Where: IASI = Instrument xxx = hard-coded value 1C = Processing level M01 = Satellite (MetOp1) Sensing_Start = the starting time of observations given in the following format YYYYMODDHHMMSSZ Sensing_End = the ending time of observations given as YYYYMODDHHMMSSZ $P = Processing mode $D = Disposition mode Processing_Time_Start = the processing time for the observations given as YYYYMODDHHMMSSZ $Unknown_Date_String = this is some time string whose meaning is not known because it is not defined by the EPS Programme Generic Product Format Specification (EUMETSAT, 2003) The string “YYYYMODDHHMMSSZ” is a date string containing the following components of time: YYYY = 4 digit year (e.g. 2005) MO = 2 digit month (01-12) DD = day of month (01-31) HH = hour (00-23) MM = minute (00-59) SS = seconds (00-59) Z = Greenwich Mean Time The variable $P can have any of the following values: N = nominal B = backlog R = reprocessing V = validation At this time NOAA/NESDIS/STAR plans to distribute only nominal mode data to the ESPC DDS. The variable $D may have any of the following values: T = testing O = operational C = commissioning |
| --- | --- |
| Data file formats | The file is a binary (big endian) data file in sequential access format. An IASI L1C data file contains 22 measurement data records each of which has a nominal record length of 2727768 bytes. If a measurement data record is missing, a 21 byte dummy measurement data record is inserted where the full record would normally be. The absence of a given record is indicated in the generic record header of the dummy measurement data record. There are 4 types of records that precede the measurement data records: (1) the Main Product Header Record (3307 bytes); (2) three Internal Pointer Records (3 X 27 bytes); (3) the Global Internal Auxiliary Data Record-Quality (228346 bytes); and (4) the Global Internal Auxiliary Data Record-Scale Factors (84 bytes). Therefore, with the headers and the 22 data records a file, with no missing records, is exactly 60242714 bytes in length. |
| Expected data file size | 60 MB/file |

There are no backup sources of these input data sets.

Specific file details (and more about data and header records) can be found in:

EPS PROGRAMME IASI Level 1 Product Format Specifications, Ref: EUM.EPS.SYS.SPE.990003,Issue 6, Rev 6, WEB number 270000, 03/23/2004, EUMETSAT. 
For the EUMETSAT L1C PFS format refer to the section "GIADR-QUALITY", "GIADR-SCALE FACTORS", and "MDR-1C" in the Appendix "IASI-L1-PFS-6.6-ANNEX" in the document “EPS PROGRAMME IASI Level 1 Product Format Specifications, Ref: EUM.EPS.SYS.SPE.990003,Issue 6, Rev 6, WEB number 270000, 03/23/2004, EUMETSAT”.

EPS Programme Generic Product Format Specification, Ref: EPS.GGS.SPE.96167, Issue 6, Rev 4, WEB number 270000, 02/11/2003, EUMETSAT.

### Access

The IASI data originate from the EPS MetOp1 satellite and are processed from Level 0 up to Level 2 at the processing facilities in Darmstadt, Germany by European Organization of the Exploration of Meteorological Satellites (EUMETSAT).  These data files are then pushed into remote server (GFT) (maco.nesdis.noaa.gov). The files are pulled into the system by the Perl script called Run_Get_L1C-Files.pl. Normally, the files arrive in the system approximately every three minutes at:

$BASE/L1C/IASI

POC - Simon Elliott

Meteorological Product Implementation Manager, Operations department

Address: Am Kavalleriesand 31

Darmstadt, Hessen, 64295

Germany

Telephone:        (+49) 6151 807 385

Fax:	               (+49) 6151 807 385

E-Mail Address: Simon.Elliott@eumetsat.int

(Reference to the Agreement between EUMETSAT and NOAA concerning IASI data will be inserted here)

## GFS Forecast Files

Global Forecast System (GFS) forecast files

### Purpose

These files are used to generate the GFS forecast global grids by the script Run_IASI_GFS_Forecast_Grids.pl.  This script is part of the Global Grids software unit.

### Data File Description

The files have the following name structure:

gfs.t${Hour}z.pgrbf${Forecast}

where:

${Hour} = the time for which the forecast is run (00Z, 06Z, 12Z, and 18Z)

${Forecast} = the forecast projection time (in hours = 00, 03, 06, 09, and 12)

00, 03, 06, 09, and 12 hour forecasts are run every six hours.  The files are GRIB format files and are read with the wgrib reader which is freely available from NCEP.  The header content of any GRIB file can be viewed by running wgrib and supplying the file name as an argument to the command.

The following forecast variables are extracted from 91 levels and used by the processing:

Run Hour

Forecast Hour

Forecast Latitude

Forecast Longitude

Pressure

Temperature

Water Vapor

Ozone

2 meter Dew Point

2 meter Temperature

Skin Temperature

Surface Pressure

Precipitable Water Content

Total Column Ozone

Sea Surface Temperature

Land Fraction

Temperature of the 30 mb to 0 mb layer

The surface pressure from these files is also used in the Level 2 Processing unit.  This will be discussed in a later release of the system.

### Access

These are forecast files generated by NCEP and pushed (by NCEP) to the ESPC/DDS.  They are then pulled by the IASI system script and put in the following directory:

$BASE/Model_Forecast/AVIATION/${Year}/${Month}/${Day}

where:

${Year} = the 4-digit year

${Month} = 2-digit month

${Day} = 2-digit day of month

POC – Nichols, Catherine L

5200 Auth Road, Room 0315, Building: FB4

Suitland, MD 20746 – 4301

Phone: (301)457-5245

Fax:      (301)457-5199

E-mail: cathy.nichols@noaa.gov

## GDAS Forecast Files

Global Data Assimilation System (GDAS) forecast files

### Purpose

These files are used to generate the GDAS forecast global grids by the script Run_IASI_GDAS_Forecast_Grids.pl.  This script is part of the Global Grids software unit.

### Data File Description

The input forecast files must be in GRIB format and are from the GDAS forecast products. The GDAS GRIB forecast files have the following name structure:

gdas1.t${Hour}z.sf${Forecast}

where:

${Hour} = the time for which the forecast is run (00Z, 06Z, 12Z, and 18Z).

${Forecast} = the forecast projection time (in hours = 00, 03, 06, and 09).

00, 03, 06, and 09 hour forecasts are run every six hours.  These files, unlike the GFS files, are in a special binary format that cannot be viewed easily.  The data are also in spectral coordinates, as opposed to rectangular coordinates.

The following forecast variables are extracted from 91 levels and used by the processing:

Run Hour

Forecast Hour

Forecast Latitude

Forecast Longitude

Pressure

Temperature

Water Vapor

Ozone

2 meter Dew Point

2 meter Temperature

Skin Temperature

Surface Pressure

Precipitable Water Content

Total Column Ozone

Sea Surface Temperature

Land Fraction

Delta Pressure

### Access

These are forecast files generated by NCEP and pushed (by NCEP) to the ESPC/DDS.  They are then pulled by the IASI system script (Run_Get_GDAS_Forecast.pl) and put in the following directory:

$BASE/Model_Forecast/GDAS/${Year}/${Month}/${Day}

where:

${Year} = the 4-digit year

${Month} = 2-digit month

${Day} = 2-digit day of month

POC – Nichols, Catherine L

5200 Auth Road, Room 0315, Building: FB4

Suitland, MD 20746 – 4301

Phone: (301)457-5245

Fax:      (301)457-5199

E-mail: cathy,Nichols@noaa.gov

## CDL Template Files

Common Data Language (CDL) Template files

The system uses a number of template files.  These are all static files that will only change with a new delivery of the system.  They are never modified by the scripts and programs that use them.  Scripts will only copy these files to a local directory or create a soft links to them.

### Purpose

These are template parameter files used for generating the IASI L1C, AMSU-A, MHS, and IASI L2 granule subsets.

### Data File Description

These files contain the lists of channels and footprints to be extracted for each type of subset.  They also contain the variable lists, array sizes and array dimensions for each NetCDF output file.  Each file can be converted into a NetCDF file using the ncgen NetCDF library utility.  This file will have a complete header based on that of the CDL template, but contains no instrument data values, only fill (missing) values.  These files are then populated with instrument data values by the subsetter code.  There is a different template file for each type of subset.  In addition, for each subset, there is a template for a granule that contains 22 or 23 scan lines.

The following CDL template files, shown in table 2, are present in the current build:

Table 2 CDL Template File Descriptions

| CDL Template Name | Description |
| --- | --- |
| iasi_2scan_22.cdl | A template for all fovs, 8461 channels, 2 scans/granule (22 scans) |
| iasi_2scan_23.cdl | A template for all fovs, 8461 channels, 2 scans/granule (23 scans) |
| iasi_all_22.cdl | A template for all fovs, 8461 channels (22 scans) |
| iasi_all_23.cdl | A template for all fovs, 8461 channels (23 scans) |
| iasi_all_pc_1b_22.cdl | template for all fovs, 616 channels of RR, 1 band (22 scans) |
| iasi_all_pc_1b_23.cdl | A template for all fovs, 616 channels of RR, 1 band (23 scans) |
| iasi_all_pc_3b_22.cdl | A template for all fovs, 616 channels of RR, 3 band (22 scans) |
| iasi_all_pc_3b_23.cdl | A template for all fovs, 616 channels of RR, 3 band (23 scans) |
| iasi_gmao_22.cdl | A template for all fovs, 616 channels (22 scans) |
| iasi_gmao_23.cdl | A template for all fovs, 616 channels (23 scans) |
| iasi_ncep_22.cdl | A template for all 1st fov, 616 channels (22 scans) |
| iasi_ncep_23.cdl | A template for all 1st fov, 616 channels (23 scans) |
| iasi_ncep_pc_1b_22.cdl | A template for 1st fov, 616 channels of RR, 1 band (22 scans) |
| iasi_ncep_pc_1b_23.cdl | A template for 1st fov, 616 channels of RR, 1 band (23 scans) |
| iasi_ncep_pc_3b_22.cdl | A template for 1st fov, 616 channels of RR, 3 band (22 scans) |
| iasi_ncep_pc_3b_23.cdl | A template for 1st fov, 616 channels of RR, 3 band (23 scans) |
| iasi_warmest_22.cdl | A template for all warmest fov, 616 channels (22 scans) |
| iasi_warmest_23.cdl | A template for all warmest fov, 616 channels (23 scans) |
| amsua_22.cdl | A template for all fovs and all channels (22 scans) |
| amsua_23.cdl | A template for all fovs and all channels (23 scans) |
| mhs_22.cdl | A template for all fovs and all channels (22 scans) |
| mhs_23.cdl | A template for all fovs and all channels (23 scans) |
| iasi_ccr_22.cdl | A template for all fovs and all 8461 channels (22 scans) |
| iasi_ccr_23.cdl | A template for all fovs and all 8461 channels (23 scans) |
| iasi_ccr_archive_22.cdl | A template for all fovs and all 8461 channels (22 scans). Unused variable names are deleted and current ones are standardized for archive. |
| iasi_ccr_archive_23.cdl | A template for all fovs and all 8461 channels (23 scans). Unused variable names are deleted and current ones are standardized for archive. |
| iasi_ccr_ncep_22.cdl | A template for all fovs and 616 channels (22 scans) |
| iasi_ccr_ncep_23.cdl | A template for all fovs and 616 channels (23 scans) |
| iasi_l2_22.cdl | A template for all fovs for level 2 profile data (22 scans) |
| iasi_l2_23.cdl | A template for all fovs for level 2 profile data (23 scans) |
| All files contain radiances unless otherwise indicated with an RR which stands for Reconstructed Radiances from principal components. |

### Access

All CDL templates are provided by STAR.

POC: Walter Wolf

5211 Auth Road Room 204

Suitland, MD, 20746

Tel: (301) 316-5003

Fax:(301) 763-8580

E-mail: walter.wolf@noaa.gov

All CDL templates are located in the system file tree at:

$BASE/OPERATIONS/NRT_OPS/CDLFILES/

## IASI L1C Granule Metadata Template File

### Purpose

To generate FGDC compliant IASI archival granule metadata for CLASS.

### Data File Description

This is an FGDC-RSE compliant xml format metadata template file.  It is a static file that is used to build the IASI granule metadata files.  It contains static metadata and some tags that are extracted and replaced with dynamic information by the IASI granule metadata generation script (Create_IASI_L1C_Metadata.pl). Below is an example of a Granule_Info file for Granule number 088 from June 8th, 2007:

YEAR=2007 MONTH=06 DAY=08 GRANULE_NUMBER=088 L1C_FILENAME=IASI_xxx_1C_M02_20070608042357Z_20070608042653Z_N_O_20070608060013Z__20070608060557 PRODUCT_NAME = IASI_xxx_1C_M02_20070608042357Z_20070608042653Z_N_O_20070608060013Z PARENT_PRODUCT_NAME_1 = IASI_xxx_00_M02_20070608042352Z_20070608042700Z_N_O_20070608055040Z PARENT_PRODUCT_NAME_2 = xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx PARENT_PRODUCT_NAME_3 = xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx PARENT_PRODUCT_NAME_4 = xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx INSTRUMENT_ID = IASI INSTRUMENT_MODEL = 1 PRODUCT_TYPE = xxx PROCESSING_LEVEL = 1C SPACECRAFT_ID = M02 SENSING_START = 20070608042357Z SENSING_END = 20070608042653Z SENSING_START_THEORETICAL = 20070608032100Z SENSING_END_THEORETICAL = 20070608050300Z PROCESSING_CENTRE = CGS1 PROCESSOR_MAJOR_VERSION = 3 PROCESSOR_MINOR_VERSION = 6 FORMAT_MAJOR_VERSION = 10 FORMAT_MINOR_VERSION = 0 PROCESSING_TIME_START = 20070608060013Z PROCESSING_TIME_END = 20070608060208Z PROCESSING_MODE = N DISPOSITION_MODE = O RECEIVING_GROUND_STATION = SVL RECEIVE_TIME_START = 20070608045844Z RECEIVE_TIME_END = 20070608045853Z ORBIT_START = 3288 ORBIT_END = 3289 ACTUAL_PRODUCT_SIZE = 60242714 STATE_VECTOR_TIME = 20070608024935000Z SEMI_MAJOR_AXIS = 7204595893 ECCENTRICITY = 1232 INCLINATION = 98697 PERIGEE_ARGUMENT = 70399 RIGHT_ASCENSION = 218902 MEAN_ANOMALY = 289679 X_POSITION = 1299767989 Y_POSITION = -7083348469 Z_POSITION = -6891965 X_VELOCITY = -1623494 Y_VELOCITY = -296280 Z_VELOCITY = 7355656 EARTH_SUN_DISTANCE_RATIO = 6 LOCATION_TOLERANCE_RADIAL = 0 LOCATION_TOLERANCE_CROSSTRACK = 0 LOCATION_TOLERANCE_ALONGTRACK = 0 YAW_ERROR = 0 ROLL_ERROR = 0 PITCH_ERROR = 0 SUBSAT_LATITUDE_START = 0 SUBSAT_LONGITUDE_START = 0 SUBSAT_LATITUDE_END = -14801 SUBSAT_LONGITUDE_END = -101599 LEAP_SECOND = 0 LEAP_SECOND_UTC = xxxxxxxxxxxxxxZ TOTAL_RECORDS = 28 TOTAL_MPHR = 1 TOTAL_SPHR = 0 TOTAL_IPR = 3 TOTAL_GEADR = 0 TOTAL_GIADR = 2 TOTAL_VEADR = 0 TOTAL_VIADR = 0 TOTAL_MDR = 22 COUNT_DEGRADED_INST_MDR = 12 COUNT_DEGRADED_PROC_MDR = 12 COUNT_DEGRADED_INST_MDR_BLOCKS= 0 COUNT_DEGRADED_PROC_MDR_BLOCKS= 0 DURATION_OF_PRODUCT = 175562 MILLISECONDS_OF_DATA_PRESENT = 175562 MILLISECONDS_OF_DATA_MISSING = 0 SUBSETTED_PRODUCT = 0 BOUNDING_LAT1=-26.31 BOUNDING_LAT2=-21.67 BOUNDING_LAT3=-16.84 BOUNDING_LAT4=-12.15 BOUNDING_LON1=-107.68 BOUNDING_LON2=-89.38 BOUNDING_LON3=-111.20 BOUNDING_LON4=-92.79 AD_STAT=AA GRANULE_STATUS=M DUMP_START_TIME=20070608032100 DUMP_END_TIME=20070608050300

### Access

The IASI granule metadata template file is provided by STAR.

POC: Walter Wolf

5211 Auth Road Room 204

Suitland, MD, 20746

Tel: (301) 316-5003

Fax:(301) 763-8580

E-mail: walter.wolf@noaa.gov

The file is in the system file tree at:

$BASE/OPERATIONS/NRT_OPS/metadata/IASI_Granule_Metadata_Template.xml

## Global Grid Metadata Template File

Global Grid (3X3 degree) Metadata Template file.

### Purpose

This file is used to build the IASI global grid metadata files.

### Data File Description

This is an FGDC-RSE compliant xml format metadata template file.  It is a static file that is used to build the IASI global grid metadata files.  It contains static metadata and some tags that are extracted and replaced with dynamic information by the IASI grid metadata generation script (Create_IASI_L2_Metadata.pl). Below is an example of a Grid_Info file from June 7th, 2007:

ASC_START_DATE=20070607 ASC_START_TIME=00030200 ASC_END_DATE=20070607 ASC_END_TIME=23520400 DESC_START_DATE=20070607 DESC_START_TIME=00130800 DESC_END_DATE=20070608 DESC_END_TIME=00024800

### Access

The Global Grid (3X3 degree) Metadata Template file is provided by STAR.

POC: Walter Wolf

5211 Auth Road Room 204

Suitland, MD, 20746

Tel: (301) 316-5003

Fax:(301) 763-8580

E-mail: walter.wolf@noaa.gov

The file is in the system file tree at:

$BASE/OPERATIONS/NRT_OPS/metadata/IASI_3X3Grid_Metadata_Template.xml

L2 Metadata Template

Purpose

This file is used to build the IASI L2 granule metadata files.

Data File Description

The granule metadata template is an FGDC-RSE compliant xml format metadata template file.  It is a static file that is used to build the IASI level 2 granule metadata files.  It contains static metadata and some tags that are extracted and replaced with dynamic information by the IASI granule metadata generation script (Create_IASI_L2_Metadata.pl).

Access

The IASI L2 Metadata Template file is provided by STAR.

POC: Walter Wolf

5211 Auth Road Room 204

Suitland, MD, 20746

Tel: (301) 316-5003

Fax:(301) 763-8580

E-mail: walter.wolf@noaa.gov

The file is in the system file tree at:

$BASE/OPERATIONS/NRT_OPS/metadata/IASI_L2_Granule_Metadata_Template.xml

IASI CCR Metadata Template

Purpose

It is a static file that is used to build the IASI CCR granule metadata files.

Data File Description

The granule metadata template is an FGDC-RSE compliant xml format metadata template file.  It is a static file that is used to build the IASI CCR granule metadata files.  It contains static metadata and some tags that are extracted and replaced with dynamic information by the IASI granule metadata generation script (Create_IASI_L2_Metadata.pl).

Access

The IASI CCR Metadata Template file is provided by STAR.

POC: Walter Wolf

5211 Auth Road Room 204

Suitland, MD, 20746

Tel: (301) 316-5003

Fax:(301) 763-8580

E-mail: walter.wolf@noaa.gov

The file is in the system file tree at:

$BASE/OPERATIONS/NRT_OPS/metadata/IASI_CCR_Granule_Metadata_Template.xml

## Matchup Template File

### Purpose

The Matchup Template file is a static text file containing a list of locations to which IASI observations will be collocated.  In the current build of the system these are only radiosonde launch sites and times.

### Data File Description

The file is an ASCII file containing the following fields for each matchup location: latitude, longitude, year, month, day, hour, minute, distance tolerance, and time tolerance.  The distance tolerance is the distance (in kilometers) within which IASI observations will be considered for a collocation.  The time tolerance is the time (plus or minus minutes) around which IASI observations are considered for a collocation.  The entire template list covers a 30 hour range of data such that it includes 24 hours from the target day plus the three hours that overlap at the end of the previous day and the beginning of the following day.  The date information in the template consists of only text tags.  A script called Create_Matchup_List.pl generates a matchup file for a given day based on this template by modifying the date tags to insert the desired processing date’s data fields.

### Access

The Matchup Template file is provided by STAR.

POC: Walter Wolf

5211 Auth Road Room 204

Suitland, MD, 20746

Tel: (301) 316-5003

Fax:(301) 763-8580

E-mail: walter.wolf@noaa.gov

This matchup template file resides at:

$BASE/OPERATIONS/NRT_OPS/matchups/radiosonde_machup_template.txt

## EUMETSAT Level 2 BUFR Files

EUMETSAT Level 2 data files in BUFR format.

### Purpose

The IASI PPS distributes METOP instrument Level 2 products (temperature and moisture profiles) in BUFR format via NRT/GTS link

### Data File Description

Data files contain atmospheric temperature and moisture profiles. They would capture the fields from IASI-L2-PFS as follows:

| ATMOSPHERIC_TEMPERATURE ATMOSPHERIC_WATER_VAPOR | Temperature (for 120 IFOV with up to 90 vertical levels) Water vapor (for 120 IFOV with up to 90 vertical levels) | 2 6 | K kg/kg | NLT NLQ | 120 120 | u-integer2 u-integer4 | 2 4 | 21600 43200 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

For atmospheric temperature profile the BUFR code is: 0-12-001.

For atmospheric moisture profile the BUFR code: 0-13-001.

Reference documents:

[IASI-L2-PFS]: EPS.MIS.SPE.980760 “EUMETSAT Polar System (EPS) InfraredAtmospheric Sounding Interferometer (IASI) Level 2 Product Format Specification (PFS).” Issue 6 Rev. 3 (08/09/2006)

### Access

The IASI data originate from the EPS MetOp2 satellite and are processed from Level 0 up to Level 2 by European Organization of the Exploration of Meteorological Satellites (EUMETSAT). These data files are then pushed into remote server (GFT) (maco.nesdis.noaa.gov).

POC - Simon Elliott

Meteorological Product Implementation Manager, Operations department

Address: Am Kavalleriesand 31

Darmstadt, Hessen, 64295

Germany

Telephone:        (+49) 6151 807 385

Fax:	               (+49) 6151 807 385

E-Mail Address: Simon.Elliott@eumetsat.int

OSDPD GFT Point of Contact

Vincent Tabor

NSOF, 4231 Suitland Road, Suitland, MD, 20746

Tel: (301) 457-5247

E-mail: Vicent.Tabor@noaa.gov

## Eigenvector Files

### Purpose

There are four eigenvector files, one for each of the three bands, and one for the entire band. It is off-line system components which are not part of the delivered system. These files contain the eigenvector coefficients required for principal component radiance reconstructions.  The files will need to be updated about once every six months or if there are major changes to the calibration of the instrument.

### Data File Description

These are binary big-endian files. They all have the same name structure as described below:

eigvec_${Year}${Month}${Day}_ascii_real

where:

$Year = 2-digit year

$Month = 2-digit month

$Day = 2-digit day

The date string indicates when the file was generated.

### Access

All four files reside in different directories in the operational system file directory tree:

$BASE/OPERATIONS/NRT_OPS/Data/pc_coeffs/band1

$BASE/OPERATIONS/NRT_OPS/Data/pc_coeffs/band2

$BASE/OPERATIONS/NRT_OPS/Data/pc_coeffs/band3

$BASE/OPERATIONS/NRT_OPS/Data/pc_coeffs/full_band

POC: Zhaohui Cheng

5211 Auth Road Room 204

Suitland, MD, 20746

Tel: (301) 316-5008

E-mail: zhaohui.cheng@noaa.gov

Local Angle correction File

Purpose

A coefficient file required by the retrieval to perform the local angle correction on IASI. The file currently being delivered with this version of the system is:

/IASI/OPERATIONS/NRT_OPS/Data/lac_coeffs/lac_iasi_080220.bin

If it becomes necessary to update this file, the operations staff only needs to copy over a new file into this directory and then update the LAC_DATE string in the NRTOPS_CONFIG which is currently set to February 20th, 2008:

LAC_DATE=080220

Data File Description

The correction is only performed if the local angle correction flag is activated (“ON”) inside NRTOPS_CONFIG file as:

LAC_FLAG=ON

Access

The local angle correction file resides in the system file directory at:

/IASI/OPERATIONS/NRT_OPS/Data/lac_coeffs/lac_iasi_${YYMMDD}.bin

where

$YYMMDD is the 2-digit year, 2-digit month, and 2-digit day

This date string indicates the date at which the file was created.

POC: Dr. Christopher Barnet

irmen Memorial Bldg, Suite 204  
5211 Auth Road                  
Camp Springs, MD 20746          
voice: (301)-316-5011    fax: (301)-238-2398 
email: chris.barnet@noaa.gov

Retrieval System Files

Static retrieval system files.

Purpose

These are inputs to the IASI retrieval, but unlike data files, they are static and are only updated with a delivery of the system.

Data File Description

Table 3 contains the file name and partial path in the first column and the second column contains a brief description of the file.

Table 3. Retrieval System Files

| RTA files |
| --- |
| RTA/airs_olr.dat | Rapid transmittance coefficients to compute Outgoing Longwave Radiation |
| RTA/amsu.v7a | Most recent version of AMSU transmittance coefficients |
| RTA/binary.trcoef.iasi.v9a | post-flight IASI RTA coefficients |
| RTA/mhs.v8a | MHS RTA coefficients |
| Cloud Averaging Table |
| avgcld/iasi_v9a_fm2_b.t1 | IASI cloud averaging table |
| Ensemble Error Estimate File |
| errest/jpl_100c.inp | Ensemble error estimate of climatology |
| MIT Retrieval Files |
| mit_ret/L2.M.cov100av.v1.0.0.anc | MW retrieval error covariance file |
| mit_ret/L2.M.ecof_705.v1.0.0.anc | MW retrieval error covariance file |
| mit_ret/L2.M.weight.hsb.v1.0.0.anc | HSB weighting file (for averaging HSB/MHS to AMSU FOV) |
| mit_ret/L2.uars_clim.v1.0.3.anc.new | L2 UARS climatology file for upper atmosphere |
| mit_ret/ncep_clim.bin | Binary NCEP climatology file for T(p) and q(p) |
| Name List Files for the Main Retrieval Program |
| namelists/clouds_iasi.nl | Cloud files name list |
| namelists/io_iasi.nl | Input/Output name list |
| namelists/microw_iasi.nl | Microwave file name list |
| namelists/ozone_iasi.nl | Ozone file name list |
| namelists/pro_iasi.nl | Profile file name list |
| namelists/temp_iasi.nl | Temperature file name list |
| namelists/water_iasi.nl | Water vapor file name list |
| Noise Files |
| noise/070124_iasi_fm2.dat | Noise file for IASI infrared channels |
| noise/L2.chan_prop.2002.05.04.v6.6.5.anc | IR noise files |
| noise/L2.chan_prop.2002.07.09.v6.6.6.anc | IR noise files |
| noise/L2.chan_prop.2002.08.30.v6.6.2.anc | IR noise files |
| noise/L2.chan_prop.2002.09.17.v6.6.3.anc | IR noise files |
| noise/L2.chan_prop.2002.10.22.v6.6.4.anc | IR noise files |
| noise/L2.chan_prop.2003.01.10.v6.6.8.anc | IR noise files |
| noise/L2.chan_prop.2003.11.19.v6.6.9.anc | IR noise files |
| noise/airs_rawcpf.lst | File that sets EPOCHS for noise files |
| noise/amsu_300.dat | Noise file for all microwave channels |
| RTA Error Terms |
| rtaerr/071019_iasi_rtaerr_v02b.asc | File containing the RTA error terms computed as half bias of the OBS-CALC(truth profile) |
| Solar Irradiance Files |
| solar/iasi_solar_v9a.txt | Solar irradiance file for the radiance calculation |
| Coefficient Files to Compute Surface Emissivity |
| surface/L2.masuda.v2.0.0.anc | Coefficients for the Masuda surface emissivity model for ocean |
| surface/preprocessor.cfg | Surface pressure preprocessing configuration template file |
| IR and MW RTA tuning coefficients for the Radiance OBS-CALC Computations |
| tuning/070115_iasi_mask.asc | IASI tuning mask file |
| tuning/071019_iasi_v02b.asc | IASI tuning |
| Standard Atmosphere Profiles |
| level2/us_std/ usstd100.asc | US Standard Atmosphere on 100 levels |
| Clear Flag Coefficient Files |
| regress/clearflag/ L2.I.cleartest_coef.v2.0.2.day.anc | Day time coefficients |
| regress/clearflag/ L2.I.cleartest_coef.v2.0.2.day.anc.met | Day time coefficient metadata file |
| regress/clearflag/ L2.I.cleartest_coef.v2.0.2.night.anc | Night time coefficients |
| regress/clearflag/ L2.I.cleartest_coef.v2.0.2.night.anc.met | Night time metadata file |
| Regression Coefficient Files |
| regress/iasi/070804_iasi.eig | NOAA IR regression radiance eigenvector file |
| regress/iasi/070804_iasi.frq | NOAA IR regression frequency file |
| regress/iasi/071116_iasi_cldy.reg | NOAA IR cloudy regression coefficient file |
| regress/iasi/071215_iasi_ccr.reg | NOAA IR cloud-clear regression coefficient file |

Access

These files all reside in subdirectories located of the retrieval subdirectory.  The retrieval subdirectory is, in turn, located off of the system file directory:

$BASE/ OPERATIONS/NRT_OPS/retrieval

All the files described below in Table 3 are located in directories relative to this system directory.

POC: Dr. Christopher Barnet

irmen Memorial Bldg, Suite 204  
5211 Auth Road                  
Camp Springs, MD 20746          
voice: (301)-316-5011    fax: (301)-238-2398 
email: chris.barnet@noaa.gov

AMSU-A Orbital files

Purpose

These files are required for the generation of all IASI Level 2 products.

Data File Description

These are big endian direct access binary files.  The format and content of these files are described online in the NOAA KLM User’s Guide at:

http://www2.ncdc.noaa.gov/docs/klm/index.htm

These files are required for the generation of all IASI Level 2 products.   Each file contains a ~100 minute orbit of data starting from, and ending at, the north pole.  Therefore, in a given day there are nominally ~14 orbital files.

The AMSU-A file sizes are nominally 1.9 – 2.0 megabytes.  Occasionally, these files will be smaller if there are problems with the preprocessing upstream at OSDPD or on the satellite.  Smaller files are typically the result of missing scans and are not necessarily corrupted data.

All NOAA product file name structures are described at:

http://www2.ncdc.noaa.gov/docs/klm/html/c8/s8-2.htm

The AMSU-A  file name structure for MetOp-A products is as follows:

${PCC}.${DDDD}.M2.D${YY}${DOY}.S${HHMM}.E${HHMM}.B${BBBBBBB}.${GS}

Where:

$PCC = 3-character processing center ID (e.g. NSS = NOAA/NESDIS Suitland, MD)

$DDDD = 4-character data type ID (e.g. AMAX = AMSU-A )

M2 = Spacecraft ID (e.g. M2 = MetOp-A)

$YY = 2-digit year

$DOY = 3-digit day of year (1-365)

S = Start time indicator

$HHMM = 2-digit hour and 2-digit minute

E = Ending time indicator

B = Processing block ID indicator

$BBBBBBB = 7-digit processing block ID number

$GS = 2-character acquisition ground station ID (SV = Svalbard, Norway)

As an example, here is AMSU-A  file name for Februrary 8th, 2008 beginning at 07:11 GMT and ending at 08:54 GMT:

NSS.AMAX.M2.D08039.S0711.E0854.B0677172.SV

Access

AMSU-A  L1B format orbital files from MetOp-A are available to the system through the DDS as shown in Figure 2.  This acquisition is performed by the Perl script called Run_Get_L1B_Files.pl.  This script is a component within the L1B Processing unit.  Nominally, the files arrive in the system approximately every 100 minutes at:

$BASE/L1B/AMSUA

POC – Nichols, Catherine L

5200 Auth Road, Room 0315, Building: FB4

Suitland, MD 20746 – 4301

Phone: (301)457-5245

Fax:      (301)457-5199

E-mail: cathy.nichols@noaa.gov

MHS Orbital files

Purpose

These files are required for the generation of all IASI Level 2 products.

Data File Description

These are big endian direct access binary files.  The format and content of these files are described online in the NOAA KLM User’s Guide at:

http://www2.ncdc.noaa.gov/docs/klm/index.htm

Each file contains a ~100 minute orbit of data starting from, and ending at, the north pole.  Therefore, in a given day there are nominally ~14 orbital files.

The MHS file sizes are nominally 6.9 – 7.2 megabytes.  Occasionally, these files will be smaller if there are problems with the preprocessing upstream at OSDPD or on the satellite.  Smaller files are typically the result of missing scans and are not necessarily corrupted data.

All NOAA product file name structures are described at:

http://www2.ncdc.noaa.gov/docs/klm/html/c8/s8-2.htm

The MHS L1B file name structure for MetOp-A products is as follows:

${PCC}.${DDDD}.M2.D${YY}${DOY}.S${HHMM}.E${HHMM}.B${BBBBBBB}.${GS}

Where:

$PCC = 3-character processing center ID (e.g. NSS = NOAA/NESDIS Suitland, MD)

$DDDD = 4-character data type ID (e.g. MHSX = MHS)

M2 = Spacecraft ID (e.g. M2 = MetOp-A)

$YY = 2-digit year

$DOY = 3-digit day of year (1-365)

S = Start time indicator

$HHMM = 2-digit hour and 2-digit minute

E = Ending time indicator

B = Processing block ID indicator

$BBBBBBB = 7-digit processing block ID number

$GS = 2-character acquisition ground station ID (SV = Svalbard, Norway)

As an example, here is MHS file name for Februrary 8th, 2008 beginning at 07:11 GMT and ending at 08:54 GMT:

NSS.MHSX.M2.D08039.S0711.E0854.B0677172.SV

Access

MHS L1B format orbital files from MetOp-A are available to the system through the DDS as shown in Figure 2.  This acquisition is performed by the Perl script called Run_Get_L1B_Files.pl.  This script is a component within the L1B Processing unit.  Nominally, the files arrive in the system approximately every 100 minutes at:

$BASE/L1B/MHS

POC – Nichols, Catherine L

5200 Auth Road, Room 0315, Building: FB4

Suitland, MD 20746 – 4301

Phone: (301)457-5245

Fax:      (301)457-5199

E-mail: cathy.nichols@noaa.gov

# Intermediate Data Sets

Intermediate datasets and files used in IASI PPS are described in this section. It is those data sets that are created during processing as a bridge between different software units. The processing errors are described in details in the Operations Manual, section 7 (NESDIS/STAR 2008c). To get a sense of where these files fit within the IASI PPS, the reader is referred to Figures 1-10.  Table 4 provides a summary description of these data files.

Table 4 .  Intermediate Data Sets

| File Content | Spectral Subset | Data type | Spatial Subset | Format |
| --- | --- | --- | --- | --- |
| IIASI radiance | 616 channels | IASI radiance | Warmest FOV from every ROR | NetCDF |
| IASI radiance | 616 channels | IASI radiance | First FOV from every FOR | NetCDF |
| IASI radiance | 616 channels | IASI radiance | All 9 FOVs from every FOR | NetCDF |
| IASI reconstructed Radiance (1band) | 616 channels | IASI reconstructed Radiance (1band) | 1 FOV from every FOR | NetCDF |
| IASI reconstructed Radiance (3band) | 616 channels | IASI Reconstructed Radiance (3band) | 1 FOV from every FOR | NetCDF |
| IASI reconstructed Radiance (1band) | 616 channels | IASI Reconstructed Radiance (1band) | 4 FOV from every FOR | NetCDF |
| IASI reconstructed Radiance (3band) | 616 channels | IASI Reconstructed Radiance (3band) | 4 FOV from every FOR | NetCDF |
| IASI Radiances | 8461 channels | IASI Radiances | 4 FOV from every FOR | NetCDF |
| IASI Radiances | 8461 channels | IASI Radiances | 4 FOVs from 2 scans/granule | NetCDF |
| IASI radiance | 8461 channels | IASI radiance | All FOV | binary |
| AMSU-A radiance | 15 channels | AMSU-A Radiance | All FOV | binary |
| MHS radiance | 5 channels | MHS radiance | All FOV | binary |
| L2 profiles | 100 levels | Profiles | All FOR | binary |
| IASI system metadata (Text) | N/A | IASI system metadata (Text) | N/A | ASCII |
| FOV = Field of View; FOR = Field of Regard; |

## IASI L1C Full Resolution Subset Files

IASI L1CT NetCDF full resolution (8461 channels) granule files (subset according to the scheme specified in the input CDL template).

### Purpose

- To generate IASI L1CT BUFR granule file.

- To generate global binary data sets for validation and to use as an input for the global matchups.

  - To generate a global coverage binary file of the full resolution data and a file containing only the locations and times of the full resolution data. Both files are used together by the global matchups downstream.

- To generate binaries of global coverage for eigenvector generation.

- To generate globally gridded data sets for validation and climate reprocessing.

  - To generate daily 3*3 global grids of the full spatial resolution RR and PCS generated from 1 band.

- To generate daily 3*3 global grids of the full spatial resolution RR and PCS generated from 3 bands.

- To generate daily 3*3 global grids of the full resolution IASI radiances.

- To generate IASI L1CT NetCDF files containing the warmest FOV from full resolution IASI L1CT.

### Data File Description

The NetCDF files are intermediate subset files generated from the IASI PFS files by the main_iasi_level1c_subsetter program.  This program is part of the L1C Subsetter unit (figure 4).

Table 5 Full resolution NetCDF header

| Data file-naming Convention Array dimension variables Variables | iasi_all_8461_$YYYYMMDD_Granule-$GGG.nc where: $YYYYMMDD = 8-digit year month day format (e.g. 20070517) $GGG = the 3-digit granule number (e.g. 088). The granule number can go from 001 to 480. Number_of_Dice = 660 ; // Number dice written Number_of_Dots = 4 ; // Number of IASI FOVS in a die Number_of_IASI_Channels = 8461 ; // Number of IASI Channels Number_of_IASI_Frequencies = 8461 ; // Number of IASI Clear Frequencies Number_of_AVHRR_Channels = 6; // Number of AVHRR channels Number_of_AVHRR_FOV_Classes = 7; // Number of AVHRR sounder FOV classes Number_of_AVHRR_Frequencies = 6; Number_of_IASI_Image_Pixels = 4096; // 64 X 64 Pixel IASI image long IASI_Channels(Number_of_IASI_Channels) ; IASI_Channels:long_name = "Channel number for data" ; IASI_Channels:units = "none" ; IASI_Channels:scale_factor = 1.0d ; IASI_Channels:add_offset = 0.0d ; IASI_Channels:parameter_type = "IASI data" ; IASI_Channels:valid_range = 1.0f, 8461.0f ; IASI_Channels:_FillValue = -9999 ; float IASI_Frequencies(Number_of_IASI_Frequencies) ; IASI_Frequencies:long_name = "Frequency at which the data is taken" ; IASI_Frequencies:units = "wavenumber cm-1" ; IASI_Frequencies:scale_factor = 1.0d ; IASI_Frequencies:add_offset = 0.0d ; IASI_Frequencies:parameter_type = "IASI data" ; IASI_Frequencies:valid_range = 0.0f, 10000.0f ; IASI_Frequencies:_FillValue = -9999.0f ; long AVHRR_Channels(Number_of_AVHRR_Channels) ; AVHRR_Channels:long_name = "Channel number for data" ; AVHRR_Channels:units = "none" ; AVHRR_Channels:scale_factor = 1.0d ; AVHRR_Channels:add_offset = 0.0d ; AVHRR_Channels:parameter_type = "AVHRR data" ; AVHRR_Channels:valid_range = 1.0f, 6.0f ; AVHRR_Channels:_FillValue = -9999 ; float AVHRR_Frequencies(Number_of_AVHRR_Frequencies) ; AVHRR_Frequencies:long_name = "Frequency at which the data is taken" ; AVHRR_Frequencies:units = "wavenumber cm-1" ; AVHRR_Frequencies:scale_factor = 1.0d ; AVHRR_Frequencies:add_offset = 0.0d ; AVHRR_Frequencies:parameter_type = "AVHRR data" ; AVHRR_Frequencies:valid_range = 0.0f, 16000.0f ; AVHRR_Frequencies:_FillValue = -9999.0f ; long AVHRR_FOV_Classes(Number_of_AVHRR_FOV_Classes) ; AVHRR_FOV_Classes:long_name = "The index of the AVHRR FOV sounder class" ; AVHRR_FOV_Classes:units = "none" ; AVHRR_FOV_Classes:scale_factor = 1.0d ; AVHRR_FOV_Classes:add_offset = 0.0d ; AVHRR_FOV_Classes:parameter_type = "AVHRR data" ; AVHRR_FOV_Classes:valid_range = 1.0f, 7.0f ; AVHRR_FOV_Classes:_FillValue = -9999 ; long Dice(Number_of_Dice) ; Dice:long_name = "The index of the IASI fields of regard" ; Dice:units = "none" ; Dice:scale_factor = 1.0d ; Dice:add_offset = 0.0d ; Dice:parameter_type = "IASI data" ; Dice:valid_range = 1.0f, 660.0f ; Dice:_FillValue = -9999 ; long Dots(Number_of_Dots) ; Dots:long_name = "The index of the IASI fields of view" ; Dots:units = "none" ; Dots:scale_factor = 1.0d ; Dots:add_offset = 0.0d ; Dots:parameter_type = "IASI data" ; Dots:valid_range = 1.0f, 4.0f ; Dots:_FillValue = -9999 ; long Scan_Line(Number_of_Dice,Number_of_Dots) ; Scan_Line:long_name = "The number of the current scan line" ; Scan_Line:units = "none" ; Scan_Line:scale_factor = 1.0d ; Scan_Line:add_offset = 0.0d ; Scan_Line:parameter_type = "IASI data" ; Scan_Line:valid_range = 1.0f, 22.0f ; Scan_Line:_FillValue = -9999 ; long AMSU_FOV(Number_of_Dice,Number_of_Dots) ; AMSU_FOV:long_name = "The number of the current AMSU FOV" ; AMSU_FOV:units = "none" ; AMSU_FOV:scale_factor = 1.0d ; AMSU_FOV:add_offset = 0.0d ; AMSU_FOV:parameter_type = "IASI data" ; AMSU_FOV:valid_range = 1.0f, 30.0f ; AMSU_FOV:_FillValue = -9999 ; long IASI_FOV(Number_of_Dice,Number_of_Dots) ; IASI_FOV:long_name = "The number of the current IASI FOV" ; IASI_FOV:units = "none" ; IASI_FOV:scale_factor = 1.0d ; IASI_FOV:add_offset = 0.0d ; IASI_FOV:parameter_type = "IASI data" ; IASI_FOV:valid_range = 1.0f, 4.0f ; IASI_FOV:_FillValue = -9999 ; short GQisFlagQual(Number_of_Dice,Number_of_Dots) ; GQisFlagQual:long_name = "System QC flag" ; GQisFlagQual:units = "none" ; GQisFlagQual:scale_factor = 1 ; GQisFlagQual:add_offset = 0 ; GQisFlagQual:parameter_type = "IASI data" ; GQisFlagQual:valid_range = 0, 1 ; GQisFlagQual:_FillValue = -9999s ; float GQisQualIndex(Number_of_Dice,Number_of_Dots) ; GQisQualIndex:long_name = "System QC flag" ; GQisQualIndex:units = "none" ; GQisQualIndex:scale_factor = 1.0d ; GQisQualIndex:add_offset = 0.0d ; GQisQualIndex:parameter_type = "IASI data" ; GQisQualIndex:valid_range = 0.0f, 9999.0f ; GQisQualIndex:_FillValue = -9999.0f ; float GQisQualIndexLoc(Number_of_Dice,Number_of_Dots) ; GQisQualIndexLoc:long_name = "System QC flag" ; GQisQualIndexLoc:units = "none" ; GQisQualIndexLoc:scale_factor = 1.0d ; GQisQualIndexLoc:add_offset = 0.0d ; GQisQualIndexLoc:parameter_type = "IASI data" ; GQisQualIndexLoc:valid_range = 0.0f, 9999.0f ; GQisQualIndexLoc:_FillValue = -9999.0f ; float GQisQualIndexRad(Number_of_Dice,Number_of_Dots) ; GQisQualIndexRad:long_name = "System QC flag" ; GQisQualIndexRad:units = "none" ; GQisQualIndexRad:scale_factor = 1.0d ; GQisQualIndexRad:add_offset = 0.0d ; GQisQualIndexRad:parameter_type = "IASI data" ; GQisQualIndexRad:valid_range = 0.0f, 9999.0f ; GQisQualIndexRad:_FillValue = -9999.0f ; float GQisQualIndexSpect(Number_of_Dice,Number_of_Dots) ; GQisQualIndexSpect:long_name = "System QC flag" ; GQisQualIndexSpect:units = "none" ; GQisQualIndexSpect:scale_factor = 1.0d ; GQisQualIndexSpect:add_offset = 0.0d ; GQisQualIndexSpect:parameter_type = "IASI data" ; GQisQualIndexSpect:valid_range = 0.0f, 9999.0f ; GQisQualIndexSpect:_FillValue = -9999.0f ; float GQisSysTecSondQual(Number_of_Dice,Number_of_Dots) ; GQisSysTecSondQual:long_name = "System QC flag" ; GQisSysTecSondQual:units = "none" ; GQisSysTecSondQual:scale_factor = 1.0d ; GQisSysTecSondQual:add_offset = 0.0d ; GQisSysTecSondQual:parameter_type = "IASI data" ; GQisSysTecSondQual:valid_range = 0.0f, 9999.0f ; GQisSysTecSondQual:_FillValue = -9999.0f ; double Time(Number_of_Dice,Number_of_Dots) ; Time:long_name = "UTC Milliseconds since Jan 1, 1970" ; Time:units = "msec" ; Time:scale_factor = 1.0d ; Time:add_offset = 0.0d ; Time:parameter_type = "IASI data" ; Time:valid_range = 0.0f, 1577836800000.0f ; Time:_FillValue = -9999.0 ; float Latitude(Number_of_Dice,Number_of_Dots) ; Latitude:long_name = "IASI Latitude values for each FOV" ; Latitude:units = "degrees North" ; Latitude:scale_factor = 1.0d ; Latitude:add_offset = 0.0d ; Latitude:parameter_type = "IASI data" ; Latitude:valid_range = 90.0f, -90.0f ; Latitude:_FillValue = -9999.0f ; float Longitude(Number_of_Dice,Number_of_Dots) ; Longitude:long_name = "IASI Longitude values for each FOV" ; Longitude:units = "degrees East" ; Longitude:scale_factor = 1.0d ; Longitude:add_offset = 0.0d ; Longitude:parameter_type = "IASI data" ; Longitude:valid_range = -180.0f, 179.99f ; Longitude:_FillValue = -9999.0f ; float IASI_Radiances(Number_of_Dice,Number_of_Dots,Number_of_IASI_Channels) ; IASI_Radiances:long_name = "IASI Radiances for each FOV" ; IASI_Radiances:units = "mW/m2/cm-1/sr" ; IASI_Radiances:scale_factor = 1.0d ; IASI_Radiances:add_offset = 0.0d ; IASI_Radiances:parameter_type = "IASI data" ; IASI_Radiances:valid_range = 0.0f, 40000.0f ; IASI_Radiances:_FillValue = -9999.0f ; float IASI_Image(Number_of_Dice,Number_of_IASI_Image_Pixels) ; IASI_Image:long_name = "IASI Image for each FOR" ; IASI_Image:units = "mW/m2/cm-1/sr" ; IASI_Image:scale_factor = 1.0d ; IASI_Image:add_offset = 0.0d ; IASI_Image:parameter_type = "IASI data" ; IASI_Image:valid_range = 0.0f, 40000.0f ; IASI_Image:_FillValue = -9999.0f ; short AVHRR_Channel_Combo(Number_of_Dice,Number_of_Dots) ; AVHRR_Channel_Combo:long_name = "AVHRR Channels used in radiance analysis" ; AVHRR_Channel_Combo:units = "none" ; AVHRR_Channel_Combo:scale_factor = 1 ; AVHRR_Channel_Combo:add_offset = 0 ; AVHRR_Channel_Combo:parameter_type = "IASI data" ; AVHRR_Channel_Combo:valid_range = 0, 1 ; AVHRR_Channel_Combo:_FillValue = -9999s ; float Fraction_of_Clear_AVHRR(Number_of_Dice,Number_of_Dots,Number_of_AVHRR _FOV_Classes) ; Fraction_of_Clear_AVHRR:long_name = "Percent clear for each AVHRR FOV class" ; Fraction_of_Clear_AVHRR:units = "%" ; Fraction_of_Clear_AVHRR:scale_factor = 1.0d ; Fraction_of_Clear_AVHRR:add_offset = 0.0d ; Fraction_of_Clear_AVHRR:parameter_type = "AVHRR data" ; Fraction_of_Clear_AVHRR:valid_range = 0.0f, 100.0f ; Fraction_of_Clear_AVHRR:_FillValue = -9999.0f ; float AVHRR_Y_Angle_Center_of_Gravity(Number_of_Dice,Number_of_Dots,Number_of_AVHRR_ FOV_Classes) ; AVHRR_Y_Angle_Center_of_Gravity:long_name = "Y angular position of the center of gravity" ; AVHRR_Y_Angle_Center_of_Gravity:units = "degrees" ; AVHRR_Y_Angle_Center_of_Gravity:scale_factor = 1.0d ; AVHRR_Y_Angle_Center_of_Gravity:add_offset = 0.0d ; AVHRR_Y_Angle_Center_of_Gravity:parameter_type = "AVHRR data" ; AVHRR_Y_Angle_Center_of_Gravity:valid_range = 0.0f, 360.0f ; AVHRR_Y_Angle_Center_of_Gravity:_FillValue = -9999.0f ; float AVHRR_Z_Angle_Center_of_Gravity(Number_of_Dice,Number_of_Dots,Number_of_AVHRR_ FOV_Classes) ; AVHRR_Z_Angle_Center_of_Gravity:long_name = "Z angular position of the center of gravity" ; AVHRR_Z_Angle_Center_of_Gravity:units = "degrees" ; AVHRR_Z_Angle_Center_of_Gravity:scale_factor = 1.0d ; AVHRR_Z_Angle_Center_of_Gravity:add_offset = 0.0d ; AVHRR_Z_Angle_Center_of_Gravity:parameter_type = "AVHRR data" ; AVHRR_Z_Angle_Center_of_Gravity:valid_range = 0.0f, 360.0f ; AVHRR_Z_Angle_Center_of_Gravity:_FillValue = -9999.0f ; float AVHRR_Mean_Radiances(Number_of_Dice,Number_of_Dots,Number_of_AVHRR_FOV_ Classes,Number_of_AVHRR_Channels) ; AVHRR_Mean_Radiances:long_name = "Mean AVHRR radiances for each FOV" ; AVHRR_Mean_Radiances:units = "mW/m2/cm-1/sr" ; AVHRR_Mean_Radiances:scale_factor = 1.0d ; AVHRR_Mean_Radiances:add_offset = 0.0d ; AVHRR_Mean_Radiances:parameter_type = "AVHRR data" ; AVHRR_Mean_Radiances:valid_range = 0.0f, 40000.0f ; AVHRR_Mean_Radiances:_FillValue = -9999.0f ; float AVHRR_Std_Radiances(Number_of_Dice,Number_of_Dots,Number_of_AVHRR_FOV_ Classes,Number_of_AVHRR_Channels) ; AVHRR_Std_Radiances:long_name = "Standard deviation of radiances for each FOV" ; AVHRR_Std_Radiances:units = "mW/m2/cm-1/sr" ; AVHRR_Std_Radiances:scale_factor = 1.0d ; AVHRR_Std_Radiances:add_offset = 0.0d ; AVHRR_Std_Radiances:parameter_type = "AVHRR data" ; AVHRR_Std_Radiances:valid_range = 0.0f, 40000.0f ; AVHRR_Std_Radiances:_FillValue = -9999.0f ; float View_Angle(Number_of_Dice,Number_of_Dots) ; View_Angle:long_name = "IASI View Angles for each FOV" ; View_Angle:units = "degrees" ; View_Angle:scale_factor = 1.0d ; View_Angle:add_offset = 0.0d ; View_Angle:parameter_type = "IASI data" ; View_Angle:valid_range = -90.0f, 90.0f ; View_Angle:_FillValue = -9999.0f ; float Satellite_Height(Number_of_Dice,Number_of_Dots) ; Satellite_Height:long_name = "Satellite height above each FOV" ; Satellite_Height:units = "km" ; Satellite_Height:scale_factor = 1.0 ; Satellite_Height:add_offset = 0.0 ; Satellite_Height:parameter_type = "IASI data" ; Satellite_Height:valid_range = 0.0f, 1000.0f ; Satellite_Height:_FillValue = -9999.0f ; float Satellite_Zenith(Number_of_Dice,Number_of_Dots) ; Satellite_Zenith:long_name = "Satellite zenith angles for each FOV" ; Satellite_Zenith:units = "degrees" ; Satellite_Zenith:scale_factor = 1.0 ; Satellite_Zenith:add_offset = 0.0 ; Satellite_Zenith:parameter_type = "IASI data" ; Satellite_Zenith:valid_range = 0.0f, 90.0f ; Satellite_Zenith:_FillValue = -9999.0f ; float Satellite_Azimuth(Number_of_Dice,Number_of_Dots) ; Satellite_Azimuth:long_name = "Satellite azimuth angles for each FOV" ; Satellite_Azimuth:units = "degrees" ; Satellite_Azimuth:scale_factor = 1.0 ; Satellite_Azimuth:add_offset = 0.0 ; Satellite_Azimuth:parameter_type = "IASI data" ; Satellite_Azimuth:valid_range = 0.0f, 180.0f ; Satellite_Azimuth:_FillValue = -9999.0f ; float Solar_Zenith(Number_of_Dice, Number_of_Dots) ; Solar_Zenith:long_name = "Solar zenith angles for each FOV" ; Solar_Zenith:units = "degrees" ; Solar_Zenith:scale_factor = 1.0 ; Solar_Zenith:add_offset = 0.0 ; Solar_Zenith:parameter_type = "IASI data" ; Solar_Zenith:valid_range = 0.f, 90.f ; Solar_Zenith:_FillValue = -9999.f ; float Solar_Azimuth(Number_of_Dice, Number_of_Dots) ; Solar_Azimuth:long_name = "Solar azimuth angles for each FOV" ; Solar_Azimuth:units = "degrees" ; Solar_Azimuth:scale_factor = 1.0 ; Solar_Azimuth:add_offset = 0.0 ; Solar_Azimuth:parameter_type = "IASI data" ; Solar_Azimuth:valid_range = 0.f, 180.f ; Solar_Azimuth:_FillValue = -9999.f ; short Ascending_Descending(Number_of_Dice, Number_of_Dots) ; Ascending_Descending:long_name = "0=Descending, 1=Ascending" ; Ascending_Descending:units = "none" ; Ascending_Descending:scale_factor = 1 ; Ascending_Descending:add_offset = 0 ; Ascending_Descending:parameter_type = "IASI data" ; Ascending_Descending:valid_range = 0, 1 ; Ascending_Descending:_FillValue = -9999s ; long Orbit_Number(Number_of_Dice,Number_of_Dots) ; Orbit_Number:long_name = "The number of the current orbit" ; Orbit_Number:units = "none" ; Orbit_Number:scale_factor = 1.0d ; Orbit_Number:add_offset = 0.0d ; Orbit_Number:parameter_type = "IASI data" ; Orbit_Number:valid_range = 1.0f, 100000.0f ; Orbit_Number:_FillValue = -9999 ; |
| --- | --- |

The information about the tools a user must use to manipulate a NetCDF file, could be found at: http://www.unidata.ucar.edu/software/netcdf/

### Access

These files are created in the following directory:

$BASE/SATELLITE_DATA/MetOpA/NRT_DATA/${Year}/${Month}/${Day}/IASI_DATA/Granule-${Granule_Number}/level1c

where:

${Year} = the 4-digit year

${Month} = 2-digit month

${Day} = 2-digit day of month

${Granule_Number} = 3-digit granule number (1-480)

These files are not maintained after processing.

## IASI L1CT Thinned Subset Files

IASI L1CT NetCDF thinned (616 channels) granule files (subset according to the scheme specified in the input CDL template).

### Purpose

- To generate IASI L1CT BUFR granule file

- To generate globally gridded data sets for validation and climate reprocessing

  - To generate daily 0.5*2 global grids of thinned RR and PCS generated from 1 band

- To generate daily 0.5*2 global grids of thinned RR and PCS generated from 3 bands

- To generate daily 0.5*2 global grids of thinned IASI radiances.

- To generate global binary data sets for validation and to use as an input for the global matchups.

  - To generate a global coverage binary file of thinned

coverage using the 616 channel set.

### Data File Description

Table 6. Thinned NetCDF File Header

| Data file-naming Convention | iasi_ncep_616_$YYYYMMDD_Granule-$GGG.nc where: 616 = is the channel subset (i.e. 616 channels) $YYYYMMDD = 8-digit year month day format (e.g. 20070517) $GGG = the 3-digit granule number (e.g. 088). The granule number can go from 001 to 480 |
| --- | --- |
| Array dimension variables Variables* | Number_of_Dice = 660 ; // Number dice written Number_of_Dots = 1 ; // Number of IASI FOVS in a die Number_of_IASI_Channels = 616 ; // Number of IASI Channels Number_of_IASI_Frequencies = 616 ; // Number of IASI Clear Frequencies Number_of_AVHRR_Channels = 6; // Number of AVHRR channels Number_of_AVHRR_FOV_Classes = 7; // Number of AVHRR sounder FOV classes Number_of_AVHRR_Frequencies = 6; Number_of_IASI_Image_Pixels = 4096; // 64 X 64 Pixel IASI image |

*  All variables in this file are the same as for the full resolution NetCDF file

(see Table 4).

The information about the tools a user must use to manipulate a NetCDF file could be found at: http://www.unidata.ucar.edu/software/netcdf/

### Access

These files are created in the following directory:

$BASE/SATELLITE_DATA/MetOpA/NRT_DATA/${Year}/${Month}/${Day}/IASI_DATA/Granule-${Granule_Number}/level1c

where:

${Year} = the 4-digit year

${Month} = 2-digit month

${Day} = 2-digit day of month

${Granule_Number} = 3-digit granule number (1-480)

These files are not maintained after processing.

## IASI Daily Full Global File

Global binary file for 8461 channels with the all IASI FOVs from each FOR.

Global binary file for 15 AMSU-A channels with the all AMSU-A FOVs.

Global binary file for 5 MHS channels with the all MHS FOVs.

Global binary file for all level 2 profiles and all IASI fields of regard.

### Purpose

These four global binary files for IASI L1C, AMSU-A, MHS, and IASI L2 are generated from the full resolution NetCDF files for their respective instruments.  These are required downstream as inputs to the Global Matchups unit.

### Data File Description

Each of these global binary files contains exactly the same number of records.  Each record, in turn, represents all the data for a single field of regard.  Therefore, any given record number (footprint) in one file corresponds to the same record number (footprint) in any other file.  To maintain this correspondence, missing scans/footprints, if they occur, are added as placeholders.  This correspondence is necessary for the functionality of the matchups.

The date information in the file names is defined as:

${Year} = the 4-digit year

${Month} = 2-digit month

${Day} = 2-digit day of month

Each record in the file contains the data for a single IASI FOV. All the variables are scalar values unless array length is shown. These are direct access binary files. Below are the variables in binary file record in the order they appear in the record:

Table 7 IASI Global Binariy Header Record Number 1

| Variable | Description | Type | Size | Dim Length |
| --- | --- | --- | --- | --- |
| Actual_Number_of_Records | Total number of records in the file including the 2 header records | Integer | 4 | 1 |
| Record_Length | Number of bytes per record | Integer | 4 | 1 |
| Number_of_Dots | The number of IASI FOV/FOR. This is always = 4 | Integer | 4 | 1 |
| Number_of_Dice | This is the actual number of IASI field of regard clusters | Integer | 4 | 1 |
| Number_of_IASI_Channels | The number of IASI channels (8461) | Integer | 4 | 1 |
| Number_of_AVHRR_Channels | The number of AVHRR channels (6) | Integer | 4 | 1 |
| Number_of_AVHRR_FOV_Classes | The number of AVHRR FOV classes (7) | Integer | 4 | 1 |
| IASI_Channels | The IASI channel numbers (1-8461) | Integer | 4 | 8461 |
| AVHRR_Channels | The AVHRR channel numbers (1-6) | Integer | 4 | 6 |
| AVHRR_Frequencies | The AVHRR channel frequencies (cm-1). | Real | 4 | 6 |
| AVHRR_FOV_Classes | The AVHRR FOV classes (1-7) | Integer | 4 | 7 |

Table 8 IASI Global Binary Header Record Number 2

| Variable | Description | Type | Size | Dim Length |
| --- | --- | --- | --- | --- |
| IASI_Frequencies | The IASI channel frequencies (cm-1) | Real | 4 | 8461 |

Table 9 IASI Global Binary Data Record

| Variable | Description | Type | Size | Dim Length |
| --- | --- | --- | --- | --- |
| The following block of variables is repeated 4 times. Each block represents the data for 1 of the 4 IASI FOVs. 4 blocks constitute 1 IASI binary data record. |
| Scan_Line | Scan line number from the source granule | Integer | 4 | 1 |
| AMSU_FOV | The AMSU footprint number (1-690) within the granule. | Integer | 4 | 1 |
| IASI_FOV | The IASI field of view number within the field of regard (1-4) | Integer | 4 | 1 |
| Latitude | The latitudes of each IASI FOV (± 90 degrees). | Real | 4 | 1 |
| Longitude | The longitudes of each IASI FOV (± 180 degrees). | Real | 4 | 1 |
| Footprint | The IASI field of regard footprint number (1-30) along the scan line. | Integer | 4 | 1 |
| View_Angle | The view angles of each IASI FOV (± 90 degrees). | Real | 4 | 1 |
| Satellite_Height | The satellite height of each IASI FOV (km). | Real | 4 | 1 |
| Satellite_Zenith | The satellite zenith of each IASI FOV (0 - 90 degrees). | Real | 4 | 1 |
| Satellite_Azimuth | The satellite azimuth of each IASI FOV (0-180 degrees). | Real | 4 | 1 |
| Solar_Zenith | The solar zenith of each IASI FOV (0-90 degrees). | Real | 4 | 1 |
| Solar_Azimuth | The solar azimuth of each IASI FOV (0-180 degrees). | Real | 4 | 1 |
| Ascending_Descending | The ascending-descending status of each IASI FOV (0 = ascending, 1=descending). | Integer | 4 | 1 |
| Orbit_Number | The number of the orbit (since launch) from which the current granule was obtained. | Integer | 4 | 1 |
| GQisFlagQual | The QC flag of each IASI FOV (0=good, 1=bad). | Integer | 4 | 1 |
| GQisQualIndex | The sounder spectra QC index of each IASI FOV. | Real | 4 | 1 |
| GQisQualIndexLoc | The IASI/AVHRR collocation index of each IASI FOV. | Real | 4 | 1 |
| GQisQualIndexRad | The radiometric QC flag of each IASI FOV. | Real | 4 | 1 |
| GQisQualIndexSpect | The spectral quality index of each IASI FOV. | Real | 4 | 1 |
| GQisSysTecSondQual | The sounder quality index of each IASI FOV. | Real | 4 | 1 |
| IASI_Radiances | The IASI radiances (mW/m2/cm-1/sr). | Real | 4 | 8461 |
| AVHRR_Mean_Radiances | The mean AVHRR radiances (mW/m2/cm-1/sr). | Real | 4 | 6*7 |
| AVHRR_Std_Radiances | The standard deviation of the AVHRR radiances (mW/m2/cm-1/sr). | Real | 4 | 6*7 |
| IASI_Image | IASI sub-pixel image radiances (mW/m2/cm-1/sr). | Real | 4 | 32*32 |

Table 10 AMSU-A Global Binary Header Record Number 1

| Variable | Description | Type | Size | Dim Length |
| --- | --- | --- | --- | --- |
| Actual_Number_of_Records | Total number of records in the file including the 2 header records | Integer | 4 | 1 |
| Record_Length | Number of bytes per record | Integer | 4 | 1 |
| Number_of_Dice | This is the actual number of AMSU-A observations | Integer | 4 | 1 |
| Number_of_AMSUA_Channels | The number of AMSUA channels (15) | Integer | 4 | 1 |
| AMSUA_Channels | The AMSUA channel numbers (1-15) | Integer | 4 | 15 |

Table 11 AMSU-A Global Binary Header Record Number 2

| Variable | Description | Type | Size | Dim Length |
| --- | --- | --- | --- | --- |
| AMSUA_Frequencies | The AMSUA channel frequencies (cm-1) | Real | 4 | 15 |

Table 12 AMSU-A Global Binary Data Record

| Variable | Description | Type | Size | Dim Length |
| --- | --- | --- | --- | --- |
| Scan_Line | Scan line number from the source granule | Integer | 4 | 1 |
| Footprint | The AMSU footprint number (1-30) along the scan line. | Integer | 4 | 1 |
| AMSU_FOV | The AMSU field of view number within the granule (1-690) | Integer | 4 | 1 |
| Latitude | The latitudes of each AMSU-A FOV (± 90 degrees). | Real | 4 | 1 |
| Longitude | The longitudes of each AMSU-A FOV (± 180 degrees). | Real | 4 | 1 |
| View_Angle | The view angles of each AMSU-A FOV (± 90 degrees). | Real | 4 | 1 |
| Satellite_Height | The satellite height of each AMSU-A FOV (km). | Real | 4 | 1 |
| Satellite_Zenith | The satellite zenith of each AMSU-A FOV (0 - 90 degrees). | Real | 4 | 1 |
| Satellite_Azimuth | The satellite azimuth of each AMSU-A FOV (0-180 degrees). | Real | 4 | 1 |
| Solar_Zenith | The solar zenith of each AMSU-A FOV (0-90 degrees). | Real | 4 | 1 |
| Solar_Azimuth | The solar azimuth of each AMSU-A FOV (0-180 degrees). | Real | 4 | 1 |
| Ascending_Descending | The ascending-descending status of each AMSU-A FOV (0 = ascending, 1=descending). | Integer | 4 | 1 |
| AMSUA_Radiances | The AMSU-A radiances (mW/m2/cm-1/sr). | Real | 4 | 15 |
| Quality_Flag | The AMSU-A Quality Flag (0=good, else bad). | Integer | 4 | 15 |

Table 13 MHS Global Binary Header Record Number 1

| Variable | Description | Type | Size | Dim Length |
| --- | --- | --- | --- | --- |
| Actual_Number_of_Records | Total number of records in the file including the 2 header records | Integer | 4 | 1 |
| Record_Length | Number of bytes per record | Integer | 4 | 1 |
| Number_of_Dots | The total number of MHS FOVs with each data record. | Integer | 4 | 1 |
| Number_of_Dice | This is the actual number of MHS field of regard clusters. | Integer | 4 | 1 |
| Number_of_MHS_Channels | The number of MHS channels (5) | Integer | 4 | 1 |
| MHS_Channels | The MHS channel numbers (1-5) | Integer | 4 | 5 |

Table 14 MHS Global Binary Header Record Number 2

| Variable | Description | Type | Size | Dim Length |
| --- | --- | --- | --- | --- |
| MHS_Frequencies | The MHS channel frequencies (cm-1) | Real | 4 | 5 |

Table 15 MHS Global Binary Data Record

| Variable | Description | Type | Size | Dim Length |
| --- | --- | --- | --- | --- |
| The following block of variables is repeated 9 times. Each block represents the data for 1 of the 9 MHS FOVs. 9 blocks constitute 1 MHS binary data record. |
| Scan_Line | MHS scan line number from the source granule (1-69) | Integer | 4 | 1 |
| Footprint | The MHS footprint number (1-90) along the scan line. | Integer | 4 | 1 |
| AMSU_FOV | The AMSU field of view number within the granule (1-690) | Integer | 4 | 1 |
| MHS_FOV | The MHS field of view number within the AMSU field of view (1-9) | Integer | 4 | 1 |
| Latitude | The latitudes of each MHS FOV (± 90 degrees). | Real | 4 | 1 |
| Longitude | The longitudes of each MHS FOV (± 180 degrees). | Real | 4 | 1 |
| View_Angle | The view angles of each MHS FOV (± 90 degrees). | Real | 4 | 1 |
| Satellite_Height | The satellite height of each MHS FOV (km). | Real | 4 | 1 |
| Satellite_Zenith | The satellite zenith of each MHS FOV (0 - 90 degrees). | Real | 4 | 1 |
| Satellite_Azimuth | The satellite azimuth of each MHS FOV (0-180 degrees). | Real | 4 | 1 |
| Solar_Zenith | The solar zenith of each MHS FOV (0-90 degrees). | Real | 4 | 1 |
| Solar_Azimuth | The solar azimuth of each MHS FOV (0-180 degrees). | Real | 4 | 1 |
| Ascending_Descending | The ascending-descending status of each MHS FOV (0 = ascending, 1=descending). | Integer | 4 | 1 |
| MHS_Radiances | The MHS radiances (mW/m2/cm-1/sr). | Real | 4 | 5 |
| Quality_Flag | The MHS Quality Flag (0=good, else bad). | Integer | 4 | 5 |

NOTE: There is only 1 IASI L2 header record….

Table 16 IASI L2 Global Binary Header Record Number 1

| Variable | Description | Type | Size | Dim Length |
| --- | --- | --- | --- | --- |
| Actual_Number_of_Records | Total number of records in the file including the 1 header record | Integer | 4 | 1 |
| Record_Length | Number of bytes per record | Integer | 4 | 1 |
| Number_of_Dice | This is the actual number of IASI L2 observations. | Integer | 4 | 1 |
| Number_of_P_Levels | The number of pressure levels | Integer | 4 | 1 |
| Number_of_MW_Spectral_Pts | The number of microwave spectral points | Integer | 4 | 1 |
| Number_of_Surf_Emis_Hinge_Pts | The number of surface emissivity hinge points | Integer | 4 | 1 |
| Number_of_Cloud_Emis_Hinge_Pts | The number of cloud emissivity hinge points | Integer | 4 | 1 |
| Number_of_Cloud_Layers | The number of cloud layers | Integer | 4 | 1 |

Table 17 IASI L2 Global Binary Data Record

| Variable | Description | Type | Size | Dim Length |
| --- | --- | --- | --- | --- |
| AMSU_FOV | The AMSU field of view number within the granule (1-690) | Integer | 4 | 1 |
| Latitude | The latitudes of each IASI FOR (± 90 degrees). | Real | 4 | 1 |
| Longitude | The longitudes of each IASI FOR (± 180 degrees). | Real | 4 | 1 |
| View_Angle | The view angles of each IASI FOR (± 90 degrees). | Real | 4 | 1 |
| Satellite_Height | The satellite height of each IASI FOR (km). | Real | 4 | 1 |
| Solar_Zenith | The solar zenith of each IASI FOR (0-90 degrees). | Real | 4 | 1 |
| Ascending_Descending | The ascending-descending status of each IASI FOR (0 = ascending, 1=descending). | Integer | 4 | 1 |
| Topography | The height of the surface above sea level (meters). | Real | 4 | 1 |
| Land_Fraction | The fraction of land coverage (0-1). | Real | 4 | 1 |
| Surface_Pressure | Surface pressure in millibars. | Real | 4 | 1 |
| Skin_Temperature | Skin temperature in Kelvin. | Real | 4 | 1 |
| Mean_CO2 | Mean CO2 in ppm. | Real | 4 | 1 |
| MW_Surface_Class | Microwave surface class. | Integer | 4 | 1 |
| MW_Surface_Emis | Microwave surface emissivity. | Real | 4 | 1 |
| Bottom_Level_Index | The index of the pressure array that marks the pressure at the surface. | Integer | 4 | 1 |
| N_Smw_Per_FOV | The number of microwave spectral points within each layer | Integer | 4 | 1 |
| nemis_Per_FOV | The number of surface emissivity hinge points within each layer | Integer | 4 | 1 |
| ncemis_Per_FOV | The number of cloud emssivity hinge points within each layer | Integer | 4 | 1 |
| ncld_Per_FOV | The number of cloud layers points within each layer | Integer | 4 | 1 |
| Quality_Flag | Retrieval quality flag (0=accept, 1=reject). | Integer | 4 | 1 |
| The following block of 2 variables is repeated Number_of_Cloud_Layers (nominally 8) times. The user of these data must check the header to obtain the value of Number_of_Cloud_Layers. |
| Cloud_Top_Pressure | Cloud top pressure in millibars. | Real | 4 | 1 |
| Cloud_Top_Fraction | Cloud top fractional coverage (0-1). | Real | 4 | 1 |
| The following block of 12 variables is repeated Number_of_P_Levels (nominally 100) times. The user of these data must check the header to obtain the value of Number_of_P_Levels. |
| Pressure | Pressure with the current layer in millibars. | Real | 4 | 1 |
| Temperature | Temperature within the current layer in Kelvin | Real | 4 | 1 |
| H2O | H2O layer column density. | Real | 4 | 1 |
| O3 | O3 layer column density (molecules/cm2). | Real | 4 | 1 |
| Liquid_H2O | Liquid H2O layer column density (molecules/cm2). | Real | 4 | 1 |
| Ice_Liquid_Flag | Ice liquid flag (0=water, 1=ice). | Integer | 4 | 1 |
| CO | O3 layer column density (molecules/cm2). | Real | 4 | 1 |
| CH4 | O3 layer column density (molecules/cm2). | Real | 4 | 1 |
| CO2 | CO2 mixing ratio (ppm). | Real | 4 | 1 |
| N2O | N2O layer column density (molecules/cm2). | Real | 4 | 1 |
| SO2 | SO2 layer column density (molecules/cm2). | Real | 4 | 1 |
| HNO3 | HNO3 layer column density (molecules/cm2). | Real | 4 | 1 |
| The following block of 2 variables is repeated Number_of_MW_Spectral_Pts (nominally 16) times. The user of these data must check the header to obtain the value of Number_of_MW_Spectral_Pts. |
| MW_Frequency | Microwave frequency (cm-1). | Real | 4 | 1 |
| MW_Emis | Microwave emissivity. | Real | 4 | 1 |
| The following block of 3 variables is repeated Number_of_Surf_Emis_Hinge_Pts (nominally 100) times. The user of these data must check the header to obtain the value of Number_of_Surf_Emis_Hinge_Pts. |
| IR_Emis_Freq | Infrared emissivity hinge point frequencies (cm-1). | Real | 4 | 1 |
| IR_Surface_Emis | Infrared surface emissivity | Real | 4 | 1 |
| IR_Surface_Refl | Infrared surface reflectances (percent). | Real | 4 | 1 |
| The following block of 3 variables is repeated Number_of_Cloud_Emis_Hinge_Pts (nominally 100) times. The user of these data must check the header to obtain the value of Number_of_Cloud_Emis_Hinge_Pts. |
| The following block of 3 variables is repeated Number_of_Cloud_Layers (nominally 8) times. The user of these data must check the header to obtain the value of Number_of_Cloud_Layers. |
| Cloud_Freq | Cloud infrared frequencies (cm-1). | Real | 4 | 1 |
| Cloud_Refl | Cloud infrared reflectivity. | Real | 4 | 1 |
| Cloud_Emis | Cloud infrared emissivity. | Real | 4 | 1 |

### Access

Global binary file for 8461 channels with the all IASI FOVs from each FOR  resides at:

$BASE/SATELLITE_DATA/MetOpA/NRT_DATA/${Year}/${Month}/${Day}/IASI_DATA/Global_Binaries/FullRes_Global_Binaries/iasi_all_8461_${Year}${Month}${Day}.binary

Global binary file for 15 AMSU-A channels with the all AMSU-A FOVs resides at:

$BASE/SATELLITE_DATA/MetOpA/NRT_DATA/${Year}/${Month}/${Day}/IASI_DATA/Global_Binaries/AMSUA_Global_Binaries/amsua_all_fov_all_chan_${Year}${Month}${Day}.binary

Global binary file for 5 MHS channels with the all MHS FOVs resides at:

$BASE/SATELLITE_DATA/MetOpA/NRT_DATA/${Year}/${Month}/${Day}/IASI_DATA/Global_Binaries/MHS_Global_Binaries/mhs_all_fov_all_chan_${Year}${Month}${Day}.binary

Global binary file for all level 2 profiles and all IASI fields of regard resides at:

$BASE/SATELLITE_DATA/MetOpA/NRT_DATA/${Year}/${Month}/${Day}/IASI_DATA/Global_Binaries/L2_Global_Binaries/iasi_l2_${Year}${Month}${Day}.binary

These files are not maintained after the processing.

## Daily Full Global Location Files

IASI single daily full global coverage binary file containing only the locations and times of all FOVs from each FOR.

AMSU-A single daily full global binary file containing only the locations and times of all FOVs from each FOR.

MHS single daily full global binary file containing only the locations and times of all FOVs from each FOR.

Global binary file containing only the locations and times of all FOVs from each FOR

### Purpose

These files are used for the matchup processing.

### Data File Description

These are direct access binary files. These files have only 3 variables:

Time

Latitude

Longitude

### These files have four records header, the same as for the full global binary files.

Access

IASI single daily full global coverage binary file containing only the locations and times of all FOVs from each FOR resides at:

$BASE/SATELLITE_DATA/MetOpA/NRT_DATA/${Year}/${Month}/${Day}/IASI_DATA/Global_Binaries/FullRes_Global_Binaries/iasi_all_8461_${Year}${Month}${Day}_locs.binary

AMSU-A single daily full global binary file containing only the locations and times of all FOVs from each FOR resides at:

$BASE/SATELLITE_DATA/MetOpA/NRT_DATA/${Year}/${Month}/${Day}/IASI_DATA/Global_Binaries/AMSUA_Global_Binaries/amsua_all_fov_all_chan_${Year}${Month}${Day}_locs.binary

MHS single daily full global binary file containing only the locations and times of all FOVs from each FOR resides at:

$BASE/SATELLITE_DATA/MetOpA/NRT_DATA/${Year}/${Month}/${Day}/IASI_DATA/Global_Binaries/MHS_Global_Binaries/mhs_all_fov_all_chan_${Year}${Month}${Day}_locs.binary

Global binary file containing only the locations and times of all FOVs from each FOR resides at:

$BASE/SATELLITE_DATA/MetOpA/NRT_DATA/${Year}/${Month}/${Day}/IASI_DATA/Global_Binaries/L2_Global_Binaries/iasi_l2_${Year}${Month}${Day}_locs.binary

These files are not maintained after the processing.

AMSU-A Level 1B NetCDF Granule Files

Purpose

These files are converted to the retrieval input binary format in the L1B Processing unit.  Therefore, they are indirectly needed by the L2 Processing Unit.  These files are also used directly in the Global Grids and Global Binaries Units.

Data File Description

The following NetCDF file is produced for each granule with the following name structure.

amsua_all_fov_all_chan_${Year}${Month}${Day}_Granule-${Granule_Number}.nc

where:

$Year = 4-digit year

$Month = 2-digit month

$Day = 2-digit day

$Granule_Number = 3-digit granule number

This is full spatial and spectral resolution file.  Its starting and ending scan lines and footprints match those of the full resolution IASI Level 1C NetCDF files for the same granule number described above.

Table 18 AMSU-A Level 1B Net CDF File Header

| dimensions: variables: | Number_of_AMSU_FOVs = 660 ; // Number FOV written per granule Number_of_AMSUA_Channels = 15 ; // Total number of AMSU-A Channels Number_of_AMSUA_Frequencies = 15 ; // Total number of AMSU-A Frequencies long AMSUA_Channels(Number_of_AMSUA_Channels) ; AMSUA_Channels:long_name = "Channel number for data" ; AMSUA_Channels:units = "none" ; AMSUA_Channels:scale_factor = 1.0d ; AMSUA_Channels:add_offset = 0.0d ; AMSUA_Channels:parameter_type = "AMSUA data" ; AMSUA_Channels:valid_range = 1.0f, 15.0f ; AMSUA_Channels:_FillValue = -9999 ; float AMSUA_Frequencies(Number_of_AMSUA_Frequencies) ; AMSUA_Frequencies:long_name = "Frequency at which the data is taken" ; AMSUA_Frequencies:units = "wavenumber cm-1" ; AMSUA_Frequencies:scale_factor = 1.0d ; AMSUA_Frequencies:add_offset = 0.0d ; AMSUA_Frequencies:parameter_type = "AMSUA data" ; AMSUA_Frequencies:valid_range = 0.0f, 10000.0f ; AMSUA_Frequencies:_FillValue = -9999.0f ; long AMSU_FOV(Number_of_AMSU_FOVs) ; AMSU_FOV:long_name = "The index of the AMSU FOV in the granule" ; AMSU_FOV:units = "none" ; AMSU_FOV:scale_factor = 1.0d ; AMSU_FOV:add_offset = 0.0d ; AMSU_FOV:parameter_type = "AMSUA data" ; AMSU_FOV:valid_range = 1.0f, 660.0f ; AMSU_FOV:_FillValue = -9999 ; long Scan_Line(Number_of_AMSU_FOVs) ; Scan_Line:long_name = "The number of the current scan line" ; Scan_Line:units = "none" ; Scan_Line:scale_factor = 1.0d ; Scan_Line:add_offset = 0.0d ; Scan_Line:parameter_type = "AMSUA data" ; Scan_Line:valid_range = 1.0f, 22.0f ; Scan_Line:_FillValue = -9999 ; long Footprint(Number_of_AMSU_FOVs) ; Footprint:long_name = "The number of the current AMSU FOV on the scan line" ; Footprint:units = "none" ; Footprint:scale_factor = 1.0d ; Footprint:add_offset = 0.0d ; Footprint:parameter_type = "AMSUA data" ; Footprint:valid_range = 1.0f, 30.0f ; Footprint:_FillValue = -9999 ; double Time(Number_of_AMSU_FOVs) ; Time:long_name = "UTC Milliseconds since Jan 1, 1970" ; Time:units = "msec" ; Time:scale_factor = 1.0d ; Time:add_offset = 0.0d ; Time:parameter_type = "AMSUA data" ; Time:valid_range = 0.0f, 1577836800000.0f ; Time:_FillValue = -9999.0 ; float Latitude(Number_of_AMSU_FOVs) ; Latitude:long_name = "AMSUA Latitude values for each FOV" ; Latitude:units = "degrees North" ; Latitude:scale_factor = 1.0d ; Latitude:add_offset = 0.0d ; Latitude:parameter_type = "AMSUA data" ; Latitude:valid_range = 90.0f, -90.0f ; Latitude:_FillValue = -9999.0f ; float Longitude(Number_of_AMSU_FOVs) ; Longitude:long_name = "AMSUA Longitude values for each FOV" ; Longitude:units = "degrees East" ; Longitude:scale_factor = 1.0d ; Longitude:add_offset = 0.0d ; Longitude:parameter_type = "AMSUA data" ; Longitude:valid_range = -180.0f, 179.99f ; Longitude:_FillValue = -9999.0f ; float AMSUA_Radiances(Number_of_AMSU_FOVs,Number_of_AMSUA_Channels) ; AMSUA_Radiances:long_name = "AMSUA Radiances for each FOV" ; AMSUA_Radiances:units = "mW/m2/cm-1/sr" ; AMSUA_Radiances:scale_factor = 1.0d ; AMSUA_Radiances:add_offset = 0.0d ; AMSUA_Radiances:parameter_type = "AMSUA data" ; AMSUA_Radiances:valid_range = 0.0f, 40000.0f ; AMSUA_Radiances:_FillValue = -9999.0f ; short Quality_Flag(Number_of_AMSU_FOVs,Number_of_AMSUA_Channels) ; Quality_Flag:long_name = "AMSUA Quality_Flag for each channel per FOV" ; Quality_Flag:units = "none" ; Quality_Flag:scale_factor = 1 ; Quality_Flag:add_offset = 0 ; Quality_Flag:parameter_type = "AMSUA data" ; Quality_Flag:valid_range = 0, 1 ; Quality_Flag:_FillValue = -9999s ; float View_Angle(Number_of_AMSU_FOVs) ; View_Angle:long_name = "AMSUA View Angles for each FOV" ; View_Angle:units = "degrees" ; View_Angle:scale_factor = 1.0d ; View_Angle:add_offset = 0.0d ; View_Angle:parameter_type = "AMSUA data" ; View_Angle:valid_range = -90.0f, 90.0f ; View_Angle:_FillValue = -9999.0f ; float Satellite_Height(Number_of_AMSU_FOVs) ; Satellite_Height:long_name = "Satellite height above each FOV" ; Satellite_Height:units = "km" ; Satellite_Height:scale_factor = 1.0 ; Satellite_Height:add_offset = 0.0 ; Satellite_Height:parameter_type = "AMSUA data" ; Satellite_Height:valid_range = 0.0f, 1000.0f ; Satellite_Height:_FillValue = -9999.0f ; float Satellite_Zenith(Number_of_AMSU_FOVs) ; Satellite_Zenith:long_name = "Satellite zenith angles for each FOV" ; Satellite_Zenith:units = "degrees" ; Satellite_Zenith:scale_factor = 1.0 ; Satellite_Zenith:add_offset = 0.0 ; Satellite_Zenith:parameter_type = "AMSUA data" ; Satellite_Zenith:valid_range = 0.0f, 90.0f ; Satellite_Zenith:_FillValue = -9999.0f ; float Satellite_Azimuth(Number_of_AMSU_FOVs) ; Satellite_Azimuth:long_name = "Satellite azimuth angles for each FOV" ; Satellite_Azimuth:units = "degrees" ; Satellite_Azimuth:scale_factor = 1.0 ; Satellite_Azimuth:add_offset = 0.0 ; Satellite_Azimuth:parameter_type = "AMSUA data" ; Satellite_Azimuth:valid_range = 0.0f, 180.0f ; Satellite_Azimuth:_FillValue = -9999.0f ; float Solar_Zenith(Number_of_AMSU_FOVs) ; Solar_Zenith:long_name = "Solar zenith angles for each FOV" ; Solar_Zenith:units = "degrees" ; Solar_Zenith:scale_factor = 1.0 ; Solar_Zenith:add_offset = 0.0 ; Solar_Zenith:parameter_type = "AMSUA data" ; Solar_Zenith:valid_range = 0.f, 90.f ; Solar_Zenith:_FillValue = -9999.f ; float Solar_Azimuth(Number_of_AMSU_FOVs) ; Solar_Azimuth:long_name = "Solar azimuth angles for each FOV" ; Solar_Azimuth:units = "degrees" ; Solar_Azimuth:scale_factor = 1.0 ; Solar_Azimuth:add_offset = 0.0 ; Solar_Azimuth:parameter_type = "AMSUA data" ; Solar_Azimuth:valid_range = 0.f, 180.f ; Solar_Azimuth:_FillValue = -9999.f ; short Ascending_Descending(Number_of_AMSU_FOVs) ; Ascending_Descending:long_name = "0=Descending, 1=Ascending" ; Ascending_Descending:units = "none" ; Ascending_Descending:scale_factor = 1 ; Ascending_Descending:add_offset = 0 ; Ascending_Descending:parameter_type = "AMSUA data" ; Ascending_Descending:valid_range = 0, 1 ; Ascending_Descending:_FillValue = -9999s ; |
| --- | --- |

Access

The AMSU-A Level 1B NetCDF granule files are generated from main_amsua_level1b.  The input files are the NOAA Level 1B orbital files.  This program is part of the L1B Processing Unit.  These files are created in the following directory:

$BASE/SATELLITE_DATA/MetOpA/NRT_DATA/${Year}/${Month}/${Day}/IASI_DATA/Granule-${Granule_Number}/level1b

where:

${Year} = the 4-digit year

${Month} = 2-digit month

${Day} = 2-digit day of month

${Granule_Number} = 3-digit granule number (1-480)

MHS Level 1B NetCDF Granule Files

Purpose

These files are converted to the retrieval input binary format in the L1B Processing unit.  Therefore, they are indirectly needed by the L2 Processing Unit.  These files are also used directly in the Global Grids and Global Binaries Units.

Data File Description

The following NetCDF files are produced for each granule with the following name structure.

mhs_all_fov_all_chan_${Year}${Month}${Day}_Granule-${Granule_Number}.nc

where:

$Year = 4-digit year

$Month = 2-digit month

$Day = 2-digit day

$Granule_Number = 3-digit granule number

These are full spatial and spectral resolution files.  Their starting and ending scan lines and footprints match those of the full resolution IASI Level 1C NetCDF files for the same granule number described above.

Table 19 MHS Level 1B NetCDF File Header

| dimensions: variables: | Number_of_AMSU_FOVs = 660 ; // Number AMSU FOVs written per granule Number_of_MHS_FOVs = 9 ; // Number of MHS FOVs per AMSU FOV Number_of_MHS_Channels = 5 ; // Total number of MHS Channels Number_of_MHS_Frequencies = 5 ; // Total number of MHS Frequencies long MHS_Channels(Number_of_MHS_Channels) ; MHS_Channels:long_name = "Channel number for data" ; MHS_Channels:units = "none" ; MHS_Channels:scale_factor = 1.0d ; MHS_Channels:add_offset = 0.0d ; MHS_Channels:parameter_type = "MHS data" ; MHS_Channels:valid_range = 1.0f, 5.0f ; MHS_Channels:_FillValue = -9999 ; float MHS_Frequencies(Number_of_MHS_Frequencies) ; MHS_Frequencies:long_name = "Frequency at which the data is taken" ; MHS_Frequencies:units = "wavenumber cm-1" ; MHS_Frequencies:scale_factor = 1.0d ; MHS_Frequencies:add_offset = 0.0d ; MHS_Frequencies:parameter_type = "MHS data" ; MHS_Frequencies:valid_range = 0.0f, 10000.0f ; MHS_Frequencies:_FillValue = -9999.0f ; long MHS_FOV(Number_of_MHS_FOVs) ; MHS_FOV:long_name = "The index of the MHS FOV in the AMSU FOV" ; MHS_FOV:units = "none" ; MHS_FOV:scale_factor = 1.0d ; MHS_FOV:add_offset = 0.0d ; MHS_FOV:parameter_type = "MHS data" ; MHS_FOV:valid_range = 1.0f, 9.0f ; MHS_FOV:_FillValue = -9999 ; long AMSU_FOV(Number_of_AMSU_FOVs) ; AMSU_FOV:long_name = "The index of the AMSU FOV in the granule" ; AMSU_FOV:units = "none" ; AMSU_FOV:scale_factor = 1.0d ; AMSU_FOV:add_offset = 0.0d ; AMSU_FOV:parameter_type = "AMSU data" ; AMSU_FOV:valid_range = 1.0f, 660.0f ; AMSU_FOV:_FillValue = -9999 ; long Scan_Line(Number_of_AMSU_FOVs,Number_of_MHS_FOVs) ; Scan_Line:long_name = "The number of the current MHS scan line" ; Scan_Line:units = "none" ; Scan_Line:scale_factor = 1.0d ; Scan_Line:add_offset = 0.0d ; Scan_Line:parameter_type = "MHS data" ; Scan_Line:valid_range = 1.0f, 66.0f ; Scan_Line:_FillValue = -9999 ; long Footprint(Number_of_AMSU_FOVs,Number_of_MHS_FOVs) ; Footprint:long_name = "The number of the current MHS FOV on the scan line" ; Footprint:units = "none" ; Footprint:scale_factor = 1.0d ; Footprint:add_offset = 0.0d ; Footprint:parameter_type = "AMSUA data" ; Footprint:valid_range = 1.0f, 90.0f ; Footprint:_FillValue = -9999 ; double Time(Number_of_AMSU_FOVs,Number_of_MHS_FOVs) ; Time:long_name = "UTC Milliseconds since Jan 1, 1970" ; Time:units = "msec" ; Time:scale_factor = 1.0d ; Time:add_offset = 0.0d ; Time:parameter_type = "MHS data" ; Time:valid_range = 0.0f, 1577836800000.0f ; Time:_FillValue = -9999.0 ; float Latitude(Number_of_AMSU_FOVs,Number_of_MHS_FOVs) ; Latitude:long_name = "MHS Latitude values for each MHS FOV" ; Latitude:units = "degrees North" ; Latitude:scale_factor = 1.0d ; Latitude:add_offset = 0.0d ; Latitude:parameter_type = "MHS data" ; Latitude:valid_range = 90.0f, -90.0f ; Latitude:_FillValue = -9999.0f ; float Longitude(Number_of_AMSU_FOVs,Number_of_MHS_FOVs) ; Longitude:long_name = "MHS Longitude values for each MHS FOV" ; Longitude:units = "degrees East" ; Longitude:scale_factor = 1.0d ; Longitude:add_offset = 0.0d ; Longitude:parameter_type = "MHS data" ; Longitude:valid_range = -180.0f, 179.99f ; Longitude:_FillValue = -9999.0f ; float MHS_Radiances(Number_of_AMSU_FOVs,Number_of_MHS_FOVs,Number_of_MHS_Channels) ; MHS_Radiances:long_name = "MHS Radiances for each MHS FOV" ; MHS_Radiances:units = "mW/m2/cm-1/sr" ; MHS_Radiances:scale_factor = 1.0d ; MHS_Radiances:add_offset = 0.0d ; MHS_Radiances:parameter_type = "MHS data" ; MHS_Radiances:valid_range = 0.0f, 40000.0f ; MHS_Radiances:_FillValue = -9999.0f ; short Quality_Flag(Number_of_AMSU_FOVs,Number_of_MHS_FOVs,Number_of_MHS_Channels) ; Quality_Flag:long_name = "MHS Quality_Flag for each channel per MHS FOV" ; Quality_Flag:units = "none" ; Quality_Flag:scale_factor = 1 ; Quality_Flag:add_offset = 0 ; Quality_Flag:parameter_type = "MHS data" ; Quality_Flag:valid_range = 0, 1 ; Quality_Flag:_FillValue = -9999s ; float View_Angle(Number_of_AMSU_FOVs,Number_of_MHS_FOVs) ; View_Angle:long_name = "MHS View Angles for each MHS FOV" ; View_Angle:units = "degrees" ; View_Angle:scale_factor = 1.0d ; View_Angle:add_offset = 0.0d ; View_Angle:parameter_type = "MHS data" ; View_Angle:valid_range = -90.0f, 90.0f ; View_Angle:_FillValue = -9999.0f ; float Satellite_Height(Number_of_AMSU_FOVs,Number_of_MHS_FOVs) ; Satellite_Height:long_name = "Satellite height above each MHS FOV" ; Satellite_Height:units = "km" ; Satellite_Height:scale_factor = 1.0 ; Satellite_Height:add_offset = 0.0 ; Satellite_Height:parameter_type = "MHS data" ; Satellite_Height:valid_range = 0.0f, 1000.0f ; Satellite_Height:_FillValue = -9999.0f ; float Satellite_Zenith(Number_of_AMSU_FOVs,Number_of_MHS_FOVs) ; Satellite_Zenith:long_name = "Satellite zenith angles for each MHS FOV" ; Satellite_Zenith:units = "degrees" ; Satellite_Zenith:scale_factor = 1.0 ; Satellite_Zenith:add_offset = 0.0 ; Satellite_Zenith:parameter_type = "MHS data" ; Satellite_Zenith:valid_range = 0.0f, 90.0f ; Satellite_Zenith:_FillValue = -9999.0f ; float Satellite_Azimuth(Number_of_AMSU_FOVs,Number_of_MHS_FOVs) ; Satellite_Azimuth:long_name = "Satellite azimuth angles for each MHS FOV" ; Satellite_Azimuth:units = "degrees" ; Satellite_Azimuth:scale_factor = 1.0 ; Satellite_Azimuth:add_offset = 0.0 ; Satellite_Azimuth:parameter_type = "MHS data" ; Satellite_Azimuth:valid_range = 0.0f, 180.0f ; Satellite_Azimuth:_FillValue = -9999.0f ; float Solar_Zenith(Number_of_AMSU_FOVs,Number_of_MHS_FOVs) ; Solar_Zenith:long_name = "Solar zenith angles for each MHS FOV" ; Solar_Zenith:units = "degrees" ; Solar_Zenith:scale_factor = 1.0 ; Solar_Zenith:add_offset = 0.0 ; Solar_Zenith:parameter_type = "MHS data" ; Solar_Zenith:valid_range = 0.f, 90.f ; Solar_Zenith:_FillValue = -9999.f ; float Solar_Azimuth(Number_of_AMSU_FOVs,Number_of_MHS_FOVs) ; Solar_Azimuth:long_name = "Solar azimuth angles for each MHS FOV" ; Solar_Azimuth:units = "degrees" ; Solar_Azimuth:scale_factor = 1.0 ; Solar_Azimuth:add_offset = 0.0 ; Solar_Azimuth:parameter_type = "MHS data" ; Solar_Azimuth:valid_range = 0.f, 180.f ; Solar_Azimuth:_FillValue = -9999.f ; short Ascending_Descending(Number_of_AMSU_FOVs,Number_of_MHS_FOVs) ; Ascending_Descending:long_name = "0=Descending, 1=Ascending" ; Ascending_Descending:units = "none" ; Ascending_Descending:scale_factor = 1 ; Ascending_Descending:add_offset = 0 ; Ascending_Descending:parameter_type = "MHS data" ; Ascending_Descending:valid_range = 0, 1 ; Ascending_Descending:_FillValue = -9999s ; |
| --- | --- |

Access

The AMSU-A and MHS Level 1B NetCDF granule files are generated from main_mhs_level1b.  The input files are the NOAA Level 1B orbital files.  This program is part of the L1B Processing Unit.  These files are created in the following directory:

$BASE/SATELLITE_DATA/MetOpA/NRT_DATA/${Year}/${Month}/${Day}/IASI_DATA/Granule-${Granule_Number}/level1b

where:

${Year} = the 4-digit year

${Month} = 2-digit month

${Day} = 2-digit day of month

${Granule_Number} = 3-digit granule number (1-480)

Retrieval Input/Output Files

Purpose

These are purely intermediate files which are not distributed to any users. The retrieval input format files are used in L2 Retrieval Processing Unit (see Figures 2 and 6).  Retrieval output files are used in the same unit to generate L2 and CCR NetCDF files.

Data File Description

There are five input files required by the retrieval.  These are all binary sequential access files for IASI L1C, AMSU-A, MHS, and GFS surface pressure.

These files have the following name structures and are stored in the following subdirectories, respectively:

/level1c/iasi_all_8461_${Year}${Month}${Day}_Granule-${Granule_Number}.binary

/level1b/amsua_all_fov_all_chan_${Year}${Month}${Day}_Granule-${Granule_Number}.binary

/level1b/mhs_all_fov_all_chan_${Year}${Month}${Day}_Granule-${Granule_Number}.binary

/level2/avntest_${Year}${Month}${Day}_${Granule_Number}.bin

/level2/avntest_${Year}${Month}${Day}_${Granule_Number}b.bin

There are a number of retrieval output files which are generated in the level2 directory:

$BASE/SATELLITE_DATA/MetOpA/NRT_DATA/${Year}/${Month}/${Day}/IASI_DATA/Granule-${Granule_Number}/level2

${Year}${Month}${Day}_${Granule_Number}_bin_0002.ccr

${Year}${Month}${Day}_${Granule_Number}_bin_0002.f61

${Year}${Month}${Day}_${Granule_Number}_bin_0002.f69

${Year}${Month}${Day}_${Granule_Number}_bin_0002.ret

${Year}${Month}${Day}_${Granule_Number}_bin_iasi_l2_retrieval.bin

${Year}${Month}${Day}_${Granule_Number}_bin_iasi_l2_retrieval.f70

${Year}${Month}${Day}_${Granule_Number}_bin_iasi_l2_retrieval.f95

${Year}${Month}${Day}_${Granule_Number}_bin_iasi_l2_retrieval.out

The retrieval profile output is located in:

${Year}${Month}${Day}_${Granule_Number}_bin_0002.ret

This file contains retrievals of temperature, moisture, and trace gases.  The CCR file is:

${Year}${Month}${Day}_${Granule_Number}_bin_0002.ccr

These radiances are identical to the original IASI radiance except the effects of clouds have been removed.

All the other files are diagnostic files and are therefore not used for any products downstream.

Access

Retrieval input/output files could be found in following directories:

$BASE/SATELLITE_DATA/MetOpA/NRT_DATA/${Year}/${Month}/${Day}/IASI_DATA/Granule-${Granule_Number}/level1

$BASE/SATELLITE_DATA/MetOpA/NRT_DATA/${Year}/${Month}/${Day}/IASI_DATA/Granule-${Granule_Number}/level2

# Output Data Sets

Output datasets are described in this section. To get a sense of where these files fit within the IASI PPS, the reader is referred to section 1, Figures 1-10. Table 19 (a, b, c) provides a summary description of the output files including their source, data and product type, contents, time period, resolution, spectral and spatial subsets, and format.

Table 20. Output Files

| Instrument | File Type | Contents | Format |
| --- | --- | --- | --- |
| IASI | EUMETSAT PFS IASI L1C | IASI Radiance | EUMETSAT Binary |
| IASI | IASI L1C, L2, CCR granule metadata file | IASI metadata (FGDC-RSE) | xml |
| IASI | EUMRTSAT IASI Level 2 data files | Temperature and moisture profiles | BUFR |

| Contents | Spectral Subset | Data type | Spatial Subset | Format |
| --- | --- | --- | --- | --- |
| IASI radiance | 616 channels | IASI radiance | Warmest FOV from every ROR | BUFR |
| IASI radiance | 616 channels | IASI radiance | First FOV from every FOR | BUFR |
| IASI radiance | 616 channels | IASI radiance | All 9 FOVs from every FOR | BUFR |
| FOV = Field of View; FOR = Field of Regard; |

| Contents | Data Type | Time period | Product Type | Resolution | Format |
| --- | --- | --- | --- | --- | --- |
| IASI Radiances | Radiances | Daily | Global grids | 3*3 | Gridded Binary |
| IASI Radiances | Radiances | Daily | Global grids | 0.5*2 | Gridded Binary |
| IASI RR/PCS | RR/PCS | Daily | Global grids | 3*3 | Gridded Binary |
| IASI RR/PCS | RR/PCS | Daily | Global grids | 0.5*2 | Gridded Binary |
| IASI GFS Radiances/Forecast | Radiances/Forecast | Daily | Global grids | 0.5*2 | Gridded Binary |
| IASI GDAS Radiances/Forecast | Radiances/Forecast | Daily | Global grids | 0.5*2 | Gridded Binary |
| AMSU-A Radiances | Radiances | Daily | Global grids | 3*3 | Griddes Binary |
| AMSU-A Radiances | Radiances | Daily | Global grids | 0.5*2 | Gridded Binary |
| MHS Radiances | Radiances | Daily | Global Grids | 3*3 | Gridded Binary |
| MHS Radiances | Radiances | Daily | Global grids | 0.5*2 | Gridded Binary |
| IASI L2 | Profiles | Daily | Global grids | 3*3 | Gridded Binary |
| IASI L2 | Profiles | Daily | Global grids | 0.5*2 | Gridded Binary |
| IASI CCR | Radiances | Daily | Global grids | 0.5*2 | Gridded Binary |
| IASI Matchups | Radiances | Daily | Matchups (Radiosondes) | N/A | Binary and NetCDF |
| IASI Thinned Radiances | Radiances | Daily | Thinned data | 2 scans/granule | Binary |
| AMSU-A Matchups | Radiances | Daily | Matchups (Radiosondes) | N/A | Binary |
| MHS Matchups | Radiances | Daily | Matchups (Radiosondes) | N/a | Binary |
| IASI L2 Matchups | Profiles | Daily | Matchups | 100 levels | Binary |
| IASI L2 | Profiles | Daily |  | 100 levels | NetCDF |
| IASI CCR | Radiances | Daily |  |  | NetCDF, BUFR |

## IASI L1C Granule Files

The EUMETSAT PFC IASI L1C binary granule files.

### Purpose

EUMETSAT IASI L1C data are transferred by the NOAA/NESDIS/STAR near real time processing system to the OSDPD DDS for retrieval by CLASS.

### Data File Description

These files are also input files. They are described in the section 2.1.2 of this document. Specific file details (and more about data and header records) can be found in:

EPS PROGRAMME IASI Level 1 Product Format Specifications, Ref: EUM.EPS.SYS.SPE.990003,Issue 6, Rev 6, WEB number 270000, 03/23/2004, EUMETSAT. 
For the EUMETSAT L1C PFS format refer to the section "GIADR-QUALITY", "GIADR-SCALE FACTORS", and "MDR-1C" in the Appendix "IASI-L1-PFS-6.6-ANNEX" in the document “EPS PROGRAMME IASI Level 1 Product Format Specifications, Ref: EUM.EPS.SYS.SPE.990003,Issue 6, Rev 6, WEB number 270000, 03/23/2004, EUMETSAT”.

EPS Programme Generic Product Format Specification, Ref: EPS.GGS.SPE.96167, Issue 6, Rev 4, WEB number 270000, 02/11/2003, EUMETSAT.

### Intended Users

CLASS

POC: John Bates

Chief, Remote Sensing and Applications Division

NOAA / NESDIS / National Climatic Data Center (NCDC) / Remote Sensing and Applications Division (RSAD)

Asheville, NC

Phone: (828) 271-4378

Fax: (828) 271-4328

Address: 151 Patton Avenue, Room 516 D Ashville, NC 28801

### Access

This file is located at Data Distribution Server:

dds.nesdis.noaa.gov:push

POC – Nichols, Catherine L

5200 Auth Road, Room 0315, Building: FB4

Suitland, MD 20746 – 4301

Phone: (301)457-5245

Fax:      (301)457-5199

E-mail: cathy.nichols@noaa.gov

NESDIS/CLASS (2006) Producer Archive Submission Agreement for IASI Products.  CLASS-1135-CLS-AGR-IASI.  X080.

## IASI Level 1C Granule-Level Metadata

The granule-level metadata files associated with the EUMETSAT IASI Level 1C data.

### Purpose

The metadata files are pushed to the DDS by the STAR near real time processing system.  This system runs in OSDPD operations.  CLASS will access the DDS in accordance with Producer-Archive Submission Agreement for IASI Products. These granule files are also used to generate subset data products to be distributed for operational use by the NWS and the Department of Defense (DOD).

### Data File Description

### This file is generated from the granule metadata template (IASI_Granule_Metadata_Template.xml) in by the Check L1C unit.

### These are Federal Geographic Data Committee Remote Sensing Extension (FGDC-RSE) compliant xml format files.  There is one metadata file for every L1C PFS file.  These metadata files have the same name structure as their associated product files except with an .xml extension.

Table 21. Metadata File Name Convention and Format

| Metadata file-naming Convention | IASI_xxx_1C_M02_${Sensing_Start}Z_${Sensing_End}Z_${P}_${D}_${Processing_Time_Start}Z__${Unknown_Date_String}.xml Where: IASI = Instrument xxx = hard-coded value 1C = Processing level M02 = Satellite Sensing_Start = the starting time of observations given in the following format YYYYMODDHHMMSSZ Sensing_End = the ending time of observations given as YYYYMODDHHMMSSZ $P = Processing mode $D = Disposition mode Processing_Time_Start = the processing time for the observations given as YYYYMODDHHMMSSZ xml = An extension indicating that the file is an xml format file The string “YYYYMODDHHMMSSZ” is a date string containing the following components of time: YYYY = 4 digit year (e.g. 2005) MO = 2 digit month (01-12) DD = day of month (01-31) HH = hour (00-23) MM = minute (00-59) SS = seconds (00-59) Z = Greenwich Mean Time The variable $P can have any of the following values: N = nominal B = backlog R = reprocessing V = validation The variable $D may have any of the following values: T = testing O = operational C = commissioning |
| --- | --- |
| Metadata file format | This is an eXtensible Markup Language (XML) format file using the FGDC Remote Sensing Extension content standard. |
| Expected metadata file size | ~12 KB |

References:

- Content Standard for Digital Geospatial Metadata: Extensions for Remote Sending Metadata, FGDC-STD-012-2002.

b.	FGDC (1998) Content Standard for Digital Geospatial Metadata, VERSION 2, FGDC-                              STD-001-1998.

More information about these data sets could be found in Metadata Description Document (NESDIS/STAR, 2008b).

### Intended Users

CLASS

POC: John Bates

Chief, Remote Sensing and Applications Division

NOAA / NESDIS / National Climatic Data Center (NCDC) / Remote Sensing and Applications Division (RSAD)

Asheville, NC

Phone: (828) 271-4378

Fax: (828) 271-4328

Address: 151 Patton Avenue, Room 516 D Ashville, NC 28801

### Access

A given granule metadata file resides in the same directory as its associated product file at:

### $BASE/SATELLITE_DATA/MetOpA/NRT_DATA/${Year}/${Month}/${Day}/IASI_DATA/Granule-${Granule_Number}/level1c

This file is located at Data Distribution Server:

dds.nesdis.noaa.gov:push

POC – Nichols, Catherine L

5200 Auth Road, Room 0315, Building: FB4

Suitland, MD 20746 – 4301

Phone: (301)457-5245

Fax:      (301)457-5199

E-mail: cathy.nichols@noaa.gov

## IASI L1CT BUFR granule files

IASI L1CT BUFR granule files.

(Subset according to the scheme specified in the input CDL template).

### Purpose

The BUFR files are L1C subset files generated for use by NWP centers.

The BUFR files are transferred to the DDS and pulled by the NWP centers.  These data are then used for assimilation in numerical models.

### Data File Description

The file structure is based on the content of the BUFR table.  Nominally there are 480 of these files per day.  They are generated from the NetCDF subset files by the program main_iasi_netcdf_to_bufr which resides in the L1C Subsetter unit (figure 4).

Table 22. IASI L1CT Granule Files Subset

| Spectral subset | Spatial subset | Data Type |
| --- | --- | --- |
| 616 channels 616 channels 616 channels | Warmest FOV from every FOR First FOV from every FOR All 9 FOV from every FOR | IASI radiances IASI radiances IASI radiances |

The output BUFR file names have the following name structure (Table 23).

Table 23. IASI L1C BUFR Granule File Name Structure

| File-naming Convention | NPR_IARD.M02_D${Year}${Doy}_S${Hour}${Minute}${Second}_E${Hour}${Minute) ${Second}_G${Granule_Number}_C${Channels}_U${Subset} Where: NPR = Near realtime processing IARD = IASI radiances M02 = MetOp2 D = Date S = Starting time E = Ending time G = Granule C = Channels U = Subset indicator $Year = 2-digit year $Doy = 3-digit day of year (1-365) $Hour = 2-digit hour $Minute = 2-digit minute $Second = 2-digit second $Granule = 3-digit granule number (1-480) $Channels = Channel subset (e.g. 616 or 8461) $Subset = FOV subset indicator (1, 3, 6, ...) |
| --- | --- |

BUFR table, needed to read IASI L1C BUFR granule files, is presented in Appendix A. BUFR encoding template for IASI L1C files is shown below.

| index | descriptor | description | value | meaning |
| --- | --- | --- | --- | --- |
| 0 | 0-01-007 | satellite id | 3 | METOP1 |
| 1 | 0-01-031 | id of originating centre | 254 | EUMETSAT |
| 2 | 0-02-019 | satellite instrument | 221 | IASI |
| 3 | 0-02-020 | satellite classification | 61 | EPS |
| 4 | 0-04-001 | year |  |  |
| 5 | 0-04-002 | month |  |  |
| 6 | 0-04-003 | day |  |  |
| 7 | 0-04-004 | hour |  |  |
| 8 | 0-04-005 | minute |  |  |
| 9 | 2-02-131 | change scale +3 |  |  |
| 10 | 2-01-138 | change width +10 |  |  |
| 11 | 0-04-006 | second |  |  |
| 12 | 2-01-000 | change width to default |  |  |
| 13 | 2-02-000 | change scale to default |  |  |
| 14 | 0-05-001 | latitude (high accuracy) |  |  |
| 15 | 0-06-001 | longitude (high accuracy) |  |  |
| 16 | 0-07-024 | Satellite zenith |  |  |
| 17 | 0-05-021 | Satellite azimuth |  |  |
| 18 | 0-07-025 | Solar zenith |  |  |
| 19 | 0-05-022 | Solar azimuth |  |  |
| 20 | 0-05-043 | Pixel number |  |  |
| 21 | 0-05-040 | Orbit number |  |  |
| 22 | 2-01-133 | change width +5 |  |  |
| 23 | 0-05-041 | Scan line number | missing |  |
| 24 | 2-01-000 | change width to default |  |  |
| 25 | 2-01-132 | change width +4 |  |  |
| 26 | 0-25-070 | Frame count / granule number | missing |  |
| 27 | 2-01-000 | change width to default |  |  |
| 28 | 2-02-126 | change scale -2 |  |  |
| 29 | 0-07-001 | Height of station |  |  |
| 30 | 2-02-000 | change scale to default |  |  |
| 31 | 0-33-192 | GQisFlagQual |  |  |
| 32 | 0-33-193 | QGisQualIndex |  |  |
| 33 | 0-33-194 | QGisQualIndexLoc |  |  |
| 34 | 0-33-195 | QGisQualIndexRad |  |  |
| 35 | 0-33-196 | QGisQualIndexSpect |  |  |
| 36 | 0-33-197 | GQisSysTecSondQual |  |  |
| 37 | 1-03-010 | Repeat next 3 descriptors 10 times |  |  |
| 38 | 0-25-192 | Start channel |  |  |
| 39 | 0-25-193 | End channel |  |  |
| 40 | 0-25-194 | Channel scale factor |  |  |
| 41 | 1-05-087 | Repeat next 5 descriptors 87 times |  |  |
| 42 | 1-04-100 | Repeat next 4 descriptors 100 times |  |  |
| 43 | 2-01-136 | change width +8 |  |  |
| 44 | 0-05-042 | Channel number |  |  |
| 45 | 2-01-000 | change width to default |  |  |
| 46 | 0-14-192 | Scaled radiance |  |  |
| 47 | 0-02-019 | satellite instrument | 591 | AVHRR/3 |
| 48 | 0-25-051 | AVHRR channel combination |  |  |
| 49 | 1-09-007 | Repeat next 9 descriptors 7 times |  |  |
| 50 | 0-05-192 | Y angular position of centre of gravity |  |  |
| 51 | 0-05-193 | Z angular position of centre of gravity |  |  |
| 52 | 0-25-085 | Fractional coverage of AVHRR radiance cluster |  |  |
| 53 | 1-05-006 | Repeat next 5 descriptors 6 times |  |  |
| 54 | 0-05-042 | Channel number |  |  |
| 55 | 0-25-194 | Channel scale factor |  |  |
| 56 | 0-14-193 | Scaled mean radiance |  |  |
| 57 | 0-25-194 | Channel scale factor |  |  |
| 58 | 0-14-194 | Scaled standard deviation of radiance |  |  |

In the encoding sequence, 14 local descriptors have been used.  These are shaded in grey. These descriptors have been used to simplify the encoding process.  They will be defined in the coordinated BUFR tables as soon as possible.  The information with indices 50 and 51 has been added in order to give the relative position of the AVHRR cluster in the IASI field of view.

The software for reading BUFR files can be downloaded from the website: http://www.nco.ncep.noaa.gov/sib/decoders/BUFRLIB/

### Intended Users

NCEP; FNMOC/NRL; GMAO; JCSDA;

### Access

The files are created in the following directory:

$BASE/SATELLITE_DATA/MetOpA/NRT_DATA/${Year}/${Month}/${Day}/IASI_DATA/Granule-${Granule_Number}/level1c

where:

${Year} = the 4-digit year

${Month} = 2-digit month

${Day} = 2-digit day of month

${Granule_Number} = 3-digit granule number (1-480)

The BUFR files are distributed from these level 1c directories to the DDS where they are retrieved by customers:

dds.nesdis.noaa.gov:push

POC – Nichols, Catherine L

5200 Auth Road, Room 0315, Building: FB4

Suitland, MD 20746 – 4301

Phone: (301)457-5245

Fax:      (301)457-5199

E-mail: cathy.nichols@noaa.gov

## IASI Global 1-Band PC Grid Files

Ascending and descending daily gridded binary files.

(0.5 x 2.0 degree grids of thinned RR and PCS generated from 1 band).

### Purpose

These data sets are used for validation purposes and by STAR scientists for climate reprocessing activities.

### Data File Description

The Global Grids products are generated from daily sets of NetCDF files and run, operationally, one day behind real time processing. These are direct access daily binary files in a GRADS readable format. For a given grid product, the processing defines two grids at a specified resolution.  One grid is for observations, obtained during ascending orbits, and the other is for descending orbits. Each daily global grid product consists of one ascending and one descending file. The file-naming convention for the 0.5 x 2.0 1-band PC grids is:

NRT_IA1PC${YEAR}${MONTH}${DAY}.asc 
NRT_IA1PC${YEAR}${MONTH}${DAY}.desc

The content of the files with variable name list and their dimensions are as follows:

| Variable | Description | Type | Size | Dim Length |
| --- | --- | --- | --- | --- |
| YearMonthDay | Year/Month/Day string given as YYYYMMDD. | real | 4 | 91,720 |
| Time | Hours.Fractional_Minutes | Real | 4 | 91,720 |
| Grid_Latitude | Lat locations of the grid points (± 90 degrees) | Real | 4 | 91,720 |
| Grid_Longitude | Lon locations of the grid points (± 90 degrees) | Real | 4 | 91,720 |
| Instrument_Latitude | Lat locations of the actual observations (± 90 degrees) | Real | 4 | 91,720 |
| Instrument_Longitude | Lon locations of the actual observations (± 90 degrees) | Real | 4 | 91,720 |
| Granule_Number | Granule number | Real | 4 | 91,720 |
| View_Angle | The view angle of the current IASI FOV (± 90 degrees) | Real | 4 | 91,720 |
| Solar_Zenith | The solar zenith of the current IASI FOV (0-90 degrees) | Real | 4 | 91,720 |
| Solar_Azimuth | The solar azimuth of the current IASI FOV (0-180 degrees) | Real | 4 | 91,720 |
| Satellite_Zenith | The satellite zenith of the current IASI FOV (0-90 degrees) | Real | 4 | 91,720 |
| Satellite_Azimuth | The satellite azimuth of the current IASI FOV (0-180 degrees) | Real | 4 | 91,720 |
| Satellite_Height | The satellite height of the current IASI FOV (km) | Real | 4 | 91,720 |
| Principal_Components | Principal component | Real | 4 | 91,720,200 |
| PC_Scores | PC_Scores | Real | 4 | 91,720,1 |
| AVHRR_Mean_Radiances | The mean AVHRR radiances (mW/m2/cm-1/sr) | Real | 4 | 91,720,7,6 |
| AVHRR_Std_Radiances | The standard deviation of the AVHRR radiances (mW/m2/cm-1/sr) | Real | 4 | 91,720,7,6 |
| IASI_RR | Reconstructed radiances (mW/m2/cm-1/sr) | Real | 4 | 91,720,616 |
| IASI_RR_Quality_Flag | 0 = accepted, 1 = rejected | Real | 4 | 91,720,1 |
| Dice | IASI FOR (1-30) | Real | 4 | 91,720 |

The date information in the file names is defined as:

${Year} = the 4-digit year

${Month} = 2-digit month

${Day} = 2-digit day of month

### Intended Users

STAR validation scientists. STAR climate scientists.

### Access

These files reside at:

$BASE/SATELLITE_DATA/MetOpA/NRT_DATA/${Year}/${Month}/${Day}/IASI_DATA/Global_Grids/PC_Global_Grids_1Band/M02_IA1PC${Year}${Month}${Day}.asc

$BASE/SATELLITE_DATA/MetOpA/NRT_DATA/${Year}/${Month}/${Day}/IASI_DATA/Global_Grids/PC_Global_Grids_1Band/M02_IA1PC${Year}${Month}${Day}.desc

Files are sent to the DDS by the scripts that generate them.  All grids are pulled from the DDS by STAR into the STAR Collaborative Environment and stored locally.

dds.nesdis.noaa.gov:push

POC – Nichols, Catherine L

5200 Auth Road, Room 0315, Building: FB4

Suitland, MD 20746 – 4301

Phone: (301)457-5245

Fax:      (301)457-5199

E-mail: cathy.nichols@noaa.gov

## IASI Global 3-Band PC Grid Files

Ascending and descending daily gridded binary files.

(0.5 x 2.0 degree grids of thinned RR and PCS generated from 3                         bands).

### Purpose

These data sets are used for validation purposes and by STAR scientists for climate reprocessing activities.

### Data File Description

The Global Grids products are generated from daily sets of NetCDF files and run, operationally, one day behind real time processing. These are direct access daily binary files in a GRADS readable format. For a given grid product, the processing defines two grids at a specified resolution.  One grid is for observations, obtained during ascending orbits, and the other is for descending orbits. Each daily global grid product consists of one ascending and one descending file. The file-naming convention for the 0.5 x 2.0 3-band PC grids is:

NRT_IA3PC${YEAR}${MONTH}${DAY}.asc 
NRT_IA3PC${YEAR}${MONTH}${DAY}.desc

The content of the files with variable name list and their dimensions are as follows:

| Variable | Description | Type | Size | Dim Length |
| --- | --- | --- | --- | --- |
| YearMonthDay | Year/Month/Day string given as YYYYMMDD. | real | 4 | 91,720 |
| Time | Hours.Fractional_Minutes | Real | 4 | 91,720 |
| Grid_Latitude | Lat locations of the grid points (± 90 degrees) | Real | 4 | 91,720 |
| Grid_Longitude | Lon locations of the grid points (± 90 degrees) | Real | 4 | 91,720 |
| Instrument_Latitude | Lat locations of the actual observations (± 90 degrees) | Real | 4 | 91,720 |
| Instrument_Longitude | Lon locations of the actual observations (± 90 degrees) | Real | 4 | 91,720 |
| Granule_Number | Granule number | Real | 4 | 91,720 |
| View_Angle | The view angle of the current IASI FOV (± 90 degrees) | Real | 4 | 91,720 |
| Solar_Zenith | The solar zenith of the current IASI FOV (0-90 degrees) | Real | 4 | 91,720 |
| Solar_Azimuth | The solar azimuth of the current IASI FOV (0-180 degrees) | Real | 4 | 91,720 |
| Satellite_Zenith | The satellite zenith of the current IASI FOV (0-90 degrees) | Real | 4 | 91,720 |
| Satellite_Azimuth | The satellite azimuth of the current IASI FOV (0-180 degrees) | Real | 4 | 91,720 |
| Satellite_Height | The satellite height of the current IASI FOV (km) | Real | 4 | 91,720 |
| Principal_Components | Principal component | Real | 4 | 91,720,600 |
| PC_Scores | PC_Scores | Real | 4 | 91,720,3 |
| AVHRR_Mean_Radiances | The mean AVHRR radiances (mW/m2/cm-1/sr) | Real | 4 | 91,720,7,6 |
| AVHRR_Std_Radiances | The standard deviation of the AVHRR radiances (mW/m2/cm-1/sr) | Real | 4 | 91,720,7,6 |
| IASI_RR | Reconstructed radiances (mW/m2/cm-1/sr) | Real | 4 | 91,720,616 |
| IASI_RR_Quality_Flag | 0 = accepted, 1 = rejected | Real | 4 | 91,720,3 |
| Dice | IASI FOR (1-30) | Real | 4 | 91,720 |

The date information in the file names is defined as:

${Year} = the 4-digit year

${Month} = 2-digit month

${Day} = 2-digit day of month

### Intended Users

STAR validation scientists. STAR climate scientists.

### Access

These files reside at:

$BASE/SATELLITE_DATA/MetOpA/NRT_DATA/${Year}/${Month}/${Day}/IASI_DATA/Global_Grids/PC_Global_Grids_3Band/M02_IA3PC${Year}${Month}${Day}.asc

$BASE/SATELLITE_DATA/MetOpA/NRT_DATA/${Year}/${Month}/${Day}/IASI_DATA/Global_Grids/PC_Global_Grids_3Band/M02_IA3PC${Year}${Month}${Day}.desc

Files are sent to the DDS by the scripts that generate them.  All grids are pulled from the DDS by STAR into the STAR Collaborative Environment and stored locally.

dds.nesdis.noaa.gov:push

POC – Nichols, Catherine L

5200 Auth Road, Room 0315, Building: FB4

Suitland, MD 20746 – 4301

Phone: (301)457-5245

Fax:      (301)457-5199

E-mail: cathy.nichols@noaa.gov

## IASI Full Global 1-Band PC Grid Files

Ascending and descending daily gridded binary files.

(3.0 x 3.0 degree grids of thinned RR and PCS generated from 1 band).

### Purpose

These data sets are used for validation purposes and by STAR scientists for climate reprocessing activities.

### Data File Description

The Global Grids products are generated from daily sets of NetCDF files and run, operationally, one day behind real time processing. These are direct access daily binary files in a GRADS readable format.  For a given grid product, the processing defines two grids at a specified resolution.  One grid is for observations, obtained during ascending orbits, and the other is for descending orbits. Each daily global grid product consists of one ascending and one descending file. The file-naming convention for the 3.0 x 3.0 1-band PC grids is:

NRT_IAF1PC${YEAR}${MONTH}${DAY}.asc 
NRT_IAF1PC${YEAR}${MONTH}${DAY}.desc

The content of the files with variable name list and their dimensions are as follows:

| Variable | Description | Type | Size | Dim Length |
| --- | --- | --- | --- | --- |
| YearMonthDay | Year/Month/Day string given as YYYYMMDD. | real | 4 | 61,120,4 |
| Time | Hours.Fractional_Minutes | Real | 4 | 61,120,4 |
| Grid_Latitude | Lat locations of the grid points (± 90 degrees) | Real | 4 | 61,120,4 |
| Grid_Longitude | Lon locations of the grid points (± 90 degrees) | Real | 4 | 61,120,4 |
| Instrument_Latitude | Lat locations of the actual observations (± 90 degrees) | Real | 4 | 61,120,4 |
| Instrument_Longitude | Lon locations of the actual observations (± 90 degrees) | Real | 4 | 61,120,4 |
| Granule_Number | Granule number | Real | 4 | 61,120,4 |
| View_Angle | The view angle of the current IASI FOV (± 90 degrees) | Real | 4 | 61,120,4 |
| Solar_Zenith | The solar zenith of the current IASI FOV (0-90 degrees) | Real | 4 | 61,120,4 |
| Solar_Azimuth | The solar azimuth of the current IASI FOV (0-180 degrees) | Real | 4 | 61,120,4 |
| Satellite_Zenith | The satellite zenith of the current IASI FOV (0-90 degrees) | Real | 4 | 61,120,4 |
| Satellite_Azimuth | The satellite azimuth of the current IASI FOV (0-180 degrees) | Real | 4 | 61,120,4 |
| Satellite_Height | The satellite height of the current IASI FOV (km) | Real | 4 | 61,120,4 |
| Principal_Components | Principal component | Real | 4 | 61,120,4,200 |
| PC_Scores | PC_Scores | Real | 4 | 61,120,4,1 |
| AVHRR_Mean_Radiances | The mean AVHRR radiances (mW/m2/cm-1/sr) | Real | 4 | 61,120,4,7,6 |
| AVHRR_Std_Radiances | The standard deviation of the AVHRR radiances (mW/m2/cm-1/sr) | Real | 4 | 61,120,4,7,6 |
| IASI_RR | Reconstructed radiances (mW/m2/cm-1/sr) | Real | 4 | 61,120,4,616 |
| IASI_RR_Quality_Flag | 0 = accepted, 1 = rejected | Real | 4 | 61,120,4,1 |
| Dice | IASI FOR (1-30) | Real | 4 | 61,120,4 |

The date information in the file names is defined as:

${Year} = the 4-digit year

${Month} = 2-digit month

${Day} = 2-digit day of month

### Intended Users

STAR validation scientists. STAR climate scientists.

### Access

These files reside at:

$BASE/SATELLITE_DATA/MetOpA/NRT_DATA/${Year}/${Month}/${Day}/IASI_DATA/Global_Grids/PC_FullRes_Global_Grids_1Band/M02_IAF1PC${Year}${Month}${Day}.asc

$BASE/SATELLITE_DATA/MetOpA/NRT_DATA/${Year}/${Month}/${Day}/IASI_DATA/Global_Grids/PC_FullRes_Global_Grids_1Band/M02_IAF1PC${Year}${Month}${Day}.desc

Files are sent to the DDS by the scripts that generate them.  All grids are pulled from the DDS by STAR into the STAR Collaborative Environment and stored locally.

dds.nesdis.noaa.gov:push

POC – Nichols, Catherine L

5200 Auth Road, Room 0315, Building: FB4

Suitland, MD 20746 – 4301

Phone: (301)457-5245

Fax:      (301)457-5199

E-mail: cathy.nichols@noaa.gov

## IASI Full Global 3-Band PC Grid Files

Ascending and descending daily gridded binary files.

(3.0 x 3.0 degree grids of thinned RR and PCS generated from 3 band).

### Purpose

These data sets are used for validation purposes and by STAR scientists for climate reprocessing activities.

### Data File Description

The Global Grids products are generated from daily sets of NetCDF files and run, operationally, one day behind real time processing. These are direct access daily binary files in a GRADS readable format.  For a given grid product, the processing defines two grids at a specified resolution.  One grid is for observations, obtained during ascending orbits, and the other is for descending orbits. Each daily global grid product consists of one ascending and one descending file. The file-naming convention for the 3.0 x 3.0, 3-band PC grids is:

NRT_IAF3PC${YEAR}${MONTH}${DAY}.asc 
NRT_IAF3PC${YEAR}${MONTH}${DAY}.desc

The content of the files with variable name list and their dimensions are as follows:

| Variable | Description | Type | Size | Dim Length |
| --- | --- | --- | --- | --- |
| YearMonthDay | Year/Month/Day string given as YYYYMMDD. | real | 4 | 61,120,4 |
| Time | Hours.Fractional_Minutes | Real | 4 | 61,120,4 |
| Grid_Latitude | Lat locations of the grid points (± 90 degrees) | Real | 4 | 61,120,4 |
| Grid_Longitude | Lon locations of the grid points (± 90 degrees) | Real | 4 | 61,120,4 |
| Instrument_Latitude | Lat locations of the actual observations (± 90 degrees) | Real | 4 | 61,120,4 |
| Instrument_Longitude | Lon locations of the actual observations (± 90 degrees) | Real | 4 | 61,120,4 |
| Granule_Number | Granule number | Real | 4 | 61,120,4 |
| View_Angle | The view angle of the current IASI FOV (± 90 degrees) | Real | 4 | 61,120,4 |
| Solar_Zenith | The solar zenith of the current IASI FOV (0-90 degrees) | Real | 4 | 61,120,4 |
| Solar_Azimuth | The solar azimuth of the current IASI FOV (0-180 degrees) | Real | 4 | 61,120,4 |
| Satellite_Zenith | The satellite zenith of the current IASI FOV (0-90 degrees) | Real | 4 | 61,120,4 |
| Satellite_Azimuth | The satellite azimuth of the current IASI FOV (0-180 degrees) | Real | 4 | 61,120,4 |
| Satellite_Height | The satellite height of the current IASI FOV (km) | Real | 4 | 61,120,4 |
| Principal_Components | Principal component | Real | 4 | 61,120,4,200 |
| PC_Scores | PC_Scores | Real | 4 | 61,120,4,1 |
| AVHRR_Mean_Radiances | The mean AVHRR radiances (mW/m2/cm-1/sr) | Real | 4 | 61,120,4,7,6 |
| AVHRR_Std_Radiances | The standard deviation of the AVHRR radiances (mW/m2/cm-1/sr) | Real | 4 | 61,120,4,7,6 |
| IASI_RR | Reconstructed radiances (mW/m2/cm-1/sr) | Real | 4 | 61,120,4,616 |
| IASI_RR_Quality_Flag | 0 = accepted, 1 = rejected | Real | 4 | 61,120,4,1 |
| Dice | IASI FOR (1-30) | Real | 4 | 61,120,4 |

The date information in the file names is defined as:

${Year} = the 4-digit year

${Month} = 2-digit month

${Day} = 2-digit day of month

### Intended Users

STAR validation scientists. STAR climate scientists.

### Access

These files reside at:

$BASE/SATELLITE_DATA/MetOpA/NRT_DATA/${Year}/${Month}/${Day}/IASI_DATA/Global_Grids/PC_FullRes_Global_Grids_1Band/M02_IAF3PC${Year}${Month}${Day}.asc

$BASE/SATELLITE_DATA/MetOpA/NRT_DATA/${Year}/${Month}/${Day}/IASI_DATA/Global_Grids/PC_FullRes_Global_Grids_1Band/M02_IAF3PC${Year}${Month}${Day}.desc

Files are sent to the DDS by the scripts that generate them.  All grids are pulled from the DDS by STAR into the STAR Collaborative Environment and stored locally.

dds.nesdis.noaa.gov:push

POC – Nichols, Catherine L

5200 Auth Road, Room 0315, Building: FB4

Suitland, MD 20746 – 4301

Phone: (301)457-5245

Fax:      (301)457-5199

E-mail: cathy.nichols@noaa.gov

## IASI Global Thinned Radiances

Ascending and descending daily gridded binary files.

(0.5 x 2.0 degree global grids of thinned IASI radiances).

### Purpose

These data sets are used for validation purposes and by STAR scientists for climate reprocessing activities.

These data sets are also intermediate data sets. They are read into the processing along with a daily set of forecast files (00Z, 06Z, 12Z, 18Z, 24Z).  The data are extracted from the forecast grid and written out to the IASI global grid resolution.

### Data File Description

The Global Grids products are generated from daily sets of NetCDF files and run, operationally, one day behind real time processing. These are direct access daily binary files in a GRADS readable format.  For a given grid product, the processing defines two grids at a specified resolution.  One grid is for observations, obtained during ascending orbits, and the other is for descending orbits. Each daily global grid product consists of one ascending and one descending file. The file-naming convention for f the 0.5 x 2.0 grids is:

NRT_IAGG${YEAR}${MONTH}${DAY}.asc 
NRT_IAGG${YEAR}${MONTH}${DAY}.desc

The content of the files with variable name list and their dimensions are as follows:

| Variable | Description | Type | Size | Dim Length |
| --- | --- | --- | --- | --- |
| YearMonthDay | Year/Month/Day string given as YYYYMMDD. | real | 4 | 91,720 |
| Time | Hours.Fractional_Minutes | Real | 4 | 91,720 |
| Grid_Latitude | Lat locations of the grid points (± 90 degrees) | Real | 4 | 91,720 |
| Grid_Longitude | Lon locations of the grid points (± 90 degrees) | Real | 4 | 91,720 |
| Instrument_Latitude | Lat locations of the actual observations (± 90 degrees) | Real | 4 | 91,720 |
| Instrument_Longitude | Lon locations of the actual observations (± 90 degrees) | Real | 4 | 91,720 |
| Granule_Number | Granule number | Real | 4 | 91,720 |
| View_Angle | The view angle of the current IASI FOV (± 90 degrees) | Real | 4 | 91,720 |
| Solar_Zenith | The solar zenith of the current IASI FOV (0-90 degrees) | Real | 4 | 91,720 |
| Solar_Azimuth | The solar azimuth of the current IASI FOV (0-180 degrees) | Real | 4 | 91,720 |
| Satellite_Zenith | The satellite zenith of the current IASI FOV (0-90 degrees) | Real | 4 | 91,720 |
| Satellite_Azimuth | The satellite azimuth of the current IASI FOV (0-180 degrees) | Real | 4 | 91,720 |
| Satellite_Height | The satellite height of the current IASI FOV (km) | Real | 4 | 91,720 |
| AVHRR_Mean_Radiances | The mean AVHRR radiances (mW/m2/cm-1/sr) | Real | 4 | 91,720,7,6 |
| AVHRR_Std_Radiances | The standard deviation of the AVHRR radiances (mW/m2/cm-1/sr) | Real | 4 | 91,720,7,6 |
| IASI_Radiance | IASI radiances (mW/m2/cm-1/sr) | Real | 4 | 91,720,616 |
| Quality_Flag | 0 = accepted, 1 = rejected | Real | 4 | 91,720 |
| Dice | IASI FOR (1-30) | Real | 4 | 91,720 |

The date information in the file names is defined as:

${Year} = the 4-digit year

${Month} = 2-digit month

${Day} = 2-digit day of month

### Intended Users

STAR validation scientists. STAR climate scientists.

### Access

These files reside at:

$BASE/SATELLITE_DATA/MetOpA/NRT_DATA/${Year}/${Month}/${Day}/IASI_DATA/Global_Grids/NCEP_Global_Grids/M02_IAGG${Year}${Month}${Day}.asc

$BASE/SATELLITE_DATA/MetOpA/NRT_DATA/${Year}/${Month}/${Day}/IASI_DATA/Global_Grids/NCEP_Global_Grids/M02_IAGG${Year}${Month}${Day}.desc

Files are sent to the DDS by the scripts that generate them.  All grids are pulled from the DDS by STAR into the STAR Collaborative Environment and stored locally.

dds.nesdis.noaa.gov:push

POC – Nichols, Catherine L

5200 Auth Road, Room 0315, Building: FB4

Suitland, MD 20746 – 4301

Phone: (301)457-5245

Fax:      (301)457-5199

E-mail: cathy.nichols@noaa.gov

## IASI Full Global Thinned Radiances

Ascending and descending daily gridded binary files.

(3.0 x 3.0 degree global grids of full resolution thinned IASI radiances).

### Purpose

These data sets are used for validation purposes and by STAR scientists for climate reprocessing activities. The 3.0 X 3.0 IASI Full Global grids and their associated metadata files are pulled by CLASS for storage in the archive. The details of the archive agreement are found in the IASI Data Submission Agreement (CLASS, 2006).

### Data File Description

The daily global 3° X 3° grids are derived from the IASI level 1C data provided by EUMETSAT. These files are created daily and consists of (1) 8461 channels of IASI Level 1C radiances, (2) 6 channels of AVHRR Level 1B radiances averaged on to the IASI fields of view, (3) all associated navigational and temporal information for the observations, and (4) quality flags.  These data are collocated to points on a 3° X 3° global grid.  On a scan line, the IASI fields of view are clustered into 2 X 2 matrices.  These clusters of fields of view are referred to as fields of regard.  It is actually this field of regard that is collocated and stored for each grid point.  A daily gridded data set consists of two files, one for the ascending orbits and the other for the descending.  Because the product requires an entire day’s data, it is produced one day behind real time.  For both the ascending and descending daily files NOAA/NESDIS/STAR generates one associated xml format metadata file.

The files are binary (big endian) data files in direct access format. The gridded format allows for Grid Analysis and Display System (GrADS) readability.  The files are each 1993265280 bytes in size.  Each file contains 17019 records that are 117120 bytes in length.  Each record is the data for an entire 61 X 120 degree grid.  Therefore, if no data were matched to a particular grid point, that space is still defined on the grid and is filled with missing values.  The file contains no headers.

The file-naming convention for the 3.0 x 3.0 grids is:

NRT_IAFGG${YEAR}${MONTH}${DAY}.asc 
NRT_IAFGG${YEAR}${MONTH}${DAY}.desc

The content of the files with variable name list and their dimensions are as follows:

| Variable | Description | Type | Size | Dim Length |
| --- | --- | --- | --- | --- |
| YearMonthDay | Year/Month/Day string given as YYYYMMDD. | real | 4 | 61,120,4 |
| Time | Hours.Fractional_Minutes | Real | 4 | 61,120,4 |
| Grid_Latitude | Lat locations of the grid points (± 90 degrees) | Real | 4 | 61,120,4 |
| Grid_Longitude | Lon locations of the grid points (± 90 degrees) | Real | 4 | 61,120,4 |
| Instrument_Latitude | Lat locations of the actual observations (± 90 degrees) | Real | 4 | 61,120,4 |
| Instrument_Longitude | Lon locations of the actual observations (± 90 degrees) | Real | 4 | 61,120,4 |
| Granule_Number | Granule number | Real | 4 | 61,120,4 |
| View_Angle | The view angle of the current IASI FOV (± 90 degrees) | Real | 4 | 61,120,4 |
| Solar_Zenith | The solar zenith of the current IASI FOV (0-90 degrees) | Real | 4 | 61,120,4 |
| Solar_Azimuth | The solar azimuth of the current IASI FOV (0-180 degrees) | Real | 4 | 61,120,4 |
| Satellite_Zenith | The satellite zenith of the current IASI FOV (0-90 degrees) | Real | 4 | 61,120,4 |
| Satellite_Azimuth | The satellite azimuth of the current IASI FOV (0-180 degrees) | Real | 4 | 61,120,4 |
| Satellite_Height | The satellite height of the current IASI FOV (km) | Real | 4 | 61,120,4 |
| AVHRR_Mean_Radiances | The mean AVHRR radiances (mW/m2/cm-1/sr) | Real | 4 | 61,120,4,7,6 |
| AVHRR_Std_Radiances | The standard deviation of the AVHRR radiances (mW/m2/cm-1/sr) | Real | 4 | 61,120,4,7,6 |
| IASI_Radiance | IASI radiances (mW/m2/cm-1/sr) | Real | 4 | 61,120,4,8461 |
| Quality_Flag | 0 = accepted, 1 = rejected | Real | 4 | 61,120,4 |
| Dice | IASI FOR (1-30) | Real | 4 | 61,120,4 |

The date information in the file names is defined as:

${Year} = the 4-digit year

${Month} = 2-digit month

${Day} = 2-digit day of month

### Intended Users

CLASS

POC: John Bates

Chief, Remote Sensing and Applications Division

NOAA / NESDIS / National Climatic Data Center (NCDC) / Remote Sensing and Applications Division (RSAD)

Asheville, NC

Phone: (828) 271-4378

Fax: (828) 271-4328

Address: 151 Patton Avenue, Room 516 D Ashville, NC 28801

### Access

These files reside at:

$BASE/SATELLITE_DATA/MetOpA/NRT_DATA/${Year}/${Month}/${Day}/IASI_DATA/Global_Grids/FullRes_Global_Grids/M02_IAFGG${Year}${Month}${Day}.asc

$BASE/SATELLITE_DATA/MetOpA/NRT_DATA/${Year}/${Month}/${Day}/IASI_DATA/Global_Grids/FullRes_Global_Grids/M02_IAFGG${Year}${Month}${Day}.desc

Files are sent to the DDS by the scripts that generate them.  All grids are pulled from the DDS by STAR into the STAR Collaborative Environment and stored locally.

dds.nesdis.noaa.gov:push

POC – Nichols, Catherine L

5200 Auth Road, Room 0315, Building: FB4

Suitland, MD 20746 – 4301

Phone: (301)457-5245

Fax:      (301)457-5199

E-mail: cathy.nichols@noaa.gov

## Full Global Grids Metadata

Metadata file for both ascending and descending 3 x 3 IASI global grids.

### Purpose

The metadata files accompanying the daily 3° X 3° globally-gridded IASI Level 1C data files.

### Data File description

There is one grid metadata file for each set of ascending and descending global grid files.  It is derived from the grid metadata template (IASI_3X3Grid_Metadata_Template.xml).  It is generated in the Global Grids unit by the script Run_IASI_FullGlobal_Grids.pl.

The metadata file has the same name as its associated data files except that it has a .xml extension.

| Metadata file-naming Convention | M01_IAFGGYYYYMODD.${ext}.xml Where: M01 = MetOp1 IA = IASI FGG = Full Global Grid YYYY = 4-digit year (e.g., 2008) MO = Month (01-12) DD = Day of month (01-31) ext = ‘asc’ for ascending , ‘desc’ for descending xml = An extension indicating that the file is an xml format file |
| --- | --- |
| Metadata file format | This is an xml format file using the FGDC Remote Sensing Extension content standard. |

References:

- Content Standard for Digital Geospatial Metadata: Extensions for Remote Sending Metadata, FGDC-STD-012-2002.

b.	FGDC (1998) Content Standard for Digital Geospatial Metadata, VERSION 2, FGDC-                              STD-001-1998.

More information about these data sets could be found in Metadata Description Document (NESDIS/STAR, 2008b).

### Intended Users

CLASS

POC: John Bates

Chief, Remote Sensing and Applications Division

NOAA / NESDIS / National Climatic Data Center (NCDC) / Remote Sensing and Applications Division (RSAD)

Asheville, NC

Phone: (828) 271-4378

Fax: (828) 271-4328

Address: 151 Patton Avenue, Room 516 D Ashville, NC 28801

### Access

This file resides in the same directory as its associated data files at:

$BASE/SATELLITE_DATA/MetOpA/NRT_DATA/${Year}/${Month}/${Day}/IASI_DATA/Global_Grids/FullRes_Global_Grids

Files are sent to the DDS by the scripts that generate them: dds.nesdis.noaa.gov:push

POC – Nichols, Catherine L

5200 Auth Road, Room 0315, Building: FB4

Suitland, MD 20746 – 4301

Phone: (301)457-5245

Fax:      (301)457-5199

E-mail: cathy.nichols@noaa.gov

## IASI GFS Forecast Global Grids

Ascending and descending daily gridded binary files of GFS data at the IASI 0.5 x 2.0 global grid locations.

### Purpose

These data sets are used for validation purposes and by STAR scientists for climate reprocessing activities.

### Data File Description

The Global Grids products are generated from daily sets of NetCDF files and run, operationally, one day behind real time processing. These are direct access daily binary files in a GRADS readable format. For a given grid product, the processing defines two grids at a specified resolution.  One grid is for observations, obtained during ascending orbits, and the other is for descending orbits. Each daily global grid product consists of one ascending and one descending file. The file-naming convention for the IASI GFS global (0.5 x 2.0) grids is:

M02_IAGFS${YEAR}${MONTH}${DAY}.asc 
M02_IAGFS${YEAR}${MONTH}${DAY}.desc

The content of the files with variable name list and their dimensions are as follows:

| Variable | Description | Type | Size | Dim Length |
| --- | --- | --- | --- | --- |
| Date | Year/Month/Day string given as YYYYMMDD. | Real | 4 | 91, 720 |
| Time | Hours.Fractional_Minutes | Real | 4 | 91, 720 |
| Run_Hour | The time of the forecast run (0, 6, 12, or 18Z). | Real | 4 | 91, 720 |
| Forecast_Hour | Forecast projection (0, 3, 6, or 9) hours. | Real | 4 | 91, 720 |
| Latitude | Latitude of IASI FOV on grid (± 90 degrees). | Real | 4 | 91, 720 |
| Longitude | Longitude of IASI FOV on grid (± 90 degrees). | Real | 4 | 91, 720 |
| Forecast_Latitude | Original latitude on the forecast grid (± 90 degrees). | Real | 4 | 91, 720 |
| Forecast_Longitude | Original longitude on the forecast grid (± 90 degrees). | Real | 4 | 91, 720 |
| Pressure | Forecast pressure (mb) for 26 levels | Real | 4 | 91,720,26 |
| Temperature | Forecast temperature (Kelvin) for 26 levels | Real | 4 | 91,720,26 |
| Water_Vapor | Forecast water vapor mole mixing ratio for 21 levels | Real | 4 | 91,720,21 |
| Ozone | Forecast ozone mole mixing ratio for 6 levels | Real | 4 | 91,720,6 |
| Dew_Point_2m | Forecast dewpoint at 2 m (Kelvin). | Real | 4 | 91,720 |
| Temperature_2m | Forecast 2 m temperature (Kelvin). | Real | 4 | 91,720 |
| Skin_Temperature | Forecast skin temperature (Kelvin) for 2 levels | Real | 4 | 91,720,2 |
| Surface_Pressure | Forecast surface pressure (mb). | Real | 4 | 91,720 |
| Precip_Water_Content | Forecast Precipitable water content (mm). | Real | 4 | 91,720 |
| Total_Column_Ozone | Forecast total column ozone (dobson) | Real | 4 | 91,720 |
| Sea_Surface_Temperature | Forecast sea surface temperature (Kelvin). | Real | 4 | 91,720 |
| Land_Fraction | Land fraction at the forecast grid location (0-1). | Real | 4 | 91,720 |
| Temperature_of_30mb_to_0mb | Forecast temperature difference between 30 mb and 0 mb (Kelvin). | Real | 4 | 91,720 |

The date information in the file names is defined as:

${Year} = the 4-digit year

${Month} = 2-digit month

${Day} = 2-digit day of month

### Intended Users

STAR validation scientists. STAR climate scientists.

### Access

These files reside at:

$BASE/SATELLITE_DATA/MetOpA/NRT_DATA/${Year}/${Month}/${Day}/IASI_DATA/Global_Grids/GFS_Forecast_Global_Grids/M02_IAGFS${Year}${Month}${Day}.asc

$BASE/SATELLITE_DATA/MetOpA/NRT_DATA/${Year}/${Month}/${Day}/IASI_DATA/Global_Grids/GFS_Forecast_Global_Grids/M02_IAGFS${Year}${Month}${Day}.desc

Files are sent to the DDS by the scripts that generate them.  All grids are pulled from the DDS by STAR into the STAR Collaborative Environment and stored locally.

dds.nesdis.noaa.gov:push

POC – Nichols, Catherine L

5200 Auth Road, Room 0315, Building: FB4

Suitland, MD 20746 – 4301

Phone: (301)457-5245

Fax:      (301)457-5199

E-mail: cathy.nichols@noaa.gov

## IASI GDAS Forecast Global Grids

Ascending and descending daily gridded binary files of GDAS data at the IASI 0.5 x 2.0 global grid locations.

### Purpose

These data sets are used for validation purposes and by STAR scientists for climate reprocessing activities.

### Data File Description

The Global Grids products are generated from daily sets of NetCDF files and run, operationally, one day behind real time processing. These are direct access daily binary files in a GRADS readable format.  For a given grid product, the processing defines two grids at a specified resolution.  One grid is for observations, obtained during ascending orbits, and the other is for descending orbits. Each daily global grid product consists of one ascending and one descending file. The file-naming convention for the IASI GDAS global (0.5 x 2.0) grids is:

M02_IAGDS${YEAR}${MONTH}${DAY}.asc 
M02_IAGDS${YEAR}${MONTH}${DAY}.desc

The content of the files with variable name list and their dimensions are as follows:

| Variable | Description | Type | Size | Dim Length |
| --- | --- | --- | --- | --- |
| Date | Year/Month/Day string given as YYYYMMDD. | real | 4 | 91, 720 |
| Time | Hours.Fractional_Minutes | Real | 4 | 91, 720 |
| Run_Hour | The time of the forecast run (0, 6, 12, or 18Z). | Real | 4 | 91, 720 |
| Forecast_Hour | Forecast projection (0, 3, 6, or 9) hours. | Real | 4 | 91, 720 |
| Latitude | Latitude of IASI FOV on grid (± 90 degrees). | Real | 4 | 91, 720 |
| Longitude | Longitude of IASI FOV on grid (± 90 degrees). | Real | 4 | 91, 720 |
| Forecast_Latitude | Original latitude on the forecast grid (± 90 degrees). | Real | 4 | 91, 720 |
| Forecast_Longitude | Original longitude on the forecast grid (± 90 degrees). | Real | 4 | 91, 720 |
| Pressure | Forecast pressure (mb) for 64 levels | Real | 4 | 91,720,64 |
| Temperature | Forecast temperature (Kelvin) for 64 levels | Real | 4 | 91,720,64 |
| Water_Vapor | Forecast water vapor mole mixing ratio for 64 levels | Real | 4 | 91,720,64 |
| Ozone | Forecast ozone mole mixing ratio for 64 levels | Real | 4 | 91,720,64 |
| Dew_Point_2m | Forecast dewpoint at 2 m (Kelvin). | Real | 4 | 91,720 |
| Temperature_2m | Forecast 2 m temperature (Kelvin). | Real | 4 | 91,720 |
| Skin_Temperature | Forecast skin temperature (Kelvin). | Real | 4 | 91,720,1 |
| Surface_Pressure | Forecast surface pressure (mb). | Real | 4 | 91,720 |
| Precip_Water_Content | Forecast Precipitable water content (mm). | Real | 4 | 91,720 |
| Total_Column_Ozone | Forecast total column ozone (dobson) | Real | 4 | 91,720 |
| Sea_Surface_Temperature | Forecast sea surface temperature (Kelvin). | Real | 4 | 91,720 |
| Land_Fraction | Land fraction at the forecast grid location (0-1). | Real | 4 | 91,720 |
| Delta_Pressure | Forecast pressure difference between (mb) each of the 64 levels. | real | 4 | 91,720,64 |

The date information in the file names is defined as:

${Year} = the 4-digit year

${Month} = 2-digit month

${Day} = 2-digit day of month

### Intended Users

STAR validation scientists. STAR climate scientists.

### Access

These files reside at:

$BASE/SATELLITE_DATA/MetOpA/NRT_DATA/${Year}/${Month}/${Day}/IASI_DATA/Global_Grids/GDAS_Forecast_Global_Grids/M02_IAGDS${Year}${Month}${Day}.asc

$BASE/SATELLITE_DATA/MetOpA/NRT_DATA/${Year}/${Month}/${Day}/IASI_DATA/Global_Grids/GDAS_Forecast_Global_Grids/M02_IAGDS${Year}${Month}${Day}.desc

Files are sent to the DDS by the scripts that generate them.  All grids are pulled from the DDS by STAR into the STAR Collaborative Environment and stored locally.

dds.nesdis.noaa.gov:push

POC – Nichols, Catherine L

5200 Auth Road, Room 0315, Building: FB4

Suitland, MD 20746 – 4301

Phone: (301)457-5245

Fax:      (301)457-5199

E-mail: cathy.nichols@noaa.gov

AMSU-A Full Global Grids

Ascending and descending daily gridded binary files.

(3.0 x 3.0 degree grids of AMSU-A radiances).

Purpose

These data sets are used for validation purposes and by STAR scientists.

Data File Description

The Global Grids products are generated from daily sets of NetCDF files and run, operationally, one day behind real time processing. These are direct access daily binary files in a GRADS readable format.  For a given grid product, the processing defines two grids at a specified resolution.  One grid is for observations, obtained during ascending orbits, and the other is for descending orbits. Each daily global grid product consists of one ascending and one descending file. The file-naming convention for the AMSU-A full global (3.0 x 3.0) grids is:

M02_AMFG${YEAR}${MONTH}${DAY}.asc 
M02_AMFG${YEAR}${MONTH}${DAY}.desc

The content of the files with variable name list and their dimensions are as follows:

| Variable | Description | Type | Size | Dim Length |
| --- | --- | --- | --- | --- |
| YearMonthDay | Year/Month/Day string given as YYYYMMDD. | real | 4 | 61,120 |
| Time | Hours.Fractional_Minutes | Real | 4 | 61,120 |
| Grid_Latitude | Lat locations of the grid points (± 90 degrees) | Real | 4 | 61,120 |
| Grid_Longitude | Lon locations of the grid points (± 90 degrees) | Real | 4 | 61,120 |
| Instrument_Latitude | Lat locations of the actual observations (± 90 degrees) | Real | 4 | 61,120 |
| Instrument_Longitude | Lon locations of the actual observations (± 90 degrees) | Real | 4 | 61,120 |
| Granule_Number | Granule number | Real | 4 | 61,120 |
| View_Angle | The view angle of the current IASI FOV (± 90 degrees) | Real | 4 | 61,120 |
| Solar_Zenith | The solar zenith of the current IASI FOV (0-90 degrees) | Real | 4 | 61,120 |
| Solar_Azimuth | The solar azimuth of the current IASI FOV (0-180 degrees) | Real | 4 | 61,120 |
| Satellite_Zenith | The satellite zenith of the current IASI FOV (0-90 degrees) | Real | 4 | 61,120 |
| Satellite_Azimuth | The satellite azimuth of the current IASI FOV (0-180 degrees) | Real | 4 | 61,120 |
| Satellite_Height | The satellite height of the current IASI FOV (km) | Real | 4 | 61,120 |
| AMSUA_Radiances | AMSU-A radiances (mW/m2/cm-1/sr) | Real | 4 | 61,120,15 |
| Quality_Flag | 0 = accepted, 1 = rejected | Real | 4 | 61,120,15 |
| Dice | AMSU-A FOV | Real | 4 | 61,120 |
| Topography | The height of the surface above sea level (meters). | Real | 4 | 61,120 |
| Land_Fraction | The fraction of land coverage (0-1). | Real | 4 | 61,120 |

The date information in the file names is defined as:

${Year} = the 4-digit year

${Month} = 2-digit month

${Day} = 2-digit day of month

Intended Users

STAR validation scientists.

Access

These files reside at:

$BASE/SATELLITE_DATA/MetOpA/NRT_DATA/${Year}/${Month}/${Day}/IASI_DATA/Global_Grids/AMSUA_FullGlobal_Grids/M02_AMFG${Year}${Month}${Day}.asc

$BASE/SATELLITE_DATA/MetOpA/NRT_DATA/${Year}/${Month}/${Day}/IASI_DATA/Global_Grids/AMSUA_FullGlobal_Grids/M02_AMFG${Year}${Month}${Day}.desc

Files are sent to the DDS by the scripts that generate them.  All grids are pulled from the DDS by STAR into the STAR Collaborative Environment and stored locally.

dds.nesdis.noaa.gov:push

POC – Nichols, Catherine L

5200 Auth Road, Room 0315, Building: FB4

Suitland, MD 20746 – 4301

Phone: (301)457-5245

Fax:      (301)457-5199

E-mail: cathy.nichols@noaa.gov

AMSU-A Global Grids

Ascending and descending daily gridded binary files.

(0.5 x 2.0 degree grids of AMSU-A radiances).

Purpose

These data sets are used for validation purposes and by STAR scientists.

### Data File Description

The Global Grids products are generated from daily sets of NetCDF files and run, operationally, one day behind real time processing. These are direct access daily binary files in a GRADS readable format.  For a given grid product, the processing defines two grids at a specified resolution.  One grid is for observations, obtained during ascending orbits, and the other is for descending orbits. Each daily global grid product consists of one ascending and one descending file. The file-naming convention for the AMSU-A global (0.5 x 2.0) grids is:

M02_AMGG${YEAR}${MONTH}${DAY}.asc 
M02_AMGG${YEAR}${MONTH}${DAY}.desc

The content of the files with variable name list and their dimensions are as follows:

| Variable | Description | Type | Size | Dim Length |
| --- | --- | --- | --- | --- |
| YearMonthDay | Year/Month/Day string given as YYYYMMDD. | real | 4 | 91,720 |
| Time | Hours.Fractional_Minutes | Real | 4 | 91,720 |
| Grid_Latitude | Lat locations of the grid points (± 90 degrees) | Real | 4 | 91,720 |
| Grid_Longitude | Lon locations of the grid points (± 90 degrees) | Real | 4 | 91,720 |
| Instrument_Latitude | Lat locations of the actual observations (± 90 degrees) | Real | 4 | 91,720 |
| Instrument_Longitude | Lon locations of the actual observations (± 90 degrees) | Real | 4 | 91,720 |
| Granule_Number | Granule number | Real | 4 | 91,720 |
| View_Angle | The view angle of the current IASI FOV (± 90 degrees) | Real | 4 | 91,720 |
| Solar_Zenith | The solar zenith of the current IASI FOV (0-90 degrees) | Real | 4 | 91,720 |
| Solar_Azimuth | The solar azimuth of the current IASI FOV (0-180 degrees) | Real | 4 | 91,720 |
| Satellite_Zenith | The satellite zenith of the current IASI FOV (0-90 degrees) | Real | 4 | 91,720 |
| Satellite_Azimuth | The satellite azimuth of the current IASI FOV (0-180 degrees) | Real | 4 | 91,720 |
| Satellite_Height | The satellite height of the current IASI FOV (km) | Real | 4 | 91,720 |
| AMSUA_Radiances | AMSU-A radiances (mW/m2/cm-1/sr) | Real | 4 | 91,720,15 |
| Quality_Flag | 0 = accepted, 1 = rejected | Real | 4 | 91,720,15 |
| Dice | AMSU-A FOV | Real | 4 | 61,120 |
| Topography | The height of the surface above sea level (meters). | Real | 4 | 61,120 |
| Land_Fraction | The fraction of land coverage (0-1). | Real | 4 | 61,120 |

Intended Users

STAR validation scientists.

Access

These files reside at:

$BASE/SATELLITE_DATA/MetOpA/NRT_DATA/${Year}/${Month}/${Day}/IASI_DATA/Global_Grids/AMSUA_Global_Grids/M02_AMGG${Year}${Month}${Day}.asc

$BASE/SATELLITE_DATA/MetOpA/NRT_DATA/${Year}/${Month}/${Day}/IASI_DATA/Global_Grids/AMSUA_Global_Grids/M02_AMGG${Year}${Month}${Day}.desc

Files are sent to the DDS by the scripts that generate them.  All grids are pulled from the DDS by STAR into the STAR Collaborative Environment and stored locally.

dds.nesdis.noaa.gov:push

POC – Nichols, Catherine L

5200 Auth Road, Room 0315, Building: FB4

Suitland, MD 20746 – 4301

Phone: (301)457-5245

Fax:      (301)457-5199

E-mail: cathy.nichols@noaa.gov

MHS Full Global Grids

Ascending and descending daily gridded binary files.

(3.0 x 3.0 degree grids of MHS radiances).

Purpose

These data sets are used for validation purposes and by STAR scientists.

Data File Description

The Global Grids products are generated from daily sets of NetCDF files and run, operationally, one day behind real time processing. These are direct access daily binary files in a GRADS readable format. For a given grid product, the processing defines two grids at a specified resolution.  One grid is for observations, obtained during ascending orbits, and the other is for descending orbits. Each daily global grid product consists of one ascending and one descending file. The file-naming convention for the MHS full  global (3.0 x 3.0) grids is:

M02_MHFG${YEAR}${MONTH}${DAY}.asc 
M02_MHFG${YEAR}${MONTH}${DAY}.desc

The content of the files with variable name list and their dimensions are as follows:

| Variable | Description | Type | Size | Dim Length |
| --- | --- | --- | --- | --- |
| YearMonthDay | Year/Month/Day string given as YYYYMMDD. | real | 4 | 61,120,9 |
| Time | Hours.Fractional_Minutes | Real | 4 | 61,120,9 |
| Grid_Latitude | Lat locations of the grid points (± 90 degrees) | Real | 4 | 61,120,9 |
| Grid_Longitude | Lon locations of the grid points (± 90 degrees) | Real | 4 | 61,120,9 |
| Instrument_Latitude | Lat locations of the actual observations (± 90 degrees) | Real | 4 | 61,120,9 |
| Instrument_Longitude | Lon locations of the actual observations (± 90 degrees) | Real | 4 | 61,120,9 |
| Granule_Number | Granule number | Real | 4 | 61,120,9 |
| View_Angle | The view angle of the current IASI FOV (± 90 degrees) | Real | 4 | 61,120,9 |
| Solar_Zenith | The solar zenith of the current IASI FOV (0-90 degrees) | Real | 4 | 61,120,9 |
| Solar_Azimuth | The solar azimuth of the current IASI FOV (0-180 degrees) | Real | 4 | 61,120,9 |
| Satellite_Zenith | The satellite zenith of the current IASI FOV (0-90 degrees) | Real | 4 | 61,120,9 |
| Satellite_Azimuth | The satellite azimuth of the current IASI FOV (0-180 degrees) | Real | 4 | 61,120,9 |
| Satellite_Height | The satellite height of the current IASI FOV (km) | Real | 4 | 61,120,9 |
| MHS_Radiances | AMSU-A radiances (mW/m2/cm-1/sr) | Real | 4 | 61,120,9,5 |
| Quality_Flag | 0 = accepted, 1 = rejected | Real | 4 | 61,120,9,5 |
| Dice | AMSU-A FOV | Real | 4 | 61,120,9 |
| Topography | The height of the surface above sea level (meters). | Real | 4 | 61,120,9 |
| Land_Fraction | The fraction of land coverage (0-1). | Real | 4 | 61,120,9 |

The date information in the file names is defined as:

${Year} = the 4-digit year

${Month} = 2-digit month

${Day} = 2-digit day of month

### Intended Users

STAR validation scientists.

### Access

These files reside at:

$BASE/SATELLITE_DATA/MetOpA/NRT_DATA/${Year}/${Month}/${Day}/IASI_DATA/Global_Grids/MHS_FullGlobal_Grids/M02_MHFG${Year}${Month}${Day}.asc

$BASE/SATELLITE_DATA/MetOpA/NRT_DATA/${Year}/${Month}/${Day}/IASI_DATA/Global_Grids/MHS_FullGlobal_Grids/M02_MHFG${Year}${Month}${Day}.desc

Files are sent to the DDS by the scripts that generate them.  All grids are pulled from the DDS by STAR into the STAR Collaborative Environment and stored locally.

dds.nesdis.noaa.gov:push

POC – Nichols, Catherine L

5200 Auth Road, Room 0315, Building: FB4

Suitland, MD 20746 – 4301

Phone: (301)457-5245

Fax:      (301)457-5199

E-mail: cathy.nichols@noaa.gov

MHS Global Grids

Ascending and descending daily gridded binary files.

(0.5 x 2.0 degree grids of MHS radiances).

Purpose

These data sets are used for validation purposes and by STAR scientists.

Data File Description

The Global Grids products are generated from daily sets of NetCDF files and run, operationally, one day behind real time processing. These are direct access daily binary files in a GRADS readable format. For a given grid product, the processing defines two grids at a specified resolution.  One grid is for observations, obtained during ascending orbits, and the other is for descending orbits. Each daily global grid product consists of one ascending and one descending file. The file-naming convention for the MHS full  global (3.0 x 3.0) grids is:

M02_MHGG${YEAR}${MONTH}${DAY}.asc 
M02_MHGG${YEAR}${MONTH}${DAY}.desc

The content of the files with variable name list and their dimensions are as follows:

| Variable | Description | Type | Size | Dim Length |
| --- | --- | --- | --- | --- |
| YearMonthDay | Year/Month/Day string given as YYYYMMDD. | real | 4 | 91,720 |
| Time | Hours.Fractional_Minutes | Real | 4 | 91,720 |
| Grid_Latitude | Lat locations of the grid points (± 90 degrees) | Real | 4 | 91,720 |
| Grid_Longitude | Lon locations of the grid points (± 90 degrees) | Real | 4 | 91,720 |
| Instrument_Latitude | Lat locations of the actual observations (± 90 degrees) | Real | 4 | 91,720 |
| Instrument_Longitude | Lon locations of the actual observations (± 90 degrees) | Real | 4 | 91,720 |
| Granule_Number | Granule number | Real | 4 | 91,720 |
| View_Angle | The view angle of the current IASI FOV (± 90 degrees) | Real | 4 | 91,720 |
| Solar_Zenith | The solar zenith of the current IASI FOV (0-90 degrees) | Real | 4 | 91,720 |
| Solar_Azimuth | The solar azimuth of the current IASI FOV (0-180 degrees) | Real | 4 | 91,720 |
| Satellite_Zenith | The satellite zenith of the current IASI FOV (0-90 degrees) | Real | 4 | 91,720 |
| Satellite_Azimuth | The satellite azimuth of the current IASI FOV (0-180 degrees) | Real | 4 | 91,720 |
| Satellite_Height | The satellite height of the current IASI FOV (km) | Real | 4 | 91,720 |
| MHS_Radiances | AMSU-A radiances (mW/m2/cm-1/sr) | Real | 4 | 91,720,5 |
| Quality_Flag | 0 = accepted, 1 = rejected | Real | 4 | 91,720,5 |
| Dice | AMSU-A FOV | Real | 4 | 91,720 |
| Topography | The height of the surface above sea level (meters). | Real | 4 | 91,720 |
| Land_Fraction | The fraction of land coverage (0-1). | Real | 4 | 91,720 |

The date information in the file names is defined as:

${Year} = the 4-digit year

${Month} = 2-digit month

${Day} = 2-digit day of month

### Intended Users

STAR validation scientists.

### Access

These files reside at:

$BASE/SATELLITE_DATA/MetOpA/NRT_DATA/${Year}/${Month}/${Day}/IASI_DATA/Global_Grids/MHS_Global_Grids/M02_MHGG${Year}${Month}${Day}.asc

$BASE/SATELLITE_DATA/MetOpA/NRT_DATA/${Year}/${Month}/${Day}/IASI_DATA/Global_Grids/MHS_Global_Grids/M02_MHGG${Year}${Month}${Day}.desc

Files are sent to the DDS by the scripts that generate them.  All grids are pulled from the DDS by STAR into the STAR Collaborative Environment and stored locally.

dds.nesdis.noaa.gov:push

POC – Nichols, Catherine L

5200 Auth Road, Room 0315, Building: FB4

Suitland, MD 20746 – 4301

Phone: (301)457-5245

Fax:      (301)457-5199

E-mail: cathy.nichols@noaa.gov

IASI L2 Full Global Grids

Ascending and descending daily gridded binary files.

(3.0 x 3.0 degree grids of IASI L2).

Purpose

These data sets are used for validation purposes and by STAR scientists.

Data File Description

The Global Grids products are generated from daily sets of NetCDF files and run, operationally, one day behind real time processing. These are direct access daily binary files in a GRADS readable format. For a given grid product, the processing defines two grids at a specified resolution.  One grid is for observations, obtained during ascending orbits, and the other is for descending orbits. Each daily global grid product consists of one ascending and one descending file. The file-naming convention for the IASI L2 full  global (3.0 x 3.0) grids is:

NRT_IAL2FGG${YEAR}${MONTH}${DAY}.asc 
NRT_IAL2FGG${YEAR}${MONTH}${DAY}.desc

The content of the files with variable name list and their dimensions are as follows:

| Variable | Description | Type | Size | Dim Length |
| --- | --- | --- | --- | --- |
| YearMonthDay | Year/Month/Day string given as YYYYMMDD. | real | 4 | 61,120 |
| Time | Hours.Fractional_Minutes | Real | 4 | 61,120 |
| Grid_Latitude | Lat locations of the grid points (± 90 degrees) | Real | 4 | 61,120 |
| Grid_Longitude | Lon locations of the grid points (± 90 degrees) | Real | 4 | 61,120 |
| Instrument_Latitude | Lat locations of the actual observations (± 90 degrees) | Real | 4 | 61,120 |
| Instrument_Longitude | Lon locations of the actual observations (± 90 degrees) | Real | 4 | 61,120 |
| Granule_Number | Granule number | Real | 4 | 61,120 |
| View_Angle | The view angle of the current IASI FOV (± 90 degrees) | Real | 4 | 61,120 |
| Satellite_Height | The satellite height of the current IASI FOV (km) | Real | 4 | 61,120 |
| Mean_CO2 | Mean CO2 in ppm. | Real | 4 | 61,120 |
| Satellite_Zenith | The satellite zenith | Real | 4 | 61,120 |
| Topography | The height of the surface above sea level (meters). | Real | 4 | 61,120 |
| Land_Fraction | The fraction of land coverage (0-1). | Real | 4 | 61,120 |
| Surface_Pressure | Surface pressure in millibars. | Real | 4 | 61,120 |
| Skin_Temperature | Skin temperature in Kelvin. | Real | 4 | 61,120 |
| MW_Surface_Class | Microwave surface class. | integer | 4 | 61,120 |
| MW_Surface_Emis | Microwave surface emissivity. | Real | 4 | 61,120 |
| N_Smw_Per_FOV | The number of microwave spectral points within each layer | Intger | 4 | 61,120 |
| nemis_Per_FOV | The number of surface emissivity hinge points within each layer | Integer | 4 | 61,120 |
| ncemis_Per_FOV | The number of cloud emssivity hinge points within each layer | Integer | 4 | 61,120 |
| ncld_Per_FOV | The number of cloud layers points within each layer | Integer | 4 | 61,120 |
| Quality_Flag | Retrieval quality flag (0=accept, 1=reject). | Integer | 4 | 61,120 |
| Cloud_Top_Pressure | Cloud top pressure in millibars. | Real | 4 | 61,120,8 |
| Cloud_Top_Fraction | Cloud top fractional coverage (0-1). | Real | 4 | 61,120 |
| Pressure | Pressure with the current layer in millibars. | Real | 4 | 61,120,100 |
| Effective_Pressure |  | Real | 4 | 61,120,100 |
| Temperature | Temperature within the current layer in Kelvin | Real | 4 | 61,120,100 |
| H2O | H2O layer column density. | Real | 4 | 61,120,100 |
| H2O_MR | H2O Mixing ratio (g/g) | Real | 4 | 61,120,100 |
| O3 | O3 layer column density (molecules/cm2). | Real | 4 | 61,120,100 |
| O3_MR | O3 mixing ration (ppb) | Real | 4 | 61,120,100 |
| Liquid_H2O | Liquid H2O layer column density (molecules/cm2). | Real | 4 | 61,120,100 |
| Liquid_H2O_MR | Liquid H2O Mixing Ration (g/g) | Real | 4 | 61,120,100 |
| Ice_Liquid_Flag | Ice liquid flag (0=water, 1=ice). | Real | 4 | 61,120,100 |
| CO | CO layer column density (molecules/cm2). | Real | 4 | 61,120,100 |
| CO_MR | CO Mixing Ration (ppb) | Real | 4 | 61,120,100 |
| CH4 | CH4 layer column density (molecules/cm2). | Real | 4 | 61,120,100 |
| CH4_MR | CH4 Mixing ratio (ppb) | Real | 4 | 61,120,100 |
| CO2 | CO2 mixing ratio (ppm). | Real | 4 | 61,120,100 |
| N2O | N2O layer column density (molecules/cm2). | Real | 4 | 61,120,100 |
| N2O_MR | N2O mixing ration (ppb) | Real | 4 | 61,120,100 |
| SO2 | SO2 layer column density (molecules/cm2). | Real | 4 | 61,120,100 |
| SO2_MR | SO2 mixing ratio (ppm). | Real | 4 | 61,120,100 |
| HNO3 | HNO3 layer column density (molecules/cm2). | Real | 4 | 61,120,100 |
| HNO3_MR | HNO3 mixing ration (ppb) | Real | 4 | 61,120,100 |
| MW_Frequency | Microwave frequency (cm-1). | Real | 4 | 61,120,16 |
| MW_Emis | Microwave emissivity. | Real | 4 | 61,120,16 |
| IR_Emis_Freq | Infrared emissivity hinge point frequencies (cm-1). | Real | 4 | 61,120,100 |
| IR_Surface_Emis | Infrared surface emissivity | Real | 4 | 61,120,100 |
| IR_Surface_Refl | Infrared surface reflectances (percent). | Real | 4 | 61,120,100 |
| Dice |  | Real | 4 | 61,120 |

The date information in the file names is defined as:

${Year} = the 4-digit year

${Month} = 2-digit month

${Day} = 2-digit day of month

Note that the format is for 1 IASI FOR.  The retieval product uses the 
whole FOR so data are not available for the individual IASI FOVs.

### Intended Users

STAR validation scientists.

### Access

These files reside at:

$BASE/SATELLITE_DATA/MetOpA/NRT_DATA/${Year}/${Month}/${Day}/IASI_DATA/Global_Grids/L2_FullGlobal_Grids/M02_IAL2FGG${Year}${Month}${Day}.asc

$BASE/SATELLITE_DATA/MetOpA/NRT_DATA/${Year}/${Month}/${Day}/IASI_DATA/Global_Grids/L2_FullGlobal_Grids/M02_IAL2FGG${Year}${Month}${Day}.desc

Files are sent to the DDS by the scripts that generate them.  All grids are pulled from the DDS by STAR into the STAR Collaborative Environment and stored locally.

dds.nesdis.noaa.gov:push

POC – Nichols, Catherine L

5200 Auth Road, Room 0315, Building: FB4

Suitland, MD 20746 – 4301

Phone: (301)457-5245

Fax:      (301)457-5199

E-mail: cathy.nichols@noaa.gov

IASI L2 Global Grids

Ascending and descending daily gridded binary files.

(0.5 x 2.0 degree grids of IASI L2).

### Purpose

These data sets are used for validation purposes and by STAR scientists.

### Data File Description

The Global Grids products are generated from daily sets of NetCDF files and run, operationally, one day behind real time processing. These are direct access daily binary files in a GRADS readable format. For a given grid product, the processing defines two grids at a specified resolution.  One grid is for observations, obtained during ascending orbits, and the other is for descending orbits. Each daily global grid product consists of one ascending and one descending file. The file-naming convention for the IASI L2 global (0.5 x 2.0) grids is:

NRT_IAL2GG${YEAR}${MONTH}${DAY}.asc 
NRT_IAL2GG${YEAR}${MONTH}${DAY}.desc

The content of the files with variable name list and their dimensions are as follows:

| Variable | Description | Type | Size | Dim Length |
| --- | --- | --- | --- | --- |
| YearMonthDay | Year/Month/Day string given as YYYYMMDD. | real | 4 | 91,720 |
| Time | Hours.Fractional_Minutes | Real | 4 | 91,720 |
| Grid_Latitude | Lat locations of the grid points (± 90 degrees) | Real | 4 | 91,720 |
| Grid_Longitude | Lon locations of the grid points (± 90 degrees) | Real | 4 | 91,720 |
| Instrument_Latitude | Lat locations of the actual observations (± 90 degrees) | Real | 4 | 91,720 |
| Instrument_Longitude | Lon locations of the actual observations (± 90 degrees) | Real | 4 | 91,720 |
| Granule_Number | Granule number | Real | 4 | 91,720 |
| View_Angle | The view angle of the current IASI FOV (± 90 degrees) | Real | 4 | 91,720 |
| Satellite_Height | The satellite height of the current IASI FOV (km) | Real | 4 | 91,720 |
| Mean_CO2 | Mean CO2 in ppm. | Real | 4 | 91,720 |
| Satellite_Zenith | The satellite zenith | Real | 4 | 91,720 |
| Topography | The height of the surface above sea level (meters). | Real | 4 | 91,720 |
| Land_Fraction | The fraction of land coverage (0-1). | Real | 4 | 91,720 |
| Surface_Pressure | Surface pressure in millibars. | Real | 4 | 91,720 |
| Skin_Temperature | Skin temperature in Kelvin. | Real | 4 | 91,720 |
| MW_Surface_Class | Microwave surface class. | Real | 4 | 91,720 |
| MW_Surface_Emis | Microwave surface emissivity | Real | 4 | 91,720 |
| N_Smw_Per_FOV | The number of microwave spectral points within each layer | Intger | 4 | 91,720 |
| nemis_Per_FOV | The number of surface emissivity hinge points within each layer | Integer | 4 | 91,720 |
| ncemis_Per_FOV | The number of cloud emssivity hinge points within each layer | Integer | 4 | 91,720 |
| ncld_Per_FOV | The number of cloud layers points within each layer | Integer | 4 | 91,720 |
| Quality_Flag | Retrieval quality flag (0=accept, 1=reject). | Integer | 4 | 91,720 |
| Cloud_Top_Pressure | Cloud top pressure in millibars. | Real | 4 | 91,720,8 |
| Cloud_Top_Fraction | Cloud top fractional coverage (0-1). | Real | 4 | 91,720 |
| Pressure | Pressure with the current layer in millibars. | Real | 4 | 91,720,100 |
| Effective_Pressure |  | Real | 4 | 91,720,100 |
| Temperature | Temperature within the current layer in Kelvin | Real | 4 | 91,720,100 |
| H2O | H2O layer column density. | Real | 4 | 91,720,100 |
| H2O_MR | H2O layer column density for mixing ratio (g/g) | Real | 4 | 91,720,100 |
| O3 | O3 layer column density (molecules/cm2). | Real | 4 | 91,720,100 |
| O3_MR | O3 layer column density for mixing ration | Real | 4 | 91,720,100 |
| Liquid_H2O | Liquid H2O layer column density (molecules/cm2). | Real | 4 | 91,720,100 |
| Liquid_H2O_MR | Liquid H2O layer column density for Mixing ration (g/g) | Real | 4 | 91,720,100 |
| Ice_Liquid_Flag | Ice liquid flag (0=water, 1=ice). | Real | 4 | 91,720,100 |
| CO | O3 layer column density (molecules/cm2). | Real | 4 | 91,720,100 |
| CO_MR |  | Real | 4 | 91,720,100 |
| CH4 | O3 layer column density (molecules/cm2). | Real | 4 | 91,720,100 |
| CH4_MR |  | Real | 4 | 91,720,100 |
| CO2 | CO2 mixing ratio (ppm). | Real | 4 | 91,720,100 |
| N2O | N2O layer column density (molecules/cm2). | Real | 4 | 91,720,100 |
| N2O_MR |  | Real | 4 | 91,720,100 |
| SO2 | SO2 layer column density (molecules/cm2). | Real | 4 | 91,720,100 |
| SO2_MR |  | Real | 4 | 91,720,100 |
| HNO3 | HNO3 layer column density (molecules/cm2). | Real | 4 | 91,720,100 |
| HNO3_MR |  | Real | 4 | 91,720,100 |
| MW_Frequency | Microwave frequency (cm-1). | Real | 4 | 91,720,16 |
| MW_Emis | Microwave emissivity. | Real | 4 | 91,720,16 |
| IR_Emis_Freq | Infrared emissivity hinge point frequencies (cm-1). | Real | 4 | 91,720,100 |
| IR_Surface_Emis | Infrared surface emissivity | Real | 4 | 91,720,100 |
| IR_Surface_Refl | Infrared surface reflectances (percent). | Real | 4 | 91,720,100 |
| Dice |  | Real | 4 | 91,720 |

The date information in the file names is defined as:

${Year} = the 4-digit year

${Month} = 2-digit month

${Day} = 2-digit day of month

Note that the format is for 1 IASI FOR.  The retieval product uses the 
whole FOR so data are not available for the individual IASI FOVs.

### Intended Users

STAR validation scientists.

### Access

These files reside at:

$BASE/SATELLITE_DATA/MetOpA/NRT_DATA/${Year}/${Month}/${Day}/IASI_DATA/Global_Grids/L2_Global_Grids/M02_IAL2GG${Year}${Month}${Day}.asc

$BASE/SATELLITE_DATA/MetOpA/NRT_DATA/${Year}/${Month}/${Day}/IASI_DATA/Global_Grids/L2_llGlobal_Grids/M02_IAL2GG${Year}${Month}${Day}.desc

Files are sent to the DDS by the scripts that generate them.  All grids are pulled from the DDS by STAR into the STAR Collaborative Environment and stored locally.

dds.nesdis.noaa.gov:push

POC – Nichols, Catherine L

5200 Auth Road, Room 0315, Building: FB4

Suitland, MD 20746 – 4301

Phone: (301)457-5245

Fax:      (301)457-5199

E-mail: cathy.nichols@noaa.gov

IASI CCR Global Grids

Ascending and descending daily gridded binary files.

(0.5 x 2.0 degree grids of IASI CCR).

### Purpose

These data sets are used for validation purposes and by STAR scientists.

### Data File Description

The Global Grids products are generated from daily sets of NetCDF files and run, operationally, one day behind real time processing. These are direct access daily binary files in a GRADS readable format. For a given grid product, the processing defines two grids at a specified resolution.  One grid is for observations, obtained during ascending orbits, and the other is for descending orbits. Each daily global grid product consists of one ascending and one descending file. The file-naming convention for the IASI CCR global (0.5 x 2.0) grids is:

NRT_IACC${YEAR}${MONTH}${DAY}.asc 
NRT_IACC${YEAR}${MONTH}${DAY}.desc

The format of the 2.0 X 0.5 CCR grids is exactly the same as the regular IASI 
Level 1C grids except that it uses 8461 (instead of 616) channels. The content of the files with variable name list and their dimensions are as follows:

| Variable | Description | Type | Size | Dim Length |
| --- | --- | --- | --- | --- |
| YearMonthDay | Year/Month/Day string given as YYYYMMDD. | real | 4 | 91,720 |
| Time | Hours.Fractional_Minutes | Real | 4 | 91,720 |
| Grid_Latitude | Lat locations of the grid points (± 90 degrees) | Real | 4 | 91,720 |
| Grid_Longitude | Lon locations of the grid points (± 90 degrees) | Real | 4 | 91,720 |
| Instrument_Latitude | Lat locations of the actual observations (± 90 degrees) | Real | 4 | 91,720 |
| Instrument_Longitude | Lon locations of the actual observations (± 90 degrees) | Real | 4 | 91,720 |
| Granule_Number | Granule number | Real | 4 | 91,720 |
| View_Angle | The view angle of the current IASI FOV (± 90 degrees) | Real | 4 | 91,720 |
| Solar_Zenith | The solar zenith of the current IASI FOV (0-90 degrees) | Real | 4 | 91,720 |
| Solar_Azimuth | The solar azimuth of the current IASI FOV (0-180 degrees) | Real | 4 | 91,720 |
| Satellite_Zenith | The satellite zenith of the current IASI FOV (0-90 degrees) | Real | 4 | 91,720 |
| Satellite_Azimuth | The satellite azimuth of the current IASI FOV (0-180 degrees) | Real | 4 | 91,720 |
| Satellite_Height | The satellite height of the current IASI FOV (km) | Real | 4 | 91,720 |
| AVHRR_Mean_Radiances | (Missing in the simulated data) These are for 7 FOV classes on 6 AVHRR channels | Real | 4 | 91,720,7,6 |
| AVHRR_Std_Radiances | Missing in the simulated data | Real | 4 | 91,720,7,6 |
| IASI_Radiance | IASI radiances (mW/m2/cm-1/sr) | Real | 4 | 91,720,8461 |
| Quality_Flag | 0 = accepted, 1 = rejected | Real | 4 | 91,720 |
| Dice |  | Real | 4 | 91,720 |
| Topography | The height of the surface above sea level (meters). | Real | 4 | 91,720 |
| Land_Fraction | The fraction of land coverage (0-1). | Real | 4 | 91,720 |

The date information in the file names is defined as:

${Year} = the 4-digit year

${Month} = 2-digit month

${Day} = 2-digit day of month

### Intended Users

STAR validation scientists.

### Access

These files reside at:

$BASE/SATELLITE_DATA/MetOpA/NRT_DATA/${Year}/${Month}/${Day}/IASI_DATA/Global_Grids/CCR_FullRes_Grids/M02_IACC${Year}${Month}${Day}.asc

$BASE/SATELLITE_DATA/MetOpA/NRT_DATA/${Year}/${Month}/${Day}/IASI_DATA/Global_Grids/CCR_FullGlobal_Grids/M02_IACC${Year}${Month}${Day}.desc

Files are sent to the DDS by the scripts that generate them.  All grids are pulled from the DDS by STAR into the STAR Collaborative Environment and stored locally.

dds.nesdis.noaa.gov:push

POC – Nichols, Catherine L

5200 Auth Road, Room 0315, Building: FB4

Suitland, MD 20746 – 4301

Phone: (301)457-5245

Fax:      (301)457-5199

E-mail: cathy.nichols@noaa.gov

## IASI Matchups

IASI matchups data files

A binary files containing the observed IASI L1CT data collocated and saved at specified locations.

### Purpose

These data sets are used for matching of IASI L1CT data with different instruments (e.g. radiosondes, aircraft, satellite measurement, etc.).

### Data File Description

These files contain IASI radiances at a set of specified instrument locations. They are direct access binary format files containing all the instrument data on a single instrument field of regard at a given radiosonde launch time and location.  Each file contains all the matchup data for the given day plus the last three hours of the previous day and the first three hours of the following day. The date information in the file names is defined as:

${Year} = the 4-digit year

${Month} = 2-digit month

${Day} = 2-digit day of month

${Doy} = 3-digit day of year

The file contains two header records (described in Tables 23 and 24).  Table 25 describes the content of the data records.  Each data record consists of all the IASI data within the 2X2 cluster of FOVs.  The top of the record contains the information about the particular sonde time and launch location.  The FOR latitude and longitude is the center averaged latitude and longitude of the 4 IASI FOVs.  Nominal file daily sizes are between 370 and 390 MB.

As a record is read from the file, the contents of each array must then be mapped into the variables shown in Tables 25.  The values must be recast from real values to what is shown in column three under “type”.  Table 23 and 24 show this mapping for the first and second headers, respectively.  Table 25 shows the contents of one of the many data records that follow the two headers.  The fifth column call “dim length” is the number of elements that are used to store each variable in the matchup file, but it is also the number of elements required to store each individual output variable after the remapping and recasting.

Table 24. Matchup Header Record Number 1

| Variable | Description | Type | Size | Dim Length |
| --- | --- | --- | --- | --- |
| Actual_Number_of_Records | Total number of records in the file including the 2 header records | Integer | 4 | 1 |
| Record_Length | Number of bytes per record | Integer | 4 | 1 |
| Number_of_Dots | The number of IASI FOV/FOR. This is always = 4 | Integer | 4 | 1 |
| Number_of_Dice | This is the actual number of matched IASI field of regard clusters | Integer | 4 | 1 |
| Number_of_IASI_Channels | The number of IASI channels (8461) | Integer | 4 | 1 |
| Number_of_AVHRR_Channels | The number of AVHRR channels (6) | Integer | 4 | 1 |
| Number_of_AVHRR_FOV_Classes | The number of AVHRR FOV classes (7) | Integer | 4 | 1 |
| IASI_Channels | The IASI channel numbers (1-8461) | Integer | 4 | 8461 |
| AVHRR_Channels | The AVHRR channel numbers (1-6) | Integer | 4 | 6 |
| AVHRR_Frequencies | The AVHRR channel frequencies (cm-1). | Real | 4 | 6 |
| AVHRR_FOV_Classes | The AVHRR FOV classes (1-7) | Integer | 4 | 7 |

Table 25. Matchup Header Record Number

| Variable | Description | Type | Size | Dim Length |
| --- | --- | --- | --- | --- |
| IASI_Frequencies | The IASI channel frequencies (cm-1) | Real | 4 | 8461 |

Table 26. Matchup Data Record

| Variable | Description | Type | Size | Dim Length |
| --- | --- | --- | --- | --- |
| Latitude | Sonde Latitude (± 90 degrees). | Real | 4 | 1 |
| Longitude | Sonde Longitude (± 180 degrees). | Real | 4 | 1 |
| Year | Sonde launch year. | Integer | 4 | 1 |
| Month | Sonde launch Month. | Integer | 4 | 1 |
| Day | Sonde launch day. | Integer | 4 | 1 |
| Hour | Sonde launch hour. | Integer | 4 | 1 |
| Minute | Sonde launch minute. | Integer | 4 | 1 |
| Maximum_Distance | Distance tolerance = 100 km. | Real | 4 | 1 |
| Time_Separation | Time tolerance = 180 minutes. | Real | 4 | 1 |
| Distance | Actual distance (km) from the sonde to the matched IASI observation. | Real | 4 | 1 |
| FOR_Latitude | The matched IASI FOR latitude (± 90 degrees). | Real | 4 | 1 |
| FOR_Longitude | The matched IASI FOR longitude (± 180 degrees). | Real | 4 | 1 |
| Year | IASI observation year. | Integer | 4 | 1 |
| Month | IASI observation month. | Integer | 4 | 1 |
| Day | IASI observation day. | Integer | 4 | 1 |
| Hour | IASI observation hour | Integer | 4 | 1 |
| Minute | IASI observation minute. | Integer | 4 | 1 |
| Seconds | IASI observation seconds | Integer | 4 | 1 |
| The following block of variables is repeated 4 times. Each block represents the data for 1 of the 4 IASI FOVs. |
| Latitude | The latitudes of each matched IASI FOV (± 90 degrees). | Real | 4 | 1 |
| Longitude | The longitudes of each matched IASI FOV (± 180 degrees). | Real | 4 | 1 |
| Footprint | The IASI field of regard footprint number (1-30) along the scan line. | Integer | 4 | 1 |
| View_Angle | The view angles of each matched IASI FOV (± 90 degrees). | Real | 4 | 1 |
| Satellite_Height | The satellite height of each matched IASI FOV (km). | Real | 4 | 1 |
| Satellite_Zenith | The satellite zenith of each matched IASI FOV (0 - 90 degrees). | Real | 4 | 1 |
| Satellite_Azimuth | The satellite azimuth of each matched IASI FOV (0-180 degrees). | Real | 4 | 1 |
| Solar_Zenith | The solar zenith of each matched IASI FOV (0-90 degrees). | Real | 4 | 1 |
| Solar_Azimuth | The solar azimuth of each matched IASI FOV (0-180 degrees). | Real | 4 | 1 |
| Ascending_Descending | The ascending-descending status of each matched IASI FOV (0 = ascending, 1=descending). | Integer | 4 | 1 |
| Orbit_Number | The number of the orbit (since launch) from which the current granule was obtained. | Integer | 4 | 1 |
| GQisFlagQual | The QC flag of each matched IASI FOV (0=good, 1=bad). | Integer | 4 | 1 |
| GQisQualIndex | The sounder spectra QC index of each matched IASI FOV. | Real | 4 | 1 |
| GQisQualIndexLoc | The IASI/AVHRR collocation index of each matched IASI FOV. | Real | 4 | 1 |
| GQisQualIndexRad | The radiometric QC flag of each matched IASI FOV. | Real | 4 | 1 |
| GQisQualIndexSpect | The spectral quality index of each matched IASI FOV. | Real | 4 | 1 |
| GQisSysTecSondQual | The sounder quality index of each matched IASI FOV. | Real | 4 | 1 |
| Topography | The height of the surface above sea level (meters). | Real | 4 | 1 |
| Land_Fraction | The fraction of land coverage (0-1). | Real | 4 | 1 |
| IASI_Radiances | The IASI radiances (mW/m2/cm-1/sr). | Real | 4 | 8461 |
| AVHRR_Mean_Radiances | The mean AVHRR radiances (mW/m2/cm-1/sr). | Real | 4 | 6*7 |
| AVHRR_Std_Radiances | The standard deviation of the AVHRR radiances (mW/m2/cm-1/sr). | Real | 4 | 6*7 |
| IASI_Image | IASI sub-pixel image radiances (mW/m2/cm-1/sr). | Real | 4 | 32*32 |

### Intended Users

STAR validation scientists. STAR climate scientists for offline level 1 and 2 product validation and reprocessing.

### Access

The binary global matchup file resides at:

$BASE/SATELLITE_DATA/MetOpA/NRT_DATA/${Year}/${Month}/${Day}/IASI_DATA/Global_Matchups/L1C/m02_iasi_radiosonde_machups_${Doy}_${Year}.binary

Files are sent to the DDS by the scripts that generate them: dds.nesdis.noaa.gov:push

POC – Nichols, Catherine L

5200 Auth Road, Room 0315, Building: FB4

Suitland, MD 20746 – 4301

Phone: (301)457-5245

Fax:      (301)457-5199

E-mail: cathy.nichols@noaa.gov

## EUMETSAT Level 2 BUFR Files

## Purpose

EUMETSAT Level 2 data files in BUFR format.

Data File Description

Description of these files is presented in section 2.10.2 of this document.

Intended Users

AFWA

POC: System Duty Officer

401-294-2586

sdo@afwa.af.mil

AFWA/XPSI

106 Peacekeeper Dr.

Offutt AFB, NE 68113

Access

These data files are pushed into remote server (GFT) (maco.nesdis.noaa.gov).

POC - Simon Elliott

Meteorological Product Implementation Manager, Operations department

Address: Am Kavalleriesand 31

Darmstadt, Hessen, 64295

Germany

Telephone:        (+49) 6151 807 385

Fax:	               (+49) 6151 807 385

E-Mail Address: Simon.Elliott@eumetsat.int

OSDPD GFT Point of Contact

Vincent Tabor

NSOF, 4231 Suitland Road, Suitland, MD, 20746

Tel: (301) 457-5247

E-mail: Vicent.Tabor@noaa.gov

## 2-Scan Global File

2 scans single daily global coverage binary file.

### Purpose

This thinned file is used to generate a binary file for offline eigenvector coefficient file generation.  These coefficients are, in turn, used for generating the principal components and reconstructed radiances.

### Data File Description

The 2-Scan files are Fortran direct access binary files.  Each record length is exactly 34260 bytes.  Each data record contains all the data for a single IASI FOV.  The file contains a single day’s data from 480 granules where scan lines 1 and 12 were selected from each.  Each 2-scan record, including the two header records at the top of the file, are written, and must be read, as a one real-valued, single dimension, 4-byte array.  This array must have 8565 elements (34260 bytes/4 bytes).  The contents of each array read from the file must then be mapped into the variables shown in table 26-28.  The values must be recast from real values to what is shown in column three under “type”.  Table 26 and 27 show this mapping for header 1 and 2, respectively.  Table 28 shows the contents of one of the many data records that follow the two headers.  The fifth column call “dim length” is the number of elements that are used to store each variable in the matchup file, but it is also the number of elements required to store each individual output variable after the remapping and recasting.

Table 27. 2-Scan Header Record Number 1

| Variable | Description | Type | Size | Dim Length |
| --- | --- | --- | --- | --- |
| Total_Number_of_Records | Total number of records in the file | Integer | 4 | 1 |
| Record_Length | Number of bytes per record | Integer | 4 | 1 |
| Number_of_Dots | The number of IASI FOV/FOR. This is always = 4 | Integer | 4 | 1 |
| Number_of_Dice | This is the number of matched IASI FORs within the file | Integer | 4 | 1 |
| Number_of_IASI_Channels | The number of IASI channels | Integer | 4 | 1 |
| Number_of_AVHRR_Channels | The number of AVHRR channels | Integer | 4 | 1 |
| Number_of_AVHRR_FOV_Classes | The number of AVHRR FOV classes | Integer | 4 | 1 |
| IASI_Channels | The IASI channel numbers | Integer | 4 | 8461 |
| AVHRR_Channels | The AVHRR channel numbers | Integer | 4 | 6 |
| AVHRR_Frequencies | The AVHRR channel frequencies | Real | 4 | 6 |
| AVHRR_FOV_Classes | The AVHRR FOV classes | Integer | 4 | 7 |

Table 28. 2-Scan Header Record Number 2

| Variable | Description | Type | Size | Dim Length |
| --- | --- | --- | --- | --- |
| IASI_Frequencies | The IASI channel frequencies (cm-1). | Real | 4 | 8461 |

Table 29. 2-Scan Data Record

| Variable | Description | Type | Size | Dim Length |
| --- | --- | --- | --- | --- |
| Scan_Line | Scan line number within the current granule (1-23) | Integer | 4 | 1 |
| AMSU_FOV | The AMSU FOV number (1-30) for the current scan line. This is the same as the IASI FOR number. | Integer | 4 | 1 |
| IASI_FOV | The IASI FOV number (1-120) for the current scan line. | Integer | 4 | 1 |
| Time | The current time of observation (in seconds since January 1st 1970). | Real | 4 | 1 |
| Latitude | The latitude of the current IASI FOV (± 90 degrees). | Real | 4 | 1 |
| Longitude | The longitude of the current IASI FOV (± 180 degrees). | Real | 4 | 1 |
| View_Angle | The view angle of the current IASI FOV (± 90 degrees). | Real | 4 | 1 |
| Satellite_Height | The satellite height of the current IASI FOV (km). | Real | 4 | 1 |
| Satellite_Zenith | The satellite zenith of the current IASI FOV (0-90 degrees). | Real | 4 | 1 |
| Satellite_Azimuth | The satellite azimuth of the current IASI FOV (0-180 degrees). | Real | 4 | 1 |
| Solar_Zenith | The solar zenith of the current IASI FOV (0-90 degrees). | Real | 4 | 1 |
| Solar_Azimuth | The solar azimuth of the current IASI FOV (0-180 degrees). | Real | 4 | 1 |
| Ascending_Descending | The ascending-descending status of the current orbit (0 = ascending, 1=descending) | Integer | 4 | 1 |
| Orbit_Number | The number of the orbit (since launch) from which the current granule was obtained. | Integer | 4 | 1 |
| GQisFlagQual | The QC flag of each matched IASI FOV (0=good, 1=bad) | Integer | 4 | 1 |
| GQisQualIndex | The sounder spectra QC index of each matched IASI FOV | Real | 4 | 1 |
| GQisQualIndexLoc | The IASI/AVHRR collocation index of each matched IASI FOV | Real | 4 | 1 |
| GQisQualIndexRad | The radiometric QC flag of each matched IASI FOV | Real | 4 | 1 |
| GQisQualIndexSpect | The spectral quality index of each matched IASI FOV | Real | 4 | 1 |
| GQisSysTecSondQual | The sounder quality index of each matched IASI FOV | Real | 4 | 1 |
| IASI_Radiances | The IASI radiances (mW/m2/cm-1/sr). | Real | 4 | 8461 |
| AVHRR_Mean_Radiances | The mean AVHRR radiances (mW/m2/cm-1/sr). | Real | 4 | 6*7 |
| AVHRR_Std_Radiances | The standard deviation of the AVHRR radiances (mW/m2/cm-1/sr). | Real | 4 | 6*7 |

# Intended Users

STAR validation scientists.

### Access

This file resides at:

$BASE/SATELLITE_DATA/MetOpA/NRT_DATA/${Year}/${Month}/${Day}/IASI_DATA/Global_Binaries/2Scan_Global_Binaries/iasi_2scans_8461_${Year}${Month}${Day}.binary

This file is sent to the DDS for access by the STAR development validation team.

POC – Nichols, Catherine L

5200 Auth Road, Room 0315, Building: FB4

Suitland, MD 20746 – 4301

Phone: (301)457-5245

Fax:      (301)457-5199

E-mail: cathy.nichols@noaa.gov

AMSU-A Matchups

AMSU-A data matchup files.

A binary files containing the observed AMSU-A data collocated and saved at specified locations.

### Purpose

These data sets are used for matching of AMSU-A data with different instruments (e.g. radiosondes, aircraft, satellite measurement, etc.).

### Data File Description

This is a direct access binary file containing all the instrument data on a single instrument field of regard at a given radiosonde launch time and location.  Each file contains all the data for the given day plus the last three hours of the previous day and the first three hours of the following day.  The date information in the file names is defined as:

${Year} = the 4-digit year

${Month} = 2-digit month

${Day} = 2-digit day of month

${Doy} = 3-digit day of year

Table 30. AMSU-A Matchup Header Record Number 1

| Variable | Description | Type | Size | Dim Length |
| --- | --- | --- | --- | --- |
| Actual_Number_of_Records | Total number of records in the file including the 2 header records | Integer | 4 | 1 |
| Record_Length | Number of bytes per record | Integer | 4 | 1 |
| Number_of_Dice | This is the actual number of matched AMSU-A observations | Integer | 4 | 1 |
| Number_of_AMSUA_Channels | The number of AMSUA channels (15) | Integer | 4 | 1 |
| AMSUA_Channels | The AMSUA channel numbers (1-15) | Integer | 4 | 15 |

Table 31. AMSU-A Matchup Header record Number 2

| Variable | Description | Type | Size | Dim Length |
| --- | --- | --- | --- | --- |
| AMSUA_Frequencies | The AMSUA channel frequencies (cm-1) | Real | 4 | 15 |

Table 32. AMSU-A Matchup Data record

| Variable | Description | Type | Size | Dim Length |
| --- | --- | --- | --- | --- |
| Latitude | Sonde Latitude (± 90 degrees). | Real | 4 | 1 |
| Longitude | Sonde Longitude (± 180 degrees). | Real | 4 | 1 |
| Year | Sonde launch year. | Integer | 4 | 1 |
| Month | Sonde launch Month. | Integer | 4 | 1 |
| Day | Sonde launch day. | Integer | 4 | 1 |
| Hour | Sonde launch hour. | Integer | 4 | 1 |
| Minute | Sonde launch minute. | Integer | 4 | 1 |
| Maximum_Distance | Distance tolerance = 100 km. | Real | 4 | 1 |
| Time_Separation | Time tolerance = 180 minutes. | Real | 4 | 1 |
| Distance | Actual distance (km) from the sonde to the matched AMSU-A observation. | Real | 4 | 1 |
| FOR_Latitude | The matched AMSU-A FOR latitude (± 90 degrees). | Real | 4 | 1 |
| FOR_Longitude | The matched AMSU-A FOR longitude (± 180 degrees). | Real | 4 | 1 |
| Year | AMSU-A observation year. | Integer | 4 | 1 |
| Month | AMSU-A observation year. | Integer | 4 | 1 |
| Day | AMSU-A observation day. | Integer | 4 | 1 |
| Hour | AMSU-A observation hour. | Integer | 4 | 1 |
| Minute | AMSU-A observation minute. | Integer | 4 | 1 |
| Second | AMSU-A observation seconds. | Integer | 4 | 1 |
| Latitude | The latitudes of each matched AMSU-A FOV (± 90 degrees). | Real | 4 | 1 |
| Longitude | The longitudes of each matched AMSU-A FOV (± 180 degrees). | Real | 4 | 1 |
| Footprint | The AMSU footprint number (1-30) along the scan line. | Integer | 4 | 1 |
| View_Angle | The view angles of each matched AMSU-A FOV (± 90 degrees). | Real | 4 | 1 |
| Satellite_Height | The satellite height of each matched AMSU-A FOV (km). | Real | 4 | 1 |
| Satellite_Zenith | The satellite zenith of each matched AMSU-A FOV (0 - 90 degrees). | Real | 4 | 1 |
| Satellite_Azimuth | The satellite azimuth of each matched AMSU-A FOV (0-180 degrees). | Real | 4 | 1 |
| Solar_Zenith | The solar zenith of each matched AMSU-A FOV (0-90 degrees). | Real | 4 | 1 |
| Solar_Azimuth | The solar azimuth of each matched AMSU-A FOV (0-180 degrees). | Real | 4 | 1 |
| Ascending_Descending | The ascending-descending status of each matched AMSU-A FOV (0 = ascending, 1=descending). | Integer | 4 | 1 |
| Topography | The height of the surface above sea level (meters). | Real | 4 | 1 |
| Land_Fraction | The fraction of land coverage (0-1). | Real | 4 | 1 |
| AMSUA_Radiances | The AMSU-A radiances (mW/m2/cm-1/sr). | Real | 4 | 15 |
| Quality_Flag | The AMSU-A Quality Flag (0=good, else bad). | Integer | 4 | 15 |

    - Intended Users

STAR validation scientists. STAR climate scientists.

    - Access

The binary global matchup file resides at:

$BASE/SATELLITE_DATA/MetOpA/NRT_DATA/${Year}/${Month}/${Day}/IASI_DATA/Global_Matchups/L1B/amsua_radiosonde_machups_${Doy}_${Year}.binary

Files are sent to the DDS by the scripts that generate them: dds.nesdis.noaa.gov:push

POC – Nichols, Catherine L

5200 Auth Road, Room 0315, Building: FB4

Suitland, MD 20746 – 4301

Phone: (301)457-5245

Fax:      (301)457-5199

E-mail: cathy.nichols@noaa.gov

  - MHS Matchups

MHS data matchup files.

A binary files containing the observed MHS data collocated and saved at specified locations.

### Purpose

These data sets are used for matching of MHS data with different instruments (e.g. radiosondes, aircraft, satellite measurement, etc.).

### Data File Description

This is a direct access binary file containing all the instrument data on a single instrument field of regard at a given radiosonde launch time and location.  Each file contains all the data for the given day plus the last three hours of the previous day and the first three hours of the following day.  The date information in the file names is defined as:

${Year} = the 4-digit year

${Month} = 2-digit month

${Day} = 2-digit day of month

${Doy} = 3-digit day of year

Table 33. MHS Matchup Header Record Number 1

| Variable | Description | Type | Size | Dim Length |
| --- | --- | --- | --- | --- |
| Actual_Number_of_Records | Total number of records in the file including the 2 header records | Integer | 4 | 1 |
| Record_Length | Number of bytes per record | Integer | 4 | 1 |
| Number_of_Dots | The total number of MHS FOVs with each data record. | Integer | 4 | 1 |
| Number_of_Dice | This is the actual number of matched MHS field of regard clusters. | Integer | 4 | 1 |
| Number_of_MHS_Channels | The number of MHS channels (5) | Integer | 4 | 1 |
| MHS_Channels | The MHS channel numbers (1-5) | Integer | 4 | 5 |

Table 34. MHS Matchup Header Record Number 2

| Variable | Description | Type | Size | Dim Length |
| --- | --- | --- | --- | --- |
| MHS_Frequencies | The MHS channel frequencies (cm-1) | Real | 4 | 5 |

Table 35. MHS Matchup Data Record

| Variable | Description | Type | Size | Dim Length |
| --- | --- | --- | --- | --- |
| Latitude | Sonde Latitude (± 90 degrees). | Real | 4 | 1 |
| Longitude | Sonde Longitude (± 180 degrees). | Real | 4 | 1 |
| Year | Sonde launch year. | Integer | 4 | 1 |
| Month | Sonde launch Month. | Integer | 4 | 1 |
| Day | Sonde launch day. | Integer | 4 | 1 |
| Hour | Sonde launch hour. | Integer | 4 | 1 |
| Minute | Sonde launch minute. | Integer | 4 | 1 |
| Maximum_Distance | Distance tolerance = 100 km. | Real | 4 | 1 |
| Time_Separation | Time tolerance = 180 minutes. | Real | 4 | 1 |
| Distance | Actual distance (km) from the sonde to the matched MHS observation. | Real | 4 | 1 |
| FOR_Latitude | The matched MHS FOR latitude (± 90 degrees). | Real | 4 | 1 |
| FOR_Longitude | The matched MHS FOR longitude (± 180 degrees). | Real | 4 | 1 |
| Year | MHS center FOV observation year. | Integer | 4 | 1 |
| Month | MHS center FOV observation month. | Integer | 4 | 1 |
| Day | MHS center FOV observation day. | Integer | 4 | 1 |
| Hour | MHS center FOV observation hour. | Integer | 4 | 1 |
| Minute | MHS center FOV observation minute. | Integer | 4 | 1 |
| Second | MHS center FOV observation second. | Integer | 4 | 1 |
| The following block of variables is repeated 9 times. Each block represents the data for 1 of the 9 MHS FOVs. |
| Latitude | The latitudes of each matched MHS FOV (± 90 degrees). | Real | 4 | 1 |
| Longitude | The longitudes of each matched MHS FOV (± 180 degrees). | Real | 4 | 1 |
| Footprint | The MHS field of regard (1-30) along the scan line. | Integer | 4 | 1 |
| View_Angle | The view angles of each matched MHS FOV (± 90 degrees). | Real | 4 | 1 |
| Satellite_Height | The satellite height of each matched MHS FOV (km). | Real | 4 | 1 |
| Satellite_Zenith | The satellite zenith of each matched MHS FOV (0 - 90 degrees). | Real | 4 | 1 |
| Satellite_Azimuth | The satellite azimuth of each matched MHS FOV (0-180 degrees). | Real | 4 | 1 |
| Solar_Zenith | The solar zenith of each matched MHS FOV (0-90 degrees). | Real | 4 | 1 |
| Solar_Azimuth | The solar azimuth of each matched MHS FOV (0-180 degrees). | Real | 4 | 1 |
| Ascending_Descending | The ascending-descending status of each matched MHS FOV (0 = ascending, 1=descending). | Integer | 4 | 1 |
| MHS_Radiances | The MHS radiances (mW/m2/cm-1/sr). | Real | 4 | 5 |
| Quality_Flag | The MHS-A Quality Flag (0=good, else bad). | Integer | 4 | 5 |

    - Intended Users

    - STAR validation scientists. STAR climate scientists.

    - Access

The binary global matchup file resides at:

$BASE/SATELLITE_DATA/MetOpA/NRT_DATA/${Year}/${Month}/${Day}/IASI_DATA/Global_Matchups/L1B/mhs_radiosonde_machups_${Doy}_${Year}.binary

Files are sent to the DDS by the scripts that generate them: dds.nesdis.noaa.gov:push

POC – Nichols, Catherine L

5200 Auth Road, Room 0315, Building: FB4

Suitland, MD 20746 – 4301

Phone: (301)457-5245

Fax:      (301)457-5199

E-mail: cathy.nichols@noaa.gov

  - IASI L2 Matchups

L2 data matchup files

Purpose

These data sets are used for matching Level 2 data with different instruments (e.g. radiosondes, aircraft, satellite measurement, etc.).

Data File Description

This is a direct access binary file containing all the instrument data on a single instrument field of regard at a given radiosonde launch time and location.  Each file contains all the data for the given day plus the last three hours of the previous day and the first three hours of the following day.  The date information in the file names is defined as:

${Year} = the 4-digit year

${Month} = 2-digit month

${Day} = 2-digit day of month

${Doy} = 3-digit day of year

Table 36. IASI L2 matchup Header Record Number 1

| Variable | Description | Type | Size | Dim Length |
| --- | --- | --- | --- | --- |
| Actual_Number_of_Records | Total number of records in the file including the 1 header record | Integer | 4 | 1 |
| Record_Length | Number of bytes per record | Integer | 4 | 1 |
| Number_of_Dice | This is the actual number of matched IASI L2 observations. | Integer | 4 | 1 |
| Number_of_P_Levels | The number of pressure levels | Integer | 4 | 1 |
| Number_of_MW_Spectral_Pts | The number of microwave spectral points | Integer | 4 | 1 |
| Number_of_Surf_Emis_Hinge_Pts | The number of surface emissivity hinge points | Integer | 4 | 1 |
| Number_of_Cloud_Emis_Hinge_Pts | The number of cloud emissivity hinge points | Integer | 4 | 1 |
| Number_of_Cloud_Layers | The number of cloud layers | Integer | 4 | 1 |

Table 37. IASI L2 Matchup Data record

| Variable | Description | Type | Size | Dim Length |
| --- | --- | --- | --- | --- |
| Latitude | Sonde Latitude (± 90 degrees). | Real | 4 | 1 |
| Longitude | Sonde Longitude (± 180 degrees). | Real | 4 | 1 |
| Year | Sonde launch year. | Integer | 4 | 1 |
| Month | Sonde launch Month. | Integer | 4 | 1 |
| Day | Sonde launch day. | Integer | 4 | 1 |
| Hour | Sonde launch hour. | Integer | 4 | 1 |
| Minute | Sonde launch minute. | Integer | 4 | 1 |
| Maximum_Distance | Distance tolerance = 100 km. | Real | 4 | 1 |
| Time_Separation | Time tolerance = 180 minutes. | Real | 4 | 1 |
| Distance | Actual distance (km) from the sonde to the matched IASI observation. | Real | 4 | 1 |
| Year | IASI observation year. | Integer | 4 | 1 |
| Month | IASI observation month. | Integer | 4 | 1 |
| Day | IASI observation day. | Integer | 4 | 1 |
| Hour | IASI observation hour | Integer | 4 | 1 |
| Minute | IASI observation minute. | Integer | 4 | 1 |
| Seconds | IASI observation seconds | Integer | 4 | 1 |
| Latitude | The latitude of the matched IASI FOR (± 90 degrees). | Real | 4 | 1 |
| Longitude | The longitude of the matched IASI FOR (± 180 degrees). | Real | 4 | 1 |
| Footprint | The IASI field of regard footprint number (1-30) along the scan line. | Integer | 4 | 1 |
| View_Angle | The view angle of the matched IASI FOR (± 90 degrees). | Real | 4 | 1 |
| Satellite_Height | The satellite height of the matched IASI FOR (km). | Real | 4 | 1 |
| Solar_Zenith | The solar zenith of the matched IASI FOR (0-90 degrees). | Real | 4 | 1 |
| Ascending_Descending | The ascending-descending status of the matched IASI FOR (0 = ascending, 1=descending). | Integer | 4 | 1 |
| Topography | The height of the surface above sea level (meters). | Real | 4 | 1 |
| Land_Fraction | The fraction of land coverage (0-1). | Real | 4 | 1 |
| Surface_Pressure | Surface pressure in millibars. | Real | 4 | 1 |
| Skin_Temperature | Skin temperature in Kelvin. | Real | 4 | 1 |
| Mean_CO2 | Mean CO2 in ppm. | Real | 4 | 1 |
| MW_Surface_Class | Microwave surface class. | Integer | 4 | 1 |
| MW_Surface_Emis | Microwave surface emissivity. | Real | 4 | 1 |
| Bottom_Level_Index | The index of the pressure array that marks the pressure at the surface. | Integer | 4 | 1 |
| N_Smw_Per_FOV | The number of microwave spectral points within each layer | Integer | 4 | 1 |
| nemis_Per_FOV | The number of surface emissivity hinge points within each layer | Integer | 4 | 1 |
| ncemis_Per_FOV | The number of cloud emssivity hinge points within each layer | Integer | 4 | 1 |
| ncld_Per_FOV | The number of cloud layers points within each layer | Integer | 4 | 1 |
| Quality_Flag | Retrieval quality flag (0=accept, 1=reject). | Integer | 4 | 1 |
| The following block of 2 variables is repeated Number_of_Cloud_Layers (nominally 8) times. The user of these data must check the header to obtain the value of Number_of_Cloud_Layers. |
| Cloud_Top_Pressure | Cloud top pressure in millibars. | Real | 4 | 1 |
| Cloud_Top_Fraction | Cloud top fractional coverage (0-1). | Real | 4 | 1 |
| The following block of 12 variables is repeated Number_of_P_Levels (nominally 100) times. The user of these data must check the header to obtain the value of Number_of_P_Levels. |
| Pressure | Pressure with the current layer in millibars. | Real | 4 | 1 |
| Temperature | Temperature within the current layer in Kelvin | Real | 4 | 1 |
| H2O | H2O layer column density. | Real | 4 | 1 |
| O3 | O3 layer column density (molecules/cm2). | Real | 4 | 1 |
| Liquid_H2O | Liquid H2O layer column density (molecules/cm2). | Real | 4 | 1 |
| Ice_Liquid_Flag | Ice liquid flag (0=water, 1=ice). | Integer | 4 | 1 |
| CO | CO layer column density (molecules/cm2). | Real | 4 | 1 |
| CH4 | CH4 layer column density (molecules/cm2). | Real | 4 | 1 |
| CO2 | CO2 mixing ratio (ppm). | Real | 4 | 1 |
| N2O | N2O layer column density (molecules/cm2). | Real | 4 | 1 |
| SO2 | SO2 layer column density (molecules/cm2). | Real | 4 | 1 |
| HNO3 | HNO3 layer column density (molecules/cm2). | Real | 4 | 1 |
| The following block of 2 variables is repeated Number_of_MW_Spectral_Pts (nominally 16) times. The user of these data must check the header to obtain the value of Number_of_MW_Spectral_Pts. |
| MW_Frequency | Microwave frequency (cm-1). | Real | 4 | 1 |
| MW_Emis | Microwave emissivity. | Real | 4 | 1 |
| The following block of 3 variables is repeated Number_of_Surf_Emis_Hinge_Pts (nominally 100) times. The user of these data must check the header to obtain the value of Number_of_Surf_Emis_Hinge_Pts. |
| IR_Emis_Freq | Infrared emissivity hinge point frequencies (cm-1). | Real | 4 | 1 |
| IR_Surface_Emis | Infrared surface emissivity | Real | 4 | 1 |
| IR_Surface_Refl | Infrared surface reflectances (percent). | Real | 4 | 1 |
| The following block of 3 variables is repeated Number_of_Cloud_Emis_Hinge_Pts (nominally 100) times. The user of these data must check the header to obtain the value of Number_of_Cloud_Emis_Hinge_Pts. |
| The following block of 3 variables is repeated Number_of_Cloud_Layers (nominally 8) times. The user of these data must check the header to obtain the value of Number_of_Cloud_Layers. |
| Cloud_Freq | Cloud infrared frequencies (cm-1). | Real | 4 | 1 |
| Cloud_Refl | Cloud infrared reflectivity. | Real | 4 | 1 |
| Cloud_Emis | Cloud infrared emissivity. | Real | 4 | 1 |

    - Intended Users

    - STAR validation scientists. STAR climate scientists.

    - Access

The binary global matchup file resides at:

$BASE/SATELLITE_DATA/MetOpA/NRT_DATA/${Year}/${Month}/${Day}/IASI_DATA/Global_Matchups/L2/iasi_l2_radiosonde_machups_${Doy}_${Year}.binary

Files are sent to the DDS by the scripts that generate them: dds.nesdis.noaa.gov:push

POC – Nichols, Catherine L

5200 Auth Road, Room 0315, Building: FB4

Suitland, MD 20746 – 4301

Phone: (301)457-5245

Fax:      (301)457-5199

E-mail: cathy.nichols@noaa.gov

  - IASI L2 NetCDF Files

    - Purpose

These files will be archived to Comprehensive Large Array-data Stewardship System (CLASS).

    - Data File Description

The Level 2 NetCDF granule files are generated from main_iasi_l2_to_netcdf .  The input files are the native binary format retrieval output files.  This program is part of the L2 Processing Unit.  The files they create are produced in the following directory:

$BASE/SATELLITE_DATA/MetOpA/NRT_DATA/${Year}/${Month}/${Day}/IASI_DATA/Granule-${Granule_Number}/level2

where:

${Year} = the 4-digit year

${Month} = 2-digit month

${Day} = 2-digit day of month

${Granule_Number} = 3-digit granule number (1-480)

The following NetCDF intermediate file is produced for each granule with the following name structure.

iasi_l2_${Year}${Month}${Day}_Granule-${Granule_Number}.nc

where:

$Year = 4-digit year

$Month = 2-digit month

$Day = 2-digit day

$Granule_Number = 3-digit granule number

This is full spatial and spectral resolution file.  It’s starting and ending scan lines and footprints match those of the full resolution Level 1C IASI, AMSU-A, and MHS L1B NetCDF files for the same granule number described above.  This file is used in both the Global Grids and Global Binaries units. It is also used to generate additional NetCDF file which is archived to CLASS:

IASI_L2_M02_V${YYMMDD}_${YYYYMODDHHMMSS}Z_${YYYYMODDHHMMSS}Z.nc

where:

IASI = Instrument name

L2  = the product type

M02 = Satellite ID (M02 = Metop-A)

V = Version indicator

$YYMMDD = 2-digit year + 2-digit month + 2-digit day (the date the version was created)

Sensing date/time string = Date/time of observations given in the following format YYYYMODDHHMMSSZ.  The first string indicates the starting date/time and the second string indicates the ending date/time.

nc = File type extension indicates NetCDF format

Where:

The string “YYYYMODDHHMMSSZ” is a date string containing the following components of time:

YYYY = 4 digit year (e.g. 2005)

MO = 2 digit month (01-12)

DD = day of month (01-31)

HH = hour (00-23)

MM = minute (00-59)

SS = seconds (00-59)

Z = Greenwich Mean Time (GMT)

Here is an example of a file created using software version 071016 on February 11th, 2008.  The granule starts at 04:23:59 GMT and ends at 04:26:55 GMT:

IASI_L2_M02_V071016_20080211042359Z_20080211042655Z.nc

    - This granule file has an associated metadata xml file which is archived to CLASS.

Table 38. IASI L2 NetCDF Header

| dimensions: variables: | Number_of_Dice = 660 ; // Number IASI fields of regard written (max nobs) Number_of_P_Levels = 100 ; // Number of pressure levels (max nl2lev) Number_of_MW_Spectral_Pts = 16 ; // Number of microwave spectral points (max N_Smw) Number_of_Surf_Emis_Hinge_Pts = 100 ; // Number of surface emissivity hinge points (max nemis) Number_of_Cloud_Emis_Hing_Pts = 100 ; // Number of cloud emissivity hinge points (max ncemis) Number_of_Cloud_Layers = 8 ; // Number of cloud layers (max ncld) Number_of_Stability_Parameters = 16 ; // Number of stability parameters long Dice(Number_of_Dice) ; Dice:long_name = "The index of the AMSU FOV" ; Dice:units = "none" ; Dice:scale_factor = 1.0d ; Dice:add_offset = 0.0d ; Dice:parameter_type = "IASI data" ; Dice:valid_range = 1.0f, 660.0f ; Dice:_FillValue = -9999 ; double Time(Number_of_Dice) ; Time:long_name = "UTC Milliseconds since Jan 1, 1970" ; Time:units = "msec" ; Time:scale_factor = 1.0d ; Time:add_offset = 0.0d ; Time:parameter_type = "IASI data" ; Time:valid_range = 0.0f, 1577836800000.0f ; Time:_FillValue = -9999.0 ; float Latitude(Number_of_Dice) ; Latitude:long_name = "Retrieval latitude values for each AMSU FOV" ; Latitude:units = "degrees North" ; Latitude:scale_factor = 1.0d ; Latitude:add_offset = 0.0d ; Latitude:parameter_type = "IASI data" ; Latitude:valid_range = 90.0f, -90.0f ; Latitude:_FillValue = -9999.0f ; float Longitude(Number_of_Dice) ; Longitude:long_name = "Retrieval longitude values for each AMSU FOV" ; Longitude:units = "degrees East" ; Longitude:scale_factor = 1.0d ; Longitude:add_offset = 0.0d ; Longitude:parameter_type = "IASI data" ; Longitude:valid_range = -180.0f, 179.99f ; Longitude:_FillValue = -9999.0f ; float View_Angle(Number_of_Dice) ; View_Angle:long_name = "View angle for each AMSU FOV" ; View_Angle:units = "degrees" ; View_Angle:scale_factor = 1.0d ; View_Angle:add_offset = 0.0d ; View_Angle:parameter_type = "IASI data" ; View_Angle:valid_range = -360.0f, 360.0f ; View_Angle:_FillValue = -9999.0f ; float Satellite_Height(Number_of_Dice) ; Satellite_Height:long_name = "Satellite height above each AMSU FOV" ; Satellite_Height:units = "km" ; Satellite_Height:scale_factor = 1.0d ; Satellite_Height:add_offset = 0.0d ; Satellite_Height:parameter_type = "IASI data" ; Satellite_Height:valid_range = 0.0f, 1000.0f ; Satellite_Height:_FillValue = -9999.0f ; float Mean_CO2(Number_of_Dice) ; Mean_CO2:long_name = "Column averaged CO2 per AMSU FOV" ; Mean_CO2:units = "ppm" ; Mean_CO2:scale_factor = 1.0d ; Mean_CO2:add_offset = 0.0d ; Mean_CO2:parameter_type = "IASI data" ; Mean_CO2:valid_range = 0.0f, 1000.0f ; Mean_CO2:_FillValue = -9999.0f ; float Solar_Zenith(Number_of_Dice) ; Solar_Zenith:long_name = "Solar zenith angles for each AMSU FOV" ; Solar_Zenith:units = "degrees" ; Solar_Zenith:scale_factor = 1.0d ; Solar_Zenith:add_offset = 0.0d ; Solar_Zenith:parameter_type = "IASI data" ; Solar_Zenith:valid_range = 0.f, 90.f ; Solar_Zenith:_FillValue = -9999.f ; short Ascending_Descending(Number_of_Dice) ; Ascending_Descending:long_name = "0=Descending, 1=Ascending" ; Ascending_Descending:units = "none" ; Ascending_Descending:scale_factor = 1 ; Ascending_Descending:add_offset = 0 ; Ascending_Descending:parameter_type = "IASI data" ; Ascending_Descending:valid_range = 0, 1 ; Ascending_Descending:_FillValue = -9999s ; float Topography(Number_of_Dice) ; Topography:long_name = "Surface height" ; Topography:units = "meters" ; Topography:scale_factor = 1.0d ; Topography:add_offset = 0.0d ; Topography:parameter_type = "IASI data" ; Topography:valid_range = 0.f, 10000.f ; Topography:_FillValue = -9999.f ; float Land_Fraction(Number_of_Dice) ; Land_Fraction:long_name = "Land fraction" ; Land_Fraction:units = "none" ; Land_Fraction:scale_factor = 1.0d ; Land_Fraction:add_offset = 0.0d ; Land_Fraction:parameter_type = "IASI data" ; Land_Fraction:valid_range = 0.f, 1.f ; Land_Fraction:_FillValue = -9999.f ; float Surface_Pressure(Number_of_Dice) ; Surface_Pressure:long_name = "Surface pressure" ; Surface_Pressure:units = "mb" ; Surface_Pressure:scale_factor = 1.0d ; Surface_Pressure:add_offset = 0.0d ; Surface_Pressure:parameter_type = "IASI data" ; Surface_Pressure:valid_range = 0.f, 10000.f ; Surface_Pressure:_FillValue = -9999.f ; float Skin_Temperature(Number_of_Dice) ; Skin_Temperature:long_name = "Skin temperature" ; Skin_Temperature:units = "Kelvin" ; Skin_Temperature:scale_factor = 1.0d ; Skin_Temperature:add_offset = 0.0d ; Skin_Temperature:parameter_type = "IASI data" ; Skin_Temperature:valid_range = 0.f, 1000.f ; Skin_Temperature:_FillValue = -9999.f ; short MW_Surface_Class(Number_of_Dice) ; MW_Surface_Class:long_name = "Microwave surface class" ; MW_Surface_Class:units = "none" ; MW_Surface_Class:scale_factor = 1 ; MW_Surface_Class:add_offset = 0 ; MW_Surface_Class:parameter_type = "IASI data" ; MW_Surface_Class:valid_range = 0, 10 ; MW_Surface_Class:_FillValue = -9999s ; float MW_Surface_Emis(Number_of_Dice) ; MW_Surface_Emis:long_name = "Microwave surface emissivity" ; MW_Surface_Emis:units = "none" ; MW_Surface_Emis:scale_factor = 1.0d ; MW_Surface_Emis:add_offset = 0.0d ; MW_Surface_Emis:parameter_type = "IASI data" ; MW_Surface_Emis:valid_range = 0.f, 1.f ; MW_Surface_Emis:_FillValue = -9999.f ; long N_Smw_Per_FOV(Number_of_Dice) ; N_Smw_Per_FOV:long_name = "Number of MW spectral points AMSU FOV" ; N_Smw_Per_FOV:units = "none" ; N_Smw_Per_FOV:scale_factor = 1.0d ; N_Smw_Per_FOV:add_offset = 0.0d ; N_Smw_Per_FOV:parameter_type = "IASI data" ; N_Smw_Per_FOV:valid_range = 1.0f, 16.0f ; N_Smw_Per_FOV:_FillValue = -9999 ; long nemis_Per_FOV(Number_of_Dice) ; nemis_Per_FOV:long_name = "Number of surface emis hinge points per AMSU FOV" ; nemis_Per_FOV:units = "none" ; nemis_Per_FOV:scale_factor = 1.0d ; nemis_Per_FOV:add_offset = 0.0d ; nemis_Per_FOV:parameter_type = "IASI data" ; nemis_Per_FOV:valid_range = 1.0f, 100.0f ; nemis_Per_FOV:_FillValue = -9999 ; long ncemis_Per_FOV(Number_of_Dice) ; ncemis_Per_FOV:long_name = "Number of cloud emis hinge points per AMSU FOV" ; ncemis_Per_FOV:units = "none" ; ncemis_Per_FOV:scale_factor = 1.0d ; ncemis_Per_FOV:add_offset = 0.0d ; ncemis_Per_FOV:parameter_type = "IASI data" ; ncemis_Per_FOV:valid_range = 1.0f, 100.0f ; ncemis_Per_FOV:_FillValue = -9999 ; long ncld_Per_FOV(Number_of_Dice) ; ncld_Per_FOV:long_name = "Number of cloud layers per AMSU FOV" ; ncld_Per_FOV:units = "none" ; ncld_Per_FOV:scale_factor = 1.0d ; ncld_Per_FOV:add_offset = 0.0d ; ncld_Per_FOV:parameter_type = "IASI data" ; ncld_Per_FOV:valid_range = 1.0f, 8.0f ; ncld_Per_FOV:_FillValue = -9999 ; long Quality_Flag(Number_of_Dice) ; Quality_Flag:long_name = "Quality flags for retrieval" ; Quality_Flag:units = "none" ; Quality_Flag:scale_factor = 1.0d ; Quality_Flag:add_offset = 0.0d ; Quality_Flag:parameter_type = "IASI data" ; Quality_Flag:valid_range = 0.f, 10000.f ; Quality_Flag:_FillValue = -9999 ; float Cloud_Top_Pressure(Number_of_Dice, Number_of_Cloud_Layers) ; Cloud_Top_Pressure:long_name = "Cloud top pressure" ; Cloud_Top_Pressure:units = "mb" ; Cloud_Top_Pressure:scale_factor = 1.0d ; Cloud_Top_Pressure:add_offset = 0.0d ; Cloud_Top_Pressure:parameter_type = "IASI data" ; Cloud_Top_Pressure:valid_range = 0.f, 10000.f ; Cloud_Top_Pressure:_FillValue = -9999.f ; float Cloud_Top_Fraction(Number_of_Dice, Number_of_Cloud_Layers) ; Cloud_Top_Fraction:long_name = "Cloud top fractional coverage" ; Cloud_Top_Fraction:units = "none" ; Cloud_Top_Fraction:scale_factor = 1.0d ; Cloud_Top_Fraction:add_offset = 0.0d ; Cloud_Top_Fraction:parameter_type = "IASI data" ; Cloud_Top_Fraction:valid_range = 0.f, 1.f ; Cloud_Top_Fraction:_FillValue = -9999.f ; float Pressure(Number_of_Dice, Number_of_P_Levels) ; Pressure:long_name = "Pressure" ; Pressure:units = "mb" ; Pressure:scale_factor = 1.0d ; Pressure:add_offset = 0.0d ; Pressure:parameter_type = "IASI data" ; Pressure:valid_range = 0.f, 2000.f ; Pressure:_FillValue = -9999.f ; float Effective_Pressure(Number_of_Dice, Number_of_P_Levels) ; Effective_Pressure:long_name = "Effective_Pressure" ; Effective_Pressure:units = "mb" ; Effective_Pressure:scale_factor = 1.0d ; Effective_Pressure:add_offset = 0.0d ; Effective_Pressure:parameter_type = "IASI data" ; Effective_Pressure:valid_range = 0.f, 2000.f ; Effective_Pressure:_FillValue = -9999.f ; float Temperature(Number_of_Dice, Number_of_P_Levels) ; Temperature:long_name = "Temperature" ; Temperature:units = "Kelvin" ; Temperature:scale_factor = 1.0d ; Temperature:add_offset = 0.0d ; Temperature:parameter_type = "IASI data" ; Temperature:valid_range = 0.f, 1000.f ; Temperature:_FillValue = -9999.f ; float H2O_LCD(Number_of_Dice, Number_of_P_Levels) ; H2O_LCD:long_name = "water vapor layer column density" ; H2O_LCD:units = "molecules/cm2" ; H2O_LCD:scale_factor = 1.0d ; H2O_LCD:add_offset = 0.0d ; H2O_LCD:parameter_type = "IASI data" ; H2O_LCD:valid_range = 0.f, 100000000.f ; H2O_LCD:_FillValue = -9999.f ; float H2O_MR(Number_of_Dice, Number_of_P_Levels) ; H2O_MR:long_name = "water vapor mixing ratio" ; H2O_MR:units = "g/g" ; H2O_MR:scale_factor = 1.0d ; H2O_MR:add_offset = 0.0d ; H2O_MR:parameter_type = "IASI data" ; H2O_MR:valid_range = 0.f, 100000000.f ; H2O_MR:_FillValue = -9999.f ; float O3_LCD(Number_of_Dice, Number_of_P_Levels) ; O3_LCD:long_name = "Ozone layer column density" ; O3_LCD:units = "molecules/cm2" ; O3_LCD:scale_factor = 1.0d ; O3_LCD:add_offset = 0.0d ; O3_LCD:parameter_type = "IASI data" ; O3_LCD:valid_range = 0.f, 100000000.f ; O3_LCD:_FillValue = -9999.f ; float O3_MR(Number_of_Dice, Number_of_P_Levels) ; O3_MR:long_name = "Ozone mixing ratio" ; O3_MR:units = "ppb" ; O3_MR:scale_factor = 1.0d ; O3_MR:add_offset = 0.0d ; O3_MR:parameter_type = "IASI data" ; O3_MR:valid_range = 0.f, 100000000.f ; O3_MR:_FillValue = -9999.f ; float Liquid_H2O_LCD(Number_of_Dice, Number_of_P_Levels) ; Liquid_H2O_LCD:long_name = "Liquid water layer column density" ; Liquid_H2O_LCD:units = "molecules/cm2" ; Liquid_H2O_LCD:scale_factor = 1.0d ; Liquid_H2O_LCD:add_offset = 0.0d ; Liquid_H2O_LCD:parameter_type = "IASI data" ; Liquid_H2O_LCD:valid_range = 0.f, 100000000.f ; Liquid_H2O_LCD:_FillValue = -9999.f ; float Liquid_H2O_MR(Number_of_Dice, Number_of_P_Levels) ; Liquid_H2O_MR:long_name = "Liquid water mixing ratio" ; Liquid_H2O_MR:units = "g/g" ; Liquid_H2O_MR:scale_factor = 1.0d ; Liquid_H2O_MR:add_offset = 0.0d ; Liquid_H2O_MR:parameter_type = "IASI data" ; Liquid_H2O_MR:valid_range = 0.f, 100000000.f ; Liquid_H2O_MR:_FillValue = -9999.f ; short Ice_Liquid_Flag(Number_of_Dice, Number_of_P_Levels) ; Ice_Liquid_Flag:long_name = "Ice liquid flag 0=water, 1=ice" ; Ice_Liquid_Flag:units = "none" ; Ice_Liquid_Flag:scale_factor = 1 ; Ice_Liquid_Flag:add_offset = 0 ; Ice_Liquid_Flag:parameter_type = "IASI data" ; Ice_Liquid_Flag:valid_range = 0, 1 ; Ice_Liquid_Flag:_FillValue = -9999s ; float CO_LCD(Number_of_Dice, Number_of_P_Levels) ; CO_LCD:long_name = "Carbon monoxide layer column density" ; CO_LCD:units = "molecules/cm2" ; CO_LCD:scale_factor = 1.0d ; CO_LCD:add_offset = 0.0d ; CO_LCD:parameter_type = "IASI data" ; CO_LCD:valid_range = 0.f, 100000000.f ; CO_LCD:_FillValue = -9999.f ; float CO_MR(Number_of_Dice, Number_of_P_Levels) ; CO_MR:long_name = "Carbon monoxide mixing ratio" ; CO_MR:units = "ppb" ; CO_MR:scale_factor = 1.0d ; CO_MR:add_offset = 0.0d ; CO_MR:parameter_type = "IASI data" ; CO_MR:valid_range = 0.f, 100000000.f ; CO_MR:_FillValue = -9999.f ; float CH4_LCD(Number_of_Dice, Number_of_P_Levels) ; CH4_LCD:long_name = "Methane layer column density" ; CH4_LCD:units = "molecules/cm2" ; CH4_LCD:scale_factor = 1.0d ; CH4_LCD:add_offset = 0.0d ; CH4_LCD:parameter_type = "IASI data" ; CH4_LCD:valid_range = 0.f, 100000000.f ; CH4_LCD:_FillValue = -9999.f ; float CH4_MR(Number_of_Dice, Number_of_P_Levels) ; CH4_MR:long_name = "Methane mixing ratio" ; CH4_MR:units = "ppb" ; CH4_MR:scale_factor = 1.0d ; CH4_MR:add_offset = 0.0d ; CH4_MR:parameter_type = "IASI data" ; CH4_MR:valid_range = 0.f, 100000000.f ; CH4_MR:_FillValue = -9999.f ; float CO2(Number_of_Dice, Number_of_P_Levels) ; CO2:long_name = "Carbon dioxide dry mixing ratio" ; CO2:units = "ppm" ; CO2:scale_factor = 1.0d ; CO2:add_offset = 0.0d ; CO2:parameter_type = "IASI data" ; CO2:valid_range = 0.f, 1000.f ; CO2:_FillValue = -9999.f ; float HNO3_LCD(Number_of_Dice, Number_of_P_Levels) ; HNO3_LCD:long_name = "Nitric Acid layer column density" ; HNO3_LCD:units = "molecules/cm2" ; HNO3_LCD:scale_factor = 1.0d ; HNO3_LCD:add_offset = 0.0d ; HNO3_LCD:parameter_type = "IASI data" ; HNO3_LCD:valid_range = 0.f, 100000000.f ; HNO3_LCD:_FillValue = -9999.f ; float HNO3_MR(Number_of_Dice, Number_of_P_Levels) ; HNO3_MR:long_name = "Nitric Acid mixing ratio" ; HNO3_MR:units = "ppb" ; HNO3_MR:scale_factor = 1.0d ; HNO3_MR:add_offset = 0.0d ; HNO3_MR:parameter_type = "IASI data" ; HNO3_MR:valid_range = 0.f, 100000000.f ; HNO3_MR:_FillValue = -9999.f ; float N2O_LCD(Number_of_Dice, Number_of_P_Levels) ; N2O_LCD:long_name = "Nitrous Oxide layer column density" ; N2O_LCD:units = "molecules/cm2" ; N2O_LCD:scale_factor = 1.0d ; N2O_LCD:add_offset = 0.0d ; N2O_LCD:parameter_type = "IASI data" ; N2O_LCD:valid_range = 0.f, 100000000.f ; N2O_LCD:_FillValue = -9999.f ; float N2O_MR(Number_of_Dice, Number_of_P_Levels) ; N2O_MR:long_name = "Nitrous Oxide mixing ratio" ; N2O_MR:units = "ppb" ; N2O_MR:scale_factor = 1.0d ; N2O_MR:add_offset = 0.0d ; N2O_MR:parameter_type = "IASI data" ; N2O_MR:valid_range = 0.f, 100000000.f ; N2O_MR:_FillValue = -9999.f ; float SO2_LCD(Number_of_Dice, Number_of_P_Levels) ; SO2_LCD:long_name = "Sulfur Dioxide layer column density" ; SO2_LCD:units = "molecules/cm2" ; SO2_LCD:scale_factor = 1.0d ; SO2_LCD:add_offset = 0.0d ; SO2_LCD:parameter_type = "IASI data" ; SO2_LCD:valid_range = 0.f, 100000000.f ; SO2_LCD:_FillValue = -9999.f ; float SO2_MR(Number_of_Dice, Number_of_P_Levels) ; SO2_MR:long_name = "Sulfur Dioxide mixing ratio" ; SO2_MR:units = "ppb" ; SO2_MR:scale_factor = 1.0d ; SO2_MR:add_offset = 0.0d ; SO2_MR:parameter_type = "IASI data" ; SO2_MR:valid_range = 0.f, 100000000.f ; SO2_MR:_FillValue = -9999.f ; float MW_Frequency(Number_of_Dice, Number_of_MW_Spectral_Pts) ; MW_Frequency:long_name = "Microwave frequency" ; MW_Frequency:units = "wavenumber cm-1" ; MW_Frequency:scale_factor = 1.0d ; MW_Frequency:add_offset = 0.0d ; MW_Frequency:parameter_type = "IASI data" ; MW_Frequency:valid_range = 0.f, 10000.f ; MW_Frequency:_FillValue = -9999.f ; float MW_Emis(Number_of_Dice, Number_of_MW_Spectral_Pts) ; MW_Emis:long_name = "Microwave emissivity" ; MW_Emis:units = "none" ; MW_Emis:scale_factor = 1.0d ; MW_Emis:add_offset = 0.0d ; MW_Emis:parameter_type = "IASI data" ; MW_Emis:valid_range = 0.f, 1.f ; MW_Emis:_FillValue = -9999.f ; float IR_Emis_Freq(Number_of_Dice, Number_of_Surf_Emis_Hinge_Pts) ; IR_Emis_Freq:long_name = "IR emissivity hinge point frequencies" ; IR_Emis_Freq:units = "wavenumber cm-1" ; IR_Emis_Freq:scale_factor = 1.0d ; IR_Emis_Freq:add_offset = 0.0d ; IR_Emis_Freq:parameter_type = "IASI data" ; IR_Emis_Freq:valid_range = 0.f, 10000.f ; IR_Emis_Freq:_FillValue = -9999.f ; float IR_Surface_Emis(Number_of_Dice, Number_of_Surf_Emis_Hinge_Pts) ; IR_Surface_Emis:long_name = "IR surface emissivity" ; IR_Surface_Emis:units = "none" ; IR_Surface_Emis:scale_factor = 1.0d ; IR_Surface_Emis:add_offset = 0.0d ; IR_Surface_Emis:parameter_type = "IASI data" ; IR_Surface_Emis:valid_range = 0.f, 1.f ; IR_Surface_Emis:_FillValue = -9999.f ; float IR_Surface_Refl(Number_of_Dice, Number_of_Surf_Emis_Hinge_Pts) ; IR_Surface_Refl:long_name = "IR surface reflectance" ; IR_Surface_Refl:units = "percent" ; IR_Surface_Refl:scale_factor = 1.0d ; IR_Surface_Refl:add_offset = 0.0d ; IR_Surface_Refl:parameter_type = "IASI data" ; IR_Surface_Refl:valid_range = 0.f, 100.f ; IR_Surface_Refl:_FillValue = -9999.f ; float Stability(Number_of_Dice, Number_of_Stability_Parameters) ; Stability:long_name = "Stability parameters" ; Stability:units = "varying" ; Stability:scale_factor = 1.0d ; Stability:add_offset = 0.0d ; Stability:parameter_type = "IASI data" ; Stability:valid_range = 0.f, 1000000.f ; Stability:_FillValue = -9999.f ; float Cloud_Freq(Number_of_Dice, Number_of_Cloud_Layers, Number_of_Cloud_Emis_Hing_Pts) ; Cloud_Freq:long_name = "Cloud IR frequencies" ; Cloud_Freq:units = "wavenumber cm-1" ; Cloud_Freq:scale_factor = 1.0d ; Cloud_Freq:add_offset = 0.0d ; Cloud_Freq:parameter_type = "IASI data" ; Cloud_Freq:valid_range = 0.f, 10000.f ; Cloud_Freq:_FillValue = -9999.f ; float Cloud_Emis(Number_of_Dice, Number_of_Cloud_Layers, Number_of_Cloud_Emis_Hing_Pts) ; Cloud_Emis:long_name = "Cloud IR emissivity" ; Cloud_Emis:units = "none" ; Cloud_Emis:scale_factor = 1.0d ; Cloud_Emis:add_offset = 0.0d ; Cloud_Emis:parameter_type = "IASI data" ; Cloud_Emis:valid_range = 0.f, 1.f ; Cloud_Emis:_FillValue = -9999.f ; float Cloud_Refl(Number_of_Dice, Number_of_Cloud_Layers, Number_of_Cloud_Emis_Hing_Pts) ; Cloud_Refl:long_name = "Cloud IR reflectivity" ; Cloud_Refl:units = "percent" ; Cloud_Refl:scale_factor = 1.0d ; Cloud_Refl:add_offset = 0.0d ; Cloud_Refl:parameter_type = "IASI data" ; Cloud_Refl:valid_range = 0.f, 100.f ; Cloud_Refl:_FillValue = -9999.f ; |
| --- | --- |

    - Intended Users

CLASS

POC: John Bates

Chief, Remote Sensing and Applications Division

NOAA / NESDIS / National Climatic Data Center (NCDC) / Remote Sensing and Applications Division (RSAD)

Asheville, NC

Phone: (828) 271-4378

Fax: (828) 271-4328

Address: 151 Patton Avenue, Room 516 D Ashville, NC 28801

    - Access

These files reside in the level2 products directory for the given granule:

$BASE/SATELLITE_DATA/MetOpA/NRT_DATA/${Year}/${Month}/${Day}/IASI_DATA/Granule-${Granule_Number}/level2

These files are sent to the DDS where they are retrieved by CLASS.  The details of the archiving of the L2 and CCR products are described in a data submission agreement separate from the level 1C products called The Producer Archive Submission Agreement for IASI L2 Products (NESDIS/CLASS, 2008).

Files are sent to the DDS by the scripts that generate them: dds.nesdis.noaa.gov:push

POC – Nichols, Catherine L

5200 Auth Road, Room 0315, Building: FB4

Suitland, MD 20746 – 4301

Phone: (301)457-5245

Fax:      (301)457-5199

E-mail: cathy.nichols@noaa.gov

IASI CCR NetCDF File

    - Purpose

    - Products files which are defined as any output files whose contents are used to satisfy user requirements.  These files will be archived to Comprehensive Large Array-data Stewardship System (CLASS).

    - Data File Description

The IASICCR NetCDF granule files are generated from main_iasi_ccr_to_netcdf.  The input files are the native binary format retrieval output files.  This program is part of the L2 Processing Unit.  The files they create are produced in the following directory:

$BASE/SATELLITE_DATA/MetOpA/NRT_DATA/${Year}/${Month}/${Day}/IASI_DATA/Granule-${Granule_Number}/level2

where:

${Year} = the 4-digit year

${Month} = 2-digit month

${Day} = 2-digit day of month

${Granule_Number} = 3-digit granule number (1-480)

The following NetCDF intermediate file is produced for each granule with the following name structure.

iasi_ccr_${Year}${Month}${Day}_Granule-${Granule_Number}.nc

iasi_ccr_ncep_${Year}${Month}${Day}_Granule-${Granule_Number}.nc

where:

$Year = 4-digit year

$Month = 2-digit month

$Day = 2-digit day

$Granule_Number = 3-digit granule number

The first file is full spatial and spectral resolution file.  It’s starting and ending scan lines and footprints match those of the full resolution Level 1C IASI, AMSU-A, and MHS L1B NetCDF files for the same granule number described above.  The “iasi_ccr_ncep” file:

iasi_ccr_ncep_${Year}${Month}${Day}_Granule-${Granule_Number}.nc

is required for the generation of CCR BUFR files.  The other file is used in both the Global Grids and Global Binaries units.  It is also used to generate  additional NetCDF file which is archived to CLASS:

IASI_CCR_M02_V${YYMMDD}_${YYYYMODDHHMMSS}Z_${YYYYMODDHHMMSS}Z.nc

where:

IASI = Instrument name

CCR = the product type (CCR = Cloud-cleared radiances)

M02 = Satellite ID (M02 = Metop-A)

V = Version indicator

$YYMMDD = 2-digit year + 2-digit month + 2-digit day (the date the version was created)

Sensing date/time string = Date/time of observations given in the following format YYYYMODDHHMMSSZ.  The first string indicates the starting date/time and the second string indicates the ending date/time.

nc = File type extension indicates NetCDF format

Where:

The string “YYYYMODDHHMMSSZ” is a date string containing the following components of time:

YYYY = 4 digit year (e.g. 2005)

MO = 2 digit month (01-12)

DD = day of month (01-31)

HH = hour (00-23)

MM = minute (00-59)

SS = seconds (00-59)

Z = Greenwich Mean Time (GMT)

Here is an example of  a CCR file created using software version 071016 on February 11th, 2008.  The granule starts at 04:23:59 GMT and ends at 04:26:55 GMT:

IASI_CCR_M02_V071016_20080211042359Z_20080211042655Z.nc

This granule file has an associated metadata xml file which is archived to CLASS.

Table 39. IASI CCR NetCDF Header

| dimensions: variables: | Number_of_Dice = 660 ; // Number dice written Number_of_Dots = 1 ; // Number of IASI FOVS in a die Number_of_IASI_Channels = 8461 ; // Number of IASI Channels Number_of_IASI_Frequencies = 8461 ; // Number of IASI Clear Frequencies Number_of_AVHRR_Channels = 6; // Number of AVHRR channels Number_of_AVHRR_FOV_Classes = 7; // Number of AVHRR sounder FOV classes Number_of_AVHRR_Frequencies = 6; Number_of_IASI_Image_Pixels = 4096; // 64 X 64 Pixel IASI image long IASI_Channels(Number_of_IASI_Channels) ; IASI_Channels:long_name = "Channel number for data" ; IASI_Channels:units = "none" ; IASI_Channels:scale_factor = 1.0d ; IASI_Channels:add_offset = 0.0d ; IASI_Channels:parameter_type = "IASI data" ; IASI_Channels:valid_range = 1.0f, 8461.0f ; IASI_Channels:_FillValue = -9999 ; float IASI_Frequencies(Number_of_IASI_Frequencies) ; IASI_Frequencies:long_name = "Frequency at which the data is taken" ; IASI_Frequencies:units = "wavenumber cm-1" ; IASI_Frequencies:scale_factor = 1.0d ; IASI_Frequencies:add_offset = 0.0d ; IASI_Frequencies:parameter_type = "IASI data" ; IASI_Frequencies:valid_range = 0.0f, 10000.0f ; IASI_Frequencies:_FillValue = -9999.0f ; long AVHRR_Channels(Number_of_AVHRR_Channels) ; AVHRR_Channels:long_name = "Channel number for data" ; AVHRR_Channels:units = "none" ; AVHRR_Channels:scale_factor = 1.0d ; AVHRR_Channels:add_offset = 0.0d ; AVHRR_Channels:parameter_type = "AVHRR data" ; AVHRR_Channels:valid_range = 1.0f, 6.0f ; AVHRR_Channels:_FillValue = -9999 ; float AVHRR_Frequencies(Number_of_AVHRR_Frequencies) ; AVHRR_Frequencies:long_name = "Frequency at which the data is taken" ; AVHRR_Frequencies:units = "wavenumber cm-1" ; AVHRR_Frequencies:scale_factor = 1.0d ; AVHRR_Frequencies:add_offset = 0.0d ; AVHRR_Frequencies:parameter_type = "AVHRR data" ; AVHRR_Frequencies:valid_range = 0.0f, 16000.0f ; AVHRR_Frequencies:_FillValue = -9999.0f ; long AVHRR_FOV_Classes(Number_of_AVHRR_FOV_Classes) ; AVHRR_FOV_Classes:long_name = "The index of the AVHRR FOV sounder class" ; AVHRR_FOV_Classes:units = "none" ; AVHRR_FOV_Classes:scale_factor = 1.0d ; AVHRR_FOV_Classes:add_offset = 0.0d ; AVHRR_FOV_Classes:parameter_type = "AVHRR data" ; AVHRR_FOV_Classes:valid_range = 1.0f, 7.0f ; AVHRR_FOV_Classes:_FillValue = -9999 ; long Dice(Number_of_Dice) ; Dice:long_name = "The index of the IASI fields of regard" ; Dice:units = "none" ; Dice:scale_factor = 1.0d ; Dice:add_offset = 0.0d ; Dice:parameter_type = "IASI data" ; Dice:valid_range = 1.0f, 660.0f ; Dice:_FillValue = -9999 ; long Dots(Number_of_Dots) ; Dots:long_name = "The index of the IASI fields of view" ; Dots:units = "none" ; Dots:scale_factor = 1.0d ; Dots:add_offset = 0.0d ; Dots:parameter_type = "IASI data" ; Dots:valid_range = 1.0f, 4.0f ; Dots:_FillValue = -9999 ; long Scan_Line(Number_of_Dice,Number_of_Dots) ; Scan_Line:long_name = "The number of the current scan line" ; Scan_Line:units = "none" ; Scan_Line:scale_factor = 1.0d ; Scan_Line:add_offset = 0.0d ; Scan_Line:parameter_type = "IASI data" ; Scan_Line:valid_range = 1.0f, 22.0f ; Scan_Line:_FillValue = -9999 ; long AMSU_FOV(Number_of_Dice,Number_of_Dots) ; AMSU_FOV:long_name = "The number of the current AMSU FOV" ; AMSU_FOV:units = "none" ; AMSU_FOV:scale_factor = 1.0d ; AMSU_FOV:add_offset = 0.0d ; AMSU_FOV:parameter_type = "IASI data" ; AMSU_FOV:valid_range = 1.0f, 30.0f ; AMSU_FOV:_FillValue = -9999 ; long IASI_FOV(Number_of_Dice,Number_of_Dots) ; IASI_FOV:long_name = "The number of the current IASI FOV" ; IASI_FOV:units = "none" ; IASI_FOV:scale_factor = 1.0d ; IASI_FOV:add_offset = 0.0d ; IASI_FOV:parameter_type = "IASI data" ; IASI_FOV:valid_range = 1.0f, 4.0f ; IASI_FOV:_FillValue = -9999 ; short GQisFlagQual(Number_of_Dice,Number_of_Dots) ; GQisFlagQual:long_name = "System QC flag" ; GQisFlagQual:units = "none" ; GQisFlagQual:scale_factor = 1 ; GQisFlagQual:add_offset = 0 ; GQisFlagQual:parameter_type = "IASI data" ; GQisFlagQual:valid_range = 0, 1 ; GQisFlagQual:_FillValue = -9999s ; float GQisQualIndex(Number_of_Dice,Number_of_Dots) ; GQisQualIndex:long_name = "System QC flag" ; GQisQualIndex:units = "none" ; GQisQualIndex:scale_factor = 1.0d ; GQisQualIndex:add_offset = 0.0d ; GQisQualIndex:parameter_type = "IASI data" ; GQisQualIndex:valid_range = 0.0f, 9999.0f ; GQisQualIndex:_FillValue = -9999.0f ; float GQisQualIndexLoc(Number_of_Dice,Number_of_Dots) ; GQisQualIndexLoc:long_name = "System QC flag" ; GQisQualIndexLoc:units = "none" ; GQisQualIndexLoc:scale_factor = 1.0d ; GQisQualIndexLoc:add_offset = 0.0d ; GQisQualIndexLoc:parameter_type = "IASI data" ; GQisQualIndexLoc:valid_range = 0.0f, 9999.0f ; GQisQualIndexLoc:_FillValue = -9999.0f ; float GQisQualIndexRad(Number_of_Dice,Number_of_Dots) ; GQisQualIndexRad:long_name = "System QC flag" ; GQisQualIndexRad:units = "none" ; GQisQualIndexRad:scale_factor = 1.0d ; GQisQualIndexRad:add_offset = 0.0d ; GQisQualIndexRad:parameter_type = "IASI data" ; GQisQualIndexRad:valid_range = 0.0f, 9999.0f ; GQisQualIndexRad:_FillValue = -9999.0f ; float GQisQualIndexSpect(Number_of_Dice,Number_of_Dots) ; GQisQualIndexSpect:long_name = "System QC flag" ; GQisQualIndexSpect:units = "none" ; GQisQualIndexSpect:scale_factor = 1.0d ; GQisQualIndexSpect:add_offset = 0.0d ; GQisQualIndexSpect:parameter_type = "IASI data" ; GQisQualIndexSpect:valid_range = 0.0f, 9999.0f ; GQisQualIndexSpect:_FillValue = -9999.0f ; float GQisSysTecSondQual(Number_of_Dice,Number_of_Dots) ; GQisSysTecSondQual:long_name = "System QC flag" ; GQisSysTecSondQual:units = "none" ; GQisSysTecSondQual:scale_factor = 1.0d ; GQisSysTecSondQual:add_offset = 0.0d ; GQisSysTecSondQual:parameter_type = "IASI data" ; GQisSysTecSondQual:valid_range = 0.0f, 9999.0f ; GQisSysTecSondQual:_FillValue = -9999.0f ; double Time(Number_of_Dice,Number_of_Dots) ; Time:long_name = "UTC Milliseconds since Jan 1, 1970" ; Time:units = "msec" ; Time:scale_factor = 1.0d ; Time:add_offset = 0.0d ; Time:parameter_type = "IASI data" ; Time:valid_range = 0.0f, 1577836800000.0f ; Time:_FillValue = -9999.0 ; float Latitude(Number_of_Dice,Number_of_Dots) ; Latitude:long_name = "IASI Latitude values for each FOV" ; Latitude:units = "degrees North" ; Latitude:scale_factor = 1.0d ; Latitude:add_offset = 0.0d ; Latitude:parameter_type = "IASI data" ; Latitude:valid_range = 90.0f, -90.0f ; Latitude:_FillValue = -9999.0f ; float Longitude(Number_of_Dice,Number_of_Dots) ; Longitude:long_name = "IASI Longitude values for each FOV" ; Longitude:units = "degrees East" ; Longitude:scale_factor = 1.0d ; Longitude:add_offset = 0.0d ; Longitude:parameter_type = "IASI data" ; Longitude:valid_range = -180.0f, 179.99f ; Longitude:_FillValue = -9999.0f ; float IASI_Radiances(Number_of_Dice,Number_of_Dots,Number_of_IASI_Channels) ; IASI_Radiances:long_name = "IASI Radiances for each FOV" ; IASI_Radiances:units = "mW/m2/cm-1/sr" ; IASI_Radiances:scale_factor = 1.0d ; IASI_Radiances:add_offset = 0.0d ; IASI_Radiances:parameter_type = "IASI data" ; IASI_Radiances:valid_range = 0.0f, 40000.0f ; IASI_Radiances:_FillValue = -9999.0f ; float IASI_Image(Number_of_Dice,Number_of_IASI_Image_Pixels) ; IASI_Image:long_name = "IASI Image for each FOR" ; IASI_Image:units = "mW/m2/cm-1/sr" ; IASI_Image:scale_factor = 1.0d ; IASI_Image:add_offset = 0.0d ; IASI_Image:parameter_type = "IASI data" ; IASI_Image:valid_range = 0.0f, 40000.0f ; IASI_Image:_FillValue = -9999.0f ; short AVHRR_Channel_Combo(Number_of_Dice,Number_of_Dots) ; AVHRR_Channel_Combo:long_name = "AVHRR Channels used in radiance analysis" ; AVHRR_Channel_Combo:units = "none" ; AVHRR_Channel_Combo:scale_factor = 1 ; AVHRR_Channel_Combo:add_offset = 0 ; AVHRR_Channel_Combo:parameter_type = "IASI data" ; AVHRR_Channel_Combo:valid_range = 0, 1 ; AVHRR_Channel_Combo:_FillValue = -9999s ; float Fraction_of_Clear_AVHRR(Number_of_Dice,Number_of_Dots,Number_of_AVHRR_FOV_Classes) ; Fraction_of_Clear_AVHRR:long_name = "Percent clear for each AVHRR FOV class" ; Fraction_of_Clear_AVHRR:units = "%" ; Fraction_of_Clear_AVHRR:scale_factor = 1.0d ; Fraction_of_Clear_AVHRR:add_offset = 0.0d ; Fraction_of_Clear_AVHRR:parameter_type = "AVHRR data" ; Fraction_of_Clear_AVHRR:valid_range = 0.0f, 100.0f ; Fraction_of_Clear_AVHRR:_FillValue = -9999.0f ; float AVHRR_Y_Angle_Center_of_Gravity(Number_of_Dice,Number_of_Dots,Number_of_AVHRR_FOV_Classes) ; AVHRR_Y_Angle_Center_of_Gravity:long_name = "Y angular position of the center of gravity" ; AVHRR_Y_Angle_Center_of_Gravity:units = "degrees" ; AVHRR_Y_Angle_Center_of_Gravity:scale_factor = 1.0d ; AVHRR_Y_Angle_Center_of_Gravity:add_offset = 0.0d ; AVHRR_Y_Angle_Center_of_Gravity:parameter_type = "AVHRR data" ; AVHRR_Y_Angle_Center_of_Gravity:valid_range = 0.0f, 360.0f ; AVHRR_Y_Angle_Center_of_Gravity:_FillValue = -9999.0f ; float AVHRR_Z_Angle_Center_of_Gravity(Number_of_Dice,Number_of_Dots,Number_of_AVHRR_FOV_Classes) ; AVHRR_Z_Angle_Center_of_Gravity:long_name = "Z angular position of the center of gravity" ; AVHRR_Z_Angle_Center_of_Gravity:units = "degrees" ; AVHRR_Z_Angle_Center_of_Gravity:scale_factor = 1.0d ; AVHRR_Z_Angle_Center_of_Gravity:add_offset = 0.0d ; AVHRR_Z_Angle_Center_of_Gravity:parameter_type = "AVHRR data" ; AVHRR_Z_Angle_Center_of_Gravity:valid_range = 0.0f, 360.0f ; AVHRR_Z_Angle_Center_of_Gravity:_FillValue = -9999.0f ; float AVHRR_Mean_Radiances(Number_of_Dice,Number_of_Dots,Number_of_AVHRR_FOV_Classes,Number_of_AVHRR_Channels) ; AVHRR_Mean_Radiances:long_name = "Mean AVHRR radiances for each FOV" ; AVHRR_Mean_Radiances:units = "mW/m2/cm-1/sr" ; AVHRR_Mean_Radiances:scale_factor = 1.0d ; AVHRR_Mean_Radiances:add_offset = 0.0d ; AVHRR_Mean_Radiances:parameter_type = "AVHRR data" ; AVHRR_Mean_Radiances:valid_range = 0.0f, 40000.0f ; AVHRR_Mean_Radiances:_FillValue = -9999.0f ; float AVHRR_Std_Radiances(Number_of_Dice,Number_of_Dots,Number_of_AVHRR_FOV_Classes,Number_of_AVHRR_Channels) ; AVHRR_Std_Radiances:long_name = "Standard deviation of radiances for each FOV" ; AVHRR_Std_Radiances:units = "mW/m2/cm-1/sr" ; AVHRR_Std_Radiances:scale_factor = 1.0d ; AVHRR_Std_Radiances:add_offset = 0.0d ; AVHRR_Std_Radiances:parameter_type = "AVHRR data" ; AVHRR_Std_Radiances:valid_range = 0.0f, 40000.0f ; AVHRR_Std_Radiances:_FillValue = -9999.0f ; float View_Angle(Number_of_Dice,Number_of_Dots) ; View_Angle:long_name = "IASI View Angles for each FOV" ; View_Angle:units = "degrees" ; View_Angle:scale_factor = 1.0d ; View_Angle:add_offset = 0.0d ; View_Angle:parameter_type = "IASI data" ; View_Angle:valid_range = -90.0f, 90.0f ; View_Angle:_FillValue = -9999.0f ; float Satellite_Height(Number_of_Dice,Number_of_Dots) ; Satellite_Height:long_name = "Satellite height above each FOV" ; Satellite_Height:units = "km" ; Satellite_Height:scale_factor = 1.0 ; Satellite_Height:add_offset = 0.0 ; Satellite_Height:parameter_type = "IASI data" ; Satellite_Height:valid_range = 0.0f, 1000.0f ; Satellite_Height:_FillValue = -9999.0f ; float Satellite_Zenith(Number_of_Dice,Number_of_Dots) ; Satellite_Zenith:long_name = "Satellite zenith angles for each FOV" ; Satellite_Zenith:units = "degrees" ; Satellite_Zenith:scale_factor = 1.0 ; Satellite_Zenith:add_offset = 0.0 ; Satellite_Zenith:parameter_type = "IASI data" ; Satellite_Zenith:valid_range = 0.0f, 90.0f ; Satellite_Zenith:_FillValue = -9999.0f ; float Satellite_Azimuth(Number_of_Dice,Number_of_Dots) ; Satellite_Azimuth:long_name = "Satellite azimuth angles for each FOV" ; Satellite_Azimuth:units = "degrees" ; Satellite_Azimuth:scale_factor = 1.0 ; Satellite_Azimuth:add_offset = 0.0 ; Satellite_Azimuth:parameter_type = "IASI data" ; Satellite_Azimuth:valid_range = 0.0f, 180.0f ; Satellite_Azimuth:_FillValue = -9999.0f ; float Solar_Zenith(Number_of_Dice, Number_of_Dots) ; Solar_Zenith:long_name = "Solar zenith angles for each FOV" ; Solar_Zenith:units = "degrees" ; Solar_Zenith:scale_factor = 1.0 ; Solar_Zenith:add_offset = 0.0 ; Solar_Zenith:parameter_type = "IASI data" ; Solar_Zenith:valid_range = 0.f, 90.f ; Solar_Zenith:_FillValue = -9999.f ; float Solar_Azimuth(Number_of_Dice, Number_of_Dots) ; Solar_Azimuth:long_name = "Solar azimuth angles for each FOV" ; Solar_Azimuth:units = "degrees" ; Solar_Azimuth:scale_factor = 1.0 ; Solar_Azimuth:add_offset = 0.0 ; Solar_Azimuth:parameter_type = "IASI data" ; Solar_Azimuth:valid_range = 0.f, 180.f ; Solar_Azimuth:_FillValue = -9999.f ; short Ascending_Descending(Number_of_Dice, Number_of_Dots) ; Ascending_Descending:long_name = "0=Descending, 1=Ascending" ; Ascending_Descending:units = "none" ; Ascending_Descending:scale_factor = 1 ; Ascending_Descending:add_offset = 0 ; Ascending_Descending:parameter_type = "IASI data" ; Ascending_Descending:valid_range = 0, 1 ; Ascending_Descending:_FillValue = -9999s ; long Orbit_Number(Number_of_Dice,Number_of_Dots) ; Orbit_Number:long_name = "The number of the current orbit" ; Orbit_Number:units = "none" ; Orbit_Number:scale_factor = 1.0d ; Orbit_Number:add_offset = 0.0d ; Orbit_Number:parameter_type = "IASI data" ; Orbit_Number:valid_range = 1.0f, 100000.0f ; Orbit_Number:_FillValue = -9999 ; |
| --- | --- |

    - Intended Users

    - CLASS

POC: John Bates

Chief, Remote Sensing and Applications Division

NOAA / NESDIS / National Climatic Data Center (NCDC) / Remote Sensing and Applications Division (RSAD)

Asheville, NC

Phone: (828) 271-4378

Fax: (828) 271-4328

Address: 151 Patton Avenue, Room 516 D Ashville, NC 28801

    - Access

These files reside in the level2 products directory for the given granule:

$BASE/SATELLITE_DATA/MetOpA/NRT_DATA/${Year}/${Month}/${Day}/IASI_DATA/Granule-${Granule_Number}/level2

These files are sent to the DDS where they are retrieved by CLASS.  The details of the archiving of the L2 and CCR products are described in a data submission agreement separate from the level 1C products called The Producer Archive Submission Agreement for IASI L2 Products (NESDIS/CLASS, 2008).

Files are sent to the DDS by the scripts that generate them: dds.nesdis.noaa.gov:push

POC – Nichols, Catherine L

5200 Auth Road, Room 0315, Building: FB4

Suitland, MD 20746 – 4301

Phone: (301)457-5245

Fax:      (301)457-5199

E-mail: cathy.nichols@noaa.gov

    - IASI L2 and CCR Metadata

    - Granule metadata files generated for each of the IASI Level 2 and CCR NetCDF product files.

    - Purpose

    - The metadata files are pushed to the DDS by the STAR near real time processing system.  This system runs in OSDPD operations.  CLASS will access the DDS in accordance with Producer-Archive Submission Agreement for IASI Level 2 Products.

    - Data File Discription

These are Federal Geographic Data Committee Remote Sensing Extension (FGDC-RSE) compliant xml format files. There is one granule metadata file associated with each NetCDF product file.  These metadata files are derived from the L2 and CCR metadata template files (IASI_L2_Granule_Metadata_Template.xml and IASI_CCR_Granule_Metadata_Template.xml) by the Perl script called Create_IASI_L2_Metadata.pl which runs within the L2 Processing unit.

These metadata files have the same name structure as their associated product files except with an .xml extension.

IASI_L2_M02_V${YYMMDD}_${YYYYMODDHHMMSS}Z_${YYYYMODDHHMMSS}Z.nc.xml

IASI_CCR_M02_V${YYMMDD}_${YYYYMODDHHMMSS}Z_${YYYYMODDHHMMSS}Z.nc.xml

    - Intended Users

    - CLASS

POC: John Bates

Chief, Remote Sensing and Applications Division

NOAA / NESDIS / National Climatic Data Center (NCDC) / Remote Sensing and Applications Division (RSAD)

Asheville, NC

Phone: (828) 271-4378

Fax: (828) 271-4328

    - Address: 151 Patton Avenue, Room 516 D Ashville, NC 28801

    - Access

These files reside with their associate data files in the level2 products directory for the given granule:

$BASE/SATELLITE_DATA/MetOpA/NRT_DATA/${Year}/${Month}/${Day}/IASI_DATA/Granule-${Granule_Number}/level2

These files are sent to the DDS where they are retrieved by CLASS.  The details of the archiving of the L2 and CCR products are described in a data submission agreement separate from the level 1C products called The Producer Archive Submission Agreement for IASI L2 Products (NESDIS/CLASS, 2008).

POC – Nichols, Catherine L

5200 Auth Road, Room 0315, Building: FB4

Suitland, MD 20746 – 4301

Phone: (301)457-5245

Fax:      (301)457-5199

E-mail: cathy.nichols@noaa.gov

    - IASI CCR BUFR Files

    - Purpose

The BUFR files are cloud-cleared radiance files generated for use by NWP centers. These data are then used for assimilation in numerical models.

Data File Description

Their structure is based on the content of the BUFR table.  Nominally there are 480 of these files per day.  They are generated from the NetCDF subset files by the program main_iasi_netcdf_to_bufr which resides in L2 Processing unit.  Therefore BUFR files are created in the following directory:

$BASE/SATELLITE_DATA/MetOpA/NRT_DATA/${Year}/${Month}/${Day}/IASI_DATA/Granule-${Granule_Number}/level2

where:

${Year} = the 4-digit year

${Month} = 2-digit month

${Day} = 2-digit day of month

${Granule_Number} = 3-digit granule number (1-480)

The BUFR files are distributed from these directories to the DDS where they are retrieved by customers.  The output BUFR file names have the following name structure.

NPR_${PROD}.M02_D${Year}${Doy}_S${Hour}${Minute}${Second}_E${Hour}${Minute}${Second}_G${Granule_Number}_C${Channel_Set}_U${Subset}

Where:

NPR = Near real-time processing 
$PROD = Product type ID (IARD = ( IASI cloud-cleared radiances)
M02 = MetOp2 abbreviation
D = date string indicator
S = starting time indicator
E = ending time indicator

${Year} = the 2-digit year

${Doy} = 3-digit day of year

${Hour} = 2-digit hour

${Minute} = 2-digit minute

${Second} = 2-digit second

G = granule number indicator

${Granule_Number} = 3-digit granule number (1-480)
C = channel set indicator

${Channel_Set} = the number of channels in the subset (e.g. 616 or 8461)
U = the subset type indicator

${Subset} = subset type (e.g. U3, U5, or U6)

BUFR table, needed to read IASI BUFR granule files, is presented in Appendix A.

Intended Users

NWP centers.

Access

The files are created in the following directory:

$BASE/SATELLITE_DATA/MetOpA/NRT_DATA/${Year}/${Month}/${Day}/IASI_DATA/Granule-${Granule_Number}/level2

where:

${Year} = the 4-digit year

${Month} = 2-digit month

${Day} = 2-digit day of month

${Granule_Number} = 3-digit granule number (1-480)

The BUFR files are distributed from these level 1c directories to the DDS where they are retrieved by customers:

dds.nesdis.noaa.gov:push

POC – Nichols, Catherine L

5200 Auth Road, Room 0315, Building: FB4

Suitland, MD 20746 – 4301

Phone: (301)457-5245

Fax:      (301)457-5199

E-mail: cathy.nichols@noaa.gov

IASI NetCDF Principal Component File

Principal components are selected from only the warmest fields of view from each IASI field of regard.

Purpose

These files are for NRL/FNMOC’s principal component data assimilation.

Data File Description

The files are about 2 MB in size each.  Their name structure is

IASI_M02_PCS_${YYYYMODDHHMMSS}Z_${YYYYMODDHHMMSS}Z.nc

where:

IASI = Instrument name

PCS = Principal Components

M02 = Satellite ID (M02 = Metop-A)

YYYYMODDHHMMSSZ = The sensing date/time of observations.  The first string indicates the starting date/time and the second string indicates the ending date/time.

nc = File type extension indicates NetCDF format

The string “YYYYMODDHHMMSSZ” is a date string containing the following components of time:

YYYY = 4 digit year (e.g. 2005)

MO = 2 digit month (01-12)

DD = day of month (01-31)

HH = hour (00-23)

MM = minute (00-59)

SS = seconds (00-59)

Z = Greenwich Mean Time (GMT)

Table 40. IASI NetCDF Principal Component File Header

| dimensions: variables: | Number_of_Dice = 660 ; // Number dice written Number_of_Dots = 1 ; // Number of IASI FOVS in a die Number_of_IASI_Channels = 8461 ; // Number of IASI channels in eigenvector set Number_of_IASI_Frequencies = 8461 ; // Number of IASI channels in eigenvector set Number_of_Principal_Components = 600 ; Number_of_PC_Scores = 3 ; Number_of_AVHRR_Channels = 6; // Number of AVHRR channels Number_of_AVHRR_FOV_Classes = 7; // Number of AVHRR sounder FOV classes Number_of_AVHRR_Frequencies = 6; long IASI_Channels(Number_of_IASI_Channels) ; IASI_Channels:long_name = "Channel number for data" ; IASI_Channels:units = "none" ; IASI_Channels:scale_factor = 1.0d ; IASI_Channels:add_offset = 0.0d ; IASI_Channels:parameter_type = "IASI data" ; IASI_Channels:valid_range = 1.0f, 8461.0f ; IASI_Channels:_FillValue = -9999 ; float IASI_Frequencies(Number_of_IASI_Frequencies) ; IASI_Frequencies:long_name = "Frequency at which the data is taken" ; IASI_Frequencies:units = "wavenumber cm-1" ; IASI_Frequencies:scale_factor = 1.0d ; IASI_Frequencies:add_offset = 0.0d ; IASI_Frequencies:parameter_type = "IASI data" ; IASI_Frequencies:valid_range = 0.0f, 10000.0f ; IASI_Frequencies:_FillValue = -9999.0f ; long AVHRR_Channels(Number_of_AVHRR_Channels) ; AVHRR_Channels:long_name = "Channel number for data" ; AVHRR_Channels:units = "none" ; AVHRR_Channels:scale_factor = 1.0d ; AVHRR_Channels:add_offset = 0.0d ; AVHRR_Channels:parameter_type = "AVHRR data" ; AVHRR_Channels:valid_range = 1.0f, 6.0f ; AVHRR_Channels:_FillValue = -9999 ; float AVHRR_Frequencies(Number_of_AVHRR_Frequencies) ; AVHRR_Frequencies:long_name = "Frequency at which the data is taken" ; AVHRR_Frequencies:units = "wavenumber cm-1" ; AVHRR_Frequencies:scale_factor = 1.0d ; AVHRR_Frequencies:add_offset = 0.0d ; AVHRR_Frequencies:parameter_type = "AVHRR data" ; AVHRR_Frequencies:valid_range = 0.0f, 16000.0f ; AVHRR_Frequencies:_FillValue = -9999.0f ; long AVHRR_FOV_Classes(Number_of_AVHRR_FOV_Classes) ; AVHRR_FOV_Classes:long_name = "The index of the AVHRR FOV sounder class" ; AVHRR_FOV_Classes:units = "none" ; AVHRR_FOV_Classes:scale_factor = 1.0d ; AVHRR_FOV_Classes:add_offset = 0.0d ; AVHRR_FOV_Classes:parameter_type = "AVHRR data" ; AVHRR_FOV_Classes:valid_range = 1.0f, 7.0f ; AVHRR_FOV_Classes:_FillValue = -9999 ; long Dice(Number_of_Dice) ; Dice:long_name = "The index of the IASI fields of regard" ; Dice:units = "none" ; Dice:scale_factor = 1.0d ; Dice:add_offset = 0.0d ; Dice:parameter_type = "IASI data" ; Dice:valid_range = 1.0f, 660.0f ; Dice:_FillValue = -9999 ; long Dots(Number_of_Dots) ; Dots:long_name = "The index of the IASI fields of view" ; Dots:units = "none" ; Dots:scale_factor = 1.0d ; Dots:add_offset = 0.0d ; Dots:parameter_type = "IASI data" ; Dots:valid_range = 1.0f, 4.0f ; Dots:_FillValue = -9999 ; long Scan_Line(Number_of_Dice,Number_of_Dots) ; Scan_Line:long_name = "The number of the current scan line" ; Scan_Line:units = "none" ; Scan_Line:scale_factor = 1.0d ; Scan_Line:add_offset = 0.0d ; Scan_Line:parameter_type = "IASI data" ; Scan_Line:valid_range = 1.0f, 22.0f ; Scan_Line:_FillValue = -9999 ; long AMSU_FOV(Number_of_Dice,Number_of_Dots) ; AMSU_FOV:long_name = "The number of the current AMSU FOV" ; AMSU_FOV:units = "none" ; AMSU_FOV:scale_factor = 1.0d ; AMSU_FOV:add_offset = 0.0d ; AMSU_FOV:parameter_type = "IASI data" ; AMSU_FOV:valid_range = 1.0f, 30.0f ; AMSU_FOV:_FillValue = -9999 ; long IASI_FOV(Number_of_Dice,Number_of_Dots) ; IASI_FOV:long_name = "The number of the current IASI FOV" ; IASI_FOV:units = "none" ; IASI_FOV:scale_factor = 1.0d ; IASI_FOV:add_offset = 0.0d ; IASI_FOV:parameter_type = "IASI data" ; IASI_FOV:valid_range = 1.0f, 4.0f ; IASI_FOV:_FillValue = -9999 ; short GQisFlagQual(Number_of_Dice,Number_of_Dots) ; GQisFlagQual:long_name = "System QC flag" ; GQisFlagQual:units = "none" ; GQisFlagQual:scale_factor = 1 ; GQisFlagQual:add_offset = 0 ; GQisFlagQual:parameter_type = "IASI data" ; GQisFlagQual:valid_range = 0, 1 ; GQisFlagQual:_FillValue = -9999s ; float GQisQualIndex(Number_of_Dice,Number_of_Dots) ; GQisQualIndex:long_name = "System QC flag" ; GQisQualIndex:units = "none" ; GQisQualIndex:scale_factor = 1.0d ; GQisQualIndex:add_offset = 0.0d ; GQisQualIndex:parameter_type = "IASI data" ; GQisQualIndex:valid_range = 0.0f, 9999.0f ; GQisQualIndex:_FillValue = -9999.0f ; float GQisQualIndexLoc(Number_of_Dice,Number_of_Dots) ; GQisQualIndexLoc:long_name = "System QC flag" ; GQisQualIndexLoc:units = "none" ; GQisQualIndexLoc:scale_factor = 1.0d ; GQisQualIndexLoc:add_offset = 0.0d ; GQisQualIndexLoc:parameter_type = "IASI data" ; GQisQualIndexLoc:valid_range = 0.0f, 9999.0f ; GQisQualIndexLoc:_FillValue = -9999.0f ; float GQisQualIndexRad(Number_of_Dice,Number_of_Dots) ; GQisQualIndexRad:long_name = "System QC flag" ; GQisQualIndexRad:units = "none" ; GQisQualIndexRad:scale_factor = 1.0d ; GQisQualIndexRad:add_offset = 0.0d ; GQisQualIndexRad:parameter_type = "IASI data" ; GQisQualIndexRad:valid_range = 0.0f, 9999.0f ; GQisQualIndexRad:_FillValue = -9999.0f ; float GQisQualIndexSpect(Number_of_Dice,Number_of_Dots) ; GQisQualIndexSpect:long_name = "System QC flag" ; GQisQualIndexSpect:units = "none" ; GQisQualIndexSpect:scale_factor = 1.0d ; GQisQualIndexSpect:add_offset = 0.0d ; GQisQualIndexSpect:parameter_type = "IASI data" ; GQisQualIndexSpect:valid_range = 0.0f, 9999.0f ; GQisQualIndexSpect:_FillValue = -9999.0f ; float GQisSysTecSondQual(Number_of_Dice,Number_of_Dots) ; GQisSysTecSondQual:long_name = "System QC flag" ; GQisSysTecSondQual:units = "none" ; GQisSysTecSondQual:scale_factor = 1.0d ; GQisSysTecSondQual:add_offset = 0.0d ; GQisSysTecSondQual:parameter_type = "IASI data" ; GQisSysTecSondQual:valid_range = 0.0f, 9999.0f ; GQisSysTecSondQual:_FillValue = -9999.0f ; double Time(Number_of_Dice,Number_of_Dots) ; Time:long_name = "UTC Milliseconds since Jan 1, 1970" ; Time:units = "msec" ; Time:scale_factor = 1.0d ; Time:add_offset = 0.0d ; Time:parameter_type = "IASI data" ; Time:valid_range = 0.0f, 1577836800000.0f ; Time:_FillValue = -9999.0 ; float Latitude(Number_of_Dice,Number_of_Dots) ; Latitude:long_name = "IASI Latitude values for each FOV" ; Latitude:units = "degrees North" ; Latitude:scale_factor = 1.0d ; Latitude:add_offset = 0.0d ; Latitude:parameter_type = "IASI data" ; Latitude:valid_range = 90.0f, -90.0f ; Latitude:_FillValue = -9999.0f ; float Longitude(Number_of_Dice,Number_of_Dots) ; Longitude:long_name = "IASI Longitude values for each FOV" ; Longitude:units = "degrees East" ; Longitude:scale_factor = 1.0d ; Longitude:add_offset = 0.0d ; Longitude:parameter_type = "IASI data" ; Longitude:valid_range = -180.0f, 179.99f ; Longitude:_FillValue = -9999.0f ; float Principal_Components(Number_of_Dice,Number_of_Dots, Number_of_Principal_Components) ; Principal_Components:long_name = "IASI principal components for each FOV"; Principal_Components:units = "mW/m2/cm-1/sr" ; Principal_Components:scale_factor = 1.0d ; Principal_Components:add_offset = 0.0d ; Principal_Components:parameter_type = "IASI data" ; Principal_Components:valid_range = 0.0f, 40000.0f ; Principal_Components:_FillValue = -9999.0f ; float PC_Scores(Number_of_Dice,Number_of_Dots,Number_of_PC_Scores) ; PC_Scores:long_name = "IASI PC scores for each FOV" ; PC_Scores:units = "mW/m2/cm-1/sr" ; PC_Scores:scale_factor = 1.0d ; PC_Scores:add_offset = 0.0d ; PC_Scores:parameter_type = "IASI data" ; PC_Scores:valid_range = 0.0f, 40000.0f ; PC_Scores:_FillValue = -9999.0f ; short AVHRR_Channel_Combo(Number_of_Dice,Number_of_Dots) ; AVHRR_Channel_Combo:long_name = "AVHRR Channels used in radiance analysis" ; AVHRR_Channel_Combo:units = "none" ; AVHRR_Channel_Combo:scale_factor = 1 ; AVHRR_Channel_Combo:add_offset = 0 ; AVHRR_Channel_Combo:parameter_type = "IASI data" ; AVHRR_Channel_Combo:valid_range = 0, 1 ; AVHRR_Channel_Combo:_FillValue = -9999s ; float Fraction_of_Clear_AVHRR(Number_of_Dice,Number_of_Dots,Number_of_AVHRR_FOV_Classes) ; Fraction_of_Clear_AVHRR:long_name = "Percent clear for each AVHRR FOV class" ; Fraction_of_Clear_AVHRR:units = "%" ; Fraction_of_Clear_AVHRR:scale_factor = 1.0d ; Fraction_of_Clear_AVHRR:add_offset = 0.0d ; Fraction_of_Clear_AVHRR:parameter_type = "AVHRR data" ; Fraction_of_Clear_AVHRR:valid_range = 0.0f, 100.0f ; Fraction_of_Clear_AVHRR:_FillValue = -9999.0f ; float AVHRR_Y_Angle_Center_of_Gravity(Number_of_Dice,Number_of_Dots,Number_of_AVHRR_FOV_Classes) ; AVHRR_Y_Angle_Center_of_Gravity:long_name = "Y angular position of the center of gravity" ; AVHRR_Y_Angle_Center_of_Gravity:units = "degrees" ; AVHRR_Y_Angle_Center_of_Gravity:scale_factor = 1.0d ; AVHRR_Y_Angle_Center_of_Gravity:add_offset = 0.0d ; AVHRR_Y_Angle_Center_of_Gravity:parameter_type = "AVHRR data" ; AVHRR_Y_Angle_Center_of_Gravity:valid_range = 0.0f, 360.0f ; AVHRR_Y_Angle_Center_of_Gravity:_FillValue = -9999.0f ; float AVHRR_Z_Angle_Center_of_Gravity(Number_of_Dice,Number_of_Dots,Number_of_AVHRR_FOV_Classes) ; AVHRR_Z_Angle_Center_of_Gravity:long_name = "Z angular position of the center of gravity" ; AVHRR_Z_Angle_Center_of_Gravity:units = "degrees" ; AVHRR_Z_Angle_Center_of_Gravity:scale_factor = 1.0d ; AVHRR_Z_Angle_Center_of_Gravity:add_offset = 0.0d ; AVHRR_Z_Angle_Center_of_Gravity:parameter_type = "AVHRR data" ; AVHRR_Z_Angle_Center_of_Gravity:valid_range = 0.0f, 360.0f ; AVHRR_Z_Angle_Center_of_Gravity:_FillValue = -9999.0f ; float AVHRR_Mean_Radiances(Number_of_Dice,Number_of_Dots, Number_of_AVHRR_FOV_Classes,Number_of_AVHRR_Channels) ; AVHRR_Mean_Radiances:long_name = "Mean AVHRR radiances for each FOV" ; AVHRR_Mean_Radiances:units = "mW/m2/cm-1/sr" ; AVHRR_Mean_Radiances:scale_factor = 1.0d ; AVHRR_Mean_Radiances:add_offset = 0.0d ; AVHRR_Mean_Radiances:parameter_type = "AVHRR data" ; AVHRR_Mean_Radiances:valid_range = 0.0f, 40000.0f ; AVHRR_Mean_Radiances:_FillValue = -9999.0f ; float AVHRR_Std_Radiances(Number_of_Dice,Number_of_Dots,Number_of_AVHRR_FOV_Classes, Number_of_AVHRR_Channels) ; AVHRR_Std_Radiances:long_name = "Standard deviation of radiances for each FOV" ; AVHRR_Std_Radiances:units = "mW/m2/cm-1/sr" ; AVHRR_Std_Radiances:scale_factor = 1.0d ; AVHRR_Std_Radiances:add_offset = 0.0d ; AVHRR_Std_Radiances:parameter_type = "AVHRR data" ; AVHRR_Std_Radiances:valid_range = 0.0f, 40000.0f ; AVHRR_Std_Radiances:_FillValue = -9999.0f ; float View_Angle(Number_of_Dice,Number_of_Dots) ; View_Angle:long_name = "IASI View Angles for each FOV" ; View_Angle:units = "degrees" ; View_Angle:scale_factor = 1.0d ; View_Angle:add_offset = 0.0d ; View_Angle:parameter_type = "IASI data" ; View_Angle:valid_range = -90.0f, 90.0f ; View_Angle:_FillValue = -9999.0f ; float Satellite_Height(Number_of_Dice,Number_of_Dots) ; Satellite_Height:long_name = "Satellite height above each FOV" ; Satellite_Height:units = "km" ; Satellite_Height:scale_factor = 1.0 ; Satellite_Height:add_offset = 0.0 ; Satellite_Height:parameter_type = "IASI data" ; Satellite_Height:valid_range = 0.0f, 1000.0f ; Satellite_Height:_FillValue = -9999.0f ; float Satellite_Zenith(Number_of_Dice,Number_of_Dots) ; Satellite_Zenith:long_name = "Satellite zenith angles for each FOV" ; Satellite_Zenith:units = "degrees" ; Satellite_Zenith:scale_factor = 1.0 ; Satellite_Zenith:add_offset = 0.0 ; Satellite_Zenith:parameter_type = "IASI data" ; Satellite_Zenith:valid_range = 0.0f, 90.0f ; Satellite_Zenith:_FillValue = -9999.0f ; float Satellite_Azimuth(Number_of_Dice,Number_of_Dots) ; Satellite_Azimuth:long_name = "Satellite azimuth angles for each FOV" ; Satellite_Azimuth:units = "degrees" ; Satellite_Azimuth:scale_factor = 1.0 ; Satellite_Azimuth:add_offset = 0.0 ; Satellite_Azimuth:parameter_type = "IASI data" ; Satellite_Azimuth:valid_range = 0.0f, 180.0f ; Satellite_Azimuth:_FillValue = -9999.0f ; float Solar_Zenith(Number_of_Dice, Number_of_Dots) ; Solar_Zenith:long_name = "Solar zenith angles for each FOV" ; Solar_Zenith:units = "degrees" ; Solar_Zenith:scale_factor = 1.0 ; Solar_Zenith:add_offset = 0.0 ; Solar_Zenith:parameter_type = "IASI data" ; Solar_Zenith:valid_range = 0.f, 90.f ; Solar_Zenith:_FillValue = -9999.f ; float Solar_Azimuth(Number_of_Dice, Number_of_Dots) ; Solar_Azimuth:long_name = "Solar azimuth angles for each FOV" ; Solar_Azimuth:units = "degrees" ; Solar_Azimuth:scale_factor = 1.0 ; Solar_Azimuth:add_offset = 0.0 ; Solar_Azimuth:parameter_type = "IASI data" ; Solar_Azimuth:valid_range = 0.f, 180.f ; Solar_Azimuth:_FillValue = -9999.f ; short Ascending_Descending(Number_of_Dice, Number_of_Dots) ; Ascending_Descending:long_name = "0=Descending, 1=Ascending" ; Ascending_Descending:units = "none" ; Ascending_Descending:scale_factor = 1 ; Ascending_Descending:add_offset = 0 ; Ascending_Descending:parameter_type = "IASI data" ; Ascending_Descending:valid_range = 0, 1 ; Ascending_Descending:_FillValue = -9999s ; long Orbit_Number(Number_of_Dice,Number_of_Dots) ; Orbit_Number:long_name = "The number of the current orbit" ; Orbit_Number:units = "none" ; Orbit_Number:scale_factor = 1.0d ; Orbit_Number:add_offset = 0.0d ; Orbit_Number:parameter_type = "IASI data" ; Orbit_Number:valid_range = 1.0f, 100000.0f ; Orbit_Number:_FillValue = -9999 ; |
| --- | --- |

Intended Users

NRL/FNMOC

Access

These files are distributed from level 1c directories to the DDS.

POC – Nichols, Catherine L

5200 Auth Road, Room 0315, Building: FB4

Suitland, MD 20746 – 4301

Phone: (301)457-5245

Fax:      (301)457-5199

E-mail: cathy.nichols@noaa.gov

# LIST OF REFERENCES

EUMETSAT (2004), IASI Level 1 Product Format Specifications, Ref:	EUM.EPS.SYS.SPE.990003, Issue 6, Rev 6, WEB number 270000.

EUMETSAT (2003), EPS Programme Generic Product Format Specification , 	Ref: EPS.GGS.SPE.96167, Issue 6, Rev 4, WEB number 270000.

FGDC (1998), Content Standard for Digital Geospatial Metadata, VERSION 2, 	FGDC-STD-001-1998.

FGDC (2002), Content Standard for Digital Geospatial Metadata: Extensions for 	Remote Sending Metadata, FGDC-STD-012-2002.

NESDIS/CLASS (2006), Producer Archive Submission Agreement for IASI 	Products.  CLASS-1135-CLS-AGR-IASI.  X080.

NESDIS/CLASS (2008), Producer Archive Submission Agreement for IASI L2	Products.  In Progress.

NESDIS/STAR (2008a), IASI Product Processing System Project Baseline	Report.

NESDIS/STAR (2008b), IASI Product Processing System Requirements	Allocation Document.

NESDIS/STAR (2007c), STAR Unit Test Plan Document Guideline Version DG-	12.3, Version 2.

NESDIS/STAR (2008d), IASI Product Processing System Metadata Document.

NESDIS/STAR (2008e), IASI Product Processing System Interface Control	Document.

NESDIS/STAR (2008f), IASI Product Processing System System Maintenance	Manual.

NESDIS/STAR (2008g), IASI Product Processing System Products Operations	Manual.

NESDIS/STAR/IPD (2006), IASI Operations and Test Machine System 	Requirements Document.

# Appendix A -  IASI L1C BUFR Table

------------   USER DEFINITIONS FOR TABLE-A TABLE-B TABLE D   -------------- |

|------------------------------------------------------------------------------|

| MNEMONIC | NUMBER | DESCRIPTION                                              |

|----------|--------|----------------------------------------------------------|

|          |        |                                                          |

| NC021241 | A61207 | IASI 1C radiance data variable channels subset           |

|          |        |                                                          |

| IASIL1CB | 340002 | IASI Level 1C band description sequence                  |

| IASICHN  | 361137 | IASI Level 1C scaled radiance sequence                   |

| IASIL1CS | 340004 | IASI Level 1C AVHRR single scene sequence                |

| AVHRCHN  | 361139 | IASI Level 1C mean and std dev radiance sequence         |

|          |        |                                                          |

| SAID     | 001007 | Satellite identifier                                     |

| GCLONG   | 001031 | Identification of originating/generating center          |

| SIID     | 002019 | Satellite instruments                                    |

| SCLF     | 002020 | Satellite classification                                 |

| YEAR     | 004001 | Year                                                     |

| MNTH     | 004002 | Month                                                    |

| DAYS     | 004003 | Day                                                      |

| HOUR     | 004004 | Hour                                                     |

| MINU     | 004005 | Minute                                                   |

| SECO     | 004006 | Second                                                   |

| CLATH    | 005001 | Latitude (high accuracy)                                 |

| CLONH    | 006001 | Longitude (high accuracy)                                |

| SAZA     | 007024 | Satellite zenith angle                                   |

| BEARAZ   | 005021 | Bearing or azimuth                                       |

| SOZA     | 007025 | Solar zenith angle                                       |

| SOLAZI   | 005022 | Solar azimuth                                            |

| FOVN     | 005043 | Field of view number                                     |

| ORBN     | 005040 | Orbit number                                             |

| SLNM     | 005041 | Scan line number                                         |

| MJFC     | 025070 | Major frame count                                        |

| SELV     | 007001 | Height of station                                        |

| QGFQ     | 033060 | Individual IASI-System quality flag                      |

| QGQI     | 033061 | Instr. noise perf. indicator (spectral & radiometric)    |

| QGQIL    | 033062 | Geometric quality index indicator                        |

| QGQIR    | 033063 | Instr. noise perf. indicator (radiometric calibration)   |

| QGQIS    | 033064 | Instrument noise perf. indicator (spectral calibration)  |

| QGSSQ    | 033065 | Output of TEC function                                   |

| AVHCST   | 025051 | AVHRR channel combination                                |

| STCH     | 025140 | Start channel                                            |

| ENCH     | 025141 | End channel                                              |

| CHSF     | 025142 | Channel scale factor                                     |

| CHNM     | 005042 | Channel number                                           |

| SCRA     | 014046 | Scaled IASI radiance                                     |

| YAPCG    | 005060 | Y angular position of center of gravity                  |

| ZAPCG    | 005061 | Z angular position of center of gravity                  |

| FCPH     | 025085 | Fraction of clear pixels in HIRS FOV                     |

| SMRA     | 014047 | Scaled mean AVHRR radiance                               |

| SSDR     | 014048 | Scaled standard deviation of AVHRR radiance              |

|          |        |                                                          |

|------------------------------------------------------------------------------|

| MNEMONIC | SEQUENCE                                                          |

|----------|-------------------------------------------------------------------|

|          |                                                                   |

| NC021241 | SAID     GCLONG   SIID     SCLF     YEAR     MNTH     DAYS        |

| NC021241 | HOUR     MINU     202131   201138   SECO     201000   202000      |

| NC021241 | CLATH    CLONH    SAZA     BEARAZ   SOZA     SOLAZI               |

| NC021241 | FOVN     ORBN     201133   SLNM     201000                        |

| NC021241 | 201132   MJFC     201000   202126   SELV     202000               |

| NC021241 | QGFQ     QGQI     QGQIL    QGQIR    QGQIS    QGSSQ                |

| NC021241 | "IASIL1CB"10       (IASICHN)                                      |

| NC021241 | SIID     AVHCST   "IASIL1CS"7                                     |

|          |                                                                   |

| IASIL1CB | STCH     ENCH     CHSF                                            |

| IASICHN  | 201136   CHNM     201000   SCRA                                   |

| IASIL1CS | YAPCG    ZAPCG    FCPH     "AVHRCHN"6                             |

| AVHRCHN  | CHNM   CHSF   SMRA    CHSF    SSDR                                |

|          |                                                                   |

|------------------------------------------------------------------------------|

| MNEMONIC | SCAL | REFERENCE   | BIT | UNITS                    |-------------|

|----------|------|-------------|-----|--------------------------|-------------|

|          |      |             |     |                          |-------------|

| SAID     |    0 |           0 |  10 | Code table               |-------------|

| GCLONG   |    0 |           0 |  16 | Code table               |-------------|

| SIID     |    0 |           0 |  11 | Code table               |-------------|

| SCLF     |    0 |           0 |   9 | Code table               |-------------|

| YEAR     |    0 |           0 |  12 | Year                     |-------------|

| MNTH     |    0 |           0 |   4 | Month                    |-------------|

| DAYS     |    0 |           0 |   6 | Day                      |-------------|

| HOUR     |    0 |           0 |   5 | Hour                     |-------------|

| MINU     |    0 |           0 |   6 | Minute                   |-------------|

| SECO     |    0 |           0 |   6 | Second                   |-------------|

| CLATH    |    5 |    -9000000 |  25 | Degree                   |-------------|

| CLONH    |    5 |   -18000000 |  26 | Degree                   |-------------|

| SAZA     |    2 |       -9000 |  15 | Degree                   |-------------|

| BEARAZ   |    2 |           0 |  16 | Degree true              |-------------|

| SOZA     |    2 |       -9000 |  15 | Degree                   |-------------|

| SOLAZI   |    2 |           0 |  16 | Degree true              |-------------|

| FOVN     |    0 |           0 |   8 | Numeric                  |-------------|

| ORBN     |    0 |           0 |  24 | Numeric                  |-------------|

| SLNM     |    0 |           0 |   8 | Numeric                  |-------------|

| MJFC     |    0 |           0 |   4 | Numeric                  |-------------|

| SELV     |    0 |        -400 |  15 | m                        |-------------|

| QGFQ     |    0 |           0 |   2 | Code table               |-------------|

| QGQI     |    0 |           0 |   7 | %                        |-------------|

| QGQIL    |    0 |           0 |   7 | %                        |-------------|

| QGQIR    |    0 |           0 |   7 | %                        |-------------|

| QGQIS    |    0 |           0 |   7 | %                        |-------------|

| QGSSQ    |    0 |           0 |  24 | Numeric                  |-------------|

| AVHCST   |    0 |           0 |   7 | Flag table               |-------------|

| STCH     |    0 |           0 |  14 | Numeric                  |-------------|

| ENCH     |    0 |           0 |  14 | Numeric                  |-------------|

| CHSF     |    0 |           0 |   6 | Numeric                  |-------------|

| CHNM     |    0 |           0 |   6 | Numeric                  |-------------|

| SCRA     |    0 |           0 |  16 | W/m**2/sr/m**-1          |-------------|

| YAPCG    |    6 |    -8000000 |  24 | Degree                   |-------------|

| ZAPCG    |    6 |    -8000000 |  24 | Degree                   |-------------|

| FCPH     |    0 |           0 |   7 | Numeric                  |-------------|

| SMRA     |    0 |           0 |  31 | W/m**2/sr/m**-1          |-------------|

| SSDR     |    0 |           0 |  31 | W/m**2/sr/m**-1          |-------------|

|          |      |             |     |                          |-------------|

`------------------------------------------------------------------------------'