PROPOSAL INSTRUCTIONS:  __  DRAFT  --

_X_ FINAL –     PROPOSAL DUE BY:  11:00 a.m., 03/09/05

DO TITLE:  PORTABLE LIFE SUPPORT SUBSYSTEM (PLSS) SCHEMATIC STUDY

DO Type:  _X_ CPFF     ___ FFP

DO Contact Information:

TMR:	________ B. Mike Lawson_______			            Phone_____39124___

DO Manager: _____ Gretchen Thomas__				Phone_____37664___

DO Mgr. Alternate: _Mike Rouen___      				Phone_____39242___

Concurrences:

___S/ 2-15-05________	___S/ 2-15-05________	___S/ 2-15-05______

Gretchen Thomas	Craig Dinsmore     	Joe Gensler

DO Manager			      DO Mgr. Management		COTR

___S/ 2-15-05________	___S/ 2-15-05________

B. M. Lawson	 Steve Miller

Division TMR		       S & MA

Task Contains Flight Hardware, Flight Software or GSE?   	___ Yes	_X_No

Program Supported:    	__Shuttle     __ISS	 __EVA    _X_Advanced All Spirals

---------------------------------------------------------------------------------------------------------------

WBS:  X 1.0 EVA  __ 2.0 FCE   __ 3.0 EVR   __ ECLSS   __ 5.0 ATCS   __ 6.0 CHeCS

For purposes of complying with FAR 52.232-22, Limitation of Funds, the total amount allotted by the Government to contract is specified in clause B.6, Contract Funding.  The funding listed in B.6 is the amount allotted for all Delivery Orders on the contract combined.

All terms and conditions of the contract apply to this Delivery Order.  In the event of a conflict between the contract and this Delivery Order, the contract shall prevail.

WBS reporting shall be done in accordance with applicable WBS reporting categories, as shown above and in the contract within Section C, Table 1.

# Narrative Task Description

## Background / Problem Description:

### Schematic Definition

For this study, a Portable Life Support Subsystem (PLSS) schematic is the single page diagram that describes the technologies selected to accomplish the life support functions and the fluid mechanical functional interconnections.  A Portable Life Support Subsystem is here taken to mean a self contained life support subsystem along with the emergency life support system required to accomplish a fail safe design. This excludes such umbilical supplied life support subsystems such as the Skylab ALSA. It does not exclude such arrangements as having recharge capability carried on a rover or other methods used to off load crew person carried weight. For this study, the term “schematic” is limited to the fluid and mechanical functions and only the electrical functions necessary to maintain safety. This definition purposely excludes the information handling architecture of the EVA informatics related hardware which is another study itself.

### Schematic History

An example of the schematic currently in use in the United States space program is shown in

Figure 1. The only other US portable life support subsystem, the Apollo PLSS, used a similar schematic as does the current Russian space suit. All three share in common the following technologies: high pressure oxygen storage, sublimator for heat rejection, battery for power, lithium hydroxide for CO2 control, and charcoal for trace contaminant control. Although they each have some different interconnections (for example the Shuttle is set up for zero g operation while the Apollo system was optimized for gravity field operation) the basic schematic is the same from the stand point of use of the technologies listed above. The only deviation from this list is the replacement of lithium hydroxide with an in orbit regenerable metal oxide for CO2 control on the ISS which was driven by a storage volume and launch cost tradeoff.

### Prior Studies

Prior studies of Portable Life Support Subsystem schematic arrangements have been accomplished. A particularly comprehensive study, the Advanced Extravehicular Protective Systems (AEPS) Study, was accomplished for the Ames Research Center (NAS 2-6021) by J. G. Sutton, P. H. Heimlich, and E. H. Tepper of the Hamilton Standard Division of United Technologies in 1972 (NASA CR114384).  A broader study of the EVA system as a work system included portable life support considerations and was accomplished in 1980 but it was focused on zero g operations and so did not include lunar and mars related information. In anticipation of the space station and in preparation to direct the technology program leading up to selection of a schematic for space station use, NASA accomplished an in house study in the 1987 time frame. It was titled the Point Design Study and was only documented via presentation charts. But, again, this study was focused on

Zero G operations only.  During the First Lunar Outpost activity some schematic study was done focused on the lunar destination. This work identified radiators as a viable heat rejection mechanism. This work is documented in “First Lunar Outpost Extravehicular Life Support System Evaluation,” Bruce C. Conger, Luis A. Trevino and B. Michael Lawson, ICES paper number 932188. This study did not cover the breath of technologies of interest being mainly concerned with the thermal subsystem. Consequently, the best study to use as a base for the present effort is the 1972 AEPS study.

Prior studies of the EVA system needed to accomplish Lunar and Mars exploration were accomplished in 1988. These studies provide excellent context for how and where the PLSS will be used. The studies were performed under the generic title of “Extravehicular Activity Systems Requirements Definition Study” resulting in “Extravehicular Activity at a Lunar Base,” September 1988 and “Extravehicular Activity in Mars Surface Exploration,” May 1989 lead by the ESSEX Co. and performed under contract NAS 9-17779.

### PLSS Interfaces:

The PLSS is strongly driven by vehicle life support and power systems for it is the vehicle systems that determine what resources are available for PLSS recharge. This interaction creates a strong tie of the PLSS technology selections to the vehicle technology selections requiring the EVA community to be ready to support vehicle trade studies with a complete picture of the impacts of various vehicle technology selections on the PLSS. Some vehicle technology selections close entire technology class path ways and others can force the PLSS into selections that tend to open loops the vehicle life support community has been striving hard to close. It is important that the PLSS community “do its homework” early so the vehicle trade studies can be properly supported.

### New Technology

Certainly in the 32 years since the 1972 study there has been a significant amount of technology development accomplished both inside the aerospace industry (most often documented in the ICES conference) and outside that is applicable to the PLSS schematic. Besides the life support technology development directly, there has been significant work done on basic materials (CO2 absorption chemistry, MEMS and nanotechnology) and fundamental process (Microchannel heat and mass transfer).

Three major areas of technology that are expected to have considerable impact on the PLSS schematic are: 1) the shrinking size of power supplies making it possible to go from battery supplied power to a fuel based power supply which can raise the power available from the current 100W range to the 1000W range, 2) the Microsystems elements that are becoming available for heat transfer and chemical processes and 3) the distributed sensing / processing technologies. The first makes it possible to consider high power thereby allowing the use of technologies that have been rejected in all previous studies because of the weight cost of the power supply required.  The second aids this trend and makes all processes potentially smaller and lighter. The third has profound implications on the packaging (which accounts for half the system weight) of a PLSS but, more germane to this study, provides the opportunity to better monitor PLSS performance and thereby aid in accomplishing the needed increases in PLSS life time and reduction in testing to assure safety.

Outside of NASA, significant work has been done on portable life support for Earth based use by the military in response to chemical and biological warfare threats and there is current interest concerning similar threats for first responders for homeland defense. Commercial applications for some subsystems of the portable life support subsystem (thermal control) have arisen for work in extreme environments and for mitigation of symptoms of some medical conditions such as MS.

Even the fundamental engineering process of how to do selection trade off studies has undergone significant change as documented in books by authors such as Pugh and Ullman.

All of these facts suggest it is time for a new comprehensive study that builds on but does not repeat prior work as we prepare to plan and implement the technology program focused on fulfillment of the Vision for Space Exploration. A study drawing on NASA and non NASA expertise is warranted

and needed to lay out a development roadmap that directs budget planning for future exploration efforts. In addition, new analysis capabilities and design methodologies are available allowing a more comprehensive study than previous studies with the same resources.

## PROCESS TO BE FOLLOWED:

### Form Design Team(s)

An interdisciplinary design team that includes both NASA and the contractor personnel is to be formed for the generation and evaluation of schematic concepts.  The contractor is to plan to accomplish the entire job without dependence on NASA effort.  NASA effort will provide operational experience and additional depth of study but shall not be planned into the critical path to accomplish the study requirements.  If it is deemed advisable, teams can be formed that focus on subsystems of the schematic and team selection, and may include or may not include NASA participants to supply the team with additional expertise.  The availability of NASA expertise is described below in the Table 1 – Potentially Available NASA Expertise is planned to be provided as a “best efforts” arrangement.

###### Develop Tasks Assignment

Since the exact nature of the expertise to be provided by NASA is needed in order to do an in-depth plan, internal team planning will be accomplished as agreed to by NASA and the contractor for accomplishment of tasks.  This planning shall not affect the scope of the contractor’s work but can increase or decrease the scope of potentially available NASA participation.

###### Schedule Project

Since the exact schedule availability of the potentially available NASA expertise is subjective, internal team planning for adjustments to various task schedules will be accomplished as agreed to by NASA and the contractor.  These schedule adjustments shall not affect the scope of the contractor’s work.

###### Form Teams

Team composition shall be based not only on the technical expertise needed but with due considerations for the different roles needed to form an effective design team.  Design teams are to

be limited to the number of people required to form an effective team.  The teams shall solicit the input of those outside the team, as needed, to accomplish the design task at hand.  The teams shall

support the contract milestone reviews and respond to any Review Item Discrepancies (RIDs) generated during those reviews that affect the design team’s efforts.

### Define the Problem

Success of a design process depends heavily on good problem definition which is not a trivial exercise. As a minimum the following steps shall be accomplished to fully define the problem of PLSS schematic selection.

###### --  Review and Update Prior Work

The following studies shall be reviewed and updated as needed to take into account new knowledge of the technologies included in those studies since their completion. Where entirely new technology or techniques have come to fore, this study is expected to address those issues. Consequently, this update task is expected to be of limited scope.

- “Advanced Extravehicular Protective Systems (AEPS) Study,” 1972

- “Extravehicular Activity at a Lunar Base,” September 1988

- “Extravehicular Activity in Mars Surface Exploration,” May 1989

One area of concern where update of the Lunar Base study is known to be required is operation in the lunar pole area. The potential for extremely cold environments (order of 40°K) is a concern and a specific analysis of the impacts on the PLSS schematic and technology selection of this case is required.

###### --  Develop Vehicle Interfaces

The PLSS is strongly driven by the resources available from the vehicle on which it is based and used. The PLSS potentially receives resources from the vehicle life support, propulsion, and power systems. An effort shall be accomplished to scope the potentially available resources that are likely to be available for the Lunar and Mars missions. To accomplish this task the NASA will provide support to address the impacts of EVA system resource needs on other spacecraft systems.

###### --  Prepare the Functional Decomposition

A functional decomposition shall be accomplished that is designed to drive out “what” is needed to accomplish the PLSS purpose. This decomposition is specifically done without regard to “how” the functions are to be accomplished. A functional decomposition shall be accomplished for the PLSS as a whole and for the major subsystems that the PLSS decomposition identifies. The purpose of the functional decomposition is to break the problem down in a way that generates the greatest understanding of the PLSS and forms a basis to allow the generation of creative solutions for the PLSS functions.

###### --  Develop Specifications

As a basis for the customer specification, the Advanced Technology Space Suit Design Requirements Document DRD, July 1999 shall be used. This specification shall be reviewed and those portions of it applicable to this effort updated as necessary by NASA with input from design team members. This customer specification includes those areas that must be controlled to accomplish the end use of the PLSS.

Engineering “Mini specifications” shall be prepared for each function that must be met to “tier down” the customer specification to the measurable, verifiable specifications needed for engineering design.  These specifications shall capture the essence of the engineering requirements for any functional component or subsystem that satisfies the functional need.  Except in rare cases, these specifications shall be contained on one page for each function.

###### --  Develop Evaluation Criteria

Evaluation criteria and their rankings shall be developed prior to the effort to generate concepts so that the figures of merit for concepts are well understood by those who generate the concepts and to avoid the pitfall of subliminally designing selection criteria that favor particular concepts. In terms of criteria ranking, safety (both Flight and Ground Operational), shall rank first.

1.  The ability of the concept to be used in non-NASA applications shall be used as a criterion.

2.  The degree a concept supports commonality shall be used as a criterion.

--  Develop Concepts

The basic premise is that to find a good idea of how to accomplish a function many ideas must be generated. So a divergent convergent path is planned.

###### --  Search for Function Satisfying Ideas

This activity is meant to be a primary place where creativity has a chance to happen at the function level. The idea is to generate as many concepts as possible for each of the lowest level functions identified in the functional decomposition. A concept is an idea that is sufficiently developed so that its behavior in the intended use can be evaluated.

###### --  Generate PLSS Concepts

This activity is meant to be the primary place where creativity has a chance to happen at the PLSS level. For this activity a PLSS concept is a combination of the concepts generated to satisfy each function which is capable of accomplishing the entire PLSS job. System level considerations shall be used to keep the number of concepts within bounds. For example, one function concept may generate an output (waste heat for example) that can be effectively used as an input for a function satisfying concept for a different function. In such a case the logical thing to do is use those different concepts together.

###### --  Document Concepts

Since there is expected to be a range of technological maturity in the concepts (i.e. the concepts currently in use in flight systems versus a wholly new concept that is the result of a creative search) it is important that all concepts be described and documented to a similar degree for comparison purposes.

At the functional concept level a Failure Modes and Effects Analysis (FMEA) will be generated for each viable concept. For the PLSS level, an FMEA will be generated using as a basis all of the functional concept level FMEAs and including system interactions so that the safety of each schematic concept can be judged. As concepts are being generated, the FMEAs are expected to be a design tool; consequently, they must be generated as early in the process as possible.

### --  Evaluate Concepts

Criteria are expected to lend themselves to two types of comparisons to requirements, absolute and relative.  Where the criteria are to be evaluated in a relative manner, the Decision-matrix method shall be used. Several rounds of evaluation are expected both at the lower function level and at the PLSS level.  The absolute comparisons made by engineering analysis shall be used in the rankings done as part of the Decision-matrix method so that a complete picture of concept performance is formulated and used in the final selection ranking.

Table 1 - Potentially Available NASA Expertise

Background and Expertise

Experience with NASA Advanced PLSS Technology. Expertise in Systems Engineering & Integration, ventilation and thermal technology; 10+ years experience as NASA project manager for advanced and flight systems. Experience acting in the shaper role on design teams

Experience as lead for PLSS group for NASA during the development of the Shuttle EMU. 20 years PLSS Advanced Technology leadership experience. Pro-E modeler. Experience with significant study of design methods including techniques to foster creativity. Experience acting in the coordinator role on design teams.

Experience as a subsystem manager for Shuttle active thermal control freon loop (radiators, flash evaporator, ammonia boiler, etc.) and EMU thermal and systems analysis manager for NASA during early Shuttle missions. Experience in Shuttle EMU thermal certification, vent loop pressure drop analyses, smoke-in-cabin contingency analyses, suit purge analysis-testing-certification, and visor thermal certification. Experience in advanced spacesuit Lunar and Mars spacesuit insulation. Experience in working well in various team roles, including creativity and implementation.

Experience in designing various Payload and EVA tools and equipment, EVA systems engineering, integration of space suit with vehicle, EVA operations and training, human/robotics interaction, advanced EVA concepts and designs, use of advanced technologies in EVA systems, and with design team roles: Creator, Resource-investigator, and monitor-evaluator.

Advanced EVA experience, including insulation testing and research, airlock concept development, and PLSS packaging concepts and lead for the PLSS ventilation system. Experience in all design team roles, especially as a coordinator, shaper, and implementer.

Approximately 15 years of spacecraft thermal control and life support analysis, thermal control system development for Space Station and advanced development projects. Experience performing systems analysis for Advanced Life Support and coordination of many trade-off studies. Experience in the development of the “equivalent system mass (ESM)” analysis methodology.

Approximately 16 years of experience in development of analytical and computational tools for performance predictions and design optimization of thermal, mechanical and chemical systems relating to extravehicular activity (EVA) and pressure suits. Specific experience with thermal, chemical and mass transfer analysis, integration and modeling for Zero g, Lunar and Mars environments, including analysis of human thermal comfort and efficiency. Experience in design teams as a shaper, to find practical but creative ways of solving complex technical problems, including stripping needless conservatism from models.

Approximately 20 years of R&D battery experience. Lead experience for the design and implementation of EVA batteries including the new lithium-ion design for the PLSS. Experience playing, coordinator, creator, and implementer in the past design teams."

Approximately 20 years battery experience and experience managing the NASA ISS Battery Team. Experience leading contractor teams for design, deployment, storage, and operation of ISS batteries. Evaluation and recommendation expertise for Lithium-ion and Nickel-Hydrogen battery technology. Polymer Energy Rechargeable System program expertise. Experience as coordinator, monitor-evaluator, team worker, implementer, and completer-finisher on past teams.

Approximately 20 years experience in analysis of electrochemical energy storage systems for a range of applications including: earth-orbiting and planetary spacecraft; lunar and Mars outpost and rover vehicle power; and unmanned air vehicles.

### Note:  Please refer to specifics concerning Potentially Available NASA Expertise in the above “Processes to be Followed” section, within this DO.

### Technical Library Contents –

Advanced Extravehicular Protective Systems (AEPS) Study, was accomplished for the Ames Research Center (NAS 2-6021) by J. G. Sutton, P. H. Heimlich, and E. H. Tepper of the Hamilton Standard Division of United Technologies in 1972 (NASA CR114384).

“Extravehicular Activity Systems Requirements Definition Study” resulting in “Extravehicular Activity at a Lunar Base,” September 1988 and “Extravehicular Activity in Mars Surface Exploration,” May 1989 lead by the ESSEX Co. and performed under contract NAS 9-17779.

Advanced Technology Space Suit Design Requirements Document DRD, July 1999

Government Project Plan and Cost estimate as documented in the Microsoft Project file titled:

PLSS Schematic Study 12-01-04.mpp

RAESR_Template.doc

GFE EVA FEMA Guide.pdf

Figure 1 - Shuttle EMU Schematic

Deliverables/Products:

| Product | Description | Qty | Due | Class |
| --- | --- | --- | --- | --- |
| Hardware | None Required |  |  |  |
| Mock Up |  |  |  |  |
| Prototype |  |  |  |  |
| Certification |  |  |  |  |
| Flight |  |  |  |  |
| Training |  |  |  |  |
| Other |  |  |  |  |
| Test | None Required |  |  |  |
| Software | None Required |  |  |  |
| Other Products |  |  |  |  |
| Road Map | A well documented and justified, multi-concept development road map that is phased by mission and spiral. Several parallel paths may be included in the road map with one listed as the baseline along with statements of the evaluation criteria that are expected to cause a change to the baseline concept. The selected concepts must be part of a planned evolutionary path that steps in a logical way to provide a good solution for the upcoming missions and spirals. The road map should assume a PLSS packaging technology that allows reasonable cost technology evolution and upgrade as the programs progress to more challenging environments and operating conditions. | 1 Electronic Copy | Upon Completion (Drafts as Required to Support Scheduled Milestones) | N/A |
| Documentation | The schematics will be documented with the following as a minimum. Top level Failure Mode and Effect Analysis Size variation with metabolic rate and EVA duration and the math models used in the sizing. Vehicle interface requirements. Rational for selection of the technology and PLSS Schematic concept | 1 Electronic Copy | Upon Completion (Drafts as Required to Support Scheduled Milestones) | N/A |
| Math Models | The information needed to upgrade the mission study support tool EVA System Sizing Analysis Tool (EVASSAT) that is used to support advanced mission and vehicle studies is also a required product. | 1 Electronic Copy | Upon Completion (Drafts as Required to Support Scheduled Milestones) | N/A |
| Lunar Pole Operation Impact Report | Report on the impact of operation at the lunar poles. | 1 Electronic Copy | Upon Completion (Drafts as Required to Support Scheduled Milestones) | N/A |
| Commonality Report | Report on commonality analysis accomplished. | 1 Electronic Copy | Upon Completion (Drafts as Required to Support Scheduled Milestones) | N/A |
| Final Report | Final Report | 1 Electronic Copy | Upon Completion | N/A |

SCHEDULE

Start Date:	03/28/05						Finish Date:	 10/13/05

| ITERIM MILESTONES | DUE DATES |
| --- | --- |
| Kick-Off Meeting | 2 weeks after DO Award |
| Problem Definition Review | 6 weeks after DO Award |
| Concept Design Review | 24 weeks after DO Award |
| Project Complete | 30 weeks after DO Award |
| For schedule detail see Microsoft Project file located on the CRAVE web site for this DO listed under the Government Cost Estimate below. |

Government Estimate Located in RFQ File in Microsoft Project File On CRAVE Web Site

The file is titled:  PLSS Schematic Study 12-01-04R3.mpp

Total Government Estimate for this DO:  $ 400 K

Option 1:  $  N/A   (See Attachment 1)

Option 2:  $  N/A   (See Attachment 2)

TOTAL COST ESTIMATE FOR THIS DO:  $

FEE:  $  (If Applicable)

OPTION 1:  $  N/A   (See Attachment 1)

OPTION 2: $  N/A   (See Attachment 2)

DATA REQUIREMENTS

All DRs contained in the contract are applicable and required unless marked N/A below.

Notes:  1. Grey Scaled Cells Need No Additional/Required Fill-ins.

2. On All Other Cells, If Necessary, Fill in Additional Rqmts/Deliveries in Last Column.

| DRD # | DATA TYPE | DRD TITLE | DUE | FREQUENCY | REQUIRED FOR DO? Y/N | ADDITIONAL REQUIREMENTS |
| --- | --- | --- | --- | --- | --- | --- |
| 1 | Written Approval | FlightGFE Configuration Management Plan | With Proposal | Once | Attachment J-8 |  |
| 2 | Mandatory Submittal | Regular Status Report/ Summary Review | Thirty (30) days following contract start | Monthly | Y |  |
| 3 | Written Approval | Project Technical Requirements Specification | Per DO schedule | Once with Revisions | Y | Support Government modification of existing specification |
| 4 | Mandatory Submittal | GFE Systems Requirements Data Package | Specified in DO | Once with Revisions | N |  |
| 5 | Written Approval | Flight GFE Projects Requirements & Verification Document | Specified in DO | Once with Revisions | N |  |
| 6 | Mandatory Submittal | Preliminary Design Review Data Package | Specified in DO | Once with Revisions |  |  |
| 7 | Written Approval | Flight GFE Workmanship Specifications List | Specified in DO | Once with Revisions | N |  |
| 8 | Written Approval | Project Schedule | PDR or 10% effort complete Milestone | Once w/Revisions (due w/DO proposal, updates & details provided as DO progresses) | Y | First update that includes detail NASA participation 2 weeks after Kickoff meeting. |
| 9 | Written Approval | Flight GFE Interface Control Document | Specified in DO | Once with Revisions | Y | Informal ICDS only with team generating vehicle impacts as no vehicle engineering teams are in place at this time. Flight approval rigor is not required |
| 10 | Written Approval | GFE End Item Specification | Specified in DO | Once with Revisions | N |  |
| 11 | Mandatory Submittal | Flight GFE Failure Analysis Report | As agreed by TMR in DO | As Required | N |  |
| 12 | Written Approval | Flight GFE Verification and Validation Plan | As Specified in EA-023 | Once with Revisions | Y | Only those unique to the schematic understudy and to a depth to assist evaluation and comparison of the schematics. Flight approval rigor is not required |
| 13 | Written Approval | GFE Software Requirements Specification | Specified in DO | Once with Revisions | Y | Only those unique to the schematic understudy and to a depth to assist evaluation and comparison of the schematics. Flight approval rigor is not required |
| 14 | Written Approval | GFE Software Development Plan | Specified in DO | Once with Revisions | N |  |
| 15 | Written Approval | GFE Software Design Document | Specified in DO | As Required | N |  |
| 16 | Written Approval | Engineering Drawings | At PDR, as specified in DO | Once with Revisions | N |  |
| 17 | Written Approval | EEE Parts Lists and Analysis Report | Specified in DO | As Required | N |  |
| 18 | Mandatory Submittal | Critical Design Review Data Package | Specified in DO | Once with Revisions | N |  |
| 19 | Mandatory Submittal | Engineering Drawing Change Proposal | As needed | As Required | N |  |
| 20 | Written Approval | GFE Qualification Test Procedure | Specified in DO | Once with Revisions | N |  |
| 21 | Written Approval | Flight Product User’s Guide | Specified in DO | Once with Revisions | N |  |
| 22 | Mandatory Submittal | Software Code | Specified in DO | As Required | N |  |
| 23 | Written Approval | Information Technology (IT) Security Program Plan and Reports | (30) days after DO award, and as specified in JPG 2810.1 | JPG 2810.1 | Attachment J-4 Due 30 days after DO award |  |
| 24 | Written Approval | Certification Plan | Specified in DO | Once with Revisions | N |  |
| 25 | Mandatory Submittal | Certification Report | Specified in DO | Once with Revisions | N |  |
| 26 | Mandatory Submittal | Engineering Analysis | Specified in DO | As Required | Y | Analysis rigor sufficient for use in hardware certification are not required. Rigor needed is that to support understanding of and selection of schematics. Flight approval rigor is not required |
| 27 | Mandatory Submittal | Acceptance Data Package | Specified in DO | One Time | N |  |
| 28 | Mandatory Submittal | Export Control Audit Results | After award of 1st DO, yearly on Sept. 30 thereafter | Yearly | Y |  |
| 29 | Written Approval | Quality Plan | With Proposal | Once with Revisions | Attachment J-11 |  |
| 30 | Written Approval | Patent Rights-Retention | As Required | As Required | Y (If Applic’ble) |  |
| 31 | Written Approval | Shuttle/Station Payload Safety Data Package | Specified in DO | As Required | N |  |
| 32 | Mandatory Submittal | Limited Life Systems List | Specified in DO | As Required | Y | Only to rigor necessary to understand schematic logistics issues. Flight approval rigor is not required |
| 33 | Written Approval | Space Station GFE Failure Modes and Effects Analysis and Critical Items List | As Early in process as possible. | As Required | Y | Flight preparation and approval rigor is not required and detail appropriate for the schematic level of understanding, evaluation and selection. |
| 34 | Written Approval | Space Shuttle GFE Safety and Analysis Report &Hazard Report | Specified in DO | As Required | N |  |
| 35 | Written Approval | Software Quality Assurance Plan Report | 90 Days Prior to Software Development | Once with Revisions | Y (If Applic’ble) |  |
| 36 | Written Approval | ISS Hazard Report | Specified in DO | As Required | N |  |
| 37 | Upon Request | Reliability and Maintainability Plan | With Proposal | One Time | Attachment J-9 |  |
| 38 | Written Approval | Government Certification Approval Request (GCAR) | Specified in DO | As Required | N |  |
| 39 | Written Approval | Risk Assessment Executive Summary Report (RAESR) | Specified in DO | As Required | Y | Use as an outline for the safety section of the schematic documentation. Flight preparation and approval rigor is not required Detail only as necessary to understand and select schematics. |
| 40 | Written Approval | Problem Reporting and Corrective Action (PRACA) | 2 business days of problem isolation but no later than 10 days after detection | As Required | N |  |
| 41 | Upon Request | Nonconformance Record | Specified in DO | As Required | N |  |
| 42 | Mandatory Submittal | Government Industry Data Exchange Program and NASA Advisory Problem Data | Reported one time when discrepancy occurs | Once with Revisions | N |  |
| 43 | Written Approval | Electrical, Electronic, and Electromechnical (EEE) Parts Control Plan | Specified in DO | Once with Revisions | N |  |
| 44 | Mandatory Submittal | Certification Data Package | Specified in DO | Once with Revisions | N |  |
| 45 | Written Approval | Certification and Acceptance Requirements Document | At CDR | Once with Revisions | N |  |
| 46 | Upon Request | Wage/Salary and Fringe Benefit Data | thirty (30) days after issuance of each DO | Once | N |  |
| 47 | Written Approval | GFE Acceptance Test Procedure | Specified in DO | One Time | N |  |
| 48 | Mandatory Submittal | Flight GFE Verification & Validation Report | Specified in DO | Once with Revisions | N |  |
| 49 | Mandatory Submittal | Space Shuttle GFE Failure Modes and Effects Analysis (FMEA) and Critical Items List | Specified in DO | As Required | N |  |
| 50 |  | Reserved | --- | --- | --- | --- |
| 51 | Mandatory Submittal | NASA Contractor Financial Management Reporting | After Issuance of 1st DO | Monthly | Y |  |
| 52 | Written Approval | Government Property Management Plan | With Proposal | Once with Revisions | Attachment J-7 |  |
| 53 | Mandatory Submittal | System Safety Plan | With Proposal | One Time | Attachment J-10 |  |
| 54 | Written Approval | R-Quality Plan Template | With Proposal/ Revisions as Required | Only applicable to B-CRAVE contracts in accordance with the SOW and the DRD | Y |  |

Type 1 = Written Approval               Type 2 = Mandatory Submittal                Type 3 = Submittal Upon Request

GOVERNMENT FURNISHED PROPERTY

None Required

# Footnotes

The ICES conference, cosponsored by multiple engineering societies and managed by the SAE, is one of the primary places the EVA community publishes.

Pugh, S.: Total Design Integrated Methods for Successful Product Engineering, Addison-Wesley, Wokingham, England, 1991

Ullman, D. G.: The Mechanical Design Process, McGraw Hill, 1992

For example see 3.5.2 Team Roles, Page 55 of Ullman’s Second Edition.

Guidance on how to accomplish the kind of functional decomposition contemplated is contained in Ullman, 2nd Edition, Chapter 7.

6 See Ullman, D. G.: The Mechanical Design Process, McGraw Hill, 1992, chapter 8.