APPENDIX E

Measuring Pavement Roughness

Introduction

In order to provide a measure of pavement surface condition that has nationwide consistency and comparability and is as realistic and practical as possible, a uniform, calibrated roughness measurement for paved roadways is required by the HPMS.

Roughness is defined in accordance with ASTM E867 as “The deviation of a surface from a true planar surface with characteristic dimensions that affect vehicle dynamics and ride quality.”  After a detailed study of various methodologies and road profiling statistics, the International Roughness Index (IRI) was chosen as the HPMS standard reference roughness index.  The summary numeric (HPMS data reporting unit) is the IRI in meters/kilometer (inches/mile).  The primary advantages of the IRI are:

- It is a time-stable, reproducible mathematical processing of the known profile.

- It is broadly representative of the effects of roughness on vehicle response and user’s perception over the range of wavelengths of interest, and is thus relevant to the definition of roughness.

- It is a zero-origin scale consistent with the roughness definition.

- It is compatible with profile measuring equipment available in the U.S. market.

- It is independent of section length and amenable to simple averaging.

      - It is consistent with established international standards and able to be related to other roughness measures.

HPMS Roughness Measurement Procedure

The reference method for obtaining IRI data for the HPMS can be found in the AASHTO Standard Practice for Determination of International Roughness Index for Quantifying Roughness of Pavements, AASHTO PP 37-04.  This Standard Practice calls for the use of a longitudinal profile measured in accordance with ASTM E-950 as a basis for estimating IRI.  AASHTO PP 37-04 is reproduced in this appendix with the written consent of AASHTO.  Roughness is reported for HPMS in IRI units of either m/km or in/mi (1 m/km = 63.36 in/mi).

Roughness data should be reported in IRI units for all sections in accordance with Table IV-1 in Chapter IV.  The lower functional systems (rural and urban collector and urban minor arterial) have been placed in the “recommended” category since there are situations where it may not be possible to obtain meaningful roughness measurements with profiling equipment.  Major obstacles include:

Speed restrictions				Traffic congestion

Short section lengths				Pavement treatments

Numerous traffic signals			Intersection treatments

However, some of these obstacles can be overcome by collecting roughness data during non-peak hours or at night, where speed, traffic, and safety are less of a problem.  There are situations where it also may not be possible to obtain meaningful roughness measurements on some urban other principal arterial sections.  In these cases, a value of “0” may be reported.

All equipment must be operated within manufacturer’s specifications; quality assurance guidelines outlined in AASHTO PP 37-04, Section 5, and Appendix B, must be followed.  Each State should document and retain records of its quality assurance procedures; FHWA field offices should monitor adherence to these procedures as part of roughness data process reviews.

Additional Recommendations for Collection of Roughness Data

The following field survey guidelines are recommended for State use in addition to the AASHTO Standard Practice:

- Where roughness data are collected in both directions, the State should use the “inventory direction” selected in accordance with the discussion on page IV-2 of the HPMS Field Manual for reporting IRI data and should use this same direction for all future HPMS reporting.

- For multi-lane facilities, roughness data for the outside (right) lane should be reported.  However, if this is not practical, whichever lane is measured should be used for all future HPMS reporting.

- Roughness data collection should be performed when the pavement is in stable condition.  Data should not be collected during winter (frost/freeze or freeze/thaw) or wet base conditions.  Data collection should be performed during good weather conditions when wind conditions will not affect equipment stability and on dry pavement.  All equipment manufacturer’s recommended procedures should be observed.

- Data should only be collected at the speeds that correspond to the manufacturer’s recommended speed range.  Constant speeds should be maintained for all measurements within specified ranges.

- Exclude the impacts of bridge approaches and railroad crossings (or other localized discontinuities) from the roughness measurement for the roadway.  Bridge decks should not be included; the objective is to obtain a measure of pavement not bridge roughness.

- Roughness measurements should be taken over the entire length of an HPMS roadway section.  However, in order to achieve equipment and speed stability, a minimum run-in length, consistent with the manufacturer’s specification, may be required prior to the beginning of the measurement area.  If this minimum cannot be met prior to the start of the sample section, a shorter portion of the HPMS section may be measured, but that same portion should always be measured in future roughness data collection activities.  Short HPMS sections also may be included in slightly longer roughness test sections for measurement and reporting purposes.  However, the same longer sections should always be measured in future data collections.

Coordination with Other Activities

One of the goals of HPMS is to avoid duplicate data collection efforts.  States are encouraged to coordinate roughness measurement activities, where possible, such that the same equipment, verification sites, and measurements are used for multiple purposes.  Therefore, HPMS activities should be coordinated with other State activities such as the Strategic Highway Research Program (SHRP)/Long Term Pavement Performance (LTPP) and the State Pavement Management Systems (PMS).

The LTPP activities monitor pavement performance and use in detail for approximately 1,500 pavement sections nationwide as part of SHRP.  The pavement and traffic monitoring data collected on LTPP sections should be used for the HPMS universe or standard sample sections where possible.  In addition, efforts should be made to utilize the LTPP established sections/profiles as multiple-use verification sections in each State.

Many State and some local transportation agencies have operational or are developing a PMS to guide program development, improve life-cycle costs, and help select the most effective pavement improvement strategies.  The HPMS pavement data reporting should make full use of existing PMS data and collection activities.  Data collected by others (cities, counties, MPO’s, etc.) should be subjected to the same AASHTO quality assurance guidelines before incorporation into the HPMS.