Fermilab

DES Lab A LN2 Test

Piping System Engineering Note

| Rev | Date | Description | Originated by | Approved by |
| --- | --- | --- | --- | --- |
| None | Aug 11, 2008 | Original issue | T. Tope H. Cease |  |

Reviewed by: ________________________

Date:  ______________________________

DES Lab A LN2 Test

Piping System Engineering Note

Table of Contents

1.0	Introduction	3

2.0	Flow schematic	3

3.0	Design codes and evaluation criteria	5

4.0	Materials	5

5.0	Piping design and analysis	5

6.0	Pressure relief system	17

7.0	Welding and inspection	17

8.0	Pressure testing	17

9.0	Appendix	17

DES Lab A LN2 Test

Piping System Engineering Note

- Introduction

This document constitutes the Piping System Engineering Note for the cryogenic piping associated with the DES Lab A LN2 test.

The pipe descriptions and a table summary of the operating parameters are shown in Table 1.1.

| Table 1.1: Cryogenic piping description and summary |
| --- |
| Description | Fluid | OD (in) | ID (in) | Poperating (psid) | Pmax (psid) | Temp (K) |
| U-tube LN2 piping 1 in. SCH 40 pipe (vacuum jacketed) | LN2 | 1.315 | 1.049 | 115 | 165 | 100 |
| Drain Line, Fill Trycock Line, and Fill Line for the DES pressure vessel ¾ in. OD tube | LN2 | 0.750 | 0.652 | 100 | 150 | 100 |
| Vent line | GN2 | 0.250 | 0.180 | 100 | 150 | > 100 |
| Cooling Ring ¾ in. SCH 10 pipe | LN2 | 1.050 | 0.884 | 100 | 150 | 100 |
| Cooling Ring ¾ in. OD tube | LN2 | 0.7500 | 0.666 | 100 | 150 | 100 |
| Valve Box (numerous components) | LN2 | * | ** | 100 | 150 | 100 |

*The largest diameter piece of piping in the valve box is 1 inch pipe.

**The thinnest pipe wall thickness in the valve box is 0.065 inches.

2.0 Flow schematic

The flow schematic for the cryostat is shown in Figure 2.1.  The flow schematic is also available at http://des-docdb.fnal.gov:8080/cgi-bin/ShowDocument?docid=1537 as “Process and Instrument Diagram - ME-436389REVA”.

Figure 2.1: DECAM Lab A LN2 test flow schematic.

A schematic of the piping layout at Lab A is shown in figure 2.2 The 200L vessel, instrument lines, all relief valves, and the valve box are located outside at Lab A. The triple jacket hose is used as a transfer line to the camera heat exchanger which is located inside Lab A under the dome.

Figure 2.2: DECAM Lab A LN2 test piping schematic.

3.0	Design codes and evaluation criteria

The DES Lab A LN2 Test piping must meet all of the requirements of Section 5031.1 of the Fermilab ES&H Manual.  This section states that piping systems containing cryogenic fluids fall under the category of Normal Fluid Service and shall adhere to the requirements of the ASME Process Piping Code B31.3.

4.0 Materials

The piping is fabricated from 304/304L and 316/316L stainless steel tube and pipe.  The allowable stress used in this document is 16,700 psi, which is the lowest value listed for these pipe and tube materials in B31.3 Appendix A.

The LN2 piping will be operated at 100 K.  This is above the minimum temperature listed for 304/316 stainless steel pipe or tube (19 K).  According to Table 323.2.2 of the Code, impact testing is not required for these austenitic stainless steels.   However, Table 323.2.2 does require impact testing of the weld metal and heat affected zone. Except as stated in Table 323.2.2 Note (6) where impact testing is not required when the minimum obtainable Charpy specimen has a width along the notch of less than 2.5 mm (0.098 in).  The 1 inch SCH 40 piping that comprises the inner line of the U-tube assembly has a wall thickness of 0.133 inches and is the only piping in the system with a wall thickness greater than 0.098 in.  See section 7.0 for comments with respect to impact testing.

5.0	Piping design and analysis

A schematic of the piping attached to the vessel is shown in Figure 5.1.  The valve box piping that attaches to the vessel is shown in Figure 5.2.  A flexible vacuum jacketed hose connects the cooling ring shown in Figure 5.3 to the valve box piping.

http://www-admscad.fnal.gov/MSDMain/cgi-bin/TP_PPDifind-web.pl

The minimum thickness of the pipes is evaluated using the procedures in 304.1.2(a) of ASME B31.3.  The minimum tube thickness for seamless or longitudinally welded piping for t<D/6 is given by:

where:	t = wall thickness, (t mfg is the manufacturers minimum wall thickness while t req’d is the thickness required by the above equation)

P = internal design pressure

D = outside diameter (manufacturers nominal value is used)

S = allowable stress from table A-1

E = quality factor from table A-1A or A-1B = 0.8 (worst case)

W = weld joint strength reduction factor = 1

Y = coefficient from Table 304.1.1 = 0.4

Table 5.1 summarizes the results of the wall thickness calculation.

| Table 5.1. Cryogenic piping parameters |
| --- |
| Pipe / Tube | P (psid) | D (in) | S (psi) | E | t req’d (in) | t mfg min (in) | MAWP (psid) |
| U-tube LN2 piping | 165 | 1.315 | 16,700 | 0.8 | 0.007 | 0.116 | 3,037 |
| Drain Line, Fill Trycock Line, and Fill Line for the DES pressure vessel | 150 | 0.750 | 16,700 | 0.8 | 0.004 | 0.044 | 1,645 |
| Vent Line | 150 | 0.250 | 16,700 | 0.8 | 0.001 | 0.0315 | 3,744 |
| Cooling Loop | 150 | 1.050 | 16,700 | 0.8 | 0.006 | 0.0726 | 1,956 |
| Cooling Loop | 150 | 0.750 | 16,700 | 0.8 | 0.004 | 0.0378 | 1,403 |
| Valve box (worst case OD and wall THK) | 150 | 1.315 | 16,700 | 0.8 | 0.007 | 0.065 | 1,375 |

In the above six cases the manufacturer’s minimum wall thickness of the piping is greater than the minimum thickness required by ASME B31.3.

The “unlisted components” installed in the piping system as defined in B31.3 Section 304.7.2 are shown in Table 5.2.

| Table 5.2. Unlisted piping components. |
| --- |
| Component | Source | Pressure rating [psig] | System Design Pressure (psig) | Comment |
| Vacuum jacketed flex hose | Duraflex part # D010TVJAVCR-720 | 150(a) | 150 | ---- |
| Bayonet | PHPK, part # PBA-10 | 150(b) | 150 | ---- |
| See the valve and instrument list for other components. |

(a)    http://des-docdb.fnal.gov:8080/cgi-bin/RetrieveFile?docid=1537&version=6&filename=Fermi_Triple_Jacketed_wgs.pdf

- PHPK literature states that “All bayonets have been computer analyzed to meet the ANSI/ASME B31.3 piping code requirements….”.

The flexibility of the U-tube piping was analyzed using ANSYS.  The model boundary conditions and results are summarized in Figures 5.2 and 5.3.

The thermal shrinkage was taken to be 321 x 10-5 (L/L for 304/316 Stainless (B31.3 Table C-1).  The modulus of elasticity of 304 Stainless was input as 30.3 x 106 psi (B31. Table C-6) along with a Poisson’s Ratio of 0.30 (B31.3 para 319.3.3).

The model is comprised of ANSYS PIPE 16 (straight), and PIPE 18 (elbow) elements in which ANSYS calculates flexibility and stress intensification per B31.1.  The stress intensification factors for B31.3 are the same as for B31.1.

As a check of the FEA model, a simple model consisting of a section of straight pipe was analyzed.  The pipe was anchored at both ends and cooled from room temperature to liquid nitrogen temperature.  The stress reported by the FEA model matched the result obtained by multiplying the unit thermal strain by the modulus of elasticity.

Per B31.3 Appendix P, the operating stress is computed using equation (P17a)

where the axial (Sa), bending (Sb), and torsional (St) stresses are combined and compared to the allowable stress SoA in para. P302.3.5(d) where

.

Sc is the basic allowable stress at the minimum metal temperature expected during the displacement cycle under analysis and Sh is the basic allowable stress at the maximum metal temperature expected during the displacement cycle under analysis.  Both Sc and Sh were taken to be 16,700 psi.  The stress reduction factor f was taken to be 1.0 because this system will see less than 1,000 cycles in its lifetime.

A macro (available in the appendix) was used to retrieve Sa, Sb, and St from ANSYS and then compute the combined stress.  The peak operating stress for the Supply U-tube was found to be 5,280 psi for the cold case (thermal shrinkage + 165 psid) and 295 psi for the warm case (165 psid loading only). The peak operating stress for the Return U-tube was found to be 6,826 psi for the cold case (thermal shrinkage + 165 psid) and 295 psi for the warm case (165 psid loading only).

Thus the operating stress range for both U-tubes is only a few thousand psi and does not exceed the allowable operating stress limit.  These stresses are well below the 16,700 psi limit for the U-tube piping components.

The Fill, Drain, and Trycock lines were also analyzed using an FEA model to investigate the thermal stress.  In the FEA model these lines were modeled as fixed to their respective VCR fittings on the top flange and to a clamp attached to the Unistrut frame (see Figure 5.1).  Figures 5.4 thru 5.6 show the model results.  Application of B31.3 equation P17a resulted in a peak stress of 6,254 psi for the Fill Line, 8,353 psi for the Drain Line, and 7,770 psi for the Fill Trycock line.  Thus the stress in each line due to thermal shrinkage and internal pressure is less than the 16,700 psi allowable.

The Cooling Ring piping bends (Figure 5.3) are analyzed per para. 304.2.1 of the Code.  The minimum required thickness is given by:

where:	t = wall thickness

P = internal design pressure, 150 psid

D = outside diameter, 1.050 in.

S = allowable stress from table A-1, 16,700 psi for 304 S.S.

E = quality factor from table A-1A or A-1B = 0.8 (worst case)

W = weld joint strength reduction factor = 1

Y = coefficient from Table 304.1.1 = 0.4

I = factor for location in pipe bend: intrados, extrados and centerline

The following equations are used to determine I at the three locations:

at the intrados:

at the extrados:

at the centerline:	I = 1.0

R1 = 	bend radius of the tubing, 8.225 in.

The results are as follows:

t(in) for 8.225 in. radius:  at intrados = 0.0061; extrados = 0.0057; centerline = 0.0059 (same as straight tube)

The bent pipe has a minimum wall thickness of 0.0726 inches so this requirement is satisfied.

6.0 Pressure relief system

| Table 6.1: DES Lab A LN2 Test relief settings. |
| --- |
| Circuit | Design pressure | Relief setting | Relief valve ID |
| Drain line | 150 psid | 150 psig | SV-6213 |
| Fill trycock line | 150 psid | 150 psig | SV-6213 |
| Fill line | 150 psid | 150 psig | SV-6200-LN, SV-6213 |
| Return U-tube | 165 psid | 150 psig | SV-6213 |
| Supply U-tube | 165 psid | 150 psig | SV-6213 |

7.0	Welding and inspection

According to B31.3 Section 341, all piping in Normal Fluid Service shall be examined.  All welding was performed by Lenny Harbacek whose stainless steel qualification is included in the Appendix.  Eight butt welds were radiographed and the results are available as an attachement.  The system contains 70 butt welds.

B31.3 requires the welding procedure for austenitic stainless steels to be qualified by impact tests of the weld metal and heat affected zone for wall thicknesses greater than 0.098 inch when used at liquid nitrogen temperatures.  The 1” SCH 40 U-tube piping has a wall thickness of 0.133 inches.  Fermilab does not have a qualified welding procedure for use of austenitic stainless steels at liquid nitrogen temperatures.  However, the stress in this piping is far below the allowable stress.  Low stress reduces the likelihood of brittle failure in the heat affected area.  The ASME pressure vessel code recognizes the suitability of 304/304L & 316/316L for use at liquid nitrogen temperatures.  In Section VIII Division 1, paragraph UHA-51(d)(1) exempts 304/304L and 316/316L from impact testing for both the base metals and the heat affected zones.

8.0	Pressure testing

The piping system will be pressure tested in accordance with Section 5034 of the Fermilab ES&H Manual and 345.5 of the Code.  The test pressure is 110% of the design pressure which is 1.1 x 150 = 165 psig.

9.0 Appendix

Figure A-1:  ANSYS macro used to compute operating stress.

Figure A-2:  Leonard Harbacek’s welding qualification for stainless steel.

# Text boxes

Figure 5.3:  Cooling Ring piping.

150 psi internal pressure applied to piping

Tube anchored to unistrut

Tube anchored to top flange

Thermal shrinkage from 70 oF to -325 oF.

Tube anchored to top flange

Thermal shrinkage from 70 oF to -325 oF.

Drain line

Full trycock

150 psi internal pressure applied to piping

Tube anchored to unistrut

Tube anchored to top flange

Thermal shrinkage from 70 oF to -325 oF.

150 psi internal pressure applied to piping

Fill line

Return U-tube

Tube anchored to unistrut

Von Mises stress - Pa

7,324 psi

Figure 5.2:  Valve box piping (contained in a foam box).

Figure 5.6: Fill trycock FEA model boundary conditions and results.

Von Mises stress - Pa

7,890 psi

Thermal shrinkage from 70 oF to -325 oF.

165 psi internal pressure applied to piping

Thermal shrinkage from 70 oF to -325 oF.

165 psi internal pressure applied to piping

Von Mises stress - Pa

Pipe anchored to vacuum jacket

6,541 psi

Figure 5.3:  Return U-tube FEA model.

Von Mises stress - Pa

Pipe anchored to vacuum jacket

5,120 psi

Figure 5.2:  Supply U-tube FEA model boundary conditions and results.

Supply U-tube

Figure 5.1:  Piping attached to the vessel.

Figure 5.5: Drain line FEA model boundary conditions and results.

Figure 5.4: Fill line FEA model boundary conditions and results.

5,801 psi

Von Mises stress - Pa

Fill, Drain, and Trycock lines attached to Unistrut with clamp