SUBJECT:		RANGE TURNAROUND TIME

PURPOSE:	To standardize procedures for providing Range turnaround information for use in Air Force Range support scheduling decisions.

REFERENCES:	None

ATTACHMENTS:	1.  Range Support request letter from (REDACTED)

2.  Nominal Range Turnaround Matrix (sample)

ANNEXES:		None

1.0	GENERAL

A.	The Range turnaround information is requested by (REDACTED) for the purpose of scheduling or rescheduling Range support for major operations (for example, launches, STS landings, major simulations).  This information is produced and provided by the RTS Senior Supervisor, Operations Support (Scheduling), in coordination with the affected RCO and ISRO, (REDACTED) and (REDACTED).

B.	(REDACTED) will also request Range turnaround information in support of special studies of Range support capabilities.

C.	RTS Operations Control is the sole source of turnaround information.  All requests for turnaround information received by instrumentation/support systems should be respectfully referred to Operations Control through (REDACTED).

D.	Range turnaround information will be produced as soon as possible after receipt of the request; however, accuracy is paramount.

2.0	PROCEDURE

A.	(REDACTED) will request Range turnaround information using the form letter in Attachment 1.

B.	Using a PC and system turnaround times (see Attachment 2) provided by the System Controllers/Managers, (REDACTED) and (REDACTED), a "Timeline" chart will be produced by RTS Scheduling for each turnaround request.  In the event of a conflict between launch operations, an Operations Control supervisor (normally the Senior Supervisor, Operations Support) will consult the appropriate launch support teams (ISRO/RCO), (REDACTED) (Cape Support), and (REDACTED) (Photo Control) to determine if any system changes have occurred since the last matrix update which would allow support of both operations.  If no changes have occurred, the senior supervisor will advise (REDACTED) that the Range cannot support on the requested date and will provide "Timeline" charts showing the next supportable date and the reason for the non-support condition on the date requested.

C.	RTS, (REDACTED), and (REDACTED) Systems Controllers/Managers will provide updated turnaround times for their respective systems as requested by RTS Operations Control or at least every six (6) months.  This information will be provided in a format consistent with Attachment 2 to this ROI.

ATTACHMENT 1

MEMO FOR (REDACTED)								DATE__________

FROM:	(REDACTED)

SUBJECT:	RANGE OPERATIONS SUPPORT ASSESSMENT

1.	Please provide an assessment of RTS support capability for the following operations

scenario:

A.

B.

C.

2.	Please advise the extent of support available or limitations to the above operations

proposals.

3.	If required, coordinate with CSR 4000 to determine the extent of operator work hours requiring a manpower variance.  If a variance approval is required, has approval been obtained?

___________________

(REDACTED)

MEMO FOR (REDACTED)							DATE__________

1.	CSR can support the operations scenario as listed on the dates requested:

Yes____No____.

A.	Reason that support cannot be provided (please provide time line).

B.	Does not violate any personnel constraints__________.

C.	Does violate personnel constraints__________.

D.	(REDACTED) poc and phone number____________________, ___________________

2.	Remarks:

___________________

(REDACTED)

ATTACHMENT 2

NOMINAL RANGE TURNAROUND MATRIX (SAMPLE)

| TYPE | COMM | TIM | TLM | RDR | CMD | CPU | WX | OPT | FCA | LBS (LIGHTS) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| ATLAS/D5 (DASO) | 39 | 10 | 48 | 17 | 17 | 18 | N/A | N/A | N/A | N/A |
| ATLAS/D5 (FCET) | 39 | 10 | 48 | 17 | 17 | 18 | N/A | N/A | N/A | N/A |
| ATLAS/DELTA | 36 | 34 | 44 | 17 | 17 | 18 | 18 | 40 | 19 | 24 |
| ATLS/STS LAUNCH | 46 | 34 | 35 | 17 | 18 | 19 | 21 | 38 | 22 | 24 |
| ATLAS/STS (LANDING) | 36 | 10 | N/A | 14 | N/A | 17 | 24 | 17.5 | 20 | 24 |
| ATLAS/TITAN 4 | 46 | 34 | 48 | 17 | 17 | 18 | 21 | 39 | 22 | 24 |
| DELTA/ATLAS | 36 | 34 | 35 | 17 | 17 | 18 | 21 | 40 | 22 | 24 |
| DELTA/D5 (DASO) | 39 | 10 | 48 | 17 | 17 | 18 | N/A | N/A | N/A | N/A |
| DELTA/D5 (FCET) | 39 | 10 | 48 | 17 | 17 | 18 | N/A | N/A | N/A | N/A |
| DELTA/STS (LAUNCH) | 46 | 10 | 37 | 17 | 18 | 19 | 26 | 38 | 22 | 24 |
| DELTA/STS (LANDING | 36 | 10 | N/A | 14 | N/A | 17 | 19 | 17.5 | 20 | N/A |
| DELTA/TITAN 4 | 46 | 34 | 48 | 17 | 17 | 18 | 21 | 39 | 22 | 24 |
| D5 (SINGLE)/ATLAS | 40 | 10 | 41 | 17 | 17 | 18 | N/A | N/A | N/A | N/A |
| D5 (SINGLE)/DELTA | 40 | 10 | 41 | 17 | 17 | 18 | N/A | N/A | N/A | N/A |
| D5 (SINGLE)/STS (LAUNCH) | 40 | 10 | 38 | 17 | 18 | 18 | N/A | N/A | N/A | N/A |
| D5 (SINGLE)/STS (LANDING) | 36 | 10 | N/A | 14 | N/A | 17 | N/A | N/A | N/A | N/A |
| D5 (SINGLE)/TITAN 4 | 40 | 10 | 48 | 17 | 17 | 18 | N/A | N/A | N/A | N/A |
| D5 (MULTI)/ATLAS | 40 | 10 | 43 | 17 | 17 | 18 | N/A | N/A | N/A | N/A |
| D5 (MULTI)/DELTA | 36 | 10 | 43 | 17 | 17 | 18 | N/A | N/A | N/A | N/A |
| D5 (MULTI)/STS (LAUNCH) | 40 | 10 | 43 | 14 | 18 | 19 | N/A | N/A | N/A | N/A |
| D5 (MULTI)STS (LANDING) | 36 | 10 | N/A | 14 | N/A | 17 | N/A | N/A | N/A | N/A |
| D5 (MULTI)/TITAN 4 | 40 | 10 | 48 | 17 | 17 | 18 | N/A | N/A | N/A | N/A |
| STS (LAUNCH)/ATLAS | 36 | 34 | 38 | 17 | 17 | 21 | 18 | 40.5 | 22 | 24 |
| STS (LAUNCH)/DELTA | 36 | 34 | 40 | 17 | 17 | 21 | 18 | 41.5 | 19 | 24 |
| STS (LAUNCH)/D5 (DASO) | 36 | 10 | 48 | 17 | 17 | 21 | N/A | N/A | N/A | N/A |
| STS (LAUNCH)/D5 (FCET) | 36 | 10 | 48 | 17 | 17 | 21 | NA/ | N/A | N/A | N/A |
| STS (LAUNCH)/TITAN 4 | 40 | 34 | 48 | 17 | 17 | 21 | 18 | 39.5 | 22 | 24 |
| STS(LANDING)/ATLAS | 36 | 10 | N/A | 17 | N/A | 17 | 18 | 21 | 22 | N/A |
| STS (LANDING)/DELTA | 36 | 10 | N/A | 17 | N/A | 17 | 18 | 22 | 19 | N/A |
| STS (LANDING)/D5 (SINGLE) | 36 | 10 | N/A | 17 | N/A | 17 | N/A | N/A | N/A | N/A |
| STS (LANDING)/D5 (MULTI) | 36 | 10 | N/A | 17 | N/A | 17 | N/A | N/A | N/A | N/A |
| STS (LANDING)/TITAN 4 | 36 | 10 | N/A | 17 | N/A | 17 | 18 | 21 | 22 | 0 |
| TITAN 4/ATLAS | 40 | 34 | 48 | 17 | 17 | 26 | 18 | 39 | 22 | 24 |
| TITAN 4/DELTA | 40 | 34 | 48 | 17 | 17 | 26 | 18 | 49 | 19 | 24 |
| TITAN 4/D5 (DASO) | 36 | 10 | 48 | 17 | 17 | 26 | N/A | N/A | N/A | N/A |
| TITAN 4/D5 (FCET) | 36 | 10 | 48 | 17 | 17 | 26 | N/A | N/A | N/A | N/A |
| TITAN 4/STS (LAUNCH) | 46 | 34 | 45 | 17 | 18 | 27 | 24 | 38 | 22 | 24 |
| TITAN 4/STS (LANDING) | 38 | 10 | N/A | 14 | N/A | 25 | 19 | 17.5 | 20 | N/A |

ATTACHMENT 3

This Attachment cancelled.