Table 7

Brookhaven Medical Research Reactor Groundwater Investigation

Geoprobe Well Sample Data

Gross Beta (pCi/L)

| Well Number | Land Surface Elev. (MSL) | Water Table Elev. (MSL) | Approx. Depth to Water (BGS) | Sample Interval (BGS) | Result (pCi/L) | Error (pCi/L) | MDL (pCi/L) |
| --- | --- | --- | --- | --- | --- | --- | --- |
| BMRRGP-01 | 101' | 44' | 57' | 60'-62' | 9.3 | 2.58 | 3.75 |
|  |  |  |  | 64-66' | <3.75 | 2.29 | 3.75 |
|  |  |  |  | 68'-70' | 7.2 | 2.50 | 3.75 |
|  |  |  |  | 76-78' | <3.75 | 2.34 | 3.75 |
| BMRRGP-02 | 100' | 44' | 56' | 60'-62' | <3.75 | 2.33 | 3.75 |
|  |  |  |  | 64'-66' | 20.2 | 2.97 | 3.75 |
|  |  |  |  | 68'-70' | <3.75 | 2.29 | 3.75 |
|  |  |  |  | 76-78' | <3.75 | 2.27 | 3.75 |
| BMRRGP-03 | 101' | 44' | 57' | 60'-62' | 19.4 | 3.12 | 4.17 |
|  |  |  |  | 64'-66' | 10.7 | 2.84 | 4.17 |
|  |  |  |  | 68'-70' | 5 | 2.64 | 4.17 |
|  |  |  |  | 76-78' | 18.1 | 3.08 | 4.17 |
| BMRRGP-04 | 101' | 44' | 57' | 60'-62' | <4.17 | 2.54 | 4.17 |
|  |  |  |  | 64'-66' | <4.17 | 2.41 | 4.17 |
|  |  |  |  | 68'-70' | <4.17 | 2.40 | 4.17 |
|  |  |  |  | 76'-78' | <4.17 | 2.39 | 4.17 |

MSL=Relative to Mean Sea Level   BGS=Below Ground Surface    MDL=Minimum Detection Limit

Table 7

Brookhaven Medical Research Reactor Groundwater Investigation

Geoprobe Well Sample Data

Gross Beta (pCi/L)

| Well Number | Land Surface Elev. (MSL) | Water Table Elev. (MSL) | Approx. Depth to Water (BGS) | Sample Interval (BGS) | Result (pCi/L) | Error (pCi/L) | MDL (pCi/L) |
| --- | --- | --- | --- | --- | --- | --- | --- |
| BMRRGP-05 | 101' | 44' | 57' | 60'-62' | <4.17 | 2.47 | 4.17 |
|  |  |  |  | 64'-66' | 21.7 | 3.19 | 4.17 |
|  |  |  |  | 68'-70' | 6.3 | 2.69 | 4.17 |
|  |  |  |  | 76'-78' | <4.17 | 2.55 | 4.17 |
| BMRRGP-06 | 101' | 44' | 57' | 60'-62' | <4.17 | 2.31 | 4.17 |
|  |  |  |  | 64'-66' | <4.17 | 2.33 | 4.17 |
|  |  |  |  | 68'-70' | <4.17 | 2.43 | 4.17 |
|  |  |  |  | 76'-78' | 12.9 | 2.91 | 4.17 |
| BMRRGP-07 | 101' | 44' | 57' | 60'-62' | <3.75 | 2.23 | 3.75 |
|  |  |  |  | 64'-66' | <3.75 | 2.26 | 3.75 |
|  |  |  |  | 68'-70' | <3.75 | 2.32 | 3.75 |
|  |  |  |  | 76'-78' | 8.7 | 2.56 | 3.75 |
| BMRRGP-08 | 101' | 44' | 57' | 60'-62' | <3.75 | 2.34 | 3.75 |
|  |  |  |  | 64'-66' | 5.6 | 2.43 | 3.75 |
|  |  |  |  | 68'-70' | 13.2 | 2.73 | 3.75 |
|  |  |  |  | 76'-78' | <4.17 | 2.32 | 4.17 |

Table 7

Brookhaven Medical Research Reactor Groundwater Investigation

Geoprobe Well Sample Data

Gross Beta (pCi/L)

| Well Number | Land Surface Elev. (MSL) | Water Table Elev. (MSL) | Approx. Depth to Water (BGS) | Sample Interval (BGS) | Result (pCi/L) | Error (pCi/L) | MDL (pCi/L) |
| --- | --- | --- | --- | --- | --- | --- | --- |
| BMRRGP-09 | 101' | 44' | 57' | 60'-62' | <3.75 | 2.23 | 3.75 |
|  |  |  |  | 64'-66' | 4.2 | 2.38 | 3.75 |
|  |  |  |  | 68'-70' | 4.9 | 2.41 | 3.75 |
|  |  |  |  | 76'-78' | 5.7 | 2.44 | 3.75 |
| BMRRGP-10 | 101' | 44' | 57' | 60'-62' | 6.9 | 2.49 | 3.75 |
|  |  |  |  | 64'-66' | 5.2 | 2.42 | 3.75 |
|  |  |  |  | 68'-70' | <3.75 | 2.32 | 3.75 |
|  |  |  |  | 76'-78' | <3.75 | 2.26 | 3.75 |
| BMRRGP-11 | 101' | 44' | 57' | 60'-62' | 4.93 | 2.29 | 3.52 |
|  |  |  |  | 64'-66' | 16.5 | 2.74 | 3.52 |
|  |  |  |  | 68'-70' | 8.02 | 2.41 | 3.52 |
|  |  |  |  | 76'-78' | 4.68 | 2.27 | 3.52 |
| BMRRGP-12 | 101' | 44' | 57' | 60'-62' | 9.06 | 2.46 | 3.52 |
|  |  |  |  | 64'-66' | 15.7 | 2.71 | 3.52 |
|  |  |  |  | 68'-70' | 20.8 | 2.89 | 3.52 |
|  |  |  |  | 76'-78' | 7.37 | 2.39 | 3.52 |

Table 7

Brookhaven Medical Research Reactor Groundwater Investigation

Geoprobe Well Sample Data

Gross Beta (pCi/L)

| Well Number | Land Surface Elev. (MSL) | Water Table Elev. (MSL) | Approx. Depth to Water (BGS) | Sample Interval (BGS) | Result (pCi/L) | Error (pCi/L) | MDL (pCi/L) |
| --- | --- | --- | --- | --- | --- | --- | --- |
| BMRRGP-13 | 97' | 44' | 53' | 56'-58' | 60 | 4.12 | 3.84 |
|  |  |  |  | 64'-66' | <3.84 | 2.38 | 3.84 |
| BMRRGP-14 | 97' | 44' | 53' | 56'-58' | 16.9 | 2.90 | 3.84 |
|  |  |  |  | 64'-66' | 7.99 | 2.58 | 3.84 |
|  |  |  |  | 72'-74' | 7.7 | 2.57 | 3.84 |
|  |  |  |  | 80'-82' | 12.8 | 2.76 | 3.84 |
|  |  |  |  | 88'-90' | 16 | 2.87 | 3.84 |
|  |  |  |  | 96'-98' | 21.1 | 3.04 | 3.84 |
| BMRRGP-15 | 98' | 44' | 54' | 60'-62' | 5.21 | 2.47 | 3.84 |
|  |  |  |  | 64'-66' | 5.16 | 2.47 | 3.84 |
|  |  |  |  | 72'-74' | <3.84 | 2.41 | 3.84 |
|  |  |  |  | 80'-82' | <3.84 | 2.39 | 3.84 |
|  |  |  |  | 88'-90' | <3.84 | 2.21 | 3.84 |

Table 7

Brookhaven Medical Research Reactor Groundwater Investigation

Geoprobe Well Sample Data

Gross Beta (pCi/L)

| Well Number | Land Surface Elev. (MSL) | Water Table Elev. (MSL) | Approx. Depth to Water (BGS) | Sample Interval (BGS) | Result (pCi/L) | Error (pCi/L) | MDL (pCi/L) |
| --- | --- | --- | --- | --- | --- | --- | --- |
| BMRRGP-16 | 98' | 44' | 54' | 60'-62' | <3.84 | 2.36 | 3.84 |
|  |  |  |  | 64'-66' | <3.84 | 2.41 | 3.84 |
|  |  |  |  | 72'-74' | <3.84 | 2.39 | 3.84 |
|  |  |  |  | 80'-82' | <3.84 | 2.32 | 3.84 |
|  |  |  |  | 88'-90' | <3.84 | 2.29 | 3.84 |
|  |  |  |  | 96'-98' | 4.22 | 2.43 | 3.84 |
| BMRRGP-17 | 97' | 44' | 53' | 60'-62' | 7.55 | 2.56 | 3.84 |
|  |  |  |  | 64'-66' | 12.6 | 2.75 | 3.84 |
|  |  |  |  | 72'-74' | 15.9 | 2.87 | 3.84 |
|  |  |  |  | 80'-82' | 26.8 | 3.22 | 3.84 |
|  |  |  |  | 88'90' | 14 | 2.80 | 3.84 |
| BMRRGP-18 | 96' | 44' | 52' | 60'-62' | 7.55 | 2.56 | 3.84 |
|  |  |  |  | 64'-66' | 6.6 | 2.53 | 3.84 |
|  |  |  |  | 72'-74' | 15.7 | 2.86 | 3.84 |
|  |  |  |  | 80'-82' | 4.57 | 2.44 | 3.84 |
|  |  |  |  | 88'-90' | <3.84 | 2.38 | 3.84 |
|  |  |  |  | 96'-98' | 4.37 | 2.44 | 3.84 |

Table 7

Brookhaven Medical Research Reactor Groundwater Investigation

Geoprobe Well Sample Data

Gross Beta (pCi/L)

| Well Number | Land Surface Elev. (MSL) | Water Table Elev. (MSL) | Approx. Depth to Water (BGS) | Sample Interval (BGS) | Result (pCi/L) | Error (pCi/L) | MDL (pCi/L) |
| --- | --- | --- | --- | --- | --- | --- | --- |
| BMRRGP-19 | 95' | 44' | 51' | 56'-58' | <3.52 | 2.19 | 3.52 |
|  |  |  |  | 64'-66' | <3.52 | 2.20 | 3.52 |
|  |  |  |  | 72'-74' | 5.13 | 2.29 | 3.52 |
|  |  |  |  | 80'-82' | 3.73 | 2.23 | 3.52 |
|  |  |  |  | 88'-90' | 3.73 | 2.23 | 3.52 |
| BMRRGP-20 | 101' | 44' | 57' | 60'-62' | 6.11 | 2.45 | 3.74 |
|  |  |  |  | 64'-66' | 6.91 | 2.48 | 3.74 |
|  |  |  |  | 68'-70' | 5.07 | 2.41 | 3.74 |
| BMRRGP-21 | 101' | 44' | 57' | 60'-62' | 47.2 | 3.74 | 1.43 |
|  |  |  |  | 64'-66' | 3.62 | 2.31 | 1.43 |
|  |  |  |  | 68'-70' | 3.02 | 2.29 | 1.43 |
| BMRRGP-22 | 101' | 44' | 57' | 60'-62' | 7.65 | 2.51 | 1.52 |
|  |  |  |  | 64'-66' | 16.0 | 2.82 | 1.52 |
|  |  |  |  | 68'-70' | 7.70 | 2.51 | 1.52 |

Table 7

Brookhaven Medical Research Reactor Groundwater Investigation

Geoprobe Well Sample Data

Gross Beta (pCi/L)

| Well Number | Land Surface Elev. (MSL) | Water Table Elev. (MSL) | Approx. Depth to Water (BGS) | Sample Interval (BGS) | Result (pCi/L) | Error (pCi/L) | MDL (pCi/L) |
| --- | --- | --- | --- | --- | --- | --- | --- |
| BMRRGP-23 | 101' | 44' | 57' | 60'-62' | 11.6 | 2.64 | 3.68 |
|  |  |  |  | 64'-66' | 6.69 | 2.44 | 3.68 |
|  |  |  |  | 68'-70' | 5.35 | 2.39 | 3.68 |
| BMRRGP-24 | 101' | 44' | 57' | 60'-62' | 8.47 | 2.51 | 3.68 |
|  |  |  |  | 64'-66' | 5.05 | 2.37 | 3.68 |
|  |  |  |  | 68'-70' | 8.72 | 2.52 | 3.68 |
| BMRRGP-25 | 101' | 44' | 57' | 60'-62' | 6.86 | 2.48 | 3.74 |
|  |  |  |  | 64'-66' | 6.71 | 2.47 | 3.74 |
|  |  |  |  | 68'-70' | 7.95 | 2.52 | 3.74 |