TCAS II V7 CHANGE PROPOSAL SUMMARY

| CP No. | Original File / Date | Status | Author | Section to Mod | Resolution Found in | Summary Description |
| --- | --- | --- | --- | --- | --- | --- |
| 01 | 12/03/97 | Approved 2/19/98 | K. Wilson /AS | Pcode | Addendum 1 | ITF.RZ is not calculated properly for 5s targets in Traffic Advisory & Detection logic. |
| 02 | 12/03/97 | Transferred 2/19/98 | L. Nivert /FAA |
| SC-186 / WG4 | Evaluate the effect of reducing tau thresholds by 5s; run simulations without pilot delay. |
| 03 | RUYCP01 11/26/97 | Approved 5/28/98 | R. Brandao /AS | Vol. I P34-35 | Addendum 1 | Military formations of TCAS aircraft may greatly reduce TCAS’s surveillance range at high altitude due to interference limiting. |
| 04 | 10/21/97 | Approved 2/19/98 | K. Wilson /AS | Vol. I | RTCA / DO-185A | Typographical errors |
| 05 | COL_CP01 11/26/97 | Approved 2/19/98 | A. Reinholtz /RC | Vol. I P189, 361 | Addendum 1 | GPWS & Windshear system interaction with TCAS TA function needs clarification. Section 2.2.7.2.5.4 |
| 06 | TCR_CP01 12/04/97 | Approved 2/19/98 | B. Abdul-Baki | CRS | Addendum 1 | Editorial errors in CRS functions. |
| 07 | TCR_CP02 12/05/97 | Approved 2/19/98 | E. Meadors /TASC | Vol. I | RTCA / DO-185A | Editorial errors in Volume I, Table 2-62 |
| 08 | TCR_CP03 12/05/97 | Approved 2/19/98 | E. Meadors /TASC | Vol. I | RTCA / DO-185A | Editorial change is needed to incorporate an unambiguous method by which CRS Test Suite results can be compared with manufacturer test results. |
| 09 / 18 | TCR_CP04 01/06/98 | Approved 2/19/98 | E. Meadors /TASC | Test Suite | Addendum 1 | Test Group 6 Test Scenario 36 in the CAS Test Suite |
| 10 | 01/06/98 | Approved 5/11/98 | K. Wilson /AS | Pcode & CRS | Addendum 1 | G.MAINTAIN flag remains set in multiaircraft encounter in which dual negative RA converts to positive Climb RA when one threat is dropped, causing Maintain Rate annunciation instead of Climb. |
| 11 | AS_CP02 01/07/98 | Approved 2/19/98 | K. Wilson /AS | Vol. I p262 | Addendum 1 | Surveillance test 2.4.2.1.6.2a (both scenarios) correction |
| 12 | AS_CP03 01/07/98 | Approved 5/18/98 | K. Wilson /AS | Vol. I p297-300 | Addendum 1 |

Surveillance test 2.4.2.1.8.2b, Scenario B

| AnnD to provide MOPS wording |
| --- |
| 13 | AS_CP04 01/07/98 | Approved 2/19/98 | K. Wilson /AS | Vol. I p244 | Addendum 1 | Surveillance test 2.4.2.1.4.1 correction |
| 14 | AS_CP05 01/07/98 | Approved 2/19/98 | K. Wilson /AS | Vol. I p268-269 | Addendum 1 | Surveillance test 2.4.2.1.6.2d correction |
| 15 | 1/06/98 | Approved 2/19/98 | R. Stead /ARINC | Vol. I p361 | Addendum 1 | Table reference in subpara 2.4.2.2.6 is incorrect. |
| 16 | LL_CP01 01/08/98 | Approved 2/19/98 | R. Sandholm /LL | Vol. I p99 | Addendum 1 | DO-185A, Paragraph 2.2.4.5.4.1.2.e contains a definition of bin-width that is no longer correct. |
| 17 | LL_CP02 01/08/98 | Approved 5/28/98 | R. Sandholm /LL | Vol. I p112 | Addendum 1 | Discrepancy exists between requirement in 2.2.4.6.2.2.3 and test in 2.4.2.1.7.3 re the total number of Mode S interrogation attempts |
| 18 | TCR_CP04 1/6/98 | Rejected 2/19/98 | E. Meadors /TASC |
|  | Duplicate of CP_09 |
| 19 | TCR_CP05 01/08/98 | Approved 2/19/98 | E. Meadors /TASC | Test Suite | Addendum 1 | CAS Test Suite produce values for AltOTHER that fall exactly on a 50 ft. 18 scenarios cited. |
| 20 | TCR_CP06 01/08/98 | Approved 2/19/98 | E. Meadors /TASC | Test Suite | Addendum 1 | CAS Test Suite produce values for AltOTHER that fall exactly on a 50 ft |
| 21 | TCR_CP07 01/19/98 | Approved 2/19/98 | M.Rubinstein /CRC | Vol. I (C-17) & Test Suite | Addendum 1 | The example C code for generating the comparison file in Appendix C of Volume I should require that “n.useAlphaBeta” is false before outputting the n.resid |
| 22 | TCR_CP08 01/19/98 | Approved 2/19/98 | M.Rubinstein /CRC | CRS | Addendum 1 | Change the Trigger Event for the transitions of the state HMD_Test_Counter |
| 23 | HW_CP01 01/21/98 | Approved 5/18/98 | K. Ybarra /HW | Vol. I p106 | Addendum 1 | Provide means for declaring TCAS aircraft airborne even if VS field says otherwise, by using RI field as discriminant. Allow for surveillance on a TCAS threat with an RI field indicating RA-capable even if VS says that the aircraft is on the ground |
| 24 | AS_CP06 02/03/98 | Approved 2/19/98 | K. Wilson /AS | Vol. I p339 | Addendum 1 | Surveillance test 2.4.2.2.4.2.1 Scenario A timing |
| 25 | AS_CP07 02/03/98 | Approved 2/19/98 | K. Wilson /AS | Vol. I p294 | Addendum 1 | Surveillance test 2.4.2.1.7.6 |
| 26 | AS_CP08 02/03/98 | Approved 2/19/98 | K. Wilson /AS | Vol. I p280 | Addendum 1 | Surveillance test 2.4.2.1.7.2 |
| 27 | AS_CP09 02/03/98 | Approved 2/19/98 | K. Wilson /AS | Test Suite | Addendum 1 | Timing of the Mode S Ground Station messages in the CAS Logic Test Suite |
| 28 | AS_CP10 02/05/98 | Rejected 5/11/98 | K. Wilson /AS |
|  | The bit definition (coding) for TIDA in Volume I, section 2.2.3.9.3.2.3, for “D1”. |
| 29 | AS_CP11 02/05/98 | Rejected 5/11/98 | K. Wilson /AS |
|  | The bit definition (coding) for CAC in Volume I, section 2.2.3.9.3.2.4, for “D1”. |
| 30 | AS_CP12 02/05/98 | Approved 2/19/98 | K. Wilson /AS | Vol. I p337-338 | Addendum 1 | Surveillance test 2.4.2.2.4.1, Scenario B |
| 31 | AS_CP13 02/05/98 | Approved 2/19/98 | K. Wilson /AS | Vol. I p359 | Addendum 1 | Surveillance test 2.4.2.2.5, clarification |
| 32 | 02/05/98 | Approved 5/18/98 | T.Berkey / AS-FTL | Vol. I p271-272, 274 | Addendum 1 |

To avoid multipath in tests 2.4.2.1.6.4 and	2.4.2.1.6.5, the intruder altitudes should be staggered by at least 300 ft.

| KevinW to provide MOPS wording |
| --- |
| 33 | 02/05/98 | Approved 5/18/98 | T.Berkey / AS-FTL | Vol. I p220 | Addendum 1 |

Same as CP 32 for test 2.4.2.1.1.3.2, and modify range of intruder 1 to force garbling.

| KevinW to provide MOPS wording |
| --- |
| 34 | AS_CP16 02/10/98 | Approved 2/19/98 | K. Wilson /AS | Vol. I p362 | Addendum 1 | In test 2.4.2.2.6, scenario K, other traffic should also be required to be displayed. |
| 35 | COL_CP02 02/05/98 | Approved 5/11/98 | A. Reinholtz /RC | Vol. I (p77), CRS & Pcode | Addendum 1 | 5 issues related to “RAI” and “RAT” fields |
| 36 | 02/05/98 | Approved 2/19/98 | K.Ybarra /HW | Vol. I p90 | Addendum 1 | Change sentence containing Table 2-11 in MOPS Vol. I to allow acceptance of Mode S FRUIT having 25 ft alt. Data. |
| 37 | 02/11/98 | Approved 2/19/98 | M.Rubinstein /CRC | Vol. I (p314, C16) & Test Suite | Addendum 1 | Ten encounter scenarios end (track is dropped) prior to test end. Data on the intruder should not be provided after the track is dropped. |
| 38 | 02/11/98 | Approved 2/19/98 | M.Rubinstein /CRC | Test Suite | Addendum 1 | Change initial altitude for Scenario 4 in test group 8 to avoid issues concerning rounding at bin boundaries. |
| 39 | 02/11/98 | Approved 2/19/98 | M.Rubinstein /CRC | Test Suite | Addendum 1 | Change resolution message time for Scenario 12 in test group 5 to show that the message arrives prior to the cycle in which it is used. |
| 40 | 02/13/98 | Approved 2/19/98 | M.Rubinstein /CRC | Test Suite | Addendum 1 | In the CRS test scenarios, explicitly specify the HSB bits in encounters that have a non-zero HRC or a non-zero CHC in the resolution message. |
| 41 | 02/17/98 | Approved 2/19/98 | D.Lubkowski /MITRE | Pcode | Addendum 1 | The first IF clause in the high-level pseudocode for PROCESS Reversal_Proj_Check is incomplete |
| 42 | LL_CP03 02/11/98 | Approved 2/19/98 | A.Drumm /LL | Vol. I p77 | Addendum 1 | Clarify requirements for broadcast interrogations. |
| 43 | LL_CP04 02/11/98 | Approved 5/11/98 | A.Drumm /LL | Vol. I p332 | Addendum 1 | Define a generic Mode S sensor interrogation to explain certain surveillance tests. |
| 44 | LL_CP05 02/17/98 | Transferred 2/19/98 | A.Drumm /LL |
| DO-181A / Mode-S MOPS | What is expected of a transponder when it receives a RA Broadcast Interrogation? It should only pass to TCAS those messages addressed to it. |
| 45 | LL_CP06 02/17/98 | Approved 2/19/98 | A.Drumm /LL | Vol. I p20,57,58 | Addendum 1 | Provide a reference for the definition of Mode-S subfields. |
| 46 | MTR_CP46 03/06/98 | Approved 5/11/98 | B. Buresh / RC | Pcode | Addendum 1 | The Vertical Rate to Display for an RA needs to be cleared when the RA is removed. |
| 47 | CP_47 02/26/98 | Approved 5/11/98 | K. Wilson /AS | Vol. I p287-288 | Addendum 1 | Surveillance test 2.4.2.1.7.4.1 |
| 48 | CP_48 03/04/98 | Approved 5/11/98 | M.Rubinstein /CRC | CRS | Addendum 1 | Transitions for the state Reversal, pg 219 |
| 49 | CP_49 03/04/98 | Approved 5/11/98 | M.Rubinstein /CRC | Test Suite | Addendum 1 | Modify scenario 12 in group 5 |
| 50 | CP_50 03/25/98 | Approved 5/11/98 | D.Lubkowski /MITRE | Pcode | Addendum 1 | A non-altitude reporting threat (TA) that is under reduced surveillance (one update every 5 s) becomes a PROX for 4 cycles of every 5 |
| 51 | HW_CP04 4/26/98 | Approved 5/11/98 | K. Ybarra /HW | CRS | Addendum 1 | Assignment of Own_Alt_Barometric in section 1.2.4 and assorted reference errors |
| 52 | TCR_CP15 4/21/98 | Approved 5/11/98 | E. Meadors /TASC | Vol. I p312, 324 | Addendum 1 | Editorial errors in the CAS Test Procedures section (2.4.2.2) of the MOPS |
| 53 | TCR_CP16 5/4/98 | Approved 5/11/98 | Bassam Abdul-Baki / TASC | CRS | Addendum 1 | Corrections of subscripts in the CRS |
| 54 | AS_CP18 5/11/98 | Approved 7/21/98 | K. Wilson /AS | Pcode 7-p30,31,34,35 | Addendum 1 | All weakening RAs should be annunciated as corrective |
| 55 | CP_55 5/29/98 | Approved 5/29/98 | K. Ybarra /HW | Vol.I p65, 69, 80, 336 | Addendum 1 | All Change 7 TCAS units should transmit the RA Broadcast regardless of the transponder version. |
| 56 | CP_56 6/2/98 | Approved 6/26/98 | Tom Berkey/AS | Vol.I p350 | Addendum 1 | Test 2.4.2.2.4.2.3, change altitude input |
| 57 | CP_57 6/3/98 | Accepted on hold 6/26/98 |

P. Holtzman and

| T. Berkey/AS | Pcode | CP_57 | Clearing of G.INTENT |
| --- | --- | --- | --- |
| 58 | CP_58 6/8/98 | Approved 7/21/98 | Kevin Wilson/AS | Vol.I p308 | Addendum 1 | Need an RF test for requirement 2.2.4.5.4.2.1 in test 2.4.2.1.10.1 |
| 59 | CP_59 6/16/98 | Approved 6/26/98 | Ellen Meadors /TASC | CRS | Addendum 1 | Change some of the descriptions in the CRS. |
| 60 | CP_60 6/16/98 | Approved 6/26/98 | E.Meadors/TASC M.Rubinstein/CRC | CRS | Addendum 1 | Make CRS match the Pcode in multi-aircraft reevaluation of RA |
| 61 | CP_61 6/18/98 | Accepted/Designing 6/26/98 | Kevin Wilson/AS | Vol.I p341-342 | CP_61A | Test 2.4.2.2.4.2.1 Scenario D |
| 62 | CP_62 6/18/98 | Accepted/On Hold 6/26/98 | K. Wilson/AS | Pcode |
| The “Crossing” bit in the ARA field should remain set. |
| 63 | CP_63 6/16/98 | Deferred to next major change 7/21/98 | E.Meadors/TASC M.Rubinstein/CRC | Pcode CRS |

PCP_For_

| CP_63 | Modify the logic to make Pcode match the DO-185A CRS in multi-aircraft reevaluation of RAs. |
| --- | --- |
| 64 | CP_64 6/19/98 | Approved 7/21/98 | A.Drumm/LL K.Wilson/AS | Vol.I p340-341 | Addendum 1 | Test 2.4.2.2.4.2.1 Scenario C |
| 65 | CP_65 6/22/98 | Approved 7/21/98 | E.Meadors/TASC B.Abdul-Baki/Rannoch | CRS | Addendum 1 | Delete Reversal_proj_check from the Pseudocode References for Macro 3.16 Crossing_RA |
| 66 | CP_66 7/10/98 | Accepted 7/21/98 | Nicolas Jean/CAE D.Lubkowski/MITRE | Pcode | Addendum 1 | Correct an indirect pointer reference in ROUTINE MANUEVER_POSITIVE_SELECTION |
| 67 | HW-cp5 6/9/98 | Approved 7/21/98 | K. Ybarra /HW | Vol.I p51 | Addendum 1 | Table 2-6: reference should be changed from 2.2.2.10.2.2.2 to 2.2.3.10.2.2.2 |
| 68 | HW-Cp6 7/14/98 | Withdrawn 8/28/98 | K. Ybarra /HW |
|  | Investigate the consequences of raising the aural inhibit altitude to 600 ft minimum to preclude TCAS interfering with GPWS aural annunciations |
| 69 | HW_CP7 | Approved 8/3/98 | K. Ybarra /HW | Vol.I p262 | Addendum 1 | 2.4.2.1.6.2 error in the published symbol |
| 70 | LL_CP09 7/23/98 | Approved 8/28/98 | A.Drumm /LL | Vol.I | CP_70 | There is a discrepancy between the TCAS MOPS and the Mode S Transponder MOPS regarding the way that the transponder reports TCAS capability changes to Mode S ground sensors. |
| 71 | LL_CP10 8/4/98 | Approved 8/28/98 | E.Glowacki/WJHTC R. Sandholm /LL | Vol.I | Ann’s 11/2 email | Require that an image track be evaluated each second to see if reclassification as a real track is warranted |
| 72 | LL_CP11 7/31/98 | Approved 8/28/98 |

A.Drumm /LL

| A. Reinholtz /RC | Vol.I | CP_72 | Test 2.4.2.1.6.2 d |
| --- | --- | --- | --- |
| 73 | LL_CP12 7/31/98 | Accepted / On Hold 8/28/98 | A.Drumm /LL | Pcode |

PCP_For_

| CP_73 | Evaluate the design and safety implications of delays in issuing an RA on pop-up threats |
| --- | --- |
| 74 | LL_CP13 8/4/98 | Accepted / On Hold 8/28/98 | A.Drumm /LL | Vol.I |
| Dynamically determine when aggressive re–interrogation is appropriate including section 2.2.4.6.2.2.2 on Acquisition |
| 75 | AS_CP24 8/3/98 | Approved 8/28/98 | K. Wilson/AS | Vol.I | CP_75 | Test 2.4.2.2.4.1 scenarios A and B |
| 76 | 8/6/98 | Approved 8/28/98 | K. Wilson/AS | Vol.I | CP_76 | Table 2-16 has two mistakes in the “Combined Control” column. |
| 77 | AS_CP26 8/13/98 | Approved 8/28/98 | K. Wilson/AS | Vol.I | CP_77 | Test 2.4.2.2.4.2.1, Scenario E has errors in the expected output of the ARA field. |
| 78 | AS_CP27 8/13/98 | Accepted / On Hold 8/28/98 | K. Wilson/AS | Pcode |
| The “reversal” bit should remain set during the entirety of a “Reversal” RA. |
| 79 | HW_08 8/24/98 | Approved 8/28/98 | K. Ybarra / HW | Test Coverage Matricies |
| Transistion counts given in coverage matricies for some states does not match the actual number given in the CRS. |
| 80 | TCR_CP20 8/3/98 | Approved 8/28/98 | E. Meadors /TASC | CRS |
| Some descriptions in the CRS are missing pcode references. |
| 81 | TCR_CP21 8/24/98 | Approved 9/10/98 | M. Rubinstein / CRC | CRS |
| Three identified differences between the pcode and CRS. |
| 82 | TCR_CP22 8/28/98 | Approved 9/10/98 | E. Meadors /TASC | CRS |
| CP06 item (f) was never implemented. |
| 83 | CP_83 8/28/98 | Accepted / Testing 8/28/98 | A. Drumm /LL | CRS / Pcode / Coord. |

PCP_For_

| CP_83 | Test 2.4.2.2.4.2.2b will not pass at present. |
| --- | --- |
| 84 | TCR_CP23 9/11/98 | Approved 9/14/98 | B. Abdul-Baki / Rannoch | CRS |
| Two changes in CRS, one in the RAT abbreviation, and the second on page xiii Non_tracking should be Not_Tracking. |
| 85 | AS_CP28 10/08/98 | Accepted 10/09/98 | K. Wilson / AS | Pcode |
| The TIDR field in RA reports innaccurately states that zero (0) indicates “no range estimate is available”, which is not possible when an RA is declared on an intruder. |
| 86 | AS_CP29 10/08/98 | Accepted 10/09/98 | K. Wilson / AS | Vol. I | CP_86 | Errors in expected output for test 2.4.2.2.4.2.1 Scenario H. |
| 87 | AS_CP30 10/08/98 | Accepted 10/09/98 | K. Wilson / AS | Vol. I | CP_87 | Success criteria for test 2.4.2.1.7.2 Intuder 1 should not rely on an RA being generated at a specific time. |
| 88 | AS_CP31 10/08/98 | Accepted 10/09/98 | K. Wilson / AS | Vol. I | CP_88 | The success criterea for test 2.4.2.1.9.1 is incorrect. (wrong comparision signs) |
| 89 | D&C_CP2 10/14/98 | Accepted 10/16/98 | R. Stead / ARINC | Vol. I | CP_89 | Delete the word “only” from the second sentence of 2.2.6.1.2.1.2. |
| 90 | COL_CP04 10/15/98 | Approved 11/02/98 | A. Reinholz / RC | Pcode | PCP_For_CP_90 | RA’s were observed to NOT change sense in a slow closure rate encounter after altitudes crossed during flight tests. |
| 91 | AS_CP32 10/27/98 | Accepted 11/02/98 | K. Wilson / AS | Pcode | PCP_For_CP_91 | G.NCYCLE is not cleared on last cycle of RA in Process Broadcast. |
| 92 | TCR_CP24 10/14/98 | Approved 11/02/98 | B. Abdul-Baki / Rannoch | CRS | CP_92 | Two-way mapping between the CRS and pseudocode for CPs 1-82 identified some errors in Pcode references in the CRS. |

CRS_CP##.doc  :  CAS Requirements Specification (CRS) Change Proposal

PCP_CP##.doc  : pseudocode Change Proposal