United States of America

DRAFT PROPOSAL FOR THE WORK OF THE CONFERENCE

Agenda Item 1.29b: to consider the results of studies related to Resolutions 138 (WRC-2000) and 78 (WRC-2000) dealing with sharing between non-GSO and GSO systems;

Background Information:  WRC-2000 adopted a combination of single-entry validation, operational and, for 3 and 10 meter antennas in the 10.7-12.75 GHz band, single-entry additional operational epfd( limits contained in Article 22, along with the aggregate epfd( limits in Resolution 76 (WRC-2000), which apply to non-GSO FSS systems to protect GSO networks in the bands 10.7-12.75 GHz, 17.8-18.6 GHz, and 19.7-20.2 GHz.  The operational epfd( limits were adopted to protect operational GSO FSS networks from interference levels that may result in loss of synchronization, or loss of capacity, or severe degradation in performance.  Resolution 78 (WRC-2000), Development of procedures in case the operational or additional operational limits in Article 22 are exceeded, invites the ITU-R to undertake the appropriate regulatory studies to develop procedures in cases where the operational or additional operational epfd( limits are exceeded at an operational GSO earth station.  Compliance with the operational epfd( and additional operational epfd( limits is not subject to verification by the ITU-BR but by individual administrations.

No. 22.5I stipulates that if a non-GSO FSS system subject to the operational or additional operational epfd( limits contained in Section II of Article 22 at an operational receiving earth station within a GSO network operating in accordance with the Radio Regulations, exceeds these limits then it is a violation of No. 22.2 except as otherwise agreed between concerned administrations.  Article 15 (section V) of the Radio Regulations contains the regulatory procedures to address infringements, which can be applied without modification when non-GSO FSS systems exceed the operational or additional operational epfd( limits given in Tables 22-4A, 22-4A1, 22-4B and 22-4C.  Thus, the U.S. supports the intent of Method A1 for satisfying this agenda item (see Section 3.2.2 of the Draft Conference Preparatory Meeting Report) to apply the existing provisions in Article 15.  Modification of No. 22.5I is also proposed in order to point Administrations toward the procedures for resolving this case of interference.  This is a slight revision of Method A1, which specified no change to either Article 15 or Article 22.

Proposal:

USA/  /1			NOC

ARTICLE  15

Interferences

Reasons:  The current procedures in Article 15 are adequate.

ARTICLE  22

Space services

USA/  /2			MOD

22.5I				6)	An administration operating a non-geostationary-satellite system in the fixed-satellite service which is in compliance with the limits in Nos. 22.5C, 22.5D and 22.5F shall be considered as having fulfilled its obligations under No. 22.2 with respect to any geostationary-satellite network, irrespective of the dates of receipt by the Bureau of the complete coordination or notification information, as appropriate, for the non-geostationary-satellite system and the geostationary-satellite network, provided that the epfd( radiated by the non-geostationary-satellite system in the fixed-satellite service into any operating geostationary fixed-satellite service earth station does not exceed the operational and additional operational limits given in Tables 22-4A, 22-4A1, 22-4B and 22-4C, when the diameter of the earth station antenna is equal to the values given in Table 22-4A, 22-4A1 or 22-4C, or the gain of the earth station is equal to or greater than the values given in Table 22-4B for the corresponding orbital inclination of the geostationary fixed-satellite service satellite. Except as otherwise agreed between concerned administrations, an administration operating a non-geostationary-satellite system in the fixed-satellite service that is subject to the limits in Nos. 22.5C, 22.5D and 22.5F and which radiates epfd( into any operating geostationary fixed-satellite service earth station at levels in excess of the operational or additional operational limits given in Tables 22-4A, 22-4A1, 22-4B and 22-4C, when the diameter of the earth station antenna is equal to the values given in Table 22-4A, 22-4A1 or 22-4C, or the gain of the earth station is equal to or greater than the values given in Table 22-4B for the corresponding orbital inclination of the geostationary fixed-satellite service satellite, shall be considered to be in violation of its obligations under No. 22.2 and the provisions of Article 15 (section V) apply.		 (Rev. WRC-032000)

Reasons:  Article 15 of the Radio Regulations contain provisions that apply when non-GSO systems exceed the operational or additional operational epfd( limits contained in No. 22.5I.  In order to direct administrations toward the procedures for addressing infringements, it is helpful to refer administrations to Article 15 (section V) in No. 22.5I.

USA/  /3			SUP

RESOLUTION  78  (WRC-2000)

Development of procedures in case the operational or additional
operational limits in Article 22 are exceeded

Reasons:  No further studies are needed to develop specific procedures in case the operational or additional operational limits in Article 22 are exceeded.