<@37>Cowarts Series

<@33><i>Depth class:<p> Very deep

<@33><i>Drainage class:<p> Well drained and moderately well drained

<@33><i>Permeability:<p> Moderately slow or slow

<@33><i>Parent material:<p> Loamy marine sediments

<@33><i>Landscape:<p> Coastal Plain

<@33><i>Landform:<p> Uplands

<@33><i>Landform position:<p> Narrow ridges; side slopes

<@33><i>Slope:<p> 2 to 25 percent

<@33><i>Taxonomic class:<p> Fine-loamy, kaolinitic, thermic Typic Kanhapludults

<@27>Commonly Associated Soils

<@30>Ailey, Bibb, Carnegie, Kinston, Lakeland, Lucy, Maubila, Nankin, Ocilla, and Troup soils are commonly associated with the Cowarts series.

<@49>The Ailey soils are in positions similar to those of the Cowarts soils and have sandy surface and subsurface layers with a combined thickness of 20 to 40 inches over dense, brittle layers.

<@29>The Bibb soils are on flood plains, have a coarse-loamy control section, and are poorly drained.

<@29>The Carnegie soils are in positions similar to those of the Cowarts soils or slightly higher, have a fine control section, and have more than 5 percent plinthite, by volume.

<@29>The Kinston soils are on flood plains and are poorly drained.

<@29>The Lakeland soils are in the higher positions, are excessively drained, and are sandy throughout.

<@29>The Lucy soils are in positions similar to those of the Cowarts soils or slightly higher and have sandy surface and subsurface layers with a combined thickness of 20 to 40 inches.

<@29>The Maubila soils are in positions similar to those of the Cowarts soils or higher, are moderately well drained, and have a fine control section.

<@29>The Nankin soils are in positions similar to those of the Cowarts soils, have a solum that is less than 60 inches thick, and have a fine control section.

<@29>The Ocilla soils are adjacent to the Cowarts soils in lower positions, have sandy surface and subsurface layers with a combined thickness of 20 to 40 inches, and are somewhat poorly drained.

<@29>The Troup soils are in the higher positions, are somewhat excessively drained, and have surface and subsurface layers with a combined thickness of 40 to 80 inches.

<@27>Typical Pedon

<@30>Cowarts loamy sand in an area of Nankin-Cowarts complex, 15 to 35 percent slopes; about 0.6 mile north of Sharon Church, 2,960 feet south of the Stewart County line, and 3,200 feet west of County Road 28; Randolph County, Georgia; USGS Sanford topographic quadrangle; lat. 31 degrees 54 minutes 58 seconds N. and long. 84 degrees 53 minutes 30 seconds W., NAD27.

<@23>Ap1—0 to 3 inches; dark grayish brown (10YR 4/2) loamy sand; weak fine granular structure; very friable; many fine and medium roots; strongly acid; clear smooth boundary.

<@33>Ap2—3 to 7 inches; brown (10YR 4/3) loamy sand; weak fine granular structure; very friable; many fine and medium roots; strongly acid; clear wavy boundary.

<@33>Bt1—7 to 15 inches; yellowish brown (10YR 5/6) sandy loam; weak coarse subangular blocky structure; very friable; many fine and medium roots; sand grains coated and bridged with clay; strongly acid; gradual wavy boundary.

<@33>Bt2—15 to 22 inches; brownish yellow (10YR 6/8) sandy clay loam; weak medium subangular blocky structure; friable; common fine and medium roots; few distinct clay films on faces of peds; strongly acid; gradual wavy boundary.

<@33>Bt3—22 to 31 inches; brownish yellow (10YR 6/8) sandy clay loam; moderate medium subangular blocky structure; firm; common medium roots and few fine roots; few distinct clay films on faces of peds; common medium distinct yellowish red (5YR 5/8) masses in which iron has accumulated; the masses have sharp boundaries and are within the matrix; strongly acid; gradual wavy boundary.

<@33>BC—31 to 40 inches; brownish yellow (10YR 6/8) sandy clay loam; weak medium subangular blocky structure; friable; few medium roots; few distinct clay films on faces of peds; common medium distinct yellowish red (5YR 5/6) and strong brown (7.5YR 5/6) masses in which iron has accumulated; the masses have sharp boundaries and are within the matrix; strongly acid; gradual wavy boundary.

<@33>C1—40 to 48 inches; brownish yellow (10YR 6/8) sandy loam; weak coarse subangular blocky structure parting to weak fine granular; friable; few fine distinct yellowish red (5YR 5/6) and reddish yellow (5YR 6/6) masses in which iron has accumulated; very strongly acid; gradual wavy boundary.

<@33>C2—48 to 59 inches; brownish yellow (10YR 6/6) sandy loam; massive parting to weak thin platy structure; firm, brittle; common thin strata of yellowish red (5YR 5/6) sandy clay loam; few fine distinct pale brown (10YR 6/3) areas from which iron has depleted; very strongly acid; gradual wavy boundary.

<@33>C3—59 to 80 inches; multicolored, about 50 percent brownish yellow (10YR 6/6), 30 percent light yellowish brown (10YR 6/4), and 20 percent yellowish red (5YR 5/6) stratified loamy sand; massive structure parting to loose single grained; firm in place, very friable if disturbed; the areas of brownish yellow and yellowish red are areas in which iron has accumulated; the areas of light yellowish brown are areas from which iron has depleted; very strongly acid.

<@27>Range in Characteristics

<@33><i>Thickness of the solum:<p> 20 to 40 inches

<@33><i>Reaction:<p> Very strongly acid or strongly acid throughout, except where the surface layer has been limed

<@23><i>A or Ap horizon:<p>

<@31>Color—hue of 10YR, value of 4 or 5, and chroma of 2 to 4

<@31>Texture—loamy sand or sandy loam

<@23><i>E horizon (where present):<p>

<@31>Color—hue of 10YR, value of 5 or 6, and chroma of 4 to 6

<@31>Texture—loamy sand or sandy loam

<@23><i>BE horizon (where present):<p>

<@31>Color—hue of 10YR, value of 5 or 6, and chroma of 4 to 8

<@31>Texture—sandy loam

<@23><i>Bt horizon:<p>

<@31>Color—hue of 5YR to 10YR, value of 5 or 6, and chroma of 4 to 8

<@31>Redoximorphic features—no, few, or common iron accumulations in shades of red, yellow, and brown

<@31>Texture—sandy loam or sandy clay loam

<@23><i>BC horizon (where present):<p>

<@31>Color—hue of 2.5YR to 10YR, value of 4 to 6, and chroma of 4 to 8; or multicolored in shades of red, yellow, brown, and gray

<@31>Redoximorphic features—few to many iron or clay depletions in shades of gray and iron accumulations in shades of red, brown, and yellow

<@31>Texture—sandy loam or sandy clay loam

<@23><i>C horizon:<p>

<@31>Color—hue of 2.5YR to 10YR, value of 4 to 6, and chroma of 4 to 8; or multicolored in shades of red, yellow, brown, and gray

<@31>Redoximorphic features—few to many iron or clay depletions in shades of gray and few to many iron accumulations in shades of red, brown, and yellow

<@31>Texture—loamy sand, sandy loam, or sandy clay loam or stratified in these textures