Table 6

Brookhaven Medical Research Reactor Groundwater Investigation

Geoprobe Well Sample Data

Gross Alpha (pCi/L)

| Well Number | Land Surface Elev. (MSL) | Water Table Elev. (MSL) | Approx. Depth to Water (BGS) | Sample Interval (BGS) | Result (pCi/L) | Error (pCi/L) | MDL (pCi/L) |
| --- | --- | --- | --- | --- | --- | --- | --- |
| BMRRGP-01 | 101' | 44' | 57' | 60'-62' | 4.6 | 1.29 | 1.39 |
|  |  |  |  | 64-66' | <1.39 | 0.75 | 1.39 |
|  |  |  |  | 68'-70' | 2.52 | 1.05 | 1.39 |
|  |  |  |  | 76-78' | 1.81 | 0.93 | 1.39 |
| BMRRGP-02 | 100' | 44' | 56' | 60'-62' | <1.39 | 0.80 | 1.39 |
|  |  |  |  | 64'-66' | 17.7 | 2.00 | 1.39 |
|  |  |  |  | 68'-70' | <1.39 | 0.89 | 1.39 |
|  |  |  |  | 76-78' | <1.39 | 0.82 | 1.39 |
| BMRRGP-03 | 101' | 44' | 57' | 60'-62' | <1.45 | 0.96 | 1.45 |
|  |  |  |  | 64'-66' | 1.76 | 0.96 | 1.45 |
|  |  |  |  | 68'-70' | <1.45 | 0.90 | 1.45 |
|  |  |  |  | 76-78' | <1.45 | 0.92 | 1.45 |
| BMRRGP-04 | 101' | 44' | 57' | 60'-62' | <1.45 | 0.87 | 1.45 |
|  |  |  |  | 64'-66' | <1.45 | 0.80 | 1.45 |
|  |  |  |  | 68'-70' | <1.45 | 0.73 | 1.45 |
|  |  |  |  | 76'-78' | 1.58 | 0.96 | 1.45 |

MSL= Relative to Mean Sea Level    BGS=Below Ground Surface    MDL=Minimum Detection Limit

Table 6 (Continued)

Brookhaven Medical Research Reactor Groundwater Investigation

Geoprobe Well Sample Data

Gross Alpha (pCi/L)

| Well Number | Land Surface Elev. (MSL) | Water Table Elev. (MSL) | Approx. Depth to Water (BGS) | Sample Interval (BGS) | Result (pCi/L) | Error (pCi/L) | MDL (pCi/L) |
| --- | --- | --- | --- | --- | --- | --- | --- |
| BMRRGP-05 | 101' | 44' | 57' | 60'-62' | <1.45 | 0.87 | 1.45 |
|  |  |  |  | 64'-66' | 13 | 1.80 | 1.45 |
|  |  |  |  | 68'-70' | 3.05 | 1.11 | 1.45 |
|  |  |  |  | 76'-78' | <1.45 | 0.91 | 1.45 |
| BMRRGP-06 | 101' | 44' | 57' | 60'-62' | <1.45 | 0.92 | 1.45 |
|  |  |  |  | 64'-66' | <1.45 | 0.87 | 1.45 |
|  |  |  |  | 68'-70' | <1.45 | 0.90 | 1.45 |
|  |  |  |  | 76'-78' | 8.78 | 1.57 | 1.45 |
| BMRRGP-07 | 101' | 44' | 57' | 60'-62' | <1.39 | 0.74 | 1.39 |
|  |  |  |  | 64'-66' | <1.39 | 0.79 | 1.39 |
|  |  |  |  | 68'-70' | 1.92 | 0.97 | 1.39 |
|  |  |  |  | 76'-78' | 3.07 | 1.59 | 1.39 |
| BMRRGP-08 | 101' | 44' | 57' | 60'-62' | <1.39 | 0.78 | 1.39 |
|  |  |  |  | 64'-66' | <1.39 | 0.77 | 1.39 |
|  |  |  |  | 68'-70' | 1.87 | 0.97 | 1.39 |
|  |  |  |  | 76'-78' | <1.45 | 0.90 | 1.45 |

Table 6 (Contined)

Brookhaven Medical Research Reactor Groundwater Investigation

Geoprobe Well Sample Data

Gross Alpha (pCi/L)

| Well Number | Land Surface Elev. (MSL) | Water Table Elev. (MSL) | Approx. Depth to Water (BGS) | Sample Interval (BGS) | Result (pCi/L) | Error (pCi/L) | MDL (pCi/L) |
| --- | --- | --- | --- | --- | --- | --- | --- |
| BMRRGP-09 | 101' | 44' | 57' | 60'-62' | <1.39 | 0.80 | 1.39 |
|  |  |  |  | 64'-66' | 1.48 | 0.91 | 1.39 |
|  |  |  |  | 68'-70' | 2.11 | 0.94 | 1.39 |
|  |  |  |  | 76'-78' | 2.21 | 1.03 | 1.39 |
| BMRRGP-10 | 101' | 44' | 57' | 60'-62' | <1.39 | 0.87 | 1.39 |
|  |  |  |  | 64'-66' | 2.52 | 1.01 | 1.39 |
|  |  |  |  | 68'-70' | <1.39 | 0.86 | 1.39 |
|  |  |  |  | 76'-78' | <1.39 | 0.72 | 1.39 |
| BMRRGP-11 | 101' | 44' | 57' | 60'-62' | 1.5 | 0.98 | 1.44 |
|  |  |  |  | 64'-66' | 2.86 | 1.06 | 1.44 |
|  |  |  |  | 68'-70' | 2.7 | 1.05 | 1.44 |
|  |  |  |  | 76'-78' | 2.8 | 1.11 | 1.44 |
| BMRRGP-12 | 101' | 44' | 57' | 60'-62' | 4.72 | 1.30 | 1.44 |
|  |  |  |  | 64'-66' | 8.03 | 1.51 | 1.44 |
|  |  |  |  | 68'-70' | 19.9 | 2.13 | 1.44 |
|  |  |  |  | 76'-78' | 4.78 | 1.27 | 1.44 |

Table 6 (Continued)

Brookhaven Medical Research Reactor Groundwater Investigation

Geoprobe Well Sample Data

Gross Alpha (pCi/L)

| Well Number | Land Surface Elev. (MSL) | Water Table Elev. (MSL) | Approx. Depth to Water (BGS) | Sample Interval (BGS) | Result (pCi/L) | Error (pCi/L) | MDL (pCi/L) |
| --- | --- | --- | --- | --- | --- | --- | --- |
| BMRRGP-13 | 97' | 44' | 53' | 56'-58' | 47.4 | 3.67 | 1.65 |
|  |  |  |  | 64'-66' | <1.65 | 1.09 | 1.65 |
| BMRRGP-14 | 97' | 44' | 53' | 56'-58' | 3.51 | 1.27 | 1.65 |
|  |  |  |  | 64'-66' | 3.8 | 1.31 | 1.65 |
|  |  |  |  | 72'-74' | 5.29 | 1.45 | 1.65 |
|  |  |  |  | 80'-82' | 7.17 | 1.58 | 1.65 |
|  |  |  |  | 88'-90' | 14.8 | 2.04 | 1.65 |
|  |  |  |  | 96'-98' | 16 | 2.17 | 1.65 |
| BMRRGP-15 | 98' | 44' | 54' | 60'-62' | <1.65 | 1.00 | 1.65 |
|  |  |  |  | 64'-66' | <1.65 | 1.05 | 1.65 |
|  |  |  |  | 72'-74' | 2.38 | 1.16 | 1.65 |
|  |  |  |  | 80'-82' | <1.65 | 0.87 | 1.65 |
|  |  |  |  | 88'-90' | <1.65 | 0.84 | 1.65 |

Table 6 (Continued)

Brookhaven Medical Research Reactor Groundwater Investigation

Geoprobe Well Sample Data

Gross Alpha (pCi/L)

| Well Number | Land Surface Elev. (MSL) | Water Table Elev. (MSL) | Approx. Depth to Water (BGS) | Sample Interval (BGS) | Result (pCi/L) | Error (pCi/L) | MDL (pCi/L) |
| --- | --- | --- | --- | --- | --- | --- | --- |
| BMRRGP-16 | 98' | 44' | 54' | 60'-62' | <1.65 | 0.88 | 1.65 |
|  |  |  |  | 64'-66' | <1.65 | 0.87 | 1.65 |
|  |  |  |  | 72'-74' | <1.65 | 0.95 | 1.65 |
|  |  |  |  | 80'-82' | <1.65 | 1.02 | 1.65 |
|  |  |  |  | 88'-90' | <1.65 | 0.93 | 1.65 |
|  |  |  |  | 96'-98' | <1.65 | 0.97 | 1.65 |
| BMRRGP-17 | 97' | 44' | 53' | 60'-62' | 3.3 | 1.27 | 1.65 |
|  |  |  |  | 64'-66' | 6.01 | 1.52 | 1.65 |
|  |  |  |  | 72'-74' | 11.8 | 1.80 | 1.65 |
|  |  |  |  | 80'-82' | 23.3 | 2.38 | 1.65 |
|  |  |  |  | 88'-90' | 10.4 | 1.72 | 1.18 |
| BMRRGP-18 | 96' | 44' | 52' | 60'-62' | 2.5 | 1.18 | 1.65 |
|  |  |  |  | 64'-66' | <1.65 | 1.06 | 1.65 |
|  |  |  |  | 72'-74' | 2.32 | 1.13 | 1.65 |
|  |  |  |  | 80'-82' | 2.13 | 1.10 | 1.65 |
|  |  |  |  | 88'-90' | <1.65 | 1.01 | 1.65 |
|  |  |  |  | 96'-98' | <1.65 | 1.01 | 1.65 |

Table 6 (Continued)

Brookhaven Medical Research Reactor Groundwater Investigation

Geoprobe Well Sample Data

Gross Alpha (pCi/L)

| Well Number | Land Surface Elev. (MSL) | Water Table Elev. (MSL) | Approx. Depth to Water (BGS) | Sample Interval (BGS) | Result (pCi/L) | Error (pCi/L) | MDL (pCi/L) |
| --- | --- | --- | --- | --- | --- | --- | --- |
| BMRRGP-19 | 95' | 44' | 51' | 56'-58' | <1.44 | 0.84 | 1.44 |
|  |  |  |  | 64'-66' | <1.44 | 0.87 | 1.44 |
|  |  |  |  | 72'-74' | 2.06 | 1.00 | 1.44 |
|  |  |  |  | 80'-82' | 2.16 | 1.00 | 1.44 |
|  |  |  |  | 88'-90' | 1.61 | 0.96 | 1.44 |
| BMRRGP-20 | 101' | 44' | 57' | 60'-62' | 3.06 | 1.17 | 1.52 |
|  |  |  |  | 64'-66' | <1.52 | 0.95 | 1.52 |
|  |  |  |  | 68'-70' | <1.52 | 0.89 | 1.52 |
| BMRRGP-21 | 101' | 44' | 57' | 60'-62' | <1.43 | 0.94 | 1.43 |
|  |  |  |  | 64'-66' | 2.06 | 0.98 | 1.43 |
|  |  |  |  | 68'-70' | <1.43 | 0.86 | 1.43 |
| BMRRGP-22 | 101' | 44' | 57' | 60'-62' | 2.11 | 1.07 | 1.52 |
|  |  |  |  | 64'-66' | 4.25 | 1.28 | 1.52 |
|  |  |  |  | 68'-70' | 3.06 | 1.14 | 1.52 |
| BMRRGP-23 | 101' | 44' | 57' | 60'-62' | <1.43 | 0.87 | 1.43 |
|  |  |  |  | 64'-66' | 2.95 | 1.06 | 1.43 |
|  |  |  |  | 68'-70' | 2.84 | 1.06 | 1.43 |

Table 6 (Continued)

Brookhaven Medical Research Reactor Groundwater Investigation

Geoprobe Well Sample Data

Gross Alpha (pCi/L)

| Well Number | Land Surface Elev. (MSL) | Water Table Elev. (MSL) | Approx. Depth to Water (BGS) | Sample Interval (BGS) | Result (pCi/L) | Error (pCi/L) | MDL (pCi/L) |
| --- | --- | --- | --- | --- | --- | --- | --- |
| BMRRGP-24 | 101' | 44' | 57' | 60'-62' | 2.25 | 1.04 | 1.43 |
|  |  |  |  | 64'-66' | 1.88 | 0.97 | 1.43 |
|  |  |  |  | 68'-70' | 2.54 | 1.05 | 1.43 |
| BMRRGP-25 | 101' | 44' | 57' | 60'-62' | <1.52 | 0.83 | 1.52 |
|  |  |  |  | 64'-66' | <1.52 | 0.86 | 1.52 |
|  |  |  |  | 68'-70' | 2.05 | 1.03 | 1.52 |