# PROCESSING IN WATER IN STILL RETORTS

| INSTRUCTIONS COMPLETE THE QUESTION BLOCKS BELOW. EACH BLOCK IS EXPANDABLE TO ACCOMMODATE NARRATION AS NEEDED. DRAW A DIAGRAM OF THE RETORT OR OBTAIN ONE FROM THE FIRM. ATTACH THE DIAGRAM TO THIS SURVEY REPORT. REPORT ALL PIPE SIZES AS INSIDE DIAMETER (ID). CROSS-SECTIONAL AREA = 3.14R² (R = ½ DIAMETER). MAKE A HARD COPY OF THE COMPLETED FORM AND ATTACH TO THE LACF INSPECTION REPORT. |
| --- |
| RETORT DESCRIPTION |
| RETORT NO. | Type of Retort: Vertical [] Horizontal [] | Length or Height | Diameter |
| NUMBER OF BASKETS OR CRATES PER RETORT: |
| FOR VERTICAL RETORTS, BOTTOM CRATE SUPPORTS ARE PRESENT TO PROTECT THE STEAM SPREADER YES [] NO [] (SHALL REQUIREMENT, 113.40(b)(6)) |
| ARE BAFFLE PLATES PRESENT IN THE BOTTOM OF RETORT? YES [] NO [] (BAFFLE PLATES SHALL NOT BE USED, 113.40(b)(6)) |
| ARE VERTICAL RETORTS EQUIPPED WITH CENTERING GUIDES TO PROVIDE A 1.5-INCH CLEARANCE BETWEEN THE SIDE WALLS OF THE RETORT AND THE CRATE? (SHOULD REQUIREMNT – 113.40(b)(6) YES [] NO [] |
| ARE THERE ANY PROTRUSIONS INSIDE THE RETORT OR THE RETORT DOOR CASING WHICH COULD DAMAGE CONTAINERS DURING LOADING/UNLOADING OF CRATES? YES [] NO [] |
| DO THE RETORTS FOLLOW THE ARRANGEMENTS IN THE DIAGRAM FOUND IN 113.40(b)(13)? YES [] NO [] IF NO, DOES THE FIRM HAVE ON HAND HEAT DISTRIBUTION DATA OR OTHER SUITABLE INFORMATION THAT DEMONSTRATES THAT THE HEAT DISTRIBUTION IS ADEQUATE? – SHALL REQUIREMENT OF 13.40(b)(13). |
| COMPUTER CONTROLS |
| DOES A COMPUTER CONTROL ANY OF THE RETORT FUNCTIONS? YES [] NO [] |
| DOES THE FIRM HAVE DOCUMENTATION ON HAND THAT INDICATES THAT THE COMPUTER SYSTEM HAS BEEN VALIDATED? YES [] NO [] EXPLAIN: |
| IS RECORD KEEPING PART OF THE COMPUTER FUNCTION? YES [] NO [] IF YES, DOES THE RECORD KEEPING COMPLY WITH 21CFR PART 11? YES [] NO [] EXPLAIN: |
| MERCURY THERMOMETERS |
| IS THE RETORT EQUIPPED WITH A MIG THERMOMETER YES [] NO [] |
| IS THE RETORT EQUIPPED WITH ANOTHER TYPE OF TEMPERATURE INDICATOR? YES [] NO [] IF YES, DESCRIBE THE TEMPERATURE INDICATOR. |
| ARE SCALE DIVISIONS EASILY READABLE TO 1°F (.5°C)? YES [] NO [] |
| NO. OF DEGREES F OR C/IN. OF GRADUATED SCALE: ____________. (TEMP. RANGE MUST NOT EXCEED 17°F PER INCH (4°C/ CM) OF GRADUATED SCALE – 113.40(A)(1) (SEE LACF GUIDE-PART 2 | DATE LAST TESTED FOR ACCURACY |
| THERMOMETERS SHALL BE TESTED FOR ACCURACY AGAINST A KNOWN ACCURATE STANDARD THERMOMETER UPON INSTALLATION AND AT LEAST ONCE A YEAR THEREAFTER; RECORDS OF ACCURACY CHECKS THAT SPECIFY DATE, STANDARD USED, METHOD USED, AND PERSON PERFORMING THE TEST SHOULD BE MAINTAINED. EACH THERMOMETER SHOULD HAVE A TAG, SEAL, OR OTHER MEANS OF IDENTITY THAT INCLUDES THE DATE IT WAS LAST TESTED FOR ACCURACY – 113.40(a)(1). |
| STANDARD USED FOR THE TEST: |
| NAME AND TITLE OF PERSON WHO PERFORMED TEST: |
| IS THE LAST TEST DATE IDENTIFIED ON THE THERMOMETER? YES [] NO[] |
| DESCRIBE THE FIRM’S ACTIONS REGARDING MIG THERMOMETERS WHICH WERE OUT OF CALIBRATION. |
| IS THE MERCURY UNDIVIDED? YES [] NO [] (A THERMOMETER THAT HAS A DIVIDED MERCURY COLUMN OR THAT CANNOT BE ADJUSTED TO THE STANDARD SHALL BE REPAIRED OR REPLACED (113.40(a)(1)) |
| WHEN MIG THERMOMETERS ARE FOUND TO BE PROVIDING READINGS ABOVE THE ACTUAL TEMPERATURES, DOES THE FIRM EVALUATE PRODUCTS PRODUCED USING THOSE THERMOMETERS? YES [] NO [] DESCRIBE THE FIRM’S PROCEDURES. |
| IS THE THERMOMETER LOCATED WHERE IT IS EASY TO READ ACCURATELY? YES[] NO [] SHALL REQUIREMENT– 113.40(a)(1) |
| IS THE SENSOR BULB POSITIONED SO THAT IT EXTENDS DIRECTLY INTO THE WATER A MINIMUM OF AT LEAST 2 INCHES WITHOUT A SEPARABLE WELL OR SLEEVE AND IS BENEATH THE SURFACE OF THE WATER DURING THE COMPLETE PROCESS? YES [] NO [] SHALL REQUIREMENT – 113.40(b)(1). |
| ON HORIZONTAL RETORTS, IS THE MIG THERMOMETER INSERTED DIRECTLY INTO THE RETORT SHELL IN THE SIDE AT THE CENTER? YES [] NO [] (SHOULD REQUIREMENT – 113.40(b)(1)). EXPLAIN WHERE AND HOW THE MIG IS POSITIONED. |
| IS THE MERCURY THERMOMETER USED AS THE REFERENCED INSTRUMENT DURING PROCESSING? YES [] NO [] (SHALL REQUIREMENT – 113.40(a)(1)) |
| TEMERATURE RECORDER |
| TYPE OF TEMPERATURE RECORDER: ROUND CIRCULAR CHART [] STRIP CHART [] OTHER [] |
| DO THE CHART SPECIFICATIONS MEET THE REQUIREMENTS OF PART 113? YES [] NO [] (GRADUATIONS ON THE TEMPERATURE-RECORDING DEVICE SHALL NOT EXCEED 2°F(1°C) WITHIN A RANGE OF 10°F(5.5°C) OF THE PROCESSING TEMPERATURE. EACH CHART SHALL HAVE A WORKING SCALE OF NOT MORE THAN 55°F/IN.(12°C/CM) WITHIN A RANGE OF 20°F(10°C) OF THE PROCESSING TEMPERATURE – 113.40(b)(2)). |
| IS THE TEMPERATURE CHART ADJUSTED TO AGREE AS NEARLY AS POSSIBLE WITH BUT NOT HIGHER THAN THE KNOWN ACCURATE MERCURY-IN-GLASS THERMOMETER DURING THE PROCESSING PERIOD? YES [] NO [] (SHALL REQUIREMENT OF – 113.40(b)(2)). NOTE ANY DIFFERENCE BETWEEN THE RECORDING THERMOMETER AND THE MERCURY-IN-GLASS THERMOMETER AND WHICH READING IS HIGHER) |
| IS THERE A MEANS FOR PREVENTING UNAUTHORIZED ADJUSTMENTS? YES [] NO [] (A MEANS OF PREVENTING UNAUTHORIZED CHANGES IN ADJUSTMENTS SHALL BE PROVIDED. A LOCK OR NOTICE FROM MANAGEMENT STATING “ONLY AUTHORIZED PERSONS ARE PERMITTED TO MAKE ADJUSTMENTS” & POSTED AT OR NEAR THE RECORDING DEVICE IS A SATISFACTORY MEANS FOR PREVENTING UNAUTHORIZED CHANGES. 113.40(b)(2)) |
| IS THE CHART DRIVE TIMING MECHANISM ACCURATE? YES [] NO [] IF NO, EXPLAIN. |
| IS THE RECORDER COMBINED WITH A STEAM CONTROLLER? YES [] NO [] |
| FOR VERTICAL STILL RETORTS EQUIPPED WITH A TEMPERATURE RECORDING/CONTROLLING DEVICE, IS THE TEMPERATURE SENSOR PROBE LOCATED AT THE BOTTOM OF THE RETORT BELOW THE LOWEST CRATE SUPPORT SO STEAM DOES NOT STRIKE IT DIRECTLY? YES [] NO [] SHALL REQUIREMENT, 113.40(b)2) |
| FOR RETORTS OTHER THAN VERTICAL STILL RETORTS EQUIPPED WITH A RECORDING/CONTROLLING INSTRUMENT, IS THE RECORDING THERMOMETER BULB LOCATED ADJACENT TO THE BULB OF THE MERCURY-IN-GLASS THERMOMETER? YES [] NO [] SHOULD REQUIREMENT, 113.40(b)(2). |
| FOR HORIZONTAL STILL RETORTS EQUIPPED WITH A TEMPERATURE RECORDING/CONTROLLING DEVICE, IS THE TEMPERATURE RECORDING/CONTROLLING BULB LOCATED BETWEEN THE WATER SURFACE AND THE HORIZONTAL PLAN PASSING THROUGH THE CENTER OF THE RETORT SO THERE IS NO DIRECT STEAM IMPINGEMENT ON THE CONTROL BULB? YES [] NO [] SHALL REQUIREMENT, 113.40(b)(2) |
| PRESSURE GAGE |
| IF A PRESSURE GAGE IS PRESENT, IS IT GRADUATED IN DIVISIONS OF 2 LBS. OR LESS? YES [] NO [] NOTE – THIS IS A RECOMMENDATION “SHOULD” REQUIREMENT OF THE REGULATIONS. |
| PRESSURE RELIEF VALVE |
| IS THE RETORT EQUIPPED WITH AN ADJUSTABLE PRESSURE RELIEF OR CONTROL VALVE INSTALLED IN THE OVERFLOW LINE? YES [] NO [] SHOULD REQUIREMENT, 113.40(b)(3) |
| AUTOMATIC STEAM CONTROLLER |
| IS THE STEAM CONTROLLER AUTOMATIC? YES [] NO [] EACH RETORT SHALL BE EQUIPPED WITH AN AUTOMATIC STEAM CONTROLLER TO MAINTAIN THE RETORT TEMPERATURE (113.40(a)(4)). |
| IS THE CONTROLLER COMBINED WITH A TEMPERATURE RECORDER TO FUNCTION AS A RECORDING/CONTROLLING INSTRUMENT? YES [] NO [] |
| IF THE TEMPERATURE (STEAM) CONTROLLER IS AIR OPERATED, DOES THE SYSTEM HAVE AN ADEQUATE FILTER TO ASSURE A SUPPLY OF CLEAN, DRY AIR? YES [] NO [] (AIR OPERATED TEMPERATURE CONTROLLERS SHOULD HAVE ADEQUATE FILTER SYSTEMS TO ASSURE A SUPPLY OF CLEAN, DRY AIR, 113.40(a)(2)). |
| REPORT THE MANUFACTURER, SIZE, MODEL AND TYPE OF AUTOMATIC STEAM CONTROL VALVE: |
| STEAM INTRODUCTION |
| IS STEAM DISTRIBUTED IN THE BOTTOM OF THE RETORT? YES [] NO [] (STEAM SHALL BE DISTRIBUTED IN THE BOTTOM OF THE RETORT IN A MANNER ADEQUATE TO PROVIDE UNIFORM HEAT DISTRIBUTION THROUGHOUT THE RETORT – 113.40(b)(5)) |
| FOR HORIZONTAL STILL RETORTS, IS THERE A STEAM DISTRIBUTION PIPE THAT RUNS THE LENGTH OF THE BOTTOM OF THE RETORT WITH PERFORATIONS DISTRIBUTED UNIFORMLY ALONG THE UPPER PART OF THE PIPE? YES [] NO [] SHALL REQUIREMENT, 113.40(b)(5). DESCRIBE THE SHAPE AND DIMENSIONS OF THE STEAM SPREADER PIPE. |
| STACKING EQUIPMENT AND CONTAINER POSITION (113.40(b)(7) |
| ARE CRATES, TRAYS, ETC. FOR HOLDING CONTAINERS MADE OF STRAP IRON OR OTHER ADEQUATELY PERFORATED MATERIAL? YES [] NO [] |
| ARE CONTAINERS POSITIONED IN THE RETORT AS SPECIFIED IN THE SCHEDULED PROCESS? YES [] NO [] |
| ARE DIVIDERS, TRAYS, RACKS OR OTHER MEANS OF POSITIONING FLEXIBLE CONTAINERS DESIGNED AND EMPLOYED TO INSURE EVEN CIRCULATION OF HEATING MEDIUM AROUND ALL CONTAINERS? YES [] NO [] |
| DRAIN LINE AND VALVE |
| ARE SCREENS USED OVER ALL DRAIN OPENINGS TO PREVENT CLOGGING OF DRAINS? YES [] NO [] (SHALL REQUIREMENT) |
| IS THE DRAIN LINE VALVE WATER TIGHT AND NON-CLOGGING? YES [] NO [] |
| WATER LEVEL CONTROL |
| DOES WATER COVER THE TOP LAYER OF CONTAINERS IN THE RETORT BASKETS DURING THE ENTIRE COME-UP TIME AND PROCESSING PERIOD? YES [] NO [] DOES WATER COVER THE TOP LAYERS OF CONTAINERS DURING THE COOLING PERIOD? YES [] NO [] (WATER SHALL COVER THE TOP LAYER OF CONTAINERS DURING THE ENTIRE COME-UP TIME AND PROCESSING PERIOD AND SHOULD COVER THE TOP LAYER DURING THE COOLING PERIODS – 113.40(b)(9)). |
| IS THERE A MEANS TO DETERMINE THE WATER LEVEL IN THE RETORT DURING OPERATION? YES [] NO [] IF YES, WHAT MONITORING DEVICES ARE USED: GAGE [], SIGHT GLASS [], PETCOCK [], OTHER [] (EXPLAIN TYPE). IF NO MONITORING DEVICES, EXPLAIN. (THERE SHALL BE A MEANS OF DETERMINING THE WATER LEVEL IN THE RETORT DURING OPERATION – 113.40(b)(9)) |
| DOES THE OPERATOR CHECK AND RECORD THE WATER LEVEL AT INTERVALS SUFFICIENT TO ENSURE ITS ADEQUACY? YES [] NO [] SHALL REQUIREMENT, 113.40(b)(9) |
| PROCESSING WATER |
| IS THE PROCESSING WATER HEATED IN A SEPARATE VESSEL AND THEN INTRODUCED INTO THE PROCESSING VESSEL? YES [] NO [] |
| WAS THE TEMPERATURE OF THE PREHEATED WATER TAKEN INTO CONSIDERATION DURING TEMPERATURE DISTRIBUTION STUDIES? YES [] NO [] |
| DOES THE FIRM CONTROL THE PREHEATING OF PROCESS WATER AS CRITICAL TO THE THERMAL PROCESS? YES [] NO [] |
| AIR SUPPLY AND CONTROLS |
| IS AIR SUPPLIED TO THE RETORTS DURING THE COME-UP, PROCESSING AND COOLING PERIODS TO PROMOTE CIRCULATION OF WATER AND TEMPERATURE DISTRIBUTION? YES [] NO [] IF YES, IS THE AIR INTRODUCED AT THE PROPER PRESSURE AND RATE? YES [] NO [] SHALL REQUIREMENT, 113.40(b)(10((I) |
| IS THE COMPRESSED AIR SUPPLIED TO THE RETORT CONTROLLED BY AN AUTOMATIC PRESSURE CONTROL UNIT? YES [] NO [] SHALL REQUIREMENT, 113.40(b)(10)(I) |
| IS THE AIR SUPPLY LINE EQUIPPED WITH A CHECK VALVE TO PREVENT WATER FROM ENTERING THE SYSTEM? YES [] NO [] SHALL REQUIREMENT, 113.40(b)(10)(I). |
| HAS THE ADEQUACY OF THE AIR OR WATER CIRCULATION FOR UNIFORM HEAT DISTRIBUTION WITHIN THE RETORT BEEN ESTABLISHED IN ACCORDANCE WITH PROCEDURES RECOGNIZED BY A COMPETENT PROCESS AUTHORITY? YES [] NO [] ARE RECORDS OF THE ESTABLISHMENT OF UNIFORM HEAT DISTRIBUTION KEPT ON FILE? YES [] NO [] 113.40(b)(10)(I) |
| IF AIR IS USED TO PROMOTE WATER CIRCULATION IN THE RETORT, IS IT INTRODUCED INTO THE STEAM LINE AT A POINT BETWEEN THE RETORT AND THE STEAM CONTROL VALVE AT THE BOTTOM OF THE RETORT? YES [] NO [] SHALL REQUIREMENT, 113.40(b)(10)(I). |
| WHEN A WATER CIRCULATING SYSTEM IS USED FOR HEAT DISTRIBUTION, IS IT INSTALLED IN SUCH A MANNER THAT WATER WILL BE DRAWN FROM THE BOTTOM OF THE RETORT THROUGH A SUCTION MANIFOLD AND DISCHARGED THROUGH A SPREADER WHICH EXTENDS THE LENGTH OF THE TOP OF THE RETORT? YES [] NO [] N/A [] SHALL REQUIREMENT, 113.40(b)(10)(II) |
| FOR WATER CIRCULATING SYSTEMS, ARE THE HOLES IN THE WATER SPREADER UNIFORMLY DISTRIBUTED AND DO THEY HAVE AN AGGREGATE AREA NOT GREATER THAN THE CROSS-SECTION AREA OF THE OUTLET LINE FROM THE PUMP? YES [] NO [] N/A [] |
| ARE SUCTION OUTLETS PROTECTED WITH NONCLOGGING SCREENS TO KEEP DEBRIS FROM ENTERING THE CIRCULATING SYSTEM? YES [] NO [] |
| IS THE WATER PUMP EQUIPPED WITH A PILOT LIGHT OR OTHER SIGNALING DEVICE TO WARN THE OPERATOR WHEN IT IS NOT RUNNING? YES[] NO [] |
| IS AN ALTERNATE METHOD OF WATER CIRCULATION USED? YES [] NO [] (113.40(b)(10)(II). IF YES, HAS THE METHOD BEEN ESTABLISHED BY A COMPETENT PROCESS AUTHORITY? YES [] NO [] DESCRIBE THE ALTERNATE METHOD. |
| COOLING WATER SUPPLY |
| FOR VERTICAL STILL RETORTS, IS THE COOLING WATER INTRODUCED AT THE TOP OF THE RETORT BETWEEN THE WATER AND CONTAINER LEVELS? YES [] NO [] N/A [] SHOULD REQUIREMENT - 113.40(b)(11) |
| FOR HORIZONTAL RETORTS, IS THE COOLING WATER INTRODUCED INTO THE SUCTION SIDE OF THE PUMP? YES [] NO [] SHOULD REQUIREMENT 113.40(b)(11) |
| IS THE WATER-COOLING LINE EQUIPPED WITH A CHECK VALVE? YES [] NO [] SHOULD REQUIREMENT – 113.40(b)(11) |
| RETORT HEADSPACE |
| IS HEADSPACE, NECESSARY TO CONTROL THE AIR PRESSURE, MAINTAINED BETWEEN THE WATER LEVEL AND THE TOP OF THE RETORT SHELL? YES [] NO [] |