National Oceanic and Atmospheric Administration

40-Day Endurance Fisheries Research Vessel

FRV40-1

Stability Analysis

DWG. NO. FRV40 802-00009

Prepared by:

Maritime Administration

May 26, 2000

This Guidance Document illustrates

design features of the ship, but does

not depict, nor is it intended that it

depict, all features and details of the

systems and structures to which it relates.

Table of Contents

- Intact Stability Analysis

  - Summary 				  		    1

  - Weather Criterion			  		    1

  - Righting Energy Criteria		  		    5

  - Lifting							  12

  - Towing						  21

- Damage Stability Analysis

  - Summary						  23

  - Damage Characteristics				  23

  - Results						  24

  - Effect of Dumping Roll Stabilization Tank	  25

  - Effect of Trim						  26

  - Compartment Descriptions				  27

  - Damage Condition Summaries (No Trim)	  29

  - Damage Condition Summaries (with Trim)	  46

  - Damage Condition D-4				  53

  - Damage Condition F-1				  56

- Capacities

  - Tank Capacity Summary				  59

  - Salt Water Ballast Tanks				  60

  - Diesel Oil Tanks					  66

  - Fresh Water Tanks					  72

  - Sewage Tank					  73

  - Stores							  74

- Loading Conditions

  - Summary						  75

  - Maximum Allowable KG				  76

  - Lightship Weight					  76

  - Loading Conditions without Icing			  77

  - Loading Conditions with Icing			  93

Appendices

A.   SHCP Offsets						109

B.   Hydrostatics						129

1.a.	Summary

Intact stability of the FRV40 was evaluated per the USCG Weather Criterion of 46 CRF170.170, the USCG requirements for vessels of unusual form of 46 CFR 170.173 (energy) and the towline criteria of 46 CFR 173.095.   Although the USCG lifting requirements of 46 CFR 173 are not applicable (the maximum heeling moment is below the threshold level) the maximum allowable KG to meet the criteria of 46 CFR 173.020(c) has been imposed as a design requirement.

The hull form and offsets used for this analysis are discussed in Appendix A.  This analysis used the General Arrangement of the FRV40-1, drawing number FRV40 802-00004, to define the extent and nature of the superstructure.  It is assumed that all openings will be fitted with appropriate closures and that downflooding is not an issue.

For each criteria curves of maximum allowable virtual KG versus draft were developed for the range of expected operating drafts.  The results are summarized in the following table.

|  | Maximum Allowable KG, m |
| --- | --- |
| Draft, m | Weather | Energy | Lifting | Towing |
| 5.20 | 7.33 | 7.43 | 7.30 | 7.72 |
| 5.40 | 7.51 | 7.49 | 7.43 | 7.83 |
| 5.60 | 7.67 | 7.54 | 7.57 | 7.95 |
| 5.80 | 7.77 | 7.58 | 7.62 | 7.99 |
| 6.00 | 7.82 | 7.57 | 7.64 | 8.01 |
| 6.20 | 7.86 | 7.39 | 7.65 | 8.00 |

The overall limiting criteria was the energy criteria of 46 CFR 170.173 for the range of operating drafts.

1.b.	Weather Criterion

The Weather Criterion of 46 CFR 170.170 was evaluated to obtain minimum required values for GM.  Once determined the GMs were converted to values of maximum allowable KGs.  The calculation was made for service on exposed waters.

The wind and underwater profile areas and centers were determined for the design draft of 5.90 meters using AutoCad and the General Arrangement drawing for FRV40-1.   Areas and centers for other drafts were determined by taking differences from those of the design draft.

The Length between perpendiculars was taken as the waterline length at the deepest operating draft in accordance with 46 CFR 170.055(I)(1).   The deepest operating draft is taken as the scantling draft of 6.2 m.  At this draft the waterline length is 60.93 m.

P = .055 + (L/1309)2  tons/m2 for ocean service

P = 0.05717

The calculations are summarized in the following pages.

| Calculation of Weather Criterion for GM per 46 CFR 170.170 |  |  |  |
| --- | --- | --- | --- |
|  |  |  |  | Wind Area |  |  | Underwater |  |  |
| Draft, m | Del wl | Del Area | y of darea | A,m2 | y abv bl | y abv wl | A,m2 | y abv bl | y below wl |
| 5.00 | 0.90 | 53.73 | 5.45 | 686.44 | 11.44 | 6.44 | 238.39 | 2.56 | 2.44 |
| 5.10 | 0.80 | 47.84 | 5.50 | 680.55 | 11.50 | 6.40 | 244.28 | 2.66 | 2.44 |
| 5.20 | 0.70 | 41.93 | 5.55 | 674.64 | 11.55 | 6.35 | 250.19 | 2.75 | 2.45 |
| 5.30 | 0.60 | 36.00 | 5.60 | 668.71 | 11.61 | 6.31 | 256.12 | 2.84 | 2.46 |
| 5.40 | 0.50 | 30.05 | 5.65 | 662.76 | 11.66 | 6.26 | 262.07 | 2.93 | 2.47 |
| 5.50 | 0.40 | 23.88 | 5.70 | 656.59 | 11.72 | 6.22 | 268.24 | 3.01 | 2.49 |
| 5.60 | 0.30 | 18.06 | 5.75 | 650.77 | 11.78 | 6.18 | 274.06 | 3.08 | 2.52 |
| 5.70 | 0.20 | 12.06 | 5.80 | 644.77 | 11.83 | 6.13 | 280.06 | 3.15 | 2.55 |
| 5.80 | 0.10 | 6.03 | 5.85 | 638.74 | 11.89 | 6.09 | 286.09 | 3.21 | 2.59 |
| 5.90 | 0.00 | 0.00 | 5.90 | 632.71 | 11.95 | 6.05 | 292.12 | 3.27 | 2.63 |
| 6.00 | -0.10 | -6.03 | 5.95 | 626.68 | 12.01 | 6.01 | 298.15 | 3.33 | 2.67 |
| 6.10 | -0.20 | -12.06 | 6.00 | 620.65 | 12.07 | 5.97 | 304.18 | 3.38 | 2.72 |
| 6.20 | -0.30 | -18.09 | 6.05 | 614.62 | 12.12 | 5.92 | 310.21 | 3.42 | 2.78 |
| 6.30 | -0.40 | -24.12 | 6.10 | 608.59 | 12.18 | 5.88 | 316.24 | 3.47 | 2.83 |
| 6.40 | -0.50 | -30.15 | 6.15 | 602.56 | 12.24 | 5.84 | 322.27 | 3.51 | 2.89 |
| P | 0.05717 |  |  |  |  |  |  |  |  |
| Above 5.9 m wl: |  | Below 5.9 m wl: |  |  |  |  |  |  |  |
| Area = | 632.71 | Area = | 292.12 |  |  |  |  |  |  |
| vcg = | 11.95 | vcg = | 3.27 |  |  |  |  |  |  |

| Calculation of Weather Criterion for GM per 46 CFR 170.170 |  |  |
| --- | --- | --- |
|  |  |  |  |  |  |  |  | Wind moment per 46 CFR 171.080 |
| Draft, m | H,m | W, mt | tan(T) | GM, m | KM, m | KG, m |  | mt-m |
| 5.00 | 8.89 | 1830.0 | 0.249 | 0.765 | 7.94 | 7.17 |  | 74.66 |
| 5.10 | 8.84 | 1889.5 | 0.249 | 0.731 | 7.99 | 7.26 |  | 73.63 |
| 5.20 | 8.80 | 1951.6 | 0.249 | 0.698 | 8.03 | 7.33 |  | 72.66 |
| 5.30 | 8.77 | 2015.1 | 0.249 | 0.668 | 8.08 | 7.41 |  | 71.74 |
| 5.40 | 8.74 | 2081.1 | 0.249 | 0.639 | 8.15 | 7.51 |  | 70.88 |
| 5.50 | 8.72 | 2149.9 | 0.249 | 0.611 | 8.22 | 7.61 |  | 70.04 |
| 5.60 | 8.70 | 2221.0 | 0.249 | 0.585 | 8.26 | 7.67 |  | 69.30 |
| 5.70 | 8.69 | 2293.1 | 0.249 | 0.561 | 8.29 | 7.73 |  | 68.57 |
| 5.80 | 8.68 | 2366.1 | 0.249 | 0.538 | 8.31 | 7.77 |  | 67.88 |
| 5.90 | 8.68 | 2439.5 | 0.249 | 0.517 | 8.32 | 7.80 |  | 67.22 |
| 6.00 | 8.68 | 2513.7 | 0.249 | 0.497 | 8.32 | 7.82 |  | 66.60 |
| 6.10 | 8.69 | 2588.4 | 0.249 | 0.478 | 8.32 | 7.84 |  | 66.01 |
| 6.20 | 8.70 | 2663.6 | 0.249 | 0.461 | 8.32 | 7.86 |  | 65.44 |
| 6.30 | 8.71 | 2739.2 | 0.249 | 0.444 | 8.31 | 7.87 |  | 64.90 |
| 6.40 | 8.73 | 2815.2 | 0.249 | 0.429 | 8.31 | 7.88 |  | 64.38 |

1.c.	Energy Criteria

The FRV40 was evaluated based on the Criterion for vessels of unusual proportion and form found in 46 CFR 170.173.  This is a righting energy bases criterion that is applicable to mechanically powered vessels under 100 meters in length, per 46 CFR 170.170(d).

In making the calculation the buoyancy of the superstructure up to the 01 level (11.4 m above baseline) aft to frame 58 was included.  The wet laboratory / fish laboratory aft of frames 58 was not included.  In modeling the superstructure the starboard side was used, since this side contains less buoyant volume than the port side.

At drafts less than 5.95 meters, the maximum allowable KG was limited by the requirement for a righting arm of at least 0.20 meters at a heel angle of 30 degrees (or greater).  At deeper drafts the allowable KG was limited by the requirement that the maximum righting arm occur at a heel angle of 25 degrees or greater.

The energy criterion calculations are given on the following pages.

Energy 46 CFR 170.173

| Draft, m | 5.2 |  |  |  |
| --- | --- | --- | --- | --- |
| Trim, m | 0.0 |  |  |  |
| Reqs of 46 CFR 170.173(2)(b) |  | Required | Actual |  |
| (1) initial GM, m |  | 0.150 | 0.588 |  |
| (2) GZ at 30 degrees |  | 0.200 | 0.200 | Limiting |
| (3) Angle of max GZ |  | 25.000 | 34.000 |  |
| (4) Area 0-30 |  | 3.150 | 3.591 |  |
| (5) Area 0-40 |  | 5.150 | 5.616 |  |
| (6) Area 30-40 |  | 1.720 | 2.025 |  |
| Pole height, m = |  | 7.500 |  |  |
| Delta KG, m= |  |  | 0.072 |  |
| Actual KG, m = |  |  | 7.428 |  |
|  | Angle | GZ |  | Area |
|  | 0 | 0 | 0.000 | 0.000 |
|  | 2 | 0.018 | 0.021 | 0.021 |
|  | 4 | 0.036 | 0.041 | 0.082 |
|  | 6 | 0.052 | 0.060 | 0.183 |
|  | 8 | 0.068 | 0.078 | 0.320 |
|  | 10 | 0.082 | 0.095 | 0.493 |
|  | 12 | 0.095 | 0.110 | 0.697 |
|  | 14 | 0.107 | 0.124 | 0.932 |
|  | 16 | 0.117 | 0.137 | 1.193 |
|  | 18 | 0.126 | 0.148 | 1.478 |
|  | 20 | 0.134 | 0.159 | 1.785 |
|  | 22 | 0.141 | 0.168 | 2.111 |
|  | 24 | 0.147 | 0.176 | 2.456 |
|  | 26 | 0.154 | 0.186 | 2.817 |
|  | 28 | 0.16 | 0.194 | 3.197 |
|  | 30 | 0.164 | 0.200 | 3.591 |
|  | 32 | 0.165 | 0.203 | 3.994 |
|  | 34 | 0.164 | 0.204 | 4.401 |
|  | 36 | 0.16 | 0.202 | 4.808 |
|  | 38 | 0.157 | 0.201 | 5.211 |
|  | 40 | 0.157 | 0.203 | 5.616 |
|  | 42 | 0.163 | 0.211 | 6.030 |
|  | 44 | 0.172 | 0.222 | 6.464 |
|  | 46 | 0.167 | 0.219 | 6.904 |
|  | 48 | 0.158 | 0.212 | 7.335 |
|  | 50 | 0.141 | 0.196 | 7.742 |
|  | 52 | 0.118 | 0.175 | 8.113 |
|  | 54 | 0.089 | 0.147 | 8.435 |
|  | 56 | 0.054 | 0.114 | 8.696 |
|  | 58 | 0.015 | 0.076 | 8.886 |

Energy 46 CFR 170.173

| Draft, m | 5.4 |  |  |  |
| --- | --- | --- | --- | --- |
| Trim, m | 0.0 |  |  |  |
| Reqs of 46 CFR 170.173(2)(b) |  | Required | Actual |  |
| (1) initial GM, m |  | 0.150 | 0.644 |  |
| (2) GZ at 30 degrees |  | 0.200 | 0.200 | Limiting |
| (3) Angle of max GZ |  | 25.000 | 31.000 |  |
| (4) Area 0-30 |  | 3.150 | 3.662 |  |
| (5) Area 0-40 |  | 5.150 | 5.617 |  |
| (6) Area 30-40 |  | 1.720 | 1.954 |  |
| Pole height, m = |  | 7.500 |  |  |
| Delta KG, m= |  |  | 0.014 |  |
| Actual KG, m = |  |  | 7.486 |  |
|  | Angle | GZ |  | Area |
|  | 0 | 0 | 0.000 | 0.000 |
|  | 2 | 0.022 | 0.022 | 0.022 |
|  | 4 | 0.043 | 0.044 | 0.089 |
|  | 6 | 0.063 | 0.064 | 0.197 |
|  | 8 | 0.08 | 0.082 | 0.344 |
|  | 10 | 0.096 | 0.098 | 0.524 |
|  | 12 | 0.11 | 0.113 | 0.736 |
|  | 14 | 0.123 | 0.126 | 0.975 |
|  | 16 | 0.135 | 0.139 | 1.240 |
|  | 18 | 0.145 | 0.149 | 1.528 |
|  | 20 | 0.155 | 0.160 | 1.837 |
|  | 22 | 0.164 | 0.169 | 2.166 |
|  | 24 | 0.173 | 0.179 | 2.514 |
|  | 26 | 0.182 | 0.188 | 2.881 |
|  | 28 | 0.19 | 0.197 | 3.266 |
|  | 30 | 0.193 | 0.200 | 3.662 |
|  | 32 | 0.193 | 0.200 | 4.063 |
|  | 34 | 0.191 | 0.199 | 4.462 |
|  | 36 | 0.186 | 0.194 | 4.855 |
|  | 38 | 0.181 | 0.190 | 5.239 |
|  | 40 | 0.179 | 0.188 | 5.617 |
|  | 42 | 0.178 | 0.187 | 5.992 |
|  | 44 | 0.17 | 0.180 | 6.359 |
|  | 46 | 0.154 | 0.164 | 6.703 |
|  | 50 | 0.113 | 0.124 | 6.991 |
|  | 52 | 0.081 | 0.092 | 7.206 |
|  | 54 | 0.047 | 0.058 | 7.357 |
|  | 56 | 0.006 | 0.018 | 7.433 |
|  | 58 | -0.039 | -0.027 | 7.423 |
|  | 56 | -0.041 | -0.029 | 7.367 |
|  | 58 | -0.082 | -0.070 | 7.267 |

Energy 46 CFR 170.173

| Draft, m | 5.6 |  |  |  |
| --- | --- | --- | --- | --- |
| Trim, m | 0.0 |  |  |  |
| Reqs of 46 CFR 170.173(2)(b) |  | Required | Actual |  |
| (1) initial GM, m |  | 0.150 | 0.701 |  |
| (2) GZ at 30 degrees |  | 0.200 | 0.200 | Limiting |
| (3) Angle of max GZ |  | 25.000 | 29.000 |  |
| (4) Area 0-30 |  | 3.150 | 3.824 |  |
| (5) Area 0-40 |  | 5.150 | 5.675 |  |
| (6) Area 30-40 |  | 1.720 | 1.851 |  |
| Pole height, m = |  | 7.500 |  |  |
| Delta KG, m= |  |  | -0.044 |  |
| Actual KG, m = |  |  | 7.544 |  |
|  | Angle | GZ |  | Area |
|  | 0 | 0 | 0.000 | 0.000 |
|  | 2 | 0.026 | 0.024 | 0.024 |
|  | 4 | 0.051 | 0.048 | 0.097 |
|  | 6 | 0.074 | 0.069 | 0.214 |
|  | 8 | 0.094 | 0.088 | 0.371 |
|  | 10 | 0.112 | 0.104 | 0.564 |
|  | 12 | 0.128 | 0.119 | 0.787 |
|  | 14 | 0.143 | 0.132 | 1.038 |
|  | 16 | 0.157 | 0.145 | 1.315 |
|  | 18 | 0.17 | 0.156 | 1.617 |
|  | 20 | 0.181 | 0.166 | 1.939 |
|  | 22 | 0.193 | 0.177 | 2.281 |
|  | 24 | 0.205 | 0.187 | 2.645 |
|  | 26 | 0.215 | 0.196 | 3.028 |
|  | 28 | 0.221 | 0.200 | 3.424 |
|  | 30 | 0.222 | 0.200 | 3.824 |
|  | 32 | 0.22 | 0.197 | 4.221 |
|  | 34 | 0.214 | 0.189 | 4.607 |
|  | 36 | 0.207 | 0.181 | 4.978 |
|  | 38 | 0.201 | 0.174 | 5.333 |
|  | 40 | 0.197 | 0.169 | 5.675 |
|  | 42 | 0.187 | 0.158 | 6.002 |
|  | 44 | 0.169 | 0.138 | 6.298 |
|  | 46 | 0.145 | 0.113 | 6.549 |
|  | 50 | 0.079 | 0.045 | 6.708 |
|  | 52 | 0.038 | 0.003 | 6.757 |
|  | 54 | -0.007 | -0.043 | 6.717 |
|  | 56 | -0.049 | -0.085 | 6.589 |
|  | 58 | -0.099 | -0.136 | 6.368 |
|  | 58 | -0.158 | -0.195 | 6.036 |

Energy 46 CFR 170.173

| Draft, m | 5.8 |  |  |  |
| --- | --- | --- | --- | --- |
| Trim, m | 0.0 |  |  |  |
| Reqs of 46 CFR 170.173(2)(b) |  | Required | Actual |  |
| (1) initial GM, m |  | 0.150 | 0.722 |  |
| (2) GZ at 30 degrees |  | 0.200 | 0.200 | Limiting |
| (3) Angle of max GZ |  | 25.000 | 26.000 |  |
| (4) Area 0-30 |  | 3.150 | 4.052 |  |
| (5) Area 0-40 |  | 5.150 | 5.812 |  |
| (6) Area 30-40 |  | 1.720 | 1.760 |  |
| Pole height, m = |  | 7.500 |  |  |
| Delta KG, m= |  |  | -0.080 |  |
| Actual KG, m = |  |  | 7.580 |  |
|  | Angle | GZ |  | Area |
|  | 0 | 0 | 0.000 | 0.000 |
|  | 2 | 0.028 | 0.025 | 0.025 |
|  | 4 | 0.055 | 0.049 | 0.100 |
|  | 6 | 0.081 | 0.073 | 0.222 |
|  | 8 | 0.104 | 0.093 | 0.387 |
|  | 10 | 0.124 | 0.110 | 0.590 |
|  | 12 | 0.143 | 0.126 | 0.827 |
|  | 14 | 0.161 | 0.142 | 1.095 |
|  | 16 | 0.177 | 0.155 | 1.391 |
|  | 18 | 0.192 | 0.167 | 1.714 |
|  | 20 | 0.207 | 0.180 | 2.061 |
|  | 22 | 0.221 | 0.191 | 2.431 |
|  | 24 | 0.234 | 0.201 | 2.824 |
|  | 26 | 0.242 | 0.207 | 3.232 |
|  | 28 | 0.244 | 0.206 | 3.646 |
|  | 30 | 0.24 | 0.200 | 4.052 |
|  | 32 | 0.234 | 0.192 | 4.444 |
|  | 34 | 0.226 | 0.181 | 4.816 |
|  | 36 | 0.217 | 0.170 | 5.168 |
|  | 38 | 0.211 | 0.162 | 5.499 |
|  | 40 | 0.202 | 0.151 | 5.812 |
|  | 42 | 0.185 | 0.131 | 6.094 |
|  | 44 | 0.16 | 0.104 | 6.330 |
|  | 46 | 0.13 | 0.072 | 6.507 |
|  | 48 | 0.092 | 0.033 | 6.612 |
|  | 50 | 0.049 | -0.012 | 6.632 |
|  | 52 | 0 | -0.063 | 6.557 |
|  | 54 | -0.05 | -0.115 | 6.379 |
|  | 56 | -0.103 | -0.169 | 6.095 |
|  | 58 | -0.158 | -0.226 | 5.700 |

Energy 46 CFR 170.173

| Draft, m | 6.0 |  |  |  |
| --- | --- | --- | --- | --- |
| Trim, m | 0.0 |  |  |  |
| Reqs of 46 CFR 170.173(2)(b) |  | Required | Actual |  |
| (1) initial GM, m |  | 0.150 | 0.762 |  |
| (2) GZ at 30 degrees |  | 0.200 | 0.211 |  |
| (3) Angle of max GZ |  | 25.000 | 25.000 | Limiting |
| (4) Area 0-30 |  | 3.150 | 4.465 |  |
| (5) Area 0-40 |  | 5.150 | 6.269 |  |
| (6) Area 30-40 |  | 1.720 | 1.804 |  |
| Pole height, m = |  | 7.500 |  |  |
| Delta KG, m= |  |  | -0.069 |  |
| Actual KG, m = |  |  | 7.569 |  |
|  | Angle | GZ |  | Area |
|  | 0 | 0 | 0.000 | 0.000 |
|  | 2 | 0.029 | 0.027 | 0.027 |
|  | 4 | 0.057 | 0.052 | 0.105 |
|  | 6 | 0.083 | 0.076 | 0.233 |
|  | 8 | 0.109 | 0.099 | 0.409 |
|  | 10 | 0.133 | 0.121 | 0.629 |
|  | 12 | 0.154 | 0.140 | 0.890 |
|  | 14 | 0.174 | 0.157 | 1.187 |
|  | 16 | 0.193 | 0.174 | 1.518 |
|  | 18 | 0.21 | 0.189 | 1.881 |
|  | 20 | 0.228 | 0.204 | 2.274 |
|  | 22 | 0.244 | 0.218 | 2.696 |
|  | 24 | 0.254 | 0.226 | 3.140 |
|  | 25 | 0.255 | 0.226 |  |
|  | 26 | 0.255 | 0.225 | 3.591 |
|  | 28 | 0.252 | 0.220 | 4.035 |
|  | 30 | 0.245 | 0.211 | 4.465 |
|  | 32 | 0.235 | 0.198 | 4.874 |
|  | 34 | 0.224 | 0.185 | 5.258 |
|  | 36 | 0.215 | 0.174 | 5.618 |
|  | 38 | 0.207 | 0.165 | 5.957 |
|  | 40 | 0.192 | 0.148 | 6.269 |
|  | 42 | 0.17 | 0.124 | 6.541 |
|  | 44 | 0.14 | 0.092 | 6.757 |
|  | 46 | 0.104 | 0.054 | 6.903 |
|  | 48 | 0.063 | 0.012 | 6.969 |
|  | 50 | 0.017 | -0.036 | 6.945 |
|  | 52 | -0.034 | -0.088 | 6.821 |
|  | 54 | -0.088 | -0.144 | 6.589 |
|  | 56 | -0.145 | -0.202 | 6.243 |
|  | 58 | -0.204 | -0.263 | 5.778 |

Energy 46 CFR 170.173

| Draft, m | 6.2 |  |  |  |
| --- | --- | --- | --- | --- |
| Trim, m | 0.0 |  |  |  |
| Reqs of 46 CFR 170.173(2)(b) |  | Required | Actual |  |
| (1) initial GM, m |  | 0.150 | 0.944 |  |
| (2) GZ at 30 degrees |  | 0.200 | 0.291 |  |
| (3) Angle of max GZ |  | 25.000 | 25.000 | Limiting |
| (4) Area 0-30 |  | 3.150 | 6.008 |  |
| (5) Area 0-40 |  | 5.150 | 8.703 |  |
| (6) Area 30-40 |  | 1.720 | 2.695 |  |
| Pole height, m = |  | 7.500 |  |  |
| Delta KG, m= |  |  | 0.113 |  |
| Actual KG, m = |  |  | 7.387 |  |
|  | Angle | GZ |  | Area |
|  | 0 | 0 | 0.000 | 0.000 |
|  | 2 | 0.029 | 0.033 | 0.033 |
|  | 4 | 0.057 | 0.065 | 0.131 |
|  | 6 | 0.085 | 0.097 | 0.292 |
|  | 8 | 0.111 | 0.127 | 0.516 |
|  | 10 | 0.137 | 0.157 | 0.799 |
|  | 12 | 0.161 | 0.184 | 1.140 |
|  | 14 | 0.184 | 0.211 | 1.536 |
|  | 16 | 0.204 | 0.235 | 1.983 |
|  | 18 | 0.225 | 0.260 | 2.478 |
|  | 20 | 0.244 | 0.283 | 3.020 |
|  | 22 | 0.256 | 0.298 | 3.601 |
|  | 24 | 0.259 | 0.305 | 4.205 |
|  | 25 | 0.257 | 0.305 |  |
|  | 26 | 0.255 | 0.305 | 4.814 |
|  | 28 | 0.246 | 0.299 | 5.418 |
|  | 30 | 0.235 | 0.291 | 6.008 |
|  | 32 | 0.223 | 0.283 | 6.583 |
|  | 34 | 0.211 | 0.274 | 7.140 |
|  | 36 | 0.201 | 0.267 | 7.681 |
|  | 38 | 0.188 | 0.258 | 8.206 |
|  | 40 | 0.167 | 0.240 | 8.703 |
|  | 42 | 0.14 | 0.216 | 9.159 |
|  | 44 | 0.107 | 0.185 | 9.560 |
|  | 46 | 0.07 | 0.151 | 9.897 |
|  | 48 | 0.026 | 0.110 | 10.158 |
|  | 50 | -0.021 | 0.066 | 10.333 |
|  | 52 | -0.072 | 0.017 | 10.416 |
|  | 54 | -0.126 | -0.035 | 10.398 |
|  | 56 | -0.183 | -0.089 | 10.275 |
|  | 58 | -0.242 | -0.146 | 10.039 |

1.d.	Lifting

Lifting was evaluated in accordance with 46 CFR 173.

46 CFR 173 applies to vessels where the maximum heeling moment due to hook load is equal to or greater than 0.67(W)(GM)(F/B) in meter-metric tons.   For the FRV40 (at the 5.9 m design draft):

W    = 2439 mt

GM  =    0.75 m (approximate)

F     = (8.65 m – 5.90 m) = 2.65 m

B     =  15.0  m

Required heeling moment =  216.5  m-t

The SOR contains several different requirements for crane performance as follows:

|  |  | Sea | Crane Radius, m | Hook Load, t | Heeling Moment, m-t |
| --- | --- | --- | --- | --- | --- |
| Either Crane | 3636 kg any point on working deck | Exposed | 10.70+ 5.92 | 3.636 | 60.43 |
|  | 1356 kg 2 m aft of stern | Exposed | 13.60+5.92 | 1.356 | 26.47 |
|  | 1588 kg 4 m from side of ship | Exposed | 7.59+5.92 | 1.588 | 21.45 |
|  | 3625 kg 9.1 m from side | Protected | 12.62+5.92 | 3.625 | 67.21 |
| Stbd Crane | 750 kg at center of side sampling station | Exposed | 18.60+5.92 | 0.750 | 18.39 |
| Stbd Crane | Maximum crane capacity |  | 3.05 + 5.92 | 22.69 | 203.4 |

For purposes of this calculation, “Crane Radius” was taken as the maximum outreach needed to meet the requirement plus the distance off centerline of the crane.  This is a conservative approach.    The maximum moment required by the SOR is well below the threshold for which 46 CFR 173 is applicable.   (The maximum heeling moment of the Appleton EB 50-60-25 marine crane, called for by the SOR, is 203.4 m-t, still below the threshold for application of 46 CFR 173).

This criterion was evaluated for drafts ranging from 5.2 m to 6.2 m for the maximum crane moment.

The criterion requires a minimum of 4.57 meter-degrees of righting energy between the righting and heeling arms from the point of intersection to the minimum of 1) the angle of the maximum heeling arm; 2) the angle of downflooding; or 3) 40 degrees.  For drafts above 5.2 m the limit for the FRV40 was the angle of the maximum righting arm.

Righting arm curves were calculated using SHCP at every two degrees up to a heel angle of 40 degrees.  Initial trim was zero.  The residual righting arm curve was calculated by subtracting the heeling moment (times the cosine of the heel angle) from the righting arm curve.  The pole height was adjusted until the area up to the maximum righting arm was equal to the required 4.57 m-deg.   The angle of maximum righting arm of the residual curve varies with draft and is about twenty-eight degrees at the design draft of 5.9 m.   Once the limiting pole height was determined, maximum allowable KG (before lifting) was determined by decreasing the pole height by the rise in KG attributable to lifting a load from the main deck to the top of the boom.

In the region of maximum righting arm the righting arm curve is very flat.  Therefore small changes in pole height, trim, and buoyant volume could be expected to have noticeable effect of the maximum allowable KG permitted by the criteria.   At thirty degrees of heel the deck edge of the 01 level is immersed.  No credit has been taken for any superstructure above the 01 level, or of any superstructure (including the 01 level) aft of frame 58.  Even small changes in buoyant volume in these locations would be expected to noticeably change maximum allowable KG.

Maximum allowable KGs based on this criterion are about 0.5 meters less than the limit imposed by other portions of the intact stability analysis, and if imposed would be the limiting KG for the vessel.

Since the criteria was originally developed for heavy lift situations, and since the FRV40 is well below the threshold of applicability, it is considered inappropriate to apply this criteria to the FRV40.  However since stability while lifting is still an important consideration, it was decided to impose the requirement that the vessel meet the alternative compliance portion of the Coast Guard lifting criteria of 46 CFR 173.020(c).   This criteria limits the lifting imposed heel angle to that which would immerse half the freeboard.

The details of this calculation follows:

Lifting per 46 CFR 173.020(c)

|  |  |  | heel tangent |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Draft | Free-board | 1/2 FB | to 1/2 FB | angle | Displ | GM | KM | KG while lifting | KG before lift |
| 5.20 | 3.45 | 1.725 | 0.230 | 12.95 | 1950.9 | 0.461 | 8.030 | 7.569 | 7.30 |
| 5.40 | 3.25 | 1.625 | 0.217 | 12.23 | 2080.4 | 0.458 | 8.140 | 7.682 | 7.43 |
| 5.60 | 3.05 | 1.525 | 0.203 | 11.49 | 2220.3 | 0.457 | 8.260 | 7.803 | 7.57 |
| 5.80 | 2.85 | 1.425 | 0.190 | 10.76 | 2365.2 | 0.458 | 8.300 | 7.842 | 7.62 |
| 6.00 | 2.65 | 1.325 | 0.177 | 10.02 | 2512.8 | 0.463 | 8.310 | 7.847 | 7.64 |
| 6.20 | 2.45 | 1.225 | 0.163 | 9.28 | 2662.7 | 0.472 | 8.320 | 7.848 | 7.65 |
|  | Heeling moment |  | 203.4 |  |  |  |  |  |  |
|  | Vertical moment |  | 516.6 |  |  |  |  |  |  |

Lifting per 46 CFR 173.020(b)

| Draft, m | 5.2 |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Displ, mt | 1950.9 |  |  |  |  |  |  |  |
| Heeling moment, m-t | 203.4 |  |  |  |  |  |  |  |
| Vert. Momt increase, m-t | 516.6 |  |  |  |  |  |  |  |
| KG while lifting, m |  |  | 7.339 |  |  | Req Area = | 4.584 |  |
| KG before lifting, m |  |  | 7.074 |  |  | Area to max = | 4.584 |  |
| Pole height, m |  | 7.500 |  |  |  |  |  |  |
|  |  |  | 0.161 |  |  |  |  |  |
|  | Angle | GZ | GZ | Area |  | HZ | GZ-HZ | Area |
|  | 0 | 0 | 0.000 | 0.000 |  | 0.104 | -0.104 |  |
|  | 2 | 0.018 | 0.024 | 0.024 |  | 0.104 | -0.081 | 0.000 |
|  | 4 | 0.036 | 0.047 | 0.094 |  | 0.104 | -0.057 | 0.000 |
|  | 6 | 0.052 | 0.069 | 0.211 |  | 0.103 | -0.035 | 0.000 |
|  | 8 | 0.068 | 0.090 | 0.370 |  | 0.102 | -0.012 | 0.000 |
|  | 10 | 0.082 | 0.110 | 0.570 |  | 0.101 | 0.009 | 0.039 |
|  | 12 | 0.095 | 0.128 | 0.809 |  | 0.099 | 0.030 | 0.119 |
|  | 14 | 0.107 | 0.146 | 1.083 |  | 0.096 | 0.050 | 0.239 |
|  | 16 | 0.117 | 0.161 | 1.390 |  | 0.092 | 0.069 | 0.396 |
|  | 18 | 0.126 | 0.176 | 1.727 |  | 0.087 | 0.088 | 0.591 |
|  | 20 | 0.134 | 0.189 | 2.092 |  | 0.082 | 0.107 | 0.823 |
|  | 22 | 0.141 | 0.201 | 2.483 |  | 0.076 | 0.125 | 1.091 |
|  | 24 | 0.147 | 0.212 | 2.896 |  | 0.070 | 0.143 | 1.396 |
|  | 26 | 0.154 | 0.225 | 3.333 |  | 0.063 | 0.162 | 1.738 |
|  | 28 | 0.16 | 0.236 | 3.794 |  | 0.055 | 0.180 | 2.115 |
|  | 30 | 0.164 | 0.244 | 4.274 |  | 0.048 | 0.197 | 2.522 |
|  | 32 | 0.165 | 0.250 | 4.768 |  | 0.041 | 0.210 | 2.952 |
|  | 34 | 0.164 | 0.254 | 5.273 |  | 0.034 | 0.220 | 3.399 |
|  | 36 | 0.16 | 0.255 | 5.781 |  | 0.027 | 0.227 | 3.862 |
|  | 38 | 0.157 | 0.256 | 6.292 |  | 0.021 | 0.235 | 4.340 |
| Maximum GZ while lifting | 40 | 0.157 | 0.260 | 6.809 |  | 0.016 | 0.244 | 4.584 |

Lifting per 46 CFR 173.020(b)

| Draft, m | 5.4 |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Displ, mt | 2080.4 |  |  |  |  |  |  |  |
| Heeling moment, m-t | 203.4 |  |  |  |  |  |  |  |
| Vert. Momt increase, m-t | 516.6 |  |  |  |  |  |  |  |
| KG while lifting, m |  |  | 7.362 |  |  | Req Area = | 4.584 |  |
| KG before lifting, m |  |  | 7.114 |  |  | Area to max = | 5.147 |  |
| Pole height, m |  | 7.500 |  |  |  |  |  |  |
|  |  |  | 0.138 |  |  |  |  |  |
|  | Angle | GZ | GZ | Area |  | HZ | GZ-HZ | Area |
|  | 0 | 0.000 | 0.000 | 0.000 |  | 0.098 | -0.098 |  |
|  | 2 | 0.022 | 0.027 | 0.027 |  | 0.098 | -0.071 | 0.000 |
|  | 4 | 0.043 | 0.053 | 0.106 |  | 0.097 | -0.045 | 0.000 |
|  | 6 | 0.063 | 0.077 | 0.236 |  | 0.097 | -0.020 | 0.000 |
|  | 8 | 0.080 | 0.099 | 0.413 |  | 0.096 | 0.003 | 0.029 |
|  | 10 | 0.096 | 0.120 | 0.632 |  | 0.095 | 0.025 | 0.100 |
|  | 12 | 0.110 | 0.139 | 0.891 |  | 0.092 | 0.046 | 0.213 |
|  | 14 | 0.123 | 0.156 | 1.186 |  | 0.090 | 0.067 | 0.366 |
|  | 16 | 0.135 | 0.173 | 1.515 |  | 0.086 | 0.087 | 0.559 |
|  | 18 | 0.145 | 0.188 | 1.876 |  | 0.082 | 0.106 | 0.789 |
|  | 20 | 0.155 | 0.202 | 2.266 |  | 0.077 | 0.125 | 1.059 |
|  | 22 | 0.164 | 0.216 | 2.684 |  | 0.071 | 0.144 | 1.367 |
|  | 24 | 0.173 | 0.229 | 3.128 |  | 0.065 | 0.164 | 1.714 |
|  | 26 | 0.182 | 0.242 | 3.600 |  | 0.059 | 0.184 | 2.101 |
|  | 28 | 0.190 | 0.255 | 4.097 |  | 0.052 | 0.203 | 2.521 |
|  | 30 | 0.193 | 0.262 | 4.614 |  | 0.045 | 0.217 | 2.966 |
|  | 32 | 0.193 | 0.266 | 5.142 |  | 0.038 | 0.228 | 3.431 |
|  | 34 | 0.191 | 0.268 | 5.677 |  | 0.032 | 0.237 | 3.909 |
|  | 36 | 0.186 | 0.267 | 6.212 |  | 0.026 | 0.242 | 4.397 |
|  | 38 | 0.181 | 0.266 | 6.745 |  | 0.020 | 0.246 | 4.895 |
| Maximum GZ while lifting | 40 | 0.179 | 0.268 | 7.279 |  | 0.015 | 0.252 | 5.147 |

Lifting per 46 CFR 173.020(b)

| Draft, m | 5.6 |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Displ, mt | 2220.3 |  |  |  |  |  |  |  |
| Heeling moment, m-t | 203.4 |  |  |  |  |  |  |  |
| Vert. Momt increase, m-t | 516.6 |  |  |  |  |  |  |  |
| KG while lifting, m |  |  | 7.323 |  |  | Req Area = | 4.584 |  |
| KG before lifting, m |  |  | 7.090 |  |  | Area to max = | 4.590 |  |
| Pole height, m |  | 7.500 |  |  |  |  |  |  |
|  |  |  | 0.177 |  |  |  |  |  |
|  | Angle | GZ | GZ | Area |  | HZ | GZ-HZ | Area |
|  | 0 | 0.000 | 0.000 | 0.000 |  | 0.092 | -0.092 |  |
|  | 2 | 0.026 | 0.032 | 0.032 |  | 0.092 | -0.059 | 0.000 |
|  | 4 | 0.051 | 0.063 | 0.128 |  | 0.091 | -0.028 | 0.000 |
|  | 6 | 0.074 | 0.093 | 0.284 |  | 0.091 | 0.002 | 0.030 |
|  | 8 | 0.094 | 0.119 | 0.495 |  | 0.090 | 0.029 | 0.113 |
|  | 10 | 0.112 | 0.143 | 0.756 |  | 0.089 | 0.054 | 0.245 |
|  | 12 | 0.128 | 0.165 | 1.064 |  | 0.087 | 0.078 | 0.425 |
|  | 14 | 0.143 | 0.186 | 1.414 |  | 0.084 | 0.102 | 0.652 |
|  | 16 | 0.157 | 0.206 | 1.806 |  | 0.081 | 0.125 | 0.925 |
|  | 18 | 0.170 | 0.225 | 2.236 |  | 0.077 | 0.148 | 1.242 |
|  | 20 | 0.181 | 0.242 | 2.702 |  | 0.072 | 0.169 | 1.603 |
|  | 22 | 0.193 | 0.259 | 3.203 |  | 0.067 | 0.192 | 2.011 |
|  | 24 | 0.205 | 0.277 | 3.740 |  | 0.061 | 0.216 | 2.465 |
|  | 26 | 0.215 | 0.293 | 4.309 |  | 0.055 | 0.238 | 2.958 |
|  | 28 | 0.221 | 0.304 | 4.906 |  | 0.049 | 0.256 | 3.482 |
|  | 30 | 0.222 | 0.310 | 5.520 |  | 0.042 | 0.268 | 4.029 |
| Maximum GZ while lifting | 32 | 0.220 | 0.314 | 6.145 |  | 0.036 | 0.278 | 4.590 |
|  | 34 | 0.214 | 0.313 | 6.771 |  | 0.030 | 0.283 | 5.161 |
|  | 36 | 0.207 | 0.311 | 7.395 |  | 0.024 | 0.287 | 5.739 |
|  | 38 | 0.201 | 0.310 | 8.016 |  | 0.019 | 0.291 | 6.326 |
|  | 40 | 0.197 | 0.311 | 8.637 |  | 0.014 | 0.296 | 6.623 |

Lifting per 46 CFR 173.020(b)

| Draft, m | 5.8 |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Displ, mt | 2365.2 |  |  |  |  |  |  |  |
| Heeling moment, m-t | 203.4 |  |  |  |  |  |  |  |
| Vert. Momt increase, m-t | 516.6 |  |  |  |  |  |  |  |
| KG while lifting, m |  |  | 7.331 |  |  | Req Area = | 4.584 |  |
| KG before lifting, m |  |  | 7.113 |  |  | Area to max = | 5.173 |  |
| Pole height, m |  | 7.500 |  |  |  |  |  |  |
|  |  |  | 0.169 |  |  |  |  |  |
|  | Angle | GZ | GZ | Area |  | HZ | GZ-HZ | Area |
|  | 0 | 0.000 | 0.000 | 0.000 |  | 0.086 | -0.086 |  |
|  | 2 | 0.028 | 0.034 | 0.034 |  | 0.086 | -0.052 | 0.000 |
|  | 4 | 0.055 | 0.067 | 0.135 |  | 0.086 | -0.019 | 0.000 |
|  | 6 | 0.081 | 0.099 | 0.300 |  | 0.085 | 0.013 | 0.056 |
|  | 8 | 0.104 | 0.128 | 0.526 |  | 0.084 | 0.043 | 0.170 |
|  | 10 | 0.124 | 0.153 | 0.807 |  | 0.083 | 0.070 | 0.337 |
|  | 12 | 0.143 | 0.178 | 1.139 |  | 0.081 | 0.097 | 0.556 |
|  | 14 | 0.161 | 0.202 | 1.519 |  | 0.079 | 0.123 | 0.827 |
|  | 16 | 0.177 | 0.224 | 1.944 |  | 0.076 | 0.148 | 1.147 |
|  | 18 | 0.192 | 0.244 | 2.412 |  | 0.072 | 0.172 | 1.516 |
|  | 20 | 0.207 | 0.265 | 2.921 |  | 0.068 | 0.197 | 1.934 |
|  | 22 | 0.221 | 0.284 | 3.470 |  | 0.063 | 0.221 | 2.401 |
|  | 24 | 0.234 | 0.303 | 4.057 |  | 0.057 | 0.245 | 2.911 |
|  | 26 | 0.242 | 0.316 | 4.676 |  | 0.052 | 0.264 | 3.453 |
|  | 28 | 0.244 | 0.323 | 5.315 |  | 0.046 | 0.278 | 4.016 |
|  | 30 | 0.240 | 0.324 | 5.963 |  | 0.039 | 0.285 | 4.591 |
| Maximum GZ while lifting | 32 | 0.234 | 0.324 | 6.611 |  | 0.033 | 0.290 | 5.173 |
|  | 34 | 0.226 | 0.320 | 7.255 |  | 0.028 | 0.293 | 5.760 |
|  | 36 | 0.217 | 0.316 | 7.892 |  | 0.022 | 0.294 | 6.351 |
|  | 38 | 0.211 | 0.315 | 8.523 |  | 0.018 | 0.297 | 6.946 |
|  | 40 | 0.202 | 0.311 | 9.149 |  | 0.014 | 0.297 | 7.243 |

Lifting per 46 CFR 173.020(b)

| Draft, m | 6.0 |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Displ, mt | 2512.8 |  |  |  |  |  |  |  |
| Heeling moment, m-t | 203.4 |  |  |  |  |  |  |  |
| Vert. Momt increase, m-t | 516.6 |  |  |  |  |  |  |  |
| KG while lifting, m |  |  | 7.310 |  |  | Req Area = | 4.584 |  |
| KG before lifting, m |  |  | 7.104 |  |  | Area to max = | 4.588 |  |
| Pole height, m |  | 7.500 |  |  |  |  |  |  |
|  |  |  | 0.190 |  |  |  |  |  |
|  | Angle | GZ | GZ | Area |  | HZ | GZ-HZ | Area |
|  | 0 | 0.000 | 0.000 | 0.000 |  | 0.081 | -0.081 |  |
|  | 2 | 0.029 | 0.036 | 0.036 |  | 0.081 | -0.045 | 0.000 |
|  | 4 | 0.057 | 0.070 | 0.142 |  | 0.081 | -0.010 | 0.000 |
|  | 6 | 0.083 | 0.103 | 0.315 |  | 0.080 | 0.023 | 0.079 |
|  | 8 | 0.109 | 0.135 | 0.553 |  | 0.079 | 0.056 | 0.222 |
|  | 10 | 0.133 | 0.166 | 0.854 |  | 0.078 | 0.088 | 0.427 |
|  | 12 | 0.154 | 0.194 | 1.214 |  | 0.077 | 0.117 | 0.689 |
|  | 14 | 0.174 | 0.220 | 1.627 |  | 0.074 | 0.146 | 1.009 |
|  | 16 | 0.193 | 0.245 | 2.093 |  | 0.071 | 0.174 | 1.384 |
|  | 18 | 0.210 | 0.269 | 2.607 |  | 0.068 | 0.201 | 1.814 |
|  | 20 | 0.228 | 0.293 | 3.168 |  | 0.064 | 0.229 | 2.299 |
|  | 22 | 0.244 | 0.315 | 3.777 |  | 0.059 | 0.256 | 2.832 |
|  | 24 | 0.254 | 0.331 | 4.423 |  | 0.054 | 0.277 | 3.399 |
|  | 26 | 0.255 | 0.338 | 5.093 |  | 0.049 | 0.290 | 3.987 |
| Maximum GZ while lifting | 28 | 0.252 | 0.341 | 5.772 |  | 0.043 | 0.298 | 4.588 |
|  | 30 | 0.245 | 0.340 | 6.453 |  | 0.037 | 0.303 | 5.195 |
|  | 32 | 0.235 | 0.336 | 7.129 |  | 0.032 | 0.304 | 5.803 |
|  | 34 | 0.224 | 0.330 | 7.795 |  | 0.026 | 0.304 | 6.413 |
|  | 36 | 0.215 | 0.327 | 8.452 |  | 0.021 | 0.306 | 7.026 |
|  | 38 | 0.207 | 0.324 | 9.102 |  | 0.017 | 0.307 | 7.634 |
|  | 40 | 0.192 | 0.314 | 9.740 |  | 0.013 | 0.301 | 7.936 |

Lifting per 46 CFR 173.020(b)

| Draft, m | 6.2 |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Displ, mt | 2662.7 |  |  |  |  |  |  |  |
| Heeling moment, m-t | 203.4 |  |  |  |  |  |  |  |
| Vert. Momt increase, m-t | 516.6 |  |  |  |  |  |  |  |
| KG while lifting, m |  |  | 7.254 |  |  | Req Area = | 4.584 |  |
| KG before lifting, m |  |  | 7.060 |  |  | Area to max = | 4.588 |  |
| Pole height, m |  | 7.500 |  |  |  |  |  |  |
|  |  |  | 0.246 |  |  |  |  |  |
|  | Angle | GZ | GZ | Area |  | HZ | GZ-HZ | Area |
|  | 0 | 0.000 | 0.000 | 0.000 |  | 0.076 | -0.076 |  |
|  | 2 | 0.029 | 0.038 | 0.038 |  | 0.076 | -0.039 | 0.000 |
|  | 4 | 0.057 | 0.074 | 0.149 |  | 0.076 | -0.002 | 0.000 |
|  | 6 | 0.085 | 0.111 | 0.334 |  | 0.076 | 0.035 | 0.105 |
|  | 8 | 0.111 | 0.145 | 0.590 |  | 0.075 | 0.070 | 0.281 |
|  | 10 | 0.137 | 0.180 | 0.915 |  | 0.074 | 0.106 | 0.527 |
|  | 12 | 0.161 | 0.212 | 1.307 |  | 0.072 | 0.140 | 0.840 |
|  | 14 | 0.184 | 0.244 | 1.763 |  | 0.070 | 0.173 | 1.218 |
|  | 16 | 0.204 | 0.272 | 2.278 |  | 0.067 | 0.204 | 1.659 |
|  | 18 | 0.225 | 0.301 | 2.851 |  | 0.064 | 0.237 | 2.164 |
|  | 20 | 0.244 | 0.328 | 3.480 |  | 0.060 | 0.268 | 2.724 |
|  | 22 | 0.256 | 0.348 | 4.156 |  | 0.056 | 0.292 | 3.325 |
|  | 24 | 0.259 | 0.359 | 4.863 |  | 0.051 | 0.308 | 3.950 |
| Maximum GZ while lifting | 26 | 0.255 | 0.363 | 5.585 |  | 0.046 | 0.317 | 4.588 |
|  | 28 | 0.246 | 0.361 | 6.310 |  | 0.040 | 0.321 | 5.231 |
|  | 30 | 0.235 | 0.358 | 7.029 |  | 0.035 | 0.323 | 5.878 |
|  | 32 | 0.223 | 0.353 | 7.740 |  | 0.030 | 0.324 | 6.525 |
|  | 34 | 0.211 | 0.349 | 8.442 |  | 0.025 | 0.324 | 7.175 |
|  | 36 | 0.201 | 0.346 | 9.136 |  | 0.020 | 0.326 | 7.824 |
|  | 38 | 0.188 | 0.339 | 9.821 |  | 0.016 | 0.324 | 8.461 |
|  | 40 | 0.167 | 0.325 | 10.486 |  | 0.012 | 0.313 | 8.774 |

1.e.	Towline Pull Criterion

Towline pull was evaluated per the requirements of 46 CFR 173.095, as follows:

N, Number of propellers = 1

P, Power = 2,300 kW (installed motor power on propeller shaft)

D, Propeller diameter = 4.3 meters

s,  fraction of propeller circle cylinder covered by rudder when turned a t 	  		45 degrees, = 0.42,  (see attached sketch of approximate rudder 			geometry)

h, vertical distance from propeller shaft centerline to towing bit = 10.0 m

(the propeller shaft is approximately 2.2 meters above baseline.  			The tow point for the trawl cables is from blocks hung from the 			gallows.  The top of the gallows deck is 12.1 m above baseline.  			Distance from gallows deck to propeller centerline is 9.9 m, 				rounded to 10 meters.  This is conservative as the towing blocks will hang on the underside of this deck structure.

f, freeboard = 8.65 meters minus the draft

B, molded beam = 15.0 meters

The resulting maximum allowable KG is approximately 8.0 meters at the design draft.  The calculation is as follows:

| Towline Pull Calculation for GM per 46 CFR 173.095(b) |
| --- |
| Draft, m | Freeboard | Displ,mt | GM,m | KM, m | KG,m |
| 5.00 | 3.65 | 1829.4 | 0.31 | 7.94 | 7.63 |
| 5.10 | 3.55 | 1888.9 | 0.31 | 7.98 | 7.67 |
| 5.20 | 3.45 | 1950.9 | 0.31 | 8.03 | 7.72 |
| 5.30 | 3.35 | 2014.4 | 0.31 | 8.08 | 7.77 |
| 5.40 | 3.25 | 2080.4 | 0.31 | 8.14 | 7.83 |
| 5.50 | 3.15 | 2149.1 | 0.31 | 8.22 | 7.91 |
| 5.60 | 3.05 | 2220.3 | 0.31 | 8.26 | 7.95 |
| 5.70 | 2.95 | 2292.4 | 0.31 | 8.29 | 7.98 |
| 5.80 | 2.85 | 2365.2 | 0.31 | 8.30 | 7.99 |
| 5.90 | 2.75 | 2438.7 | 0.31 | 8.31 | 8.00 |
| 6.00 | 2.65 | 2512.8 | 0.31 | 8.32 | 8.01 |
| 6.10 | 2.55 | 2587.5 | 0.32 | 8.32 | 8.00 |
| 6.20 | 2.45 | 2662.7 | 0.32 | 8.32 | 8.00 |
| 6.30 | 2.35 | 2738.3 | 0.32 | 8.32 | 8.00 |
| 6.40 | 2.25 | 2814.3 | 0.33 | 8.31 | 7.98 |
| N = | 1 |  |  |  |  |
| P, kW = | 2300 |  |  |  |  |
| s = | 0.42 |  |  |  |  |
| h, m = | 10.00 |  |  |  |  |
| K = | 13.93 |  |  |  |  |
| B, m = | 15.00 |  |  |  |  |
| D, m = | 4.30 |  |  |  |  |

2.a.	Summary

Damage stability of FRV40-1 was evaluated per the USCG requirements of 46 CRF171.080 for “Z” type damage (one compartment damage).   Curves of maximum allowable KG were developed.  Since the Roll Stabilization Tank has a significant effect on stability, curves were developed to show the effect of dumping this tank.

Equalization of certain pairs of port and starboard of deep and double bottom tanks is required for certain conditions of damage.  Deep Tanks #2 P/S, Double Bottom Tank #3 P/S, and Double Bottom Tank #4 P/S must be cross connected.   Equalization of the double bottom tanks will be automatic.  Equalization of Deep Tanks #2 P/S must be manual as the location of the tank top makes automatic equalization impractical.

The overall limiting damage condition is flooding of the Accommodation, Stores, and Sewage Holding Tanks between frames 29 and 39.

2.b.	Damage Characteristics

As an Oceanographic Research Vessel, the FRV40 must comply with the requirements of a “Z” type vessel.   Longitudinal penetration is 3 meters plus 0.03L, where L is LBP.   The Length between perpendiculars was taken as the waterline length at the deepest operating draft in accordance with 46 CFR 170.055(I)(1).   The deepest operating draft is taken as the scantling draft of 6.2 m.  At this draft the waterline length is 60.93 m.  Therefore the longitudinal penetration is 4.83 m.

Transverse penetration is B/5.  The beam of the FRV40 is 15 m so that B/5 = 3.0 m.

Vertical penetration is unlimited, and there is no damage to any main transverse bulkheads.

Main transverse bulkheads are located as follows:

| Frame | m aft FP |
| --- | --- |
| 7 | 4.6 |
| 19 | 11.8 |
| 29 | 17.8 |
| 39 | 23.8 |
| 49 | 29.8 |
| 72 | 43.6 |
| 82 | 49.6 |

The margin line was taken as 7.6 cm below the main deck, throughout the vessels length.  Since the main deck is located at 8.65 m above baseline, and there is no sheer on the main deck, the margin line is located at 8.574 m above the baseline.

Heeling arms required by 46 CFR 171.080(f)(4) were calculated as follows:

Passenger heeling moment = 39 passengers x .075 t x 7.5 m = 21.9 m-t

Asymmetric passenger escape route heeling moment 		= 21.9 m-t

Launching of survival craft heeling moment =

Rescue boat = 2.17 t x  3.1 m 				=    6.7 m-t

Rescue boat davit = 2.90 t x 1.6 m = 			=    4.6 m-t

Passengers in boat = 11 x .075 t x 9 m =			=    7.4 m-t

Liferafts (4) = 4 x .19t x 2.0 m =				=    1.5 m-t

Passengers in liferafts = 28 x .075 t x 9 m = 		=  18.9 m-t

Total 								=  39.1 m-t

Wind pressure heeling moment (at 5.9 m draft)			= 67.2 m-t

The wind pressure heeling moment is the largest of these moments.  Details of the wind area and heeling calculation are given in the Intact Stability section.  Heeling arms at various drafts are given in the following table.

| Draft, m | Displ, m | Wind Moment, m-t | Heeling Arm, m |
| --- | --- | --- | --- |
| 5.2 | 1951.6 | 72.66 | 0.0372 |
| 5.4 | 2081.1 | 70.88 | 0.0341 |
| 5.6 | 2221.0 | 69.30 | 0.0312 |
| 5.8 | 2366.1 | 67.88 | 0.0287 |
| 6.0 | 2513.7 | 66.60 | 0.0265 |
| 6.2 | 2663.6 | 65.44 | 0.0246 |

2.c.	Results

Stability calculations were performed using SHCP.

The hull form and offsets used for this analysis are discussed in Appendix A.   The superstructure was not included in the hull form definition used for the damage analysis and no credit has been taken for buoyancy from the superstructure.   This analysis has used the General Arrangement of the FRV40-1 to define compartmentation.  It is assumed that all openings will be fitted with appropriate closures and that downflooding is not an issue.  Compartment descriptions are given in Part f of this Section.

For each damage zone curves of maximum allowable virtual KG versus draft were developed for the range of expected operating drafts.

# 2.d.	Effect of Dumping Roll Stabilization Tank

The Roll Stabilization Tank is located at the 02 Level between frames 22 –29.   A preliminary tank design indicates that tank level will range from 31 to 37 tons depending on the GM.  The moment of inertia of the tank is 478 m4.   The SOR requires that this tank be provided with a means to rapidly dump the water in the tank in order to reduce the free-surface in the event of an emergency (SOR Section 079c).  The SOR further requires that dump valves are to be controlled from the bridge and that they be large enough to empty the tank from the highest operating level in 15 minutes (SOR Section 565a).

Dumping of the Roll Stabilization Tank has a beneficial effect on stability by reducing displacement, reducing KG, and of reducing the free-surface.   This damage analysis has concluded that the dumping of the Roll Stabilization Tank is necessary for certain cases of damage in order for the vessel to meet the required criteria.   The effect on ship KG of dumping the roll tank is given in the following table, which assumes 37 t of water in the roll tank before dumping (the value used in the sample loading conditions) and a before dumping ship KG of 7.5 m.

| Draft, m | Change in Ship KG caused by dumping roll tank. m |
| --- | --- |
| 5.2 | -0.381 |
| 5.4 | -0.357 |
| 5.6 | -0.334 |
| 5.8 | -0.314 |
| 6.0 | -0.295 |
| 6.2 | -0.279 |

In cases where the roll tank must be dumped, the time period between when damage occurs and the dumping of the Roll Stabilization Tank has been completed has been treated as an “earlier stage of flooding”.  In this stage the requirements of 46 CFR  171.080(f)(7) and (8) must be met.

The maximum allowable KG was calculated for each draft.  This KG was then increased (based on the table above) to obtain a maximum allowable the KG before dumping the roll tank.     Also for each such condition the maximum allowable KG in order to meet the requirements of each “earlier stage of flooding” was determined.  For certain conditions the “earlier stage” KG was more limiting than the “before dumping” KG.

Since it is possible that the vessel may operate at times with the Roll Stabilization Tank empty (in fact this may be a requirement for heavy icing situations) maximum allowable KG curves were also developed for cases where the roll tank is not dumped.

Curves of maximum allowable virtual KG versus draft are given on the following pages.  Summaries of damage conditions at zero trim are given in Part g.

Details of the limiting damage condition (Zone D-4) and of damage to the machinery space (Zone F-1) are given in Parts i and j.

2.e.	Effect of Trim

The expected range of trim for this vessel is 1 meter of trim by the stern and 0.5 meter of trim by the bow.

A before damage condition with 1 meter of trim by the stern was evaluated for damage to Zone H (the after most compartment) and Zone F (the machinery space).

A before damage condition with 0.5 meter of trim by the bow was evaluated for damage to Zone D.  This was the most severe damage for the no trim condition.

Trim by the bow reduces the overall limiting KG of the vessel by about 0.13 meters.  Trim by the stern does not effect the overall limiting KG.  Although the limiting KG of the stern compartments is reduced, it is still above that of the forward compartments which determine the overall limiting KG for the vessel.

Summaries of the damage conditions with trim are given in Part h.

2.f.	Compartment Descriptions

Zone A

010 Forepeak fr  B –5       0 .95  -0.8    3.4  999999 999999 999999 999999

011 Forepeak fr  5- 7       0 .95   3.4    4.6   1.20  999999 999999 999999

020 Chain lkrfr  5- 7      +1 .95   3.4    4.6  999999  1.20  999999 999999

Zone B

100 DT #1F S fr  7 –13     +1 .95   4.6    8.2  999999 999999 999999  6.15

110 DT #1F P fr   7-13     -1 .95   4.6    8.2  999999 999999 999999  6.15

120 DT #1A S fr  13-15     +1 .95   8.2    9.4   1.667 999999 999999  6.15

121 DT #1A S fr  13-17     +1 .95   9.4   10.6   2.00  999999 999999  6.15

122 DT #1A S fr  17-19     +1 .95  10.6   11.8   2.333 999999 999999  6.15

140 Bow thrstr   13-15      0 .85   8.2    9.4  999999  1.667 999999  6.15

141 Bow thrstr   15-17      0 .85   9.4   10.6  999999  2.00  999999  6.15

142 Bow thrstr   17-19      0 .85  10.6   11.8  999999  2.333 999999  6.15

150 Laundry       7-19     +1 .95   4.6   11.8   1.0   999999  6.15  999999

160 Stores        7-19     +1 .60   4.6   11.8  999999  1.0    6.15  999999

161 Stores        7-19     -1 .60   4.6   11.8  999999 999999  6.15  999999

Zone C

300 DT #2S   fr 19-29      +1 .95  11.8   17.8   2.50  999999 999999  6.15

310 DT #2P   fr 19-29      -1 .95  11.8   17.8   2.50  999999 999999  6.15

320 DT #2CL  fr 19-23       0 .95  11.8   14.2  999999  2.50  999999  6.15

330 Trans Rm fr 23-29       0 .95  14.2   17.8  999999  2.50  999999  6.15

340 Accomd   fr 19-29       0 .95  11.8   17.8  999999 999999  6.15  999999

Zone D

300 DB #3S   fr 29-39       1 .95  17.8   23.8   2.50  999999 999999  3.65

310 DB #3P   fr 29-39      -1 .95  17.8   23.8   2.50  999999 999999  3.65

320 Stores   fr 29-39      +1 .60  17.8   23.8   2.50  999999  3.65   6.15

330 Access   fr 37-39 S    +1 .95  22.6   23.8  999999  2.50   3.65   6.15

331 Access   fr 34-39 P    -1 .95  20.8   23.8   1.40  999999  3.65   6.15

340 Sewage tr rm fr 34-39  -1 .85  20.8   23.8   1.40  999999  3.65   6.15

350 Void fr 29-34          -1 .95  17.8   20.8   2.50   3.00   3.65   6.15

360 Sewage Hld tk fr29-34  -1 .95  17.8   20.8   3.00  999999  3.65   6.15

370 Accom fr 29-39          0 .95  17.8   23.8  999999 999999  6.15 999999

Zone E

400 DB #4S   fr 39-49       1 .95  23.8   29.8   2.50  999999 999999  3.65

410 DB #4P   fr 39-49      -1 .95  23.8   29.8   2.50  999999 999999  3.65

420 Aux machy rm fr 39-45   0 .85  23.8   27.4   0.50  999999  3.65   6.15

421 Aux machy rm fr 45-49   0 .85  27.4   29.8  999999 999999  3.65   6.15

430 Accomd       fr 39-45   0 .95  23.8   27.4   0.50  999999  6.15  999999

431 Accomd       fr 45-49   0 .95  27.4   29.8  999999 999999  6.15  999999

Zone F

450 Machy Rm fr 49-72       0 .85  29.8   43.6   2.50  999999 999999   1.0

451 Machy Rm fr 49-72       0 .85  29.8   43.6  999999 999999  1.0    3.65

452 Machy Rm fr 49-69.5     0 .85  29.8   42.1  999999 999999  3.65  999999

453 Machy Rm fr 69.5-72     0 .85  42.1   43.6  999999  5.50   3.65  999999

454 Recess 2nd dk 69-72S   +1-.85  42.25  43.6  999999  1.50   6.15  999999

455 Recess 2nd dk 69-72P   -1-.85  42.25  43.6  999999  1.80   6.15  999999

456 Recess shaft alley      0 .85  43.6   45.4  999999  1.15   1.00    4.0

460 Fuel Day Tk P          +1 .95  42.1   43.6   5.50  999999  3.65  999999

470 Machy DB                0 .95  29.8   43.6  999999  2.50  999999   1.0

Zone G

500 DT #65 S fr 72-82       1 .95  43.6   49.6   2.50  999999 999999  6.15

501 DT #65 P fr 72-82      -1 .95  43.6   49.6   2.50  999999 999999  6.15

520 Winch rm fr 72-82       0 .85  43.6   49.6  999999 999999  6.15  999999

454 Recess 2nd dk 69-72S   +1 .95  42.25  43.6  999999  1.50   6.15  999999

455 Recess 2nd dk 69-72P   -1 .95  42.25  43.6  999999  1.80   6.15  999999

Zone H

600 DT #6F S fr 82-91       1 .95  49.6   55.0   2.25  999999 999999  6.15

601 DT #6F P fr 82-91      -1 .95  49.6   55.0   2.25  999999 999999  6.15

610 DT #6A S fr 91-101      1 .95  49.6   55.0   2.00  999999 999999  6.15

611 DT #6A P fr 91 101     -1 .95  49.6   55.0   2.00  999999 999999  6.15

620 Trawl rm fr 82-101      0 .85  49.6   60.3  999999 999999  6.15  999999

2.g.	Damage Condition Summaries (No Trim)

Stem - Frame 7 (Zone A)

Summary

Condition A comprises flooding of the Forepeak and Chain Locker.  This is not a significant damage condition and no special measures are required.

| Draft | A-1 |
| --- | --- |
| 5.2 | 7.51 |
| 5.4 | 7.58 |
| 5.6 | 7.67 |
| 5.8 | 7.75 |
| 6.0 | 7.81 |
| 6.2 | 7.86 |

Cond A-1:	Forepeak Tank, CL, perm = 0.95 (010, 011)

Chain locker, S, perm = 0.95

| Draft | Trim | KG-eq | KG-range | KG-min GZ | KG-min Area | KG-min abv HZ | KG-ML | Limiting KG |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 5.2 | 0.0 | 7.95 | 7.90 | 7.51 | 7.70 | 7.59 | 7.94 | 7.51 |
| 5.4 | 0.0 | 8.04 | 8.00 | 7.58 | 7.74 | 7.68 | 7.90 | 7.58 |
| 5.6 | 0.0 | 8.15 | 8.04 | 7.67 | 7.84 | 7.78 | 7.99 | 7.67 |
| 5.8 | 0.0 | 8.23 | 8.20 | 7.74 | 7.92 | 7.87 | 8.08 | 7.74 |
| 6.0 | 0.0 | 8.27 | 8.18 | 7.81 | 8.00 | 7.94 | 8.16 | 7.81 |
| 6.2 | 0.0 | 8.29 | 8.24 | 7.85 | 8.01 | 7.99 | 8.22 | 7.85 |

Frames 7 -19 (Zone B)

Summary

Zone B includes the forward and aft pairs of Deep Tank # 1 and the Bow Thruster Compartment as well as the Laundry / Bosun’s Stores space located on the 2nd deck.  The most severe case is damage to both deep tanks (starboard side only)

| Draft | B-1 | B-2 | B-3 | B-4 | B-5 |
| --- | --- | --- | --- | --- | --- |
| 5.2 | 7.44 | 7.50 |  | 7.41 | 7.52 |
| 5.4 | 7.50 | 7.58 |  | 7.48 | 7.59 |
| 5.6 | 7.61 | 7.67 |  | 7.56 | 7.66 |
| 5.8 | 7.70 | 7.75 |  | 7.64 | 7.73 |
| 6.0 | 7.78 | 7.82 |  | 7.70 | 7.77 |
| 6.2 | 7.84 | 7.87 |  | 7.74 | 7.80 |

Cond B-1:	DT #1F, S, perm = 0.95 (100)

DT #1A, S, perm = 0.95 (120,121,122)

| Draft | Trim | KG-eq | KG-range | KG-min GZ | KG-min Area | KG-min abv HZ | KG-ML | Limiting KG |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 5.2 | 0.0 | 7.61 | 7.60 | 7.44 | 7.50 | 7.52 | 7.58 | 7.44 |
| 5.4 | 0.0 | 7.70 | 7.50 | 7.51 | 7.50 | 7.61 | 7.83 | 7.50 |
| 5.6 | 0.0 | 7.84 | 7.84 | 7.61 | 7.70 | 7.71 | 7.92 | 7.61 |
| 5.8 | 0.0 | 7.95 | 7.98 | 7.70 | 7.80 | 7.81 | 8.01 | 7.70 |
| 6.0 | 0.0 | 8.03 | 8.05 | 7.78 | 7.84 | 7.89 | 8.09 | 7.78 |
| 6.2 | 0.0 | 8.07 | 8.08 | 7.84 | 7.90 | 7.95 | 8.15 | 7.84 |

Cond B-2:	DT #1F, S, perm = 0.95 (100)

DT #1A, S, perm = 0.95 (120,121,122)

Bow thruster room, CL, perm = 0.85 (140,141,142)

| Draft | Trim | KG-eq | KG-range | KG-min GZ | KG-min Area | KG-min abv HZ | KG-ML | Limiting KG |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 5.2 | 0.0 | 7.55 | 7.80 | 7.52 | 7.50 | 7.61 | 7.79 | 7.50 |
| 5.4 | 0.0 | 7.65 | 7.80 | 7.58 | 7.60 | 7.68 | 7.86 | 7.58 |
| 5.6 | 0.0 | 7.80 | 7.92 | 7.67 | 7.70 | 7.77 | 7.96 | 7.67 |
| 5.8 | 0.0 | 7.94 | 7.99 | 7.75 | 7.80 | 7.86 | 8.05 | 7.75 |
| 6.0 | 0.0 | 8.05 | 8.11 | 7.82 | 7.90 | 7.93 | 8.14 | 7.82 |
| 6.2 | 0.0 | 8.12 | 8.11 | 7.87 | 7.94 | 7.99 | 8.20 | 7.87 |

Cond B-3:	DT #1F, S, perm = 0.95 (100)

DT #1A, S, perm = 0.95 (120,121,122)

Laundry, P, perm = 0.95 (150)

Stores, S, perm = 0.60 (160,161)

| Draft | Trim | KG-eq | KG-range | KG-min GZ | KG-min Area | KG-min abv HZ | KG-ML | Limiting KG |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 5.2 | 0.0 | 7.61 | 7.64 | 7.39 | 7.45 | 7.47 | 7.70 | 7.39 |
| 5.4 | 0.0 | 7.70 | 7.75 | 7.46 | 7.52 | 7.54 | 7.77 | 7.46 |
| 5.6 | 0.0 | 7.82 | 7.86 | 7.54 | 7.62 | 7.64 | 7.86 | 7.54 |
| 5.8 | 0.0 | 7.91 | 7.89 | 7.62 | 7.70 | 7.73 | 7.94 | 7.62 |
| 6.0 | 0.0 | 7.96 | 7.98 | 7.69 | 7.80 | 7.81 | 8.01 | 7.69 |
| 6.2 | 0.0 | 7.99 | 7.97 | 7.74 | 7.80 | 7.85 | 8.07 | 7.74 |

Cond B-4:	DT #1F, S, perm = 0.95 (100)

DT #1A, S, perm = 0.95 (120,121,122)

Bow thruster room, CL, perm = 0.85 (140,141,142)

Laundry, P, perm = 0.95 (150)

Stores, S, perm = 0.60 (160,161)

| Draft | Trim | KG-eq | KG-range | KG-min GZ | KG-min Area | KG-min abv HZ | KG-ML | Limiting KG |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 5.2 | 0.0 | 7.52 | 7.58 | 7.41 | 7.41 | 7.50 | 7.70 | 7.41 |
| 5.4 | 0.0 | 7.59 | 7.71 | 7.48 | 7.50 | 7.57 | 7.77 | 7.48 |
| 5.6 | 0.0 | 7.71 | 7.79 | 7.56 | 7.60 | 7.66 | 7.86 | 7.56 |
| 5.8 | 0.0 | 7.83 | 7.93 | 7.64 | 7.70 | 7.74 | 7.94 | 7.64 |
| 6.0 | 0.0 | 7.93 | 7.93 | 7.70 | 7.80 | 7.81 | 8.02 | 7.70 |
| 6.2 | 0.0 | 7.99 | 7.95 | 7.74 | 7.80 | 7.85 | 8.08 | 7.74 |

Cond B-5:	Laundry, P, perm = 0.95 (150)

Stores, S, perm = 0.60 (160,161)

| Draft | Trim | KG-eq | KG-range | KG-min GZ | KG-min Area | KG-min abv HZ | KG-ML | Limiting KG |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 5.2 | 0.0 | - | 7.90 | 7.52 | 7.70 | 7.61 | 7.70 | 7.52 |
| 5.4 | 0.0 | - | 7.97 | 7.59 | 7.76 | 7.69 | 7.77 | 7.59 |
| 5.6 | 0.0 | - | 8.04 | 7.66 | 7.84 | 7.78 | 7.86 | 7.66 |
| 5.8 | 0.0 | - | 8.22 | 7.73 | 7.90 | 7.85 | 7.94 | 7.73 |
| 6.0 | 0.0 | - | 8.15 | 7.77 | 7.94 | 7.90 | 8.02 | 7.77 |
| 6.2 | 0.0 | 8.26 | 8.24 | 7.80 | 7.96 | 7.94 | 8.08 | 7.80 |

Frames 19 – 29 (Zone C)

Summary

Condition C includes Deep Tanks #2 P/S and CL, the Transducer Room, and the Accommodations over these spaces.   Deep Tanks # 2 P/S must be cross connected.  Since the top of these tanks is above the waterline, cross connection can not be automatic.  Cross connection will be manual, with the valve located on the main deck in the mess-room.  The Roll Stabilization Tank must be dumped when damage occurs to the Deep Tanks.

Roll Tank Dumped

| Draft | C-1 | C-2 | C-3 | C-4 | C-5 |
| --- | --- | --- | --- | --- | --- |
| 5.2 | 7.50 | 7.58 | 7.36 | 7.40 | 7.48 |
| 5.4 | 7.60 | 7.72 | 7.42 | 7.48 | 7.53 |
| 5.6 | 7.69 | 7.82 | 7.49 | 7.54 | 7.59 |
| 5.8 | 7.76 | 7.89 | 7.56 | 7.59 | 7.64 |
| 6.0 | 7.82 | 7.94 | 7.61 | 7.64 | 7.67 |
| 6.2 | 7.87 | 7.98 | 7.64 | 7.66 | 7.69 |

Roll Tank Not Dumped

| Draft | C-1 | C-2 | C-3 | C-4 | C-5 |
| --- | --- | --- | --- | --- | --- |
| 5.2 | 7.43 | 7.62 | 7.29 | 7.39 | - |
| 5.4 | 7.51 | 7.71 | 7.36 | 7.45 | - |
| 5.6 | 7.63 | 7.83 | 7.45 | 7.55 | - |
| 5.8 | 7.74 | 7.95 | 7.54 | 7.66 | - |
| 6.0 | 7.83 | 8.05 | 7.62 | 7.74 | - |
| 6.2 | 7.90 | 8.11 | 7.68 | 7.80 | - |

Cond C-1:	DT #2 P/S, perm = 0.95 (200)

|  | Limiting KG -before dump |
| --- | --- |
| Draft | Trim | KG-eq | KG-range | KG-min GZ | KG-min Area | KG-min abv HZ | KG-ML | without dump | with dump | Earlier KG* |
| 5.2 | 0.0 | - | 7.70 | 7.43 | 7.60 | 7.51 | 7.78 | 7.43 | 7.81 | 7.50 |
| 5.4 | 0.0 | - | 7.86 | 7.51 | 7.70 | 7.61 | 7.88 | 7.51 | 7.87 | 7.60 |
| 5.6 | 0.0 | - | 8.01 | 7.63 | 7.80 | 7.74 | 7.99 | 7.63 | 7.96 | 7.69 |
| 5.8 | 0.0 | - | 8.12 | 7.74 | 7.91 | 7.86 | 8.10 | 7.74 | 8.05 | 7.76 |
| 6.0 | 0.0 | - | 8.21 | 7.83 | 8.00 | 7.96 | 8.20 | 7.83 | 8.13 | 7.82 |
| 6.2 | 0.0 | - | 8.29 | 7.90 | 8.10 | 8.04 | 8.28 | 7.90 | 8.18 | 7.87 |

- Earlier KG for this condition is before cross flooding Deep Tanks #2 P/S and before Roll Stabilization Tank is dumped.

Cond C-2:	DT #2P/S, perm = 0.95 (200)

DT #2C, perm = 0.95 (220)

Transducer Room, perm = 0.95 (230)

Note: Equalization is not required for this condition but will occur as 			          equalization is automatic.

|  | Limiting KG -before dump |
| --- | --- |
| Draft | Trim | KG-eq | KG-range | KG-min GZ | KG-min Area | KG-min abv HZ | KG-ML | without dump | with dump | Earlier KG* |
| 5.2 | 0.0 | - | 8.04 | 7.62 | 7.80 | 7.71 | 8.02 | 7.62 | 8.00 | 7.58 |
| 5.4 | 0.0 | - | 8.12 | 7.71 | 7.90 | 7.81 | 8.10 | 7.71 | 8.07 | 7.72 |
| 5.6 | 0.0 | - | 8.22 | 7.83 | 8.00 | 7.94 | 8.22 | 7.83 | 8.16 | 7.82 |
| 5.8 | 0.0 | - | 8.33 | 7.95 | 8.10 | 8.07 | 8.33 | 7.95 | 8.26 | 7.89 |
| 6.0 | 0.0 | - | 8.42 | 8.05 | 8.20 | 8.17 | 8.44 | 8.05 | 8.35 | 7.94 |
| 6.2 | 0.0 | - | 8.51 | 8.11 | 8.22 | 8.25 | 8.53 | 8.11 | 8.39 | 7.98 |

- Earlier KG for this condition is before cross flooding Deep Tanks #2 P/S and before Roll Stabilization Tank is dumped.

Cond C-3	DT #2P/S, perm = 0.95 (200)

Accommodations, perm = 0.95 (230)

|  | Limiting KG -before dump |
| --- | --- |
| Draft | Trim | KG-eq | KG-range | KG-min GZ | KG-min Area | KG-min abv HZ | KG-ML | without dump | with dump | Earlier KG* |
| 5.2 | 0.0 | - | 7.70 | 7.29 | 7.45 | 7.38 | 7.63 | 7.29 | 7.67 | 7.36 |
| 5.4 | 0.0 | - | 7.74 | 7.36 | 7.53 | 7.46 | 7.71 | 7.36 | 7.72 | 7.42 |
| 5.6 | 0.0 | - | 7.85 | 7.45 | 7.62 | 7.56 | 7.81 | 7.45 | 7.78 | 7.49 |
| 5.8 | 0.0 | - | 8.00 | 7.54 | 7.71 | 7.66 | 7.91 | 7.54 | 7.85 | 7.56 |
| 6.0 | 0.0 | - | 8.00 | 7.62 | 7.80 | 7.75 | 7.99 | 7.62 | 7.92 | 7.61 |
| 6.2 | 0.0 | - | 8.11 | 7.68 | 7.82 | 7.81 | 8.07 | 7.68 | 7.96 | 7.64 |

- Earlier KG for this condition is before cross flooding Deep Tanks #2 P/S and before Roll Stabilization Tank is dumped.

Cond C-4	DT #2S, perm = 0.95 (200)

DT #2C, perm = 0.95 (220)

Transducer Room, perm = 0.95 (230)

Accommodations, perm = 0.95 (230)

|  | Limiting KG -before dump |
| --- | --- |
| Draft | Trim | KG-eq | KG-range | KG-min GZ | KG-min Area | KG-min abv HZ | KG-ML | without dump | with dump | Earlier KG* |
| 5.2 | 0.0 | - | 7.78 | 7.39 | 7.55 | 7.48 | 7.78 | 7.39 | 7.77 | 7.40 |
| 5.4 | 0.0 | - | 7.82 | 7.45 | 7.61 | 7.55 | 7.85 | 7.45 | 7.81 | 7.48 |
| 5.6 | 0.0 | - | 7.93 | 7.55 | 7.70 | 7.67 | 7.94 | 7.55 | 7.88 | 7.54 |
| 5.8 | 0.0 | - | 8.03 | 7.66 | 7.80 | 7.78 | 8.05 | 7.66 | 7.97 | 7.59 |
| 6.0 | 0.0 | - | 8.11 | 7.74 | 7.90 | 7.87 | 8.15 | 7.74 | 8.04 | 7.64 |
| 6.2 | 0.0 | - | 8.20 | 7.80 | 7.91 | 7.94 | 8.25 | 7.80 | 8.08 | 7.66 |

- Earlier KG for this condition is before cross flooding Deep Tanks #2 P/S and before Roll Stabilization Tank is dumped.

Cond C-5	Accommodations, perm = 0.95 (230)

| Draft | Trim | KG-eq | KG-range | KG-min GZ | KG-min Area | KG-min abv HZ | KG-ML | Limiting KG |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 5.2 | 0.0 | - | 7.86 | 7.48 | 7.65 | 7.57 | 7.71 | 7.48 |
| 5.4 | 0.0 | - | 7.90 | 7.53 | 7.70 | 7.63 | 7.77 | 7.53 |
| 5.6 | 0.0 | - | 8.00 | 7.59 | 7.80 | 7.70 | 7.86 | 7.59 |
| 5.8 | 0.0 | - | 8.02 | 7.64 | 7.82 | 7.76 | 8.21 | 7.64 |
| 6.0 | 0.0 | - | 8.05 | 7.67 | 7.84 | 7.80 | 8.01 | 7.67 |
| 6.2 | 0.0 | - | 8.11 | 7.69 | 7.84 | 7.82 | 8.05 | 7.69 |

Frames 29 – 39 (Zone D)

Summary

Condition D includes Double Bottom Tanks #3 P/S, the Stores space, Sewage Treatment Room, and Sewage Holding Tank located above the tank top, and the Accommodations located above these spaces.  Double Bottom Tank #3 CL and the Fresh Water Tanks are not damaged as they are located inboard of B/5.  Cross-flooding of DB #3 P/S is required, and can be automatic as top of tank is well below waterline.   The Roll Stabilization Tank must be dumped for any damage in this zone other than to just the Deep Tank.

Condition D-4 is the overall limiting stability condition for the FRV40-1.  There is the potential that the allowable KG for this condition could be increased, if necessary by relocating the Sewage Holding Tank.

Roll Tank Dumped

| Draft | D-1 | D-2 | D-3 | D-4 | D-5 |
| --- | --- | --- | --- | --- | --- |
| 5.2 | 7.69 | 7.38 | 7.42 | 7.28 | 7.42 |
| 5.4 | 7.76 | 7.45 | 7.50 | 7.32 | 7.47 |
| 5.6 | 7.84 | 7.53 | 7.58 | 7.43 | 7.53 |
| 5.8 | 7.91 | 7.61 | 7.65 | 7.51 | 7.60 |
| 6.0 | 7.97 | 7.67 | 7.71 | 7.58 | 7.64 |
| 6.2 | 8.01 | 7.71 | 7.76 | 7.63 | 7.68 |

Roll Tank Not Dumped

| Draft | D-1 | D-2 | D-3 | D-4 | D-5 |
| --- | --- | --- | --- | --- | --- |
| 5.2 |  | 7.20 | 7.25 | 7.07 | 7.25 |
| 5.4 |  | 7.30 | 7.32 | 6.96 | 7.29 |
| 5.6 |  | 7.39 | 7.42 | 7.24 | 7.36 |
| 5.8 |  | 7.47 | 7.50 | 7.34 | 7.42 |
| 6.0 |  | 7.52 | 7.56 | 7.42 | 7.48 |
| 6.2 |  | 7.54 | 7.59 | 7.47 | 7.52 |

Cond D-1:	DB #3 P/S, perm = 0.95 (300)

| Draft | Trim | KG-eq | KG-range | KG-min GZ | KG-min Area | KG-min abv HZ | KG-ML | Limiting KG |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 5.2 | 0.0 | - | 8.09 | 7.69 | 7.85 | 7.78 | 7.98 | 7.69 |
| 5.4 | 0.0 | - | 8.21 | 7.76 | 7.93 | 7.86 | 8.08 | 7.76 |
| 5.6 | 0.0 | - | 8.23 | 7.84 | 8.01 | 7.95 | 8.18 | 7.84 |
| 5.8 | 0.0 | - | 8.34 | 7.91 | 8.10 | 8.03 | 8.26 | 7.91 |
| 6.0 | 0.0 | - | 8.35 | 7.97 | 8.13 | 8.10 | 8.33 | 7.97 |
| 6.2 | 0.0 | - | 8.41 | 8.01 | 8.20 | 8.15 | 8.39 | 8.01 |

Cond D-2:	DB #3 P/S, perm = 0.95 (300)

Stores, tank top S, perm = 0.60 (320)

Access, tank top CL, perm = 0.95 (330, 331)

Sewage Treatment Room, tank top P, perm = 0.85 (340)

Void, tank top P, perm = 0.95 (350)

Accommodations, 2nd deck, perm = 0.95 (370)

|  | Limiting KG -before dump |
| --- | --- |
| Draft | Trim | KG-eq | KG-range | KG-min GZ | KG-min Area | KG-min abv HZ | KG-ML | without dump | with dump | Earlier KG* |
| 5.2 | 0.0 | 7.23 | 7.43 | 7.23 | 7.20 | 7.30 | 7.50 | 7.20 | 7.58 | 7.38 |
| 5.4 | 0.0 | 7.31 | 7.50 | 7.31 | 7.30 | 7.38 | 7.58 | 7.30 | 7.66 | 7.45 |
| 5.6 | 0.0 | 7.43 | 7.58 | 7.39 | 7.40 | 7.47 | 7.67 | 7.39 | 7.72 | 7.53 |
| 5.8 | 0.0 | 7.53 | 7.65 | 7.47 | 7.50 | 7.56 | 7.75 | 7.47 | 7.78 | 7.61 |
| 6.0 | 0.0 | 7.60 | 7.69 | 7.52 | 7.54 | 7.62 | 7.81 | 7.52 | 7.82 | 7.67 |
| 6.2 | 0.0 | 7.66 | 7.70 | 7.54 | 7.60 | 7.66 | 7.86 | 7.54 | 7.82 | 7.71 |

- Earlier KG for this condition is before Roll Stabilization Tank is dumped.

Cond D-3:	DB #3 P/S, perm = 0.95 (310)

Stores, tank top S, perm = 0.60 (320)

Access, tank top CL, perm = 0.95 (330, 331)

Sewage Treatment Room, tank top P, perm = 0.85 (340)

Void, tank top P, perm = 0.95 (350)

Sewage Tank, tank top, perm = 0.95

Accommodations, 2nd deck, perm = 0.95 (370)

|  | Limiting KG -before dump |
| --- | --- |
| Draft | Trim | KG-eq | KG-range | KG-min GZ | KG-min Area | KG-min abv HZ | KG-ML | without dump | with dump | Earlier KG* |
| 5.2 | 0.0 | 7.40 | 7.51 | 7.25 | 7.30 | 7.33 | 7.26 | 7.25 | 7.63 | 7.42 |
| 5.4 | 0.0 | 7.48 | 7.57 | 7.32 | 7.35 | 7.42 | 7.32 | 7.32 | 7.68 | 7.50 |
| 5.6 | 0.0 | 7.58 | 7.71 | 7.42 | 7.45 | 7.51 | 7.41 | 7.42 | 7.75 | 7.58 |
| 5.8 | 0.0 | 7.67 | 7.73 | 7.50 | 7.54 | 7.60 | 7.49 | 7.50 | 7.81 | 7.65 |
| 6.0 | 0.0 | 7.74 | 7.80 | 7.56 | 7.60 | 7.66 | 7.56 | 7.56 | 7.86 | 7.71 |
| 6.2 | 0.0 | 7.79 | 7.78 | 7.59 | 7.64 | 7.71 | 7.60 | 7.59 | 7.87 | 7.76 |

- Earlier KG for this condition is before Roll Stabilization Tank is dumped.

Cond D-4:	Stores, tank top S, perm = 0.60 (320)

Access, tank top CL, perm = 0.95 (330, 331)

Sewage Treatment Room, tank top P, perm = 0.85 (340)

Void, tank top P, perm = 0.95 (350)

Sewage Tank, tank top, perm = 0.95

Accommodations, 2nd deck, perm = 0.95 (370)

(DB tanks not damaged)

|  | Limiting KG -before dump |
| --- | --- |
| Draft | Trim | KG-eq | KG-range | KG-min GZ | KG-min Area | KG-min abv HZ | KG-ML | without dump | with dump | Earlier KG* |
| 5.2 | 0.0 | 7.30 | 7.31 | 7.07 | 7.13 | 7.15 | 7.40 | 7.07 | 7.45 | 7.28 |
| 5.4 | 0.0 | 7.38 | 6.96 | 7.12 | 7.01 | 7.22 | 7.04 | 6.96 | 7.32 | 7.32 |
| 5.6 | 0.0 | 7.50 | 7.54 | 7.24 | 7.31 | 7.34 | 7.56 | 7.24 | 7.57 | 7.43 |
| 5.8 | 0.0 | 7.58 | 7.63 | 7.34 | 7.40 | 7.44 | 7.65 | 7.34 | 7.65 | 7.51 |
| 6.0 | 0.0 | 7.63 | 7.70 | 7.42 | 7.50 | 7.53 | 7.73 | 7.42 | 7.72 | 7.58 |
| 6.2 | 0.0 | 7.66 | 7.71 | 7.47 | 7.52 | 7.58 | 7.79 | 7.47 | 7.75 | 7.63 |

- Earlier KG for this condition is before Roll Stabilization Tank is dumped.

Cond D-5:	Sewage Tank, P tank top, perm = 0.95

Accommodations, 2nd deck, perm = 0.95 (370)

|  | Limiting KG -before dump |
| --- | --- |
| Draft | Trim | KG-eq | KG-range | KG-min GZ | KG-min Area | KG-min abv HZ | KG-ML | without dump | with dump | Earlier KG* |
| 5.2 | 0.0 | 7.59 | 7.60 | 7.25 | 7.35 | 7.33 | 7.53 | 7.25 | 7.63 | 7.42 |
| 5.4 | 0.0 | 7.65 | 7.60 | 7.29 | 7.40 | 7.38 | 7.59 | 7.29 | 7.65 | 7.47 |
| 5.6 | 0.0 | 7.72 | 7.70 | 7.36 | 7.50 | 7.46 | 7.67 | 7.36 | 7.69 | 7.53 |
| 5.8 | 0.0 | 7.74 | 7.73 | 7.42 | 7.51 | 7.53 | 7.74 | 7.42 | 7.73 | 7.60 |
| 6.0 | 0.0 | 7.72 | 7.74 | 7.48 | 7.54 | 7.59 | 7.79 | 7.48 | 7.78 | 7.64 |
| 6.2 | 0.0 | 7.67 | 7.72 | 7.52 | 7.60 | 7.63 | 7.83 | 7.52 | 7.80 | 7.68 |

- Earlier KG for this condition is before Roll Stabilization Tank is dumped.

Frames 39 – 49 (Zone E)

Summary

Zone E includes Double Bottom Tanks #4 P/S, the Auxiliary Machinery Space, and the Accommodations above the Auxiliary Machinery Space.  Double Bottom Tank #4 CL and the Centerboard Trunk are not damaged as they are inside B/5. Cross-flooding of DB #4 P/S is required, and can be automatic as top of tank is well below waterline.

Roll Tank Dumped

| Draft | E-1 | E-2 | E-3 |
| --- | --- | --- | --- |
| 5.2 | 8.04 | 7.52 | 7.37 |
| 5.4 | 8.09 | 7.61 | 7.36 |
| 5.6 | 8.16 | 7.71 | 7.44 |
| 5.8 | 8.22 | 7.81 | 7.52 |
| 6.0 | 8.27 | 7.88 | 7.61 |
| 6.2 | 8.31 | 7.94 | 7.69 |

Roll Tank Not Dumped

| Draft | E-1 | E-2 | E-3 |
| --- | --- | --- | --- |
| 5.2 | 7.84 | 7.32 | 6.99 |
| 5.4 | 7.90 | 7.41 | 7.09 |
| 5.6 | 7.97 | 7.52 | 7.22 |
| 5.8 | 8.03 | 7.61 | 7.33 |
| 6.0 | 8.07 | 7.68 | 7.42 |
| 6.2 | 8.10 | 7.74 | 7.49 |

Cond E-1:	DB #4 P/S, perm = 0.95 (400.410)

|  | Limiting KG -before dump |
| --- | --- |
| Draft | Trim | KG-eq | KG-range | KG-min GZ | KG-min Area | KG-min abv HZ | KG-ML | without dump | with dump | Earlier KG* |
| 5.2 | 0.0 | - | 8.30 | 7.84 | 8.00 | 7.93 | 8.04 | 7.84 | 8.22 | 8.04 |
| 5.4 | 0.0 | - | 8.29 | 7.90 | 8.06 | 8.00 | 8.15 | 7.90 | 8.26 | 8.09 |
| 5.6 | 0.0 | - | 8.43 | 7.97 | 8.13 | 8.08 | 8.27 | 7.97 | 8.30 | 8.16 |
| 5.8 | 0.0 | - | 8.51 | 8.03 | 8.20 | 8.15 | 8.37 | 8.03 | 8.34 | 8.22 |
| 6.0 | 0.0 | - | 8.50 | 8.07 | 8.23 | 8.20 | 8.43 | 8.07 | 8.37 | 8.27 |
| 6.2 | 0.0 | - | 8.48 | 8.10 | 8.25 | 8.24 | 8.48 | 8.10 | 8.38 | 8.31 |

- Earlier KG for this condition is before Roll Stabilization Tank is dumped.

.

Cond E-2:	DB #4 P/S, perm = 0.95 (400,410)

Auxiliary Machinery Room, tank top CL, perm = 0.85 (420,421)

Accommodations, 2nd deck, perm = 0.95 (430,431)

Note: Centerboard trunk is not damaged

.

|  | Limiting KG -before dump |
| --- | --- |
| Draft | Trim | KG-eq | KG-range | KG-min GZ | KG-min Area | KG-min abv HZ | KG-ML | without dump | with dump | Earlier KG* |
| 5.2 | 0.0 | - | 7.80 | 7.32 | 7.50 | 7.41 | 7.65 | 7.32 | 7.70 | 7.52 |
| 5.4 | 0.0 | - | 7.79 | 7.41 | 7.60 | 7.51 | 7.75 | 7.41 | 7.77 | 7.61 |
| 5.6 | 0.0 | - | 8.00 | 7.52 | 7.70 | 7.63 | 7.87 | 7.52 | 7.85 | 7.71 |
| 5.8 | 0.0 | - | 8.00 | 7.61 | 7.80 | 7.73 | 7.98 | 7.61 | 7.92 | 7.81 |
| 6.0 | 0.0 | - | 8.10 | 7.68 | 7.83 | 7.81 | 8.07 | 7.68 | 7.98 | 7.88 |
| 6.2 | 0.0 | - | 8.11 | 7.74 | 7.90 | 7.88 | 8.14 | 7.74 | 8.02 | 7.94 |

- Earlier KG for this condition is before Roll Stabilization Tank is dumped.

Cond E-3:	Auxiliary Machinery Room, tank top CL, perm = 0.85 (420,421)

Accommodations, 2nd deck, perm = 0.95 (430,431)

Note: Centerboard trunk is not damaged

|  | Limiting KG -before dump |
| --- | --- |
| Draft | Trim | KG-eq | KG-range | KG-min GZ | KG-min Area | KG-min abv HZ | KG-ML | without dump | with dump | Earlier KG* |
| 5.2 | 0.0 | - | 8.01 | 6.99 | 7.23 | 7.08 | 7.40 | 6.99 | 7.37 | 8.01 |
| 5.4 | 0.0 | - | 7.48 | 7.09 | 7.30 | 7.19 | 7.47 | 7.09 | 7.45 | 7.36 |
| 5.6 | 0.0 | - | 7.60 | 7.22 | 7.40 | 7.33 | 7.57 | 7.22 | 7.55 | 7.44 |
| 5.8 | 0.0 | - | 7.74 | 7.33 | 7.50 | 7.45 | 7.68 | 7.33 | 7.64 | 7.52 |
| 6.0 | 0.0 | - | 7.80 | 7.42 | 7.60 | 7.55 | 7.79 | 7.42 | 7.72 | 7.61 |
| 6.2 | 0.0 | - | 7.86 | 7.49 | 7.63 | 7.63 | 7.88 | 7.49 | 7.77 | 7.69 |

- Earlier KG for this condition is before Roll Stabilization Tank is dumped.

Frames 49 – 72 (Zone F)

# Summary

Zone F involves the flooding of the main machinery space.  The only off-center flooding is the result of the small fuel day tank located P/S in the aft end of the compartment.  The machinery space double bottom (below the 1 m flat) will contain miscellaneous tanks that have not been fully defined at this time.  For the purpose of this analysis it was assumed that these tanks would be inboard 2.5 m off centerline and therefore not subject to damage.

| Draft | F-1 | F-2 |
| --- | --- | --- |
| 5.2 | 7.85 | 7.81 |
| 5.4 | 7.88 | 7.85 |
| 5.6 | 7.88 | 7.86 |
| 5.8 | 7.85 | 7.82 |
| 6.0 | 7.77 | 7.76 |
| 6.2 | 7.67 | 7.66 |

Cond F-1:	Machinery space, perm = 0.85 (450, 451,452,453)

Fuel day tank S, perm = 0.95 (460)

Machinery DB, perm = 0.95 (470)

| Draft | Trim | KG-eq | KG-range | KG-min GZ | KG-min Area | KG-min abv HZ | KG-ML | Limiting KG |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 5.2 | 0.0 | 8.21 | 8.14 | 7.85 | 7.95 | 8.33 | 8.19 | 7.85 |
| 5.4 | 0.0 | 8.21 | 8.13 | 7.88 | 8.00 | 8.36 | 8.24 | 7.88 |
| 5.6 | 0.0 | 8.21 | 8.10 | 7.88 | 7.95 | 8.28 | 8.27 | 7.88 |
| 5.8 | 0.0 | 8.21 | 8.02 | 7.85 | 7.90 | 8.21 | 8.27 | 7.85 |
| 6.0 | 0.0 | 8.20 | 7.90 | 7.77 | 7.80 | 8.10 | 8.25 | 7.77 |
| 6.2 | 0.0 | 8.21 | 7.74 | 7.67 | 7.70 | 7.98 | 8.22 | 7.67 |

Cond F-2:	Machinery space, perm = 0.85 (450, 451,452,453)

Fuel day tank S, perm = 0.95 (460)

| Draft | Trim | KG-eq | KG-range | KG-min GZ | KG-min Area | KG-min abv HZ | KG-ML | Limiting KG |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 5.2 | 0.0 | 8.18 | 8.11 | 7.81 | 7.92 | 8.30 | 8.15 | 7.81 |
| 5.4 | 0.0 | 8.18 | 8.21 | 7.85 | 7.94 | 8.30 | 8.21 | 7.85 |
| 5.6 | 0.0 | 8.18 | 8.08 | 7.86 | 7.93 | 8.26 | 8.24 | 7.86 |
| 5.8 | 0.0 | 8.18 | 8.01 | 7.82 | 7.90 | 8.21 | 8.25 | 7.82 |
| 6.0 | 0.0 | 8.18 | 7.88 | 7.76 | 7.80 | 8.10 | 8.23 | 7.76 |
| 6.2 | 0.0 | 8.18 | 7.73 | 7.66 | 7.70 | 7.98 | 8.20 | 7.66 |

Frames 39 – 49 (Zone G)

Summary

Zone G includes Deep Tank #5 P/S and the Stores and Oceanographic Winch space on the 2nd deck.  The void (in the skeg) on centerline is not damaged as it is inside B/5.  However the Scientific Stores area on centerline below the 2nd deck is flooded when the space above it is damaged.

There are two recess in the bulkhead between this Zone and the Machinery Space.  On the 2nd deck level the recess adds additional volume to Zone G.  On the level between the Tank Top and the 2nd Deck the recess reduces the volume of Zone G.   Both recess are inside of B/5.

Cross flooding of the Deep Tanks is not required.  However the Roll Stabilization Tank must be dumped when both the Deep Tank and the space above it are flooded.

Roll Tank Dumped

| Draft | G-1 | G-2 | G-3 |
| --- | --- | --- | --- |
| 5.2 | 7.35 | 7.50 | 7.48 |
| 5.4 | 7.41 | 7.59 | 7.53 |
| 5.6 | 7.49 | 7.65 | 7.59 |
| 5.8 | 7.57 | 7.68 | 7.63 |
| 6.0 | 7.62 | 7.70 | 7.65 |
| 6.2 | 7.66 | 7.62 | 7.73 |

Roll Tank Not Dumped

| Draft | G-1 | G-2 | G-3 |
| --- | --- | --- | --- |
| 5.2 |  | 7.34 |  |
| 5.4 |  | 7.39 |  |
| 5.6 |  | 7.42 |  |
| 5.8 |  | 7.41 |  |
| 6.0 |  | 7.38 |  |
| 6.2 |  | 7.34 |  |

Cond G-1:	DB #5 S, perm = 0.95 (500)

| Draft | Trim | KG-eq | KG-range | KG-min GZ | KG-min Area | KG-min abv HZ | KG-ML | Limiting KG |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 5.2 | 0.0 | 7.35 | 7.65 | 7.50 | 7.41 | 7.57 | 7.75 | 7.35 |
| 5.4 | 0.0 | 7.41 | 7.73 | 7.57 | 7.50 | 7.64 | 7.81 | 7.41 |
| 5.6 | 0.0 | 7.49 | 7.81 | 7.65 | 7.60 | 7.72 | 7.89 | 7.49 |
| 5.8 | 0.0 | 7.57 | 7.83 | 7.71 | 7.61 | 7.79 | 7.96 | 7.57 |
| 6.0 | 0.0 | 7.62 | 8.00 | 7.74 | 7.70 | 7.83 | 8.01 | 7.62 |
| 6.2 | 0.0 | 7.66 | 7.88 | 7.77 | 7.74 | 7.87 | 8.05 | 7.66 |

Cond G-2:	DB #5 S, perm = 0.95 (500)

Winch Room / Stores, 2nd deck, perm = 0.85  (520,521)

Machy space recess, 2nd deck, perm = 0.95 (454, 455)

|  | Limiting KG -before dump |
| --- | --- |
| Draft | Trim | KG-eq | KG-range | KG-min GZ | KG-min Area | KG-min abv HZ | KG-ML | without dump | with dump | Earlier KG* |
| 5.2 | 0.0 | 7.36 | 7.50 | 7.39 | 7.34 | 7.46 | 7.66 | 7.34 | 7.72 | 7.50 |
| 5.4 | 0.0 | 7.39 | 7.59 | 7.45 | 7.40 | 7.53 | 7.71 | 7.39 | 7.75 | 7.59 |
| 5.6 | 0.0 | 7.42 | 7.70 | 7.52 | 7.44 | 7.60 | 7.76 | 7.42 | 7.75 | 7.65 |
| 5.8 | 0.0 | 7.41 | 7.70 | 7.55 | 7.50 | 7.63 | 7.81 | 7.41 | 7.72 | 7.68 |
| 6.0 | 0.0 | 7.38 | 7.68 | 7.56 | 7.51 | 7.65 | 7.83 | 7.38 | 7.68 | 7.70 |
| 6.2 | 0.0 | 7.34 | 7.63 | 7.54 | 7.51 | 7.65 | 7.81 | 7.34 | 7.62 | 7.69 |

- Earlier KG for this condition is before Roll Stabilization Tank is dumped.

Cond G-3:	Winch Room / Stores, 2nd deck, perm = 0.85  (520)

Machy space recess, tank top, perm = -0.95 (454, 455)

| Draft | Trim | KG-eq | KG-range | KG-min GZ | KG-min Area | KG-min abv HZ | KG-ML | Limiting KG |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 5.2 | 0.0 | - | 8.01 | 7.48 | 7.70 | 7.57 | 7.76 | 7.48 |
| 5.4 | 0.0 | - | 7.91 | 7.53 | 7.72 | 7.63 | 7.82 | 7.53 |
| 5.6 | 0.0 | - | 7.97 | 7.59 | 7.80 | 7.70 | 7.89 | 7.59 |
| 5.8 | 0.0 | - | 8.01 | 7.63 | 7.81 | 7.75 | 7.96 | 7.63 |
| 6.0 | 0.0 | - | 8.04 | 7.65 | 7.82 | 7.78 | 8.01 | 7.65 |
| 6.2 | 0.0 | 8.02 | 8.03 | 7.73 | 7.81 | 7.84 | 8.05 | 7.73 |

Frames 29 – 39 (Zone H)

Summary

Zone H includes both pairs of Deep Tanks #6 P/S (forward and aft) and the Trawl Winch Room.  The void inboard of the Deep Tanks is not flooded as it is inboard of B/5.  Since the length of each Deep Tank exceeds the minimum damage length they are not considered to both be damaged at the same time.

Roll Tank Dumped

| Draft | H-1 | H-2 | H-3 | H-4 | H-5 |
| --- | --- | --- | --- | --- | --- |
| 5.2 | 7.69 | 7.72 | 7.60 | 7.66 | 7.70 |
| 5.4 | 7.76 | 7.79 | 7.64 | 7.68 | 7.74 |
| 5.6 | 7.84 | 7.87 | 7.67 | 7.70 | 7.77 |
| 5.8 | 7.91 | 7.94 | 7.67 | 7.71 | 7.75 |
| 6.0 | 7.96 | 8.00 | 7.66 | 7.70 | 7.74 |
| 6.2 | 8.01 | 8.04 | 7.61 | 7.66 | 7.71 |

Roll Tank Not Dumped

| Draft | H-1 | H-2 | H-3 | H-4 | H-5 |
| --- | --- | --- | --- | --- | --- |
| 5.2 | 7.48 | 7.51 | 7.41 | 7.47 | 7.50 |
| 5.4 | 7.56 | 7.58 | 7.44 | 7.49 | 7.53 |
| 5.6 | 7.65 | 7.66 | 7.46 | 7.50 | 7.55 |
| 5.8 | 7.74 | 7.75 | 7.48 | 7.50 | 7.55 |
| 6.0 | 7.80 | 7.81 | 7.50 | 7.50 | 7.52 |
| 6.2 | 7.85 | 7.86 | 7.45 | 7.50 | 7.48 |

Cond H-1:	DT #6F –S, perm = 0.95 (600)

|  | Limiting KG -before dump |
| --- | --- |
| Draft | Trim | KG-eq | KG-range | KG-min GZ | KG-min Area | KG-min abv HZ | KG-ML | without dump | with dump | Earlier KG* |
| 5.2 | 0.0 | 7.83 | 7.81 | 7.48 | 7.61 | 7.56 | 7.83 | 7.48 | 7.86 | 7.69 |
| 5.4 | 0.0 | 7.86 | 7.90 | 7.56 | 7.70 | 7.65 | 7.88 | 7.56 | 7.92 | 7.76 |
| 5.6 | 0.0 | 7.93 | 7.93 | 7.65 | 7.74 | 7.75 | 7.97 | 7.65 | 7.98 | 7.84 |
| 5.8 | 0.0 | 7.98 | 8.01 | 7.74 | 7.81 | 7.84 | 8.04 | 7.74 | 8.05 | 7.91 |
| 6.0 | 0.0 | 8.02 | 8.06 | 7.80 | 7.90 | 7.91 | 8.11 | 7.80 | 8.10 | 7.96 |
| 6.2 | 0.0 | 8.04 | 8.10 | 7.85 | 7.90 | 7.96 | 8.16 | 7.85 | 8.13 | 8.01 |

- Earlier KG for this condition is before Roll Stabilization Tank is dumped.

Cond H-2:	DT #6A –S, perm = 0.95 (610)

|  | Limiting KG -before dump |
| --- | --- |
| Draft | Trim | KG-eq | KG-range | KG-min GZ | KG-min Area | KG-min abv HZ | KG-ML | without dump | with dump | Earlier KG* |
| 5.2 | 0.0 | - | 7.91 | 7.51 | 7.70 | 7.60 | 7.83 | 7.51 | 7.89 | 7.72 |
| 5.4 | 0.0 | 8.02 | 8.01 | 7.58 | 7.74 | 7.68 | 7.91 | 7.58 | 7.94 | 7.79 |
| 5.6 | 0.0 | 8.08 | 8.02 | 7.66 | 7.81 | 7.77 | 7.99 | 7.66 | 7.99 | 7.87 |
| 5.8 | 0.0 | 8.13 | 8.10 | 7.75 | 7.90 | 7.86 | 8.08 | 7.75 | 8.06 | 7.94 |
| 6.0 | 0.0 | 8.17 | 8.14 | 7.81 | 7.93 | 7.93 | 8.15 | 7.81 | 8.11 | 8.00 |
| 6.2 | 0.0 | 8.18 | 8.16 | 7.86 | 8.00 | 7.99 | 8.20 | 7.86 | 8.14 | 8.04 |

- Earlier KG for this condition is before Roll Stabilization Tank is dumped.

Cond H-3:	DT #6F –S, perm = 0.95 (600)

Winch Room, perm = 0.85 (620)

|  | Limiting KG -before dump |
| --- | --- |
| Draft | Trim | KG-eq | KG-range | KG-min GZ | KG-min Area | KG-min abv HZ | KG-ML | without dump | with dump | Earlier KG* |
| 5.2 | 0.0 | 7.83 | 7.80 | 7.41 | 7.56 | 7.50 | 7.72 | 7.41 | 7.79 | 7.60 |
| 5.4 | 0.0 | 7.86 | 7.79 | 7.44 | 7.60 | 7.53 | 7.76 | 7.44 | 7.80 | 7.64 |
| 5.6 | 0.0 | 7.86 | 7.85 | 7.46 | 7.60 | 7.57 | 7.79 | 7.46 | 7.79 | 7.67 |
| 5.8 | 0.0 | 7.79 | 7.79 | 7.48 | 7.60 | 7.59 | 7.81 | 7.48 | 7.79 | 7.67 |
| 6.0 | 0.0 | 7.66 | 7.80 | 7.50 | 7.53 | 7.61 | 7.80 | 7.50 | 7.80 | 7.66 |
| 6.2 | 0.0 | 7.51 | 7.60 | 7.45 | 7.50 | 7.56 | 7.74 | 7.45 | 7.73 | 7.61 |

- Earlier KG for this condition is before Roll Stabilization Tank is dumped.

Cond H-4:	DT #6A –S, perm = 0.95 (610)

Winch Room, perm = 0.85 (620)

|  | Limiting KG -before dump |
| --- | --- |
| Draft | Trim | KG-eq | KG-range | KG-min GZ | KG-min Area | KG-min abv HZ | KG-ML | without dump | with dump | Earlier KG* |
| 5.2 | 0.0 | 999.00 | 7.85 | 7.47 | 7.64 | 7.56 | 7.74 | 7.47 | 7.85 | 7.66 |
| 5.4 | 0.0 | 8.02 | 8.00 | 7.49 | 7.70 | 7.59 | 7.79 | 7.49 | 7.85 | 7.68 |
| 5.6 | 0.0 | 8.03 | 7.89 | 7.50 | 7.70 | 7.61 | 7.83 | 7.50 | 7.83 | 7.70 |
| 5.8 | 0.0 | 7.96 | 7.86 | 7.50 | 7.70 | 7.62 | 7.85 | 7.50 | 7.81 | 7.71 |
| 6.0 | 0.0 | 7.83 | 7.83 | 7.50 | 7.61 | 7.62 | 7.85 | 7.50 | 7.80 | 7.70 |
| 6.2 | 0.0 | 7.67 | 7.69 | 7.50 | 7.54 | 7.61 | 7.80 | 7.50 | 7.78 | 7.66 |

- Earlier KG for this condition is before Roll Stabilization Tank is dumped.

Cond H-5:	Winch Room, perm = 0.85 (620)

|  | Limiting KG -before dump |
| --- | --- |
| Draft | Trim | KG-eq | KG-range | KG-min GZ | KG-min Area | KG-min abv HZ | KG-ML | without dump | with dump | Earlier KG* |
| 5.2 | 0.0 | - | 7.90 | 7.50 | 7.70 | 7.59 | 7.76 | 7.50 | 7.88 | 7.70 |
| 5.4 | 0.0 | - | 7.91 | 7.53 | 7.71 | 7.63 | 7.81 | 7.53 | 7.89 | 7.74 |
| 5.6 | 0.0 | - | 7.93 | 7.55 | 7.75 | 7.66 | 7.85 | 7.55 | 7.88 | 7.77 |
| 5.8 | 0.0 | - | 8.00 | 7.55 | 7.75 | 7.67 | 7.88 | 7.55 | 7.86 | 7.75 |
| 6.0 | 0.0 | - | 7.92 | 7.52 | 7.70 | 7.65 | 7.89 | 7.52 | 7.82 | 7.74 |
| 6.2 | 0.0 | - | 7.82 | 7.48 | 7.63 | 7.62 | 7.87 | 7.48 | 7.76 | 7.71 |

- Earlier KG for this condition is before Roll Stabilization Tank is dumped.

2.h. 	Damage Condition Summaries With Trim

Frames 29 – 39 (Zone D) – Trim by Bow

Summary

A before damage trim of 0.5 meters reduces the allowable KG for this condition by about 0.1 meters.  This is because the broad transom, which emerges from the water as the vessel trims by the bow,  adds noticeable stability at small heel angles.

Roll Tank Dumped

| Draft | D-1 | D-2 | D-3 | D-4 | D-5 |
| --- | --- | --- | --- | --- | --- |
| 5.2 | 7.59 | 7.38 | 7.34 | 7.13 | 7.32 |
| 5.4 | 7.64 | 7.45 | 7.40 | 7.23 | 7.36 |
| 5.6 | 7.70 | 7.53 | 7.47 | 7.30 | 7.41 |
| 5.8 | 7.78 | 7.61 | 7.53 | 7.38 | 7.46 |
| 6.0 | 7.86 | 7.67 | 7.60 | 7.46 | 7.52 |
| 6.2 | 7.92 | 7.71 | 7.65 | 7.52 | 7.57 |

Roll Tank Not Dumped

| Draft | D-1 | D-2 | D-3 | D-4 | D-5 |
| --- | --- | --- | --- | --- | --- |
| 5.2 |  | 7.08 | 7.17 | 6.98 | 7.14 |
| 5.4 |  | 7.14 | 7.23 | 7.05 | 7.17 |
| 5.6 |  | 7.22 | 7.31 | 7.13 | 7.22 |
| 5.8 |  | 7.33 | 7.39 | 7.22 | 7.28 |
| 6.0 |  | 7.40 | 7.44 | 7.31 | 7.36 |
| 6.2 |  | 7.44 | 7.48 | 7.37 | 7.42 |

Cond D-1:	DB #3 P/S, perm = 0.95 (300)

| Draft | Trim | KG-eq | KG-range | KG-min GZ | KG-min Area | KG-min abv HZ | KG-ML | Limiting KG |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 5.2 | -0.5 | - | 7.96 | 7.59 | 7.74 | 7.67 | 7.92 | 7.59 |
| 5.4 | -0.5 | - | 8.01 | 7.64 | 7.80 | 7.73 | 7.99 | 7.64 |
| 5.6 | -0.5 | - | 8.11 | 7.70 | 7.90 | 7.81 | 8.07 | 7.70 |
| 5.8 | -0.5 | - | 8.20 | 7.78 | 7.95 | 7.90 | 8.15 | 7.78 |
| 6.0 | -0.5 | - | 8.28 | 7.86 | 8.02 | 7.98 | 8.23 | 7.86 |
| 6.2 | -0.5 | - | 8.30 | 7.92 | 8.10 | 8.05 | 8.30 | 7.92 |

Cond D-2:	DB #3 P/S, perm = 0.95 (300)

Stores, tank top S, perm = 0.60 (320)

Access, tank top CL, perm = 0.95 (330, 331)

Sewage Treatment Room, tank top P, perm = 0.85 (340)

Void, tank top P, perm = 0.95 (350)

Accommodations, 2nd deck, perm = 0.95 (370)

|  | Limiting KG -before dump |
| --- | --- |
| Draft | Trim | KG-eq | KG-range | KG-min GZ | KG-min Area | KG-min abv HZ | KG-ML | without dump | with dump | Earlier KG* |
| 5.2 | -0.5 | 7.08 | 7.40 | 7.21 | 7.14 | 7.26 | 7.44 | 7.08 | 7.46 | 7.34 |
| 5.4 | -0.5 | 7.14 | 7.39 | 7.22 | 7.20 | 7.29 | 7.47 | 7.14 | 7.50 | 7.35 |
| 5.6 | -0.5 | 7.22 | 7.50 | 7.28 | 7.23 | 7.36 | 7.53 | 7.22 | 7.55 | 7.41 |
| 5.8 | -0.5 | 7.33 | 7.51 | 7.34 | 7.33 | 7.43 | 7.61 | 7.33 | 7.64 | 7.49 |
| 6.0 | -0.5 | 7.46 | 7.57 | 7.40 | 7.41 | 7.50 | 7.69 | 7.40 | 7.70 | 7.55 |
| 6.2 | -0.5 | 7.56 | 7.60 | 7.44 | 7.50 | 7.55 | 7.75 | 7.44 | 7.72 | 7.60 |

- Earlier KG for this condition is before Roll Stabilization Tank is dumped.

Cond D-3:	DB #3 P/S, perm = 0.95 (310)

Stores, tank top S, perm = 0.60 (320)

Access, tank top CL, perm = 0.95 (330, 331)

Sewage Treatment Room, tank top P, perm = 0.85 (340)

Void, tank top P, perm = 0.95 (350)

Sewage Tank, tank top, perm = 0.95

Accommodations, 2nd deck, perm = 0.95 (370)

|  | Limiting KG -before dump |
| --- | --- |
| Draft | Trim | KG-eq | KG-range | KG-min GZ | KG-min Area | KG-min abv HZ | KG-ML | without dump | with dump | Earlier KG* |
| 5.2 | -0.5 | 7.26 | 7.40 | 7.17 | 7.20 | 7.26 | 7.46 | 7.17 | 7.55 | 7.34 |
| 5.4 | -0.5 | 7.31 | 7.46 | 7.24 | 7.23 | 7.33 | 7.52 | 7.23 | 7.59 | 7.40 |
| 5.6 | -0.5 | 7.39 | 7.60 | 7.32 | 7.31 | 7.41 | 7.59 | 7.31 | 7.64 | 7.47 |
| 5.8 | -0.5 | 7.48 | 7.61 | 7.39 | 7.40 | 7.47 | 7.66 | 7.39 | 7.70 | 7.53 |
| 6.0 | -0.5 | 7.60 | 7.64 | 7.44 | 7.50 | 7.54 | 7.75 | 7.44 | 7.74 | 7.60 |
| 6.2 | -0.5 | 7.69 | 7.68 | 7.48 | 7.54 | 7.60 | 7.82 | 7.48 | 7.76 | 7.65 |

- Earlier KG for this condition is before Roll Stabilization Tank is dumped.

Cond D-4:	Stores, tank top S, perm = 0.60 (320)

Access, tank top CL, perm = 0.95 (330, 331)

Sewage Treatment Room, tank top P, perm = 0.85 (340)

Void, tank top P, perm = 0.95 (350)

Sewage Tank, tank top, perm = 0.95

Accommodations, 2nd deck, perm = 0.95 (370)

(DB tanks not damaged)

|  | Limiting KG -before dump |
| --- | --- |
| Draft | Trim | KG-eq | KG-range | KG-min GZ | KG-min Area | KG-min abv HZ | KG-ML | without dump | with dump | Earlier KG* |
| 5.2 | -0.5 | 7.14 | 7.17 | 6.98 | 7.02 | 7.07 | 7.30 | 6.98 | 7.36 | 7.13 |
| 5.4 | -0.5 | 7.21 | 7.23 | 7.05 | 7.10 | 7.15 | 7.36 | 7.05 | 7.41 | 7.23 |
| 5.6 | -0.5 | 7.28 | 7.40 | 7.13 | 7.15 | 7.23 | 7.43 | 7.13 | 7.46 | 7.30 |
| 5.8 | -0.5 | 7.38 | 7.50 | 7.22 | 7.25 | 7.32 | 7.52 | 7.22 | 7.53 | 7.38 |
| 6.0 | -0.5 | 7.48 | 7.60 | 7.31 | 7.34 | 7.41 | 7.61 | 7.31 | 7.61 | 7.46 |
| 6.2 | -0.5 | 7.55 | 7.58 | 7.37 | 7.41 | 7.48 | 7.68 | 7.37 | 7.65 | 7.52 |

- Earlier KG for this condition is before Roll Stabilization Tank is dumped.

Cond D-5:	Sewage Tank, P tank top, perm = 0.95

Accommodations, 2nd deck, perm = 0.95 (370)

|  | Limiting KG -before dump |
| --- | --- |
| Draft | Trim | KG-eq | KG-range | KG-min GZ | KG-min Area | KG-min abv HZ | KG-ML | without dump | with dump | Earlier KG* |
| 5.2 | -0.5 | 7.41 | 7.43 | 7.14 | 7.22 | 7.21 | 7.44 | 7.14 | 7.55 | 7.32 |
| 5.4 | -0.5 | 7.44 | 7.46 | 7.17 | 7.25 | 7.26 | 7.48 | 7.17 | 7.59 | 7.36 |
| 5.6 | -0.5 | 7.48 | 7.51 | 7.22 | 7.30 | 7.31 | 7.53 | 7.22 | 7.64 | 7.41 |
| 5.8 | -0.5 | 7.53 | 7.53 | 7.28 | 7.35 | 7.39 | 7.60 | 7.28 | 7.70 | 7.46 |
| 6.0 | -0.5 | 7.55 | 7.61 | 7.36 | 7.40 | 7.47 | 7.66 | 7.36 | 7.74 | 7.52 |
| 6.2 | -0.5 | 7.55 | 7.70 | 7.42 | 7.44 | 7.52 | 7.71 | 7.42 | 7.76 | 7.57 |

- Earlier KG for this condition is before Roll Stabilization Tank is dumped.

Frames 49 – 72 (Zone F) – Trim by Stern

# Summary

A before damage trim of 1.0 meters by the stern the allowable KG for this condition by about 0.2 meters.  The loss of freeboard aft reduces the residual righting arms.

| Draft | F-1 | F-2 |
| --- | --- | --- |
| 5.2 | 7.97 | 7.94 |
| 5.4 | 7.93 | 7.90 |
| 5.6 | 7.85 | 7.83 |
| 5.8 | 7.71 | 7.70 |
| 6.0 | 7.55 | 7.53 |
| 6.2 | 7.33 | 7.33 |

Cond F-1:	Machinery space, perm = 0.85 (450, 451,452,453)

Fuel day tank S, perm = 0.95 (460)

Machinery DB, perm = 0.95 (470)

| Draft | Trim | KG-eq | KG-range | KG-min GZ | KG-min Area | KG-min abv HZ | KG-ML | Limiting KG |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 5.2 | 1.0 | 8.31 | 8.22 | 7.97 | 8.10 | 8.05 | 8.35 | 7.97 |
| 5.4 | 1.0 | 8.28 | 8.15 | 7.93 | 8.01 | 8.03 | 8.34 | 7.93 |
| 5.6 | 1.0 | 8.26 | 8.05 | 7.85 | 7.91 | 7.98 | 8.29 | 7.85 |
| 5.8 | 1.0 | 8.24 | 7.89 | 7.71 | 7.80 | 7.88 | 8.23 | 7.71 |
| 6.0 | 1.0 | 8.20 | 7.66 | 7.55 | 7.60 | 7.75 | 8.12 | 7.55 |
| 6.2 | 1.0 | 8.08 | 7.41 | 7.33 | 7.40 | 7.57 | 7.99 | 7.33 |

Cond F-2:	Machinery space, perm = 0.85 (450, 451,452,453)

Fuel day tank S, perm = 0.95 (460)

| Draft | Trim | KG-eq | KG-range | KG-min GZ | KG-min Area | KG-min abv HZ | KG-ML | Limiting KG |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 5.2 | 1.0 | 8.29 | 8.20 | 7.94 | 8.03 | 8.03 | 8.35 | 7.94 |
| 5.4 | 1.0 | 8.26 | 8.14 | 7.90 | 8.00 | 8.01 | 8.34 | 7.90 |
| 5.6 | 1.0 | 8.23 | 8.03 | 7.83 | 7.90 | 7.96 | 8.29 | 7.83 |
| 5.8 | 1.0 | 8.21 | 7.87 | 7.70 | 7.80 | 7.86 | 8.23 | 7.70 |
| 6.0 | 1.0 | 8.18 | 7.65 | 7.53 | 7.60 | 7.73 | 8.12 | 7.53 |
| 6.2 | 1.0 | 8.07 | 7.41 | 7.33 | 7.40 | 7.56 | 7.99 | 7.33 |

Frames 29 – 39 (Zone H) – Trim by Stern

Summary

A before damage trim of 1.0 meters by the stern the allowable KG for this condition by about 0.2 meters.  The loss of freeboard aft reduces the residual righting arms.

Roll Tank Dumped

| Draft | H-1 | H-2 | H-3 | H-4 | H-5 |
| --- | --- | --- | --- | --- | --- |
| 5.2 | 7.98 | 8.04 | 7.77 | 7.86 | 7.98 |
| 5.4 | 8.04 | 8.10 | 7.78 | 7.82 | 7.90 |
| 5.6 | 8.09 | 8.13 | 7.74 | 7.79 | 7.83 |
| 5.8 | 8.12 | 8.16 | 7.68 | 7.73 | 7.79 |
| 6.0 | 8.15 | 8.18 | 7.58 | 7.64 | 7.70 |
| 6.2 | 8.16 | 8.17 | 7.45 | 7.51 | 7.58 |

Roll Tank Not Dumped

| Draft | H-1 | H-2 | H-3 | H-4 | H-5 |
| --- | --- | --- | --- | --- | --- |
| 5.2 | 7.81 | 7.85 | 7.60 | 7.66 | 7.71 |
| 5.4 | 7.88 | 7.92 | 7.59 | 7.63 | 7.68 |
| 5.6 | 7.93 | 7.96 | 7.59 | 7.61 | 7.63 |
| 5.8 | 7.97 | 7.99 | 7.53 | 7.58 | 7.56 |
| 6.0 | 7.98 | 8.01 | 7.42 | 7.48 | 7.48 |
| 6.2 | 7.96 | 8.00 | 7.28 | 7.34 | 7.38 |

Cond H-1:	DT #6F –S, perm = 0.95 (600)

|  | Limiting KG -before dump |
| --- | --- |
| Draft | Trim | KG-eq | KG-range | KG-min GZ | KG-min Area | KG-min abv HZ | KG-ML | without dump | with dump | Earlier KG* |
| 5.2 | 1.0 | 8.16 | 8.12 | 7.81 | 7.92 | 7.89 | 8.06 | 7.81 | 8.19 | 7.98 |
| 5.4 | 1.0 | 8.18 | 8.17 | 7.88 | 8.00 | 7.97 | 8.15 | 7.88 | 8.24 | 8.04 |
| 5.6 | 1.0 | 8.19 | 8.22 | 7.93 | 8.01 | 8.02 | 8.23 | 7.93 | 8.26 | 8.09 |
| 5.8 | 1.0 | 8.19 | 8.22 | 7.97 | 8.03 | 8.07 | 8.28 | 7.97 | 8.28 | 8.12 |
| 6.0 | 1.0 | 8.17 | 8.19 | 7.98 | 8.03 | 8.08 | 8.30 | 7.98 | 8.28 | 8.15 |
| 6.2 | 1.0 | 8.16 | 8.15 | 7.96 | 8.01 | 8.08 | 8.29 | 7.96 | 8.24 | 8.16 |

- Earlier KG for this condition is before Roll Stabilization Tank is dumped.

Cond H-2:	DT #6A –S, perm = 0.95 (610)

|  | Limiting KG -before dump |
| --- | --- |
| Draft | Trim | KG-eq | KG-range | KG-min GZ | KG-min Area | KG-min abv HZ | KG-ML | without dump | with dump | Earlier KG* |
| 5.2 | 1.0 | 8.32 | 8.19 | 7.85 | 8.00 | 7.94 | 8.07 | 7.85 | 8.23 | 8.04 |
| 5.4 | 1.0 | 8.35 | 8.27 | 7.92 | 8.05 | 8.01 | 8.17 | 7.92 | 8.28 | 8.10 |
| 5.6 | 1.0 | 8.35 | 8.31 | 7.96 | 8.10 | 8.06 | 8.26 | 7.96 | 8.29 | 8.13 |
| 5.8 | 1.0 | 8.34 | 8.29 | 7.99 | 8.10 | 8.10 | 8.32 | 7.99 | 8.30 | 8.16 |
| 6.0 | 1.0 | 8.32 | 8.28 | 8.01 | 8.10 | 8.12 | 8.35 | 8.01 | 8.31 | 8.18 |
| 6.2 | 1.0 | 8.29 | 8.33 | 8.00 | 8.10 | 8.12 | 8.35 | 8.00 | 8.28 | 8.17 |

- Earlier KG for this condition is before Roll Stabilization Tank is dumped.

Cond H-3:	DT #6F –S, perm = 0.95 (600)

Winch Room, perm = 0.85 (620)

|  | Limiting KG -before dump |
| --- | --- |
| Draft | Trim | KG-eq | KG-range | KG-min GZ | KG-min Area | KG-min abv HZ | KG-ML | without dump | with dump | Earlier KG* |
| 5.2 | 1.0 | 8.04 | 7.93 | 7.60 | 7.74 | 7.68 | 7.90 | 7.60 | 7.98 | 7.77 |
| 5.4 | 1.0 | 7.91 | 7.91 | 7.59 | 7.70 | 7.68 | 7.92 | 7.59 | 7.95 | 7.78 |
| 5.6 | 1.0 | 7.73 | 7.81 | 7.59 | 7.61 | 7.69 | 7.88 | 7.59 | 7.92 | 7.74 |
| 5.8 | 1.0 | 7.54 | 7.69 | 7.53 | 7.53 | 7.63 | 7.77 | 7.53 | 7.84 | 7.68 |
| 6.0 | 1.0 | 7.43 | 7.56 | 7.42 | 7.43 | 7.53 | 7.61 | 7.42 | 7.72 | 7.58 |
| 6.2 | 1.0 | 7.40 | 7.44 | 7.28 | 7.32 | 7.40 | 7.44 | 7.28 | 7.56 | 7.45 |

- Earlier KG for this condition is before Roll Stabilization Tank is dumped.

Cond H-4:	DT #6A –S, perm = 0.95 (610)

Winch Room, perm = 0.85 (620)

|  | Limiting KG -before dump |
| --- | --- |
| Draft | Trim | KG-eq | KG-range | KG-min GZ | KG-min Area | KG-min abv HZ | KG-ML | without dump | with dump | Earlier KG* |
| 5.2 | 1.0 | 8.23 | 8.02 | 7.66 | 7.84 | 7.75 | 7.93 | 7.66 | 8.04 | 7.86 |
| 5.4 | 1.0 | 8.10 | 7.99 | 7.63 | 7.80 | 7.73 | 7.97 | 7.63 | 7.99 | 7.82 |
| 5.6 | 1.0 | 7.91 | 7.91 | 7.61 | 7.70 | 7.71 | 7.95 | 7.61 | 7.94 | 7.79 |
| 5.8 | 1.0 | 7.72 | 7.80 | 7.58 | 7.61 | 7.68 | 7.86 | 7.58 | 7.89 | 7.73 |
| 6.0 | 1.0 | 7.59 | 7.65 | 7.48 | 7.51 | 7.59 | 7.72 | 7.48 | 7.78 | 7.64 |
| 6.2 | 1.0 | 7.54 | 7.60 | 7.34 | 7.40 | 7.47 | 7.58 | 7.34 | 7.62 | 7.51 |

- Earlier KG for this condition is before Roll Stabilization Tank is dumped.

Cond H-5:	Winch Room, perm = 0.85 (620)

|  | Limiting KG -before dump |
| --- | --- |
| Draft | Trim | KG-eq | KG-range | KG-min GZ | KG-min Area | KG-min abv HZ | KG-ML | without dump | with dump | Earlier KG* |
| 5.2 | 1.0 | - | 8.09 | 7.71 | 7.92 | 7.82 | 7.95 | 7.71 | 8.09 | 7.98 |
| 5.4 | 1.0 | - | 8.07 | 7.68 | 7.90 | 7.79 | 7.99 | 7.68 | 8.04 | 7.90 |
| 5.6 | 1.0 | - | 8.05 | 7.63 | 7.80 | 7.75 | 8.00 | 7.63 | 7.96 | 7.83 |
| 5.8 | 1.0 | - | 7.86 | 7.56 | 7.70 | 7.68 | 7.95 | 7.56 | 7.87 | 7.79 |
| 6.0 | 1.0 | - | 7.76 | 7.48 | 7.60 | 7.61 | 7.84 | 7.48 | 7.78 | 7.70 |
| 6.2 | 1.0 | - | 7.66 | 7.38 | 7.50 | 7.52 | 7.70 | 7.38 | 7.66 | 7.58 |

- Earlier KG for this condition is before Roll Stabilization Tank is dumped.

2.i.	Damage Condition D-4

Ship-  FRV40-1   6-30-99                  Number-     1            7/ 8/99

DAMG Ver. 1.07

DAMAGED STATICAL STABILITY CALCULATIONS

Condition  5  Compartments Included 320 330 331 340 350 360 370

Station 0 is located at the bow

Ship Properties Before Damage

Draft     Trim     Displ      LCG     Pole Ht

6.00      .00      2512.8     29.50     7.40

Change in transverse center of gravity after damage due to run-off

TCG =   .000 m. (+ = Stbd, - = Port)

Net Damaged Ship Properties

Displ    LCG    Pole   Heel    RA     TCB    VCB     LCB    Draft    Trim

Ht

2512.8  29.496  7.40   .00   -.038   -.038   3.840  29.456   6.236   -.638

5.00    .009    .319   3.856  29.453   6.235   -.689

7.50    .032    .496   3.875  29.450   6.232   -.751

10.00    .052    .670   3.902  29.445   6.225   -.839

12.50    .069    .839   3.936  29.439   6.213   -.953

15.00    .085   1.005   3.976  29.432   6.197  -1.086

17.50    .099   1.169   4.024  29.424   6.175  -1.231

20.00    .110   1.327   4.078  29.415   6.149  -1.399

25.00    .086   1.593   4.189  29.395   6.113  -1.822

30.00   -.002   1.791   4.293  29.371   6.110  -2.323

REQUIREMENTS FOR DAMAGE SURVIVAL OF 46 CFR 171.080(f)(1)-(5)

Limiting KG for  7.0 degree equilibrium heel angle        =   7.63 m.

Limiting KG for 15.0 degree range of positive stablity    =   7.70 m.

Limiting KG for minimum of 0.1 m of residual righting arm =   7.42 m.

Limiting KG for minimum of  .86 m-deg residual area       =   7.50 m.

Limiting KG for 0.040 m of GZ above HZ of  .027 m         =   7.53 m.

Minimum residual righting arm of 0.10 m   is limiting criteria

Maximum allowable KG =   7.42

Righting arm curve for KG =   7.42 m.

Heel      GZ, m.

.00     -.038

4.29      .000  <--- Equlibrium heel angle

5.00      .007

7.50      .029

10.00      .048

12.50      .065

15.00      .079

17.50      .093

20.00      .103

20.70      .104  <--- Maximum residual righting arm

25.00      .077

29.33      .000  <--- Limit of positive stability

30.00     -.013

REQUIREMENTS FOR DAMAGE SURVIVAL OF 46 CFR 171.080(f)(6) (MARGIN LINE)

(Unsymmetric Damage)

Heel  Sta0-ML   BL-ML   Sta0-DF  BL-ML

.00    -.833   2.010

5.00   18.769   1.603

7.50   21.785   1.280

10.00   21.788    .946

12.50   21.791    .612

15.00   21.796    .279

17.50   21.801   -.052

20.00   21.809   -.383

25.00   21.832  -1.069

30.00   21.868  -1.790

Sta0-ML = distance from station 0 to margin line in meters

BL-ML   = distance from baseline to margin line in meters

Sta0-DF = distance from station 0 to downflooding point in meters

BL-ML   = distance from baseline to downflooding point in meters

Margin line/downflooding point is first immersed at heel  17.11 degrees

at point  21.800 meters from station 0

Maximum allowable KG at heel which immerses

margin line / Downflooding point =   7.730 meters

Maximum allowable KG at heel of   7.00 degrees =   7.625 meters

Righting arms for pole height =  7.625

Heel    RA

.00   -.038

5.00   -.010

7.50    .003

10.00    .013

12.50    .021

15.00    .026

17.50    .032

20.00    .034

25.00   -.009

30.00   -.115

At heel   6.98 degrees, righting arm is    .000 meters

At heel  24.36 degrees, righting arm is    .000 meters

At heel  19.53 degrees, maxima/minima RA value is    .034 meters

REQUIREMENTS FOR EARLIER STAGE OF FLOODING 46 CFR 171.080(f)(7)&(8)

Limiting KG for 15.0 degree equilibrium heel angle        =   7.73 m.

Limiting KG for  7.0 degree range of positive stablity    =   7.71 m.

Limiting KG for minimum of 0.05 m of residual righting arm=   7.58 m.

Minimum residual righting arm of 0.05 m is limiting criteria

Maximum allowable KG =   7.58

Righting arm curve for KG =   7.58 m.

Heel      GZ, m.

.00     -.038

5.00     -.006

6.15      .000  <--- Equlibrium heel angle

7.50      .009

10.00      .021

12.50      .031

15.00      .039

17.50      .046

19.71      .050  <--- Maximum residual righting arm

20.00      .050

25.00      .012

25.68      .000  <--- Limit of positive stability

30.00     -.090

2.j.	Damage Condition F-1

Ship- FRV40-1   6-30-99                  Number-     1            7/ 9/99

DAMG Ver. 1.07

DAMAGED STATICAL STABILITY CALCULATIONS

Condition  5  Compartments Included 450 451 452 453 454 455 456 460 470

Station 0 is located at the bow

Ship Properties Before Damage

Draft     Trim     Displ      LCG     Pole Ht

6.00      .00      2512.8     29.50     7.40

Change in transverse center of gravity after damage due to run-off

TCG =   .000 m. (+ = Stbd, - = Port)

Net Damaged Ship Properties

Displ    LCG    Pole   Heel    RA     TCB    VCB     LCB    Draft    Trim

Ht

2512.9  29.496  7.40   .00   -.022   -.022   4.557  29.516   7.159    .418

5.00    .064    .311   4.572  29.516   7.157    .419

7.50    .107    .478   4.590  29.516   7.153    .416

10.00    .150    .643   4.616  29.515   7.146    .410

12.50    .181    .796   4.646  29.516   7.141    .428

15.00    .181    .918   4.676  29.518   7.152    .480

17.50    .157   1.014   4.704  29.522   7.178    .547

20.00    .114   1.093   4.731  29.525   7.219    .624

25.00   -.006   1.215   4.781  29.531   7.340    .783

30.00   -.155   1.306   4.828  29.538   7.508    .951

REQUIREMENTS FOR DAMAGE SURVIVAL OF 46 CFR 171.080(f)(1)-(5)

Limiting KG for  7.0 degree equilibrium heel angle        =   8.20 m.

Limiting KG for 15.0 degree range of positive stablity    =   7.90 m.

Limiting KG for minimum of 0.1 m of residual righting arm =   7.77 m.

Limiting KG for minimum of  .86 m-deg residual area       =   7.80 m.

Limiting KG for 0.040 m of GZ above HZ of  .027 m         =   7.93 m.

Minimum residual righting arm of 0.10 m   is limiting criteria

Maximum allowable KG =   7.77

Righting arm curve for KG =   7.77 m.

Heel      GZ, m.

.00     -.022

2.17      .000  <--- Equlibrium heel angle

5.00      .031

7.50      .059

10.00      .086

12.50      .101

12.56      .101  <--- Maximum residual righting arm

15.00      .086

17.50      .045

19.48      .000  <--- Limit of positive stability

20.00     -.012

25.00     -.162

30.00     -.340

REQUIREMENTS FOR DAMAGE SURVIVAL OF 46 CFR 171.080(f)(6) (MARGIN LINE)

Maximum Allowable KG Calculations

(Unsymmetric Damage)

Heel  Sta0-ML   BL-ML   Sta0-DF  BL-ML

.00   61.007   1.184

5.00   61.003    .534

7.50   61.000    .212

10.00   59.491   -.106

12.50   59.489   -.443

15.00   59.485   -.812

17.50   59.481  -1.203

20.00   59.475  -1.609

25.00   59.461  -2.450

30.00   59.441  -3.312

Sta0-ML = distance from station 0 to margin line in meters

BL-ML   = distance from baseline to margin line in meters

Sta0-DF = distance from station 0 to downflooding point in meters

3.a.	Tank Capacity Summary

FRV40 Tank Capacities

Summary

|  |  | 100% | 95% | VCG | LCG | TCG | i/d |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  |  | m-tons | m-tons | m abv bl | m aft fp | m off cl | m-tons |
| Diesel Oil (s.g. = 0.850) |  |  |  |  |  |  |  |
| Deep Tank #1F | P |  | 26.08 | 3.72 | 6.60 | -0.97 | 3.95 |
| Deep Tank #1F | S |  | 26.08 | 3.72 | 6.60 | 0.97 | 3.95 |
| Deep Tank #2 | P |  | 49.25 | 3.91 | 15.22 | -3.67 | 11.76 |
| Deep Tank #2 | S |  | 49.25 | 3.91 | 15.22 | 3.67 | 11.76 |
| Deep Tank #2 | C |  | 48.00 | 3.48 | 13.00 | 0.00 | 21.28 |
| Double Bottom Tank #4 | P |  | 47.42 | 2.38 | 26.89 | -4.39 | 41.37 |
| Double Bottom Tank #4 | S |  | 47.42 | 2.38 | 26.89 | 4.39 | 41.37 |
| Day Tank | P |  | 10.26 | 6.32 | 42.84 | -6.42 | 0.85 |
| Day Tank | S |  | 10.26 | 6.32 | 42.84 | 6.42 | 0.85 |
| Deep Tank #5 | P |  | 42.16 | 5.07 | 46.23 | -4.56 | 49.77 |
| Deep Tank #5 | S |  | 42.16 | 5.07 | 46.23 | 4.56 | 49.77 |
| Total Diesel Oil |  |  | 398.33 | 3.84 | 24.59 | 0.00 | 236.69 |
| Salt Water Ballast (s.g. = 1.026) |  |  |  |  |  |
| Forepeak | C | 45.04 |  | 5.80 | 2.91 | 0.00 | 0.00 |
| Double Bottom Tank #3 | C | 84.30 |  | 2.24 | 20.83 | 0.00 | 0.00 |
| Double Bottom Tank #3 | P | 45.19 |  | 2.51 | 21.00 | -4.04 | 0.00 |
| Double Bottom Tank #3 | S | 45.19 |  | 2.51 | 21.00 | 4.04 | 0.00 |
| Double Bottom Tank #4 | C | 78.49 |  | 2.16 | 26.99 | 0.00 | 0.00 |
| Deep Tank #6F | P | 23.91 |  | 5.61 | 51.99 | -4.25 | 0.00 |
| Deep Tank #6F | S | 23.91 |  | 5.61 | 51.99 | 4.25 | 0.00 |
| Deep Tank #6A | P | 14.70 |  | 5.81 | 57.67 | -3.73 | 0.00 |
| Deep Tank #6A | S | 14.70 |  | 5.81 | 57.67 | 3.73 | 0.00 |
| Total Salt Water |  | 375.44 |  | 3.42 | 26.86 | 0.00 | 0.00 |
| Fresh Water (s.g. = 1.000) |  |  |  |  |  |
| Fresh Water Tank | P | 13.82 |  | 4.90 | 19.30 | -1.25 | 0.00 |
| Fresh Water Tank | S | 22.12 |  | 4.90 | 20.20 | 1.25 | 0.00 |
| Total Fresh Water |  | 35.94 |  | 4.90 | 19.85 | 0.29 | 0.00 |
| Sewage Tank (s.g. = 1.000) | P | 23.65 |  | 4.94 | 19.35 | -4.64 | 0.00 |

3.b.	Salt Water Ballast Tanks

FRV40

Forepeak Tank

Stem – Fr 7

Salt Water Ballast

|  |  | CENTER |  |  |  |
| --- | --- | --- | --- | --- | --- |
|  | Salt Water | VCG | LCG | TCG | I/d |
|  | m tons | m abv bl | m aft fp | m off cl | m-ton |
| 10% | 45.00 | 2.03 | 3.55 | 0.00 | 1.02 |
| 20% | 9.01 | 2.59 | 3.46 | 0.00 | 1.08 |
| 30% | 13.51 | 3.14 | 3.40 | 0.00 | 1.47 |
| 40% | 18.02 | 3.60 | 3.35 | 0.00 | 2.27 |
| 50% | 22.52 | 4.01 | 3.31 | 0.00 | 3.47 |
| 60% | 27.02 | 4.47 | 3.20 | 0.00 | 4.63 |
| 70% | 31.53 | 4.91 | 3.10 | 0.00 | 7.96 |
| 80% | 36.03 | 5.44 | 3.01 | 0.00 | 13.09 |
| 90% | 40.54 | 5.74 | 2.97 | 0.00 | 16.91 |
| 100% | 45.04 | 5.80 | 2.91 | 0.00 | 0.00 |

FRV40

Double Bottom Tank No. 3 Center

Fr 29 – 39

Salt Water Ballast

|  |  | PORT |  |  |  |
| --- | --- | --- | --- | --- | --- |
|  | Salt Water | VCG | LCG | TCG | I/d |
|  | m tons | m abv bl | m aft fp | m off cl | m-ton |
| 10% | 4.52 | 1.26 | 21.19 | -3.31 | 5.28 |
| 20% | 9.04 | 1.45 | 21.10 | -3.51 | 9.35 |
| 30% | 13.56 | 1.62 | 21.06 | -3.63 | 12.83 |
| 40% | 18.08 | 1.76 | 21.04 | -3.72 | 15.87 |
| 50% | 22.60 | 1.90 | 21.02 | -3.80 | 18.38 |
| 60% | 27.11 | 2.03 | 21.02 | -3.86 | 20.64 |
| 70% | 31.63 | 2.16 | 21.01 | -3.91 | 22.74 |
| 80% | 36.15 | 2.28 | 21.00 | -3.96 | 24.66 |
| 90% | 40.67 | 2.40 | 21.00 | -4.00 | 26.42 |
| 100% | 45.19 | 2.51 | 21.00 | -4.04 | 0.00 |
|  |  | STBD |  |  |  |
|  | Salt Water | VCG | LCG | TCG | I/d |
|  | m tons | m abv bl | m aft fp | m off cl | m-ton |
| 10% | 4.52 | 1.26 | 21.19 | 3.31 | 5.28 |
| 20% | 9.04 | 1.45 | 21.10 | 3.51 | 9.35 |
| 30% | 13.56 | 1.62 | 21.06 | 3.63 | 12.83 |
| 40% | 18.08 | 1.76 | 21.04 | 3.72 | 15.87 |
| 50% | 22.60 | 1.90 | 21.02 | 3.80 | 18.38 |
| 60% | 27.11 | 2.03 | 21.02 | 3.86 | 20.64 |
| 70% | 31.63 | 2.16 | 21.01 | 3.91 | 22.74 |
| 80% | 36.15 | 2.28 | 21.00 | 3.96 | 24.66 |
| 90% | 40.67 | 2.40 | 21.00 | 4.00 | 26.42 |
| 100% | 45.19 | 2.51 | 21.00 | 4.04 | 0.00 |

FRV40

Double Bottom Tank No. 3 Center

Fr 29 – 39

Salt Water Ballast

|  |  | CENTER |  |  |  |
| --- | --- | --- | --- | --- | --- |
|  | Salt Water | VCG | LCG | TCG | I/d |
|  | m tons | m abv bl | m aft fp | m off cl | m-ton |
| 10% | 8.43 | 0.96 | 21.12 | 0.00 | 64.78 |
| 20% | 16.86 | 1.10 | 20.96 | 0.00 | 64.10 |
| 30% | 25.29 | 1.25 | 20.90 | 0.00 | 64.10 |
| 40% | 33.72 | 1.39 | 20.88 | 0.00 | 64.10 |
| 50% | 42.15 | 1.53 | 20.86 | 0.00 | 64.10 |
| 60% | 50.58 | 1.67 | 20.85 | 0.00 | 64.10 |
| 70% | 59.01 | 1.81 | 20.85 | 0.00 | 64.10 |
| 80% | 67.44 | 1.95 | 20.84 | 0.00 | 64.10 |
| 90% | 75.87 | 2.10 | 20.84 | 0.00 | 64.10 |
| 100% | 84.30 | 2.24 | 20.83 | 0.00 | 0.00 |

FRV40

Double Bottom Tank No. 4 C

Fr 39 – 49

Salt Water Ballast

|  |  | CENTER |  |  |  |
| --- | --- | --- | --- | --- | --- |
|  | Salt Water | VCG | LCG | TCG | I/d |
|  | m tons | m abv bl | m aft fp | m off cl | m-ton |
| 10% | 7.85 | 0.81 | 27.22 | 0.00 | 64.11 |
| 20% | 15.70 | 0.93 | 27.10 | 0.00 | 63.79 |
| 30% | 23.55 | 1.11 | 27.04 | 0.00 | 63.79 |
| 40% | 31.40 | 1.26 | 27.02 | 0.00 | 63.79 |
| 50% | 39.25 | 1.41 | 27.01 | 0.00 | 63.79 |
| 60% | 47.09 | 1.56 | 27.00 | 0.00 | 63.79 |
| 70% | 54.94 | 1.71 | 27.00 | 0.00 | 63.79 |
| 80% | 62.79 | 1.86 | 26.99 | 0.00 | 63.79 |
| 90% | 70.64 | 2.01 | 26.99 | 0.00 | 63.79 |
| 100% | 78.49 | 2.16 | 26.99 | 0.00 | 0.00 |

FRV40

Deep Tank No. 6F P/S

Fr 82 – 91

Salt Water Ballast

|  |  | PORT |  |  |  |
| --- | --- | --- | --- | --- | --- |
|  | Salt Water | VCG | LCG | TCG | I/d |
|  | m tons | m abv bl | m aft fp | m off cl | m-ton |
| 10% | 2.39 | 4.99 | 50.66 | -3.78 | 12.15 |
| 20% | 4.78 | 5.10 | 51.21 | -3.84 | 20.02 |
| 30% | 7.17 | 5.19 | 51.50 | -3.91 | 25.03 |
| 40% | 9.57 | 5.26 | 51.66 | -3.98 | 29.10 |
| 50% | 11.96 | 5.33 | 51.76 | -4.03 | 32.93 |
| 60% | 14.35 | 5.39 | 51.84 | -4.09 | 36.32 |
| 70% | 16.74 | 5.45 | 51.89 | -4.13 | 39.39 |
| 80% | 19.13 | 5.50 | 51.93 | -4.18 | 42.17 |
| 90% | 21.52 | 5.56 | 51.96 | -4.21 | 44.83 |
| 100% | 23.91 | 5.61 | 51.99 | -4.25 | 0.00 |
|  |  | STBD |  |  |  |
|  | Salt Water | VCG | LCG | TCG | I/d |
|  | m tons | m abv bl | m aft fp | m off cl | m-ton |
| 10% | 2.39 | 4.99 | 50.66 | 3.78 | 12.15 |
| 20% | 4.78 | 5.10 | 51.21 | 3.84 | 20.02 |
| 30% | 7.17 | 5.19 | 51.50 | 3.91 | 25.03 |
| 40% | 9.57 | 5.26 | 51.66 | 3.98 | 29.10 |
| 50% | 11.96 | 5.33 | 51.76 | 4.03 | 32.93 |
| 60% | 14.35 | 5.39 | 51.84 | 4.09 | 36.32 |
| 70% | 16.74 | 5.45 | 51.89 | 4.13 | 39.39 |
| 80% | 19.13 | 5.50 | 51.93 | 4.18 | 42.17 |
| 90% | 21.52 | 5.56 | 51.96 | 4.21 | 44.83 |
| 100% | 23.91 | 5.61 | 51.99 | 4.25 | 0.00 |

FRV40

Deep Tank No. 6A P/S

Fr 91 – 101

Salt Water Ballast

|  |  | PORT |  |  |  |
| --- | --- | --- | --- | --- | --- |
|  | Salt Water | VCG | LCG | TCG | I/d |
|  | m tons | m abv bl | m aft fp | m off cl | m-ton |
| 10% | 1.47 | 5.43 | 56.60 | -3.19 | 9.25 |
| 20% | 2.94 | 5.49 | 57.09 | -3.27 | 13.81 |
| 30% | 4.41 | 5.54 | 57.30 | -3.36 | 17.75 |
| 40% | 5.88 | 5.59 | 57.41 | -3.43 | 21.30 |
| 50% | 7.35 | 5.63 | 57.49 | -3.50 | 24.54 |
| 60% | 8.82 | 5.67 | 57.55 | -3.55 | 27.51 |
| 70% | 10.29 | 5.71 | 57.59 | -3.60 | 30.20 |
| 80% | 11.76 | 5.74 | 57.62 | -3.65 | 32.70 |
| 90% | 13.23 | 5.78 | 57.65 | -3.69 | 35.09 |
| 100% | 14.70 | 5.81 | 57.67 | -3.73 | 0.00 |
|  |  | STBD |  |  |  |
|  | Salt Water | VCG | LCG | TCG | I/d |
|  | m tons | m abv bl | m aft fp | m off cl | m-ton |
| 10% | 1.47 | 5.43 | 56.60 | 3.19 | 9.25 |
| 20% | 2.94 | 5.49 | 57.09 | 3.27 | 13.81 |
| 30% | 4.41 | 5.54 | 57.30 | 3.36 | 17.75 |
| 40% | 5.88 | 5.59 | 57.41 | 3.43 | 21.30 |
| 50% | 7.35 | 5.63 | 57.49 | 3.50 | 24.54 |
| 60% | 8.82 | 5.67 | 57.55 | 3.55 | 27.51 |
| 70% | 10.29 | 5.71 | 57.59 | 3.60 | 30.20 |
| 80% | 11.76 | 5.74 | 57.62 | 3.65 | 32.70 |
| 90% | 13.23 | 5.78 | 57.65 | 3.69 | 35.09 |
| 100% | 14.70 | 5.81 | 57.67 | 3.73 | 0.00 |

3.c.	Diesel Oil Tanks

FRV40

Deep Tank No. 1F P/S

Fr 7 – 13

Diesel Oil

|  |  | PORT |  |  |  |
| --- | --- | --- | --- | --- | --- |
|  | Diesel Oil | VCG | LCG | TCG | I/d |
|  | m tons | m abv bl | m aft fp | m off cl | m-ton |
| 10% | 2.75 | 1.53 | 6.65 | -0.78 | 1.64 |
| 20% | 5.49 | 1.80 | 6.62 | -0.85 | 1.80 |
| 30% | 8.23 | 2.07 | 6.62 | -0.88 | 1.74 |
| 40% | 10.98 | 2.33 | 6.61 | -0.89 | 1.70 |
| 50% | 13.72 | 2.59 | 6.61 | -0.89 | 1.79 |
| 60% | 16.47 | 2.85 | 6.61 | -0.90 | 2.02 |
| 70% | 19.21 | 3.11 | 6.61 | -0.91 | 2.41 |
| 80% | 21.96 | 3.36 | 6.61 | -0.93 | 2.95 |
| 90% | 24.70 | 3.60 | 6.60 | -0.96 | 3.60 |
| 95% | 26.08 | 3.72 | 6.60 | -0.97 | 3.95 |
|  |  | STBD |  |  |  |
|  | Diesel Oil | VCG | LCG | TCG | I/d |
|  | m tons | m abv bl | m aft fp | m off cl | m-ton |
| 10% | 2.75 | 1.53 | 6.65 | 0.78 | 1.64 |
| 20% | 5.49 | 1.80 | 6.62 | 0.85 | 1.80 |
| 30% | 8.23 | 2.07 | 6.62 | 0.88 | 1.74 |
| 40% | 10.98 | 2.33 | 6.61 | 0.89 | 1.70 |
| 50% | 13.72 | 2.59 | 6.61 | 0.89 | 1.79 |
| 60% | 16.47 | 2.85 | 6.61 | 0.90 | 2.02 |
| 70% | 19.21 | 3.11 | 6.61 | 0.91 | 2.41 |
| 80% | 21.96 | 3.36 | 6.61 | 0.93 | 2.95 |
| 90% | 24.70 | 3.60 | 6.60 | 0.96 | 3.60 |
| 95% | 26.08 | 3.72 | 6.60 | 0.97 | 3.95 |

FRV40

Deep Tank No. 2 P/S

Fr 19 – 29

Diesel Oil

|  |  | PORT |  |  |  |
| --- | --- | --- | --- | --- | --- |
|  | Diesel Oil | VCG | LCG | TCG | I/d |
|  | m tons | m abv bl | m aft fp | m off cl | m-ton |
| 10% | 5.18 | 1.68 | 15.36 | -3.20 | 2.60 |
| 20% | 10.37 | 2.01 | 15.30 | -3.33 | 4.04 |
| 30% | 15.55 | 2.31 | 15.28 | -3.41 | 5.03 |
| 40% | 20.74 | 2.59 | 15.27 | -3.46 | 5.93 |
| 50% | 25.92 | 2.85 | 15.27 | -3.51 | 6.82 |
| 60% | 31.10 | 3.10 | 15.26 | -3.55 | 7.83 |
| 70% | 36.29 | 3.34 | 15.25 | -3.59 | 8.89 |
| 80% | 41.47 | 3.57 | 15.24 | -3.62 | 10.02 |
| 90% | 46.66 | 3.80 | 15.23 | -3.65 | 11.18 |
| 95% | 49.25 | 3.91 | 15.22 | -3.67 | 11.76 |
|  |  | STBD |  |  |  |
|  | Diesel Oil | VCG | LCG | TCG | I/d |
|  | m tons | m abv bl | m aft fp | m off cl | m-ton |
| 10% | 5.18 | 1.68 | 15.36 | 3.20 | 2.60 |
| 20% | 10.37 | 2.01 | 15.30 | 3.33 | 4.04 |
| 30% | 15.55 | 2.31 | 15.28 | 3.41 | 5.03 |
| 40% | 20.74 | 2.59 | 15.27 | 3.46 | 5.93 |
| 50% | 25.92 | 2.85 | 15.27 | 3.51 | 6.82 |
| 60% | 31.10 | 3.10 | 15.26 | 3.55 | 7.83 |
| 70% | 36.29 | 3.34 | 15.25 | 3.59 | 8.89 |
| 80% | 41.47 | 3.57 | 15.24 | 3.62 | 10.02 |
| 90% | 46.66 | 3.80 | 15.23 | 3.65 | 11.18 |
| 95% | 49.25 | 3.91 | 15.22 | 3.67 | 11.76 |

FRV40

Double Bottom Tank No. 2 C

Fr 19 – 29

Diesel Oil

|  |  | CENTER |  |  |  |
| --- | --- | --- | --- | --- | --- |
|  | Diesel Oil | VCG | LCG | TCG | I/d |
|  | m tons | m abv bl | m aft fp | m off cl | m-ton |
| 10% | 5.05 | 1.32 | 13.03 | 0.00 | 21.78 |
| 20% | 10.11 | 1.57 | 13.01 | 0.00 | 21.65 |
| 30% | 15.16 | 1.83 | 13.01 | 0.00 | 21.65 |
| 40% | 20.21 | 2.08 | 13.00 | 0.00 | 21.67 |
| 50% | 25.26 | 2.34 | 13.00 | 0.00 | 21.67 |
| 60% | 30.32 | 2.59 | 13.00 | 0.00 | 21.64 |
| 70% | 35.37 | 2.84 | 13.00 | 0.00 | 21.57 |
| 80% | 40.42 | 3.10 | 13.00 | 0.00 | 21.47 |
| 90% | 45.47 | 3.35 | 13.00 | 0.00 | 21.35 |
| 95% | 48.00 | 3.48 | 13.00 | 0.00 | 21.28 |

FRV40

Double Bottom Tank No. 4 P/S

Fr 39 – 49

Diesel Oil

|  |  | PORT |  |  |  |
| --- | --- | --- | --- | --- | --- |
|  | Diesel Oil | VCG | LCG | TCG | I/d |
|  | m tons | m abv bl | m aft fp | m off cl | m-ton |
| 10% | 4.99 | 1.12 | 27.03 | -3.50 | 8.38 |
| 20% | 9.98 | 1.32 | 26.97 | -3.75 | 15.13 |
| 30% | 14.98 | 1.49 | 26.94 | -3.91 | 20.54 |
| 40% | 19.97 | 1.65 | 26.93 | -4.03 | 25.12 |
| 50% | 24.96 | 1.79 | 26.92 | -4.12 | 28.91 |
| 60% | 29.95 | 1.93 | 26.91 | -4.20 | 32.34 |
| 70% | 34.94 | 2.06 | 26.90 | -4.26 | 35.37 |
| 80% | 39.94 | 2.19 | 26.90 | -4.32 | 37.99 |
| 90% | 44.93 | 2.32 | 26.89 | -4.37 | 40.32 |
| 95% | 47.42 | 2.38 | 26.89 | -4.39 | 41.37 |
|  |  | STBD |  |  |  |
|  | Diesel Oil | VCG | LCG | TCG | I/d |
|  | m tons | m abv bl | m aft fp | m off cl | m-ton |
| 10% | 4.99 | 1.12 | 27.03 | 3.50 | 8.38 |
| 20% | 9.98 | 1.32 | 26.97 | 3.75 | 15.13 |
| 30% | 14.98 | 1.49 | 26.94 | 3.91 | 20.54 |
| 40% | 19.97 | 1.65 | 26.93 | 4.03 | 25.12 |
| 50% | 24.96 | 1.79 | 26.92 | 4.12 | 28.91 |
| 60% | 29.95 | 1.93 | 26.91 | 4.20 | 32.34 |
| 70% | 34.94 | 2.06 | 26.90 | 4.26 | 35.37 |
| 80% | 39.94 | 2.19 | 26.90 | 4.32 | 37.99 |
| 90% | 44.93 | 2.32 | 26.89 | 4.37 | 40.32 |
| 95% | 47.42 | 2.38 | 26.89 | 4.39 | 41.37 |

FRV40

Diesel Oil Day Tank P/S

Fr 69-1/2 – 72

Diesel Oil

|  |  | PORT |  |  |  |
| --- | --- | --- | --- | --- | --- |
|  | Diesel Oil | VCG | LCG | TCG | I/d |
|  | m tons | m abv bl | m aft fp | m off cl | m-ton |
| 10% | 1.08 | 4.20 | 42.81 | -6.03 | 0.30 |
| 20% | 2.16 | 4.53 | 42.82 | -6.17 | 0.59 |
| 30% | 3.24 | 4.81 | 42.83 | -6.26 | 0.78 |
| 40% | 4.32 | 5.06 | 42.83 | -6.32 | 0.85 |
| 50% | 5.40 | 5.30 | 42.84 | -6.35 | 0.85 |
| 60% | 6.48 | 5.53 | 42.84 | -6.38 | 0.85 |
| 70% | 7.56 | 5.76 | 42.84 | -6.39 | 0.85 |
| 80% | 8.64 | 5.98 | 42.84 | -6.41 | 0.85 |
| 90% | 9.72 | 6.21 | 42.84 | -6.42 | 0.85 |
| 95% | 10.26 | 6.32 | 42.84 | -6.42 | 0.85 |
|  |  | STBD |  |  |  |
|  | Diesel Oil | VCG | LCG | TCG | I/d |
|  | m tons | m abv bl | m aft fp | m off cl | m-ton |
| 10% | 1.08 | 4.20 | 42.81 | 6.03 | 0.30 |
| 20% | 2.16 | 4.53 | 42.82 | 6.17 | 0.59 |
| 30% | 3.24 | 4.81 | 42.83 | 6.26 | 0.78 |
| 40% | 4.32 | 5.06 | 42.83 | 6.32 | 0.85 |
| 50% | 5.40 | 5.30 | 42.84 | 6.35 | 0.85 |
| 60% | 6.48 | 5.53 | 42.84 | 6.38 | 0.85 |
| 70% | 7.56 | 5.76 | 42.84 | 6.39 | 0.85 |
| 80% | 8.64 | 5.98 | 42.84 | 6.41 | 0.85 |
| 90% | 9.72 | 6.21 | 42.84 | 6.42 | 0.85 |
| 95% | 10.26 | 6.32 | 42.84 | 6.42 | 0.85 |

FRV40

Deep Tank No. 5 P/S

Fr 72 – 82

Diesel Oil

|  |  | PORT |  |  |  |
| --- | --- | --- | --- | --- | --- |
|  | Diesel Oil | VCG | LCG | TCG | I/d |
|  | m tons | m abv bl | m aft fp | m off cl | m-ton |
| 10% | 4.44 | 3.85 | 44.84 | -3.88 | 9.92 |
| 20% | 8.88 | 4.09 | 45.29 | -4.05 | 18.63 |
| 30% | 13.31 | 4.28 | 45.61 | -4.15 | 25.62 |
| 40% | 17.75 | 4.44 | 45.82 | -4.25 | 30.88 |
| 50% | 22.19 | 4.55 | 45.95 | -4.32 | 35.56 |
| 60% | 26.63 | 4.68 | 46.04 | -4.38 | 39.74 |
| 70% | 31.07 | 4.79 | 46.11 | -4.44 | 43.35 |
| 80% | 35.50 | 4.91 | 46.17 | -4.50 | 46.39 |
| 90% | 39.94 | 5.01 | 46.21 | -4.54 | 48.80 |
| 95% | 42.16 | 5.07 | 46.23 | -4.56 | 49.77 |
|  |  | STBD |  |  |  |
|  | Diesel Oil | VCG | LCG | TCG | I/d |
|  | m tons | m abv bl | m aft fp | m off cl | m-ton |
| 10% | 4.44 | 3.85 | 44.84 | 3.88 | 9.92 |
| 20% | 8.88 | 4.09 | 45.29 | 4.05 | 18.63 |
| 30% | 13.31 | 4.28 | 45.61 | 4.15 | 25.62 |
| 40% | 17.75 | 4.44 | 45.82 | 4.25 | 30.88 |
| 50% | 22.19 | 4.55 | 45.95 | 4.32 | 35.56 |
| 60% | 26.63 | 4.68 | 46.04 | 4.38 | 39.74 |
| 70% | 31.07 | 4.79 | 46.11 | 4.44 | 43.35 |
| 80% | 35.50 | 4.91 | 46.17 | 4.50 | 46.39 |
| 90% | 39.94 | 5.01 | 46.21 | 4.54 | 48.80 |
| 95% | 42.16 | 5.07 | 46.23 | 4.56 | 49.77 |

3.d.	Fresh Water Tanks

FRV40

Fresh Water Tanks

|  |  | PORT Fr 29 - 33 |  |  |  |
| --- | --- | --- | --- | --- | --- |
|  | Fresh Water | VCG | LCG | TCG | I/d |
|  | m tons | m abv bl | m aft fp | m off cl | m-ton |
| 10% | 1.38 | 4.05 | 19.30 | -1.25 | 3.91 |
| 20% | 2.76 | 4.14 | 19.30 | -1.25 | 3.91 |
| 30% | 4.15 | 4.24 | 19.30 | -1.25 | 3.91 |
| 40% | 5.53 | 4.33 | 19.30 | -1.25 | 3.91 |
| 50% | 6.91 | 4.43 | 19.30 | -1.25 | 3.91 |
| 60% | 8.29 | 4.52 | 19.30 | -1.25 | 3.91 |
| 70% | 9.68 | 4.62 | 19.30 | -1.25 | 3.91 |
| 80% | 11.06 | 4.71 | 19.30 | -1.25 | 3.91 |
| 90% | 12.44 | 4.81 | 19.30 | -1.25 | 3.91 |
| 100% | 13.82 | 4.90 | 19.30 | -1.25 | 0.00 |
|  |  | STBD Fr 29 - 37 |  |  |  |
|  | Fresh Water | VCG | LCG | TCG | I/d |
|  | m tons | m abv bl | m aft fp | m off cl | m-ton |
| 10% | 2.21 | 4.05 | 20.20 | 1.25 | 6.25 |
| 20% | 4.42 | 4.14 | 20.20 | 1.25 | 6.25 |
| 30% | 6.64 | 4.24 | 20.20 | 1.25 | 6.25 |
| 40% | 8.85 | 4.33 | 20.20 | 1.25 | 6.25 |
| 50% | 11.06 | 4.43 | 20.20 | 1.25 | 6.25 |
| 60% | 13.27 | 4.52 | 20.20 | 1.25 | 6.25 |
| 70% | 15.48 | 4.62 | 20.20 | 1.25 | 6.25 |
| 80% | 17.69 | 4.71 | 20.20 | 1.25 | 6.25 |
| 90% | 19.90 | 4.81 | 20.20 | 1.25 | 6.25 |
| 100% | 22.12 | 4.90 | 20.20 | 1.25 | 0.00 |

3.e.	Sewage Tank

FRV40

Sewage Holding Tank

Fr 29 – 34

|  |  | PORT |  |  |  |
| --- | --- | --- | --- | --- | --- |
|  |  | VCG | LCG | TCG | I/d |
|  | m tons | m abv bl | m aft fp | m off cl | m-ton |
| 10% | 2.37 | 3.79 | 19.36 | -4.49 | 6.94 |
| 20% | 4.73 | 3.92 | 19.36 | -4.51 | 7.48 |
| 30% | 7.09 | 4.06 | 19.36 | -4.53 | 8.01 |
| 40% | 9.46 | 4.19 | 19.36 | -4.54 | 8.51 |
| 50% | 11.82 | 4.32 | 19.36 | -4.56 | 9.00 |
| 60% | 14.19 | 4.44 | 19.36 | -4.58 | 9.46 |
| 70% | 16.55 | 4.57 | 19.35 | -4.59 | 9.90 |
| 80% | 18.92 | 4.69 | 19.35 | -4.61 | 10.32 |
| 90% | 21.28 | 4.82 | 19.35 | -4.62 | 10.74 |
| 100% | 23.65 | 4.94 | 19.35 | -4.64 | 0.00 |

3.f.	Stores

FRV40

Stores

|  |  |  |  |  |  | Ship's Stores |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  | mld vol | vol | vcg | lcg | tcg |
| Tank Top |  |  |  |  |  |  |  |  |  |
| Locked Stores | fr | 29 | - | 32 | 16.29 | 13.03 | 4.94 | 18.72 | 4.32 |
| General Stores | fr | 32 | - | 39 | 44.27 | 35.42 | 4.92 | 21.76 | 4.62 |
| 2nd Deck |  |  |  |  |  |  |  |  |  |
| Bosun Stores | fr | 7 | - | 15 | 51.16 | 40.93 | 7.46 | 7.18 | -1.18 |
| Engineers Stores | fr | 77 | - | 82 | 53.39 | 42.71 | 7.40 | 46.60 | 5.75 |
| Main Deck |  |  |  |  |  |  |  |  |  |
| Freeze Stores | fr | 7 | - | 11 |  | 24.82 | 10.06 | 5.93 | -1.22 |
| Chill Stores | fr | 11 | - | 13 |  | 20.89 | 10.07 | 8.44 | -3.07 |
| Dry Stores | fr | 7 | - | 16 | 43.80 | 35.04 | 10.21 | 7.44 | 3.85 |
| Stewards Stores | fr | 16 | - | 19 | 19.06 | 15.25 | 10.15 | 10.89 | 4.47 |
| HazMat Stores | fr | 78 | - | 82 | 13.20 | 10.56 | 10.03 | 48.40 | -6.50 |
|  |  |  |  |  |  | 238.65 | 8.12 | 19.11 | 1.92 |
|  |  |  |  |  |  | Scientific Stores |  |  |  |
|  |  |  |  |  | mld vol | vol | vcg | lcg | tcg |
| Scientific Stores |  |  |  |  |  |  |  |  |  |
| Tank top | fr | 75 | - | 82 | 21.00 | 16.80 | 6.65 | 47.50 | 0.00 |
| 2nd Deck | fr | 72 | - | 82 | 79.48 | 63.58 | 7.40 | 47.07 | 1.03 |
| 2nd Deck | fr | 82 | - | 101 | 112.30 | 89.84 | 7.40 | 54.55 | 0.00 |
|  |  |  |  |  |  | 170.22 | 4.56 | 33.48 | 0.00 |
| Scientifc Freezer | fr | 56 | - | 62 |  | 12.60 | 10.03 | 35.88 | -1.50 |
| Notes: |  |  |  |  |  |  |  |  |  |
| 1. Volume is taken as 80% of molded volume, except for freeze and chill stores and scientific freezer |  |  |  |  |  |  |  |  |  |
| 2. Freezer and chill volumes based on 200 mm insulation on all boundaries |  |  |  |  |  |  |  |  |  |

4.a.	Summary

Loading conditions were developed with and without icing, which meet the stability requirements for the ship.  Eighty tons of medium density fixed ballast has been used in order to achieve acceptable values of KG and trim.  The loading conditions reflect a reasonable fuel burn / ballast sequence.

All loading conditions include an itinerant load of 50 tons at a center 2 meters above the main deck (10.65 m abv bl) per section 079b of the SOR as well as a service life growth margin.  The service life growth margin of 54.2 mt located 12.85 m above BL is 3% of lightship weight.  The KG of the item, when combined with the lightship KG results in an increase in lightship KG of 0.15 m.

### 4.b.	Maximum Allowable KG

A curve of maximum allowable virtual KG versus draft was developed based on the intact and damage stability analyses.  The limiting condition was damage for all but the deepest drafts.   The curve of Maximum Allowable KG is given in Figure 4-1.   The virtual KG is the actual KG adjusted to include the effect of free surface.  In loading conditions with trim by the bow of over 0.4 m, the maximum KG curve for trim of 0.5 m by the bow was used.

4.c.	Lightship Weight

The lightship characteristics (without fixed ballast) are as follows:

Lightship Weight		1805 mt

Lightship KG			 7.70 m abv BL

Lightship LCG		32.10 m aft FP

Lightship TCG		0.01 m off CL (+ to stbd)

These lightship values include an 8% margin on lightship weight and a KG margin of 0.33 meters.

4.d.	Loading Conditions

Loading condition summaries, along with the actual loading conditions are given in Section 4.d (without icing) and 4.e (with icing).    All loading conditions include 34 mt of water in the roll stabilization tank.

Crew & Effects reflect at total complement of 38 persons, with a weight of 170 kg/person (80 kg per person plus 90 kg effects).  The LCG and TCG is taken as the center of the staterooms.  The VCG is taken as 1.0 m above center of stateroom decks.

The center of the stores was taken as follows:

VCG  - 0.25 m below volumetric center of all ship’s stores spaces.

LCG and TCG taken at centroid of those spaces.

Figure 4-1

## 4.d.  Loading Conditions without Icing

FRV40-1

Loading Conditions (including Service Life Growth Margin)

|  |  | Fuel | SW Ball | FW | Draft | Trim | KG | KG All |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| A | Maximum Fuel | 398 | 0 | 36 | 5.97 | 0.30 | 7.45 | 7.57 | 0.12 |
|  | Burn (DO) 50% from DT#5P/S |  |  |  |  |  |  |  |  |
| B | Design Departure | 355 | 0 | 36 | 5.91 | 0.12 | 7.48 | 7.55 | 0.07 |
|  | Empty (DO) DT#5P/S |  |  |  |  |  |  |  |  |
| C | Mid-Voyage | 314 | 0 | 36 | 5.86 | -0.06 | 7.53 | 7.53 | 0.00 |
|  | Fill (SW) DT#6A P/S |  |  |  |  |  |  |  |  |
| D | Mid-Voyage | 314 | 29 | 36 | 5.90 | 0.19 | 7.51 | 7.55 | 0.04 |
|  | Burn (DO) 50% from DT#1F P/S |  |  |  |  |  |  |  |  |
| E | Mid-Voyage | 289 | 29 | 36 | 5.87 | 0.51 | 7.49 | 7.54 | 0.05 |
|  | Fill (SW) DB #3C |  |  |  |  |  |  |  |  |
| F | Mid-Voyage | 289 | 114 | 18 | 5.95 | 0.12 | 7.32 | 7.56 | 0.24 |
|  | Empty (DO) DT#1F P/S |  |  |  |  |  |  |  |  |
| G | Mid-Voyage | 261 | 114 | 18 | 5.92 | 0.39 | 7.38 | 7.55 | 0.17 |
|  | Burn (DO) 50% from DB#4P/S |  |  |  |  |  |  |  |  |
| H | Mid-Voyage | 216 | 114 | 18 | 5.86 | 0.50 | 7.46 | 7.53 | 0.07 |
|  | Empty (SW) DT#6A P/S |  |  |  |  |  |  |  |  |
| I | Mid-Voyage | 216 | 84 | 18 | 5.82 | 0.28 | 7.48 | 7.52 | 0.04 |
|  | Fill (SW) DB #4C |  |  |  |  |  |  |  |  |
| J | Mid-Voyage | 216 | 162 | 18 | 5.92 | 0.07 | 7.31 | 7.55 | 0.24 |
|  | Empty (DO) DB#4 P/S |  |  |  |  |  |  |  |  |
| K | Mid-Voyage | 167 | 162 | 18 | 5.86 | 0.20 | 7.42 | 7.53 | 0.11 |
|  | Empty (DO) DT#2C |  |  |  |  |  |  |  |  |
|  | Fill (SW) Forepeak 30% |  |  |  |  |  |  |  |  |
| L | Mid-Voyage | 119 | 176 | 18 | 5.81 | 0.42 | 7.48 | 7.52 | 0.04 |
|  | Fill (SW) DB#3 P/S |  |  |  |  |  |  |  |  |
| M | Mid-Voyage | 119 | 267 | 18 | 5.93 | -0.02 | 7.30 | 7.56 | 0.26 |
|  | Burn (DO) DT#2P/S |  |  |  |  |  |  |  |  |
|  | Fill (SW) Forepeak 100% |  |  |  |  |  |  |  |  |
| N | Arrival | 20 | 298 | 4 | 5.82 | 0.38 | 7.45 | 7.52 | 0.07 |

TRAS  Ver. 2.7

8/26/99

FRV40-1

Loading Condition        A Maximum Fuel  DO-398; SW-  0; FW-36

Item       Item           Weight     KG     LCG     TCG      I/d

No.                      M.Tons   m abv   m fwd   m off    at 0

bl    Sta 0     cl     heel

1   LS 8/05/99 wi 8% ma 1805.00    7.70   32.10    .01      .00

90   Fixed ballast         80.00    3.36   10.07   -.60      .00

9   Service life grwth    54.20   12.85   32.10    .00      .00

2   Crew & Effects         6.50   12.26   21.74   -.01      .00

3   Stores                24.20    7.87   19.11   1.92      .00

10   Lube Oil               4.50    2.23   34.70  -4.84     1.00

20   Roll tank             34.00   14.51   15.70    .00   478.00

100   Itinerant Load        50.00   10.65   39.70    .00      .00

200   Fresh Water             .00     .00     .00    .00      .00

210    FW Tk     P FW100%   13.82    4.90   19.30  -1.25     3.91

220    FW Tk     S FW100%   22.12    4.90   20.20   1.25     6.25

233   Sewage Hldg     0%      .00    3.79   19.36  -4.49      .00

300   Diesel Oil              .00     .00     .00    .00      .00

310    DT #1F    P DO 95%   26.08    3.72    6.60   -.97      .00

311    DT #1F    S DO 95%   26.08    3.72    6.60    .97      .00

320    DT #2     P DO 95%   49.25    3.91   15.22  -3.67      .00

321    DT #2     S DO 95%   49.25    3.91   15.22   3.67      .00

324    DT #2     C DO 95%   48.00    3.48   13.00    .00      .00

340    DB #4     P DO 95%   47.42    2.38   26.89  -4.39      .00

341    DB #4     S DO 95%   47.42    2.38   26.89   4.39      .00

350    DT #5     P DO 95%   42.16    5.07   46.23  -4.56      .00

351    DT #5     S DO 95%   42.16    5.07   46.23   4.56      .00

380    DO day    P DO 95%   10.26    6.32   42.84  -6.42      .00

381    DO day    S DO 95%   10.26    6.32   42.84   6.42      .00

309   DO free surface         .00     .00     .00    .00      .00

359    DT #5   P/S    FS      .00     .00     .00    .00   199.08

389    DO day  P/S    FS      .00     .00     .00    .00     1.70

TOTAL              2492.66    7.17   29.80    .00   689.94

Mean S.W. Draft     5.97 m.      LCG              29.80 m. from Sta 0

KM                  8.32 m.      LCB              29.45 m. from Sta 0

KG                  7.17 m.      Trim lever         .34 m. by stern

GM                  1.15 m.      Mmt to trim 1cm  28.37 m.-tons

Corr for F.S.        .28 m.      Trim               .30 m. by stern

GM Available         .87 m.      LCF              34.52 m. from Sta 0

Mmt to heel 1 dg   37.82 m-tons  Draft @ F.P.      5.79 m.

List                 .13 deg     Draft @ A.P.      6.09 m.

KG         =  7.17 m.

F.S. Corr. =   .28 m.

Virtual KG =  7.45 m.

TRAS  Ver. 2.7

8/26/99

FRV40-1

Loading Condition        B Design Depart DO-355; SW-  0; FW-36

Item       Item           Weight     KG     LCG     TCG      I/d

No.                      M.Tons   m abv   m fwd   m off    at 0

bl    Sta 0     cl     heel

1   LS 8/05/99 wi 8% ma 1805.00    7.70   32.10    .01      .00

90   Fixed ballast         80.00    3.36   10.07   -.60      .00

9   Service life grwth    54.20   12.85   32.10    .00      .00

2   Crew & Effects         6.50   12.26   21.74   -.01      .00

3   Stores                24.20    7.87   19.11   1.92      .00

10   Lube Oil               4.50    2.23   34.70  -4.84     1.00

20   Roll tank             34.00   14.51   15.70    .00   478.00

100   Itinerant Load        50.00   10.65   39.70    .00      .00

200   Fresh Water             .00     .00     .00    .00      .00

210    FW Tk     P FW100%   13.82    4.90   19.30  -1.25     3.91

220    FW Tk     S FW100%   22.12    4.90   20.20   1.25     6.25

233   Sewage Hldg     0%      .00    3.79   19.36  -4.49      .00

300   Diesel Oil              .00     .00     .00    .00      .00

310    DT #1F    P DO 95%   26.08    3.72    6.60   -.97      .00

311    DT #1F    S DO 95%   26.08    3.72    6.60    .97      .00

320    DT #2     P DO 95%   49.25    3.91   15.22  -3.67      .00

321    DT #2     S DO 95%   49.25    3.91   15.22   3.67      .00

324    DT #2     C DO 95%   48.00    3.48   13.00    .00      .00

340    DB #4     P DO 95%   47.42    2.38   26.89  -4.39      .00

341    DB #4     S DO 95%   47.42    2.38   26.89   4.39      .00

352    DT #5     P DO 50%   20.49    4.55   45.95  -4.32      .00

353    DT #5     S DO 50%   20.49    4.55   45.95   4.32      .00

380    DO day    P DO 95%   10.26    6.32   42.84  -6.42      .00

381    DO day    S DO 95%   10.26    6.32   42.84   6.42      .00

309   DO free surface         .00     .00     .00    .00      .00

359    DT #5   P/S    FS      .00     .00     .00    .00   199.08

389    DO day  P/S    FS      .00     .00     .00    .00     1.70

TOTAL              2449.32    7.20   29.50    .00   689.94

Mean S.W. Draft     5.91 m.      LCG              29.50 m. from Sta 0

KM                  8.31 m.      LCB              29.36 m. from Sta 0

KG                  7.20 m.      Trim lever         .14 m. by stern

GM                  1.12 m.      Mmt to trim 1cm  28.23 m.-tons

Corr for F.S.        .28 m.      Trim               .12 m. by stern

GM Available         .83 m.      LCF              34.52 m. from Sta 0

Mmt to heel 1 dg   35.63 m-tons  Draft @ F.P.      5.84 m.

List                 .14 deg     Draft @ A.P.      5.96 m.

KG         =  7.20 m.

F.S. Corr. =   .28 m.

Virtual KG =  7.48 m.

TRAS  Ver. 2.7

8/26/99

FRV40-1

Loading Condition        C Mid-voyage    DO-314; SW-  0; FW-36

Item       Item           Weight     KG     LCG     TCG      I/d

No.                      M.Tons   m abv   m fwd   m off    at 0

bl    Sta 0     cl     heel

1   LS 8/05/99 wi 8% ma 1805.00    7.70   32.10    .01      .00

90   Fixed ballast         80.00    3.36   10.07   -.60      .00

9   Service life grwth    54.20   12.85   32.10    .00      .00

2   Crew & Effects         6.50   12.26   21.74   -.01      .00

3   Stores                24.20    7.87   19.11   1.92      .00

10   Lube Oil               4.50    2.23   34.70  -4.84     1.00

20   Roll tank             34.00   14.51   15.70    .00   478.00

100   Itinerant Load        50.00   10.65   39.70    .00      .00

200   Fresh Water             .00     .00     .00    .00      .00

210    FW Tk     P FW100%   13.82    4.90   19.30  -1.25     3.91

220    FW Tk     S FW100%   22.12    4.90   20.20   1.25     6.25

233   Sewage Hldg     0%      .00    3.79   19.36  -4.49      .00

300   Diesel Oil              .00     .00     .00    .00      .00

310    DT #1F    P DO 95%   26.08    3.72    6.60   -.97      .00

311    DT #1F    S DO 95%   26.08    3.72    6.60    .97      .00

320    DT #2     P DO 95%   49.25    3.91   15.22  -3.67      .00

321    DT #2     S DO 95%   49.25    3.91   15.22   3.67      .00

324    DT #2     C DO 95%   48.00    3.48   13.00    .00      .00

340    DB #4     P DO 95%   47.42    2.38   26.89  -4.39      .00

341    DB #4     S DO 95%   47.42    2.38   26.89   4.39      .00

380    DO day    P DO 95%   10.26    6.32   42.84  -6.42      .00

381    DO day    S DO 95%   10.26    6.32   42.84   6.42      .00

309   DO free surface         .00     .00     .00    .00      .00

359    DT #5   P/S    FS      .00     .00     .00    .00   199.08

389    DO day  P/S    FS      .00     .00     .00    .00     1.70

TOTAL              2408.34    7.24   29.22    .00   689.94

Mean S.W. Draft     5.86 m.      LCG              29.22 m. from Sta 0

KM                  8.31 m.      LCB              29.28 m. from Sta 0

KG                  7.24 m.      Trim lever         .06 m. by bow

GM                  1.07 m.      Mmt to trim 1cm  27.98 m.-tons

Corr for F.S.        .29 m.      Trim               .05 m. by bow

GM Available         .78 m.      LCF              34.48 m. from Sta 0

Mmt to heel 1 dg   32.74 m-tons  Draft @ F.P.      5.89 m.

List                 .15 deg     Draft @ A.P.      5.84 m.

KG         =  7.24 m.

F.S. Corr. =   .29 m.

Virtual KG =  7.53 m.

TRAS  Ver. 2.7

8/26/99

FRV40-1

Loading Condition        D Mid-voyage    DO-314; SW- 29; FW-36

Item       Item           Weight     KG     LCG     TCG      I/d

No.                      M.Tons   m abv   m fwd   m off    at 0

bl    Sta 0     cl     heel

1   LS 8/05/99 wi 8% ma 1805.00    7.70   32.10    .01      .00

90   Fixed ballast         80.00    3.36   10.07   -.60      .00

9   Service life grwth    54.20   12.85   32.10    .00      .00

2   Crew & Effects         6.50   12.26   21.74   -.01      .00

3   Stores                24.20    7.87   19.11   1.92      .00

10   Lube Oil               4.50    2.23   34.70  -4.84     1.00

20   Roll tank             34.00   14.51   15.70    .00   478.00

100   Itinerant Load        50.00   10.65   39.70    .00      .00

200   Fresh Water             .00     .00     .00    .00      .00

210    FW Tk     P FW100%   13.82    4.90   19.30  -1.25     3.91

220    FW Tk     S FW100%   22.12    4.90   20.20   1.25     6.25

233   Sewage Hldg     0%      .00    3.79   19.36  -4.49      .00

300   Diesel Oil              .00     .00     .00    .00      .00

310    DT #1F    P DO 95%   26.08    3.72    6.60   -.97      .00

311    DT #1F    S DO 95%   26.08    3.72    6.60    .97      .00

320    DT #2     P DO 95%   49.25    3.91   15.22  -3.67      .00

321    DT #2     S DO 95%   49.25    3.91   15.22   3.67      .00

324    DT #2     C DO 95%   48.00    3.48   13.00    .00      .00

340    DB #4     P DO 95%   47.42    2.38   26.89  -4.39      .00

341    DB #4     S DO 95%   47.42    2.38   26.89   4.39      .00

380    DO day    P DO 95%   10.26    6.32   42.84  -6.42      .00

381    DO day    S DO 95%   10.26    6.32   42.84   6.42      .00

309   DO free surface         .00     .00     .00    .00      .00

359    DT #5   P/S    FS      .00     .00     .00    .00   199.08

389    DO day  P/S    FS      .00     .00     .00    .00     1.70

400   SW Ballast              .00     .00     .00    .00      .00

470    DT #6A    P SW100%   14.70    5.81   57.67  -3.73      .00

471    DT #6A    S SW100%   14.70    5.81   57.67   3.73      .00

TOTAL              2437.74    7.23   29.56    .00   689.94

Mean S.W. Draft     5.90 m.      LCG              29.56 m. from Sta 0

KM                  8.31 m.      LCB              29.34 m. from Sta 0

KG                  7.23 m.      Trim lever         .22 m. by stern

GM                  1.09 m.      Mmt to trim 1cm  28.19 m.-tons

Corr for F.S.        .28 m.      Trim               .19 m. by stern

GM Available         .80 m.      LCF              34.52 m. from Sta 0

Mmt to heel 1 dg   34.20 m-tons  Draft @ F.P.      5.78 m.

List                 .15 deg     Draft @ A.P.      5.98 m.

KG         =  7.23 m.

F.S. Corr. =   .28 m.

Virtual KG =  7.51 m.

TRAS  Ver. 2.7

8/26/99

FRV40-1

Loading Condition        E Mid-voyage    DO-289; SW- 29; FW-36

Item       Item           Weight     KG     LCG     TCG      I/d

No.                      M.Tons   m abv   m fwd   m off    at 0

bl    Sta 0     cl     heel

1   LS 8/05/99 wi 8% ma 1805.00    7.70   32.10    .01      .00

90   Fixed ballast         80.00    3.36   10.07   -.60      .00

9   Service life grwth    54.20   12.85   32.10    .00      .00

2   Crew & Effects         6.50   12.26   21.74   -.01      .00

3   Stores                24.20    7.87   19.11   1.92      .00

10   Lube Oil               4.50    2.23   34.70  -4.84     1.00

20   Roll tank             34.00   14.51   15.70    .00   478.00

100   Itinerant Load        50.00   10.65   39.70    .00      .00

200   Fresh Water             .00     .00     .00    .00      .00

210    FW Tk     P FW100%   13.82    4.90   19.30  -1.25     3.91

220    FW Tk     S FW100%   22.12    4.90   20.20   1.25     6.25

233   Sewage Hldg     0%      .00    3.79   19.36  -4.49      .00

300   Diesel Oil              .00     .00     .00    .00      .00

312    DT #1F    P DO 50%   13.72    2.59    6.61   -.89      .00

313    DT #1F    S DO 50%   13.72    2.59    6.61    .89      .00

320    DT #2     P DO 95%   49.25    3.91   15.22  -3.67      .00

321    DT #2     S DO 95%   49.25    3.91   15.22   3.67      .00

324    DT #2     C DO 95%   48.00    3.48   13.00    .00      .00

340    DB #4     P DO 95%   47.42    2.38   26.89  -4.39      .00

341    DB #4     S DO 95%   47.42    2.38   26.89   4.39      .00

380    DO day    P DO 95%   10.26    6.32   42.84  -6.42      .00

381    DO day    S DO 95%   10.26    6.32   42.84   6.42      .00

309   DO free surface         .00     .00     .00    .00      .00

349    DB #4   P/S    FS      .00     .00     .00    .00    82.74

389    DO day  P/S    FS      .00     .00     .00    .00     1.70

400   SW Ballast              .00     .00     .00    .00      .00

470    DT #6A    P SW100%   14.70    5.81   57.67  -3.73      .00

471    DT #6A    S SW100%   14.70    5.81   57.67   3.73      .00

TOTAL              2413.04    7.25   29.80    .00   573.60

Mean S.W. Draft     5.87 m.      LCG              29.80 m. from Sta 0

KM                  8.31 m.      LCB              29.29 m. from Sta 0

KG                  7.25 m.      Trim lever         .51 m. by stern

GM                  1.06 m.      Mmt to trim 1cm  28.02 m.-tons

Corr for F.S.        .24 m.      Trim               .44 m. by stern

GM Available         .82 m.      LCF              34.49 m. from Sta 0

Mmt to heel 1 dg   34.64 m-tons  Draft @ F.P.      5.60 m.

List                 .15 deg     Draft @ A.P.      6.04 m.

KG         =  7.25 m.

F.S. Corr. =   .24 m.

Virtual KG =  7.49 m.

TRAS  Ver. 2.7

8/26/99

FRV40-1

Loading Condition        F Mid-voyage    DO-289; SW-114; FW-18

Item       Item           Weight     KG     LCG     TCG      I/d

No.                      M.Tons   m abv   m fwd   m off    at 0

bl    Sta 0     cl     heel

1   LS 8/05/99 wi 8% ma 1805.00    7.70   32.10    .01      .00

90   Fixed ballast         80.00    3.36   10.07   -.60      .00

9   Service life grwth    54.20   12.85   32.10    .00      .00

2   Crew & Effects         6.50   12.26   21.74   -.01      .00

3   Stores                24.20    7.87   19.11   1.92      .00

10   Lube Oil               4.50    2.23   34.70  -4.84     1.00

20   Roll tank             34.00   14.51   15.70    .00   478.00

100   Itinerant Load        50.00   10.65   39.70    .00      .00

200   Fresh Water             .00     .00     .00    .00      .00

211    FW Tk     P FW 50%    6.91    4.43   19.30  -1.25     3.91

221    FW Tk     S FW 50%   11.06    4.43   20.20   1.25     6.25

233   Sewage Hldg     0%      .00    3.79   19.36  -4.49      .00

300   Diesel Oil              .00     .00     .00    .00      .00

312    DT #1F    P DO 50%   13.72    2.59    6.61   -.89      .00

313    DT #1F    S DO 50%   13.72    2.59    6.61    .89      .00

320    DT #2     P DO 95%   49.25    3.91   15.22  -3.67      .00

321    DT #2     S DO 95%   49.25    3.91   15.22   3.67      .00

324    DT #2     C DO 95%   48.00    3.48   13.00    .00      .00

340    DB #4     P DO 95%   47.42    2.38   26.89  -4.39      .00

341    DB #4     S DO 95%   47.42    2.38   26.89   4.39      .00

380    DO day    P DO 95%   10.26    6.32   42.84  -6.42      .00

381    DO day    S DO 95%   10.26    6.32   42.84   6.42      .00

309   DO free surface         .00     .00     .00    .00      .00

349    DB #4   P/S    FS      .00     .00     .00    .00    82.74

389    DO day  P/S    FS      .00     .00     .00    .00     1.70

400   SW Ballast              .00     .00     .00    .00      .00

434    DB #3     C SW100%   84.30    2.24   20.83    .00      .00

470    DT #6A    P SW100%   14.70    5.81   57.67  -3.73      .00

471    DT #6A    S SW100%   14.70    5.81   57.67   3.73      .00

TOTAL              2479.37    7.09   29.57    .00   573.60

Mean S.W. Draft     5.95 m.      LCG              29.57 m. from Sta 0

KM                  8.32 m.      LCB              29.43 m. from Sta 0

KG                  7.09 m.      Trim lever         .14 m. by stern

GM                  1.22 m.      Mmt to trim 1cm  28.33 m.-tons

Corr for F.S.        .23 m.      Trim               .12 m. by stern

GM Available         .99 m.      LCF              34.52 m. from Sta 0

Mmt to heel 1 dg   42.90 m-tons  Draft @ F.P.      5.88 m.

List                -.00 deg     Draft @ A.P.      6.00 m.

KG         =  7.09 m.

F.S. Corr. =   .23 m.

Virtual KG =  7.32 m.

TRAS  Ver. 2.7

8/26/99

FRV40-1

Loading Condition        G Mid-voyage    DO-261; SW-114; FW-18

Item       Item           Weight     KG     LCG     TCG      I/d

No.                      M.Tons   m abv   m fwd   m off    at 0

bl    Sta 0     cl     heel

1   LS 8/05/99 wi 8% ma 1805.00    7.70   32.10    .01      .00

90   Fixed ballast         80.00    3.36   10.07   -.60      .00

9   Service life grwth    54.20   12.85   32.10    .00      .00

2   Crew & Effects         6.50   12.26   21.74   -.01      .00

3   Stores                24.20    7.87   19.11   1.92      .00

10   Lube Oil               4.50    2.23   34.70  -4.84     1.00

20   Roll tank             34.00   14.51   15.70    .00   478.00

100   Itinerant Load        50.00   10.65   39.70    .00      .00

200   Fresh Water             .00     .00     .00    .00      .00

211    FW Tk     P FW 50%    6.91    4.43   19.30  -1.25     3.91

221    FW Tk     S FW 50%   11.06    4.43   20.20   1.25     6.25

233   Sewage Hldg     0%      .00    3.79   19.36  -4.49      .00

300   Diesel Oil              .00     .00     .00    .00      .00

320    DT #2     P DO 95%   49.25    3.91   15.22  -3.67      .00

321    DT #2     S DO 95%   49.25    3.91   15.22   3.67      .00

324    DT #2     C DO 95%   48.00    3.48   13.00    .00      .00

340    DB #4     P DO 95%   47.42    2.38   26.89  -4.39      .00

341    DB #4     S DO 95%   47.42    2.38   26.89   4.39      .00

380    DO day    P DO 95%   10.26    6.32   42.84  -6.42      .00

381    DO day    S DO 95%   10.26    6.32   42.84   6.42      .00

309   DO free surface         .00     .00     .00    .00      .00

349    DB #4   P/S    FS      .00     .00     .00    .00    82.74

389    DO day  P/S    FS      .00     .00     .00    .00     1.70

400   SW Ballast              .00     .00     .00    .00      .00

434    DB #3     C SW100%   84.30    2.24   20.83    .00      .00

470    DT #6A    P SW100%   14.70    5.81   57.67  -3.73      .00

471    DT #6A    S SW100%   14.70    5.81   57.67   3.73      .00

TOTAL              2451.92    7.14   29.82    .00   573.60

Mean S.W. Draft     5.92 m.      LCG              29.82 m. from Sta 0

KM                  8.31 m.      LCB              29.37 m. from Sta 0

KG                  7.14 m.      Trim lever         .45 m. by stern

GM                  1.17 m.      Mmt to trim 1cm  28.24 m.-tons

Corr for F.S.        .23 m.      Trim               .39 m. by stern

GM Available         .94 m.      LCF              34.52 m. from Sta 0

Mmt to heel 1 dg   40.10 m-tons  Draft @ F.P.      5.68 m.

List                -.00 deg     Draft @ A.P.      6.08 m.

KG         =  7.14 m.

F.S. Corr. =   .23 m.

Virtual KG =  7.38 m.

TRAS  Ver. 2.7

8/26/99

FRV40-1

Loading Condition        H Mid-voyage    DO-216; SW-114; FW-18

Item       Item           Weight     KG     LCG     TCG      I/d

No.                      M.Tons   m abv   m fwd   m off    at 0

bl    Sta 0     cl     heel

1   LS 8/05/99 wi 8% ma 1805.00    7.70   32.10    .01      .00

90   Fixed ballast         80.00    3.36   10.07   -.60      .00

9   Service life grwth    54.20   12.85   32.10    .00      .00

2   Crew & Effects         6.50   12.26   21.74   -.01      .00

3   Stores                24.20    7.87   19.11   1.92      .00

10   Lube Oil               4.50    2.23   34.70  -4.84     1.00

20   Roll tank             34.00   14.51   15.70    .00   478.00

100   Itinerant Load        50.00   10.65   39.70    .00      .00

200   Fresh Water             .00     .00     .00    .00      .00

211    FW Tk     P FW 50%    6.91    4.43   19.30  -1.25     3.91

221    FW Tk     S FW 50%   11.06    4.43   20.20   1.25     6.25

233   Sewage Hldg     0%      .00    3.79   19.36  -4.49      .00

300   Diesel Oil              .00     .00     .00    .00      .00

320    DT #2     P DO 95%   49.25    3.91   15.22  -3.67      .00

321    DT #2     S DO 95%   49.25    3.91   15.22   3.67      .00

324    DT #2     C DO 95%   48.00    3.48   13.00    .00      .00

342    DB #4     P DO 50%   24.96    1.79   26.92  -4.12      .00

343    DB #4     S DO 50%   24.96    1.79   26.92   4.12      .00

380    DO day    P DO 95%   10.26    6.32   42.84  -6.42      .00

381    DO day    S DO 95%   10.26    6.32   42.84   6.42      .00

309   DO free surface         .00     .00     .00    .00      .00

349    DB #4   P/S    FS      .00     .00     .00    .00    82.74

400   SW Ballast              .00     .00     .00    .00      .00

434    DB #3     C SW100%   84.30    2.24   20.83    .00      .00

470    DT #6A    P SW100%   14.70    5.81   57.67  -3.73      .00

471    DT #6A    S SW100%   14.70    5.81   57.67   3.73      .00

TOTAL              2407.00    7.22   29.88    .00   571.90

Mean S.W. Draft     5.86 m.      LCG              29.88 m. from Sta 0

KM                  8.31 m.      LCB              29.27 m. from Sta 0

KG                  7.22 m.      Trim lever         .61 m. by stern

GM                  1.09 m.      Mmt to trim 1cm  27.97 m.-tons

Corr for F.S.        .24 m.      Trim               .50 m. by stern

GM Available         .85 m.      LCF              34.48 m. from Sta 0

Mmt to heel 1 dg   35.77 m-tons  Draft @ F.P.      5.55 m.

List                -.00 deg     Draft @ A.P.      6.07 m.

KG         =  7.22 m.

F.S. Corr. =   .24 m.

Virtual KG =  7.46 m.

TRAS  Ver. 2.7

8/26/99

FRV40-1

Loading Condition        I Mid-voyage    DO-216; SW- 84; FW-18

Item       Item           Weight     KG     LCG     TCG      I/d

No.                      M.Tons   m abv   m fwd   m off    at 0

bl    Sta 0     cl     heel

1   LS 8/05/99 wi 8% ma 1805.00    7.70   32.10    .01      .00

90   Fixed ballast         80.00    3.36   10.07   -.60      .00

9   Service life grwth    54.20   12.85   32.10    .00      .00

2   Crew & Effects         6.50   12.26   21.74   -.01      .00

3   Stores                24.20    7.87   19.11   1.92      .00

10   Lube Oil               4.50    2.23   34.70  -4.84     1.00

20   Roll tank             34.00   14.51   15.70    .00   478.00

100   Itinerant Load        50.00   10.65   39.70    .00      .00

200   Fresh Water             .00     .00     .00    .00      .00

211    FW Tk     P FW 50%    6.91    4.43   19.30  -1.25     3.91

221    FW Tk     S FW 50%   11.06    4.43   20.20   1.25     6.25

233   Sewage Hldg     0%      .00    3.79   19.36  -4.49      .00

300   Diesel Oil              .00     .00     .00    .00      .00

320    DT #2     P DO 95%   49.25    3.91   15.22  -3.67      .00

321    DT #2     S DO 95%   49.25    3.91   15.22   3.67      .00

324    DT #2     C DO 95%   48.00    3.48   13.00    .00      .00

342    DB #4     P DO 50%   24.96    1.79   26.92  -4.12      .00

343    DB #4     S DO 50%   24.96    1.79   26.92   4.12      .00

380    DO day    P DO 95%   10.26    6.32   42.84  -6.42      .00

381    DO day    S DO 95%   10.26    6.32   42.84   6.42      .00

309   DO free surface         .00     .00     .00    .00      .00

349    DB #4   P/S    FS      .00     .00     .00    .00    82.74

400   SW Ballast              .00     .00     .00    .00      .00

434    DB #3     C SW100%   84.30    2.24   20.83    .00      .00

TOTAL              2377.60    7.24   29.54    .00   571.90

Mean S.W. Draft     5.82 m.      LCG              29.54 m. from Sta 0

KM                  8.31 m.      LCB              29.21 m. from Sta 0

KG                  7.24 m.      Trim lever         .33 m. by stern

GM                  1.07 m.      Mmt to trim 1cm  27.77 m.-tons

Corr for F.S.        .24 m.      Trim               .28 m. by stern

GM Available         .83 m.      LCF              34.45 m. from Sta 0

Mmt to heel 1 dg   34.32 m-tons  Draft @ F.P.      5.65 m.

List                -.00 deg     Draft @ A.P.      5.93 m.

KG         =  7.24 m.

F.S. Corr. =   .24 m.

Virtual KG =  7.48 m.

TRAS  Ver. 2.7

8/26/99

FRV40-1

Loading Condition        J Mid-voyage    DO-216; SW-162; FW-18

Item       Item           Weight     KG     LCG     TCG      I/d

No.                      M.Tons   m abv   m fwd   m off    at 0

bl    Sta 0     cl     heel

1   LS 8/05/99 wi 8% ma 1805.00    7.70   32.10    .01      .00

90   Fixed ballast         80.00    3.36   10.07   -.60      .00

9   Service life grwth    54.20   12.85   32.10    .00      .00

2   Crew & Effects         6.50   12.26   21.74   -.01      .00

3   Stores                24.20    7.87   19.11   1.92      .00

10   Lube Oil               4.50    2.23   34.70  -4.84     1.00

20   Roll tank             34.00   14.51   15.70    .00   478.00

100   Itinerant Load        50.00   10.65   39.70    .00      .00

200   Fresh Water             .00     .00     .00    .00      .00

211    FW Tk     P FW 50%    6.91    4.43   19.30  -1.25     3.91

221    FW Tk     S FW 50%   11.06    4.43   20.20   1.25     6.25

233   Sewage Hldg     0%      .00    3.79   19.36  -4.49      .00

300   Diesel Oil              .00     .00     .00    .00      .00

320    DT #2     P DO 95%   49.25    3.91   15.22  -3.67      .00

321    DT #2     S DO 95%   49.25    3.91   15.22   3.67      .00

324    DT #2     C DO 95%   48.00    3.48   13.00    .00      .00

342    DB #4     P DO 50%   24.96    1.79   26.92  -4.12      .00

343    DB #4     S DO 50%   24.96    1.79   26.92   4.12      .00

380    DO day    P DO 95%   10.26    6.32   42.84  -6.42      .00

381    DO day    S DO 95%   10.26    6.32   42.84   6.42      .00

309   DO free surface         .00     .00     .00    .00      .00

349    DB #4   P/S    FS      .00     .00     .00    .00    82.74

400   SW Ballast              .00     .00     .00    .00      .00

434    DB #3     C SW100%   84.30    2.24   20.83    .00      .00

440    DB #4     C SW100%   78.52    2.15   26.99    .00      .00

TOTAL              2456.12    7.08   29.45    .00   571.90

Mean S.W. Draft     5.92 m.      LCG              29.45 m. from Sta 0

KM                  8.31 m.      LCB              29.38 m. from Sta 0

KG                  7.08 m.      Trim lever         .08 m. by stern

GM                  1.24 m.      Mmt to trim 1cm  28.25 m.-tons

Corr for F.S.        .23 m.      Trim               .07 m. by stern

GM Available        1.01 m.      LCF              34.52 m. from Sta 0

Mmt to heel 1 dg   43.16 m-tons  Draft @ F.P.      5.88 m.

List                -.00 deg     Draft @ A.P.      5.95 m.

KG         =  7.08 m.

F.S. Corr. =   .23 m.

Virtual KG =  7.31 m.

TRAS  Ver. 2.7

8/26/99

FRV40-1

Loading Condition        K Mid-voyage    DO-167; SW-162; FW-18

Item       Item           Weight     KG     LCG     TCG      I/d

No.                      M.Tons   m abv   m fwd   m off    at 0

bl    Sta 0     cl     heel

1   LS 8/05/99 wi 8% ma 1805.00    7.70   32.10    .01      .00

90   Fixed ballast         80.00    3.36   10.07   -.60      .00

9   Service life grwth    54.20   12.85   32.10    .00      .00

2   Crew & Effects         6.50   12.26   21.74   -.01      .00

3   Stores                24.20    7.87   19.11   1.92      .00

10   Lube Oil               4.50    2.23   34.70  -4.84     1.00

20   Roll tank             34.00   14.51   15.70    .00   478.00

100   Itinerant Load        50.00   10.65   39.70    .00      .00

200   Fresh Water             .00     .00     .00    .00      .00

211    FW Tk     P FW 50%    6.91    4.43   19.30  -1.25     3.91

221    FW Tk     S FW 50%   11.06    4.43   20.20   1.25     6.25

233   Sewage Hldg     0%      .00    3.79   19.36  -4.49      .00

300   Diesel Oil              .00     .00     .00    .00      .00

320    DT #2     P DO 95%   49.25    3.91   15.22  -3.67      .00

321    DT #2     S DO 95%   49.25    3.91   15.22   3.67      .00

324    DT #2     C DO 95%   48.00    3.48   13.00    .00      .00

380    DO day    P DO 95%   10.26    6.32   42.84  -6.42      .00

381    DO day    S DO 95%   10.26    6.32   42.84   6.42      .00

309   DO free surface         .00     .00     .00    .00      .00

349    DB #4   P/S    FS      .00     .00     .00    .00    82.74

400   SW Ballast              .00     .00     .00    .00      .00

434    DB #3     C SW100%   84.30    2.24   20.83    .00      .00

440    DB #4     C SW100%   78.52    2.15   26.99    .00      .00

TOTAL              2406.20    7.18   29.51    .00   571.90

Mean S.W. Draft     5.86 m.      LCG              29.51 m. from Sta 0

KM                  8.31 m.      LCB              29.27 m. from Sta 0

KG                  7.18 m.      Trim lever         .23 m. by stern

GM                  1.12 m.      Mmt to trim 1cm  27.97 m.-tons

Corr for F.S.        .24 m.      Trim               .20 m. by stern

GM Available         .89 m.      LCF              34.48 m. from Sta 0

Mmt to heel 1 dg   37.25 m-tons  Draft @ F.P.      5.74 m.

List                -.00 deg     Draft @ A.P.      5.94 m.

KG         =  7.18 m.

F.S. Corr. =   .24 m.

Virtual KG =  7.42 m.

TRAS  Ver. 2.7

8/26/99

FRV40-1

Loading Condition        L Mid-voyage    DO-119; SW-176; FW-18

Item       Item           Weight     KG     LCG     TCG      I/d

No.                      M.Tons   m abv   m fwd   m off    at 0

bl    Sta 0     cl     heel

1   LS 8/05/99 wi 8% ma 1805.00    7.70   32.10    .01      .00

90   Fixed ballast         80.00    3.36   10.07   -.60      .00

9   Service life grwth    54.20   12.85   32.10    .00      .00

2   Crew & Effects         6.50   12.26   21.74   -.01      .00

3   Stores                24.20    7.87   19.11   1.92      .00

10   Lube Oil               4.50    2.23   34.70  -4.84     1.00

20   Roll tank             34.00   14.51   15.70    .00   478.00

100   Itinerant Load        50.00   10.65   39.70    .00      .00

200   Fresh Water             .00     .00     .00    .00      .00

211    FW Tk     P FW 50%    6.91    4.43   19.30  -1.25     3.91

221    FW Tk     S FW 50%   11.06    4.43   20.20   1.25     6.25

233   Sewage Hldg     0%      .00    3.79   19.36  -4.49      .00

300   Diesel Oil              .00     .00     .00    .00      .00

320    DT #2     P DO 95%   49.25    3.91   15.22  -3.67      .00

321    DT #2     S DO 95%   49.25    3.91   15.22   3.67      .00

380    DO day    P DO 95%   10.26    6.32   42.84  -6.42      .00

381    DO day    S DO 95%   10.26    6.32   42.84   6.42      .00

309   DO free surface         .00     .00     .00    .00      .00

349    DB #4   P/S    FS      .00     .00     .00    .00    82.74

400   SW Ballast              .00     .00     .00    .00      .00

402    Forepk    C SW 30%   13.51    3.14    3.40    .00     1.50

434    DB #3     C SW100%   84.30    2.24   20.83    .00      .00

440    DB #4     C SW100%   78.52    2.15   26.99    .00      .00

TOTAL              2371.71    7.24   29.69    .00   573.40

Mean S.W. Draft     5.81 m.      LCG              29.69 m. from Sta 0

KM                  8.30 m.      LCB              29.20 m. from Sta 0

KG                  7.24 m.      Trim lever         .49 m. by stern

GM                  1.07 m.      Mmt to trim 1cm  27.72 m.-tons

Corr for F.S.        .24 m.      Trim               .42 m. by stern

GM Available         .83 m.      LCF              34.44 m. from Sta 0

Mmt to heel 1 dg   34.19 m-tons  Draft @ F.P.      5.56 m.

List                -.00 deg     Draft @ A.P.      5.98 m.

KG         =  7.24 m.

F.S. Corr. =   .24 m.

Virtual KG =  7.48 m.

TRAS  Ver. 2.7

8/26/99

FRV40-1

Loading Condition        M Mid-voyage    DO-119; SW-267; FW-18

Item       Item           Weight     KG     LCG     TCG      I/d

No.                      M.Tons   m abv   m fwd   m off    at 0

bl    Sta 0     cl     heel

1   LS 8/05/99 wi 8% ma 1805.00    7.70   32.10    .01      .00

90   Fixed ballast         80.00    3.36   10.07   -.60      .00

9   Service life grwth    54.20   12.85   32.10    .00      .00

2   Crew & Effects         6.50   12.26   21.74   -.01      .00

3   Stores                24.20    7.87   19.11   1.92      .00

10   Lube Oil               4.50    2.23   34.70  -4.84     1.00

20   Roll tank             34.00   14.51   15.70    .00   478.00

100   Itinerant Load        50.00   10.65   39.70    .00      .00

200   Fresh Water             .00     .00     .00    .00      .00

211    FW Tk     P FW 50%    6.91    4.43   19.30  -1.25     3.91

221    FW Tk     S FW 50%   11.06    4.43   20.20   1.25     6.25

233   Sewage Hldg     0%      .00    3.79   19.36  -4.49      .00

300   Diesel Oil              .00     .00     .00    .00      .00

320    DT #2     P DO 95%   49.25    3.91   15.22  -3.67      .00

321    DT #2     S DO 95%   49.25    3.91   15.22   3.67      .00

380    DO day    P DO 95%   10.26    6.32   42.84  -6.42      .00

381    DO day    S DO 95%   10.26    6.32   42.84   6.42      .00

309   DO free surface         .00     .00     .00    .00      .00

349    DB #4   P/S    FS      .00     .00     .00    .00    82.74

400   SW Ballast              .00     .00     .00    .00      .00

402    Forepk    C SW 30%   13.51    3.14    3.40    .00     1.50

430    DB #3     P SW100%   45.19    2.51   21.00  -4.04      .00

431    DB #3     S SW100%   45.19    2.51   21.00   4.04      .00

434    DB #3     C SW100%   84.30    2.24   20.83    .00      .00

440    DB #4     C SW100%   78.52    2.15   26.99    .00      .00

TOTAL              2462.09    7.06   29.37    .00   573.40

Mean S.W. Draft     5.93 m.      LCG              29.37 m. from Sta 0

KM                  8.32 m.      LCB              29.39 m. from Sta 0

KG                  7.06 m.      Trim lever         .02 m. by bow

GM                  1.25 m.      Mmt to trim 1cm  28.27 m.-tons

Corr for F.S.        .23 m.      Trim               .02 m. by bow

GM Available        1.02 m.      LCF              34.52 m. from Sta 0

Mmt to heel 1 dg   43.79 m-tons  Draft @ F.P.      5.94 m.

List                -.00 deg     Draft @ A.P.      5.93 m.

KG         =  7.06 m.

F.S. Corr. =   .23 m.

Virtual KG =  7.30 m.

TRAS  Ver. 2.7

8/26/99

FRV40-1

Loading Condition        N Mid-voyage    DO- 20; SW-298; FW- 4

Item       Item           Weight     KG     LCG     TCG      I/d

No.                      M.Tons   m abv   m fwd   m off    at 0

bl    Sta 0     cl     heel

1   LS 8/05/99 wi 8% ma 1805.00    7.70   32.10    .01      .00

90   Fixed ballast         80.00    3.36   10.07   -.60      .00

9   Service life grwth    54.20   12.85   32.10    .00      .00

2   Crew & Effects         6.50   12.26   21.74   -.01      .00

3   Stores                24.20    7.87   19.11   1.92      .00

10   Lube Oil               4.50    2.23   34.70  -4.84     1.00

20   Roll tank             34.00   14.51   15.70    .00   478.00

100   Itinerant Load        50.00   10.65   39.70    .00      .00

200   Fresh Water             .00     .00     .00    .00      .00

212    FW Tk     P FW 10%    1.38    4.05   19.30  -1.25     3.91

222    FW Tk     S FW 10%    2.21    4.05   20.20   1.25     6.25

233   Sewage Hldg     0%      .00    3.79   19.36  -4.49      .00

300   Diesel Oil              .00     .00     .00    .00      .00

380    DO day    P DO 95%   10.26    6.32   42.84  -6.42      .00

381    DO day    S DO 95%   10.26    6.32   42.84   6.42      .00

309   DO free surface         .00     .00     .00    .00      .00

349    DB #4   P/S    FS      .00     .00     .00    .00    82.74

400   SW Ballast              .00     .00     .00    .00      .00

401    Forepk    C SW100%   45.05    5.80    2.91    .00      .00

430    DB #3     P SW100%   45.19    2.51   21.00  -4.04      .00

431    DB #3     S SW100%   45.19    2.51   21.00   4.04      .00

434    DB #3     C SW100%   84.30    2.24   20.83    .00      .00

440    DB #4     C SW100%   78.52    2.15   26.99    .00      .00

TOTAL              2380.76    7.21   29.66   -.00   571.90

Mean S.W. Draft     5.82 m.      LCG              29.66 m. from Sta 0

KM                  8.31 m.      LCB              29.22 m. from Sta 0

KG                  7.21 m.      Trim lever         .45 m. by stern

GM                  1.10 m.      Mmt to trim 1cm  27.79 m.-tons

Corr for F.S.        .24 m.      Trim               .38 m. by stern

GM Available         .86 m.      LCF              34.45 m. from Sta 0

Mmt to heel 1 dg   35.65 m-tons  Draft @ F.P.      5.59 m.

List                -.12 deg     Draft @ A.P.      5.98 m.

KG         =  7.21 m.

F.S. Corr. =   .24 m.

Virtual KG =  7.45 m.

## 4.e.   Loading Conditions with Icing

FRV40-1

Loading Conditions with Icing (including Service Life Growth Margin)

|  |  | Fuel | SW Ball | FW | Draft | Trim | KG | KG All |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| A | Maximum Fuel | 398 | 79 | 36 | 6.17 | 0.01 | 7.42 | 7.42 | 0.00 |
|  | Burn (DO) 50% from DT#5 P/S |  |  |  |  |  |  |  |  |
| B | Design Departure | 355 | 79 | 36 | 6.11 | -0.19 | 7.46 | 7.48 | 0.02 |
|  | Empty (DO) DT#5P/S |  |  |  |  |  |  |  |  |
| C | Mid-Voyage | 314 | 79 | 36 | 6.06 | -0.38 | 7.50 | 7.52 | 0.02 |
|  | Fill (SW) DT#6A P/S |  |  |  |  |  |  |  |  |
| D | Mid-Voyage | 314 | 108 | 36 | 6.10 | -0.11 | 7.48 | 7.49 | 0.01 |
|  | Burn (DO) 50% from DT#1F P/S |  |  |  |  |  |  |  |  |
| E | Mid-Voyage | 289 | 108 | 36 | 6.06 | 0.16 | 7.46 | 7.52 | 0.06 |
|  | Fill (SW) DB #3C |  |  |  |  |  |  |  |  |
| F | Mid-Voyage | 289 | 192 | 18 | 6.15 | -0.19 | 7.31 | 7.44 | 0.13 |
|  | Empty (DO) DT#1F P/S |  |  |  |  |  |  |  |  |
| G | Mid-Voyage | 261 | 192 | 18 | 6.12 | 0.11 | 7.36 | 7.47 | 0.11 |
|  | Burn (DO) 50% from DB#4P/S |  |  |  |  |  |  |  |  |
| H | Mid-Voyage | 216 | 192 | 18 | 6.06 | 0.22 | 7.43 | 7.52 | 0.09 |
|  | Empty (SW) DT#6A P/S |  |  |  |  |  |  |  |  |
| I | Mid-Voyage | 216 | 162 | 18 | 6.02 | -0.02 | 7.45 | 7.56 | 0.11 |
|  | Fill (DO) DB#3P/S |  |  |  |  |  |  |  |  |
| J | Mid-Voyage | 216 | 253 | 18 | 6.14 | -0.44 | 7.28 | 7.45 | 0.17 |
|  | Empty (DO) DB#4 P/S |  |  |  |  |  |  |  |  |
| K | Mid-Voyage | 167 | 253 | 18 | 6.07 | -0.31 | 7.39 | 7.48 | 0.09 |
|  | Empty (DO) DT#2C |  |  |  |  |  |  |  |  |
|  | Fill (SW) Forepeak 50% |  |  |  |  |  |  |  |  |
| M | Mid-Voyage | 119 | 267 | 18 | 6.02 | 0.14 | 7.44 | 7.56 | 0.12 |
|  | Burn (DO) DT#2P/S |  |  |  |  |  |  |  |  |
|  | Fill (SW) Forepeak 100% |  |  |  |  |  |  |  |  |
| N | Arrival | 35 | 298 | 4 | 6.00 | 0.55 | 7.52 | 7.57 | 0.05 |

TRAS  Ver. 2.7

8/27/99

FRV40-1 - Icing

Loading Condition        A Maximum Fuel  DO-398; SW- 79; FW-36

Item       Item           Weight     KG     LCG     TCG      I/d

No.                      M.Tons   m abv   m fwd   m off    at 0

bl    Sta 0     cl     heel

1   LS 8/05/99 wi 8% ma 1805.00    7.70   32.10    .01      .00

90   Fixed ballast         80.00    3.36   10.07   -.60      .00

9   Service life grwth    54.20   12.85   32.10    .00      .00

2   Crew & Effects         6.50   12.26   21.74   -.01      .00

3   Stores                24.20    7.87   19.11   1.92      .00

10   Lube Oil               4.50    2.23   34.70  -4.84     1.00

20   Roll tank             34.00   14.51   15.70    .00   478.00

100   Itinerant Load        50.00   10.65   39.70    .00      .00

200   Fresh Water             .00     .00     .00    .00      .00

210    FW Tk     P FW100%   13.82    4.90   19.30  -1.25     3.91

220    FW Tk     S FW100%   22.12    4.90   20.20   1.25     6.25

233   Sewage Hldg     0%      .00    3.79   19.36  -4.49      .00

300   Diesel Oil              .00     .00     .00    .00      .00

310    DT #1F    P DO 95%   26.08    3.72    6.60   -.97      .00

311    DT #1F    S DO 95%   26.08    3.72    6.60    .97      .00

320    DT #2     P DO 95%   49.25    3.91   15.22  -3.67      .00

321    DT #2     S DO 95%   49.25    3.91   15.22   3.67      .00

324    DT #2     C DO 95%   48.00    3.48   13.00    .00      .00

340    DB #4     P DO 95%   47.42    2.38   26.89  -4.39      .00

341    DB #4     S DO 95%   47.42    2.38   26.89   4.39      .00

350    DT #5     P DO 95%   42.16    5.07   46.23  -4.56      .00

351    DT #5     S DO 95%   42.16    5.07   46.23   4.56      .00

380    DO day    P DO 95%   10.26    6.32   42.84  -6.42      .00

381    DO day    S DO 95%   10.26    6.32   42.84   6.42      .00

309   DO free surface         .00     .00     .00    .00      .00

359    DT #5   P/S    FS      .00     .00     .00    .00   199.08

389    DO day  P/S    FS      .00     .00     .00    .00     1.70

400   SW Ballast              .00     .00     .00    .00      .00

440    DB #4     C SW100%   78.52    2.15   26.99    .00      .00

7   Icing abv 66-30       69.00   12.58   31.16    .00      .00

TOTAL              2640.18    7.16   29.75    .00   689.94

Mean S.W. Draft     6.17 m.      LCG              29.75 m. from Sta 0

KM                  8.32 m.      LCB              29.74 m. from Sta 0

KG                  7.16 m.      Trim lever         .01 m. by stern

GM                  1.16 m.      Mmt to trim 1cm  29.06 m.-tons

Corr for F.S.        .26 m.      Trim               .01 m. by stern

GM Available         .90 m.      LCF              34.58 m. from Sta 0

Mmt to heel 1 dg   41.25 m-tons  Draft @ F.P.      6.17 m.

List                 .12 deg     Draft @ A.P.      6.17 m.

KG         =  7.16 m.

F.S. Corr. =   .26 m.

Virtual KG =  7.42 m.

TRAS  Ver. 2.7

8/27/99

FRV40-1 - Icing

Loading Condition        B Design Depart DO-355; SW- 79; FW-36

Item       Item           Weight     KG     LCG     TCG      I/d

No.                      M.Tons   m abv   m fwd   m off    at 0

bl    Sta 0     cl     heel

1   LS 8/05/99 wi 8% ma 1805.00    7.70   32.10    .01      .00

90   Fixed ballast         80.00    3.36   10.07   -.60      .00

9   Service life grwth    54.20   12.85   32.10    .00      .00

2   Crew & Effects         6.50   12.26   21.74   -.01      .00

3   Stores                24.20    7.87   19.11   1.92      .00

10   Lube Oil               4.50    2.23   34.70  -4.84     1.00

20   Roll tank             34.00   14.51   15.70    .00   478.00

100   Itinerant Load        50.00   10.65   39.70    .00      .00

200   Fresh Water             .00     .00     .00    .00      .00

210    FW Tk     P FW100%   13.82    4.90   19.30  -1.25     3.91

220    FW Tk     S FW100%   22.12    4.90   20.20   1.25     6.25

233   Sewage Hldg     0%      .00    3.79   19.36  -4.49      .00

300   Diesel Oil              .00     .00     .00    .00      .00

310    DT #1F    P DO 95%   26.08    3.72    6.60   -.97      .00

311    DT #1F    S DO 95%   26.08    3.72    6.60    .97      .00

320    DT #2     P DO 95%   49.25    3.91   15.22  -3.67      .00

321    DT #2     S DO 95%   49.25    3.91   15.22   3.67      .00

324    DT #2     C DO 95%   48.00    3.48   13.00    .00      .00

340    DB #4     P DO 95%   47.42    2.38   26.89  -4.39      .00

341    DB #4     S DO 95%   47.42    2.38   26.89   4.39      .00

352    DT #5     P DO 50%   20.49    4.55   45.95  -4.32      .00

353    DT #5     S DO 50%   20.49    4.55   45.95   4.32      .00

380    DO day    P DO 95%   10.26    6.32   42.84  -6.42      .00

381    DO day    S DO 95%   10.26    6.32   42.84   6.42      .00

309   DO free surface         .00     .00     .00    .00      .00

359    DT #5   P/S    FS      .00     .00     .00    .00   199.08

389    DO day  P/S    FS      .00     .00     .00    .00     1.70

400   SW Ballast              .00     .00     .00    .00      .00

440    DB #4     C SW100%   78.52    2.15   26.99    .00      .00

7   Icing abv 66-30       69.00   12.58   31.16    .00      .00

TOTAL              2596.84    7.19   29.47    .00   689.94

Mean S.W. Draft     6.11 m.      LCG              29.47 m. from Sta 0

KM                  8.32 m.      LCB              29.66 m. from Sta 0

KG                  7.19 m.      Trim lever         .19 m. by bow

GM                  1.13 m.      Mmt to trim 1cm  28.86 m.-tons

Corr for F.S.        .27 m.      Trim               .17 m. by bow

GM Available         .86 m.      LCF              34.56 m. from Sta 0

Mmt to heel 1 dg   39.16 m-tons  Draft @ F.P.      6.22 m.

List                 .13 deg     Draft @ A.P.      6.04 m.

KG         =  7.19 m.

F.S. Corr. =   .27 m.

Virtual KG =  7.46 m.

TRAS  Ver. 2.7

8/27/99

FRV40-1 - Icing

Loading Condition        C Mid-voyage    DO-314; SW- 79; FW-36

Item       Item           Weight     KG     LCG     TCG      I/d

No.                      M.Tons   m abv   m fwd   m off    at 0

bl    Sta 0     cl     heel

1   LS 8/05/99 wi 8% ma 1805.00    7.70   32.10    .01      .00

90   Fixed ballast         80.00    3.36   10.07   -.60      .00

9   Service life grwth    54.20   12.85   32.10    .00      .00

2   Crew & Effects         6.50   12.26   21.74   -.01      .00

3   Stores                24.20    7.87   19.11   1.92      .00

10   Lube Oil               4.50    2.23   34.70  -4.84     1.00

20   Roll tank             34.00   14.51   15.70    .00   478.00

100   Itinerant Load        50.00   10.65   39.70    .00      .00

200   Fresh Water             .00     .00     .00    .00      .00

210    FW Tk     P FW100%   13.82    4.90   19.30  -1.25     3.91

220    FW Tk     S FW100%   22.12    4.90   20.20   1.25     6.25

233   Sewage Hldg     0%      .00    3.79   19.36  -4.49      .00

300   Diesel Oil              .00     .00     .00    .00      .00

310    DT #1F    P DO 95%   26.08    3.72    6.60   -.97      .00

311    DT #1F    S DO 95%   26.08    3.72    6.60    .97      .00

320    DT #2     P DO 95%   49.25    3.91   15.22  -3.67      .00

321    DT #2     S DO 95%   49.25    3.91   15.22   3.67      .00

324    DT #2     C DO 95%   48.00    3.48   13.00    .00      .00

340    DB #4     P DO 95%   47.42    2.38   26.89  -4.39      .00

341    DB #4     S DO 95%   47.42    2.38   26.89   4.39      .00

380    DO day    P DO 95%   10.26    6.32   42.84  -6.42      .00

381    DO day    S DO 95%   10.26    6.32   42.84   6.42      .00

309   DO free surface         .00     .00     .00    .00      .00

359    DT #5   P/S    FS      .00     .00     .00    .00   199.08

389    DO day  P/S    FS      .00     .00     .00    .00     1.70

400   SW Ballast              .00     .00     .00    .00      .00

440    DB #4     C SW100%   78.52    2.15   26.99    .00      .00

7   Icing abv 66-30       69.00   12.58   31.16    .00      .00

TOTAL              2555.86    7.23   29.21    .00   689.94

Mean S.W. Draft     6.06 m.      LCG              29.21 m. from Sta 0

KM                  8.32 m.      LCB              29.58 m. from Sta 0

KG                  7.23 m.      Trim lever         .38 m. by bow

GM                  1.09 m.      Mmt to trim 1cm  28.66 m.-tons

Corr for F.S.        .27 m.      Trim               .33 m. by bow

GM Available         .82 m.      LCF              34.54 m. from Sta 0

Mmt to heel 1 dg   36.44 m-tons  Draft @ F.P.      6.26 m.

List                 .14 deg     Draft @ A.P.      5.92 m.

KG         =  7.23 m.

F.S. Corr. =   .27 m.

Virtual KG =  7.50 m.

TRAS  Ver. 2.7

8/27/99

FRV40-1 - Icing

Loading Condition        D Mid-voyage    DO-314; SW-108; FW-36

Item       Item           Weight     KG     LCG     TCG      I/d

No.                      M.Tons   m abv   m fwd   m off    at 0

bl    Sta 0     cl     heel

1   LS 8/05/99 wi 8% ma 1805.00    7.70   32.10    .01      .00

90   Fixed ballast         80.00    3.36   10.07   -.60      .00

9   Service life grwth    54.20   12.85   32.10    .00      .00

2   Crew & Effects         6.50   12.26   21.74   -.01      .00

3   Stores                24.20    7.87   19.11   1.92      .00

10   Lube Oil               4.50    2.23   34.70  -4.84     1.00

20   Roll tank             34.00   14.51   15.70    .00   478.00

100   Itinerant Load        50.00   10.65   39.70    .00      .00

200   Fresh Water             .00     .00     .00    .00      .00

210    FW Tk     P FW100%   13.82    4.90   19.30  -1.25     3.91

220    FW Tk     S FW100%   22.12    4.90   20.20   1.25     6.25

233   Sewage Hldg     0%      .00    3.79   19.36  -4.49      .00

300   Diesel Oil              .00     .00     .00    .00      .00

310    DT #1F    P DO 95%   26.08    3.72    6.60   -.97      .00

311    DT #1F    S DO 95%   26.08    3.72    6.60    .97      .00

320    DT #2     P DO 95%   49.25    3.91   15.22  -3.67      .00

321    DT #2     S DO 95%   49.25    3.91   15.22   3.67      .00

324    DT #2     C DO 95%   48.00    3.48   13.00    .00      .00

340    DB #4     P DO 95%   47.42    2.38   26.89  -4.39      .00

341    DB #4     S DO 95%   47.42    2.38   26.89   4.39      .00

380    DO day    P DO 95%   10.26    6.32   42.84  -6.42      .00

381    DO day    S DO 95%   10.26    6.32   42.84   6.42      .00

309   DO free surface         .00     .00     .00    .00      .00

359    DT #5   P/S    FS      .00     .00     .00    .00   199.08

389    DO day  P/S    FS      .00     .00     .00    .00     1.70

400   SW Ballast              .00     .00     .00    .00      .00

440    DB #4     C SW100%   78.52    2.15   26.99    .00      .00

470    DT #6A    P SW100%   14.70    5.81   57.67  -3.73      .00

471    DT #6A    S SW100%   14.70    5.81   57.67   3.73      .00

7   Icing abv 66-30       69.00   12.58   31.16    .00      .00

TOTAL              2585.26    7.22   29.53    .00   689.94

Mean S.W. Draft     6.10 m.      LCG              29.53 m. from Sta 0

KM                  8.32 m.      LCB              29.64 m. from Sta 0

KG                  7.22 m.      Trim lever         .11 m. by bow

GM                  1.10 m.      Mmt to trim 1cm  28.80 m.-tons

Corr for F.S.        .27 m.      Trim               .10 m. by bow

GM Available         .84 m.      LCF              34.56 m. from Sta 0

Mmt to heel 1 dg   37.76 m-tons  Draft @ F.P.      6.16 m.

List                 .13 deg     Draft @ A.P.      6.06 m.

KG         =  7.22 m.

F.S. Corr. =   .27 m.

Virtual KG =  7.48 m.

TRAS  Ver. 2.7

8/27/99

FRV40-1 - Icing

Loading Condition        E Mid-voyage    DO-289; SW-108; FW-36

Item       Item           Weight     KG     LCG     TCG      I/d

No.                      M.Tons   m abv   m fwd   m off    at 0

bl    Sta 0     cl     heel

1   LS 8/05/99 wi 8% ma 1805.00    7.70   32.10    .01      .00

90   Fixed ballast         80.00    3.36   10.07   -.60      .00

9   Service life grwth    54.20   12.85   32.10    .00      .00

2   Crew & Effects         6.50   12.26   21.74   -.01      .00

3   Stores                24.20    7.87   19.11   1.92      .00

10   Lube Oil               4.50    2.23   34.70  -4.84     1.00

20   Roll tank             34.00   14.51   15.70    .00   478.00

100   Itinerant Load        50.00   10.65   39.70    .00      .00

200   Fresh Water             .00     .00     .00    .00      .00

210    FW Tk     P FW100%   13.82    4.90   19.30  -1.25     3.91

220    FW Tk     S FW100%   22.12    4.90   20.20   1.25     6.25

233   Sewage Hldg     0%      .00    3.79   19.36  -4.49      .00

300   Diesel Oil              .00     .00     .00    .00      .00

312    DT #1F    P DO 50%   13.72    2.59    6.61   -.89      .00

313    DT #1F    S DO 50%   13.72    2.59    6.61    .89      .00

320    DT #2     P DO 95%   49.25    3.91   15.22  -3.67      .00

321    DT #2     S DO 95%   49.25    3.91   15.22   3.67      .00

324    DT #2     C DO 95%   48.00    3.48   13.00    .00      .00

340    DB #4     P DO 95%   47.42    2.38   26.89  -4.39      .00

341    DB #4     S DO 95%   47.42    2.38   26.89   4.39      .00

380    DO day    P DO 95%   10.26    6.32   42.84  -6.42      .00

381    DO day    S DO 95%   10.26    6.32   42.84   6.42      .00

309   DO free surface         .00     .00     .00    .00      .00

349    DB #4   P/S    FS      .00     .00     .00    .00    82.74

389    DO day  P/S    FS      .00     .00     .00    .00     1.70

400   SW Ballast              .00     .00     .00    .00      .00

440    DB #4     C SW100%   78.52    2.15   26.99    .00      .00

470    DT #6A    P SW100%   14.70    5.81   57.67  -3.73      .00

471    DT #6A    S SW100%   14.70    5.81   57.67   3.73      .00

7   Icing abv 66-30       69.00   12.58   31.16    .00      .00

TOTAL              2560.56    7.24   29.75    .00   573.60

Mean S.W. Draft     6.06 m.      LCG              29.75 m. from Sta 0

KM                  8.32 m.      LCB              29.59 m. from Sta 0

KG                  7.24 m.      Trim lever         .16 m. by stern

GM                  1.08 m.      Mmt to trim 1cm  28.68 m.-tons

Corr for F.S.        .22 m.      Trim               .14 m. by stern

GM Available         .86 m.      LCF              34.54 m. from Sta 0

Mmt to heel 1 dg   38.32 m-tons  Draft @ F.P.      5.98 m.

List                 .13 deg     Draft @ A.P.      6.12 m.

KG         =  7.24 m.

F.S. Corr. =   .22 m.

Virtual KG =  7.46 m.

TRAS  Ver. 2.7

8/27/99

FRV40-1 - Icing

Loading Condition        F Mid-voyage    DO-289; SW-192; FW-18

Item       Item           Weight     KG     LCG     TCG      I/d

No.                      M.Tons   m abv   m fwd   m off    at 0

bl    Sta 0     cl     heel

1   LS 8/05/99 wi 8% ma 1805.00    7.70   32.10    .01      .00

90   Fixed ballast         80.00    3.36   10.07   -.60      .00

9   Service life grwth    54.20   12.85   32.10    .00      .00

2   Crew & Effects         6.50   12.26   21.74   -.01      .00

3   Stores                24.20    7.87   19.11   1.92      .00

10   Lube Oil               4.50    2.23   34.70  -4.84     1.00

20   Roll tank             34.00   14.51   15.70    .00   478.00

100   Itinerant Load        50.00   10.65   39.70    .00      .00

200   Fresh Water             .00     .00     .00    .00      .00

211    FW Tk     P FW 50%    6.91    4.43   19.30  -1.25     3.91

221    FW Tk     S FW 50%   11.06    4.43   20.20   1.25     6.25

233   Sewage Hldg     0%      .00    3.79   19.36  -4.49      .00

300   Diesel Oil              .00     .00     .00    .00      .00

312    DT #1F    P DO 50%   13.72    2.59    6.61   -.89      .00

313    DT #1F    S DO 50%   13.72    2.59    6.61    .89      .00

320    DT #2     P DO 95%   49.25    3.91   15.22  -3.67      .00

321    DT #2     S DO 95%   49.25    3.91   15.22   3.67      .00

324    DT #2     C DO 95%   48.00    3.48   13.00    .00      .00

340    DB #4     P DO 95%   47.42    2.38   26.89  -4.39      .00

341    DB #4     S DO 95%   47.42    2.38   26.89   4.39      .00

380    DO day    P DO 95%   10.26    6.32   42.84  -6.42      .00

381    DO day    S DO 95%   10.26    6.32   42.84   6.42      .00

309   DO free surface         .00     .00     .00    .00      .00

349    DB #4   P/S    FS      .00     .00     .00    .00    82.74

389    DO day  P/S    FS      .00     .00     .00    .00     1.70

400   SW Ballast              .00     .00     .00    .00      .00

434    DB #3     C SW100%   84.30    2.24   20.83    .00      .00

440    DB #4     C SW100%   78.52    2.15   26.99    .00      .00

470    DT #6A    P SW100%   14.70    5.81   57.67  -3.73      .00

471    DT #6A    S SW100%   14.70    5.81   57.67   3.73      .00

7   Icing abv 66-30       69.00   12.58   31.16    .00      .00

TOTAL              2626.89    7.09   29.53    .00   573.60

Mean S.W. Draft     6.15 m.      LCG              29.53 m. from Sta 0

KM                  8.32 m.      LCB              29.72 m. from Sta 0

KG                  7.09 m.      Trim lever         .19 m. by bow

GM                  1.23 m.      Mmt to trim 1cm  29.00 m.-tons

Corr for F.S.        .22 m.      Trim               .17 m. by bow

GM Available        1.01 m.      LCF              34.57 m. from Sta 0

Mmt to heel 1 dg   46.36 m-tons  Draft @ F.P.      6.25 m.

List                -.00 deg     Draft @ A.P.      6.08 m.

KG         =  7.09 m.

F.S. Corr. =   .22 m.

Virtual KG =  7.31 m.

TRAS  Ver. 2.7

8/27/99

FRV40-1 - Icing

Loading Condition        G Mid-voyage    DO-261; SW-192; FW-18

Item       Item           Weight     KG     LCG     TCG      I/d

No.                      M.Tons   m abv   m fwd   m off    at 0

bl    Sta 0     cl     heel

1   LS 8/05/99 wi 8% ma 1805.00    7.70   32.10    .01      .00

90   Fixed ballast         80.00    3.36   10.07   -.60      .00

9   Service life grwth    54.20   12.85   32.10    .00      .00

2   Crew & Effects         6.50   12.26   21.74   -.01      .00

3   Stores                24.20    7.87   19.11   1.92      .00

10   Lube Oil               4.50    2.23   34.70  -4.84     1.00

20   Roll tank             34.00   14.51   15.70    .00   478.00

100   Itinerant Load        50.00   10.65   39.70    .00      .00

200   Fresh Water             .00     .00     .00    .00      .00

211    FW Tk     P FW 50%    6.91    4.43   19.30  -1.25     3.91

221    FW Tk     S FW 50%   11.06    4.43   20.20   1.25     6.25

233   Sewage Hldg     0%      .00    3.79   19.36  -4.49      .00

300   Diesel Oil              .00     .00     .00    .00      .00

320    DT #2     P DO 95%   49.25    3.91   15.22  -3.67      .00

321    DT #2     S DO 95%   49.25    3.91   15.22   3.67      .00

324    DT #2     C DO 95%   48.00    3.48   13.00    .00      .00

340    DB #4     P DO 95%   47.42    2.38   26.89  -4.39      .00

341    DB #4     S DO 95%   47.42    2.38   26.89   4.39      .00

380    DO day    P DO 95%   10.26    6.32   42.84  -6.42      .00

381    DO day    S DO 95%   10.26    6.32   42.84   6.42      .00

309   DO free surface         .00     .00     .00    .00      .00

349    DB #4   P/S    FS      .00     .00     .00    .00    82.74

389    DO day  P/S    FS      .00     .00     .00    .00     1.70

400   SW Ballast              .00     .00     .00    .00      .00

434    DB #3     C SW100%   84.30    2.24   20.83    .00      .00

440    DB #4     C SW100%   78.52    2.15   26.99    .00      .00

470    DT #6A    P SW100%   14.70    5.81   57.67  -3.73      .00

471    DT #6A    S SW100%   14.70    5.81   57.67   3.73      .00

7   Icing abv 66-30       69.00   12.58   31.16    .00      .00

TOTAL              2599.44    7.14   29.77    .00   573.60

Mean S.W. Draft     6.12 m.      LCG              29.77 m. from Sta 0

KM                  8.32 m.      LCB              29.67 m. from Sta 0

KG                  7.14 m.      Trim lever         .11 m. by stern

GM                  1.18 m.      Mmt to trim 1cm  28.87 m.-tons

Corr for F.S.        .22 m.      Trim               .10 m. by stern

GM Available         .96 m.      LCF              34.56 m. from Sta 0

Mmt to heel 1 dg   43.62 m-tons  Draft @ F.P.      6.06 m.

List                -.00 deg     Draft @ A.P.      6.16 m.

KG         =  7.14 m.

F.S. Corr. =   .22 m.

Virtual KG =  7.36 m.

TRAS  Ver. 2.7

8/27/99

FRV40-1 - Icing

Loading Condition        H Mid-voyage    DO-216; SW-192; FW-18

Item       Item           Weight     KG     LCG     TCG      I/d

No.                      M.Tons   m abv   m fwd   m off    at 0

bl    Sta 0     cl     heel

1   LS 8/05/99 wi 8% ma 1805.00    7.70   32.10    .01      .00

90   Fixed ballast         80.00    3.36   10.07   -.60      .00

9   Service life grwth    54.20   12.85   32.10    .00      .00

2   Crew & Effects         6.50   12.26   21.74   -.01      .00

3   Stores                24.20    7.87   19.11   1.92      .00

10   Lube Oil               4.50    2.23   34.70  -4.84     1.00

20   Roll tank             34.00   14.51   15.70    .00   478.00

100   Itinerant Load        50.00   10.65   39.70    .00      .00

200   Fresh Water             .00     .00     .00    .00      .00

211    FW Tk     P FW 50%    6.91    4.43   19.30  -1.25     3.91

221    FW Tk     S FW 50%   11.06    4.43   20.20   1.25     6.25

233   Sewage Hldg     0%      .00    3.79   19.36  -4.49      .00

300   Diesel Oil              .00     .00     .00    .00      .00

320    DT #2     P DO 95%   49.25    3.91   15.22  -3.67      .00

321    DT #2     S DO 95%   49.25    3.91   15.22   3.67      .00

324    DT #2     C DO 95%   48.00    3.48   13.00    .00      .00

342    DB #4     P DO 50%   24.96    1.79   26.92  -4.12      .00

343    DB #4     S DO 50%   24.96    1.79   26.92   4.12      .00

380    DO day    P DO 95%   10.26    6.32   42.84  -6.42      .00

381    DO day    S DO 95%   10.26    6.32   42.84   6.42      .00

309   DO free surface         .00     .00     .00    .00      .00

349    DB #4   P/S    FS      .00     .00     .00    .00    82.74

400   SW Ballast              .00     .00     .00    .00      .00

434    DB #3     C SW100%   84.30    2.24   20.83    .00      .00

440    DB #4     C SW100%   78.52    2.15   26.99    .00      .00

470    DT #6A    P SW100%   14.70    5.81   57.67  -3.73      .00

471    DT #6A    S SW100%   14.70    5.81   57.67   3.73      .00

7   Icing abv 66-30       69.00   12.58   31.16    .00      .00

TOTAL              2554.52    7.21   29.82    .00   571.90

Mean S.W. Draft     6.06 m.      LCG              29.82 m. from Sta 0

KM                  8.32 m.      LCB              29.58 m. from Sta 0

KG                  7.21 m.      Trim lever         .25 m. by stern

GM                  1.11 m.      Mmt to trim 1cm  28.65 m.-tons

Corr for F.S.        .22 m.      Trim               .22 m. by stern

GM Available         .89 m.      LCF              34.54 m. from Sta 0

Mmt to heel 1 dg   39.48 m-tons  Draft @ F.P.      5.92 m.

List                -.00 deg     Draft @ A.P.      6.14 m.

KG         =  7.21 m.

F.S. Corr. =   .22 m.

Virtual KG =  7.43 m.

TRAS  Ver. 2.7

8/27/99

FRV40-1 - Icing

Loading Condition        I Mid-voyage    DO-216; SW-162; FW-18

Item       Item           Weight     KG     LCG     TCG      I/d

No.                      M.Tons   m abv   m fwd   m off    at 0

bl    Sta 0     cl     heel

1   LS 8/05/99 wi 8% ma 1805.00    7.70   32.10    .01      .00

90   Fixed ballast         80.00    3.36   10.07   -.60      .00

9   Service life grwth    54.20   12.85   32.10    .00      .00

2   Crew & Effects         6.50   12.26   21.74   -.01      .00

3   Stores                24.20    7.87   19.11   1.92      .00

10   Lube Oil               4.50    2.23   34.70  -4.84     1.00

20   Roll tank             34.00   14.51   15.70    .00   478.00

100   Itinerant Load        50.00   10.65   39.70    .00      .00

200   Fresh Water             .00     .00     .00    .00      .00

211    FW Tk     P FW 50%    6.91    4.43   19.30  -1.25     3.91

221    FW Tk     S FW 50%   11.06    4.43   20.20   1.25     6.25

233   Sewage Hldg     0%      .00    3.79   19.36  -4.49      .00

300   Diesel Oil              .00     .00     .00    .00      .00

320    DT #2     P DO 95%   49.25    3.91   15.22  -3.67      .00

321    DT #2     S DO 95%   49.25    3.91   15.22   3.67      .00

324    DT #2     C DO 95%   48.00    3.48   13.00    .00      .00

342    DB #4     P DO 50%   24.96    1.79   26.92  -4.12      .00

343    DB #4     S DO 50%   24.96    1.79   26.92   4.12      .00

380    DO day    P DO 95%   10.26    6.32   42.84  -6.42      .00

381    DO day    S DO 95%   10.26    6.32   42.84   6.42      .00

309   DO free surface         .00     .00     .00    .00      .00

349    DB #4   P/S    FS      .00     .00     .00    .00    82.74

400   SW Ballast              .00     .00     .00    .00      .00

434    DB #3     C SW100%   84.30    2.24   20.83    .00      .00

440    DB #4     C SW100%   78.52    2.15   26.99    .00      .00

7   Icing abv 66-30       69.00   12.58   31.16    .00      .00

TOTAL              2525.12    7.23   29.50    .00   571.90

Mean S.W. Draft     6.02 m.      LCG              29.50 m. from Sta 0

KM                  8.32 m.      LCB              29.52 m. from Sta 0

KG                  7.23 m.      Trim lever         .02 m. by bow

GM                  1.09 m.      Mmt to trim 1cm  28.50 m.-tons

Corr for F.S.        .23 m.      Trim               .02 m. by bow

GM Available         .87 m.      LCF              34.53 m. from Sta 0

Mmt to heel 1 dg   38.16 m-tons  Draft @ F.P.      6.03 m.

List                -.00 deg     Draft @ A.P.      6.01 m.

KG         =  7.23 m.

F.S. Corr. =   .23 m.

Virtual KG =  7.45 m.

TRAS  Ver. 2.7

8/27/99

FRV40-1 - Icing

Loading Condition        J Mid-voyage    DO-216; SW-253; FW-18

Item       Item           Weight     KG     LCG     TCG      I/d

No.                      M.Tons   m abv   m fwd   m off    at 0

bl    Sta 0     cl     heel

1   LS 8/05/99 wi 8% ma 1805.00    7.70   32.10    .01      .00

90   Fixed ballast         80.00    3.36   10.07   -.60      .00

9   Service life grwth    54.20   12.85   32.10    .00      .00

2   Crew & Effects         6.50   12.26   21.74   -.01      .00

3   Stores                24.20    7.87   19.11   1.92      .00

10   Lube Oil               4.50    2.23   34.70  -4.84     1.00

20   Roll tank             34.00   14.51   15.70    .00   478.00

100   Itinerant Load        50.00   10.65   39.70    .00      .00

200   Fresh Water             .00     .00     .00    .00      .00

211    FW Tk     P FW 50%    6.91    4.43   19.30  -1.25     3.91

221    FW Tk     S FW 50%   11.06    4.43   20.20   1.25     6.25

233   Sewage Hldg     0%      .00    3.79   19.36  -4.49      .00

300   Diesel Oil              .00     .00     .00    .00      .00

320    DT #2     P DO 95%   49.25    3.91   15.22  -3.67      .00

321    DT #2     S DO 95%   49.25    3.91   15.22   3.67      .00

324    DT #2     C DO 95%   48.00    3.48   13.00    .00      .00

342    DB #4     P DO 50%   24.96    1.79   26.92  -4.12      .00

343    DB #4     S DO 50%   24.96    1.79   26.92   4.12      .00

380    DO day    P DO 95%   10.26    6.32   42.84  -6.42      .00

381    DO day    S DO 95%   10.26    6.32   42.84   6.42      .00

309   DO free surface         .00     .00     .00    .00      .00

349    DB #4   P/S    FS      .00     .00     .00    .00    82.74

400   SW Ballast              .00     .00     .00    .00      .00

430    DB #3     P SW100%   45.19    2.51   21.00  -4.04      .00

431    DB #3     S SW100%   45.19    2.51   21.00   4.04      .00

434    DB #3     C SW100%   84.30    2.24   20.83    .00      .00

440    DB #4     C SW100%   78.52    2.15   26.99    .00      .00

7   Icing abv 66-30       69.00   12.58   31.16    .00      .00

TOTAL              2615.50    7.06   29.21    .00   571.90

Mean S.W. Draft     6.14 m.      LCG              29.21 m. from Sta 0

KM                  8.32 m.      LCB              29.70 m. from Sta 0

KG                  7.06 m.      Trim lever         .49 m. by bow

GM                  1.26 m.      Mmt to trim 1cm  28.95 m.-tons

Corr for F.S.        .22 m.      Trim               .44 m. by bow

GM Available        1.04 m.      LCF              34.57 m. from Sta 0

Mmt to heel 1 dg   47.38 m-tons  Draft @ F.P.      6.40 m.

List                -.00 deg     Draft @ A.P.      5.96 m.

KG         =  7.06 m.

F.S. Corr. =   .22 m.

Virtual KG =  7.28 m.

TRAS  Ver. 2.7

8/27/99

FRV40-1 - Icing

Loading Condition        K Mid-voyage    DO-167; SW-253; FW-18

Item       Item           Weight     KG     LCG     TCG      I/d

No.                      M.Tons   m abv   m fwd   m off    at 0

bl    Sta 0     cl     heel

1   LS 8/05/99 wi 8% ma 1805.00    7.70   32.10    .01      .00

90   Fixed ballast         80.00    3.36   10.07   -.60      .00

9   Service life grwth    54.20   12.85   32.10    .00      .00

2   Crew & Effects         6.50   12.26   21.74   -.01      .00

3   Stores                24.20    7.87   19.11   1.92      .00

10   Lube Oil               4.50    2.23   34.70  -4.84     1.00

20   Roll tank             34.00   14.51   15.70    .00   478.00

100   Itinerant Load        50.00   10.65   39.70    .00      .00

200   Fresh Water             .00     .00     .00    .00      .00

211    FW Tk     P FW 50%    6.91    4.43   19.30  -1.25     3.91

221    FW Tk     S FW 50%   11.06    4.43   20.20   1.25     6.25

233   Sewage Hldg     0%      .00    3.79   19.36  -4.49      .00

300   Diesel Oil              .00     .00     .00    .00      .00

320    DT #2     P DO 95%   49.25    3.91   15.22  -3.67      .00

321    DT #2     S DO 95%   49.25    3.91   15.22   3.67      .00

324    DT #2     C DO 95%   48.00    3.48   13.00    .00      .00

380    DO day    P DO 95%   10.26    6.32   42.84  -6.42      .00

381    DO day    S DO 95%   10.26    6.32   42.84   6.42      .00

309   DO free surface         .00     .00     .00    .00      .00

349    DB #4   P/S    FS      .00     .00     .00    .00    82.74

400   SW Ballast              .00     .00     .00    .00      .00

430    DB #3     P SW100%   45.19    2.51   21.00  -4.04      .00

431    DB #3     S SW100%   45.19    2.51   21.00   4.04      .00

434    DB #3     C SW100%   84.30    2.24   20.83    .00      .00

440    DB #4     C SW100%   78.52    2.15   26.99    .00      .00

7   Icing abv 66-30       69.00   12.58   31.16    .00      .00

TOTAL              2565.58    7.17   29.25    .00   571.90

Mean S.W. Draft     6.07 m.      LCG              29.25 m. from Sta 0

KM                  8.32 m.      LCB              29.60 m. from Sta 0

KG                  7.17 m.      Trim lever         .35 m. by bow

GM                  1.15 m.      Mmt to trim 1cm  28.71 m.-tons

Corr for F.S.        .22 m.      Trim               .31 m. by bow

GM Available         .93 m.      LCF              34.55 m. from Sta 0

Mmt to heel 1 dg   41.68 m-tons  Draft @ F.P.      6.26 m.

List                -.00 deg     Draft @ A.P.      5.94 m.

KG         =  7.17 m.

F.S. Corr. =   .22 m.

Virtual KG =  7.39 m.

TRAS  Ver. 2.7

8/27/99

FRV40-1 - Icing

Loading Condition        M Mid-voyage    DO-119; SW-267; FW-18

Item       Item           Weight     KG     LCG     TCG      I/d

No.                      M.Tons   m abv   m fwd   m off    at 0

bl    Sta 0     cl     heel

1   LS 8/05/99 wi 8% ma 1805.00    7.70   32.10    .01      .00

90   Fixed ballast         80.00    3.36   10.07   -.60      .00

9   Service life grwth    54.20   12.85   32.10    .00      .00

2   Crew & Effects         6.50   12.26   21.74   -.01      .00

3   Stores                24.20    7.87   19.11   1.92      .00

10   Lube Oil               4.50    2.23   34.70  -4.84     1.00

20   Roll tank             34.00   14.51   15.70    .00   478.00

100   Itinerant Load        50.00   10.65   39.70    .00      .00

200   Fresh Water             .00     .00     .00    .00      .00

211    FW Tk     P FW 50%    6.91    4.43   19.30  -1.25     3.91

221    FW Tk     S FW 50%   11.06    4.43   20.20   1.25     6.25

233   Sewage Hldg     0%      .00    3.79   19.36  -4.49      .00

300   Diesel Oil              .00     .00     .00    .00      .00

320    DT #2     P DO 95%   49.25    3.91   15.22  -3.67      .00

321    DT #2     S DO 95%   49.25    3.91   15.22   3.67      .00

380    DO day    P DO 95%   10.26    6.32   42.84  -6.42      .00

381    DO day    S DO 95%   10.26    6.32   42.84   6.42      .00

309   DO free surface         .00     .00     .00    .00      .00

349    DB #4   P/S    FS      .00     .00     .00    .00    82.74

400   SW Ballast              .00     .00     .00    .00      .00

402    Forepk    C SW 30%   13.51    3.14    3.40    .00     1.50

430    DB #3     P SW100%   45.19    2.51   21.00  -4.04      .00

431    DB #3     S SW100%   45.19    2.51   21.00   4.04      .00

434    DB #3     C SW100%   84.30    2.24   20.83    .00      .00

440    DB #4     C SW100%   78.52    2.15   26.99    .00      .00

7   Icing abv 66-30       69.00   12.58   31.16    .00      .00

TOTAL              2531.09    7.21   29.42    .00   573.40

Mean S.W. Draft     6.02 m.      LCG              29.42 m. from Sta 0

KM                  8.32 m.      LCB              29.53 m. from Sta 0

KG                  7.21 m.      Trim lever         .11 m. by bow

GM                  1.10 m.      Mmt to trim 1cm  28.53 m.-tons

Corr for F.S.        .23 m.      Trim               .10 m. by bow

GM Available         .88 m.      LCF              34.53 m. from Sta 0

Mmt to heel 1 dg   38.79 m-tons  Draft @ F.P.      6.08 m.

List                -.00 deg     Draft @ A.P.      5.98 m.

KG         =  7.21 m.

F.S. Corr. =   .23 m.

Virtual KG =  7.44 m.

TRAS  Ver. 2.7

8/27/99

FRV40-1 - Icing

Loading Condition        N Mid-voyage    DO- 20; SW-298; FW- 4

Item       Item           Weight     KG     LCG     TCG      I/d

No.                      M.Tons   m abv   m fwd   m off    at 0

bl    Sta 0     cl     heel

1   LS 8/05/99 wi 8% ma 1805.00    7.70   32.10    .01      .00

90   Fixed ballast         80.00    3.36   10.07   -.60      .00

9   Service life grwth    54.20   12.85   32.10    .00      .00

2   Crew & Effects         6.50   12.26   21.74   -.01      .00

3   Stores                24.20    7.87   19.11   1.92      .00

10   Lube Oil               4.50    2.23   34.70  -4.84     1.00

20   Roll tank             34.00   14.51   15.70    .00   478.00

100   Itinerant Load        50.00   10.65   39.70    .00      .00

200   Fresh Water             .00     .00     .00    .00      .00

212    FW Tk     P FW 10%    1.38    4.05   19.30  -1.25     3.91

222    FW Tk     S FW 10%    2.21    4.05   20.20   1.25     6.25

233   Sewage Hldg     0%      .00    3.79   19.36  -4.49      .00

300   Diesel Oil              .00     .00     .00    .00      .00

344    DB #4     P DO 15%    7.50    1.22   27.00  -3.67      .00

345    DB #4     S DO 15%    7.50    1.22   27.00   3.67      .00

380    DO day    P DO 95%   10.26    6.32   42.84  -6.42      .00

381    DO day    S DO 95%   10.26    6.32   42.84   6.42      .00

309   DO free surface         .00     .00     .00    .00      .00

349    DB #4   P/S    FS      .00     .00     .00    .00    82.74

400   SW Ballast              .00     .00     .00    .00      .00

401    Forepk    C SW100%   45.05    5.80    2.91    .00      .00

430    DB #3     P SW100%   45.19    2.51   21.00  -4.04      .00

431    DB #3     S SW100%   45.19    2.51   21.00   4.04      .00

434    DB #3     C SW100%   84.30    2.24   20.83    .00      .00

440    DB #4     C SW100%   78.52    2.15   26.99    .00      .00

460    DT #6F    P SW100%   23.91    5.61   51.99  -4.25      .00

461    DT #6F    S SW100%   23.91    5.61   51.99   4.25      .00

7   Icing abv 66-30       69.00   12.58   31.16    .00      .00

TOTAL              2512.58    7.29   30.11   -.00   571.90

Mean S.W. Draft     6.00 m.      LCG              30.11 m. from Sta 0

KM                  8.32 m.      LCB              29.50 m. from Sta 0

KG                  7.29 m.      Trim lever         .62 m. by stern

GM                  1.03 m.      Mmt to trim 1cm  28.44 m.-tons

Corr for F.S.        .23 m.      Trim               .55 m. by stern

GM Available         .80 m.      LCF              34.52 m. from Sta 0

Mmt to heel 1 dg   35.14 m-tons  Draft @ F.P.      5.67 m.

List                -.12 deg     Draft @ A.P.      6.22 m.

KG         =  7.29 m.

F.S. Corr. =   .23 m.

Virtual KG =  7.52 m.

Appendix A

## SHCP Offsets

SHCP Offsets were developed as follows:

- Offsets represent DWG FRV-40 802-00001.

- Basic offsets were represent hull with no appendages

- Skeg is modeled as an appendage defined by offsets

- Tunnel sections of the stern are modeled as a negative appendage defined by offsets.

- Geometry of hull, skeg, and tunnel is shown in attached sketch.  Note the shaded area is added in twice (once by hull, once by skeg) and subtracted once (but negative tunnel) for net of one.

- Baseline is 0.5 m below keel at 30.15 m aft of fp.  Note that this is the keel at bottom of the skeg, which extends lower than the basic hull at the stern.

- Depth to 01 level is 11.4 m

- Depth to main deck is 8.65 m

- The offsets do not include any camber

- The offsets include sheer in the 01 level forward

- In the basic offsets the superstructure (from main deck to 01 level) extends aft to 24.818 m aft  of fp.

- The following are modeled as appendages:

  - Skeg

    - Appendage # 1, Skeg

    - Appendage # 2, Stern tunnel

  - Appendage #3, Stern ramp cutout (negative appendage)

  - Appendage #4, Propeller (point appendage)

  - Appendage #5, Rudder (point appendage)

  - Appendage #6, Bilge keels (point appendage)

  - Appendage #7, Shell plating (point appendage)

  - Superstructure – Based on arrangement drawing.

Modeled up to the 01 level (11.4 m above bl), from stem to frame 58.  Superstructure from stem to 24.818 m aft of fp is included in basic offsets.  Superstructure aft of 24.818 m aft of fp is modeled as appendages as follows:

    - Appendage # 8, Superstructure, 24.818 m aft fp to frame 45

    - Appendage # 9, Superstructure, frame 45 – 58

- These offsets do not include:

  - Bow thruster free-flooding volume.  This is treated as part of lightship

  - Centerboard

  - Centerboard trunk free-flooding volume.  This is treated as part of lightship

- The offsets and appendages represent the starboard side of the vessel.  Because of the presence on the starboard side of the longline pit cutout and the superstructure configuration, this stability characteristics of this side are worse than for the port side.

0001 FRV40     6-30-99

001                     003003  1

1.000        0.005     0.005    58.000     0.125    9    2

1 +1 Skeg

1.000        0.005     0.005    58.000     0.125    0    2

1 -1 Stern tunnel

1.000        0.005     0.005    58.000     0.125    0    2

1 -1 Stern ramp

1.000        0.005     0.005    58.000     0.125    0    2

0 +1 Propeller                           1.5       55.2     2.20      0.

0 +1 Rudder                              3.6       58.3     2.40      0.

0 +1 Bilge keels                         1.9       29.7     2.40      0.

0 +1 Shell plating                      10.0       29.3     2.50      0.

1 +1 Suprstrt 24.818 - fr 45

1.000        0.005     0.005    58.000     0.125    0    2

1 +1 Suprstrt fr 45 - fr 58

1.000        0.005     0.005    58.000     0.125    0    2

99999999999999999999   5.90    0.00

021        3  3

4.4       4.5       4.6       4.7       4.8       4.9       5.0       5.1

5.2       5.3       5.4       5.5       5.6       5.7       5.8       6.0

6.1       6.2       6.3       6.4       6.5       4.3       4.2       4.1

9999999999

9999

-1.900   .000 11.078     0    1      AK-INT.OFF

-1.900   .075 11.117     0    1 	 FRV40  6-30-99

-1.900   .172 11.219     0    1

-1.900   .293 11.373     0    1      OFFSETS FOR INTACT STABILITY

-1.900   .448 11.592     0    1      Includes superstructure up to

-1.900   .500 11.670 88888    1      01 Level (11.4 m abv bl) from

-.809   .000  8.109     0    2      stem to Fr 58 (located 35.2 m

-.809   .026  8.136     0    2      aft of FP)

-.809   .045  8.204     0    2

-.809   .048  8.215     0    2

-.809   .075  8.341     0    2

-.809   .120  8.527     0    2

-.809   .215  8.869     0    2

-.809   .356  9.301     0    2

-.809   .427  9.494     0    2

-.809   .880 10.448     0    2

-.809   .940 10.551     0    2

-.809  1.765 11.649 88888    2

.699   .000  4.024     0    3

.699   .021  4.054     0    3

.699   .035  4.137     0    3

.699   .048  4.269     0    3

.699   .064  4.455     0    3

.699   .080  4.624     0    3

.699   .093  4.758     0    3

.699   .148  5.276     0    3

.699   .158  5.355     0    3

.699   .263  6.136     0    3

.699   .273  6.202     0    3

.699   .459  7.147     0    3

.699   .536  7.454     0    3

.699   .746  8.163     0    3

.699  1.197  9.239     0    3

.699  1.260  9.357     0    3

.699  1.946 10.385     0    3

.699  3.143 11.619 88888    3

2.204   .000  1.630     0    4

2.204   .053  1.647     0    4     SHCP Offsets

2.204   .106  1.694     0    4     SHCP "C" Card data is as follows:

2.204   .111  1.700     0    4       Station spacing      =    1.000

2.204   .205  1.853     0    4       Vert. scale factor   =      .0050

2.204   .213  1.870     0    4       Horz. scale factor   =      .0050

2.204   .281  2.064     0    4       L.B.P.               =   58.00

2.204   .312  2.202     0    4       Body plan scale      =     .125

2.204   .360  2.545     0    4       Number of appendages =    7

2.204   .369  2.645     0    4

2.204   .408  3.200     0    4     Appendages are as follows:

2.204   .425  3.477     0    4

2.204   .460  4.000     0    4        1.  Skeg

2.204   .500  4.445     0    4          Volume Addition      ; ISIGN =  1

2.204   .518  4.611     0    4          Described by offsets; KIND  =  1

2.204   .621  5.326     0    4

2.204   .795  6.156     0    4        2.  Stern tunnel

2.204   .905  6.567     0    4          Volume Deduction     ; ISIGN = -1

2.204  1.064  7.082     0    4          Described by offsets; KIND  =  1

2.204  1.436  8.079     0    4

2.204  1.984  9.142     0    4        3.  Stern ramp

2.204  2.411  9.754     0    4          Volume Deduction     ; ISIGN = -1

2.204  2.871 10.300     0    4          Described by offsets; KIND  =  1

2.204  4.261 11.591 88888    4

3.712   .000  1.244     0    5        4.  Propeller

3.712   .312  1.286     0    5          Volume Addition      ; ISIGN =  1

3.712   .543  1.397     0    5          Point Volume =    1.50

3.712   .600  1.442     0    5          Point LCB    =   55.200

3.712   .704  1.555     0    5          Point VCB    =    2.200

3.712   .805  1.744     0    5          Point TCB    =     .000

3.712   .860  1.970     0    5

3.712   .885  2.244     0    5        5.  Rudder

3.712   .893  2.577     0    5          Volume Addition      ; ISIGN =  1

3.712   .896  2.972     0    5          Point Volume =    3.60

3.712   .901  3.429     0    5          Point LCB    =   58.300

3.712   .906  3.610     0    5          Point VCB    =    2.400

3.712   .923  3.950     0    5          Point TCB    =     .000

3.712   .986  4.552     0    5

3.712  1.118  5.253     0    5        6.  Bilge keels

3.712  1.347  6.070     0    5          Volume Addition      ; ISIGN =  1

3.712  1.679  6.984     0    5          Point Volume =    1.90

3.712  1.774  7.217     0    5          Point LCB    =   29.700

3.712  2.107  7.967     0    5          Point VCB    =    2.400

3.712  2.708  9.020     0    5          Point TCB    =     .000

3.712  3.678 10.196     0    5

3.712  5.204 11.562 88888    5        7.  Shell plating

5.220   .000  1.197     0    6          Volume Addition      ; ISIGN =  1

5.220   .442  1.222     0    6          Point Volume =   10.00

5.220   .803  1.298     0    6          Point LCB    =   29.300

5.220  1.075  1.425     0    6          Point VCB    =    2.500

5.220  1.253  1.604     0    6          Point TCB    =     .000

5.220  1.353  1.838     0    6

5.220  1.395  2.132     0    6        8.  Superstructure, 24.818 m aft of

5.220  1.400  2.489     0    6          FP to fr 45

5.220  1.387  2.904     0    6          Volume Addition      ; ISIGN =  1

5.220  1.377  3.371     0    6          Described by offsets; KIND  =  1

5.220  1.394  3.888     0    6

5.220  1.417  4.136     0    6        9.  Superstrucure, fr 45 - fr 58

5.220  1.467  4.475     0    6          Volume Addition      ; ISIGN =  1

5.220  1.629  5.161     0    6          Described by offsets; KIND  =  1

5.220  1.902  5.965     0    6

5.220  2.277  6.867     0    6

5.220  2.735  7.838     0    6

5.220  3.353  8.881     0    6

5.220  4.353 10.081     0    6

5.220  5.932 11.533 88888    6

6.728   .000  1.156     0    7

6.728   .500  1.171     0    7

6.728   .969  1.224     0    7

6.728  1.361  1.329     0    7

6.728  1.638  1.498     0    7

6.728  1.808  1.734     0    7

6.728  1.890  2.038     0    7

6.728  1.904  2.408     0    7

6.728  1.883  2.835     0    7

6.728  1.863  3.306     0    7

6.728  1.880  3.814     0    7

6.728  1.965  4.385     0    7

6.728  2.147  5.055     0    7

6.728  2.446  5.846     0    7

6.728  2.842  6.738     0    7

6.728  3.304  7.697     0    7

6.728  3.909  8.732     0    7

6.728  4.887  9.963     0    7

6.728  6.447 11.503 88888    7

9.744   .000  1.074     0    8

9.744   .568  1.090     0    8

9.744  1.202  1.142     0    8

9.744  1.796  1.237     0    8

9.744  2.263  1.383     0    8

9.744  2.591  1.590     0    8

9.744  2.788  1.867     0    8

9.744  2.870  2.221     0    8

9.744  2.882  2.638     0    8

9.744  2.879  3.099     0    8

9.744  2.910  3.596     0    8

9.744  3.007  4.154     0    8

9.744  3.195  4.806     0    8

9.744  3.489  5.576     0    8

9.744  3.862  6.445     0    8

9.744  4.279  7.384     0    8

9.744  4.802  8.410     0    8

9.744  5.651  9.715     0    8

9.744  7.078 11.445 88888    8

12.757   .000   .992     0    9

12.757   .614  1.013     0    9

12.757  1.358  1.071     0    9

12.757  2.087  1.162     0    9

12.757  2.682  1.284     0    9

12.757  3.131  1.453     0    9

12.757  3.449  1.686     0    9

12.757  3.654  1.999     0    9

12.757  3.780  2.381     0    9

12.757  3.865  2.818     0    9

12.757  3.944  3.303     0    9

12.757  4.051  3.853     0    9

12.757  4.219  4.493     0    9

12.757  4.470  5.240     0    9

12.757  4.783  6.082     0    9

12.757  5.128  6.997     0    9

12.757  5.332  7.522     0    9

12.757  5.548  8.016     0    9

12.757  6.260  9.362     0    9

12.757  7.416 11.407 88888    9

15.773   .000   .910     0   10

15.773   .632   .929     0   10

15.773  1.423   .981     0   10

15.773  2.212  1.059     0   10

15.773  2.872  1.160     0   10

15.773  3.399  1.300     0   10

15.773  3.823  1.498     0   10

15.773  4.167  1.770     0   10

15.773  4.444  2.114     0   10

15.773  4.659  2.523     0   10

15.773  4.825  2.997     0   10

15.773  4.972  3.543     0   10

15.773  5.137  4.175     0   10

15.773  5.348  4.900     0   10

15.773  5.594  5.714     0   10

15.773  5.856  6.606     0   10

15.773  6.169  7.624     0   10

15.773  6.319  8.052     0   10

15.773  6.694  9.065     0   10

15.773  7.484 11.400 88888   10

18.789   .000   .828     0   11

18.789   .622   .844     0   11

18.789  1.396   .886     0   11

18.789  2.186   .951     0   11

18.789  2.880  1.036     0   11

18.789  3.473  1.155     0   11

18.789  3.989  1.327     0   11

18.789  4.445  1.567     0   11

18.789  4.842  1.882     0   11

18.789  5.178  2.275     0   11

18.789  5.452  2.749     0   11

18.789  5.682  3.304     0   11

18.789  5.890  3.939     0   11

18.789  6.091  4.653     0   11

18.789  6.287  5.442     0   11

18.789  6.472  6.301     0   11

18.789  6.681  7.297     0   11

18.789  7.009  8.817     0   11

18.789  7.498 11.400 88888   11

21.802   .000   .746     0   12

21.802   .601   .758     0   12

21.802  1.335   .793     0   12

21.802  2.100   .847     0   12

21.802  2.811   .920     0   12

21.802  3.459  1.024     0   12

21.802  4.054  1.178     0   12

21.802  4.602  1.395     0   12

21.802  5.100  1.690     0   12

21.802  5.542  2.076     0   12

21.802  5.923  2.561     0   12

21.802  6.241  3.136     0   12

21.802  6.494  3.787     0   12

21.802  6.687  4.500     0   12

21.802  6.832  5.257     0   12

21.802  6.946  6.042     0   12

21.802  7.083  6.953     0   12

21.802  7.262  8.447     0   12

21.802  7.269  8.523     0   12

21.802  7.365  9.658     0   12

21.802  7.500 11.400 88888   12

24.818   .000   .664     0   13  *

24.818   .582   .674     0   13  * Longl breakpoint - end of superstructure

24.818  1.279   .704     0   13  *

24.818  2.017   .751     0   13  *

24.818  2.732   .817     0   13  *

24.818  3.417   .913     0   13  *

24.818  4.076  1.053     0   13  *

24.818  4.709  1.254     0   13  *

24.818  5.303  1.536     0   13  *

24.818  5.842  1.922     0   13  *

24.818  6.310  2.427     0   13  *

24.818  6.608  2.877     0   13  *

24.818  6.691  3.031     0   13  *

24.818  6.968  3.707     0   13  *

24.818  7.103  4.244     0   13  *

24.818  7.137  4.423     0   13  *

24.818  7.230  5.132     0   13  *

24.818  7.266  5.566     0   13  *

24.818  7.282  5.793     0   13  *

24.818  7.335  6.239     0   13  *

24.818  7.365  6.481     0   13  *

24.818  7.449  7.504     0   13  *

24.818  7.473  8.223     0   13  *

24.818  7.490 10.120     0   13  *

24.818  7.500 11.400 88888   13  *

24.819   .000   .664     0   14  *

24.819   .582   .674     0   14  *

24.819  1.279   .704     0   14  *

24.819  2.017   .751     0   14  *

24.819  2.732   .817     0   14  *

24.819  3.417   .913     0   14  *

24.819  4.076  1.053     0   14  *

24.819  4.709  1.254     0   14  *

24.819  5.303  1.536     0   14  *

24.819  5.842  1.922     0   14  *

24.819  6.310  2.427     0   14  *

24.819  6.608  2.877     0   14  *

24.819  6.691  3.031     0   14  *

24.819  6.968  3.707     0   14  *

24.819  7.103  4.244     0   14  *

24.819  7.137  4.423     0   14  *

24.819  7.230  5.132     0   14  *

24.819  7.266  5.566     0   14  *

24.819  7.282  5.793     0   14  *

24.819  7.335  6.239     0   14  *

24.819  7.365  6.481     0   14  *

24.819  7.449  7.504     0   14  *

24.819  7.473  8.223     0   14  *

24.819  7.489 10.025 88888   14  *

24.820   .000   .664     0   15  *

24.820   .582   .674     0   15  *

24.820  1.279   .704     0   15  *

24.820  2.017   .751     0   15  *

24.820  2.732   .817     0   15  *

24.820  3.417   .913     0   15  *

24.820  4.076  1.053     0   15  *

24.820  4.709  1.254     0   15  *

24.820  5.303  1.536     0   15  *

24.820  5.842  1.922     0   15  *

24.820  6.310  2.427     0   15  *

24.820  6.608  2.877     0   15  *

24.820  6.691  3.031     0   15  *

24.820  6.968  3.707     0   15  *

24.820  7.103  4.244     0   15  *

24.820  7.137  4.423     0   15  *

24.820  7.230  5.132     0   15  *

24.820  7.266  5.566     0   15  *

24.820  7.282  5.793     0   15  *

24.820  7.335  6.239     0   15  *

24.820  7.365  6.481     0   15  *

24.820  7.449  7.504     0   15  *

24.820  7.473  8.223     0   15  *

24.820  7.477  8.650 88888   15  *

27.833   .000   .585     0   16

27.833   .902   .607     0   14

27.833  1.972   .668     0   14

27.833  3.033   .774     0   14

27.833  3.584   .860     0   14

27.833  4.081   .960     0   14

27.833  4.654  1.106     0   14

27.833  5.130  1.271     0   14

27.833  5.483  1.430     0   14

27.833  5.797  1.609     0   14

27.833  6.072  1.811     0   14

27.833  6.334  2.051     0   14

27.833  6.575  2.332     0   14

27.833  6.791  2.649     0   14

27.833  6.968  2.966     0   14

27.833  7.120  3.313     0   14

27.833  7.248  3.685     0   14

27.833  7.367  4.200     0   14

27.833  7.440  4.752     0   14

27.833  7.483  5.569     0   14

27.833  7.492  6.736     0   14

27.833  7.493  8.650 88888   14

30.848  1.649   .604     0   15

30.848  3.015   .716     0   15

30.848  3.560   .802     0   15

30.848  4.075   .911     0   15

30.848  4.667  1.070     0   15

30.848  5.166  1.250     0   15

30.848  5.453  1.381     0   15

30.848  5.709  1.518     0   15

30.848  5.941  1.667     0   15

30.848  6.151  1.829     0   15

30.848  6.416  2.082     0   15

30.848  6.657  2.374     0   15

30.848  6.870  2.698     0   15

30.848  7.117  3.191     0   15

30.848  7.303  3.725     0   15

30.848  7.413  4.218     0   15

30.848  7.486  4.856     0   15

30.848  7.498  5.395     0   15

30.848  7.501  7.708     0   15

30.848  7.499  8.650 88888   15

33.863  2.134   .808     0   16

33.863  3.011   .878     0   16

33.863  3.551   .963     0   16

33.863  4.063  1.079     0   16

33.863  4.630  1.253     0   16

33.863  5.142  1.460     0   16

33.863  5.672  1.750     0   16

33.863  5.907  1.911     0   16

33.863  6.120  2.079     0   16

33.863  6.392  2.341     0   16

33.863  6.636  2.634     0   16

33.863  6.852  2.947     0   16

33.863  7.114  3.426     0   16

33.863  7.300  3.901     0   16

33.863  7.416  4.343     0   16

33.863  7.474  4.743     0   16

33.863  7.501  5.316     0   16

33.863  7.501  5.575     0   16

33.863  7.501  5.813     0   16

33.863  7.501  6.410     0   16

33.863  7.500  8.650 88888   16

36.878  2.097  1.362     0   17

36.878  3.557  1.494     0   17

36.878  4.060  1.600     0   17

36.878  4.609  1.762     0   17

36.878  5.115  1.966     0   17

36.878  5.633  2.243     0   17

36.878  6.078  2.563     0   17

36.878  6.477  2.951     0   17

36.878  6.822  3.383     0   17

36.878  7.099  3.834     0   17

36.878  7.288  4.246     0   17

36.878  7.413  4.636     0   17

36.878  7.474  4.959     0   17

36.878  7.501  5.422     0   17

36.878  7.501  5.721     0   17

36.878  7.501  6.056     0   17

36.878  7.501  6.465     0   17

36.878  7.500  8.650 88888   17

38.386  1.969  1.719     0   18

38.386  3.024  1.771     0   18

38.386  3.566  1.838     0   18

38.386  4.060  1.936     0   18

38.386  4.603  2.091     0   18

38.386  5.105  2.283     0   18

38.386  5.614  2.545     0   18

38.386  6.059  2.853     0   18

38.386  6.462  3.225     0   18

38.386  6.806  3.639     0   18

38.386  7.090  4.072     0   18

38.386  7.285  4.459     0   18

38.386  7.413  4.825     0   18

38.386  7.474  5.118     0   18

38.386  7.501  5.538     0   18

38.386  7.501  5.822     0   18

38.386  7.501  6.148     0   18

38.386  7.501  6.550     0   18

38.386  7.499  8.650 88888   18

39.893  1.838  2.112     0   19

39.893  3.030  2.146     0   19

39.893  3.572  2.207     0   19

39.893  4.063  2.295     0   19

39.893  4.603  2.435     0   19

39.893  5.099  2.615     0   19

39.893  5.602  2.862     0   19

39.893  6.044  3.155     0   19

39.893  6.447  3.508     0   19

39.893  6.797  3.905     0   19

39.893  7.087  4.322     0   19

39.893  7.279  4.685     0   19

39.893  7.410  5.029     0   19

39.893  7.474  5.297     0   19

39.893  7.501  5.685     0   19

39.893  7.501  5.956     0   19

39.893  7.501  6.276     0   19

39.893  7.501  6.669     0   19

39.893  7.500  8.650 88888   19

41.401  1.686  2.521     0   20

41.401  3.575  2.579     0   20

41.401  4.069  2.658     0   20

41.401  4.606  2.786     0   20

41.401  5.096  2.954     0   20

41.401  5.596  3.185     0   20

41.401  6.035  3.463     0   20

41.401  6.437  3.798     0   20

41.401  6.788  4.173     0   20

41.401  7.081  4.572     0   20

41.401  7.279  4.913     0   20

41.401  7.410  5.243     0   20

41.401  7.471  5.496     0   20

41.401  7.501  5.861     0   20

41.401  7.501  6.124     0   20

41.401  7.501  6.434     0   20

41.401  7.501  6.815     0   20

41.400  7.499  8.650 88888   20

42.908  3.036  2.920 77777   21

42.908  3.581  2.957     0   21

42.908  4.075  3.027     0   21

42.908  4.612  3.143     0   21

42.908  5.096  3.295     0   21

42.908  5.593  3.508     0   21

42.908  6.032  3.767     0   21

42.908  6.434  4.087     0   21

42.908  6.785  4.441     0   21

42.908  7.081  4.822     0   21

42.908  7.276  5.148     0   21

42.908  7.410  5.465     0   21

42.908  7.471  5.709     0   21

42.908  7.501  6.063     0   21

42.908  7.501  6.316     0   21

42.908  7.501  6.614     0   21

42.908  7.501  6.986     0   21

42.908  7.499  8.650 88888   21

44.416  3.042  3.313 77777   22

44.416  3.588  3.341     0   22

44.416  4.081  3.396     0   22

44.416  4.621  3.499     0   22

44.416  5.102  3.636     0   22

44.416  5.599  3.834     0   22

44.416  6.032  4.072     0   22

44.416  6.434  4.374     0   22

44.416  6.782  4.709     0   22

44.416  7.078  5.075     0   22

44.416  7.276  5.386     0   22

44.416  7.410  5.694     0   22

44.416  7.471  5.931     0   22

44.416  7.501  6.279     0   22

44.416  7.501  6.526     0   22

44.416  7.501  6.815     0   22

44.416  7.501  7.175     0   22

44.416  7.499  8.650 88888   22

45.923  3.048  3.713 77777   23

45.923  3.597  3.728     0   23

45.923  4.094  3.770     0   23

45.923  4.633  3.856     0   23

45.923  5.112  3.975     0   23

45.923  5.608  4.154     0   23

45.923  6.038  4.374     0   23

45.923  6.441  4.657     0   23

45.923  6.785  4.977     0   23

45.923  7.081  5.328     0   23

45.923  7.276  5.630     0   23

45.923  7.410  5.928     0   23

45.923  7.471  6.163     0   23

45.923  7.501  6.511     0   23

45.923  7.501  6.748     0   23

45.923  7.501  7.032     0   23

45.923  7.501  7.376     0   23

45.923  7.499  8.650 88888   23

47.431  3.054  4.109 77777   24

47.431  4.106  4.142     0   24

47.431  4.654  4.209     0   24

47.431  5.127  4.307     0   24

47.431  5.627  4.468     0   24

47.431  6.050  4.670     0   24

47.431  6.450  4.938     0   24

47.431  6.791  5.243     0   24

47.431  7.084  5.581     0   24

47.431  7.279  5.880     0   24

47.431  7.410  6.172     0   24

47.431  7.474  6.407     0   24

47.431  7.501  6.748     0   24

47.431  7.501  6.983     0   24

47.431  7.501  7.254     0   24

47.431  7.501  7.587     0   24

47.430  7.500  8.650 88888   24

48.938  3.636  4.471 77777   25

48.938  4.121  4.490     0   25

48.938  4.682  4.542     0   25

48.938  5.145  4.621     0   25

48.938  5.648  4.764     0   25

48.938  6.066  4.950     0   25

48.938  6.462  5.206     0   25

48.938  6.803  5.505     0   25

48.938  7.090  5.834     0   25

48.938  7.282  6.130     0   25

48.938  7.410  6.419     0   25

48.938  7.474  6.654     0   25

48.938  7.501  6.998     0   25

48.938  7.501  7.227     0   25

48.938  7.501  7.486     0   25

48.938  7.501  7.803     0   25

48.938  7.500  8.650 88888   25

50.446  4.142  4.782 77777   26

50.446  4.709  4.825     0   26

50.446  5.169  4.895     0   26

50.446  5.669  5.029     0   26

50.446  6.084  5.206     0   26

50.446  6.477  5.456     0   26

50.446  6.812  5.755     0   26

50.446  7.096  6.084     0   26

50.446  7.285  6.383     0   26

50.446  7.413  6.672     0   26

50.446  7.474  6.907     0   26

50.446  7.501  7.248     0   26

50.446  7.501  7.471     0   26

50.446  7.501  7.718     0   26

50.446  7.501  8.022     0   26

50.446  7.500  8.650 88888   26

51.953  4.164  5.002 77777   27

51.953  4.737  5.048     0   27

51.953  5.191  5.118     0   27

51.953  5.694  5.255     0   27

51.953  6.105  5.435     0   27

51.953  6.489  5.691     0   27

51.953  6.825  5.992     0   27

51.953  7.102  6.328     0   27

51.953  7.288  6.629     0   27

51.953  7.413  6.922     0   27

51.953  7.474  7.157     0   27

51.953  7.501  7.498     0   27

51.953  7.501  7.666     0   27

51.953  7.501  7.827     0   27

51.953  7.501  8.242     0   27

51.953  7.500  8.650 88888   27

53.461  3.316  5.133 77777   28

53.461  4.191  5.160     0   28

53.461  4.761  5.218     0   28

53.461  5.218  5.297     0   28

53.461  5.715  5.447     0   28

53.461  6.124  5.636     0   28

53.461  6.505  5.901     0   28

53.461  6.834  6.218     0   28

53.461  7.105  6.559     0   28

53.461  7.294  6.870     0   28

53.461  7.416  7.169     0   28

53.461  7.474  7.407     0   28

53.461  7.501  7.754     0   28

53.461  7.501  7.916     0   28

53.461  7.501  8.071     0   28

53.461  7.501  8.464     0   28

53.461  7.500  8.650 88888   28

54.968  3.124  5.240 77777   29

54.968  3.725  5.255     0   29

54.968  4.215  5.288     0   29

54.968  4.788  5.358     0   29

54.968  5.243  5.453     0   29

54.968  5.736  5.614     0   29

54.968  6.142  5.819     0   29

54.968  6.517  6.093     0   29

54.968  6.846  6.425     0   29

54.968  7.111  6.779     0   29

54.968  7.297  7.102     0   29

54.968  7.416  7.410     0   29

54.968  7.474  7.657     0   29

54.968  7.501  8.013     0   29

54.968  7.501  8.175     0   29

54.968  7.501  8.321     0   29

54.968  7.500  8.650 88888   29

56.476  2.006  5.328 77777   30

56.476  3.746  5.358     0   30

56.476  4.243  5.401     0   30

56.476  4.816  5.486     0   30

56.476  5.270  5.593     0   30

56.476  5.758  5.767     0   30

56.476  6.163  5.986     0   30

56.476  6.532  6.276     0   30

56.476  6.855  6.620     0   30

56.476  7.117  6.986     0   30

56.476  7.300  7.327     0   30

56.476  7.416  7.651     0   30

56.476  7.474  7.916     0   30

56.476  7.501  8.300     0   30

56.476  7.501  8.605     0   30

56.476  7.500  8.650 88888   30

57.988  2.012  5.395 77777   31

57.988  3.155  5.407     0   31

57.988  3.761  5.447     0   31

57.988  4.267  5.502     0   31

57.988  4.837  5.605     0   31

57.988  5.301  5.733     0   31

57.988  5.788  5.928     0   31

57.988  6.194  6.166     0   31

57.988  6.559  6.477     0   31

57.988  6.876  6.837     0   31

57.988  7.129  7.224     0   31

57.988  7.306  7.590     0   31

57.988  7.419  7.934     0   31

57.988  7.477  8.236     0   31

57.988  7.500  8.650 88888   31

59.491  2.015  5.450 77777   32

59.491  3.164  5.474     0   32

59.491  3.770  5.523     0   32

59.491  4.289  5.596     0   32

59.491  4.859  5.721     0   32

59.491  5.337  5.877     0   32

59.491  5.828  6.102     0   32

59.491  6.233  6.370     0   32

59.491  6.596  6.703     0   32

59.491  6.904  7.090     0   32

59.491  7.145  7.495     0   32

59.491  7.315  7.897     0   32

59.491  7.422  8.278     0   32

59.491  7.479  8.650 88888   32

60.998  2.015  5.499 77777   33

60.998  3.170  5.529     0   33

60.998  3.777  5.593     0   33

60.998  4.307  5.685     0   33

60.998  4.880  5.837     0   33

60.998  5.377  6.026     0   33

60.998  5.874  6.288     0   33

60.998  6.282  6.590     0   33

60.998  6.468  6.764     0   33

60.998  6.639  6.953     0   33

60.998  6.937  7.367     0   33

60.998  7.163  7.800     0   33

60.998  7.327  8.245     0   33

60.998  7.423  8.650 99999   33

27.833   .000   .585       A1-1

27.833   .500   .587 88888 A1-1     APPENDAGE: SKEG

30.848   .000   .503       A1-2

30.848   .451   .503       A1-2

30.848   .902   .503       A1-2

30.848  1.567   .579       A1-2

30.848  1.649   .604 88888 A1-2     SHCP Offsets

33.863   .000   .421       A1-3     SHCP "C" Card data is as follows:

33.863   .677   .421       A1-3       Station spacing      =    1.000

33.863  1.356   .421       A1-3       Vert. scale factor   =      .0050

33.863  1.844   .549       A1-3       Horz. scale factor   =      .0050

33.863  2.064   .716       A1-3       L.B.P.               =   58.00

33.863  2.134   .808 88888 A1-3       Body plan scale      =     .125

36.878   .000   .341       A1-4       Number of appendages =    0

36.878   .549   .341       A1-4

36.878  1.097   .341       A1-4

36.878  1.585   .469       A1-4

36.878  1.804   .634       A1-4

36.878  1.969   .853       A1-4

36.878  2.067  1.097       A1-4

36.878  2.097  1.341       A1-4

36.878  2.097  1.362 88888 A1-4

38.386   .000   .302       A1-5

38.386   .485   .302       A1-5

38.386   .969   .302       A1-5

38.386  1.457   .430       A1-5

38.386  1.676   .594       A1-5

38.386  1.841   .814       A1-5

38.386  1.939  1.058       A1-5

38.386  1.969  1.302 77777 A1-5

38.386  1.969  1.719 88888 A1-5

39.893   .000   .262       A1-6

39.893   .421   .262       A1-6

39.893   .838   .262       A1-6

39.893  1.329   .390       A1-6

39.893  1.545   .555       A1-6

39.893  1.710   .771       A1-6

39.893  1.807  1.018       A1-6

39.893  1.838  1.262 77777 A1-6

39.893  1.838  2.112 88888 A1-6

41.401   .000   .223       A1-7

41.401   .354   .223       A1-7

41.401   .710   .223       A1-7

41.401  1.198   .347       A1-7

41.401  1.417   .515       A1-7

41.401  1.582   .732       A1-7

41.401  1.679   .978       A1-7

41.401  1.710  1.222 77777 A1-7

41.401  1.710  2.326 77777 A1-7

41.401  1.686  2.521 88888 A1-7

42.908   .000   .180       A1-8

42.908   .290   .180       A1-8

42.908   .582   .180       A1-8

42.908  1.070   .308       A1-8

42.908  1.289   .472       A1-8

42.908  1.454   .692       A1-8

42.908  1.551   .936       A1-8

42.908  1.582  1.180 77777 A1-8

42.908  1.582  2.286 77777 A1-8

42.908  1.454  2.774       A1-8

42.908  1.414  2.826       A1-8

42.908  1.414  2.951 88888 A1-8

44.416   .000   .140       A1-9

44.416   .226   .140       A1-9

44.416   .451   .140       A1-9

44.416   .942   .268       A1-9

44.416  1.158   .433       A1-9

44.416  1.323   .652       A1-9

44.416  1.420   .896       A1-9

44.416  1.451  1.140       A1-9

44.416  1.451  2.243       A1-9

44.416  1.323  2.734       A1-9

44.416  1.173  2.932 77777 A1-9

44.416  1.173  3.402 88888 A1-9

45.923   .000   .101       A1-10

45.923   .162   .101       A1-10

45.923   .323   .101       A1-10

45.923   .811   .229       A1-10

45.923  1.030   .393       A1-10

45.923  1.195   .613       A1-10

45.923  1.292   .856       A1-10

45.923  1.323  1.100       A1-10

45.923  1.323  2.204       A1-10

45.923  1.195  2.694       A1-10

45.923  1.030  2.911       A1-10

45.923   .930  2.987 77777 A1-10

45.923   .930  3.853 88888 A1-10

47.431   .000   .061       A1-11

47.431   .098   .061       A1-11

47.431   .195   .061       A1-11

47.431   .683   .189       A1-11

47.431   .902   .354       A1-11

47.431  1.067   .570       A1-11

47.431  1.164   .817       A1-11

47.431  1.195  1.061       A1-11

47.431  1.195  2.164       A1-11

47.431  1.067  2.652       A1-11

47.431   .902  2.871       A1-11

47.431   .689  3.033 77777 A1-11

47.431   .689  4.273 88888 A1-11

48.938   .000   .021       A1-12

48.938   .034   .021       A1-12

48.938   .064   .021       A1-12

48.938   .555   .149       A1-12

48.938   .771   .314       A1-12

48.938   .939   .530       A1-12

48.938  1.033   .777       A1-12

48.938  1.064  1.021       A1-12

48.938  1.064  2.121       A1-12

48.938   .939  2.612       A1-12

48.938   .771  2.829       A1-12

48.938   .555  2.996       A1-12

48.938   .445  3.039 77777 A1-12

48.938   .445  4.636 88888 A1-12

50.446   .000   .137       A1-13

50.446   .229   .165       A1-13

50.446   .457   .259       A1-13

50.446   .661   .418       A1-13

50.446   .817   .628       A1-13

50.446   .908   .866       A1-13

50.446   .936  1.100 77777 A1-13

50.446   .936  2.100 77777 A1-13

50.446   .908  2.329       A1-13

50.446   .817  2.557       A1-13

50.446   .661  2.762       A1-13

50.446   .457  2.917       A1-13

50.446   .229  3.008       A1-13

50.446   .204  3.011 77777 A1-13

50.446   .204  4.913 88888 A1-13

51.953   .000   .427       A1-14

51.953   .198   .454       A1-14

51.953   .393   .540       A1-14

51.953   .570   .689       A1-14

51.953   .704   .881       A1-14

51.953   .783  1.100       A1-14

51.953   .808  1.317       A1-14

51.953   .808  2.097       A1-14

51.953   .783  2.295       A1-14

51.953   .704  2.493       A1-14

51.953   .570  2.670       A1-14

51.953   .396  2.801       A1-14

51.953   .198  2.880       A1-14

51.953   .000  2.905 88888 A1-14

53.461   .000  1.149       A1-15

53.461   .165  1.170       A1-15

53.461   .332  1.241       A1-15

53.461   .479  1.356       A1-15

53.461   .591  1.509       A1-15

53.461   .658  1.683       A1-15

53.461   .680  1.853       A1-15

53.461   .680  2.094       A1-15

53.461   .658  2.262       A1-15

53.461   .591  2.426       A1-15

53.461   .479  2.576       A1-15

53.461   .332  2.688       A1-15

53.461   .165  2.752       A1-15

53.461   .000  2.774 99999 A1-15

42.908   .000  2.919       A2-1

42.908  3.036  2.920 77777 A2-1    APPENDAGE: Stern Tunnel

42.908  1.414  2.951 77777 A2-1

42.908   .000  2.952 88888 A2-1

44.418   .000  3.312       A2-2

44.418  3.042  3.313 77777 A2-2

44.418  1.173  3.402 77777 A2-2     SHCP Offsets

44.418   .000  3.403 88888 A2-2     SHCP "C" Card data is as follows:

45.928   .000  3.712       A2-3       Station spacing      =    1.000

45.928  3.048  3.713 77777 A2-3       Vert. scale factor   =      .0050

45.928   .930  3.853 77777 A2-3       Horz. scale factor   =      .0050

45.928   .000  3.854 88888 A2-3       L.B.P.               =   58.00

47.428   .000  4.108       A2-4       Body plan scale      =     .125

47.428  3.054  4.109 77777 A2-4       Number of appendages =    0

47.428  1.978  4.167       A2-4

47.428   .689  4.273 77777 A2-4

47.428   .000  4.274 88888 A2-4

48.938   .000  4.470       A2-5

48.938  3.636  4.471 77777 A2-5

48.938  1.981  4.539       A2-5

48.938   .445  4.636 77777 A2-5

48.938   .000  4.637 88888 A2-5

50.448   .000  4.781       A2-6

50.448  4.142  4.782 77777 A2-6

50.448   .204  4.913 77777 A2-6

50.448   .000  4.914 88888 A2-6

51.958   .000  5.001       A2-7

51.958  4.164  5.002 77777 A2-7

51.958  1.990  5.038       A2-7

51.958   .000  5.105 77777 A2-7

51.958   .000  5.106 88888 A2-7

53.458   .000  5.132       A2-8

53.458  3.316  5.133 77777 A2-8

53.458  1.996  5.163       A2-8

53.458   .000  5.224 88888 A2-8

54.968   .000  5.239       A2-9

54.968  3.124  5.240 77777 A2-9

54.968  2.000  5.252       A2-9

54.968   .000  5.307 88888 A2-9

56.478   .000  5.327       A2-10

56.478  2.006  5.328 77777 A2-10

56.478   .000  5.368 88888 A2-10

57.988   .000  5.394       A2-11

57.988  2.012  5.395 77777 A2-11

57.988   .000  5.426 88888 A2-11

59.488   .000  5.449       A2-12

59.488  2.015  5.450 77777 A2-12

59.488   .000  5.483 88888 A2-12

60.998   .000  5.498       A2-13

60.998  2.015  5.499 77777 A2-13

60.998   .000  5.544 99999 A2-13

56.798   .000  8.63        A3-1    NEGATIVE APPENDAGE: Stern Ramp

56.798  1.95   8.64  77777 A3-1    Frame 93 - Transom

56.798  1.95   8.65  88888 A3-1    SHCP Offsets

58.898   .000  7.25        A3-2    SHCP "C" Card data is same as above

58.898  1.95   7.26  77777 A3-2

58.898  1.95   7.27  88888 A3-2

60.998   .000  5.88        A3-3

60.998  1.95   5.89  77777 A3-3

60.998  1.95   5.90  99999 A3-3

24.818   .000  8.649       A8-1

24.818  7.493  8.650 77777 A8-1

24.818  7.493 11.400 88888 A8-1    APPENDAGE: Superstructure

26.109   .000  8.649       A8-1    24.818 m aft FP - frame 45

26.109  7.500  8.650 77777 A8-1

26.109  7.500 11.400 88888 A8-1

27.400   .000  8.649       A8-1

27.400  7.500  8.650 77777 A8-1

27.400  7.500 11.400 99999 A8-1

27.400   .000  8.649       A9-1

27.400  3.500  8.650 77777 A9-1

27.400  3.500 11.400 88888 A9-1    APPENDAGE: Superstructure

31.300   .000  8.649       A9-1    frame 45 - frame 58

31.300  3.500  8.650 77777 A9-1

31.300  3.500 11.400 88888 A9-1

35.200   .000  8.649       A9-1

35.200  3.500  8.650 77777 A9-1

35.200  3.500 11.400 99999 A9-1

Appendix B

Hydrostatics

SHIP-  FRV40  6-30-99                  NUMBER-     1            6/30/99

SHCP Ver. 3.16

Design Displacement           2438.696 metric tons SW

Design LCG                      29.342 meters from Station 0

Design Draft                     5.900 meters

Design Trim                       .000 meters (+ by stern)

Length Overall                  62.898 meters

Length Between Perpendiculars   58.000 meters

Length on Design Waterline      60.748 meters

Station of Max Area (at DWL)    30.422 meters from Station 0

Beam at Station of Max Area     15.013 meters

Section Area Coefficient         .7926

Prismatic Coefficient            .5840

Block Coefficient                .4628

Station 0 is located at the bow

No hog or sag

Appendage Properties at Design Condition --

No           Title                  Volume    Displ     TCB    VCB    LCB

1   Skeg                               118.7    121.8    .00   1.59  43.93

2   Stern tunnel                        -5.7     -5.8    .00   4.44  49.39

3   Stern ramp                           -.1      -.1    .00   6.99  60.16

4   Propeller                            1.5      1.5    .00   2.20  55.20

5   Rudder                               3.6      3.7    .00   2.40  58.30

6   Bilge keels                          1.9      1.9    .00   2.40  29.70

7   Shell plating                       10.0     10.3    .00   2.50  29.30

8   Suprstrt 24.818 - fr 45               .0       .0    .00    .00    .00

9   Suprstrt fr 45 - fr 58                .0       .0    .00    .00    .00

Ship-  FRV40  6-30-99                                              6/30/99

SHCP Ver. 3.16

HYDROSTATICS

Units and Definitions

CIDOMTS        Change in displacement for one meter of trim

by stern in tons

Displacement   Displacement in metric tons SW

Draft          Height above baseline in meters amidships

KB             Height of center of buoyance above baseline in

meters

LCB            Longitudinal center of buoyancy in meters from

Station 0

LCF            Longitudinal center of floatation in meters from

Station 0

Long BM        Longitudinal BM in meters

Long KM        Longitudinal KM in meters

MT1            Moment to change trim one centimeter in meter-tons

Prismatic      Prismatic Coefficient - Volume/(LBP X Area*)

TPC            Tons per centimeter immersion

Trnsv BM       Transverse BM in meters

Trnsv KM       Transverse KM in meters

Volume         Displaced volume in cubic meters

Wetted Surface Surface area of wetted portion of hull in square meters

WPlane Coef    Waterplane Coefficient - Waterplane Area/(LBP X Beam*)

WPlane I Coef  Inertia Coeff - WPlane Transv. Inertia/(LBP x Beam* cubed/12)

Station 0 is located at the bow

Area* and Beam* are properties at the tabulated draft of the station of

maximum area at design draft

All tons are metric tons = 1000 KG

Ship-  FRV40  6-30-99                                                   6/30/99

SHCP Ver. 3.16

HYDROSTATICS - PART I     Trim    .000 meters  with appendages

SW at   .975 cubic meters per ton

Hog =  .0000 meters

Draft   Volume  Displacement   LCB     KB    Wetted   Prism  WPlane WPlane

Surface   Coef   Coef  I Coef

4.50     1507.    1545.7    27.82    2.83      701.   .528   .615   .474

4.60     1560.    1600.1    27.87    2.89      716.   .530   .626   .484

4.70     1614.    1655.9    27.92    2.95      733.   .533   .635   .494

4.80     1670.    1712.7    27.99    3.01      750.   .536   .645   .505

4.90     1726.    1770.0    28.05    3.07      768.   .539   .657   .516

5.00     1784.    1829.4    28.13    3.13      787.   .542   .669   .528

5.10     1842.    1888.9    28.20    3.19      810.   .546   .687   .543

5.20     1902.    1950.9    28.29    3.25      834.   .549   .707   .558

5.30     1964.    2014.4    28.40    3.32      862.   .553   .728   .574

5.40     2028.    2080.4    28.53    3.38      895.   .558   .754   .592

5.50     2095.    2149.1    28.68    3.45      935.   .563   .786   .612

5.60     2165.    2220.3    28.85    3.52      955.   .568   .803   .629

5.70     2235.    2292.4    29.02    3.58      972.   .573   .812   .644

5.80     2306.    2365.2    29.18    3.65      988.   .579   .820   .657

DWL  5.90     2378.    2438.7    29.34    3.72     1003.   .584   .827   .669

6.00     2450.    2512.8    29.50    3.78     1017.   .589   .831   .679

6.10     2523.    2587.5    29.64    3.85     1032.   .594   .836   .689

6.20     2596.    2662.7    29.78    3.91     1045.   .599   .841   .699

6.30     2670.    2738.3    29.92    3.98     1059.   .604   .845   .708

6.40     2744.    2814.3    30.05    4.04     1072.   .609   .849   .716

6.50     2818.    2890.7    30.17    4.10     1086.   .613   .853   .723

HYDROSTATICS - PART II    Trim    .000 meters  with appendages

Draft  WPlane    LCF     TPC   CIDOMTS  Long.  Trnsv    Long.  Trnsv    MT1

Area                             BM      BM     KM      KM

4.50    532.   29.25    5.45    2.31    46.5   5.04    49.3   7.87    12.4

4.60    542.   29.52    5.56    4.97    47.1   4.99    50.0   7.88    13.0

4.70    550.   29.72    5.65    7.05    47.3   4.94    50.3   7.89    13.5

4.80    560.   29.96    5.74    9.55    47.8   4.89    50.8   7.90    14.1

4.90    570.   30.23    5.85   12.44    48.5   4.85    51.5   7.92    14.8

5.00    581.   30.53    5.96   15.68    49.3   4.81    52.5   7.94    15.6

5.10    596.   30.97    6.12   20.76    51.3   4.79    54.5   7.98    16.7

5.20    614.   31.50    6.30   27.15    53.9   4.77    57.1   8.03    18.1

5.30    633.   32.07    6.49   34.37    56.8   4.76    60.2   8.08    19.7

5.40    655.   32.78    6.72   43.85    60.9   4.76    64.3   8.14    21.8

5.50    684.   33.72    7.01   57.00    67.0   4.77    70.4   8.22    24.8

5.60    699.   34.14    7.16   63.46    68.8   4.74    72.3   8.26    26.3

5.70    707.   34.31    7.25   66.40    68.5   4.70    72.1   8.29    27.1

5.80    714.   34.43    7.32   68.57    67.9   4.65    71.5   8.30    27.7

DWL  5.90    720.   34.52    7.39   70.28    67.1   4.60    70.8   8.31    28.2

6.00    724.   34.52    7.42   70.67    65.6   4.54    69.4   8.32    28.4

6.10    728.   34.56    7.47   71.58    64.6   4.47    68.4   8.32    28.8

6.20    732.   34.58    7.51   72.31    63.5   4.41    67.4   8.32    29.2

6.30    736.   34.60    7.55   72.88    62.5   4.34    66.4   8.32    29.5