RCS WRC –07 Agenda Item Scope and High-Level Work Plan

Agenda Item 1.8 (Res 122):  “to consider the results of ITU-R studies on technical sharing and regulatory provisions for the application of high altitude platform stations operating in the bands 27.5-28.35 GHz and 31-31.3 GHz in response to Resolution 145 (WRC-03), and for high altitude platform stations operating in the bands 47.2-47.5 GHz and 47.9-48.2 GHz, in accordance with Resolution 122 (Rev. WRC-03);

Short Description:  Resolution 122 (WRC-03), contains the following issues:

- To study, as a matter of urgency, power limitations applicable for HAPS ground stations to facilitate sharing with space stations receivers.

- To review refinements to the regulatory provisions that might be needed in order to address those cases where the deployment of HAPS in the territory of one administration may affect other administrations.

- Continue to carry on studies to determine the appropriate technical sharing criteria, considering the operational environments and requirements of the Fixed, MSS, FSS, and RAS services.

Background:

WRC-97 made a provision for the operation of High Altitude Platform Stations (HAPS), also known as strategic repeaters, within a 2 X 300 MHz portion of the fixed-service allocation in the bands 47.2-47.5 GHz and 47.9-48.2 GHz.  During WRC-00, several countries expressed a need for a lower frequency band for HAPS due to excessive rain attenuation that occurs at 47 GHz.

In the WRC-03 revision to Resolution 122, the ITU-R was requested to complete sharing studies between the FSS and HAPS operation in the fixed service.  Following WRC-2000, Recommendation ITU-R SF.1481 was developed and adopted.  This recommendation makes clear that co-frequency operation between HAPS in the fixed service and FSS networks and systems is feasible in the 47.2 – 47.5 GHz and 47.9 – 48.2 GHz band (even though it was noted that “there may be a need to develop the maximum allowable power flux-density at satellites on the GSO due to aggregate interference caused by ground user terminals of high altitude platform networks”).

In the revision to Resolution 122 approved at WRC-03, co-existence between HAPS in the FS and the FSS at 47.2 – 47.5 GHz and 47.9 – 48.2 GHz was presumed feasible, as administrations were encouraged to facilitate inter-service coordination.  The ITU-R was invited to study power limitations on HAPS ground stations to facilitate sharing with space station receivers, regulatory criteria between HAPS in the FS and both radio astronomy and FSS systems (taking into account operational environments and the requirements of FSS systems).  WRC-03 decided, after much debate, to retain the prior limitation on notices for new FSS networks – but only in Regions 1 and 3.  WRC-03 also decided to maintain indefinitely notices for HAPS that were received by the BR prior to 22 November 1997.

Countries with a particular interest: Japan

Scope of Agenda Item:  The responsible group for this agenda item is WP 4-9S, with WP 9B and 9D as contributing groups, and WP 4A(orbit/spectrum utilization), as an interested group.

Key technical/regulatory issues to be resolved:

- Appropriate power limits that permit HAPS ground station operation while protecting space borne receivers.

- Refinement of regulatory provisions applicable to HAPS stations in the fixed service in these bands.

Key policy issues to be resolved:

- Possible sharing and continued protection of incumbent services.

- Coordination procedures between systems in the fixed service and systems of the co-primary satellite service in the same bands (47.2-47.5 GHz and 47.9-48.2 GHz)

Work Plan and Organization Participation:

Work to be completed in support of this agenda item is as follows:

- Determine future HAPS operational and technical requirements. (Government and Industry)

- Determine acceptable power limitations that provide protection for incumbent satellite services. (Government and Industry)

- Perform appropriate sharing studies. (Government and Industry)

- Develop Draft CPM text. (Government and Industry)

- The responsible group for this agenda item is WP 4-9S while WP 9B and 9D are Contributing groups and WP 4A is an interested group.

Reference Material:

ITU-R Recommendation F.1500, ITU-R Recommendation SF.1481, WRC-03 Resolution 122, RR No. 5.552

# Footnotes

Author:  G. Chinault (DoD) and Lily Assefa (DoD) Document Date:  June 1, 2004