#### Geologic datasets for weights-of-evidence analysis in northeast Washington

#### —2. Mineral databases

by  D.E. Boleneus

##### Open-File Report 99-384

1999

Manuscript approved July 28, 1999

This report is preliminary and has not been reviewed for conformity with U.S. Geological Survey editorial standards and the North American Stratigraphic Code.  Any use of trade, product, or firm names is for descriptive purposes only and does not imply endorsement by the U.S. Government.

Although this program has been used the US Geological Survey, no warranty, expressed or implied, is made by the USGS as to the accuracy and functioning of the program and related program material, nor shall the fact of distribution constitute any such warranty, and no responsibility is assumed by the USGS in connection therewith.

# U.S DEPARTMENT OF THE INTERIOR

U.S. GEOLOGICAL SURVEY

Contents

Abstract	3

Introduction	3

Description of data	3

Training sites for epithermal gold model.	5

Placer gold sites.	5

Training sites for carbonate-hosted lead-zinc model	5

Small lead-zinc mines and prospects	5

How to obtain digital data	6

References	7

Appendix I. Metadata	26

### Tables

Table 1.  Training sites for epithermal gold.	8

Table 2. Placer gold sites	11

Table 3. Training sites for carbonate-hosted lead-zinc.	16

Table 4. Small lead-zinc mines and prospects.	17

Table 5.  Township and range location for sites	19

### Figure

Figure 1. Location map showing study areas of epithermal gold and carbonate-hosted lead-zinc deposits.	4

# Abstract

Digital mineral databases are necessary to carry out weights-of-evidence modeling of mineral resources for epithermal gold and carbonate-hosted lead-zinc deposits in northeast Washington. This report describes spreadsheet tables consisting of:  1) training sites for epithermal gold, 2) placer gold sites, 3) training sites for carbonate-hosted lead-zinc, and 4) small lead-zinc mines and prospects. A fifth table provides location data about sites in the four tables.

# Introduction

Digital mineral databases were necessary to perform spatial modeling of mineral resources and to investigate mineral potential in Northeastern.  The spatial modeling was performed using weights-of-evidence analysis on a geographic information system and requires all digital data.  Four mineral database themes necessary for the spatial modeling are described in this report, placer gold sites, a training set for epithermal gold deposits, a training set for carbonate-hosted lead-zinc deposits, and small lead-zinc mines and prospects. Tables 1 and 2 were used in weights-of-evidence modeling of epithermal gold deposits of northeast Washington (unpublished data). Tables 3 and 4 were similarly used for modeling of carbonate-hosted lead-zinc deposits of northeastern Washington (unpublished data). A fifth table provides additional township and range location data about sites in the four tables. The data in these tables occur within a 138-mile by 72-mile area in northeast Washington bounded by Idaho on the east and Canada on the north. It includes all of Pend Oreille County and large portions of Douglas, Ferry, Okanogan, and Stevens counties. (Figure 1)

# Description of data

The data in each of the tables described below were obtained primarily from the USGS Mineral Resource Data System (MRDS, 1998) database and supplemented using the USBM Minerals Availability System (MAS-MILS, 1995) database by applying specific selection criteria. The USGS MRDS and USBM MAS-MILS databases contain economic geology data for over 220,000 mines, prospects or mineral occurrences worldwide. The MRDS number begins with the letters “SP”, “D”, “W”, “K” or “M” followed by a 5- or 6-digit number and the MAS-MILS sequence number contains 10 digits. MAS-MILS record data were included because they complement the MRDS.  Multiple MRDS records describing the same property were identified for at least 33 properties The duplicated MRDS records were retained for later reference.

Figure 1. Location map showing study areas of epithermal gold and carbonate-hosted lead-zinc deposits.

### Training sites for epithermal gold model.

The training sites consist of a collection of mines, prospects or occurrences selected from MRDS or MAS-MILS database because of their epithermal gold-like characteristics. Sites were qualified for the epithermal gold model if they met the selection criteria below for any of the USGS models for Au-Ag hot spring, 25a (Berger, 1992), Creede epithermal veins, 25b (Mosier and others, 1992), or Comstock epithermal veins, 25c (Mosier, Singer and Berger, 1992). See Table 1.  Fifty sites were selected where

- sites are spatially associated with Eocene volcanic or hypabyssal rocks and

- gold occurs in quartz veins or disseminations.

Additional characteristics provided from records for each site facilitated classifying the deposit with models, 25a, 25b, or 25c.

In addition to location data, the mining district, commodities present, production size and development status are also provided.

### Placer gold sites.

Placer sites indicate locations of mines or prospects of placer gold mining or prospecting. (Table 2) Sixty-seven sites were selected from the MRDS and MAS-MILS where:

- gold is the primary commodity and

- “placer” was indicated by the name, deposit type, or modifier of commodity.

Thirty-six of the sites were obtained from the USGS MRDS database and the remaining 31 sites were obtained from the MAS-MILS database. Production data were not available for any sites.

### Training sites for carbonate-hosted lead-zinc model

The second group of training sites were selected because they exhibit characteristics similar to the USGS model for carbonate-hosted lead-zinc (Briskey, 1992). Eleven mines were selected where  (Table 3):

- lead and zinc are the primary commodities,

- the deposit is either stratiform or pipe-like in form or exhibit breccia or replacement texture,

- the deposit occurs within strata of either the Maitlen Phyllite of Cambrian age, the Metaline Formation of Cambrian age or the Ledbetter Slate of Ordovician age, and

- the mine has produced more than 100,000 tons of ore.

### Small lead-zinc mines and prospects

Smaller deposits described as carbonate-hosted lead-zinc deposits are those where no ore was produced or those having total production up to 100,000 tons. These smaller deposits were selected using the selection criteria used (above) for training sites of carbonate-hosted lead-zinc deposits. Sixty-two deposits are represented in the group.  See Table 4.

Table 5 provides locations for sites in tables 1-4 given by township, range and section (TRS)and by latitude and longitude. The latitude and longitude were calculated from the TRS. The latitude and longitude were calculated for a central point in a section. For sites occupying two or more sections, this was done by arbitrarily selecting an “assumed section” that occupied that occurred at the center. The calculation method then uses the freeware script, ‘TRS2LL’ (Martin Wefald, written commun.). The resulting latitude and longitude refer to a point in the center of the assumed section.

Four files found on the diskette include:

- Report containing all tables and metadata appendices labeled “of99-384.doc” (~415 kb, MS Word 97);

- Tables 1-5 on spreadsheet (~200 kb, MS Excel 97) which contains five worksheet tables in file labeled “of99-384.xls”. Worksheets are labeled as follows:      1. Small_PbZn_Mines, 2. Placer_Sites, 3. Trainsites_epith, 4. Trainsites_PbZn, and 5. Township_location;

- Metadata (~16 kb) in text document labeled “of99-384.met”; and

- Figure 1 (139 kb, JPEG image) labeled “of99-384.jpg”.

# How to obtain digital data

The complete digital files are available at the USGS web site.

To obtain copies of the digital data, do one of the following:

# Download the digital files from the USGS public access World Wide Web site on the

# Internet URL = http://wrgis.wr.usgs.gov/open-file/of99-384/of99-384.html

The data are also available on diskette from USGS Open-File Services, Denver Federal Center, Denver, CO.

# References

Berger, B.R., 1992, Descriptive model of hot-spring Au-Ag (25a):  U S Geological Survey Bulletin 1693, p. 143.

Briskey, J.A., 1992, Descriptive model of southeast Missouri Pb-Zn (32a):  U S Geological Survey Bulletin 1693, p 220.

Derkey, R.E., Joseph, N.L., and Lasmanis, R., 1990, Metal mines of Washington—preliminary report: Washington Division of Geology and Earth Resources Open File Report 90-18, 577 p.

Huntting, M.T., 1956, Inventory of Washington minerals: Washington Division of Mines and Geology, Bulletin 37, vol. 1, 428 p.

Long, K.R., DeYoung, J.H., Jr., and Ludington, S.D., 1998, Database of significant deposits of gold, silver, copper, lead, and zinc in the United States; Part A, Database description and analysis; Part B, Database: U.S. Geological Survey Open-File Report 98-206A, 33p., 98-206B, one 3.5 inch floppy diskette.

Mills, J.W., 1977, Zinc and lead ore deposits in carbonate rocks, Stevens County, Washington: Washington Division of Geology and Earth Resources Bulletin 70, 171 p.

Mosier, D.L. Sato, T., Page, N.J., Singer, D.A., and Berger, B.A., 1992, Descriptive model of Creede epithermal veins (25b): U S Geological Survey Bulletin 1693, p 145.

Mosier, D.L., Singer, D.A., and Berger, B.R., 1992, Descriptive model of Comstock epithermal veins (25c): U S Geological Survey Bulletin 1693, p. 150.

USBM, 1995, US Bureau of Mines MAS/MILS CD-ROM: Spatial data extracted from the Mineral Availability System/Mineral Industry Location System (MAS/MILS):  US Bureau of Mines Special Publication 12-95, 1 CD-ROM.

# USGS, Mineral Resource Data System: U.S. Geological Survey.

# Table 1.  Training sites for epithermal gold.

| NO. | SITE NAME | MRDS ID. NO. | MAS ID. NO. | LATITUDE | LONGITUDE | COUNTY | STATE | COMMODITIES PRESENT | USGS MODEL1 | PRODUCTION SIZE | DEVELOPMENT STATUS |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | ADMIRAL | M056000 |  | 48.6600 | -118.7369 | FERRY | WA | AU | 25a | No production | Occurrence |
| 2 | ADVANCE | M056001 |  | 48.6267 | -118.7453 | FERRY | WA | AU AG | 25a | No production | Occurrence |
| 3 | ALPINE | M056023 |  | 48.6767 | -118.7578 | FERRY | WA | AU AG | 25a | No production | Occurrence |
| 4 | ANECIA | M056024 |  | 48.6619 | -118.7803 | FERRY | WA | AU AG | 25a | No production | Occurrence |
| 5 | BEN HUR | SP00062 |  | 48.6686 | -118.7581 | FERRY | WA | AU AG | 25c | No production | Developed prospect |
| 6 | BLACK TAIL (Hope) | SP00063 |  | 48.6633 | -118.7475 | FERRY | WA | AU AG | 25c | No production | Occurrence |
| 7 | BODIE | M056027 |  | 48.6606 | -118.7572 | FERRY | WA | AU AG | 25a | No production | Occurrence |
| 8 | COOK | M056029 |  | 48.6372 | -118.7536 | FERRY | WA | AU | 25a | No production | Occurrence |
| 9 | EAST SAN POIL | M056030 |  | 48.6614 | -118.7572 | FERRY | WA | AU AG | 25a | No production | Occurrence |
| 10 | EL CALIPH | M056031,SP00068 |  | 48.6592 | -118.7639 | FERRY | WA | AU AG | 25c | No production | Prospect |
| 11 | FLAG HILL | M056032,SP00069 |  | 48.6522 | -118.7536 | FERRY | WA | AU AG SE | 25c | No production | Prospect |
| 12 | GOLDEN EAGLE | M056004 |  | 48.6600 | -118.7369 | FERRY | WA | AU AG | 25a | No production | Occurrence |
| 13 | IDA MAY | SP00075 |  | 48.6547 | -118.7647 | FERRY | WA | AU AG | 25c | No production | Occurrence |
| 14 | INSURGENT | SP00076 |  | 48.6669 | -118.7461 | FERRY | WA | AU AG | 25c | No production | Occurrence |
| 15 | IRON MASK | M056033 |  | 48.6561 | -118.7544 | FERRY | WA | AU AG | 25a | No production | Prospect |
| 16 | IRON MOUNTAIN | M056123 |  | 48.5639 | -118.5994 | FERRY | WA | AG AU | 25a | No production | Prospect |
| 17 | JIM BLAINE FRACTION | M056009 |  | 48.6328 | -118.7453 | FERRY | WA | AU AG | 25a | No production | Occurrence |
| 18 | K2 MINE2 | na | 0530190470 | 48.8660 | -118.6680 | FERRY | WA | AU AG | 25a | Large | Active mine |
| 19 | KANGAROO | M056034 |  | 48.6614 | -118.7572 | FERRY | WA | AU AG | 25a | No production | Occurrence |
| 20 | KETTLE | SP00080 |  | 48.8789 | -118.6256 | FERRY | WA | AU AG | 25a | Large | Active mine |
| 21 | KNOB HILL MINE-PLANT | na | 0530190084 | 48.6734 | -118.7578 | FERRY | WA | AU AG | 25c | Large | Inactive producer |
| NO. | SITE NAME | MRDS ID. NO. | MAS ID. NO. | LATITUDE | LONGITUDE | COUNTY | STATE | COMMODITIES PRESENT | USGS MODEL1 | PRODUCTION SIZE | DEVELOPMENT STATUS |
| 22 | LAST CHANCE | M056010,D001629, SP0008 |  | 48.6658 | -118.7458 | FERRY | WA | AU AG | 25a | Small | Developed prospect |
| 23 | LITTLE COVE | M056036,SP00085 |  | 48.6669 | -118.7533 | FERRY | WA | AU AG | 25c | No production | Prospect |
| 24 | LONE PINE | M056037,SP00086 |  | 48.6653 | -118.7506 | FERRY | WA | AU AG | 25c | Small | Developed prospect |
| 25 | MAMMOTH | M056011 |  | 48.6725 | -118.7428 | FERRY | WA | AU AG | 25a | No production | Occurrence |
| 26 | MOUNTAIN LION | M056039,SP00095 |  | 48.6789 | -118.7686 | FERRY | WA | AU AG | 25c | Small | Developed prospect |
| 27 | NORTH SAN POIL | SP00096,M056012 |  | 48.6667 | -118.7586 | FERRY | WA | AU AG | 25c | No production | Occurrence |
| 28 | OLD HICKORY | SP00097,M056013 |  | 48.6392 | -118.7428 | FERRY | WA | AU | 25c | No production | Occurrence |
| 29 | PEARL | M056040,SP00100 |  | 48.6669 | -118.7533 | FERRY | WA | AU AG | 25c | No production | Prospect |
| 30 | PRINCESS MAUDE (Southern Republic) | SP00102 |  | 48.6347 | -118.7475 | FERRY | WA | AU AG | 25c | No production | Occurrence |
| 31 | QUILP (Imperator, Eureka) | M056016 |  | 48.6561 | -118.7475 | FERRY | WA | AU AG | 25c | Small | Developed prospect |
| 32 | REBATE | M056041 |  | 48.6939 | -118.7542 | FERRY | WA | AU AG | 25a | No production | Occurrence |
| 33 | REPUBLIC (Blaine Republic) | SP00104 |  | 48.6375 | -118.7453 | FERRY | WA | AU AG SE | 25c | No production | Occurrence |
| 34 | SAN POIL FRACTION | M056043, M056042, SP0010 |  | 48.6669 | -118.7533 | FERRY | WA | AU AG | 25a | No production | Occurrence |
| 35 | SEATTLE | M056044,SP00107 |  | 48.6642 | -118.7669 | FERRY | WA | AU AG | 25c | No production | Prospect |
| 36 | SNOWSTORM | M056045 |  | 48.6614 | -118.7572 | FERRY | WA | AU AG | 25a | No production | Occurrence |
| 37 | SOUTH PENN | SP00112,M056046 |  | 48.6903 | -118.7558 | FERRY | WA | AU AG | 25c | No production | Occurrence |
| 38 | STANDARD AND EMMA | M056018 |  | 48.6306 | -118.7461 | FERRY | WA | AU AG | 25a | No production | Occurrence |
| NO. | SITE NAME | MRDS ID. NO. | MAS ID. NO. | LATITUDE | LONGITUDE | COUNTY | STATE | COMMODITIES PRESENT | USGS MODEL1 | PRODUCTION SIZE | DEVELOPMENT STATUS |
| 39 | SURPRISE | SP00114,M056019 |  | 48.6608 | -118.7492 | FERRY | WA | AU AG | 25c | No production | Occurrence |
| 40 | TOM THUMB | SP00117,M056047 |  | 48.6961 | -118.7572 | FERRY | WA | AU AG | 25c | No production | Occurrence |
| 41 | TRADE DOLLAR | M056048,SP00118 |  | 48.6733 | -118.7508 | FERRY | WA | AU AG | 25c | No production | Prospect |
| 42 | V FRACTION | M056021 |  | 48.6658 | -118.7458 | FERRY | WA | AU AG | 25a | No production | Occurrence |
| 43 | ZALLA M | M056126,SP00122 |  | 48.7667 | -118.8314 | FERRY | WA | AG CU AU | 25b | Small | Developed prospect |
| 44 | AMERICAN FLAG | SP00186 |  | 48.7536 | -118.8453 | OKANOGAN | WA | AU CU ZN | 25b | No production | Occurrence |
| 45 | BODIE GOLD MINE (Northern Gold) | M056791 |  | 48.8158 | -118.9036 | OKANOGAN | WA | AU AG CU | 25a | Small | Developed prospect |
| 46 | SHERIDAN (Phil Sheridan) | SP00283 |  | 48.7786 | -118.8547 | OKANOGAN | WA | AG AU | 25a | Small | Inactive producer |
| 47 | SILVER BELL | SP00285 |  | 48.7597 | -118.8383 | OKANOGAN | WA | AU AG | 25b | Small | Occurrence |
| 48 | FIRST THOUGHT MINE | M060170,M056476 |  | 48.8839 | -118.1611 | STEVENS | WA | AU AG | 25c | Small | Inactive producer |
| 49 | HIDDEN TREASURE | M056495 |  | 48.8739 | -118.1656 | STEVENS | WA | AU | 25a | No production | Prospect |
| 50 | NEST EGG | M056501 |  | 48.8481 | -118.1586 | STEVENS | WA | AU AG CU | 25a | No production | Occurrence |
| 1 Hot spring Au-Ag (25a); Creede epithermal veins(25b); Comstock epithermal veins (25c);; 2 Long, DeYoung, and Ludington, 1998; (..) alternate name; na none available |  |  |  |  |  |  |  |  |  |  |  |

# Table 2. Placer gold sites

| NO. | SITE NAME | MRDS ID. NO. | MAS ID. NO. | LATITUDE | LONGITUDE | COUNTY | STATE | DISTRICT |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | BOULDER CR. PLACERS | W007555 |  | 48.6006 | -116.0883 | BOUNDARY | ID | PRIEST LAKE |
| 2 | COPPER CREEK | na | 0160210133 | 48.9803 | -116.1728 | BOUNDARY | ID |  |
| 3 | POINT BAR PLACER | na | 0160210134 | 48.7861 | -116.1533 | BOUNDARY | ID |  |
| 4 | ALVA STOUT | M056072 |  | 48.6494 | -118.7744 | FERRY | WA | REPUBLIC |
| 5 | BLANCE | M056073 |  | 48.6528 | -118.8058 | FERRY | WA | REPUBLIC |
| 6 | BLUE BAR ISLAND | M056062 |  | 48.2000 | -118.2003 | FERRY | WA |  |
| 7 | BLUE BAR ISLAND PLACER | na | 0530190123 | 48.2072 | -118.1994 | FERRY | WA |  |
| 8 | BRIDGE CREEK | M056063 |  | 48.2264 | -118.1767 | FERRY | WA |  |
| 9 | DAISY | M056067 |  | 48.3897 | -118.1981 | FERRY | WA |  |
| 10 | DORA B PLACER | na | 0530190127 | 48.6472 | -118.8153 | FERRY | WA |  |
| 11 | DOVA B | M056074 |  | 48.6528 | -118.8058 | FERRY | WA | EUREKA |
| 12 | GOLD CREEK | M056077 |  | 48.4253 | -118.8450 | FERRY | WA |  |
| 13 | GOOSMUS CREEK PLACER | na | 0530190129 | 48.9631 | -118.5806 | FERRY | WA |  |
| 14 | JOHNSON PLACER | M056068 |  | 48.2911 | -118.1633 | FERRY | WA |  |
| 15 | KELLER PLACERS | na | 0530190397 | 48.0856 | -118.6903 | FERRY | WA |  |
| NO. | SITE NAME | MRDS ID. NO. | MAS ID. NO. | LATITUDE | LONGITUDE | COUNTY | STATE | DISTRICT |
| 16 | NINEMILE | M056070 |  | 48.0158 | -118.3972 | FERRY | WA |  |
| 17 | SANDPOIL RIVER, WEST FLA. | M056076 |  | 48.4581 | -118.7719 | FERRY | WA |  |
| 18 | SINGER PLACER | SP00111 |  | 48.9961 | -118.5308 | FERRY | WA | DANVILLE |
| 19 | STRAY DOG PLACER | M056065 |  | 48.2053 | -118.1992 | FERRY | WA |  |
| 20 | THOMPSON | M056066 |  | 48.2189 | -118.1861 | FERRY | WA |  |
| 21 | TURTLE RAPIDS PLACER | na | 0530190177 | 48.1783 | -118.2500 | FERRY | WA |  |
| 22 | BALLARD PLACER | na | 0530470493 | 48.5319 | -119.7450 | OKANOGAN | WA |  |
| 23 | CASSIMER BAR PLACER | SP00204 |  | 48.0992 | -119.7181 | OKANOGAN | WA |  |
| 24 | CONDON FERRY PLACER | na | 0530470512 | 48.1100 | -119.3111 | OKANOGAN | WA |  |
| 25 | CROUNSE PLACER | SP00211 |  | 48.3997 | -118.8789 | OKANOGAN | WA |  |
| 26 | CUBA LINE PLACER | M056821 |  | 48.9967 | -119.1053 | OKANOGAN | WA | MYERS CREEK; CHESAW |
| 27 | DAN MOONEY PLACER | na | 0530470513 | 48.9606 | -119.0406 | OKANOGAN | WA |  |
| 28 | DAVEY PLACER | na | 0530470514 | 48.9600 | -119.0408 | OKANOGAN | WA |  |
| NO. | SITE NAME | MRDS ID. NO. | MAS ID. NO. | LATITUDE | LONGITUDE | COUNTY | STATE | DISTRICT |
| 29 | DEADMAN CREEK PLACER | na | 0530470497 | 48.9167 | -119.0550 | OKANOGAN | WA |  |
| 30 | FOURTH OF JULY CREEK PLACER | na | 0530470498 | 48.9167 | -119.0558 | OKANOGAN | WA |  |
| 31 | GOLD BAR PLACER | na | 0530470508 | 48.1053 | -119.2664 | OKANOGAN | WA |  |
| 32 | HOPKINS PLACER | na | 0530470499 | 48.1133 | -119.2311 | OKANOGAN | WA |  |
| 33 | MARY ANN CREEK PLACER | SP00250 |  | 48.9403 | -119.0517 | OKANOGAN | WA |  |
| 34 | MEADOWS PLACER | na | 0530470501 | 48.6550 | -119.8528 | OKANOGAN | WA |  |
| 35 | MURRAY PLACER | M056823 |  | 48.2000 | -119.2544 | OKANOGAN | WA | KARTAR |
| 36 | NESPELEM BAR PLACER | na | 0530470502 | 48.1361 | -119.0539 | OKANOGAN | WA |  |
| 37 | NUGGET PLACER | na | 0530470503 | 48.4100 | -118.9039 | OKANOGAN | WA |  |
| 38 | RICH BAR PLACER | na | 0530470045 | 48.9822 | -119.5364 | OKANOGAN | WA |  |
| 39 | SHOTWELL PLACER | SP00284 |  | 48.0342 | -119.6828 | OKANOGAN | WA |  |
| 40 | SIMILKAMEEN FALLS PLACER | na | 0530470505 | 48.9703 | -119.5017 | OKANOGAN | WA |  |
| NO. | SITE NAME | MRDS ID. NO. | MAS ID. NO. | LATITUDE | LONGITUDE | COUNTY | STATE | DISTRICT |
| 41 | SIMILKAMEEN PLACERS | na | 0530470506 | 48.9806 | -119.5492 | OKANOGAN | WA |  |
| 42 | WALKER PLACER | SP00299 |  | 48.9689 | -119.1144 | OKANOGAN | WA | MYERS CREEK |
| 43 | BROWNS LAKE PLACER | M025803 |  | 48.4392 | -117.1828 | PEND OREILLE | WA | BEAD LAKE |
| 44 | HARVEY BAR PLACER | M025804 |  | 48.9439 | -117.3300 | PEND OREILLE | WA | METALINE |
| 45 | SCHIERDING PLACER | M025805 |  | 48.9881 | -117.3447 | PEND OREILLE | WA | METALINE |
| 46 | SCHULTZ PLACER | na | 0530510304 | 48.8597 | -117.4111 | PEND OREILLE | WA |  |
| 47 | SULLIVAN CREEK PLACER | na | 0530510305 | 48.8383 | -117.2653 | PEND OREILLE | WA |  |
| 48 | AMBROSE MINING | na | 0530650884 | 48.9611 | -117.8500 | STEVENS | WA |  |
| 49 | BLUE BAR | M056523 |  | 48.1714 | -118.1875 | STEVENS | WA | KETTLE FALLS |
| 50 | BLUE BAR PLACER | na | 0530650172 | 48.1700 | -118.1833 | STEVENS | WA |  |
| 51 | BOSSBURG BAR | M056520 |  | 48.7564 | -118.0475 | STEVENS | WA |  |
| 52 | CHINA BEND PLACER | na | 0530650173 | 48.8006 | -118.0192 | STEVENS | WA |  |
| 53 | COLLINS | M056525 |  | 48.3883 | -118.1697 | STEVENS | WA |  |
| 54 | EVANS PLACER | na | 0530650174 | 48.9350 | -117.7631 | STEVENS | WA |  |
| 55 | GIBSON BAR | M056524 |  | 48.0214 | -118.3919 | STEVENS | WA |  |
| NO. | SITE NAME | MRDS ID. NO. | MAS ID. NO. | LATITUDE | LONGITUDE | COUNTY | STATE | DISTRICT |
| 56 | HOLSTEN | M056522 |  | 48.5000 | -118.1750 | STEVENS | WA |  |
| 57 | MARCUS PLACER | M056518 |  | 48.6656 | -118.0675 | STEVENS | WA |  |
| 58 | MEYERS FALLS | M056515 |  | 48.5936 | -118.0647 | STEVENS | WA |  |
| 59 | NIGGER CREEK BAR PLACER | na | 0530650179 | 48.9403 | -117.7656 | STEVENS | WA |  |
| 60 | NINEMILE BAR | M056519 |  | 48.7956 | -118.0036 | STEVENS | WA |  |
| 61 | NOBLES PLACER | na | 0530650182 | 48.8472 | -117.9117 | STEVENS | WA |  |
| 62 | ORIENT | M056521 |  | 48.8611 | -118.1997 | STEVENS | WA | ORIENT |
| 63 | ORIENT PLACER | na | 0530650184 | 48.8606 | -118.0722 | STEVENS | WA |  |
| 64 | REED AND ROBERTS PLACER | na | 0530650185 | 48.9544 | -117.7344 | STEVENS | WA | NORTHPORT |
| 65 | SANDOZ | M056517 |  | 48.6964 | -118.0164 | STEVENS | WA |  |
| 66 | STRANGER CREEK | M056069 |  | 48.3083 | -118.1478 | STEVENS | WA |  |
| 67 | VALBUSH BAR | M056516 |  | 48.7000 | -118.0206 | STEVENS | WA |  |
| na none available |  |  |  |  |  |  |

# Table 3. Training sites for carbonate-hosted lead-zinc.

| NO. | SITE NAME | MRDS ID. NO. | MAS ID. NO. | LATITUDE | LONGITUDE | COUNTY | STATE | DISTRICT | COMMODITIES PRESENT | TONS PRODUCED1 | DEVELOPMENT STATUS |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | ADMIRAL CONSOLIDATED1 | na | 0530650405 | 48.92720 | -117.57580 | STEVENS | WA | NORTHPORT | ZN PB AG CD | 115,545 | INACTIVE PRODUCER |
| 2 | BLUE BUCKET MINE (Kroll) | M025855 |  | 48.84333 | -117.40690 | PEND OREILLE | WA | METALINE | ZN PB AG | 183,000 | INTERMITTENT PRODUCER |
| 3 | DEEP CREEK MINE (Gorien Zinc, Northport) | M060115 |  | 48.86389 | -117.71500 | STEVENS | WA | NORTHPORT | PB ZN CU AG AU | 450,000 | INACTIVE PRODUCER |
| 4 | ELECTRIC POINT1 | na | 0530650244 | 48.88280 | -117.54140 | STEVENS | WA | NORTHPORT | PB AG ZN CU | 600,000 | INACTIVE PRODUCER |
| 5 | GLADSTONE MINE | M060143 |  | 48.88611 | -117.54167 | STEVENS | WA | NORTHPORT | PB AG ZN CU | 310,000 | INTERMITTENT PRODUCER |
| 6 | GRANDVIEW MINE | na | 0530510133 | 48.87778 | -117.35750 | PEND OREILLE | WA | METALINE | ZN PB AG CD U CU | 2,348,000 | INACTIVE PRODUCER |
| 7 | JOSEPHINE MINE (Clark) | M025825 |  | 48.88000 | -117.37111 | PEND OREILLE | WA | METALINE | ZN PB AG CD U F | 283,000 | INACTIVE PRODUCER |
| 8 | LAST CHANCE MINE (Jupiter) | M060171 |  | 48.86694 | -117.69917 | STEVENS | WA | NORTHPORT | PB ZN AG | 118,000 | INACTIVE PRODUCER |
| 9 | METALINE FALLS PROSPECT | M025845 |  | 48.86833 | -117.36667 | PEND OREILLE | WA | METALINE | PB ZN | 410,724 | PROSPECT |
| 10 | PEND OREILLE MINE (Josephine, Metaline Metals, Yellowhead, Flusey-Hoopala) | M060153 |  | 48.86330 | -117.35530 | PEND OREILLE | WA | METALINE | ZN PB CU AG CD | 14,000,000 | INTERMITTENT PRODUCER |
| 11 | VAN STONE MINE | M060114 |  | 48.76250 | -117.75528 | STEVENS | WA | NORTHPORT | ZN PB | 4,400,000 | INACTIVE PRODUCER |
| 1 Additional data also provided by Derkey, Joseph, and Lasmanis, 1990; (…) alternate name; na none available |

# Table 4. Small lead-zinc mines and prospects.

| NO. | SITE NAME | MRDS ID. NO. | MAS ID. NO. | LATITUDE | LONGITUDE | COUNTY | STATE | DISTRICT | TONS PRODUCED |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | BELLA MAY MINE | M060151 |  | 48.8481 | -117.4042 | PEND OREILLE | WA | METALINE | 0 |
| 2 | CLIFF PROSPECT | M025857 |  | 48.9578 | -117.3550 | PEND OREILLE | WA | METALINE | 848 |
| 3 | DIAMOND R. CLAIM | M025840 |  | 48.8508 | -117.4208 | PEND OREILLE | WA | METALINE | 200 |
| 4 | DUMONT PROSPECT - LOWER | M025822 |  | 48.9361 | -117.3006 | PEND OREILLE | WA | METALINE | 0 |
| 5 | DUMONT PROSPECT - UPPER | M025823 |  | 48.9375 | -117.2578 | PEND OREILLE | WA | METALINE | 0 |
| 6 | FLUSEY-HOOPALULA | M025815 |  | 48.9356 | -117.3339 | PEND OREILLE | WA | METALINE | 0 |
| 7 | GIANT - FLYING SQUIRREL MINE | M025790 |  | 48.9550 | -117.3533 | PEND OREILLE | WA | METALINE | 0 |
| 8 | HANLEY1 | na | 0530510134 | 48.9861 | -117.3500 | PEND OREILLE | WA | METALINE | 400 |
| 9 | HOAGE1 | M025824 | 0530510135 | 48.9492 | -117.3547 | PEND OREILLE | WA | METALINE | 50 |
| 10 | JIM CREEK MINE | M060167 |  | 48.8111 | -117.5153 | PEND OREILLE | WA | METALINE | 0 |
| 11 | KING TUT1 | na | 0530510052 | 48.9750 | -117.2014 | PEND OREILLE | WA | METALINE | 20 |
| 12 | LAKEVIEW PROPERTY | M025826 |  | 48.9894 | -117.3117 | PEND OREILLE | WA | METALINE | 0 |
| 13 | LEAD HILL MINE | M025832 |  | 48.9708 | -117.1961 | PEND OREILLE | WA | METALINE | 10,850 |
| 14 | LEAD KING PROPERTY | M025816 |  | 48.9378 | -117.3536 | PEND OREILLE | WA | METALINE | 20 |
| 15 | LEAD QUEEN PROSPECT | M025817 |  | 48.9764 | -117.3292 | PEND OREILLE | WA | METALINE | 20 |
| 16 | LEHIGH IRON PITS | M025807 |  | 48.8503 | -117.4153 | PEND OREILLE | WA | METALINE | 800 |
| 17 | LUCKY STRIKE MINE1 | na | 0530650445 | 48.9306 | -117.3306 | PEND OREILLE | WA | METALINE | 99 |
| 18 | METALINE DISTRICT | K002909 |  | 48.8833 | -117.3553 | PEND OREILLE | WA | METALINE | 0 |
| 19 | MM PROSPECT | M025818 |  | 48.9972 | -117.3111 | PEND OREILLE | WA |  | 0 |
| 20 | MOCKINGBIRD PROSPECT | M025820 |  | 48.9311 | -117.3450 | PEND OREILLE | WA |  | 0 |
| 21 | MOHAWK LODE | M025847 |  | 48.8719 | -117.3531 | PEND OREILLE | WA | METALINE | 0 |
| 22 | MORNING AND MAMMOTH MINES | M025821 |  | 48.8778 | -117.3597 | PEND OREILLE | WA | METALINE | 0 |
| 23 | RED TOP MINE | M025842 |  | 48.9958 | -117.3222 | PEND OREILLE | WA | METALINE | 5 |
| 24 | RIVERSIDE MINE | M025833 |  | 48.9186 | -117.3336 | PEND OREILLE | WA | METALINE | 0 |
| 25 | ROBERT E. LEE MINE | M025834 |  | 48.9258 | -117.3408 | PEND OREILLE | WA | METALINE | 0 |
| 26 | STAR1 | na | 0530510086 | 48.9389 | -117.2458 | PEND OREILLE | WA | METALINE | 0 |
| 27 | STERLING2 | na | 0530510154 | 48.8389 | -117.3903 | PEND OREILLE | WA | METALINE | 99 |
| 28 | SULLIVAN CLAIM | M025836 |  | 48.8786 | -117.3747 | PEND OREILLE | WA | METALINE | 99 |
| 29 | TOM CAT PROSPECT | M025828 |  | 48.9894 | -117.3553 | PEND OREILLE | WA | METALINE | 0 |
| 30 | TORRENTIAL - SPHINX PROSPECT | M025829 |  | 48.9811 | -117.3400 | PEND OREILLE | WA | METALINE | 0 |
| 31 | TROYER MINE | M025844 |  | 48.9542 | -117.2236 | PEND OREILLE | WA | METALINE | 0 |
| 32 | TWIN LAKES PROSPECT | M025837 |  | 48.9461 | -117.3494 | PEND OREILLE | WA | METALINE | 0 |
| NO. | SITE NAME | MRDS ID. NO. | MAS ID. NO. | LATITUDE | LONGITUDE | COUNTY | STATE | DISTRICT | TONS PRODUCED |
| 33 | UNCAS PROSPECT | M025830 |  | 48.9406 | -117.2458 | PEND OREILLE | WA | METALINE | 0 |
| 34 | WASHINGTON CLAIM | M025814 |  | 48.8678 | -117.3733 | PEND OREILLE | WA | METALINE | 99 |
| 35 | WEST CONTACT1 | na | 0530510336 | 48.8519 | -117.4156 | PEND OREILLE | WA | METALINE | 0 |
| 36 | WOLF CREEK MINE | M025841 |  | 48.8283 | -117.3814 | PEND OREILLE | WA | METALINE | 0 |
| 37 | YELLOWHEAD MINE1 | na | 0530510311 | 48.8839 | -117.3753 | PEND OREILLE | WA | METALINE | 12,000 |
| 38 | Z CANYON MUTUAL PROSPECT | M025831 |  | 48.9786 | -117.3389 | PEND OREILLE | WA | METALINE | 99 |
| 39 | ANDERSON PROSPECT | W001169 |  | 48.9167 | -117.5911 | STEVENS | WA | NORTHPORT | 0 |
| 40 | AVONDALE-DOME (Tenderfoot)2,3 | na | 0530650221 | 48.6886 | -117.8550 | STEVENS | WA |  | 0 |
| 41 | BECHTOL-THOMPSON-DEEPLAKE | W017880 |  | 48.8661 | -117.5944 | STEVENS | WA | METALINE | 999 |
| 42 | BIG CHIEF MINE | M060173 |  | 48.7047 | -117.8650 | STEVENS | WA | BOSSBURG | 220 |
| 43 | CHLORIDE QUEEN | M060174 |  | 48.6925 | -117.8572 | STEVENS | WA | BOSSBURG | 435 |
| 44 | FARMER MINE | M060120 |  | 48.8494 | -117.6222 | STEVENS | WA | NORTHPORT | 99 |
| 45 | GALENA KNOB1 | na | 0530650251 | 48.6961 | -117.7633 | STEVENS | WA | NORTHPORT | 50 |
| 46 | GREAT WESTERN1 | na | 0530650254 | 48.8686 | -117.6969 | STEVENS | WA | NORTHPORT | 46,000 |
| 47 | IROQUOIS MINE | M060169 |  | 48.9519 | -117.5392 | STEVENS | WA | NORTHPORT | 2,898 |
| 48 | KEYSTONE1 | na | 0530650203 | 48.8814 | -117.5286 | STEVENS | WA | NORTHPORT | 99 |
| 49 | LEAD TRUST1 | na | 0530650267 | 48.8972 | -117.5586 | STEVENS | WA | LEADPOINT | 30,000 |
| 50 | LUCKY FOUR1 | na | 0530650354 | 48.8864 | -117.5514 | STEVENS | WA | NORTHPORT | 9 |
| 51 | MAGMA | D001414 |  | 48.7667 | -117.6403 | STEVENS | WA | NORTHPORT | 5 |
| 52 | MAKI & DOSSER PROSPECTS1 | na | 0530650277 | 48.8450 | -117.6008 | STEVENS | WA | NORTHPORT | 99 |
| 53 | NEGLECTED1 | na | 0530650286 | 48.7217 | -117.8642 | STEVENS | WA | COLVILLE | 99 |
| 54 | NEW LEADVILLE | D000702 |  | 48.7333 | -117.8756 | STEVENS | WA | BOSSBURG | 9 |
| 55 | NORTHPORT | W017867 |  | 48.8811 | -117.7669 | STEVENS | WA | NORTHPORT | 0 |
| 56 | ORE CACHE1 | na | 0530650293 | 48.5486 | -117.7689 | STEVENS | WA | COLVILLE | 9 |
| 57 | R J1 | na | 0530650297 | 48.7367 | -117.8803 | STEVENS | WA | NORTHPORT | 40 |
| 58 | SCAMAN1 | na | 0530650304 | 48.9583 | -117.5492 | STEVENS | WA | NORTHPORT | 65 |
| 59 | SCANDIA MINE | M060172 |  | 48.8761 | -117.7189 | STEVENS | WA | NORTHPORT | 999 |
| 60 | SIERRA ZINC MINE | M060113 |  | 48.7750 | -117.6675 | STEVENS | WA | NORTHPORT | 100,000 |
| 61 | TYEE (Idler, Bechtol)1 | na | 0530650200 | 48.8581 | -117.6192 | STEVENS | WA | NORTHPORT | 300 |
| 62 | UNCLE SAM1 | na | 0530650314 | 48.7381 | -117.8828 | STEVENS | WA | NORTHPORT | 999 |
| Additional data also provided from: 1 Derkey, Joseph, and Lasmanis, 1990 contains additional data; 2 Huntting, 1956 contains additional data; 3 Mills, 1977 contains additional data; na none available |

# Table 5.  Township and range location for sites

| NO. | SITE NAME | MRDS ID. NO. | MAS ID. NO. | LATITUDE | LONGITUDE | TOWNSHIP | RANGE | SECTION | TABLE |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | ADMIRAL | M056000 |  | 48.6600 | -118.7369 | 37N | 32E | 35 | 1 |
| 2 | ADMIRAL CONSOLIDATED | na | 0530650405 | 48.9272 | -117.5758 | 40N | 41E | 36 | 3 |
| 3 | ADVANCE | M056001 |  | 48.6267 | -118.7453 | 36N | 32E | 12, 13 | 1 |
| 4 | ALPINE | M056023 |  | 48.6767 | -118.7578 | 37N | 32E | 27 | 1 |
| 5 | ALVA STOUT | M056072 |  | 48.6494 | -118.7744 | 036N | 032E | 02 | 2 |
| 6 | AMBROSE MINING | na | 0530650884 | 48.9611 | -117.8500 | 040 N | 039 E | 16 | 2 |
| 7 | AMERICAN FLAG | SP00186 |  | 48.7536 | -118.8453 | 38N | 31E | 36 | 1 |
| 8 | ANDERSON PROSPECT | W001169 |  | 48.9167 | -117.5911 | 40N | 41E | 35 | 4 |
| 9 | ANECIA | M056024 |  | 48.6619 | -118.7803 | 37N | 32E | 33 | 1 |
| 10 | AVONDALE-DOME (Tenderfoot) | na | 0530650221 | 48.6886 | -117.8550 | 37N | 39 E | 23 | 4 |
| 11 | BALLARD PLACER | na | 0530470493 | 48.5319 | -119.7450 | 035 N | 025 E | 18 | 2 |
| 12 | BECHTOL-THOMPSON-DEEPLAKE | W017880 |  | 48.8661 | -117.5944 | 39N | 41E | 23 | 4 |
| 13 | BELLA MAY MINE | M060151 |  | 48.8481 | -117.4042 | 39N | 43E | 32 | 4 |
| 14 | BEN HUR | SP00062 |  | 48.6686 | -118.7581 | 37N | 32E | 34, 27 | 1 |
| 15 | BIG CHIEF MINE | M060173 |  | 48.7047 | -117.8650 | 37N | 39E | 14 | 4 |
| 16 | BLACK TAIL (Hope) | SP00063 |  | 48.6633 | -118.7475 | 37N | 32E | 34 | 1 |
| 17 | BLANCE | M056073 |  | 48.6528 | -118.8058 | 036N | 032E | 04 | 2 |
| 18 | BLUE BAR | M056523 |  | 48.1714 | -118.1875 | 031N | 037E | 20 | 2 |
| 19 | BLUE BAR ISLAND | M056062 |  | 48.2000 | -118.2003 | 031N | 036E | 12 | 2 |
| 20 | BLUE BAR ISLAND PLACER | na | 0530190123 | 48.2072 | -118.1994 | 031N | 036 E | 12 | 2 |
| 21 | BLUE BAR PLACER | na | 0530650172 | 48.1700 | -118.1833 | 031 N | 037 E | 20 | 2 |
| 22 | BLUE BUCKET MINE (Kroll) | M025855 |  | 48.8433 | -117.4069 | 39 N | 43 E | 29 | 3 |
| 23 | BODIE | M056027 |  | 48.6606 | -118.7572 | 37N | 32E | 34 | 1 |
| 24 | BODIE GOLD MINE (Northern Gold) | M056791 |  | 48.8158 | -118.9036 | 38N | 31E | 03 | 1 |
| NO. | SITE NAME | MRDS ID. NO. | MAS ID. NO. | LATITUDE | LONGITUDE | TOWNSHIP | RANGE | SECTION | TABLE |
| 25 | BOSSBURG BAR | M056520 |  | 48.7564 | -118.0475 | 038N | 037E | 25 | 2 |
| 26 | BOULDER CR. PLACERS | W007555 |  | 48.6006 | -116.0883 | 061N | 003E | 33 | 2 |
| 27 | BRIDGE CREEK | M056063 |  | 48.2264 | -118.1767 | 032N | 037E | 31, 32 | 2 |
| 28 | BROWNS LAKE PLACER | M025803 |  | 48.4392 | -117.1828 | 034 N | 044 E | 24 | 2 |
| 29 | CASSIMER BAR PLACER | SP00204 |  | 48.0992 | -119.7181 | 030N | 025E | 17 | 2 |
| 30 | CHINA BEND PLACER | na | 0530650173 | 48.8006 | -118.0192 | 038 N | 038 E | 07 | 2 |
| 31 | CHLORIDE QUEEN | M060174 |  | 48.6925 | -117.8572 | 37N | 39E | 23 | 4 |
| 32 | CLIFF PROSPECT | M025857 |  | 48.9578 | -117.3550 | 40N | 43E | 22 | 4 |
| 33 | COLLINS | M056525 |  | 48.3883 | -118.1697 | 033N | 037E | 05 | 2 |
| 34 | CONDON FERRY PLACER | na | 0530470512 | 48.1100 | -119.3111 | 030 N | 028 E | 09 | 2 |
| 35 | COOK | M056029 |  | 48.6372 | -118.7536 | 36N | 32E | 12 | 1 |
| 36 | COPPER CREEK | na | 0160210133 | 48.9803 | -116.1728 | 065 N | 002 E | 14 | 2 |
| 37 | CROUNSE PLACER | SP00211 |  | 48.3997 | -118.8789 | 034N | 031E | 35 | 2 |
| 38 | CUBA LINE PLACER | M056821 |  | 48.9967 | -119.1053 | 040N | 029E | 01 | 2 |
| 39 | DAISY | M056067 |  | 48.3897 | -118.1981 | 033N | 036E | 01 | 2 |
| 40 | DAN MOONEY PLACER | na | 0530470513 | 48.9606 | -119.0406 | 040 N | 030 E | 16 | 2 |
| 41 | DAVEY PLACER | na | 0530470514 | 48.9600 | -119.0408 | 040 N | 030 E | 16 | 2 |
| 42 | DEADMAN CREEK PLACER | na | 0530470497 | 48.9167 | -119.0550 | 040 N | 030 E | 32 | 2 |
| 43 | DEEP CREEK MINE (Gorien Zinc, Northport) | M060115 |  | 48.8639 | -117.7150 | 39N | 41E | 26 | 3 |
| 44 | DIAMOND R. CLAIM | M025840 |  | 48.8508 | -117.4208 | 39N | 43E | 30 | 4 |
| 45 | DORA B PLACER | na | 0530190127 | 48.6472 | -118.8153 | 036 N | 032 E | 04 | 2 |
| 46 | DOVA B | M056074 |  | 48.6528 | -118.8058 | 036N | 032E | 04 | 2 |
| 47 | DUMONT PROSPECT - LOWER | M025822 |  | 48.9361 | -117.3006 | 40N | 43E | 25 | 4 |
| 48 | DUMONT PROSPECT - UPPER | M025823 |  | 48.9375 | -117.2578 | 40N | 44E | 29 | 4 |
| 49 | EAST SAN POIL | M056030 |  | 48.6614 | -118.7572 | 37N | 32E | 34 | 1 |
| 50 | EL CALIPH | M056031,SP00068 |  | 48.6592 | -118.7639 | 37N | 32E | 34 | 1 |
| 51 | ELECTRIC POINT | na | 0530650244 | 48.8828 | -117.5414 | 39N | 42E | 17,18,19,20 | 3 |
| 52 | EVANS PLACER | na | 0530650174 | 48.9350 | -117.7631 | 040 N | 040 E | 30 | 2 |
| 53 | FARMER MINE | M060120 |  | 48.8494 | -117.6222 | 39N | 41E | 34 | 4 |
| NO. | SITE NAME | MRDS ID. NO. | MAS ID. NO. | LATITUDE | LONGITUDE | TOWNSHIP | RANGE | SECTION | TABLE |
| 54 | FIRST THOUGHT MINE | M060170,M056476 |  | 48.8839 | -118.1611 | 39N | 37E | 18 | 1 |
| 55 | FLAG HILL | M056032,SP00069 |  | 48.6522 | -118.7536 | 36N | 32E | 01, 02 | 1 |
| 56 | FLUSEY-HOOPALULA | M025815 |  | 48.9356 | -117.3339 | 40N | 43E | 26 | 4 |
| 57 | FOURTH OF JULY CREEK PLACER | na | 0530470498 | 48.9167 | -119.0558 | 040 N | 030 E | 32 | 2 |
| 58 | GALENA KNOB | na | 0530650251 | 48.6961 | -117.7633 | 37N | 40E | 21 | 4 |
| 59 | GIANT - FLYING SQUIRREL MINE | M025790 |  | 48.9550 | -117.3533 | 40N | 43E | 22 | 4 |
| 60 | GIBSON BAR | M056524 |  | 48.0214 | -118.3919 | 029N | 035E | 10, 15 | 2 |
| 61 | GLADSTONE MINE | M060143 |  | 48.8861 | -117.5417 | 39N | 42E | 17, 18 | 3 |
| 62 | GOLD BAR PLACER | na | 0530470508 | 48.1053 | -119.2664 | 030 N | 028 E | 14 | 2 |
| 63 | GOLD CREEK | M056077 |  | 48.4253 | -118.8450 | 034N, 034N | 031E, 032E | 25, 35, 36, 17, 18 | 2 |
| 64 | GOLDEN EAGLE | M056004 |  | 48.6600 | -118.7369 | 37N | 32E | 35 | 1 |
| 65 | GOOSMUS CREEK PLACER | na | 0530190129 | 48.9631 | -118.5806 | 040 N | 033 E | 13 | 2 |
| 66 | GRANDVIEW MINE | na | 0530510133 | 48.8778 | -117.3575 | 39N | 43E | 14,15,22 | 3 |
| 67 | GREAT WESTERN | na | 0530650254 | 48.8686 | -117.6969 | 39N | 40E | 24 | 4 |
| 68 | HANLEY | na | 0530510134 | 48.9861 | -117.3500 | 40N | 43E | 10 | 4 |
| 69 | HARVEY BAR PLACER | M025804 |  | 48.9439 | -117.3300 | 040 N | 043 E | 26 | 2 |
| 70 | HIDDEN TREASURE | M056495 |  | 48.8739 | -118.1656 | 39N | 37E | 18 | 1 |
| 71 | HOAGE | M025824 | 0530510135 | 48.9492 | -117.3547 | 40N | 43E | 22 | 4 |
| 72 | HOLSTEN | M056522 |  | 48.5000 | -118.1750 | 035N | 037E | 29 | 2 |
| 73 | HOPKINS PLACER | na | 0530470499 | 48.1133 | -119.2311 | 030 N | 029 E | 07 | 2 |
| 74 | IDA MAY | SP00075 |  | 48.6547 | -118.7647 | 37N | 32E | 34 | 1 |
| 75 | INSURGENT | SP00076 |  | 48.6669 | -118.7461 | 37N | 32E | 35 | 1 |
| 76 | IRON MASK | M056033 |  | 48.6561 | -118.7544 | 37N | 32E | 34 | 1 |
| 77 | IRON MOUNTAIN | M056123 |  | 48.5639 | -118.5994 | 35N | 34E | 06 | 1 |
| 78 | IROQUOIS MINE | M060169 |  | 48.9519 | -117.5392 | 40N | 42E | 30 | 4 |
| 79 | JIM BLAINE FRACTION | M056009 |  | 48.6328 | -118.7453 | 36N | 32E | 12 | 1 |
| 80 | JIM CREEK MINE | M060167 |  | 48.8111 | -117.5153 | 38N | 42E | 09 | 4 |
| 81 | JOHNSON PLACER | M056068 |  | 48.2911 | -118.1633 | 032N | 037E | 08 | 2 |
| NO. | SITE NAME | MRDS ID. NO. | MAS ID. NO. | LATITUDE | LONGITUDE | TOWNSHIP | RANGE | SECTION | TABLE |
| 82 | JOSEPHINE MINE (Clark) | M025825 |  | 48.8800 | -117.3711 | 39 N | 43 E | 16 | 3 |
| 83 | K2 MINE | na | 0530190470 | 48.8660 | -118.6680 | 39N | 33E | 20 | 1 |
| 84 | KANGAROO | M056034 |  | 48.6614 | -118.7572 | 37N | 32E | 34 | 1 |
| 85 | KELLER PLACERS | na | 0530190397 | 48.0856 | -118.6903 | 030N | 033E | 20 | 2 |
| 86 | KETTLE | SP00080 |  | 48.8789 | -118.6256 | 39N | 33E | 15 | 1 |
| 87 | KEYSTONE | na | 0530650203 | 48.8814 | -117.5286 | 39N | 42E | 17 | 4 |
| 88 | KING TUT | na | 0530510052 | 48.9750 | -117.2014 | 40N | 44E | 11 | 4 |
| 89 | KNOB HILL MINE-PLANT | na | 0530190084 | 48.6734 | -118.7578 | 37N | 32E | 27 | 1 |
| 90 | LAKEVIEW PROPERTY | M025826 |  | 48.9894 | -117.3117 | 40N | 43E | 1 | 4 |
| 91 | LAST CHANCE | M056010, D001629,SP0008 |  | 48.6658 | -118.7458 | 37N | 32E | 35 | 1 |
| 92 | LAST CHANCE MINE (Jupiter) | M060171 |  | 48.8669 | -117.6992 | 39N | 40E | 24 | 3 |
| 93 | LEAD HILL MINE | M025832 |  | 48.9708 | -117.1961 | 40N | 44E | 14 | 4 |
| 94 | LEAD KING PROPERTY | M025816 |  | 48.9378 | -117.3536 | 40N | 43E | 27 | 4 |
| 95 | LEAD QUEEN PROSPECT | M025817 |  | 48.9764 | -117.3292 | 40N | 43E | 11 | 4 |
| 96 | LEAD TRUST | na | 0530650267 | 48.8972 | -117.5586 | 39N | 42E | 07 | 4 |
| 97 | LEHIGH IRON PITS | M025807 |  | 48.8503 | -117.4153 | 39N | 43E | 30 | 4 |
| 98 | LITTLE COVE | M056036,SP00085 |  | 48.6669 | -118.7533 | 37N | 32E | 34 | 1 |
| 99 | LONE PINE | M056037,SP00086 |  | 48.6653 | -118.7506 | 37N | 32E | 34 | 1 |
| 100 | LUCKY FOUR | na | 0530650354 | 48.8864 | -117.5514 | 39N | 42E | 18 | 4 |
| 101 | LUCKY STRIKE MINE | na | 0530650445 | 48.9306 | -117.3306 | 39N | 42E | 18 | 4 |
| 102 | MAGMA | D001414 |  | 48.7667 | -117.6403 | 38N | 41E | 28 | 4 |
| 103 | MAKI & DOSSER PROSPECTS | na | 0530650277 | 48.8450 | -117.6008 | 39N | 41E | 35 | 4 |
| 104 | MAMMOTH | M056011 |  | 48.6725 | -118.7428 | 37N | 32E | 26 | 1 |
| 105 | MARCUS PLACER | M056518 |  | 48.6656 | -118.0675 | 037N | 038E | 31 | 2 |
| 106 | MARY ANN CREEK PLACER | SP00250 |  | 48.9403 | -119.0517 | 040N | 030E | 30 | 2 |
| 107 | MEADOWS PLACER | na | 0530470501 | 48.6550 | -119.8528 | 037 N | 024 E | 32 | 2 |
| 108 | METALINE DISTRICT | K002909 |  | 48.8833 | -117.3553 | 39N | 43E | 15 | 4 |
| NO. | SITE NAME | MRDS ID. NO. | MAS ID. NO. | LATITUDE | LONGITUDE | TOWNSHIP | RANGE | SECTION | TABLE |
| 109 | METALINE FALLS PROSPECT | M025845 |  | 48.8683 | -117.3667 | 39 N | 43 E | 21 | 3 |
| 110 | MEYERS FALLS | M056515 |  | 48.5936 | -118.0647 | 036N | 038E | 30 | 2 |
| 111 | MM PROSPECT | M025818 |  | 48.9972 | -117.3111 | 40N | 43E | 1 | 4 |
| 112 | MOCKINGBIRD PROSPECT | M025820 |  | 48.9311 | -117.3450 | 40N | 43E | 27 | 4 |
| 113 | MOHAWK LODE | M025847 |  | 48.8719 | -117.3531 | 39N | 43E | 22 | 4 |
| 114 | MORNING AND MAMMOTH MINES | M025821 |  | 48.8778 | -117.3597 | 39N | 43E | 15 | 4 |
| 115 | MOUNTAIN LION | M056039,SP00095 |  | 48.6789 | -118.7686 | 37N | 32E | 27 | 1 |
| 116 | MURRAY PLACER | M056823 |  | 48.2000 | -119.2544 | 030N | 028E | 11 | 2 |
| 117 | NEGLECTED | na | 0530650286 | 48.7217 | -117.8642 | 37N | 39E | 10 | 4 |
| 118 | NESPELEM BAR PLACER | na | 0530470502 | 48.1361 | -119.0539 | 030 N | 030 E | 04 | 2 |
| 119 | NEST EGG | M056501 |  | 48.8481 | -118.1586 | 39N | 37E | 30 | 1 |
| 120 | NEW LEADVILLE | D000702 |  | 48.7333 | -117.8756 | 37N | 39E | 03 | 4 |
| 121 | NIGGER CREEK BAR PLACER | na | 0530650179 | 48.9403 | -117.7656 | 040 N | 040 E | 28 | 2 |
| 122 | NINEMILE | M056070 |  | 48.0158 | -118.3972 | 029N | 035E | 16 | 2 |
| 123 | NINEMILE BAR | M056519 |  | 48.7956 | -118.0036 | 038N | 038E | 15 | 2 |
| 124 | NOBLES PLACER | na | 0530650182 | 48.8472 | -117.9117 | 039 N | 039 E | 29 | 2 |
| 125 | NORTH SAN POIL | SP00096,M056012 |  | 48.6667 | -118.7586 | 37N | 32E | 34 | 1 |
| 126 | NORTHPORT | W017867 |  | 48.8811 | -117.7669 | 39N | 40E | 16 | 4 |
| 127 | NUGGET PLACER | na | 0530470503 | 48.4100 | -118.9039 | 034 N | 031 E | 34 | 2 |
| 128 | OLD HICKORY | SP00097,M056013 |  | 48.6392 | -118.7428 | 36N | 32E | 12 | 1 |
| 129 | ORE CACHE | na | 0530650293 | 48.5486 | -117.7689 | 35N | 40E | 09 | 4 |
| 130 | ORIENT | M056521 |  | 48.8611 | -118.1997 | 039N | 036E | 23 | 2 |
| 131 | ORIENT PLACER | na | 0530650184 | 48.8606 | -118.0722 | 039 N | 037 E | 23 | 2 |
| 132 | PEARL | M056040,SP00100 |  | 48.6669 | -118.7533 | 37N | 32E | 34 | 1 |
| 133 | PEND OREILLE MINE (Josephine, Metaline Metals, Yellowhead, Flusey-Hoopala) | M060153 |  | 48.8633 | -117.3553 | 39N | 43E | 16 | 3 |
| 134 | POINT BAR PLACER | na | 0160210134 | 48.7861 | -116.1533 | 063 N | 002 E | 25 | 2 |
| NO. | SITE NAME | MRDS ID. NO. | MAS ID. NO. | LATITUDE | LONGITUDE | TOWNSHIP | RANGE | SECTION | TABLE |
| 135 | PRINCESS MAUDE (Southern Republic) | SP00102 |  | 48.6347 | -118.7475 | 36N | 32E | 12 | 1 |
| 136 | QUILP (Imperator, Eureka) | M056016 |  | 48.6561 | -118.7475 | 37N | 32E | 35 | 1 |
| 137 | R J | na | 0530650297 | 48.7367 | -117.8803 | 37N | 39E | 03 | 4 |
| 138 | REBATE | M056041 |  | 48.6939 | -118.7542 | 37N | 32E | 22 | 1 |
| 139 | RED TOP MINE | M025842 |  | 48.9958 | -117.3222 | 40N | 43E | 2 | 4 |
| 140 | REED AND ROBERTS PLACER | na | 0530650185 | 48.9544 | -117.7344 | 040 N | 040 E | 20 | 2 |
| 141 | REPUBLIC (Blaine Republic) | SP00104 |  | 48.6375 | -118.7453 | 36N | 32E | 12 | 1 |
| 142 | RICH BAR PLACER | na | 0530470045 | 48.9822 | -119.5364 | 040 N | 026 E | 11 | 2 |
| 143 | RIVERSIDE MINE | M025833 |  | 48.9186 | -117.3336 | 40N | 43E | 35 | 4 |
| 144 | ROBERT E. LEE MINE | M025834 |  | 48.9258 | -117.3408 | 40N | 43E | 35 | 4 |
| 145 | SAN POIL FRACTION | M056043, M056042,SP0010 |  | 48.6669 | -118.7533 | 37N | 32E | 34 | 1 |
| 146 | SANDOZ | M056517 |  | 48.6964 | -118.0164 | 037N | 038E | 22 | 2 |
| 147 | SANDPOIL RIVER, WEST FLA. | M056076 |  | 48.4581 | -118.7719 | 034N | 032E | 09, 10 | 2 |
| 148 | SCAMAN | na | 0530650304 | 48.9583 | -117.5492 | 40N | 42E | 19 | 4 |
| 149 | SCANDIA MINE | M060172 |  | 48.8761 | -117.7189 | 39N | 40E | 23 | 4 |
| 150 | SCHIERDING PLACER | M025805 |  | 48.9881 | -117.3447 | 040 N | 043 E | 14 | 2 |
| 151 | SCHULTZ PLACER | na | 0530510304 | 48.8597 | -117.4111 | 039 N | 043 E | 19 | 2 |
| 152 | SEATTLE | M056044,SP00107 |  | 48.6642 | -118.7669 | 37N | 32E | 34 | 1 |
| 153 | SHERIDAN (Phil Sheridan) | SP00283 |  | 48.7786 | -118.8547 | 38N | 31E | 24 | 1 |
| 154 | SHOTWELL PLACER | SP00284 |  | 48.0342 | -119.6828 | 029N | 025E | 10 | 2 |
| 155 | SIERRA ZINC MINE | M060113 |  | 48.7750 | -117.6675 | 38N | 41E | 19 | 4 |
| 156 | SILVER BELL | SP00285 |  | 48.7597 | -118.8383 | 38N | 31E | 28 | 1 |
| 157 | SIMILKAMEEN FALLS PLACER | na | 0530470505 | 48.9703 | -119.5017 | 040 N | 026 E | 13 | 2 |
| 158 | SIMILKAMEEN PLACERS | na | 0530470506 | 48.9806 | -119.5492 | 040 N | 026 E | 10 | 2 |
| 159 | SINGER PLACER | SP00111 |  | 48.9961 | -118.5308 | 040N | 034E | 4,5 | 2 |
| 160 | SNOWSTORM | M056045 |  | 48.6614 | -118.7572 | 37N | 32E | 34 | 1 |
| 161 | SOUTH PENN | SP00112,M056046 |  | 48.6903 | -118.7558 | 37N | 32E | 22 | 1 |
| 162 | STANDARD AND EMMA | M056018 |  | 48.6306 | -118.7461 | 36N | 32E | 12 | 1 |
| NO. | SITE NAME | MRDS ID. NO. | MAS ID. NO. | LATITUDE | LONGITUDE | TOWNSHIP | RANGE | SECTION | TABLE |
| 163 | STAR | na | 0530510086 | 48.9389 | -117.2458 | 40N | 44E | 28, 29 | 4 |
| 164 | STERLING | na | 0530510154 | 48.8389 | -117.3903 | 39N | 43E | 32 | 4 |
| 165 | STRANGER CREEK | M056069 |  | 48.3083 | -118.1478 | 033N | 037E | 34 | 2 |
| 166 | STRAY DOG PLACER | M056065 |  | 48.2053 | -118.1992 | 031N | 036E | 12 | 2 |
| 167 | SULLIVAN CLAIM | M025836 |  | 48.8786 | -117.3747 | 39N | 43E | 16 | 4 |
| 168 | SULLIVAN CREEK PLACER | na | 0530510305 | 48.8383 | -117.2653 | 039 N | 044 E | 32 | 2 |
| 169 | SURPRISE | SP00114,M056019 |  | 48.6608 | -118.7492 | 37N | 32E | 34 | 1 |
| 170 | THOMPSON | M056066 |  | 48.2189 | -118.1861 | 031N | 037E | 06 | 2 |
| 171 | TOM CAT PROSPECT | M025828 |  | 48.9894 | -117.3553 | 40N | 43E | 3 | 4 |
| 172 | TOM THUMB | SP00117,M056047 |  | 48.6961 | -118.7572 | 37N | 32E | 15, 22 | 1 |
| 173 | TORRENTIAL - SPHINX PROSPECT | M025829 |  | 48.9811 | -117.3400 | 40N | 43E | 11 | 4 |
| 174 | TRADE DOLLAR | M056048,SP00118 |  | 48.6733 | -118.7508 | 37N | 32E | 27 | 1 |
| 175 | TROYER MINE | M025844 |  | 48.9542 | -117.2236 | 40N | 44E | 22 | 4 |
| 176 | TURTLE RAPIDS PLACER | na | 0530190177 | 48.1783 | -118.2500 | 031 N | 036 E | 15 | 2 |
| 177 | TWIN LAKES PROSPECT | M025837 |  | 48.9461 | -117.3494 | 40N | 43E | 22 | 4 |
| 178 | TYEE (Idler, Bechtol) | na | 0530650200 | 48.8581 | -117.6192 | 39N | 41E | 27 | 4 |
| 179 | UNCAS PROSPECT | M025830 |  | 48.9406 | -117.2458 | 40N | 44E | 28 | 4 |
| 180 | UNCLE SAM | na | 0530650314 | 48.7381 | -117.8828 | 37N | 39E | 03 | 4 |
| 181 | V FRACTION | M056021 |  | 48.6658 | -118.7458 | 37N | 32E | 35 | 1 |
| 182 | VALBUSH BAR | M056516 |  | 48.7000 | -118.0206 | 037N | 038E | 16, 21 | 2 |
| 183 | VAN STONE MINE | M060114 |  | 48.7625 | -117.7553 | 38N | 40E | 33, 34 | 3 |
| 184 | WALKER PLACER | SP00299 |  | 48.9689 | -119.1144 | 040N | 029E | 13, 14 | 2 |
| 185 | WASHINGTON CLAIM | M025814 |  | 48.8678 | -117.3733 | 39N | 43E | 21 | 4 |
| 186 | WEST CONTACT | na | 0530510336 | 48.8519 | -117.4156 | 39N | 43E | 30 | 4 |
| 187 | WOLF CREEK MINE | M025841 |  | 48.8283 | -117.3814 | 38N | 43E | 4 | 4 |
| 188 | YELLOWHEAD MINE | na | 0530510311 | 48.8839 | -117.3753 | 39N | 43E | 16 | 4 |
| 189 | Z CANYON MUTUAL PROSPECT | M025831 |  | 48.9786 | -117.3389 | 40N | 43E | 11 | 4 |
| 190 | ZALLA M | M056126,SP00122 |  | 48.7667 | -118.8314 | 38N | 32E | 30 | 1 |

na not available

### Appendix I. Metadata

Identification_Information:

Citation:

Citation_Information:

Originator: David Boleneus

Publication_Date: 1999

Title:

Geologic datasets for weights-of-evidence analysis in

northeast Washington--2. Mineral databases

Edition: version 1.0

Geospatial_Data_Presentation_Form:

spreadsheet files in Microsoft Excel 97

format

Series_Information:

Series_Name: Open-File Report 99-384

Issue_Identification:

of99-384.xls

Publication_Information:

Publication_Place: Spokane WA

Publisher: U.S. Geological Survey

Online_Linkage: http://wrgis.wr.usgs.gov/open-file/of99-384

Description:

Abstract:

Digital mineral databases are necessary to carry out

weights-of-evidence modeling of mineral resources for

epithermal gold and carbonate-hosted lead-zinc deposits

in northeast Washington.  This report describes four

digital data sets (presented as separate sheets in

tables.xls, an Excel97-format file) used for this

modeling: 1) training sites for epithermal gold,

2) placer gold sites, 3) training sites for

carbonate-hosted lead-zinc, and 4) small lead-zinc

mines.

Purpose:

This dataset was developed to provide mineral resource data

for northeast Washington for use in future spatial

analysis by a variety of users.

This database is not meant to be used or displayed at any

scale larger than 1:24,000 (e.g., 1:12,000 or 1:2,000).

Supplemental_Information:

The Excel97 file, of9-384.xls, contains five (5) sheets

corresponding to the five tables listed in the Open-File

Report 99-384 text.

Table 1 in the text corresponds to the sheet titled

'Trainsites_epith'

Table 2 in the text corresponds to the sheet titled

'Placer_gold_sites'

Table 3 in the text corresponds to the sheet titled

'Trainsites_PbZn'

Table 4 in the text corresponds to the sheet titled

'Small_PbZn_Mines'

Table 5 in the text corresponds to the sheet titled

'Township_location'

Time_Period_of_Content:

Time_Period_Information:

Single_Date/Time:

Calendar_Date: 1998

Currentness_Reference:

Date that original data was extracted from the USGS MRDS

and MAS/MILS databases.

Status:

Progress: Complete

Maintenance_and_Update_Frequency: No updates are planned.

Spatial_Domain:

Bounding_Coordinates:

West_Bounding_Coordinate: -121.0

East_Bounding_Coordinate: -117.0

North_Bounding_Coordinate: 49.0

South_Bounding_Coordinate: 47.75

Keywords:

Theme:

Theme_Keyword_Thesaurus: none

Theme_Keyword: mineral resources

Theme_Keyword: lead

Theme_Keyword: zinc

Theme_Keyword: gold

Theme_Keyword: silver

Theme_Keyword: training sites

Theme_Keyword: placers

Theme_Keyword: mines

Theme_Keyword: prospects

Theme_Keyword: occurrences

Place:

Place_Keyword_Thesaurus: none

Place_Keyword: Washington

Place_Keyword: northeast Washington

Place_Keyword: Ferry County

Place_Keyword: Okanogan County

Place_Keyword: Pend Oreille County

Place_Keyword: Stevens County

Place_Keyword: Colville National Forest

Place_Keyword: Okanogan National Forest

Place_Keyword: Sandpoint

Place_Keyword: Okanogan

Place_Keyword: Pacific Northwest

Place_Keyword: USA

Access_Constraints: none

Use_Constraints:

This digital database is not meant to be used or

displayed at any scale larger than 1:24,000 (e.g.,

1:12,000 or 1:2,000).

Any hardcopies utilizing these data sets shall clearly

indicate their source.  If the user has modified the data

in any way they are obligated to describe the types of

modifications they have performed on the hardcopy

map/report.  User specifically agrees not to misrepresent

these data sets, nor to imply that changes they made were

approved by the U.S. Geological Survey.

Data_Set_Credit:

David Boleneus compiled the data in digital format from

the USGS MRDS and MAS/MILS databases. Compilation included

removal of duplicate records, verifying

latitude-longitude location and classifying sites as type of

mineral deposit as described in the text. The accuracy of the data

in the MRDS and MAS/MILS was relied upon as correct and was

not field checked. Other sources were used to verify the correctness

of the data to the extent possible.

Point_of_Contact:

Contact_Information:

Contact_Person_Primary:

Contact_Person: David Boleneus

Contact_Organization: U.S. Geological Survey

Contact_Position: geologist

Contact_Address:

Address_Type: mailing and physical address

Address: 904 W. Riverside Ave., Rm. 202

City: Spokane

State_or_Province: WA

Postal_Code: 99201

Country: USA

Contact_Voice_Telephone: 1-509-368-3100

Contact_Facsimile_Telephone: 1-509-368-3199

Contact_Electronic_Mail_Address: dboleneu@usgs.gov

Native_Data_Set_Environment: Microsoft Excel97 for Windows95

Data_Quality_Information:

Attribute_Accuracy:

Attribute_Accuracy_Report:

Attribute accuracy was verified by manual comparison of

MRDS record printouts with MAS/MILS record printouts to the

extent possible.

Logical_Consistency_Report:

Point data is given in latitude and longitude (decimal

degrees).

Completeness_Report:

This digital dataset was produced from unpublished MRDS

and MAS/MILS databases and is not considered to be a

unique mineral resource dataset for the area.

Positional_Accuracy:

Horizontal_Positional_Accuracy:

Horizontal_Positional_Accuracy_Report:

The horizontal positional accuracy for the digital data

was not checked.  The point locations given by the MRDS

and MAS/MILS databases were not modified and were compared to

determine the most accurate location.

Lineage:

Source_Information:

Source_Citation:

Citation_Information:

Originator: U.S. Bureau of Mines/U.S. Geological Survey

Publication_Date: unpublished

Title:

MAS/MILS (Minerals Availability System/Mineral Industry

Location System)

Geospatial_Data_Presentation_Form: digital database

Type_of_Source_Media: digital files

Source_Time_Period_of_Content:

Time_Period_Information:

Single_Date/Time:

Calendar_Date: 1998

Source_Currentness_Reference:

Date that the digital data was extracted from the

MAS/MILS database for this report.

Source_Citation_Abbreviation:

U.S. Bureau of Mines MAS/MILS CD-ROM (USBM,1995)

Source_Contribution: Locations and attributes of sites.

Source_Information:

Source_Citation:

Citation_Information:

Originator: U.S. Geological Survey

Publication_Date: unpublished

Title: MRDS (Mineral Resources Data System)

Geospatial_Data_Presentation_Form: digital database

Type_of_Source_Media: digital files

Source_Time_Period_of_Content:

Time_Period_Information:

Single_Date/Time:

Calendar_Date: 1998

Source_Currentness_Reference:

Date that the digital data was extracted from the

MRDS database for this report.

Source_Citation_Abbreviation:

USGS MRDS

Process_Step:

Process_Description:

The data was originally provided in two formats.

The USGS MRDS was provided in an ACCESS database and was exported

to EXCEL97 for purposes in this report 1998. The USBM MAS/MILS was provided

in dBase format by Douglas Causey of USGS and was exported to EXCEL97 for

purposes of this report in 1998.

Spatial_Reference_Information:

Horizontal_Coordinate_System_Definition:

Geographic:

Geographic_Coordinate_Units: Decimal degrees

Entity_and_Attribute_Information:

Overview_Description:

Entity_and_Attribute_Overview:

The data consists of five worksheets in the Excel97 file,

"tables.xls".

Definitions of attributes in Excel97 file, of99-384.xls:

The following eight field names/items/column headers are

common to Tables 1, 2, 3, 4, and 5:

1. No.-- Record number in table

2. Site name -- Name used in MRDS or MAS/MILS databases

3. MRDS ID NO. -- MRDS identifier number, 1st

or 2nd digit are letters, followed by numbers

4. MAS ID NO.-- MAS identifier number, a 10-digit number

5. Latitude -- Latitude location of the site as cited in the database

in decimal degrees. If the latitude was not cited, then it was

calculated from the township, range and section using the Wefald script.

6. Longitude--Longitude location of the site as cited in the database

in decimal degrees.  If the longitue was not cited, then it was

calculated from the township, range and section using the Wefald script.

7. County -- County in which site/deposit is located.

8. State -- State in which site/deposit is located.

Other field names/items/column headers used in

tables.xls:

9. Commodities present -- Elements/mineral commodities

present

10. USGS Model -- Name and number of USGS mineral

deposit-type model (Berger, 1992; Briskey, 1992;

Mosier, Sato, Page, Singer, and Berger, 1992;

Mosier, Singer, and Berger, 1992)

11. Production size -- Qualifier of quantity of ore

produced

12. Development status -- Status of exploration or

development at the site

13. District -- Mining district name

14. Tons produced -- Short tons of all historical ore

produced (estimated from Derkey, Joseph and Lasmanis,

1990)

15. Township -- Township and direction (N=north)

16. Range -- Range and direction (E=east)

17. Section -- Section(s)

18. Table -- item in Table 5 indicating in which table

(either Table 1, 2, 3, or 4) the site is described.

Table 1. Training sites for epithermal gold model

File name: of99-384.xls; sheet name: Trainsites_epith

The training sites consist of a collection of sites

(either mines, prospects or occurrences) selected from

MRDS or MAS/MILS database because of their epithermal

gold-like characteristics. Sites were qualified for the

epithermal gold model if they met the selection criteria

below for any of the USGS models for Au-Ag hot spring, 25a

(Berger, 1992), Creede epithermal veins, 25b (Mosier et

al., 1992), or Comstock epithermal veins, 25c (Mosier,

Singer and Berger, 1992). Minimum selection criteria are

a) Sites are spatially associated with Eocene volcanic or

hypabyssal rocks and b) Sites contain gold in quartz veins

or disseminations.

Table 2. Placer gold sites

File name: of99-384.xls; sheet name: Placer_gold_sites

Placer gold sites -- Indicates locations of mines or

prospects of placer gold exploration or development.

Selection criteria for the 67 sites obtained from MRDS

and MAS/MILS were a)"gold" is the primary commodity and

b) "placer" was indicated by the name, deposit type, or

modifier of commodity.  See definition of attributes from

Table 1.

Table 3. Training sites for carbonate-hosted lead-zinc

model

File name: of99-384.xls; sheetname: Trainsites_PbZn

The training sites consist of sites (mines, prospects or

occurrences) selected from MRDS or MAS/MILS, because they

exhibit characteristics of explored or developed

carbonate-hosted lead-zinc deposits. Sites were qualified

as carbonate-hosted lead-zinc deposits if they met the

selection criteria below for the USGS model for

carbonate-hosted lead-zinc deposits (Briskey, 1992).

Minimum criteria by which the 11 mines were selected are

a) lead and zinc are the primary commodities; b) the

deposit is either strataform, pipe-like, or breccia in

form or replacement in nature; c) the deposit occurs

within strata of either the Maitlen Phyllite of Cambrian

age, the Metaline Formation of Cambro-Ordovician age, or

the Ledbetter Slate of Ordovician age; and d) the mine

has produced more than 100,000 tons of ore.

Table 4. Small lead-zinc mines and prospects

File name: of99-384.xls; sheet name: Small_PbZn_Mines

Smaller deposits described as carbonate-hosted lead-zinc

deposits are those where no ore was produced or had total

production up to 100,000 tons. These smaller deposits

were selected using the selection criteria used for

training sites of carbonate-hosted lead-zinc deposits

(Briskey, 1992) with the exception that the deposits from

this group were selected because they had no commercial

production or produced 100,000 tons or less of ore.

Table 5. Township and range location for sites

File name: of99-384.xls; sheet name: Township_location

The township-range-section and latitude-longitude locations

in this table are taken from the databases. For those not

available, the Wefald script was used to calculate from

available data. Some sites were checked against those listed

by the Washington Department of Natural Resources

(Derkey, R.E., Joseph, N.L., and Lasmanis, R., 1990)

Entity_and_Attribute_Detail_Citation:

See Open-File Report 99-384 text, available on-line at

http://wrgis.wr.usgs.gov/open-file/of99-384/of99-384.html

Distribution_Information:

Distributor:

Contact_Information:

Contact_Organization_Primary:

Contact_Organization:

U.S. Geological Survey

Information Services

Contact_Address:

Address_Type: mailing and physical address

Address: Open-File Reports, Box 25286

City: Denver

State_or_Province: CO

Postal_Code: 80225

Country: USA

Contact_Voice_Telephone: 1-303-202-4200

Contact_Facsimile_Telephone: 1-303-202-4693

Distribution_Information:

Distributor:

Contact_Information:

Contact_Organization_Primary:

Contact_Organization:

U.S. Geological Survey

Earth Science Information Office

Contact_Address:

Address_Type: mailing and physical address

Address: 904 West Riverside, Rm. 135

City: Spokane

State_or_Province: WA

Postal_Code: 99201

Country: USA

Contact_Voice_Telephone: 1-509-368-3130

Contact_Facsimile_Telephone: 1-509-368-3194

Contact_Electronic_Mail_Address: esnfic@mailmcan1.wr.usgs.gov

Hours_of_Service: 8:00 a.m. - 4:30 p.m., Pacific time zone

Distribution_Information:

Distributor:

Contact_Information:

Contact_Person_Primary:

Contact_Person: David Boleneus

Contact_Organization: U.S. Geological Survey

Contact_Position: geologist

Contact_Address:

Address_Type: mailing and physical address

Address: 904 West Riverside, Rm. 202

City: Spokane

State_or_Province: WA

Postal_Code: 99201

Country: USA

Contact_Voice_Telephone: 1-509-368-3100

Contact_Facsimile_Telephone: 1-509-368-3199

Contact_Electronic_Mail_Address: dboleneu@usgs.gov

Distribution_Liability:

The U.S. Geological Survey (USGS) provides these geographic

data "as is." The USGS makes no guarantee or warranty

concerning the accuracy of information contained in the

geographic data.  The USGS further makes no warranties,

either expressed or implied as to any other matter

whatsoever, including, without limitation, the condition of

the product, or its fitness for any particular purpose. The

burden for determining fitness for use lies entirely with

the user.  Although these data have been processed

successfully on computers at the USGS, no warranty,

expressed or implied, is made by the USGS regarding the use

of these data on any other system, nor does the fact of

distribution constitute or imply any such warranty.

In no event shall the USGS have any liability whatsoever

for payment of any consequential, incidental, indirect,

special, or tort damages of any kind, including, but not

limited to, any loss of profits arising out of use of or

reliance on the geographic data or arising out of the

delivery, installation, operation, or support by USGS.

Metadata_Reference_Information:

Metadata_Date: 19990915

Metadata_Review_Date: 19990517

Metadata_Contact:

Contact_Information:

Contact_Organization_Primary:

Contact_Organization: U.S. Geological Survey

Contact_Person: David Boleneus

Contact_Position: geologist

Contact_Address:

Address_Type: mailing and physical address

Address: 904 West Riverside Avenue, Rm. 202

City: Spokane

State_or_Province: WA

Postal_Code: 99201

Country: USA

Contact_Voice_Telephone: 1-509-368-3110

Contact_Facsimile_Telephone: 1-509-368-3199

Contact_Electronic_Mail_Address: dboleneu@usgs.gov

Metadata_Standard_Name: FGDC Content Standards for Digital Geospatial Metadata

Metadata_Standard_Version: FGDC-STD-001-1998

Metadata_Access_Constraints: none

Metadata_Use_Constraints:

These data are not meant to be used or displayed at any

scale larger than 1:24,000 (e.g., 1:12,000 or 1:6,000).

# Footnotes

Spokane, Washington