January 11, 2002

Notes on dd and Odd Sized Disks

By Dr. James Lyle

cftt@nist.gov

National Institute of Standards and Technology (NIST)

I’ve been asked to comment on digests 105-107 since I’m directly involved in testing dd and I may be able to add a little bit about this. These digests contain good questions; most of them should be answered by our test report when it comes out. Feel free to contact us with suggestions and comments. We are not working alone; we have regular discussions with a number of forensic practitioners. These discussions often lead to productive exchanges for both parties. If anyone has time, please try to duplicate these results and let us know what happens.

# Disks with an odd number of sectors

## Question

The message that started the dd thread was:

Subject: Re: dd missing sectors - never in my experience

I have been thinking about how to get dd to miss sectors and I am now really confused.  The claim is that dd misses the last sector on disks with odd numbers of sectors, but I can't find any disks that have odd numbers of sectors and have not been able to reproduce these results. We need specifics on how to reproduce this. Does anyone have a concrete example?

## Response

The claim actually is that dd (GNU fileutils) 4.0.36 running on Red Hat Linux Version 7.1 misses the last sector from a source device that has an odd number of sectors. A source device may be either a disk drive (e.g., /dev/hda or /dev/sdc) or a partition (e.g., /dev/hdb3 or /dev/sda6).

It is no surprise that finding a disk with an odd number of sectors is hard. The odds are against finding an IDE (ATA) drive with an odd number of sectors. Since both the number of heads and cylinders would need to be odd. However a partition with an odd number of sectors is easy to create if the number of heads is odd. Some drives allow selection of the number of heads (either 15 or 16) by jumper. Some SCSI disks do have an odd number of sectors, e.g., QUANTUM ATLAS10K2-TY092J 17938985 or a SEAGATE ST39204LC 17921835 Sectors. A visit to vendor web sites would likely turn up more.

Here is an extract from three of our test cases. DI(Linux)-06 is a partition copy of a partition that just happened to have an odd number of sectors. DI(Linux)-08 is a copy of a SCSI disk to an identical model (the selected disk again just happens to have an odd number of sectors). DI(Linux)-09 is a copy to a smaller destination drive that is odd sized. The last sector is dropped for each case. The last sector of the destination is not changed from the contents present before dd is executed.

Test case DI(Linux)-06 copies a partition (entry #9 from the partition table). Note that the partition is on an IBM-DTLA-307020 ATA disk with an even number of sectors (40188960), but since the disk has 255 heads (logically not physically) the partition has an odd number of sectors (9430155). The last sector was not copied.

The dd command line was:

dd if=/dev/hda3 of=/dev/hdb1 bs=1b

Test case DI(Linux)-08 copies an entire disk to another disk of the same model. The last sector is not copied. (QUANTUM ATLAS10K2-TY092J 17938985 sectors)

Test case DI(Linux)-09 copies part of a disk (QUANTUM ATLAS10K2-TY092J 17938985 sectors) to another disk of a smaller size (SEAGATE ST39204LC 17921835 Sectors). dd outputs a message that the destination is too small, but stops the copy one sector short, i.e., dd could have copied one more sector to the destination drive but it did not do so. The destination disk has an odd number of sectors.

(The test report will contain formats similar to the following for each test case.)

| Product Name: | dd (GNU fileutils) 4.0.36 |
| --- | --- |
| Test ID: | DI(Linux)-06 |
| Case Summary: | Copy a LINUX IDE source disk to a LINUX IDE destination disk and the source contains a LINUX partition where the source disk is larger than the destination |
| Tester Name: | JRL |
| Test Date: | Thu Aug 30 18:06:47 2001 |
| PC: | Cadfael |
| Disks: | Source: DOS Drive 80 Physical Label F5 Linux device hda3 Destination: DOS Drive 81 Physical Label A6 Linux device hdb1 Boot/Image media: Physical Label CD F5 is an IBM-DTLA-307020 40188960 Sectors, IDE A6 is a WDC WD200BB-00AUA1 39102336 Sectors, IDE CD is a SEAGATE ST336705LC 71687370 Sectors, SCSI Jaz disk with Support software, scripts PC DOS 6.3 Boot floppy |
| Source disk setup: | Dual boot Linux/Windows Me with EXT2 & Fat16 Disk: F5 N Start LBA Length Start C/H/S End C/H/S boot Partition type 1 P 000000063 001236942 0000/001/01 0076/254/63 Boot 06 Fat16 2 X 002249100 007181055 0140/000/01 0586/254/63 05 extended 3 S 000000063 000208782 0140/001/01 0152/254/63 83 Linux 4 x 000208845 000144585 0153/000/01 0161/254/63 05 extended 5 S 000000063 000144522 0153/001/01 0161/254/63 06 Fat16 6 x 004450005 000192780 0417/000/01 0428/254/63 05 extended 7 S 000000063 000192717 0417/001/01 0428/254/63 16 other 9 P 009430155 006152895 0587/000/01 0969/254/63 83 Linux 10 P 039760875 000417690 1023/000/01 1023/254/63 82 Linux swap |
| Expected Results: | src compares qualified equal to dst, src is truncated on dst truncation is logged Source disk unchanged |
| Actual Results: | src compares qualified equal to dst, src is truncated on dst truncation is logged except for 1 sector not copied to destination Source disk is unchanged |
| Log File Highlights: | Sectors Compared 5943987 Sectors Differ 1 Diffs range: 5943986 Source (6152895) has 208908 more sectors than destination (5943987) Hash after test: 83A0002816BBF089F8BE33C41C92C3B5A0F42A54 dd: writing /dev/hdb1: No space left on device |

| Product Name: | dd (GNU fileutils) 4.0.36 |
| --- | --- |
| Test ID: | DI(Linux)-08 |
| Case Summary: | Copy a LINUX SCSI source disk to a LINUX SCSI destination disk where the source disk is the same size as the destination |
| Disks: | Source: DOS Drive 80 Physical Label E3 Linux device sda Destination: DOS Drive 81 Physical Label E0 Linux device sdb Boot/Image media: Physical Label AD E3 is a QUANTUM ATLAS10K2-TY092J 17938985 Sectors, SCSI E0 is a QUANTUM ATLAS10K2-TY092J 17938985 Sectors, SCSI AD is a Maxtor53073H4 60030432 Sectors, IDE Jaz disk with Support software, scripts PC DOS 6.3 Boot floppy |
| Source disk setup: | Dual boot Linux/Windows Me with EXT2 & Fat16 Disk: E3 N Start LBA Length Start C/H/S End C/H/S boot Partition type 1 P 000000063 001236942 0000/001/01 0076/254/63 Boot 06 Fat16 2 X 002249100 007181055 0140/000/01 0586/254/63 05 extended 3 S 000000063 000208782 0140/001/01 0152/254/63 83 Linux 4 x 000208845 000144585 0153/000/01 0161/254/63 05 extended 5 S 000000063 000144522 0153/001/01 0161/254/63 06 Fat16 6 x 004450005 000192780 0417/000/01 0428/254/63 05 extended 7 S 000000063 000192717 0417/001/01 0428/254/63 16 other 9 P 009430155 006152895 0587/000/01 0969/254/63 83 Linux 10 P 017510850 000417690 1023/000/01 1023/254/63 82 Linux swap |
| Execute: | dd if=/dev/sda of=/dev/sdb bs=1b |
| Expected Results: | src compares equal to dst Source disk unchanged |
| Actual Results: | src compares equal to dst except for 1 sector not copied to destination Source disk is unchanged |
| Log File Highlights: | Sectors Compared 17938985 Sectors Differ 1 Diffs range 17938984 |

| Product Name: | dd (GNU fileutils) 4.0.36 |
| --- | --- |
| Test ID: | DI(Linux)-09 |
| Case Summary: | Copy a LINUX SCSI source disk to a LINUX SCSI destination disk where the source disk is larger than the destination |
| Disks: | Source: DOS Drive 80 Physical Label E4 Linux device sda Destination: DOS Drive 81 Physical Label EA Linux device sdb Boot/Image media: Physical Label AE E4 is a QUANTUM ATLAS10K2-TY092J 17938985 Sectors, SCSI EA is a SEAGATE ST39204LC 17921835 Sectors, SCSI AE is a Maxtor53073H4 60030432 Sectors, IDE Jaz disk with Support software, scripts PC DOS 6.3 Boot floppy |
| Source disk setup: | Windows 2000 with NTFS & Fat32 Disk: E4 N Start LBA Length Start C/H/S End C/H/S boot Partition type 1 P 000000063 006152832 0000/001/01 0382/254/63 Boot 0B Fat32 2 X 008193150 009735390 0510/000/01 1023/254/63 0F extended 4 x 002056320 001237005 0638/000/01 0714/254/63 05 extended 5 S 000000063 001236942 0638/001/01 0714/254/63 07 NTFS 6 x 005349645 001638630 0843/000/01 0944/254/63 05 extended 7 S 000000063 001638567 0843/001/01 0944/254/63 17 other 8 x 008498385 001237005 1023/000/01 1023/254/63 05 extended 9 S 000000063 001236942 1023/001/01 1023/254/63 1B other |
| Execute: | dd if=/dev/sda of=/dev/sdb bs=1b |
| Expected Results: | src compares qualified equal to dst, src is truncated on dst truncation is logged Source disk unchanged |
| Actual Results: | src compares qualified equal to dst, src is truncated on dst truncation is logged except for 1 sector not copied to destination Source disk is unchanged |
| Log File Highlights: | Sectors Compared 17921835 Sectors Differ 1 Diffs range 17921834 Source (17938985) has 17150 more sectors than destination (17921835) dd: writing /dev/sdb: No space left on device |

NOTE: “Source compares qualified equal to destination” in the expected results box denotes that data blocks were copied correctly and that allowed changes, such as would be found in the partition table information and boot records, were expected.

# Source of the problem

As some folks have commented, the problem is not in dd. Looking at the dd source code is a red herring; the source of the problem is in a software layer under dd, i.e., kernel or driver. This missing sector issue has implications beyond dd. For example, compute an md5 message digest with a DOS based tool and compare the results with md5sum running under Linux. The results are based on different data (1 more sector is used by the DOS tool) and yield different values.

## Scope of the dd problem

A simple experiment to check if a unix-like OS sees all of a disk is to run the following command and note the results:

dd if=/dev/disk_in_question of=/dev/null bs=1b

For dd (GNU fileutils) 4.0.36  on Red Hat Linux Version 7.1 we get the following:

QUANTUM ATLAS10K2-TY092J (17938985):

17938984+0 Records in

17938984+0 Records out

SEAGATE ST39204LC 17921835 Sectors

17921834+0 Records in

17921834+0 Records out

For Mandrake Linux Version 7.2 dd (GNU fileutils) 4.0.p we get the same result:

QUANTUM ATLAS10K2-TY092J (17938985):

17938984+0 Records in

17938984+0 Records out

SEAGATE ST39204LC 17921835 Sectors

17921834+0 Records in

17921834+0 Records out

But for FreeBSD 4.4-Release#0 we get (for the Atlas):

17938985+0 Records in

17938985+0 Records out

9184760320 bytes transferred in 1094.73 Secs

Bottom line: The some operating systems or underlying drivers skip that last sector, but others see it all.

## Suggested dd problem workaround

If you see dd miss that last sector, we recommend that you use another tool to either capture the last sector. Otherwise, print the contents in hex and ASCII.

Note that if the disk is on a Linux system, then that sector is unlikely to contain any data since Linux does not allow the sector to be used. If the disk comes from a DOS/WIN system with a FAT file system, it is still unlikely to be used in any cluster (the last cluster would have to be an exact fit with nothing left over). In fact, it usually would be outside any partition. I would try to capture that last sector no matter how unlikely it is to contain data, just to be complete.

## Driver vs parameter

An additional comment on the discussion was the following:

>> as far as disks with odd numbers of sectors, it also stands to

>> reason, that if you are using any of the linux programs that use the

>> same disk drivers as dd, you will not be able to see disks with that

>> odd sector because it will not realize it is there.

>

> If this is the correct assessment.  this is not a driver issue –

> it is a parameter issue.

The problem is in a layer under dd. Call it driver or kernel, or whatever, but this is not a dd parameter issue. If there were a way to advise the lower level to modify its behavior, then dd could get that last sector. Is there a way to do that?

# Reporting our results

The dd report will be out soon. Once it has been released, the National Institute of Justice (NIJ) will publish it on a JUSTNET web site. The NIST CFTT web site will point to it and provide other supporting information.