# Laser wire neutralization simulations at 1000 MeV

R. E. Shafer   8/4/01

For a given rms H- beam width, the width of the laser wire can be set to a range of values. For a 200-mJ Nd:YAG laser, if the laser beam is too narrow, saturation (depletion of the H- beam) limits the percentage yield of  neutralized beam. Because of the low signal to noise ratio, maximizing the neutralization yield is important. However, if the laser beam is too wide, the measured profile of the H- beam is significantly wider than the actual H- profile.

Linac beam simulations show that the expected rms width of the H- beam is about 1.7-mm at 1 GeV, for both x and y, midway between the two quadrupoles in the quad doublet. An H- energy of 1 GeV was selected for this analysis, because the photo-neutralization yield scales roughly as 1/, and is lowest at 1GeV.

The following simulations are carried out with the simulation program LASERY4A.exe, based on the laser wire paper in the 1998 Beam Instrumentation Workshop (SLAC, 1998). The simulation includes saturation effects, and assumes Gaussian shapes for both the laser and beam pulse transverse profiles. A rectangular (not Gaussian) longitudinal pulse shape is used for the laser pulse length. When saturation is important, the number of neutralized H- atoms will vary, depending on the longitudinal pulse shape used. The photo-neutralization cross section is probably accurate to about +/- 10%. In the simulations, the H- beam is assumed to be an unmodulated (i.e., dc), 38 mA beam. All the simulations are “single-pass” of the laser beam through the H- beam, at 90( to the beam in the lab reference frame.

The following table shows the percentage yield and measured width, for a 200-mJ Q-switched laser wire and a 2.0-mm-rms wide, 1 000-MeV H- beam.

Laser wire	percentage	measured 	ratio to

# rms width	yield	width	actual width

0.1 mm	7.4%	2.003 mm	1.002

0.2	11.1	2.012	1.006

0.3	13.0	2.026	1.01

0.4	14.2	2.045	1.02

0.5	14.9	2.069	1.03

0.6	15.3	2.097	1.05

0.7	15.5	2.129	1.06

0.8	15.6	2.166	1.08

0.9	15.6	2.206	1.10

1.0	15.5	2.251	1.12

Figures 1, 2, and 3 show the profiles for the incident beam (blue), the neutralized beam (red), the un-neutralized H- beam (green), and the measured fit (magenta points), for 0.1 mm, 0.5 mm, and 1.0 mm laser wires. Specific parameters for the simulation are shown in the figures. Saturation is very apparent for the 0.1-mm laser wire. The measured width using the 1.0-mm laser wire is clearly a poor fit to the actual width. From the table above, the maximum yield occurs with a laser wire width of about 0.8 mm. Based on these simulations, the optimum laser wire width for a beam profile diagnostic is about 0.5 mm.

The following table shows the expected neutralization yield vs. beam energy in the SRF linac, using a 200 mJ laser wire with a 0.5-mm rms width on a 2-mm-wide H- beam..

Beam energy		Yield

200 MeV		24.1%

500		19.5

1000		14.9

The simulations were done at an H- current of 38 mA, the expected peak current for normal operation. For a 0.5-mm wide laser wire, the total yield of neutral H0’s is about 4.25E8, corresponding to about 70 pC. If a 1:50 beam current transformer (BCT) is used, the charge across the secondary termination is about 1.5 pC.

Figures 4 and 5 show the simulation results for the laser wire displaced by 2 mm and 4 mm. The yields are about 8.7% and 2.0% respectively.

The percentage yield is roughly inversely proportional to the laser pulse length, as seen in the following table. However, the number of neutralized atoms is nearly independent of laser pulse length, as expected. The reduction in the total number of neutralized atoms for shorter pulse lengths is due to saturation effects.

Pulse	Number of	Percentage

length	neutralized atoms	yield

12 ns	4.25E8	14.9%

24	4.83E8	8.5

48	5.17E8	4.5

Although the total number of neutralized atoms is slightly larger with the longer pulse lengths, the shorter pulses with the higher % yield may be easier to discriminate from background. This depends on the detection method, however, because higher required bandwidths are often accompanied with higher noise.

Fig. 1. 0.1-mm rms width, 12-ns long laser beam. Maximum % neutralization yield is 7.4%. Peak saturation is 98.2%. The profile fit is very good.

Fig. 2.  Same as above, except laser beam 0.5 mm wide.  Maximum % neutralization yield is 14.9%. Peak saturation is 55.2%. The profile fit is acceptable.

Fig. 3.  Same as Figures 1 and 2, except laser wire is 1.0-mm wide. Maximum % neutralization yield is 15.5%. Note that the measured width is 13% wider than the actual width of the H- beam. The profile fit (magenta points) is not very good.

Fig. 4.  Simulation of the 0.5-mm laser wire offset by 2 mm (1 ). The yield is about 8.7%.

Fig. 5.  Simulation of the 0.5-mm laser wire offset by 4 mm (2 ). The yield is about 2%.