# Modification of Antiproton Source Transfer Lines and their Optics Correction

##### Valeri Lebedev

April 12, 2001

### Motivation

Currently we experience multiple problems with the antiproton source transfer lines. This document presents a proposal for correction of the problems. That should yield better stability and reproducibility of the optics, an increase of the antiproton production and a decrease of emittance dilution in the course of beam transfers. The document also outlines the optics tuning procedure and requirements for optics measurements.

### 1. Modifications of AP1 transfer line (Transport of the 120 GeV beam from Main injector to the antiproton production target)

1.1. Line status and requirements

Currently, we can focus the beam on the antiproton production target to the rms beam sizes x ( 130 m, y ( 220 m and the vertical beam size growing with increase of beam energy spread. The optimum beam size is in the range of 100-150 m; and it is desirable to decrease the vertical beam size but it is more crucial to prevent any significant beam size increase or beam scraping with increase of the beam energy spread.

The aim of the transfer line optics changes is to build the optics with the achromatic beam transport and effective regulation of rms beam sizes at the target in the range of 100-150 m. For the normalized 95% beam emittance of 20 mm mrad and the base line 95% momentum spread of 2.4(10-4 it requires the beta-function at the target to be in the range of 38 - 86 cm and residual dispersion to be below 20 cm. It is expected that with the slip stacking the energy spread will grow in three times which will require a better dispersion correction.

1.2. Optics

The beta-functions and dispersions of the proposed optics are presented in Figure 1. As one can see the beam transport in horizontal plane is achromatic (the horizontal dispersion and its derivative are equal to zero at the target). Unfortunately, it is impossible to achieve achromatic beam transport for vertical plane without changes of beam line magnets, i.e. adding new or moving existing magnets. It originates from improper locations of two groups of major vertical benders, F11AH - F11BH and 17LAM1 – 4. Instead of required cancellation their effects are added up due to inappropriate vertical betatron phase advance between them. To archive dispersion cancellation one would need to increase the phase advance from about to about 2. It is impossible to do with small number of quads between these groups. Therefore we adopted a choice where only vertical dispersion is nullified on the target. The base line design presented in Figure 1 has beta-function on the target equal to 68 cm. That corresponds to rms beam size of 130 m for both horizontal and vertical plane. For the base line optics we adopted that the vertical dispersion is equal to 10 cm at the target. The dispersion is sufficiently small so that the synchrotron beam size, Dy = Dyp/p = 24 m, for p/p=2.4(10-4 is 5 times smaller than the betatron size and contributes only 4% into the vertical beam size. This is a compromise between minimum dispersion at the target and in the final focus quads. Figure 2 depicts the beta-functions and dispersion for the case when vertical dispersion is nullified on the target. As one can see this increases the vertical dispersion in two times for the final focus quadrupoles and also significantly increases the beta-functions in Q201 and Q202 quads.

Figure 1. The beta-functions and dispersions for the base line optics from the main injector extraction to the target; x* = y* = 68 cm, Dy* = 10 cm, Dx* = 0.

Figure 2. The beta-functions and dispersions for the case of zero vertical dispersion on the target from the main injector extraction to the target; x* = y* = 68 cm, Dy* = Dx* = 0.

The maximum of beta-function in the final focus quads is equal to 500 m. That is about two times smaller than for currently used optics. This decrease is achieved due to reconnection of quadrupoles to power supplies. Figure 3 presents a comparison of optimized behavior of beta-functions for the current and proposed powering of quads. Currently, the final focus quadrupoles are connected in pairs so that two nearby 3 m quads represent a single 6 m quadrupole. That yields that the quads are powered to less than half of their maximum allowed strength, which unnecessary amplifies maximum beta-functions. Proposed reconnection of quadrupoles uses quads at their maximum strength, which yields better stability of the final focus optics due to smaller beta-functions, and reduced effects of residual magnetic field and ripple of power

Figure 3. The comparison of optimized beta-functions near the final focus for new (left) and current (right) powering of AP1 line quads; x* = y* = 68 cm, longitudinal coordinate is inversed and starts at the target.

supplies. Table 1 presents comparison of focusing strength of optimized optics for current and new powering scheme of quads.

If necessary the beta-functions and beam sizes at the target can be decreased. Figure 4 presents the beta-functions and dispersions for the case of the rms beam sizes equal to 80 m. In this case both betatron and synchrotron beam sizes grow in the final focus quads and a use of such scheme requires clearing current aperture limitations at the end of AP1 line.

Better matching of the proposed optics in comparison with currently used optics allowed us to get smaller beam sizes through the entire beam line and therefore even in a few places with tight aperture of only 36 mm there is sufficiently large room for orbit correction. Figure 5 shows the beam sizes through the line for the base line optics presented in Figure 1 and decreased spot size optics presented in Figure 4. Table 2 presents aperture limitations for AP1 line.

Figure 4. The beta-functions and dispersions for the case of decreased spot size on the target from the main injector extraction to the target; x* = y* = 26 cm, Dy* = Dx* = 0. x =x = 80 m.

Table 2. Aperture limitations for AP1 line

| Magnet | Serial # | Length | Horizontal aperture | Vertical aperture | Comments |
| --- | --- | --- | --- | --- | --- |
|  |  | meters | millimeters | millimeters |  |
| AP1 |  |  |  |  |  |
| F17B3 |  | 6.096 | 73 | >100 | B-3 dipole |
| CMAG1 | C102 | 3.011 | 37 | 76 |  |
| CMAG2 | C103 | 3.011 | 37 | 76 |  |
| PHT0 | 2 | 0.506 | 95 | 48 |  |
| PB1 | MH203-6 | 3.048 | 80 | 35 | EPB |
| PB2 | MH203-23 | 3.048 | 80 | 35 | EPB |
| PBR1 | MH203-2 | 3.048 | 37 | 50 | EPB, rolled 41 degrees |
| PBR2 | MH203-8 | 3.048 | 37 | 50 | EPB, rolled 41 degrees |
| PQ1 | 3Q120-07 | 3.048 | 73 | 73 | QQK |
| PVT1A | SY-trim | 0.506 | 48 | 95 |  |
| PVT1 | SY-trim | 0.890 | 48 | 95 |  |
| PQ2 | 3Q120-10 | 3.048 | 73 | 73 | QQK |
| PBR3 |  | 3.048 | 47 | 47 | EPB, rolled 45 degrees |
| PB3 |  | 3.048 | 80 | 35 | EPB |
| PB4 |  | 3.048 | 80 | 35 | EPB |
| PB5 |  | 3.048 | 80 | 35 | EPB |
| PQ3 | 3Q120-5 | 3.048 | 73 | 73 | QQQ |
| PQ4 | 3Q120-1 | 3.048 | 73 | 73 | QQQ |
| PQ5A | 3Q120-2 | 3.048 | 73 | 73 | QQQ |
| PQ5B | 3Q120-3 | 3.048 | 73 | 73 | QQQ |
| PHT5 | SY-trim | 0.890 | 85 | 35 |  |
| PBV1 | MH201-8 | 3.048 | 35 | 80 | EPB |
| PBV2 | MH203-5 | 3.048 | 35 | 80 | EPB |
| PQ6A | 3Q120-13 | 3.048 | 73 | 73 | QQK |
| PQ6B | 3Q120-1 | 3.048 | 73 | 73 | QQK |
| PQ7A | 3Q120-9 | 3.048 | 73 | 73 | QQK |
| PQ7B | 3Q120-5 | 3.048 | 73 | 73 | QQK |
| PHT7 | SY-trim | 0.890 | 85 | 35 |  |
| PQ8A | 3Q120-6 | 3.048 | 73 | 73 | QQK |
| PQ8B | 3Q120-4 | 3.048 | 73 | 73 | QQK |
| PVT8 | SY-trim | 0.890 | 35 | 85 |  |
| PQ9A | 3Q120-2 | 3.048 | 73 | 73 | QQK |
| PQ9B | 3Q120-11 | 3.048 | 73 | 73 | QQK |

1.3. Powering of quadrupoles

Proposed optics does not require any change in powering quads of P1 and P2 lines. All optics adjustments are achieved by changing currents of existing supplies. Table 1 presents comparison of focusing strength of optimized optics for current and new powering scheme of quads.

power supplies. But new optics requires reconnection of quads for AP1 line. All AP1 quads are of the same 3Q120 type with 3 inch aperture and 120 inch length. Table 3 presents required gradients and currents for all quads of 120 GeV beam transport. Quads of AP1 line shown for proposed new powering. It requires seven instead of currently used nine 500 A power supplies. Five quads Q204, Q2051, Q2052, Q2061 and Q2062 have zero gradients and are not necessary for optics adjustments. Quads Q204, Q2061 and Q2062 have to be demagnetized and disconnected from power supplies. Quads Q2051 and Q2052 will be used for 8 GeV antiproton transport discussed below. They can be dismounted later when new optics arrangement will prove that the beam transport is reliable and does not require further improvements.

Figure 5. The beam envelopes from the main injector extraction to the target for the base line optics of Figure 1 (top) and decreased beam size optics of Figure 4 (bottom) for the 95% normalized emittance of 20  mm mrad and the 95% energy spread of  6(10-4.

1.5. Optics tuning procedure

### Table 3. Gradients and currents of quadrupoles for 120 GeV operation

| Power supply name | Power supply current [A] | Shunt name | Shunt current [A] | Quad name | Quad type | L[cm] | Aperture, 2a, [cm] | G[kG/cm] |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  | Q522 |  | 213.36 |  | 1.64076 |
| P1 Line |  |  |  |  |  |  |  |  |
| IQ701 | 259.9 |  |  | Q701 |  | 304.8 |  | -1.3041 |
| IQ702 | 194.9 |  |  | Q702 |  | 304.8 |  | 0.986002 |
| IQ703 | 2593 |  |  | Q703, Q705, Q707, Q709 |  | 213.36 |  | -1.48547 |
|  |  |  |  | Q704, Q706, Q708 |  | 213.36 |  | 1.48547 |
| IQ710 | 193 |  |  | Q710 |  | 304.8 |  | 0.962833 |
| IQ711 | 169 |  |  | Q711 |  | 304.8 |  | -0.84891 |
| IQ712 | 162 |  |  | Q712A |  | 304.8 |  | 0.842468 |
|  |  |  |  | Q712B |  | 152.4 |  | 0.837106 |
| IQ713 | 252 |  |  | Q713A |  | 304.8 |  | -1.27656 |
|  |  |  |  | Q713B |  | 152.4 |  | -1.26843 |
| IQ714 | 236 |  |  | Q714 |  | 304.8 |  | 1.16987 |
| P2 Line |  |  |  |  |  |  |  |  |
| IQF11A | 365.2 |  |  | QF11A |  | 152.4 |  | -1.74096 |
| IQF11B | 237.6 |  |  | QF11B |  | 304.8 |  | 1.17051 |
| IQF12 | 1655.9 |  |  | QF12, QF14, QF16 QF13, QF15, QF17 |  | 213.36 213.36 |  | -0.94907 0.949072 |
| AP1 line |  |  |  |  |  |  |  |  |
| IQ201 | 162.4 |  |  | Q201 | 3Q120 | 304.8 | 7.62 | -0.74732 |
| IQ202 | 217.5 |  |  | Q202 | 3Q120 | 304.8 | 7.62 | 1.00094 |
| IQ203 | 281.6 |  |  | Q203 | 3Q120 | 304.8 | 7.62 | -1.29605 |
| IQ2071 | 308.3 |  |  | Q2071 | 3Q120 | 304.8 | 7.62 | 1.41872 |
| IQ2072 | 409.0 |  |  | Q2072 | 3Q120 | 304.8 | 7.62 | -1.88189 |
| IQ208 | 478.1 |  |  | Q1081, Q1092 | 3Q120 | 304.8 | 7.62 | 2.2 |
| IQ209 | 365.1 |  |  | Q1082, Q1091 | 3Q120 | 304.8 | 7.62 | -1.68 |

### 2. Modifications of AP3  - P1 transfer line (Transport of the 8 GeV antiproton beam from Accumulator to Main injector)

2.1. Line status and requirements

Currently, the line for transfer antiprotons from the Accumulator to the Main injector has two problems. First, the amplitude of beta-function in many quads is too large making the line oversensitive to quadrupole and dipole errors. Second, the vertical dispersion is not matched to the main injector causing the emittance dilution in the process of beam transfers. The aim of the transfer line optics changes is to build the optics with matched dispersions and beta-functions in both vertical and horizontal planes. The maximum beta-functions and beam overfocusing should be minimized.

2.2. Optics

The beta-functions and dispersions of the proposed optics are presented in Figure 6 and the beam envelopes in Figure 7. The dispersions and beta-functions for both vertical and horizontal planes are matched to the rings. The horizontal dispersion is nullified in part of AP1 line. This feature is useful for optics tuning and measurements. The vertical dispersion leakage from

Figure 6. The beta-functions and dispersions for antiproton transport from the accumulator to the main injector.

Figure 7. The beam envelopes for antiproton transport from the accumulator to the main injector for the 95% normalized emittance of 20  mm mrad and the 95% energy spread of  2.5(10-4.

### Table 4. Gradients and currents of quadrupoles for 8 GeV antiproton transport

| Power supply name | Power supply current [A] | Shunt name | Shunt current [A] | Quad name | Quad Type | L[cm] | Aperture, 2a, [cm] | G[kG/cm] |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| AP3 line |  |  |  |  |  |  |  |  |
| IQ901 | 104 |  |  | Q901 | SQC | 70.1 |  | -0.43142 |
| IQ902 | 80 |  |  | Q902 | SQD | 82.8 |  | 0.331517 |
| IQ903 | 201.4 |  |  | Q903A Q903B, Q906 | SQD SQD | 82.8 82.8 |  | -0.83213 0.832134 |
|  |  |  |  | Q904 | SQB | 64.01 |  | 0 |
| IQ905 | 252.2 |  |  | Q905 | SQC | 70.1 |  | -1.03996 |
| IQ907 | 36.1 |  |  | Q907 | SQE | 131.17 |  | -0.15329 |
| IQ908 | 179.1 |  |  | Q908, Q912 | SQA | 45.72 |  | 0.74504 |
| IQ909 | 114.7 |  |  | Q909, Q913 Q916 Q918 | SQA SQC SQA | 45.72 70.1 45.72 |  | -0.47679 -0.47577 -0.47679 |
| IQ910 | 126.1 |  |  | Q910 Q927 | SQA SQC | 45.72 70.1 |  | 0.52422 0.523138 |
| IQ911 | 89.5 |  |  | Q911, Q920 | SQA | 45.72 |  | -0.37232 |
|  |  |  |  | Q914 | SQA | 45.72 |  | 0 |
| IQ915 | 154.7 |  |  | Q915 | SQC | 70.1 |  | 0.642237 |
| IQ917 | 244.1 |  |  | Q917 | SQA | 45.72 |  | 1.01184 |
| IQ919 | 70.5 |  |  | Q919 Q921 | SQB SQA | 64.01 45.72 |  | 0.293867 0.29404 |
| IQ922 | 59 |  |  | Q922 Q926 Q928 | SQA SQB SQD | 45.72 64.01 82.8 |  | -0.24691 -0.24676 -0.24582 |
| IQ923 | 98 |  |  | Q923, Q925 | SQA | 45.72 |  | 0.407484 |
| IQ924 | 165 |  |  | Q924 | SQA | 45.72 |  | -0.68636 |
| AP1 line |  |  |  |  |  |  |  |  |
| IQ2072 | 18.7 |  |  | Q2072 | 3Q120 | 304.8 |  | -0.09311 |
| IQ2071 | 21.4 |  |  | Q2071 | 3Q120 | 304.8 |  | 0.105616 |
|  |  |  |  | Q2062, Q2061 | 3Q120 | 304.8 |  | 0 |
| IQ205 | 21.7 |  |  | Q2052 Q2051 | 3Q120 3Q120 | 304.8 304.8 |  | -0.10701 0.107006 |
|  |  |  |  | Q204 | 3Q120 | 304.8 |  | 0 |
| IQ203 | 5.12 |  |  | Q203 | 3Q120 | 304.8 |  | -0.03025 |
| IQ202 | 9.6 |  |  | Q202 | 3Q120 | 304.8 |  | 0.050979 |
| IQ201 | 7.21 |  |  | Q201 | 3Q120 | 304.8 |  | -0.03992 |
| P2 line |  |  |  |  |  |  |  |  |
| IQF12K | 111 |  |  | QF17 QF16 QF15 QF14 QF13 QF12 |  | 213.36 213.36 213.36 213.36 213.36 213.36 |  | 0.063616 -0.06362 0.063616 -0.06362 0.063616 -0.06362 |
| IQF11BK | 17.01 |  |  | QF11B |  | 304.8 |  | 0.083825 |
| IQF11AK | 25.68 |  |  | QF11A |  | 152.4 |  | -0.12241 |
| P1 line |  |  |  |  |  |  |  |  |
| IQ714K | 18.47 |  |  | Q714 |  | 304.8 |  | 0.091577 |
| IQ713K | 17.58 |  |  | Q713B Q713A |  | 152.4 304.8 |  | -0.08849 -0.08906 |
| IQ712K | 13.11 |  |  | Q712B Q712A |  | 152.4 304.8 |  | 0.067741 0.068175 |
| IQ711K | 14.93 |  |  | Q711 |  | 304.8 |  | -0.07503 |
| IQ710K | 14.51 |  |  | Q710 |  | 304.8 |  | 0.07239 |
| IQ703K | 187.55 |  |  | Q709, Q707 Q708, Q706 Q705, Q703 Q704 |  | 213.36 213.36 213.36 213.36 |  | -0.10745 0.107445 -0.10745 0.107445 |
| IQ702K | 13.46 |  |  | Q702 |  | 304.8 |  | 0.068074 |
| IQ701K | 19.63 |  |  | Q701 |  | 304.8 |  | -0.09851 |

vertical bends located at the beginning of AP1 line is used for cancellation of the vertical dispersion excited in P2 line so that the vertical dispersion and its derivative would be equal to zero at the line end.

2.3. Powering of quadrupoles

Table 3 presents parameters of quadrupoles for new optics. It does not require any change in powering quads of P1 and P2 lines but involves reconnection of quadrupoles in AP1 and AP3 lines. New arrangement requires the same number of quadrupole power supplies for AP3 line and 6 versus current 7 power supplies for AP1 line. Quad arrangements in AP1 line for 8 GeV antiproton transport is consistent with 120 GeV proton transport to the target.

The same as for proton transport five quads of AP1 line (Q204, Q2061 and Q2062) have zero gradients and are not necessary for optics adjustments. Additionally, two quadrupoles of AP3 line (Q904 and Q914) are not required. All these quadrupoles have to be demagnetized and disconnected from power supplies. They can be dismounted later when new optics arrangement will prove that the beam transport is reliable and does not require further improvements.

2.3. Optics tuning procedure

### 3. Field maps of quadrupoles

We have sufficiently good magnetic measurement data for SQ type quadrupoles. Figure 8 presents data and their fit for SQA, SQB, SQC, SQD and SQE quadrupoles. As one can see short quads are saturated faster than the long ones. The measured data can be fitted well with fourth order polynomials. Three sets of polynomial coefficients are used to fit five quad families. Lengths of SQB and SQC, and SQD and SQE are close and the same polynomials can be used for each pair. For rising hysteresis curve the polynomials can be written in the following form:

For descending hysteresis curve they are

Here the quadrupole current is in amps and the integrated gradient is in kG. As one can see polynomials fit data with accuracy better than data accuracy and an error estimate of the fit related to maximum strength at 400 A is about 3(10-3.

Figure 8. Measured dependence of effective quad gradient  on quadrupole current and their polynomial fits for SQ series of quadrupoles: SQA - red (, Leff=45.27 cm;  SQB - blue +, Leff=63.34 cm, SQC - magenta (, Leff=69.25 cm; SQD - green (, Leff=81.67 cm, SQE -brown (, Leff=129.55 cm. For better resolution the linear dependence with k=4.197 G/cm/A has been subtracted from the data.

# Text boxes

Table 1. Comparison of quad gradients for optimized optics with current and proposed powering of quads

| Name | G[kG/cm] |
| --- | --- |
|  | Current connection | Proposed connection |
| Q1092 | 1.00579 | 2.2 |
| Q1091 | 1.00579 | -1.68 |
| Q1082 | -0.86316 | -1.68 |
| Q1081 | -0.86316 | 2.2 |
| Q2072 | 0.763774 | -1.88189 |
| Q2071 | 0.763774 | 1.41872 |
| Q2062 | -0.54292 | 0 |
| Q2061 | -0.54292 | 0 |
| Q2052 | 0 | 0 |
| Q2051 | 0 | 0 |
| Q204 | 0 | 0 |
| Q203 | -1.29605 | -1.29605 |
| Q202 | 1.00094 | 1.00094 |
| Q201 | -0.74732 | -0.74732 |