Survey Plans

Submittal Form

## Approvals

## _______________________________________________         ____________

George Ison									Date

Ship Operations Contract Project Officer, Ship

Safety Officer

## _______________________________________________         ____________

Glenn Warren								Date

Environmental Monitoring and Indicators Team Leader

## _______________________________________________         ____________

Paul Horvatin								Date

Monitoring Indicators and Reporting Branch Chief

# IFYLE-2005

# June Diel Cruise

Dates:		June 15, 2005 – June 22, 2005

Vessel:	Lake Guardian

#### Ports:

Embark:  		Cleveland Port Authority:   0900 EDT June 15 (depart for 1st site @ 1100 EDT)

Disembarkment:    	Cleveland Port Authority:   1330 EDT June 22

Ports of Call:	 None

## Cruise Participants:

PIs (indicate project PI if PI will not be on board)                                             Status      Cabin    Citizen

| (F) Joann Cavaletto (Chief Scientist) (for H. Vanderploeg) | PI |  | US |
| --- | --- | --- | --- |
| (F) Samantha Bickel (for H. Vanderploeg) | student |  | US |
| (F) Kate Bailey (for S. Ludsin) | student |  | US |
| (F) Amanda Poste (for R. Smith) | support |  | CAN |
| (M) Greg Silsbe (for R. Smith) | PI |  | CAN |
| (M) Jesse Kipp (for S. Ruberg) | student |  | US |
| (M) Darryl Hondorp (for S. Ludsin) | PI |  | US |

Purpose of Cruise:

To determine the vertical distribution of fish, zooplankton, and primary producers in central Lake Erie relative to physical habitat features (e.g., oxygen, temperature).

Objectives:

- Monitor 6 stations in central Lake Erie for 24 hours each using fish acoustics, a plankton survey system (PSS), zooplankton net and pump sampling, and a fast repitation-rate fluorometer (FRRP).

- Coordinate sampling with fish trawling efforts conducted by the R/V Laurentian, which will be operating in tandem with the Lake Guardian.

Environmental questions asked by the project:

-How does low dissolved oxygen influence phytoplankton, zooplankton, and fish distributions, feeding behavior, condition, and production?

# Survey Plan

## Chemical background information:

Sugar formalin (10%)

Any others? (Greg?)

#### Core measurements for surveys:

| Variable | Responsible Group | Technique |
| --- | --- | --- |
| Depth profiles for temp, O2, transmissometry, fluorometry | Lake support staff | EBT, Seabird fluorometer |
| Secchi depths Zooplankton net (whole water column) Discrete water/zooplankton Phytoplankton condition, productivity Major phytoplankton pigment group composition PSS Acoustics | Lake Guardian support staff Cavaletto/Kipp/Bickel/Lake Guardian support staff Cavaletto/Kipp/Bickel/Lake Guardian staff Silsbe/Poste/Lake Guardian staff Silsbe/Poste/Lake Guardian staff Cavaletto/Kipp/Bickel/Lake Guardian staff Bailey/Hondorp | Secchi Disk 64um net Diaphragm pump Fast Repetition Rate Fluorometer (FRRF) Spectral fluorometer (Fluororobe) Tow-yo PSS Towed acoustics (~1 m below surface) |

## Equipment to be brought and used on Deck:

## (Equipment marked with an * will be provided by the individual PI)

- *Diaphragm pump: for pumping water at discrete depths (compressed air required)

- Rosette sampler (multiple)

- Go Flow bottles EBT, DO, Conductivity, pH, Transmissometer

- *Plankton survey system (Cavaletto)

- *Acoustics system (Bailey/Hondorp)

- *64 µm zooplankton net  (Cavaletto)

- *Fast Repetition Rate Fluorometer (Silsbe)

- *Spectral fluoroprobe

- *Par Sensor

- Secchi disk

## Mooring Requirements:

No mooring experiments are currently planned for this cruise.

## Diving Operations:

No diving operations are currently planned for this cruise.

## Special Operating Requirements:

Our experimental site is actually a 3 nautical mile transect with sampling occurring continuously along the transect, and at both ends (~1000 m outside the transect line).  We will sample each 3 nautical mile transect for 24 hr, with sampling blocks divided into the following intervals (EDT): 0100-0500; 0500-0900; 0900-1300; 1300-1700; 1700-2100; 2100-0100. We would like to complete six 24-hour experiments at six different sites in the central basin.  Ideally, ship speed will be 4 knots, when on a transect.

Sampling Protocol for Diel Experiment:

At each station, we would like to do the following:

- With ship not moving (or only drifting), deploy PSS (from A-frame on stern to depth of 4 m) and acoustics (side from crane to depth of 1 m) at ~1000 m before first station (i.e., outside transect line).

- Tow PSS and acoustics along a 3 nautical mile transect (ideally at ~4 knots, 5 knots max). Transect should take about 45-50 min. at 4 knots.  End at coordinates on the opposite end of transect.

  - Please notify PSS and acoustics operators when 10, 5, 1 and then 0 minutes from end of transect

  - Continue steaming at 4 knots through the end of the transect until PSS is parked at a depth of 4 m

  - Once up at 4 m, we will notify captain, who then can turn around and/or “park” ship ~1000 m from the end of the transect (i.e., park ship outside of transect line)

PSS and acoustics equipment can remain in the water during the entire 24 hr sampling period, but should be pulled up during the steam to the next station.

- Once at a stop and waters are settled, conduct a CTD cast to determine vertical structure.

- Use a rosette sampler to collect water at different depths (2-4 depths)

- Two zooplankton net tows, full water column

- Pump for zooplankton at no more than 4 depths (to be determined from CTD cast).

- Deploy an ‘optics rig’ by means of vertical casts.  The rig will include a Fast Repetition Rate Fluorometer (FRRF), a spectral fluorometer (Fluororobe), and a PAR meter.  The instrument will be deployed at a rate of 4-5 m/min from surface to 1 m above bottom depth and back up at the same rate.

Table 1: Requirement for water at each station and depth sampled

| Parameter | Volume of water in ml |
| --- | --- |
|  | Reps | Vol./Rep | Total |
| Chlorophyll-a | 3 | 250 | 750 |
| Particle absorption (PABs) | 1 | 1500 | 3000 |
| Preserved Phytoplankton | 1 | 100 | 100 |
| TOTAL | 3850 |

- Sit and wait until next cycle to start, per times above.

- Repeat the cycle until 6 cycles have been conducted at the site (24 hr).

- During each cycle in the daytime, we need an extra 30 minutes with acoustics over the side (at surface, but not towed) to calibrate the instrument.  This can only occur in calm conditions.

- Move to next station and repeat, until 6 stations are completed.

In theory, time will permit all stations to be sampled by morning of June 22.  Below is the prioritizations of stations to be sampled (i.e., 1st stations are more important than last stations).

1.  FW-FE (note, this station is near a real-time buoy)

2.  BW-BE (note, this station is near a mooring)

3.  DW-DE (note, this station is near a mooring)

4.  CW-CE

5.  AW-AE

6.  GW-GE

See Table 2 for sampling station coordinates and Table 3 and Figure 1 for the project cruise track.

# Lab Space Requests (if known):

Cavaletto (for Vanderploeg):   	Back Lab for PSS computer and joy stick; freezer space

Filtering space for chlorophyll samples

Bailey (for Ludsin):			Back Lab area for acoustics computer

Silsbe (for Smith):			Filtering space (4 ft by 2 ft); fridge and freezer space

Cavaletto:  				Lab space for water filtration

# Master Sample Sites and Location:

Table 2. Mast list of stations.  The coordinates on the right correspond to those used in Table 2 and the mast Excel spreadsheet.

|  | West | East |  | West | East |
| --- | --- | --- | --- | --- | --- |
| Station | Lat | Long | Lat | Long | Station | Lat | Long | Lat | Long |
| F | 4145.70 | 8145.52 | 4145.70 | 8141.50 | F | 41.7617 | -81.7587 | 41.7617 | -81.6917 |
| B | 4157.95 | 8143.05 | 4157.95 | 8139.00 | B | 41.9658 | -81.7175 | 41.9658 | -81.6500 |
| D | 4212.00 | 8052.65 | 4212.00 | 8048.60 | D | 42.2000 | -80.8775 | 42.2000 | -80.8100 |
| G | 4219.00 | 8113.06 | 4219.00 | 8109.00 | G | 42.3167 | -81.2177 | 42.3167 | -81.1500 |
| C | 4210.50 | 8120.05 | 4210.50 | 8116.00 | C | 42.1750 | -81.3342 | 42.1750 | -81.2667 |
| A | 4159.40 | 8207.54 | 4159.40 | 8203.50 | A | 41.9900 | -82.1257 | 41.9900 | -82.0583 |

# Projected Cruise Plan

Table 3.  Sampling coordinates and estimated sampling times for June 15-22 Lake Guardian diel cruise.  I assumed that sampling occurred at 4 knots while on station, and that the ship steamed at 8 knots during transit between stations.

| Station 1 (FW-FE) |
| --- |
| Cycle | Station name | Lat | Long | Date | ETA | Site Time (hr) | Tasks | Transit time (hr)* | Transit dist. (nm) |
|  | Cleve. Port Auth. | 41.549 | -81.704 | 15-Jun | 11:00 |  | Depart Cleve. Port Authority |  | 0 |
| Transit | FW | 41.762 | -81.759 | 15-Jun | 12:37 |  | Arrive 1st station | 1.62 | 13.0 |
| Start 1 | FW | 41.762 | -81.759 | 15-Jun | 13:01 | 0.4 | PSS/acoustics | 0.00 | 0.0 |
| End 1 | FE | 41.762 | -81.692 | 15-Jun | 17:00 | 3.25 | CTD/rosette ZP pump/net Secchi FRRF/fluoroprobe | 0.74 | 3.0 |
| Start 2 | FE | 41.762 | -81.692 | 15-Jun | 17:00 | 0 | PSS/acoustics | 0.00 | 0.0 |
| End 2 | FW | 41.762 | -81.759 | 15-Jun | 21:00 | 3.25 | CTD/rosette ZP pump/net Secchi FRRF/fluoroprobe | 0.74 | 3.0 |
| Start 3 | FW | 41.762 | -81.759 | 15-Jun | 21:00 | 0 | PSS/acoustics | 0.00 | 0.0 |
| End 3 | FE | 41.762 | -81.692 | 16-Jun | 0:59 | 3.25 | CTD/rosette ZP pump/net Secchi FRRF/fluoroprobe | 0.74 | 3.0 |
| Start 4 | FE | 41.762 | -81.692 | 16-Jun | 0:59 | 0 | PSS/acoustics | 0.00 | 0.0 |
| End 4 | FW | 41.762 | -81.759 | 16-Jun | 4:59 | 3.25 | CTD/rosette ZP pump/net Secchi FRRF/fluoroprobe | 0.74 | 3.0 |
| Start 5 | FW | 41.762 | -81.759 | 16-Jun | 4:59 | 0 | PSS/acoustics | 0.00 | 0.0 |
| End 5 | FE | 41.762 | -81.692 | 16-Jun | 8:58 | 3.25 | CTD/rosette ZP pump/net Secchi FRRF/fluoroprobe | 0.74 | 3.0 |
| Start 6 | FE | 41.762 | -81.692 | 16-Jun | 8:58 | 0 | PSS/acoustics | 0.00 | 0.0 |
| End 6 | FW | 41.762 | -81.759 | 16-Jun | 12:57 | 3.25 | CTD/rosette ZP pump/net Secchi FRRF/fluoroprobe | 0.74 | 3.0 |

| Station 2 (BW-BE) |
| --- |
| Cycle | Station name | Lat | Long | Date | ETA | Site Time (hr) | Tasks | Transit time (hr)* | Transit dist. (nm) |
| Start 1 | BW | 41.966 | -81.718 | 16-Jun | 17:00 | 2.5 | PSS/acoustics | 1.55 | 12.4 |
| End 1 | BE | 41.966 | -81.650 | 16-Jun | 21:00 | 3.25 | CTD/rosette ZP pump/net Secchi FRRF/fluoroprobe | 0.75 | 3.0 |
| Start 2 | BE | 41.966 | -81.650 | 16-Jun | 21:00 | 0 | PSS/acoustics | 0.00 | 0.0 |
| End 2 | BW | 41.966 | -81.718 | 17-Jun | 1:00 | 3.25 | CTD/rosette ZP pump/net Secchi FRRF/fluoroprobe | 0.75 | 3.0 |
| Start 3 | BW | 41.966 | -81.718 | 17-Jun | 1:00 | 0 | PSS/acoustics | 0.00 | 0.0 |
| End 3 | BE | 41.966 | -81.650 | 17-Jun | 5:00 | 3.25 | CTD/rosette ZP pump/net Secchi FRRF/fluoroprobe | 0.75 | 3.0 |
| Start 4 | BE | 41.966 | -81.650 | 17-Jun | 5:00 | 0 | PSS/acoustics | 0.00 | 0.0 |
| End 4 | BW | 41.966 | -81.718 | 17-Jun | 9:00 | 3.25 | CTD/rosette ZP pump/net Secchi FRRF/fluoroprobe | 0.75 | 3.0 |
| Start 5 | BW | 41.966 | -81.718 | 17-Jun | 9:00 | 0 | PSS/acoustics | 0.00 | 0.0 |
| End 5 | BE | 41.966 | -81.650 | 17-Jun | 12:59 | 3.25 | CTD/rosette ZP pump/net Secchi FRRF/fluoroprobe | 0.75 | 3.0 |
| Start 6 | BE | 41.966 | -81.650 | 17-Jun | 12:59 | 0 | PSS/acoustics | 0.00 | 0.0 |
| End 6 | BW | 41.966 | -81.718 | 17-Jun | 16:14 | 3.25 | CTD/rosette ZP pump/net Secchi FRRF/fluoroprobe | 0.00 | 3.0 |

| Station 3 (DW-DE) |
| --- |
| Cycle | Station name | Lat | Long | Date | ETA | Site Time (hr) | Tasks | Transit time (hr)* | Transit dist. (nm) |
| Start 1 | DW | 42.200 | -80.878 | 17-Jun | 21:12 | 0 | PSS/acoustics | 4.97 | 39.7 |
| End 1 | DE | 42.200 | -80.810 | 18-Jun | 1:00 | 3.05 | CTD/rosette ZP pump/net Secchi FRRF/fluoroprobe | 0.75 | 3.0 |
| Start 2 | DE | 42.200 | -80.810 | 18-Jun | 1:00 | 0 | PSS/acoustics | 0.00 | 0.0 |
| End 2 | DW | 42.200 | -80.878 | 18-Jun | 5:00 | 3.25 | CTD/rosette ZP pump/net Secchi FRRF/fluoroprobe | 0.75 | 3.0 |
| Start 3 | DW | 42.200 | -80.878 | 18-Jun | 5:00 | 0 | PSS/acoustics | 0.00 | 0.0 |
| End 3 | DE | 42.200 | -80.810 | 18-Jun | 9:00 | 3.25 | CTD/rosette ZP pump/net Secchi FRRF/fluoroprobe | 0.75 | 3.0 |
| Start 4 | DE | 42.200 | -80.810 | 18-Jun | 9:00 | 0 | PSS/acoustics | 0.00 | 0.0 |
| End 4 | DW | 42.200 | -80.878 | 18-Jun | 12:59 | 3.25 | CTD/rosette ZP pump/net Secchi FRRF/fluoroprobe | 0.75 | 3.0 |
| Start 5 | DW | 42.200 | -80.878 | 18-Jun | 12:59 | 0 | PSS/acoustics | 0.00 | 0.0 |
| End 5 | DE | 42.200 | -80.810 | 18-Jun | 16:59 | 3.25 | CTD/rosette ZP pump/net Secchi FRRF/fluoroprobe | 0.75 | 3.0 |
| Start 6 | DE | 42.200 | -80.810 | 18-Jun | 16:59 | 0 | PSS/acoustics | 0.00 | 0.0 |
| End 6 | DW | 42.200 | -80.878 | 18-Jun | 20:59 | 3.25 | CTD/rosette ZP pump/net Secchi FRRF/fluoroprobe | 0.75 | 3.0 |

| Station 4 (GE-GW) |
| --- |
| Cycle | Station name | Lat | Long | Date | ETA | Site Time (hr) | Tasks | Transit time (h)* | Transit dist. (nm) |
| Start 1 | GE | 42.317 | -81.150 | 19-Jun | 1:00 | 2.27 | PSS/acoustics | 1.74 | 13.9 |
| End 1 | GW | 42.317 | -81.218 | 19-Jun | 5:00 | 3.25 | CTD/rosette ZP pump/net Secchi FRRF/fluoroprobe | 0.75 | 3.0 |
| Start 2 | GW | 42.317 | -81.218 | 19-Jun | 5:00 | 0 | PSS/acoustics | 0.00 | 0.0 |
| End 2 | GE | 42.317 | -81.150 | 19-Jun | 9:00 | 3.25 | CTD/rosette ZP pump/net Secchi FRRF/fluoroprobe | 0.75 | 3.0 |
| Start 3 | GE | 42.317 | -81.150 | 19-Jun | 9:00 | 0 | PSS/acoustics | 0.00 | 0.0 |
| End 3 | GW | 42.317 | -81.218 | 19-Jun | 13:00 | 3.25 | CTD/rosette ZP pump/net Secchi FRRF/fluoroprobe | 0.75 | 3.0 |
| Start 4 | GW | 42.317 | -81.218 | 19-Jun | 13:00 | 0 | PSS/acoustics | 0.00 | 0.0 |
| End 4 | GE | 42.317 | -81.150 | 19-Jun | 16:59 | 3.25 | CTD/rosette ZP pump/net Secchi FRRF/fluoroprobe | 0.75 | 3.0 |
| Start 5 | GE | 42.317 | -81.150 | 19-Jun | 16:59 | 0 | PSS/acoustics | 0.00 | 0.0 |
| End 5 | GW | 42.317 | -81.218 | 19-Jun | 20:59 | 3.25 | CTD/rosette ZP pump/net Secchi FRRF/fluoroprobe | 0.75 | 3.0 |
| Start 6 | GW | 42.317 | -81.218 | 19-Jun | 20:59 | 0 | PSS/acoustics | 0.00 | 0.0 |
| End 6 | GE | 42.317 | -81.150 | 20-Jun | 0:59 | 3.25 | CTD/rosette ZP pump/net Secchi FRRF/fluoroprobe | 0.75 | 3.0 |

| Station 5 (CE-CW) |
| --- |
| Cycle | Station name | Lat | Long | Date | ETA | Site Time (hr) | Tasks | Transit time (hr)* | Transit dist. (nm) |
| Start 1 | CE | 42.175 | -81.267 | 20-Jun | 5:00 | 2.77 | PSS/acoustics | 1.24 | 9.9 |
| End 1 | CW | 42.175 | -81.334 | 20-Jun | 9:00 | 3.25 | CTD/rosette ZP pump/net Secchi FRRF/fluoroprobe | 0.75 | 3.0 |
| Start 2 | CW | 42.175 | -81.334 | 20-Jun | 9:00 | 0 | PSS/acoustics | 0.00 | 0.0 |
| End 2 | CE | 42.175 | -81.267 | 20-Jun | 13:00 | 3.25 | CTD/rosette ZP pump/net Secchi FRRF/fluoroprobe | 0.75 | 3.0 |
| Start 3 | CE | 42.175 | -81.267 | 20-Jun | 13:00 | 0 | PSS/acoustics | 0.00 | 0.0 |
| End 3 | CW | 42.175 | -81.334 | 20-Jun | 16:59 | 3.25 | CTD/rosette ZP pump/net Secchi FRRF/fluoroprobe | 0.75 | 3.0 |
| Start 4 | CW | 42.175 | -81.334 | 20-Jun | 16:59 | 0 | PSS/acoustics | 0.00 | 0.0 |
| End 4 | CE | 42.175 | -81.267 | 20-Jun | 20:59 | 3.25 | CTD/rosette ZP pump/net Secchi FRRF/fluoroprobe | 0.75 | 3.0 |
| Start 5 | CE | 42.175 | -81.267 | 20-Jun | 20:59 | 0 | PSS/acoustics | 0.00 | 0.0 |
| End 5 | CW | 42.175 | -81.334 | 21-Jun | 0:59 | 3.25 | CTD/rosette ZP pump/net Secchi FRRF/fluoroprobe | 0.75 | 3.0 |
| Start 6 | CW | 42.175 | -81.334 | 21-Jun | 0:59 | 0 | PSS/acoustics | 0.00 | 0.0 |
| End 6 | CE | 42.175 | -81.267 | 21-Jun | 4:59 | 3.25 | CTD/rosette ZP pump/net Secchi FRRF/fluoroprobe | 0.75 | 3.0 |

| Station 6 (AE-AW) |
| --- |
| Cycle | Station name | Lat | Long | Date | ETA | Site Time (hr) | Tasks | Transit time (hr)* | Transit dist. (nm) |
| Start 1 | AE | 41.990 | -82.058 | 21-Jun | 9:34 | 0 | PSS/acoustics | 4.59 | 36.7 |
| End 1 | AW | 41.990 | -82.126 | 21-Jun | 13:34 | 3.25 | CTD/rosette ZP pump/net Secchi FRRF/fluoroprobe | 0.74 | 3.0 |
| Start 2 | AW | 41.990 | -82.126 | 21-Jun | 13:34 | 0 | PSS/acoustics | 0.00 | 0.0 |
| End 2 | AE | 41.990 | -82.058 | 21-Jun | 17:34 | 3.25 | CTD/rosette ZP pump/net Secchi FRRF/fluoroprobe | 0.74 | 3.0 |
| Start 3 | AE | 41.990 | -82.058 | 21-Jun | 17:34 | 0 | PSS/acoustics | 0.00 | 0.0 |
| End 3 | AW | 41.990 | -82.126 | 21-Jun | 21:33 | 3.25 | CTD/rosette ZP pump/net Secchi FRRF/fluoroprobe | 0.74 | 3.0 |
| Start 4 | AW | 41.990 | -82.126 | 21-Jun | 21:33 | 0 | PSS/acoustics | 0.00 | 0.0 |
| End 4 | AE | 41.990 | -82.058 | 22-Jun | 1:33 | 3.25 | CTD/rosette ZP pump/net Secchi FRRF/fluoroprobe | 0.74 | 3.0 |
| Start 5 | AE | 41.990 | -82.058 | 22-Jun | 1:33 | 0 | PSS/acoustics | 0.00 | 0.0 |
| End 5 | AW | 41.990 | -82.126 | 22-Jun | 5:33 | 3.25 | CTD/rosette ZP pump/net Secchi FRRF/fluoroprobe | 0.74 | 3.0 |
| Start 6 | AW | 41.990 | -82.126 | 22-Jun | 5:33 | 0 | PSS/acoustics | 0.00 | 0.0 |
| End 6 | AE | 41.990 | -82.058 | 22-Jun | 9:32 | 3.25 | CTD/rosette ZP pump/net Secchi FRRF/fluoroprobe | 0.74 | 3.0 |
| 49 | Cleve. Port Author. | 41.549 | -81.704 | 22-Jun | 13:23 | 0 | Arrive Cleveland | 3.84 | 30.7 |

# Figure 1.  We want to sample end point stations and tow the PSS and acoustics on the 3 nautical miles transects.  Arrows and sequential numbers describe planned cruise track.  Note, however, that station prioritizations are as follows, ranked from most important to least important (FW-FE; BW-BE; DW-DE; AW-AE; CW-CE; and GW-GE).