| Alaskan Region - 129 Ramp Inspection Job Aid |
| --- |
| This job aid is intended to aid the inspector in conducting 129 ramp inspections by providing a guide to the requirements of foreign carriers operating to the U.S. Foreign Air Carriers operating under 14 CFR Part 129 are required to comply with the following FAA Regulations: Part 91 and 129 and additionally for U.S. registered aircraft Parts 21, 43, 61, 63, 65 Their FAA issued operations specifications and ICAO Annex 6 (within the limitations of HBAT/HBAW 98-04) are required to be complied with by 14 CFR Section 129.11 Operations specifications. (a) Each foreign air carrier shall conduct its operations within the United States in accordance with operations specifications issued by the Administrator under this part and in accordance with the Standards and Recommended Practices contained in Part I (International Commercial Air Transport) of Annex 6 (Operation of Aircraft) to the Convention on International Civil Aviation Organization. ICAO CC art.= ICAO Chicago Convention article AN6 = ICAO Annex 6 Standard 129 OpsSpec = foreign carrier operations specification paragraph requirement |
| FAR 129 Foreign Air Carrier, Ramp Check-Surveillance Plan checklist. NOTE - *Asterisk items are not required to be aboard the aircraft. |
|  | 1.0 Aircraft documentation and records |
|  | 1.1 Registration certificate (129.13(a), 91.203(a)(2), 375.20, ICAO CC art 29 a) |
|  | 1.2 Airworthiness certificate (129.13(a), 91.203(a)(1), 375.20, ICAO CC art 29 b) & 31 |
|  | 1.3 Radio station license ICAO CC art 29 e), art 30 a) |
|  | 1.4 Journey log book ICAO AN6-11.4.1, CC art 29 d) |
|  | 1.5 Maintenance release AN6-4.3.1(c) & 8.8 |
|  | 1.6 *Maintenance program/manual AN6-8.2, 8.3 and 11.3 For U.S. registered aircraft 129.14(a) |
|  | 1.7 *Minimum Equipment List (MEL) 129.11(a), 129 Ops Spec A003 (d), AN6-6.1.2 For U.S registered aircraft 129.14(b), verify FAA issued 129 Ops Spec D095 (letter) authorizing the use of the MEL is on board. |
|  | 2.0 Flight Deck |
|  | 2.1 Are their checklists for normal and emergency operations AN6-4.2.5 & 6.1.3 |
|  | 2.2 Do they correspond to the checklists in the AOM AN6-6.1.3 |
|  | 2.3 Aircraft Performance Limitations in AFM & Calculations AN6-6.2.3 (b) & 4.3.1 (f) |
|  | 2.4 Airport operating minimums AN6-4.2.7 & AN6-AP2-9 |
|  | 2.5 Current aeronautical charts AN6-6.2.3 (c) |
|  | 2.6 Operations manual AN6-6.2.3 (a) |
|  | 2.7* Air Operator Certificate (AOC) and 129 Ops Specs (Annex 6 4.2.1.5) and 129.11 *Verify in office |
|  | 3.0 Flight Operations Requirements |
|  | 3.1 Is the passenger manifest completed ICAO CC art 29 f) |
|  | 3.2 Is there a cargo declaration ICAO CC art 29 g) |
|  | 3.3 Were the Weight and Balance forms available and completed AN6-4.3.1 (d)&(e) |
|  | 3.4 Weather reports and forecasts available AN6-4.3.5 |
|  | 3.5 Operational and ATS flight plans available 91.153, 91.707, 91.711(d), 91.169, 91.173, AN6-4.3.3 |
|  | 3.6 Proper fuel supply on board 91.151VFR, 91.167IFR, 129 OpsSpec A001, B051, B056 & AN6-4.3.6 |
|  | 3.7 Alternate airports and fuel for alternate 91.169IFR, AN6-4.3.4 & 4.3.6 (if required) |
|  | 3.8 Preflight action 91.103 & AN6-4.1.1 |

| Alaskan Region - 129 Ramp Inspection Job Aid |
| --- |
|  | 4.0 Flight Crew |
|  | 4.1 Flight crew licenses 61.3(a)&(b), 91.711(c)(2) 129 OpsSpec A001 |
|  | 4.2 Flight crew medical certification 61.3(c) |
|  | 4.3 Flight crew age limit 129 OpsSpec A001, |
|  | 4.4 Flight attendants manuals AN6-4.2.2.1, 6.2.3 (a) & AN6-AP2 |
|  | 4.5 Flashlights for each crew station, including flight attendants AN6-6.10 f) |
|  | 4.6 Crew seat belts & shoulder harness 91.107US Registered, AN6-6.2.2 (c) |
|  | 5.0 Aircraft Equipment |
|  | 5.1 Is there an adequate oxygen supply for the passengers and crew 91.211US Registry, AN6-4.3.8 & 6.7 |
|  | 5.2 Passenger briefing cards & contents AN6-6.2.2 (d) |
|  | 5.3 Are there portable fire extinguishers on the flight deck and in the Cabin? AN6-6.2.2 (b) |
|  | 5.4 TCAS (ACAS) 91.221, 129.18, 129 OpsSpec A036, AN6-6.18 |
|  | 5.5 Does the flight deck door meet the flight deck security requirements of 129.28 |
|  | 5.6 Life rafts and jackets 91.205(b)(12) US Registered, AN6-6.5.2 |
|  | 5.7 Pyrotechnical distress devices 91.205(b)(12) US Registered, AN6-6.5.3.1 (b) |
|  | 5.8 First aid kit AN6-6.2.2 |