#### 1977 Cessna–U206G – N7304N

# Preflight Cabin

- Pilot’s Operating Handbook Available

- Airplane Weight & Balance	Check

- Parking Brake	Set

- Hobbs, Tach & Squawks	Check

- Fire Extinguisher	Charged

- Documents	AROW in airplane

- Control/Avionics Lock	Remove

- Avionics Power Switch	Off

- Ignition Switch	Off

- Master Switch	On

- Fuel Quantity Indicators	Check Quantity

- Low-Vacuum Warning Light	Check On

- Avionics Power Switch	On

- Avionics Cooling Fan	Check Audibly

- Avionics Power Switch	Off

- Pitot Heat 	Check

- Lights	Check

- Master Switch	Off

- Alternate Static	Off

- Fuel Selector	Fuller Tank

Preflight Empennage

- Rudder Gust Lock	Remove

- Tail Tie-Down	Disconnect

- Control Surfaces	Check

- Check Cargo Door.	Latched & Locked (right side only)

Note

The cargo doors must be fully closed and latched before operating the electric wing flaps…

Preflight Right Wing trailing edge

- Right Flap	Check

- Right Aileron	Check

- Right Wingtip & Light	Check

# Preflight Right Wing

- Wing Tie Down	Disconnect

- Right Fuel Vent	Check Clear

- Rt. Main Wheel Tire & Brake..	Check

- Right Fuel Sump(s)	Drain

- Right Fuel Quantity	Visually Check

- Fuel Filler Cap	Secure, vent unobstructed

Nose

- Static Sources	Check (Both sides)

- Prop/Spinner/Engine Inlet	Check

- Landing / Taxi Lights	Check

- Nose Wheel, Strut & Tire	Check

- Nose Tie-Down	Disconnect

- Engine Oil Filler Cap	Check Secure

- Engine Oil Dipstick	9-12 Quarts

- Fuel Strainer Drain Knob	Pullout to Drain

# Preflight Left Wing

- Left Main Wheel Tire & Brake.	Check

- Left Fuel Sump(s)	Drain

- Left Fuel Quantity	Visually Check

- Fuel Filler Cap	Secure

# Preflight Left Wing Leading Edge

- Pitot Tube Cover	Remove & Check

- Left Fuel Vent	Check Clear

- Stall Warning Vane	Check

- Wing Tie-Down	Disconnect

- Left Wingtip & Light	Check

# Preflight Left Wing Trailing Edge

- Left Aileron	Check

- Left Flap	Check

##### PASSENGER BRIEF

- Seat Belts / Shoulder Harness

- Personal Electronic Devices off

- Air Vents / Comfort

- Fire Extinguisher Location / Operation

- Emergency Procedures & Exits

##### MISSION BRIEF

- Mission Objective

- Destination, WX, Route, Alt, ETE

- NOTAMS

- Crew Coordination & CRM

- Sterile Cockpit Procedures

- Cockpit Layout

- Intercom & Radio Usage

- Seats, Seatbelts, Doors

- Emergency Action & Equipment

Before Starting Engine

- Preflight Inspection	Complete

- Passenger Brief	Complete

- Seats / Belts / Shoulder Harness	Adjust and Lock

- Brakes	Test & Set

- Avionics Power Switch	Off

Caution

The avionics power switch must be OFF during engine start to prevent possible damage to avionics.

- Electrical Equipment	Off

- Autopilot (If installed)	Off

9.  Cowl Flaps	Open

10. Master Switch	On

11. Fuel Selector	Fuller Tank

12. Circuit Breakers	Check In

# Starting Engine

- Mixture	Rich

- Propeller	High RPM

- Throttle	Closed

- Auxiliary Fuel Pump	On

- Throttle.	Advance to obtain 8-10 gal/hr fuel flow, then return to CLOSED position.

- Auxiliary Fuel Pump	Off

- Propeller Area	Clear

- Ignition Switch	Start

- Throttle	Advance Slowly

- Ignition Switch.	Release when engine starts

Note

The engine should start in two or three revolutions. If it does not continue running, start again at step 3 above. If the engine does not start, leave auxiliary fuel pump switch off, set mixture to idle cut-off, open throttle, and crank until engine fires or for approximately 15 seconds. If unsuccessful, start again using the normal starting procedure after allowing the starter motor to cool.

- Throttle	Idle

- Oil Pressure	Check

- Starter	Check Disengaged

- Avionics Power Switch	On

- Beacon & Nav Lights	On

- Taxi Lights	As Required

- Flaps	Up

- Transponder	TEST/STBY

- Radios	On

Taxi

- Brakes	Test

- Attitude Indicator, Turn Coordinator, H.I. & Compass	Verify Proper Operation

Before Takeoff - Run-Up

- Parking Brake	Set

- Cabin Doors & Window	Closed

and Locked

- Cowl Flaps	Open

- Flight Controls	Free & Correct

- Flight Instruments	Check

- Fuel Selector Valve	Fuller Tank

- Mixture	Rich

- Elevator & Rudder Trim	Takeoff Setting

- Throttle	1700 RPM

- Magnetos	Max Drop 150 RPM

Max Differential 50 RPM

- Propeller	Cycle

- Engine Inst & Ammeter	Check

- Suction Gauge	..Check (4.6 to 5.4 In. Hg.)

- Throttle	Idle Check, then 800 to 1000 RPM

- Avionics Power Switch	On

- Radios	Set

- Autopilot (If Installed)	Off

- Flashing Beacon, Nav lights, Strobe Lights, Pulse Lights (If installed)…	As Desired

- Throttle Friction Lock	Adjust

- Flaps set for Takeoff	0°-20°

- Electric Trim (If Installed)	Test

- Takeoff Briefing	Complete

- Lights	Set

- Transponder	Set to ALT

- Time	Record

- Parking Brake	Release

Takeoff

- Flaps	0°-20°

- Power	Full Throttle and 2850 RPM

- Mixture	Lean for field elevation per fuel flow placard

- Engine Instruments	In Green

- Rotate	50 KIAS

- Climb Speed	70 - 80 KIAS

- Short Field T.O.	20° Flaps / 65 KIAS Until Clear

- Soft Field T.O	20° Flaps / Ground Effect ASAP

7.  Flaps..	Retract when clear of obstacles and 80 KIAS is reached

Normal Climb

- Airspeed	90 - 100 KIAS

- Power	25 In. Hg. & 2550 RPM

- Mixture	Lean to 18 gal/hr fuel flow

- Cowl Flaps	Open as required

- Engine Instruments	Check

Cruise

- Power	15-23 Inches & 2200-2550 RPM (no more than 75% power).

- Mixture	Lean

- Elevator & Rudder Trim	Adjust

- Cowl Flaps	As required

- Engine Instruments / Fuel	Check

- Heading Indicator (H.I.)	to Compass

- Lights	As Required

- Flight Plan	Activate as Required

Descent

- Heading Indicator.	To Compass

- Altimeter	Set

- Lights	As Required

- Engine Instruments	Check

- Power	As Desired

- Mixture…	Lean for Smoothness; use full rich mixture for idle power.

- Cowl Flaps	Closed

- Wing Flaps	As Desired

Before Landing

- Seat, Seat Belts, Shoulder Harness 	Adjust and Lock

- Fuel Selector	Fuller Tank

- Mixture	Rich (Below 3000 ft.)

- Propeller	High RPM

- Autopilot (If installed)	Off

- Airspeed	75-85 KIAS  (Flaps Up)

- Wing Flaps	As Desired

- Airspeed..	65-75 KIAS (Flaps Down)

- Elevator Trim	Adjust

10.Touchdown	Main Wheel First

11. Landing Roll	Lower Nose Wheel Gently

## 12. Braking	Minimum required

## Short Field Landing

- Airspeed	75-85 KIAS  (Flaps Up)

- Flaps	40º (below 100 KIAS)

- Airspeed	Maintain 64 KIAS

- Elevator Trim	Adjust

- Power	Reduce to idle as obstacle

is cleared

- Touchdown	Main Wheels First

- Brakes	Apply Heavily

- Flaps	Retract for Max brake effectiveness.

## Balked Landing

- Power	Full Throttle  & 2850 RPM

- Flaps	Retract to 20°

- Airspeed	80 KIAS

- Flaps.	Retract Slowly

- Cowl Flaps	Open

After Landing (Clear of Runway)

- Wing Flaps	Retract

- Cowl Flaps	Open

- Lights	As Required

- Transponder	STBY & 1200

- Mixture	Lean

- Pitot Heat	Off

# Securing Aircraft

- Parking Brake	Set

- Throttle	Idle

- Avionics Power & Electrical Equipment	Off

- Magnetos	Check for Ground

- Mixture	Idle Cut Off

- Ignition & Master Switch	Off

- Control/Avionics Lock	Install

- Parking Brake 	 Off

- Cowl Flaps 	Closed

- Hobbs & Tach	Record

- Aircraft	Secured & Locked

- Flight Plan	Closed

# V Speeds and Specs

- X-Wind (Max Demo’d)	15 Knots

- Vr  Rotation Speed	50 KIAS

- Vx  Best Angle Climb	66 KIAS

- Vy  Best Rate Climb	84 KIAS

- Vso  Stall w/ Flaps	46 KIAS

- Vs1  Stall w/o Flaps	55 KIAS

- Best Glide (3600 Lbs)	75 KIAS

- Best Glide (3200 Lbs)	70 KIAS

- Best Glide (2800 Lbs)	65 KIAS

- Va  Max Abrupt Ctrl (3600 Lbs)	120 KIAS

- Va  Max Abrupt Ctrl (2900 Lbs)	106 KIAS

- VA Max Abrupt Ctrl (2200 Lbs)	93 KIAS

- Vno  Max Structural Cruise..	149 KIAS

- Vne  Never Exceed	183 KIAS

- Vfe  10° Flaps	140 KIAS

- Vfe  10°-Full Flaps	100 KIAS

General...

- EMERGENCY	121.50

- Unicom	122.70-122.80-122.95

123.00-123.05

- Multicom	122.90 (CTAF)

- Flight Service	122.20 (Most Common) 122.10-122.60-123.60

- Flight Watch	122.00

- Air to Air	122.75-122.85-123.45

Transponder Codes/Light Signals...

- 1200	VFR

- 7500	HIJACK

- 7600	LOST COMMS

- 7700	EMERGENCY

- Gross Weight Capacity

3600 (Takeoff)	3600 (Landing)

- Engine	Continental  IO-520-F

- Max Power	300 BHP

- Fuel Type	100LL (Blue)

- Fuel Capacity (Standard)	88 Gal Usable

- Oil Type	Aeroshell 15W-50

- Oil Capacity	12 Qts (Minimum 9)

- Electrical	24-28 Volt / 60 Amp

- Tire Pressure	Nose-49 PSI / Main-42 PSI

This checklist is a guide to coordinate Pilot Operating Handbook and STC data applicable to this particular aircraft only.  The applicable Pilot Operating Handbook and STC installations remain the official documentation for this aircraft.

The pilot in command is responsible for complying with all items in the Pilot Operating Handbook and applicable STCs.

I certify this checklist has been reviewed for accuracy.

__________________________________

Wing Director of Maintenance

Dated: ___________________

# Text boxes

Warning

When turning on the master switch, using an external power source, or pulling the propeller through by hand, treat the propeller as if the ignition switch were on.  Do not stand, nor allow anyone else to stand, within the arc of the propeller, since a loose or broken wire, or a component malfunction, could cause the propeller to rotate.