Table 3

Medical Research Facility Area

Groundwater Monitoring Program - Permanent Wells

Tritium Results for CY 1997

| Well Number | Collection Date | COC Number | Tritium Result (pCi/L) | Error (pCi/L) | MDL (pCi/L) |
| --- | --- | --- | --- | --- | --- |
| 94-01 | 01/23/97 | 97012308 | 2,450 (a) | 316 | 372 |
|  | “ | “ | 2,540 (re-analysis) | 341 | 401 |
|  | 04/28/97 | 97042807 | <401 (a) | 240 | 401 |
|  | 05/22/97 | 97052216 | 384 (a) | 237 | 384 |
|  | “ | “ | 535 (b) | 243 | 384 |
|  | “ | “ | 465 (c) | 240 | 384 |
|  | 06/13/97 | 97061302 | <451 (a) | 237 | 451 |
| 94-02 | 06/13/97 | 97061302 | <451 (a) | 242 | 451 |
| 84-12 (Former 94-09) | 04/29/97 | 97042909 | 367 (d) | 208 | 326 |
|  | 05/27/97 | 97052710 | 686 (d) | 269 | 403 |
|  | 06/12/97 | 97061210 | 501 (d) | 283 | 451 |
|  | 06/18/97 | 97061812 | 3,030 (e) | 371 | 445 |
| 84-13 (Former 94-10) | 05/22/97 | 97052216 | 4,310 (d) | 402 | 384 |
|  | 06/12/97 | 97061210 | 4,800 (d) | 454 | 451 |
|  | 06/18/97 | 97061812 | 11,400 (e) | 618 | 445 |

(a): Dedicated Geoguard pump in standard position in well screen (i.e., lower 1/3 of ten foot screen).

(b): Dedicated Geoguard pump raised two feet within well screen.

(c): Dedicated Geoguard pump raised four feet within well screen.

(d): Grundfos pump positioned approximately eight feet below water table.

(e): Grundfos pump positioned within upper three feet of water table.

Table 3 (Continued)

Medical Research Facility Area

Groundwater Monitoring Program - Permanent Wells

Gross Alpha Results for CY 1997

| Well Number | Collection Date | COC Number | Gross Alpha Result (pCi/L) | Error (pCi/L) | MDL (pCi/L) |
| --- | --- | --- | --- | --- | --- |
| 94-01 | 01/23/97 | 97012308 | <0.75 (a) | --- | 0.75 |
|  | 04/28/97 | 97042807 | <1.53 (a) | 0.79 | 1.53 |
|  | 05/22/97 | 97052216 | <0.88 (a) | 0.57 | 0.88 |
|  | 06/13/97 | 97061302 | 2.13 (a) | 1.01 | 1.35 |
| 94-02 | 06/13/97 | 97061302 | <1.35 (a) | 0.89 | 1.35 |
| 84-12 (Former 94-09) | 04/29/97 | 97042909 | 2.08 (d) | 1.09 | 1.53 |
|  | 05/27/97 | 97052710 | 1.77 (d) | 0.73 | 0.88 |
|  | 06/12/97 | 97061210 | 1.38 (d) | 0.87 | 1.35 |
|  | 06/18/97 | 97061812 | 1.50 (e) | 0.89 | 1.35 |
| 84-13 (Former 94-10) | 05/22/97 | 97052216 | 1.32 (d) | 0.70 | 0.88 |
|  | 06/12/97 | 97061210 | 2.90 (d) | 1.08 | 1.35 |
|  | 06/18/97 | 97061812 | <1.35 (e) | 0.75 | 1.35 |

(a): Dedicated Geoguard pump in standard position in well screen (i.e., lower 1/3 of ten foot screen).

(b): Dedicated Geoguard pump raised two feet within well screen.

(c): Dedicated Geoguard pump raised four feet within well screen.

(d): Grundfos pump positioned approximately eight feet below water table.

(e): Grundfos pump positioned within upper three feet of water table.

Table 3 (Continued)

Medical Research Facility Area

Groundwater Monitoring Program - Permanent Wells

Gross Beta  Results for CY 1997

| Well Number | Collection Date | COC Number | Gross Beta Result (pCi/L) | Error (pCi/L) | MDL (pCi/L) |
| --- | --- | --- | --- | --- | --- |
| 94-01 | 01/23/97 | 97012308 | 2.78 (a) | --- | 1.49 |
|  | 04/28/97 | 97042807 | <4.21 (a) | 2.63 | 4.21 |
|  | 05/22/97 | 97052216 | 4.65(a) | 2.17 | 3.35 |
|  | 06/13/97 | 97061302 | <3.68 (a) | 5.57 | 3.68 |
| 94-02 | 06/13/97 | 97061302 | 4.76 (a) | 2.36 | 3.68 |
| 84-12 (Former 94-09) | 04/29/97 | 97042909 | 5.55 (d) | 2.73 | 4.21 |
|  | 05/27/97 | 97052710 | 7.27 (d) | 2.29 | 3.35 |
|  | 06/12/97 | 97061210 | 23.2 (d) | 3.01 | 3.68 |
|  | 06/18/97 | 97061812 | <3.68 (e) | 2.26 | 3.68 |
| 84-13 (Former 94-10) | 05/22/97 | 97052216 | 4.11 (d) | 2.15 | 3.35 |
|  | 06/12/97 | 97061210 | 11.3 (d) | 2.61 | 3.68 |
|  | 06/18/97 | 97061812 | <3.68 (e) | 2.23 | 3.68 |

(a): Dedicated Geoguard pump in standard position in well screen (i.e., lower 1/3 of ten foot screen).

(b): Dedicated Geoguard pump raised two feet within well screen.

(c): Dedicated Geoguard pump raised four feet within well screen.

(d): Grundfos pump positioned approximately eight feet below water table.

(e): Grundfos pump positioned within upper three feet of water table.

Table 3 (Continued)

Medical Research Facility Area

Groundwater Monitoring Program - Permanent Wells

Gamma  Results for CY 1997

| Well Number | Collection Date | COC Number | Gamma Result (pCi/L) | 1-Sigma % Error |
| --- | --- | --- | --- | --- |
| 94-01 | 01/23/97 | 97012708 | K-40=4.25, Ra-224=3.10 (a) | 27.58%, 43.00% |
|  | 04/28/97 | 97042807 | Tl-208=0.99 (a) | 27.99% |
|  | 05/22/97 | 97052216 | K-40=3.97 (a) | 27.33% |
|  | 06/13/97 | 97061302 | Ra-224=20.7 (a) | 35.36% |
| 94-02 | 06/13/97 | 97061302 | ND (a) | --- |
| 84-12 (Former 94-09) | 04/29/97 | 97042909 | Not Analyzed? (d) | --- |
|  | 05/27/97 | 97052710 | K-40 =3.45 (d) | 33.69% |
|  | 06/12/97 | 97061210 | K-40=3.53 (d) | 27.10% |
|  | 06/18/97 | 97061812 | K-40=9.44 (e) | 19.69% |
| 84-13 (Former 94-10) | 05/22/97 | 97052216 | K-40=2.48 (d) | 42.74% |
|  | 06/12/97 | 97061210 | K-40=2.63 (d) | 39.29% |
|  | 06/18/97 | 97061812 | K-40=3.58, Tl-208=0.26 (e) | 31.58%, 45.00% |

(a): Dedicated Geoguard pump in standard position in well screen (i.e., lower 1/3 of ten foot screen).

(b): Dedicated Geoguard pump raised two feet within well screen.

(c): Dedicated Geoguard pump raised four feet within well screen.

(d): Grundfos pump positioned approximately eight feet below water table.

(e): Grundfos pump positioned within upper three feet of water table.

ND: Not Detected