Before the

Federal Communications Commission

Washington, D.C. 20554

| In the Matter of Amendment of Parts 2 and 25 of the Commission's Rules to Permit Operation of NGSO FSS Systems Co-Frequency with GSO and Terrestrial Systems in the Ku-Band Frequency Range; Amendment of the Commission's Rules to Authorize Subsidiary Terrestrial Use of the 12.2-12.7 GHz Band by Direct Broadcast Satellite Licensees and Their Affiliates; and Applications of Broadwave USA, PDC Broadband Corporation, and Satellite Receivers, Ltd. to Provide A Fixed Service in the 12.2-12.7 GHz Band | ) ) ) ) ) ) ) ) ) ) ) ) ) ) ) ) ) | ET Docket No. 98-206 RM-9147 RM-9245 |
| --- | --- | --- |

FOURTH ERRATUM

Adopted:  February 13, 2001	Released: February 16, 2001

By the Office of Engineering and Technology:

On December 8, 2000, the Commission released a First Report and Order and Further Notice of Proposed Rule Making in the above captioned proceeding.  Subsequent to the release of this document, a minor error was discovered in the program used to calculate the satellite outage time data presented in Appendices G, H, and J.  Therefore, with this Erratum we correct Appendices G, H, and J.

Accordingly, IT IS ORDERED that this Erratum is issued pursuant to Section 0.241 of the Commission’s rules on delegated authority, 47 C.F.R. § 0.241.

FEDERAL COMMUNICATIONS COMMISSION

Bruce Franca

Acting Chief

Office of Engineering and Technology

APPENDIX G – EXAMPLES OF DBS SERVICE OUTAGES FOR DIFFERENT PERCENTAGES OF SERVICE UNAVAILABILITY (45 cm antenna)

| Table 1 EchoStar @ 119 WL |
| --- |
| DBS satellite orbital location | Degrees | 119.0 | 119.0 | 119.0 | 119.0 |
| Earth station location |  | Denver, CO | Washington, D.C. | Seattle, WA | Miami, FL |
| DBS satellite e.i.r.p. towards the Earth station location | DBW | 48.6 | 52.6 | 46.7 | 52.6 |
| Earth station elevation above mean sea level | Mm | 1.58 | 0.01 | 0.01 | 0.0 |
| Earth station elevation angle | Degrees | 41.8 | 27.6 | 35.2 | 37.7 |
| Free space loss | DB | 205.9 | 206.1 | 206.0 | 205.9 |
| Earth station antenna miss-pointing error | DB | 0.5 | 0.5 | 0.5 | 0.5 |
| Atmospheric absorption | DB | 0.2 | 0.2 | 0.2 | 0.2 |
| Clear-sky receive system noise temperature | Kelvin | 85 | 85 | 85 | 85 |
| Clear-sky earth station antenna G/T | DB | 14.5 | 14.5 | 14.5 | 14.5 |
| C/I for other assignments in the BSS Plan | DB | 20.0 | 20.0 | 20.0 | 20.0 |
| Clear-sky feeder link C/(N+I) | DB | 26.2 | 26.2 | 26.2 | 26.2 |
| Clear-sky carrier-to-noise plus interference ratio | DB | 10.7 | 13.6 | 8.9 | 13.8 |
| Required C/(N+I) for operating threshold | DB | 6.1 | 6.1 | 6.1 | 6.1 |
| Link margin | DB | 4.6 | 7.5 | 2.8 | 7.7 |
| Rain margin | DB | 1.83 | 4.09 | 0.94 | 4.23 |
| Rain intensity exceeded for 0.01% of an average year | mm/h | 30.3 | 48.2 | 36.5 | 95.8 |
| Satellite link availability for an average year | % | 99.97 | 99.94 | 99.69 | 99.77 |
| Satellite link unavailability for an average year | % | 0.0285 | 0.0647 | 0.3142 | 0.2279 |
| Total link unavailable time for an average year | Minutes | 149.9 | 340.1 | 1652.5 | 1198.8 |
| 10% of the unavailable time in an average year | Minutes | 15.0 | 34.0 | 165.3 | 119.9 |
| 5% of the unavailable time in an average year | Minutes | 7.5 | 17.0 | 82.6 | 59.9 |
| 2.86% of the unavailable time in an average year | Minutes | 4.3 | 9.7 | 47.3 | 34.3 |
| Satellite link unavailability for the worst-month | % | 0.1290 | 0.2631 | 1.0409 | 0.7873 |
| Total link unavailable time for the worst-month | Minutes | 56.5 | 115.3 | 456.2 | 345.1 |
| 10% of the unavailable time in the worst-month | Minutes | 5.7 | 11.5 | 45.6 | 34.5 |
| 5% of the unavailable time in the worst-month | Minutes | 2.8 | 5.8 | 22.8 | 17.3 |
| 2.86% of the unavailable time in the worst-month | Minutes | 1.6 | 3.3 | 13.0 | 9.9 |
| Rainy sky C/I for a 2.86% increase in link unavailability | DB | 23.9 | 22.6 | 25.0 | 22.2 |

| Table 2 DIRECTTV @ 101 WL |
| --- |
| DBS satellite orbital location | Degrees | 101.0 | 101.0 | 101.0 | 101.0 |
| Earth station location |  | Denver, CO | Washington, D.C. | Seattle, WA | Miami, FL |
| DBS satellite e.i.r.p. towards the Earth station location | DBW | 49.4 | 52.4 | 48.4 | 53.4 |
| Earth station elevation above mean sea level | Km | 1.58 | 0.01 | 0.01 | 0.0 |
| Earth station elevation angle | Degrees | 43.8 | 38.5 | 31.5 | 52.0 |
| Free space loss | DB | 205.8 | 205.9 | 206.0 | 205.7 |
| Earth station antenna miss-pointing error | DB | 0.5 | 0.5 | 0.5 | 0.5 |
| Atmospheric absorption | DB | 0.2 | 0.2 | 0.2 | 0.2 |
| Clear-sky receive system noise temperature | Kelvin | 125 | 125 | 125 | 125 |
| Clear-sky earth station antenna G/T | DB | 12.9 | 12.9 | 12.9 | 12.9 |
| C/I for other assignments in the BSS Plan | DB | 20.7 | 20.7 | 20.7 | 20.7 |
| Clear-sky feeder link C/(N+I) | DB | 24.2 | 24.2 | 24.2 | 24.2 |
| Clear-sky carrier-to-noise plus interference ratio | DB | 10.0 | 12.4 | 8.9 | 13.3 |
| Required C/(N+I) for operating threshold | DB | 5.0 | 5.0 | 5.0 | 5.0 |
| Link margin | DB | 5.0 | 7.4 | 3.9 | 8.3 |
| Rain margin | DB | 2.48 | 4.48 | 1.77 | 5.43 |
| Rain intensity exceeded for 0.01% of an average year | mm/h | 30.3 | 48.2 | 36.5 | 95.8 |
| Satellite link availability for an average year | % | 99.99 | 99.96 | 99.87 | 99.88 |
| Satellite link unavailability for an average year | % | 0.0146 | 0.0386 | 0.1251 | 0.1188 |
| Total link unavailable time for an average year | Minutes | 76.6 | 203.0 | 658.0 | 625.0 |
| 10% of the unavailable time in an average year | Minutes | 7.7 | 20.3 | 65.8 | 62.5 |
| 5% of the unavailable time in an average year | Minutes | 3.8 | 10.2 | 32.9 | 31.3 |
| 2.86% of the unavailable time in an average year | Minutes | 2.2 | 5.8 | 18.8 | 19.9 |
| Satellite link unavailability for the worst-month | % | 0.0720 | 0.1680 | 0.4672 | 0.4468 |
| Total link unavailable time for the worst-month | Minutes | 31.51 | 73.6 | 204.8 | 195.8 |
| 10% of the unavailable time in the worst-month | Minutes | 3.2 | 7.4 | 20.5 | 19.6 |
| 5% of the unavailable time in the worst-month | Minutes | 1.6 | 3.7 | 10.2 | 9.8 |
| 2.86% of the unavailable time in the worst-month | Minutes | 0.9 | 2.1 | 5.9 | 5.6 |
| Rainy sky C/I for a 2.86% increase in link unavailability | DB | 23.6 | 22.9 | 23.5 | 22.8 |

APPENDIX H -- A METHOD OF CONVERTING PERCENTAGE OF UNAVAILABLE TIME INTO A CARRIER-TO-INTERFERENCE RATIO

This appendix presents a method for determining the relationship between DBS service outage time and a DBS system’s carrier-to-noise plus interference ratio (C/N+I).  Specifically, this method can be used to determine the C/I that a terrestrial system needs to meet in relation to a DBS satellite system to keep service disruptions of the satellite system to a certain amount of outage time.  In this case the terrestrial system represents the interference and the satellite system represents the desired carrier.

The availability of a satellite space-to-Earth link is defined as the total amount of time that the satellite service is available to the user without disruption.  Conversely, the unavailability of that same link is the total time during which the user is without service (outage).  Generally, availability and unavailability are expressed in terms of percentage of time of an average year (8765.76 hours) or the worst month in an average year.  These two variables are complementary and always sum to 100 percent.  For example if a satellite system has an availability of 99.7%, its unavailability is 0.3% which equates to total outage time of 26.3 hours averaged over a year.

In a shared environment (satellite and terrestrial service), the total unavailability can be attributed to two sources: natural propagation phenomenon such as precipitation (e.g., rain) in the space-to-earth path and external radio interference.  In the frequency bands used by DBS for downlink (12.2-12.7 GHz), the predominant propagation impairment is rain attenuation in the space-to-earth slant path.  The amount of service outage caused by rain can be estimated using the prediction procedures of ITU-R Recommendation P.618-6.  This rain attenuation model predicts, for a given geographic area, the average service outage time over an average year for a specific level of precipitation attenuation along the space-to-earth slant path.

To determine the portion of the total C/I that is attributable to a terrestrial system, we first establish the amount of outage time of the DBS space-to-earth link that is caused by precipitation only. This outage time is directly dependent on the link margin of the space-to-earth link, which is calculated from the system’s link power budget.  Link margin is the amount of power received at the earth station receiver above its operating threshold that is designed into the satellite link to overcome the effects of rain and other impediments.  During rain, the satellite link is affected in two ways: the carrier signal strength is attenuated due to rain and the rain causes an increase in the system’s noise temperature.  If the rain attenuation and earth station G/T (gain / system noise temperature) degradation cause a reduction to the carrier-to-noise (C/N) power that exceeds the available link margin, the satellite link will experience an outage.  The amount of attenuation due to rain that causes an outage is referred to as the rain margin.

The satellite link budget (carrier-to-noise plus interference ratio) and the associated rain margin can be derived from the parameters identified in Table B-1.  It is evident from the table that the rain margin depends on the DBS satellite E.I.R.P. in the direction of the receiving earth station, the free space path loss, the earth station antenna gain-to-system noise temperature (G/T) ratio and the operating threshold.  Once the link margin is known, one can proceed to determine the rain margin.  This is accomplished by adding a rain attenuation term to the equation used to find the clear-sky carrier-to-noise ratio to instead find a rainy-sky carrier-to-noise ratio.  Additionally, the G/T must be recalculated to account for the increase in atmospheric noise due to the rain.  Thus, the G/T will be reduced during a rain event and the rain margin will be less than the link margin.

Once the rain margin is determined, the expected outage time of a satellite link in an average year or in the worst month can be computed using the prediction method contained in ITU-R Recommendation P.618-6.  This recommendation entitled “Propagation Data and Prediction Method required for the Design of Earth-Space Telecommunication Systems” provides a procedure to estimate the long-term statistics of the space-to-earth path precipitation attenuation and the associated percentage of outage time.

Now that the percentage of outage time due solely to rain is known, we can reverse the procedure to determine the minimum C/I that a terrestrial system must maintain to effect a specific amount of additional outage time on the satellite system.  First, the additional outage time must be determined, either as a percentage of additional outage time or a number of minutes per time period.  This additional outage time can then be added to the outage time due to rain only to find the ‘equivalent unavailability.’ For example, if a satellite space-to-earth link has an unavailability of 0.3% and the minimum C/I for the terrestrial system to cause no more than an additional 10% outage is to be determined, the equivalent unavailability would be 0.33% (0.3 * 1.1).  Using the equivalent unavailability, the ITU rain model can be used to find the corresponding ‘equivalent rain margin.’  That is, the ITU model can be used to find the amount of attenuation associated with the increased outage time.  This change in attenuation is attributed to interference from the terrestrial system.

The C/I for the terrestrial system can now be found by modifying the methodology used to determine the satellite link budget (carrier-to-noise plus interference ratio).  The terrestrial system is factored into the link budget by adding a term representing its C/I.  By using the equivalent rain margin in the link budget, we find an ‘equivalent link margin.’  We can then find the C/I of the terrestrial system that causes the reduction of the equivalent link margin to zero.  This is the minimum C/I that the terrestrial system must maintain to cause no more than the amount of additional outage time chosen.

It is important to note that the above methodology results in the rainy-sky C/I for the terrestrial service interference, which would produce the additional outage time at the DBS earth station.  The reason for calculating the rainy-sky C/I is based on the assumption that in a typical satellite path, rain cells in the space-to-earth slant path are generally to the south of the earth station location.  Because the terrestrial interfering path generally emanates from the north of the DBS earth station location, it will usually not be in the rain cell.  Thus, at the time when a rain cell in the space-to-earth path attenuates a DBS signal, the terrestrial signal will not similarly be attenuated.  Therefore, the calculated C/I is performed by not fading the terrestrial signal with rain.

Table B-2 provides an example of the process described above.

Table B-1:  Required Parameters for the Determination of DBS Link Rain Margin and Satellite Link Availability and Unavailability

Input Parameters:

- Satellite longitude;

- Earth station location (latitude and longitude);

- Earth station altitude above mean sea level (AMSL);

- Satellite E.I.R.P. in the direction of the DBS earth station;

- The operating frequency;

- The required operating threshold for the DBS earth station receiver;

- Receiver noise bandwidth;

- Earth station antenna diameter;

- Earth station antenna pointing loss towards the DBS satellite;

- Clear-sky earth station system noise temperature;

- Atmospheric absorption;

- Carrier-to-interference ratio from other assignments in the BSS plan;

- Clear-sky feeder link carrier-to-interference ratio;

- Boltzman’s constant.

Calculation method:

- Calculate the distance and elevation angle between satellite and earth station using the satellite longitude (1) and the earth station location (2).

- Calculate the free space transmission loss using the distance (A) and the operating frequency (5).

- Calculate DBS antenna gain using the operating frequency (5) and the earth station antenna diameter (8).

- Calculate the clear-sky G/T ratio using the antenna gain (C) and the clear-sky earth station system noise temperature (10).

- Calculate the clear-sky carrier-to-noise ratio using the E.I.R.P. (4), free space transmission loss (B), earth station antenna pointing loss (9), clear-sky G/T (D), receiver noise bandwidth (7), Boltzman’s constant (14) and atmospheric absorption (11).

- Calculate the clear-sky carrier-to-noise plus interference ratio using the clear-sky carrier-to-noise ratio (E), the carrier-to-interference ration from other assignments in the BSS plan (12), and the clear-sky feeder link carrier-to-interference ratio (13)

- Calculate the link and rain margins using the clear-sky carrier-to-noise plus interference ratio (F) and the operating threshold (6).

- Calculate the satellite link unavailability using ITU-R Recommendation P.618-6, the rain margin (G), earth station location (2), earth station elevation angle (A), AMSL (3), and operating frequency (5).

- Determine the acceptable increase in unavailability due to terrestrial service interference and calculate equivalent unavailability of the satellite by adding the satellite link unavailability (H) and the increase in unavailability due to terrestrial interference.

- Determine the equivalent rain margin using the equivalent unavailability (I) and ITU-R Recommendation P.618-6.

- Determine the C/I for the terrestrial interference using the equivalent rain margin (J) in the step (G) calculation.

| Table B-2: An Example of A Satellite Downlink Power Budget, Rain Margin, Unavailability and Carrier-to-Interference Ratio |
| --- |
| A. Inputs |
| Satellite longitude | Degrees | 119.0 |
| Earth station latitude and longitude (lat/long) | Degrees | 38.90/77.01 |
| Earth station altitude above mean sea level | Km | 0.01 |
| Satellite e.i.r.p. in the direction of the DBS earth station | DBW | 52.6 |
| Operating frequency | GHz | 12.45 |
| Required operating threshold | DB | 6.1 |
| Receiver noise bandwidth | MHz | 24.0 |
| Earth station antenna diameter | M | 0.45 |
| Earth station antenna pointing loss towards the satellite | DB | 0.5 |
| Clear-sky earth station antenna system noise temperature | Kelvin | 85.0 |
| Atmospheric absorption | DB | 0.2 |
| C/I for other assignments in the BSS Plan | DB | 20.0 |
| Clear-sky feeder link C/(N+I) | DB | 26.2 |
| Boltzman’s constant | DB | 228.6 |
| B. Calculate |
| Distance from GSO satellite to earth station | Km | 38,825 |
| Earth station antenna elevation angle | Degrees | 27.6 |
| Free space path loss | DB | 206.1 |
| Earth station antenna gain | DBi | 33.83 |
| Clear-sky earth station antenna G/T | DB | 14.5 |
| Clear-sky carrier-to-thermal noise ratio | DB | 15.1 |
| Clear-sky carrier-to-thermal noise plus interference ratio | DB | 13.6 |
| Clear-sky link margin | DB | 7.5 |
| Rain margin | DB | 4.09 |
| Satellite link unavailability due to rain | % | 0.0647 |
| Calculated satellite link availability | % | 99.9353 |
| Acceptable increase in unavailability due to terrestrial service interference | % | 2.86 |
| Equivalent unavailability due to rain and terrestrial interference | % | 0.0665 |
| Equivalent rain margin | DB | 4.03 |
| Rainy sky C/I for the terrestrial service interference | DB | 22.6 |

APPENDIX J: UNAVAILABILITY STATISTICS FOR INCREASES IN DBS OUTAGES OF 2.86%, 60 MINUTES, AND 30 MINUTES ANNUALLY (45 cm antenna)

| Unavailability Statistics for DIRECTV Satellite at 101o W.L for Top Markets (Statistics computed using inputs as listed in Appendix G and the method described in Appendix H) |
| --- |
| Market | Average Yearly Statistics | Increased Outage = 2.86% | Increased Minutes of Outage = 60 min. | Increased Minutes of Outage = 30 Min. |
|  | Percentage of Availability | Minutes of Outage | Percentage of Availability | Minutes of Outage | Increased Minutes of Outage | Change in Percentage of Availability | Change in Percentage of Availability = 0.0114 % | Change in Percentage of Availability = 0.0057 % |
|  |  |  |  |  |  |  | Percentage of Availability | Minutes of Outage | Percentage of Availability | Minutes of Outage |
| New York | 99.9498 | 264.02 | 99.9484 | 271.58 | 7.55 | 0.0014 | 99.9384 | 324.02 | 99.9441 | 294.02 |
| Los Angeles | 99.9639 | 189.87 | 99.9629 | 195.30 | 5.43 | 0.0010 | 99.9525 | 249.87 | 99.9582 | 219.87 |
| Chicago | 99.9618 | 200.91 | 99.9607 | 206.66 | 5.75 | 0.0011 | 99.9504 | 260.91 | 99.9561 | 230.91 |
| Philadelphia | 99.9604 | 208.27 | 99.9593 | 214.23 | 5.96 | 0.0011 | 99.9490 | 268.27 | 99.9547 | 238.27 |
| San Francisco | 99.9313 | 361.32 | 99.9293 | 371.66 | 10.33 | 0.0020 | 99.9199 | 421.32 | 99.9256 | 391.32 |
| Boston | 99.9586 | 217.74 | 99.9574 | 223.97 | 6.23 | 0.0012 | 99.9472 | 277.74 | 99.9529 | 247.74 |
| Washington, DC | 99.9614 | 203.02 | 99.9603 | 208.82 | 5.81 | 0.0011 | 99.9500 | 263.02 | 99.9557 | 233.02 |
| Dallas | 99.8567 | 753.68 | 99.8526 | 775.24 | 21.56 | 0.0041 | 99.8453 | 813.68 | 99.8510 | 783.68 |
| Detroit | 99.9477 | 275.07 | 99.9462 | 282.94 | 7.87 | 0.0015 | 99.9363 | 335.07 | 99.9420 | 305.07 |
| Atlanta | 99.9701 | 157.26 | 99.9692 | 161.76 | 4.50 | 0.0009 | 99.9587 | 217.26 | 99.9644 | 187.26 |
| Houston | 99.8177 | 958.80 | 99.8125 | 986.22 | 27.42 | 0.0052 | 99.8063 | 1018.80 | 99.8120 | 988.80 |
| Seattle | 99.8749 | 657.96 | 99.8713 | 676.78 | 18.82 | 0.0036 | 99.8635 | 717.96 | 99.8692 | 687.96 |
| Cleveland | 99.9355 | 339.23 | 99.9337 | 348.94 | 9.70 | 0.0018 | 99.9241 | 399.23 | 99.9298 | 369.23 |
| Minneapolis | 99.9476 | 275.60 | 99.9461 | 283.48 | 7.88 | 0.0015 | 99.9362 | 335.60 | 99.9419 | 305.60 |
| Tampa | 99.9035 | 507.54 | 99.9007 | 522.05 | 14.52 | 0.0028 | 99.8921 | 567.54 | 99.8978 | 537.54 |
| Miami | 99.8812 | 624.82 | 99.8778 | 642.69 | 17.87 | 0.0034 | 99.8698 | 684.82 | 99.8755 | 654.82 |
| Phoenix | 99.9301 | 367.64 | 99.9281 | 378.15 | 10.51 | 0.0020 | 99.9187 | 427.64 | 99.9244 | 397.64 |
| Denver | 99.9854 | 76.79 | 99.9850 | 78.98 | 2.20 | 0.0004 | 99.9740 | 136.79 | 99.9797 | 106.79 |
| Pittsburgh | 99.9576 | 223.00 | 99.9564 | 229.38 | 6.38 | 0.0012 | 99.9462 | 283.00 | 99.9519 | 253.00 |
| Sacramento | 99.9190 | 426.02 | 99.9167 | 438.20 | 12.18 | 0.0023 | 99.9076 | 486.02 | 99.9133 | 456.02 |
| St. Louis | 99.9593 | 214.06 | 99.9581 | 220.18 | 6.12 | 0.0012 | 99.9479 | 274.06 | 99.9536 | 244.06 |
| Orlando | 99.8995 | 528.58 | 99.8966 | 543.69 | 15.12 | 0.0029 | 99.8881 | 588.58 | 99.8938 | 558.58 |
| Portland | 99.9037 | 506.49 | 99.9009 | 520.97 | 14.49 | 0.0028 | 99.8923 | 566.49 | 99.8980 | 536.49 |
| Indianapolis | 99.9475 | 276.12 | 99.9460 | 284.02 | 7.90 | 0.0015 | 99.9361 | 336.12 | 99.9418 | 306.12 |
| San Diego | 99.9773 | 119.39 | 99.9767 | 122.80 | 3.41 | 0.0006 | 99.9659 | 179.39 | 99.9716 | 149.39 |
| Charlotte | 99.9632 | 193.55 | 99.9621 | 199.08 | 5.54 | 0.0011 | 99.9518 | 253.55 | 99.9575 | 223.55 |
| Cincinnati | 99.9442 | 293.48 | 99.9426 | 301.87 | 8.39 | 0.0016 | 99.9328 | 353.48 | 99.9385 | 323.48 |
| Kansas City | 99.9644 | 187.24 | 99.9634 | 192.59 | 5.35 | 0.0010 | 99.9530 | 247.24 | 99.9587 | 217.24 |
| Milwaukee | 99.9462 | 282.96 | 99.9447 | 291.05 | 8.09 | 0.0015 | 99.9348 | 342.96 | 99.9405 | 312.96 |
| Nashville | 99.9656 | 180.93 | 99.9646 | 186.10 | 5.17 | 0.0010 | 99.9542 | 240.93 | 99.9599 | 210.93 |
| Columbus | 99.9644 | 187.24 | 99.9634 | 192.59 | 5.35 | 0.0010 | 99.9530 | 247.24 | 99.9587 | 217.24 |
| Greenville | 99.9505 | 260.34 | 99.9491 | 267.79 | 7.45 | 0.0014 | 99.9391 | 320.34 | 99.9448 | 290.34 |
| Unavailability Statistics for EchoStar Satellite at 119o W.L for Top Markets (Statistics computed using inputs as listed in Appendix G and the method described in Appendix H) |
| Market | Average Yearly Statistics | Increased Outage = 2.86% | Increased Minutes of Outage = 60 Min. | Increased Minutes of Outage = 30 Min. |
|  | Percentage of Availability | Minutes of Outage | Percentage of Availability | Minutes of Outage | Increased Minutes of Outage | Change in Percentage of Availability | Change in Percentage of Availability = 0.0114 % | Change in Percentage of Availability = 0.0057 % |
|  |  |  |  |  |  |  | Percentage of Availability | Minutes of Outage | Percentage of Availability | Minutes of Outage |
| New York | 99.9546 | 238.78 | 99.9533 | 245.61 | 6.83 | 0.0013 | 99.9432 | 298.78 | 99.9489 | 268.78 |
| Los Angeles | 99.9063 | 492.81 | 99.9036 | 506.91 | 14.09 | 0.0027 | 99.8949 | 552.81 | 99.9006 | 522.81 |
| Chicago | 99.9291 | 372.90 | 99.9271 | 383.56 | 10.66 | 0.0020 | 99.9177 | 432.90 | 99.9234 | 402.90 |
| Philadelphia | 99.9501 | 262.45 | 99.9487 | 269.95 | 7.51 | 0.0014 | 99.9387 | 322.45 | 99.9444 | 292.45 |
| San Francisco | 99.8328 | 879.38 | 99.8280 | 904.53 | 25.15 | 0.0048 | 99.8214 | 939.38 | 99.8271 | 909.38 |
| Boston | 99.9446 | 291.37 | 99.9430 | 299.71 | 8.33 | 0.0016 | 99.9332 | 351.37 | 99.9389 | 321.37 |
| Washington, DC | 99.9353 | 340.29 | 99.9334 | 350.02 | 9.73 | 0.0019 | 99.9239 | 400.29 | 99.9296 | 370.29 |
| Dallas | 99.7470 | 1330.64 | 99.7398 | 1368.70 | 38.06 | 0.0072 | 99.7356 | 1390.64 | 99.7413 | 1360.64 |
| Detroit | 99.9457 | 285.59 | 99.9441 | 293.76 | 8.17 | 0.0016 | 99.9343 | 345.59 | 99.9400 | 315.59 |
| Atlanta | 99.8917 | 569.60 | 99.8886 | 585.89 | 16.29 | 0.0031 | 99.8803 | 629.60 | 99.8860 | 599.60 |
| Houston | 99.6844 | 1659.88 | 99.6754 | 1707.36 | 47.47 | 0.0090 | 99.6730 | 1719.88 | 99.6787 | 1689.88 |
| Seattle | 99.6858 | 1652.52 | 99.6768 | 1699.78 | 47.26 | 0.0090 | 99.6744 | 1712.52 | 99.6801 | 1682.52 |
| Cleveland | 99.9321 | 357.12 | 99.9302 | 367.33 | 10.21 | 0.0019 | 99.9207 | 417.12 | 99.9264 | 387.12 |
| Minneapolis | 99.9304 | 366.06 | 99.9284 | 376.53 | 10.47 | 0.0020 | 99.9190 | 426.06 | 99.9247 | 396.06 |
| Tampa | 99.8180 | 957.22 | 99.8128 | 984.60 | 27.38 | 0.0052 | 99.8066 | 1017.22 | 99.8123 | 987.22 |
| Miami | 99.7721 | 1198.63 | 99.7656 | 1232.91 | 34.28 | 0.0065 | 99.7607 | 1258.63 | 99.7664 | 1228.63 |
| Phoenix | 99.8115 | 991.41 | 99.8061 | 1019.76 | 28.35 | 0.0054 | 99.8001 | 1051.41 | 99.8058 | 1021.41 |
| Denver | 99.9715 | 149.89 | 99.9707 | 154.18 | 4.29 | 0.0008 | 99.9601 | 209.89 | 99.9658 | 179.89 |
| Pittsburgh | 99.9524 | 250.35 | 99.9510 | 257.51 | 7.16 | 0.0014 | 99.9410 | 310.35 | 99.9467 | 280.35 |
| Sacramento | 99.8052 | 1024.54 | 99.7996 | 1053.84 | 29.30 | 0.0056 | 99.7938 | 1084.54 | 99.7995 | 1054.54 |
| St. Louis | 99.8340 | 873.07 | 99.8293 | 898.04 | 24.97 | 0.0047 | 99.8226 | 933.07 | 99.8283 | 903.07 |
| Orlando | 99.8073 | 1013.50 | 99.8018 | 1042.48 | 28.99 | 0.0055 | 99.7959 | 1073.50 | 99.8016 | 1043.50 |
| Portland | 99.8567 | 753.68 | 99.8526 | 775.24 | 21.56 | 0.0041 | 99.8453 | 813.68 | 99.8510 | 783.68 |
| Indianapolis | 99.8910 | 573.28 | 99.8879 | 589.68 | 16.40 | 0.0031 | 99.8796 | 633.28 | 99.8853 | 603.28 |
| San Diego | 99.9382 | 325.03 | 99.9364 | 334.33 | 9.30 | 0.0018 | 99.9268 | 385.03 | 99.9325 | 355.03 |
| Charlotte | 99.9220 | 410.24 | 99.9198 | 421.97 | 11.73 | 0.0022 | 99.9106 | 470.24 | 99.9163 | 440.24 |
| Cincinnati | 99.9182 | 430.22 | 99.9159 | 442.53 | 12.30 | 0.0023 | 99.9068 | 490.22 | 99.9125 | 460.22 |
| Kansas City | 99.9056 | 496.49 | 99.9029 | 510.69 | 14.20 | 0.0027 | 99.8942 | 556.49 | 99.8999 | 526.49 |
| Milwaukee | 99.9239 | 400.24 | 99.9217 | 411.69 | 11.45 | 0.0022 | 99.9125 | 460.24 | 99.9182 | 430.24 |
| Nashville | 99.9328 | 353.44 | 99.9309 | 363.54 | 10.11 | 0.0019 | 99.9214 | 413.44 | 99.9271 | 383.44 |
| Columbus | 99.9237 | 401.30 | 99.9215 | 412.77 | 11.48 | 0.0022 | 99.9123 | 461.30 | 99.9180 | 431.30 |
| Greenville | 99.9000 | 525.95 | 99.8971 | 540.99 | 15.04 | 0.0029 | 99.8886 | 585.95 | 99.8943 | 555.95 |

# Footnotes

A method for converting annual statistics to worst-month statistics is contained in Recommendation ITU-R P.841-1, Conversion Of Annual Statistics To Worst-Month Statistics.

In this analysis, we omitted the uplink (earth-to-space) outage contribution.