4910.1

INDEX

A

Section   Page

Abbreviations --------------------------------------   Appendix B

Accepted Engineering Practice

Standards ----------------------------------------   Appendix E

Access

Building and Nondwelling

Facilities------------------------------------   204-2     2-4

Living Unit Doors-------------------------------   402-1.1   4-3

Streets-----------------------------------------   204-1     2-4

Acceptability

General-----------------------------------------   200       2-3

Materials---------------------------------------   500-1     5-3

Aluminum

Doors-------------------------------------------   508-2.2   5-4

Windows-----------------------------------------   508-4.3   5-5

Application of Standards----------------------------   100       1-3

Attic

Ventilation-------------------------------------   403-1     4-5

B

Base Course, Material

Concrete Slab-----------------------------------   603-1.2   6-4

Bathrooms

Central-----------------------------------------   100-2.4   1-5

1-6

Building Design

Access and Circulation--------------------------   402       4-3

Baths-------------------------------------------   401-2     4-3

Elevators---------------------------------------   402-3     4-4

Ventilation-------------------------------------   403       4-5

1994

_____________________________________________________________________

4910.1

C

Section   Page

Cabinets, Kitchen

Construction and Materials----------------------   611-1     6-13

Carpeting-------------------------------------------   609-5.2   6-13

Carpets & Mats--------------------------------------   509-4     5-9

Caulking & Sealants---------------------------------   507-2     5-3

Ceramic Tile, Installation

Floors------------------------------------------   609-1     6-8

Circulation and Access------------------------------   402       4-3

Codes, Local----------------------------------------   102       1-12

Compliance with---------------------------------   102-1.1   1-12

Partially Accepted------------------------------   Appendix J

Standards, As-----------------------------------   102-1     1-12

Community Sewage Disposal System--------------------   615-3     6-16

Concrete

Exterior Slabs----------------------------------   603-2     6-4

Interior Slabs----------------------------------   603-1     6-4

Corrosion Protection--------------------------------   602-1.1   6-3

Crawl Space Ventilation-----------------------------   403-1     4-5

D

Decay Protection------------------------------------   606-2     6-5

Definitions-----------------------------------------   Appendix A

Dietitian's Office----------------------------------   100-2.4   1-4

Dining Areas

Central-----------------------------------------   100-2.4   1-5

Doors

Aluminum----------------------------------------   508-2.2   5-4

Exterior----------------------------------------   608-2     6-7

Flashing----------------------------------------   607-2     6-6

Installation------------------------------------   608-2     6-7

Labeling----------------------------------------   508-2.2   5-4

Locks-------------------------------------------   402-1.2   4-4

Materials for Doors & Windows-------------------   508       5-3

Metal Doors & Frames----------------------------   508-2     5-4

Performance Testing-----------------------------   508-1     5-3

Sizes-------------------------------------------   402-1.1   4-3

Wood--------------------------------------------   508-3     5-4

Drainage

Grading Design----------------------------------   306       3-4

Surface-----------------------------------------   602-2.2   6-3

1994

_____________________________________________________________________

4910.1

E

Section   Page

Elderly, Housing for

Accessibility of Bed----------------------------   100-2.5   1-6

Bathrooms---------------------------------------   100-2.6   1-6

Central Bathing---------------------------------   100-2.4   1-5

Central Dining----------------------------------   100-2.4   1-5

Central Kitchen---------------------------------   100-2.4   1-5

Combined Spaces, Furnishability-----------------   100-2.5   1-6

Community Social Rooms--------------------------   100-2.3   1-4

Dietitian's Office------------------------------   100-2.4   1-4

Elevators---------------------------------------   100-2.9   1-7

Emergency Call System---------------------------   100-2.20  1-9

Emergency Lighting------------------------------   100-2.10  1-7

First Aid Room----------------------------------   100-2.4   1-4

Flame Spread Ratings----------------------------   100-2.11  1-7

Floors------------------------------------------   100-2.13  1-7

Hall--------------------------------------------   100-2.7   1-6

Handrails, Exterior-----------------------------   100-2.1   1-3

Heating Design Temperature----------------------   100-2.14  1-8

Heating System----------------------------------   100-2.15  1-8

Medical Facilities------------------------------   100-2.4   1-5

Night Light Outlet------------------------------   100-2.19  1-9

Nursing Facilities------------------------------   100-2.4   1-4

Occupational Therapy----------------------------   100-2.4   1-4

Optional Project Facilities---------------------   100-2.4   1-4

Stairs------------------------------------------   100-2.8   1-7

Values, Nonscald--------------------------------   100-2.17  1-8

Walks-------------------------------------------   100-2.2   1-4

Wall Finishes-----------------------------------   100-2.12  1-7

Water Heating, Quantity-------------------------   100-2.18  1-8

Water, Hot and Cold-----------------------------   100-2.16  1-8

Elevators---------------------------------------   402-3     4-4

Required Service--------------------------------   402-3.1   4-4

Size--------------------------------------------   614-1     6-15

Existing Construction-------------------------------   100-5     1-10

Exterior Painting (See Painting)

Exterior Walls

Materials---------------------------------------   509-1     5-6

1994

_____________________________________________________________________

4910.1

F

Section   Page

Finish Materials

Exterior Walls----------------------------------   509-1     5-6

Flooring, Rigid---------------------------------   509-2     5-6

Flooring, Resilient-----------------------------   509-3     5-7

Painting----------------------------------------   509-5     5-9

Flashing--------------------------------------------   607-2     6-6

Flood Hazard Exposure-------------------------------   Appendix K

Flooring, Installation

Carpeting---------------------------------------   609-5.2   6-13

Resilient---------------------------------------   609-2     6-8

Rigid-------------------------------------------   609-1     6-8

Flooring Materials

Ceramic Tile------------------------------------   509-2     5-6

Resilient---------------------------------------   509-3     5-7

Rigid-------------------------------------------   509-2     5-6

G

General Acceptability-------------------------------   200       2-3

General Site Design

Design Quality----------------------------------   300-1     3-3

Glass and Glazing

Installation Standards--------------------------   608-4     6-8

Grading Design--------------------------------------   306       3-4

Ground Water----------------------------------------   301-2     3-3

Gutters---------------------------------------------   607-3     6-6

H

Disabled People, Accessibility to

Elevators---------------------------------------   100-2.9   1-7

Emergency Call System---------------------------   100-2.20  1-9

Emergency Exit Lighting-------------------------   100-2.10  1-7

General-----------------------------------------   100-3     1-9

Technical Standards-----------------------------   102-1     1-12

Variation Procedures----------------------------   101-3     1-11

Handrails and Railings------------------------------   402-2     4-4

Hardware, Door--------------------------------------   508-6     5-5

High Pressure Laminated Plastic---------------------   611-1.2   6-14

1994

_____________________________________________________________________

4910.1

Section   Page

I

Insulation, Thermal (Building)

Construction------------------------------------   607-1.1   6-5

Materials---------------------------------------   507-1     5-3

K

Kitchen

Cabinets----------------------------------------   611-1     6-13

Central-----------------------------------------   100-2.4   1-5

L

Land Use

Noise Control-----------------------------------   302-2     3-3

Local Codes and Regulations-------------------------   102       1-12

Lots, Yards, Setbacks

Building Parking Setback------------------------   303-2     3-4

M

Modular or Panelized Housing------------------------   613-1     6-15

Materials

Bulletins, Use of Material----------------------   Appendix F

New---------------------------------------------   101-1     1-11

Special Conditions------------------------------   101-2     1-11

Special Construction Materials------------------   513       5-9

Standards---------------------------------------   Appendix C

Medical Facilities----------------------------------   100-2.4   1-5

Metric Conversion-----------------------------------   Appendix G

Minimum Property Standards,

Application-------------------------------------   100       1-3

N

Natural Topography----------------------------------   301-1     3-3

Noise Control---------------------------------------   302-2     3-3

Nursing Facilities----------------------------------   100-2.4   1-4

1994

_____________________________________________________________________

4910.1

O

Section   Page

Occupational and Physical Therapy-------------------   100-2.4   1-4

P

Painting

Application-------------------------------------   609-3     6-9

Exterior Masonry--------------------------------   609-3.3   6-10

Exterior Metal----------------------------------   609-3.4   6-11

Exterior Wood-----------------------------------   609-3.2   6-9

Interior Floors---------------------------------   609-3.5   6-12

Interior Metal----------------------------------   609-3.7   6-12

Interior Wood-----------------------------------   609-3.5   6-11

Interior Plaster

and Gypsum Wallboard--------------------------   609-3.6   6-12

Lead Content------------------------------------   509-5     5-9

Materials---------------------------------------   509-5     5-9

Parking Areas---------------------------------------   304       3-4

Piping

Special Piping Systems--------------------------   615-1     6-15

Proposed Site---------------------------------------   301       3-3

Protection Against Decay----------------------------   606-2     6-5

Public Walks----------------------------------------   305       3-4

R

Railings--------------------------------------------   402-2     4-4

Real Estate Entity----------------------------------   201       2-3

Reference Sources-----------------------------------   Appendix H

Regulations, Local----------------------------------   102       1-12

Rehabilitation Construction-------------------------   100-5     1-10

Resilient Flooring

Installation------------------------------------   609-2     6-8

Materials---------------------------------------   509-3     5-7

Roads and Walks-------------------------------------   602-2     6-3

Rules for Multifamily and Care-Type

Housing, 24 C.F.R. 200.925a-c-------------------   Appendix I

Rules for One and Two Family

Dwellings, 24 C.F.R 200.926---------------------   Appendix K

1994

_____________________________________________________________________

4910.1

S

Section   Page

Screening-------------------------------------------   608-3.3   6-8

Sealants--------------------------------------------   507-2     5-3

Sewage Disposal Systems

Construction------------------------------------   615-3     6-16

Shakes

Material----------------------------------------   509-1     5-6

Site

Access------------------------------------------   204       2-4

Conditions--------------------------------------   203       2-3

Conditions, Unforeseen--------------------------   203-2     2-4

Design------------------------------------------   300       3-3

Hazards-----------------------------------------   203       2-3

Proposed Site-----------------------------------   301       3-3

Roads and Walks---------------------------------   602-2     6-3

Topography--------------------------------------   301-1     3-3

Underground Utilities---------------------------   602-1     6-3

Water, Ground-----------------------------------   301-2     3-3

Slab, Concrete

Exterior----------------------------------------   603-2     6-4

Interior----------------------------------------   603-1     6-4

Slope,

Grading-----------------------------------------   306       3-4

Social and Community Rooms--------------------------   100-2.3   1-4

Space Planning--------------------------------------   401       4-3

Baths-------------------------------------------   401-2     4-3

Non-Residential---------------------------------   401-1     4-3

Special Construction--------------------------------   613       6-15

Special Construction Materials----------------------   513       5-9

Standards

Application-------------------------------------   100.1     1-3

Building Access---------------------------------   204.2     2-4

Existing Construction---------------------------   100-5     1-10

Local Codes and Regulations---------------------   102       1-12

Nonresidential Use------------------------------   401-1     4-3

Property Access---------------------------------   204-1     2-4

Proposed Construction---------------------------   100-5     1-13

Real Estate Entry-------------------------------   201       2-3

Referenced--------------------------------------   103       1-13

Rehabilitation----------------------------------   100-5     1-10

Variations--------------------------------------   101       1-11

Swimming Pools--------------------------------------   613-2     6-15

1994

_____________________________________________________________________

4910.1

T

Section   Page

Termite Protection----------------------------------   606-1     6-4

Test Procedures and Performance---------------------   Appendix D

Thermal and Moisture Protection---------------------   507       5-3

"    "     "         "     ---------------------   607       6-5

Caulking and Joint Sealants---------------------   507-2     5-3

Insulation--------------------------------------   507-1     5-3

Tile

Resilient Floor---------------------------------   609-2     6-8

Rigid Floor-------------------------------------   609-1     6-8

Topography

Natural-----------------------------------------   301-1     3-3

Treated Lumber

Termite Protection------------------------------   606-1     6-4

Trespass--------------------------------------------   202-1     2-3

U

Utilities

Independent-------------------------------------   202-2     2-3

V

Vapor Retarders (Barriers)

Attic-------------------------------------------   403-1     4-5

Concrete Slabs----------------------------------   603-1.2   6-4

Crawl Space-------------------------------------   403-1     4-5

Variations, Standards-------------------------------   101       1-11

Procedures--------------------------------------   101-3     1-11

Ventilation-----------------------------------------   403       4-5

W

Walks-----------------------------------------------   305       3-4

Wall Coverings

Installation------------------------------------   609-4     6-13

Wall Finishes

Elderly Housing---------------------------------   100-2.12  1-7

Exterior----------------------------------------   509-1     5-6

Interior----------------------------------------   609-3.6   6-12

1994

_____________________________________________________________________

4910.1

Section   Page

Water Supply Systems

Construction------------------------------------   615-2     6-16

Windows---------------------------------------------   508-4     5-4

Aluminum----------------------------------------   508-4.3   5-5

Installation------------------------------------   608-3     6-8

Metal-------------------------------------------   508-4     5-4

Screens-----------------------------------------   608-3.3   6-8

Steel-------------------------------------------   508-4.2   5-5

Wood--------------------------------------------   508-5     5-5

Wood Construction-----------------------------------   606-3     6-5

Y

Yard Space

Building Parking--------------------------------   303-2     3-4

General-----------------------------------------   300       3-3

303-1     3-4

Parking-----------------------------------------   304       3-4

Walks-------------------------------------------   305       3-4

1994