ELT Checklist (L-Tronics) ELT Mission

Pinpointing

Sensitivity – Minimum Frequency – Turn from 121.5 to 121.6 then 121.7 (If you still have the signal you are very close) Crew – Transition into visual search

Signal Dropout

Observer – Record current Lat/Long Pilot – Continue on original heading Observer – Start watch Pilot – If signal not required after 3 min begin climbing turn to recorded Lat/Long, gain 1000ft MSL Crew – Continue on original heading Observer – Increase sensitivity slightly as needed if signal again fades

Cone of Silence (Similar to passing a VOR station)

Volume – Will be very loud as you approach station DF Needle – Will waiver Volume – Will drop but not go silent Strength – Will drop but not go silent Freq – Tune from 121.5 to 121.6 or 121.7 Crew – Transition to lower altitude