# WELL DECOMMISSIONING

## PRACTICE INTRODUCTION

USDA, Natural Resources Conservation Service―Practice Code 351

Photo courtesy of the Cass Soil and Water Conservation District, ND

### WELL DECOMMISSIONING

Well decommissioning is the sealing and permanent closure of water well no longer in use.

### PRACTICE INFORMATION

Well decommissioning applies to the sealing and closure of any drilled, dug, driven, bored, or otherwise constructed water well determined to have no further beneficial use.

This practice requires the removal of all pumping equipment, valves, pipelines, liners, debris, and other foreign material. The well casing should be removed if possible, but can be sealed and left in place. Once cleared, the well water is brought to a 100 parts per million chlorine concentration or other solution specified by local or State requirements. The well is sealed and plugged as allowable by ASTM D5299 and State regulations.

### COMMON ASSOCIATED PRACTICES

Well Decommissioning is used in a Conservation Management System with Critical Area Planting (342) and other conservation practices to enhance and protect water quality.

For further information, refer to the practice standard in the local Field Office Technical Guide and associated practice specifications and job sheets.

# Text boxes

I.5 (-) Risk of future regulatory compliance

I.1 (-) Liability

I.3 (+) Water available for other users

I.2 (+/-) Net return

Well Decommissioning

6/2008

I. 6 (-) Contaminants, pathogens, sediments to ground water

D.4 (-) On-farm available water supply

Well Decommissioning (351)

Note: Effects are qualified with a plus (+) or minus (-). These symbols indicate only an increase (+) or a decrease (-) in the effect upon the resource, not whether the effect is beneficial or adverse.

D.  Direct effect

(+) increase; (-) decrease

Pathway

C.  Cumulative effect

I.  Indirect effect

LEGEND

#.  Created by practice

D.2 (-) Maintenance costs

C.3 (+) Habitat suitability, health for humans, domestic and wild animals

I.4 (+) Meeting water quality standards

I.6 (+) Water quality

D.5 (-) Potential for ground water contamination

Start

Initial settings: A water well that is no longer used and is a potential source for ground water contamination

1. Removal of all pumps, pipes, casing, and material, plugging and backfill of well as allowed by local and State laws

I.7 (+) Quality of ground waters

C.2 (+) Quality of available water supply for domestic, agricultural and wildlife uses

C.1 (+) Income and income stability (individuals and community)

D.1 (+) Cost of materials and labor for installation

D.3 (-) Physical risk/ hazard to people, livestock, and wildlife