WG Phase Shifter

Main ideas:

- Better cooling

- Minimal fringe fields

- Low inductance

Copper side walls with water cooling

Copper plated stainless steel top and bottom

Water cooled windings for the first model– can be optimized later by adding permanent magnets.

Yoke Material  - Ni-Zn Ferrite (NM Inc) CMD-10

Amount of material: L = 20 cm, t = 20 mm, p = 100 cm

V = 4000 cm3 = 250 in3

W = 5 g/cm3 * 4000 cm3 = 20,000 g = 20 kg = 40 lbs

$$ = $2.00 1/in3 * 250 in3 = $500.00

Amount of material L = 150 mm, t = 20 mm, h = 40 mm

V = 120 cm3 x 2 = 240 cm3 = 15 in3

P = 240 cm3 x 5 g/cm3 = 1200 g = 1.2 kg = 2.5 lbs

$$ = ??????

Main design parameters

Current I = 2400/8 = 300 A

Current density j = 300A / 50 mm2 = 6 A/mm2

Coil resistance – R = 1.2 mOhm

Power dissipated in one coil – P = 110 W

Power for one PhSh – 440 W

Voltage for one PhSh – 1.5 V (all coils in series)

Inductance of a PhSh – 0.4 mH

Power for an IQ modulator – 900 W

Directions to go.

- Postulate frequency 				Now

- Choose waveguide height			1 week

- Design phase shifter including ferrite cooling, waveguide matching and magnetic circuit optimization		3 weeks

- YIG procurement					???

- Yoke material procurement			???

- Waveguide fabrication				6 weeks

- Find an appropriate power supply

- Assemble and tune PhSh				8 weeks

- High power test.					10 weeks

Totally 1 quarter

Region    1: shape code POLY, coordinates in MM

X           Y           CURV         N  BIAS F    V           DV

Side   1: corner   1 (105.0      ,0.0        ) to   2 (105.0      ,19.0       )

Side   2: corner   2 (105.0      ,19.0       ) to   3 (123.999    ,19.0       )

Side   3: corner   3 (123.999    ,19.0       ) to   4 (123.999    ,0.0        )

Side   4: corner   4 (123.999    ,0.0        ) to   1 (105.0      ,0.0        )

Region    2: shape code POLY, coordinates in MM

X           Y           CURV         N  BIAS F    V           DV

Side   1: corner   1 (0.0        ,40.0       ) to   2 (61.0       ,40.0       )

Side   2: corner   2 (61.0       ,40.0       ) to   3 (96.0       ,40.0       )

Side   3: corner   3 (96.0       ,40.0       ) to   4 (96.0       ,22.0       )

Side   4: corner   4 (96.0       ,22.0       ) to   5 (105.0      ,22.0       )

Side   5: corner   5 (105.0      ,22.0       ) to   6 (132.0      ,22.0       )

Side   6: corner   6 (132.0      ,22.0       ) to   7 (132.0      ,40.0       )

Side   7: corner   7 (132.0      ,40.0       ) to   8 (167.0      ,40.0       )

Side   8: corner   8 (167.0      ,40.0       ) to   9 (167.0      ,22.0       )

Side   9: corner   9 (167.0      ,22.0       ) to  10 (167.0      ,0.0        )

Side  10: corner  10 (167.0      ,0.0        ) to  11 (187.0      ,0.0        )

Side  11: corner  11 (187.0      ,0.0        ) to  12 (187.0      ,60.0       )

Side  12: corner  12 (187.0      ,60.0       ) to  13 (0.0        ,60.0       )

Side  13: corner  13 (0.0        ,60.0       ) to   1 (0.0        ,40.0       )

Region    3: shape code POLY, coordinates in MM

X           Y           CURV         N  BIAS F    V           DV

Side   1: corner   1 (61.0       ,40.0       ) to   2 (96.0       ,40.0       )

Side   2: corner   2 (96.0       ,40.0       ) to   3 (96.0       ,22.0       )

Side   3: corner   3 (96.0       ,22.0       ) to   4 (61.0       ,22.0       )

Side   4: corner   4 (61.0       ,22.0       ) to   1 (61.0       ,40.0       )

Region    4: shape code POLY, coordinates in MM

X           Y           CURV         N  BIAS F    V           DV

Side   1: corner   1 (167.0      ,40.0       ) to   2 (132.0      ,40.0       )

Side   2: corner   2 (132.0      ,40.0       ) to   3 (132.0      ,22.0       )

Side   3: corner   3 (132.0      ,22.0       ) to   4 (167.0      ,22.0       )

Side   4: corner   4 (167.0      ,22.0       ) to   1 (167.0      ,40.0       )

Region    3: MATE =  1         , PERM = 1.0        , DENS = -4.0

SIGM = 0.0        , PHAS = 0.0        , VELO = 0.0

N =   0        , SYMM = 0

Area of region = 630.0

Total current = -2520.0

Region    4: MATE =  1         , PERM = 1.0        , DENS = 4.0

SIGM = 0.0        , PHAS = 0.0        , VELO = 0.0

N =   0        , SYMM = 0

Area of region = 630.0

Total current = 2520.0

# Text boxes

An example of waveguide phase shifter.

- Simplicity

- Effective cooling

Magnetic field distribution in WG phase shifter

Bias =1800Oe

Bias = 600Oe

ANSYS simulation of temperature (degree C) distribution in phase shifter (quarter of geometry). Cooling water 20 C°.

Program used HFSS data of power losses density for bias 600Oe