1910.134(c)

Respiratory protection program. This paragraph requires the employer to develop and implement a written respiratory protection program with required worksite-specific procedures and elements for required respirator use. The program must be administered by a suitably trained program administrator. In addition, certain program elements may be required for voluntary use to prevent potential hazards associated with the use of the respirator. The Small Entity Compliance Guide contains criteria for the selection of a program administrator and a sample program that meets the requirements of this paragraph. Copies of the Small Entity Compliance Guide will be available on or about April 8, 1998 from the Occupational Safety and Health Administration's Office of Publications, Room N 3101, 200 Constitution Avenue, NW, Washington, DC, 20210 (202-219-4667).

1910.134(c)(2)(i)

An employer may provide respirators at the request of employees or permit employees to use their own respirators, if the employer determines that such respirator use will not in itself create a hazard. If the employer determines that any voluntary respirator use is permissible, the employer shall provide the respirator users with the information contained in Appendix D to this section ("Information for Employees Using Respirators When Not Required Under the Standard"); and

1910.134(c)(2)(ii)

In addition, the employer must establish and implement those elements of a written respiratory protection program necessary to ensure that any employee using a respirator voluntarily is medically able to use that respirator, and that the respirator is cleaned, stored, and maintained so that its use does not present a health hazard to the user. Exception: Employers are not required to include in a written respiratory protection program those employees whose only use of respirators involves the voluntary use of filtering facepieces (dust masks).

October 5, 1998

Mr. William R. Jaggi
Trans World Airlines, Inc.
Ground Operations Center
P.O. Box 10007
St. Louis, MO 63145

Dear Mr. Jaggi:

This is in response to your letter of March 31, addressed to Ms. Bonnie Friedman, in the Occupational Safety and Health Administration's (OSHA's) Office of Public Affairs. We apologize for the long delay of this response. Enforcement of this standard will begin on the compliance date, October 5, 1998.

In your letter, you requested clarification on several respiratory protection issues. There were several statements listed that you sought to determine if they were true or not. The statements are responded to in the same order as given in your letter.

Please note that in your letter, you used the term "medical surveillance." The respiratory protection standard 1910.134 uses the term "medical evaluation."

- Statement:  Use of the disposable paper type dust respirators does not require medical surveillance.

Response:  Non-voluntary use of a filtering facepiece (dust mask/disposable paper type dust respirator) requires that the employer establish and implement a written respiratory protection program with worksite-specific procedures. The respiratory protection program must include the medical evaluation of employees.

Voluntary use of a filtering facepiece respirator does not require medical evaluation. The employer needs only to ensure that the dust masks are not dirty or contaminated, that their use does not interfere with the employee's ability to work safety, and provide a copy of Appendix D to each voluntary wearer.

- Statement:  Use of an air supplied positive pressure face mask does not require medical surveillance unless intended for rescue or emergency purposes.

- Statement:  Use of an air supplied positive pressure hood does not require medical surveillance unless intended for rescue or emergency purposes.

Response:  The new respiratory protection standard, 29 CFR 1910.134, states, "The employer shall provide a medical evaluation to determine that the employee's ability to use a respirator, before the employee is fit tested or required to use the respirator in the workplace." Employees that use any respirators including respirators such as air supplied positive pressure face masks or hoods must have a medical evaluation before use. Medical evaluations are needed to prevent injuries and illnesses that can arise from respirator use. Clinical studies show that even positive pressure respirator use can harm an employee. Respirator use of all kinds can cause alterations in breathing patterns, hypoventilation, retention of carbon dioxide, and an increase in workload on the body.

Please note that on August 3, 1998, OSHA published Questions and Answers on the Respiratory Protection Standard. This 79 page document contains guidance and interpretations on the most frequently asked questions. The section on medical evaluations and the attachments may be particularly helpful in developing your respiratory protection program. This can be found on the Internet on the OSHA Home Page at http://www.osha.gov.

Should you require any additional information on this matter, please, feel free to contact our Office of Health Compliance Assistance at (202) 219-8036.

Sincerely,

Richard E. Fairfax
Acting Director
Directorate of Compliance Programs

March 8, 1999

Ms. Mary Kiester
System Safety Engineer
Landsat 7 Program
LMMS
230 Mall Boulevard
Room U2101
King of Prussia, PA 19406

Dear Ms. Kiester:

This is in response to your letter to the Occupational Safety and Health Administration (OSHA) dated November 16, 1998. We apologize for the long delay in getting this response to you. You requested that we provide you with a clarification of the requirement that a medical evaluation be provided to employees whose only respirator use would be the use of an escape-only respirator, used to escape from a building in the event of an emergency. These employees have been trained in the use of the five minute Emergency Life Support Apparatus (ELSA) escape only respirator.

OSHA's current policy states that the employer does not have to provide a medical evaluation for employees whose only respirator use would be the use of escape-only respirators. The ELSA is a NIOSH-approved escape-only respirator which provides less than 30 minutes of breathing air. Please note that the employer would still be responsible for compliance with all other provisions of the respirator standard, as applicable, such as the written program and training requirements. If the employer were to provide any other self-contained breathing apparatus (SCBA) which provides 30 minutes of breathing air and which would be used to enter potentially IDLH atmospheres, the employer would have to provide a medical evaluation in accordance with 1910.134(e).

We hope this addresses your concerns. Should you have further questions, please feel free to call OSHA's Office of Health Compliance Assistance at (202) 693-2190.

Sincerely,

Richard E. Fairfax
Director
Directorate of Compliance Programs

October 5, 1998

Mr. William R. Jaggi
Trans World Airlines, Inc.
Ground Operations Center
P.O. Box 10007
St. Louis, MO 63145

Dear Mr. Jaggi:

This is in response to your letter of March 31, addressed to Ms. Bonnie Friedman, in the Occupational Safety and Health Administration's (OSHA's) Office of Public Affairs. We apologize for the long delay of this response. Enforcement of this standard will begin on the compliance date, October 5, 1998.

In your letter, you requested clarification on several respiratory protection issues. There were several statements listed that you sought to determine if they were true or not. The statements are responded to in the same order as given in your letter.

Please note that in your letter, you used the term "medical surveillance." The respiratory protection standard 1910.134 uses the term "medical evaluation."

- Statement:  Use of the disposable paper type dust respirators does not require medical surveillance.

Response:  Non-voluntary use of a filtering facepiece (dust mask/disposable paper type dust respirator) requires that the employer establish and implement a written respiratory protection program with worksite-specific procedures. The respiratory protection program must include the medical evaluation of employees.

Voluntary use of a filtering facepiece respirator does not require medical evaluation. The employer needs only to ensure that the dust masks are not dirty or contaminated, that their use does not interfere with the employee's ability to work safety, and provide a copy of Appendix D to each voluntary wearer.

- Statement:  Use of an air supplied positive pressure face mask does not require medical surveillance unless intended for rescue or emergency purposes.

- Statement:  Use of an air supplied positive pressure hood does not require medical surveillance unless intended for rescue or emergency purposes.

Response:  The new respiratory protection standard, 29 CFR 1910.134, states, "The employer shall provide a medical evaluation to determine that the employee's ability to use a respirator, before the employee is fit tested or required to use the respirator in the workplace." Employees that use any respirators including respirators such as air supplied positive pressure face masks or hoods must have a medical evaluation before use. Medical evaluations are needed to prevent injuries and illnesses that can arise from respirator use. Clinical studies show that even positive pressure respirator use can harm an employee. Respirator use of all kinds can cause alterations in breathing patterns, hypoventilation, retention of carbon dioxide, and an increase in workload on the body.

Please note that on August 3, 1998, OSHA published Questions and Answers on the Respiratory Protection Standard. This 79 page document contains guidance and interpretations on the most frequently asked questions. The section on medical evaluations and the attachments may be particularly helpful in developing your respiratory protection program. This can be found on the Internet on the OSHA Home Page at http://www.osha.gov.

Should you require any additional information on this matter, please, feel free to contact our Office of Health Compliance Assistance at (202) 219-8036.

Sincerely,

Richard E. Fairfax
Acting Director
Directorate of Compliance Programs

CPL 2-0.120 - Inspection Procedures for the Respiratory Protection Standard

# VII  Inspection Guidelines for the Standard on Respiratory Protection, 29 CFR 1910.134. These guidelines relate to specific provisions of 29 CFR 1910.134 and are provided to assist compliance officers with conducting inspections where the standard may apply. Any subparagraphs of the standard not discussed in this Directive, should be enforced according to their terms.

  - Scope and Application

    - This new standard applies to all respirator usage in General Industry, Shipyards, Marine Terminals, Longshoring and Construction workplaces. It does not apply to agricultural operations or to occupational exposure to M. tuberculosis. Respiratory protection against tuberculosis will continue to be enforced under the old 1910.134, which has been redesignated 1910.139.

    - The standard covers respirator use where respirators are being worn to protect employees from exposure to air contaminants above an exposure limit or are otherwise necessary to protect employee health, where respirators are otherwise required to be worn by the employer, and where respirators are voluntarily worn by employees for comfort or other reasons.

- Respiratory Protection Program-1910.134(c)(1): A written respiratory protection program is required when necessary to protect the health of the employee from workplace contaminants or when the employer requires the use of respirators. A limited written program is also required when respirators (other than filtering facepieces) are being voluntarily worn by employees. The program must include workplace specific procedures and contain all applicable program elements. Where respirators are required, respirators (and their associated requirements such as fit-testing and maintenance), training and medical evaluations must be provided at no cost to the employee. It is the intent of the standard that the employer would not be required to incur any costs associated with voluntary use of filtering facepieces other than providing a copy of Appendix D to each user. If employers allow the voluntary use of respirators other than filtering facepieces, the costs associated with ensuring the respirator itself does not create a hazard, such as medical evaluations and maintenance must be provided at no cost to the employee.

2.  Citation Guidelines. If respirators are required to be worn in the workplace or respirators other than dust masks are worn by voluntary users, a written program is required. An overexposure is not required to cite this paragraph. If the CSHO determines that specific provisions are lacking or deficient in the written program, the CSHO should cite section (c)(1) with the specific element(s) that are missing. Discrepancies between the written program and implemented work practices at the worksite should be cited by the appropriate paragraph in the standard that requires the work practice. If overexposures are found and no program at all exists, paragraph (a)(2) should be cited.

3.  (c)(2) Voluntary Use: Normally, respirators that are voluntarily used by employees will be filtering facepieces (dust masks). NIOSH-approved respirators are strongly recommended, but they are not required for voluntary use. This voluntary use of dust masks alone does not require the employer to have a written program. For filtering facepiece respirator use, the employer needs only ensure that dust masks are not dirty or contaminated, that their use does not interfere with the employee's ability to work safely, and that a copy of Appendix D is provided to each voluntary wearer. Merely posting Appendix D is not considered adequate.  Use of elastomeric or supplied-air respirators, even when voluntary on the part of the employee, will require the employer to include all elements in a written program that will ensure use of these respirators does not create a hazard.

4.  Inspection Guidelines Even though employees may be voluntarily using respirators, adverse health conditions can be caused by the wearing of a respirator itself. Examples include, but are not limited to;

      - (1) an employee's health being jeopardized by the wearing of a respirator (e.g., employee has a cardiac and/or pulmonary disorder that could be aggravated by respirator use),

      - (2) the wearing of a dirty respirator that can cause dermatitis or ingestion of a hazardous chemical;

      - (3) the sharing of a respirator that leads to transmittal of disease.

Employees who voluntarily wear respirators must, at least, be given the information in Appendix D.