# Calculations for the Opening of Rough Port Pipe for  Pipe Thickness, Weld Size and

Reinforcement-Numi Decay Pipe Downstream End.

By:   Edward Chi – PPD/ME     03/31/2003

This edition superseded the edition dated on 05/28/2002

(For Chapter 3 only)

The main decay pipe:

P:   15 psi, external design pressure

Do: 78.75 in, outside dia. Of the decay pipe.

Di: 78 in, inside dia. Of the decay pipe.

t:    0.375 in, the nominal pipe wall thickness.

Fa: 13,800 psi, the max. allowable stress of the pipe material at the operating temp,

also know as Sv. (See Page 1-1).

Pipe material: SA 285, grade C, carbon steel.

Lv: Design length of the vessel section between lines of support (see Page UG-28(b)),

=81.875” (see Page 1-1)

Find out the reguired pipe shell thickness tr:

- Try tr1 = 0.35”

Lv/Do = 81.875”/78.75” = 1.04

Do/tr = 78.75/0.35 =225

From section UG-28, also Fig. G & Fig. CS-2 in Subpart 3 of section II, part D,

ASME VIII, Div I:

Find:

A = 0.0004

B = 5750

Pa1= (4B)/(3(Do/tr)) = 34.07 psi

Where:

A:  Factor determined from Fig. G.

B:  Factor determined from applicable material chart in Fig. CS-2

Pa: Max. allowable external working pressure, psi

- Try tr2 = 0.250”

Lv/Do = 1.04

Do/tr2 = 78.75/0.25 = 315

Find:

A = 0.00025

B = 3550

Pa2 = (4B/3(Do/tr2)) = 15.026 psi

So, tr = 0.250”

The rough prot pipe:

do: 6.625”, outside dia. Of the rough-port pipe.

di:  6.357”, inside dia . of the rough-port pipe.

tn:  0.134”, wall thickness  of the rough-port pipe.

trn: required thickness of a seamless nozzle wall.

L:  length of projection defining the thickness portion of integral reinforcement of a

nozzle neck beyond the outside surface of the vessel wall.

E:  29 x 106 psi, modulus of elasticity of the material at the opening temp.

Material: SA 312 304 stainless steel pipe, Fa = Sn = 16,700 psi at the operating temp.

-200  F to 2000 F (per talbe 1A, part D, Section II, ASME Boiler & Pressure

Vessel Code 1995, 1997 Addenda).

Reference drawings: MC-406148, MD-406870 & ME-406873

- Try:  L1 = 30 in, tr1 = 0.125 in, then:

L1/do = 30/6.625 = 4.5283

do/tr1 = 6.625/0.125 = 53

From Fig. G and Fig. HA-1 of subpart 3 of Sect. II, part D:

A = 0.00069

B = 7800

Pa = (4B)/(3(do/tr1)) = (4 x 7800)/(3 x 53) = 196 psi > P

- Try: L2 = 40 in, tr2 = 0.0625 in

L2/do = 6.0377

do/tr2 = 106

get:

A = 0.00021

B = 2800

Pa = (4B)/(3(do/tr2)) = (4 x 2800)/(3 x 106) = 35.22 psi > P

- Try: L3 = 40 in, tr3 = 0.045 in

L3/do = 6.0377

do/tr3 = 6.625/0.045 = 147

get:

A = 0.000115

Since the value of “A” falls to the left side of the curve of the Fig. HA-1, so:

Pa = 2AE/3(do/tr3) = (2 x 0.000115 x 29 x 106) / (3 x 147) = 15.12 psi

So: trn = tr3 = 0.045 in

Size of the weld required:

Per UG-37, UW-16 and Fig. UW-16.1(i) of ASME VIII, Div. I of 1998.

t1 = t2 = Not less than the smaller of ¼ in or 0.7 tmin

t1 = t2 = 0.134” x 0.7 = 0.094 in

t1 + t2 = 0.094 in + 0.094 in =0.188 in > 1.25 tmin = 0.1675 in

So, the weld size t1 = t2 = 0.094 in, the fillet size is about 0.13 in

Area of the reinforcement required Ar:

Per section UG-37(d)(1):

Ar = 0.5(dtrF + 2tntrF(1-fr1)

= 0.5 x (6.357” x 0.250” x 1.0 +2 x 0.134” x 0.250” x 1.0 x 0)

= 0.7946 in2

Where:

d:  Finished diameterof circle opening, see Fif. UG-37.1

F: Correction factor

Fr1: Sn/Sv, for nozzle wall inserted through the vessel wall.

(not greater than 1.0)

Area of reinforcement available Aa:

A1: Larger of the following (area available in shell):

= d(E1t – Ftr)-2tn(E1t – ftr) x (1-fr1)

= 6.357” x  (1 x 0.375” – 1.0 x 0.25”) – 0

= 0.7946 in2

or      = 2(t + tr)(E1t –Ftr)-2tn(E1t – Ftr) x (1-fr1)

= 2 (0.375” + 0.25”) x (1.0 x 0.375” – 1.0 x 0.25”) – 0

= 0.15625 in2

So pick A1 = 0.7946 in2

A2: Smaller of the following (area available in feedthru pipe projected outwards):

= 5 (tn-trn)tfr2

= 5 x (0.134 in – 0.045 in) x 0.375 in x 1.0

=  0.1669 in2

or     = 5 (tn-trn) fr2tn

= 5 x (0.134 in – 0.045 in) x 1.0 x 0.134 in

= 0.05963 in2

So pick A2 = 0.05963 in2

A3: Area available in inward nozzle, use the smallest value:

= 5ttifr2

= 5 x 0.375 in x 0.134” x 1.0

= 0.25125 in2

or  =5titifr2

= 5 x 0.134 in x 0.134 in x 1.0

= 0.08978 in2

or  = 5htifr2

= 5 x 0.94 in x 0.134 in x 1.0

= 0.6298 in2

So pick A3 = 0.08978 in2

where:

ti: Nominal thickness of the internal projection of the nozzle wall (see Fig. UG-37.1).

A41: Outward nozzle weld

= leg2 fr2

= 0.132 in2 x 1.0

=0.0169 in2

A43: Inward nozzle weld

= leg2 fr2

= 0.132 in2 x 1.0

= 0.0169 in2

Then:

Aa = A1 + A2 + A3 + A41 + A43

= (0.7946 + 0.05963 + 0.08978 + 0.0169 + 0.0169) in2

= 0.9778 in2 > Ar = 0.7946 in2

# Per Fig. UG-37.1, section UG-37, the opening is adequately reinforced under the current designated boundary conditions.