Fermi National Accelerator Laboratory

Technical Division

Engineering and Fabrication Department

P.O. Box 500, MS 314

Batavia, IL  60510

Phone: (630) 840-4622

Fax: (630) 840-8079

Fermilab

To:  USCMSEMU Cathode Strip Chamber ISR Team

From:  Nelson Chester, ISR Review Group Leader

Subject:  Results of the ISR Interim Readiness Review held on Thursday Morning, February 27, 2003

Conclusion:

As a result of this review, the reviewers believe that the ISR Team has a satisfactory understanding of the work that has to be done, and has the necessary skills and knowledge to perform all of the work in a safe, efficient, and accurate manner.   We believe that this Interim Review can serve as a Final Review without the need for additional future formal reviews.

Acknowledgements:

On behalf of the CMS EMU management and the ISR Review group, I want to thank you all for your excellent efforts and hard work to prepare for this review. You provided very complete and detailed information that describes the work you are doing in the ISR. You are to be congratulated on the accomplishments that you have made over the past many months to set up the ISR work area, and to test and store chambers and cables.  The database management system should supply valuable support for the day-to-day activities, as well as provide important information that will be very useful in the future.  We want you to know that your long hours of work are very much appreciated.  This hard work has produced excellent results and a high level of achievement for the CMS ISR activity.

We want to thank Peter for taking on the ISR Team Manager task and leading it successfully. We want to thank Richard Breedon for accepting the position as Deputy Manager for the CMS ISR activity, and believe can provide the valuable support to Peter. We also want to thank Armando Lanaro for acting as a Safety expert and consultant to the ISR group.  In addition we thank each of the ISR Team members for their cooperation with each other and with Peter.  Without this team effort we do not think that you could have accomplished all of the things you did.  We hope that this spirit will continue on in the future.

Lastly, I want to thank all the reviewers for their participation in the review and for their comments and recommendations.  Your support and helping hand to the ISR Team has been a major contributing factor to the success of the review. Special thanks are due to Vladislav Razmyslovitch for his help in preparing the ISR Review documentation and for providing stimulation to the ISR team members.  And I thank our Project Management Team for allowing me to be a part of the ISR effort and for being a part of carrying out their objectives for the success of CMS at CERN.

Recommendations:

The Review Team identified no major deficiencies in the configuration, setup, and operation of the ISR activities, but offers the following recommendations in order to acheive continued success:

- An individual should be identified who will periodically check all ISR shared equipment to insure that it remains in proper functioning condition for our needs.

- All documents prepared and displayed at the ISR review should be converted into working procedures and instructions that are kept in both books that are available to the ISR Team and on the ISR Web Page so that others may refer to them as needed.  Safety related requirements should be added to all procedures as required (see below).

- The documents in item #2 should be used along with “on-the-spot training” to train team members how to do various jobs efficiently, accurately, and safely.  The cross training of various individuals to do the same job is encouraged.

- The ISR team members described needed tools and equipment that were not fully in place or operational.  We encourage the team to obtain these needed items by the end of March.  Peter and Richard are asked to further explore alternate simple and efficient procurement methodologies that will allow the team to procure needed items easily without the difficulties of getting reimbursed.

- Peter and Richard are encouraged to refine the organization structure to eliminate to the extent possible the job overlap of many people doing many jobs, yet still preserving the cross training of individuals so that there is more than one trained person capable of doing any one job.  Particularly for repairs and alignment plate installation, personnel who are trained and capable of performing these operations should be identified.

- The Team members are reminded that when any repairs are made to the chambers or chamber components, or when parts are replaced, the details of the problems encountered and the details of the repairs or replacements made, should be documented for statistical analysis, archival purposes, and future reference.  A list of approved types of repairs with basic procedures has been provided to the ISR team.  The documentation should be submitted by systematic inclusion in the CMS ISR database as well as on the CMS ISR website.  The preferred method of communication and notification among individuals is by email.

- New or previously non-existent problems that are encountered along with proposals for fixing them should be presented to the Repair Committee for assessment and corrective action direction.  Communication should be in writing (email) and all correspondence containing problem identification, recommendations for correction, and the final results obtained should be kept in the database as well as on the website in a systematically consistent form that is easy to understandable and read.  If a problem or issue turns out to be recurring, then it should be added to the list of visual inspections or otherwise to the list of inspections or tests that are done on all chambers.  Updating of existing documentation should then follow and notification should be made to all concerned.

- Safety precautions, instructions, inspections, and other elements related to the health of all personnel and the safety of personnel and equipment should be documented on the website as well as included in the operating procedures and instructions.

- A number of repair and special procedures to be performed on chambers (e.g. alignment plate installation) have already been identified as being needed on some or all chambers.  Descriptions of where and how these repair and special operations are to be performed should be written and maintained in books available to the ISR Team, as well as placed on the Web and in the Database.  The descriptions should define the tools and equipment that are needed to perform these tasks, and describe the location of where needed equipment is kept or stored.

- An overall work schedule has not been presented, although individual time estimates for various operations have been provided.  In conjunction with the receiving schedules of chambers and parts to the ISR, and in conjunction with the most up to date delivery schedule of these items to SX5, a flow chart or plan depicting the anticipated work flow in ISR should be created and kept up to date as work progresses.  This work plan and activity flow chart should show the time required to carry out the particular jobs and should show the personnel required for all operations.

- The choice of pre-determining the particular chambers that are to have alignment hardware attached as presented to the reviewers appears to be inappropriate.  It is suggested that perhaps one out of five or six chambers evaluated should have the appropriate alignment hardware attached, and then when put back into a crate, the crate be appropriately marked to show that alignment hardware has been attached.  These crates should then be separately stored such that they can easily be identified and obtained when required for delivery to the SX5 personnel.

Follow-up Action Item:

The Review Team kindly asks Peter and Richard, on behalf of the ISR Team, for a written response to the above recommendations.  Your response should include the action to be taken for each numbered recommendation and the anticipated completion date.  We would like to have your response no later than the end of March, 2003.

Review Team:

Giorgio Apollinari			Andrey Korytov

Richard Breedon				Armando Lanaro

Nelson Chester (Leader)			Richard Loveless

Yuri Ivanov				Sergei Lusin

Chunhua Jiang				Guenakh Mitselmakher

Vladislav Razmyslovitch