| World Radiocommunication Conference (WRC-07) Geneva, 22 October - 16 November 2007 |  |
| --- | --- |
| PLENARY MEETING | Addendum 9 to Document 43-E |
|  | 3 September 2007 |
|  | Original: English |
| African Telecommunications Union Administrations |
| AFRICAN COMMON Proposals for the work of the Conference |
| Agenda item 1.15 |

1.15	to consider a secondary allocation to the amateur service in the frequency band 135.7-137.8 kHz

Introduction

The African administrations support a secondary allocation to the amateur service in the frequency band 135.7-137.8 kHz.

ARTICLE  5

Frequency allocations

Section IV  –  Table of Frequency Allocations
(See No. 2.1)

MOD	AFCP/43A9/1

110-255 kHz

| Allocation to services |
| --- |
| Region 1 | Region 2 | Region 3 |
| 130-135.7 FIXED MARITIME MOBILE 5.64 5.67 | 130-135.7 FIXED MARITIME MOBILE 5.64 | 130-135.7 FIXED MARITIME MOBILE RADIONAVIGATION 5.64 |
| 135.7-137.8 FIXED MARITIME MOBILE Amateur ADD 5.A15 5.64 5.67 | 135.7-137.8 FIXED MARITIME MOBILE Amateur ADD 5.A15 5.64 | 135.7-137.8 FIXED MARITIME MOBILE RADIONAVIGATION Amateur ADD 5.A15 5.64 |
| 137.8-148.5 FIXED MARITIME MOBILE 5.64 5.67 | 137.8-160 FIXED MARITIME MOBILE | 137.8-160 FIXED MARITIME MOBILE RADIONAVIGATION |
| ... | 5.64 | 5.64 |

ADD	AFCP/43A9/2

5.A15	Stations in the amateur service using frequencies in the band 135.7-137.8 kHz shall not exceed a maximum radiated power of 1 W (e.i.r.p.) and shall not cause harmful interference to stations of the radionavigation service operating in countries listed in No. 5.67.

Reasons:	ITU-R studies have shown that the radiation efficiency is typically less than 1% from practical antennas at typical amateur stations, resulting, in practice, in an e.i.r.p. of about 1 W. Reception over long paths has been demonstrated using receiving systems employing long integration times. A secondary allocation would provide opportunities for radio amateurs to contribute to the development of radiocommunication techniques and practices. Furthermore, no cases of interference to other services from amateur service operations in the frequency band 135.7-137.8 kHz have been reported.

______________