| World Radiocommunication Conference (WRC-07) Geneva, 22 October - 16 November 2007 |  |
| --- | --- |
| PLENARY MEETING | Addendum 15 to Document 41-E |
|  | 22 August 2007 |
|  | Original: English |
| Asia-Pacific Telecommunity Administrations |
| COMMON proposals for the work of the conference |
| Agenda item 1.15 |

1.15	to consider a secondary allocation to the amateur service in the frequency band 135.7-137.8 kHz

Introduction

Agenda item 1.15 is to consider a secondary allocation to the amateur service in the band 135.7-137.8 kHz. ITU-R studies have shown that the radiation efficiency is typically less than 1% from practical antennas at typical amateur stations, resulting in practice in an e.i.r.p. of about 1 W. Reception over long paths has been demonstrated using receiving systems employing long integration times.

Two methods to satisfy the agenda item have been identified. Method A is the addition of a new entry to the Table of Frequency Allocations. Method B is the “No Change” method.

Since 1997, radio amateurs in some countries in parts of all three Regions were granted authority to operate in the band. There have been no reports of interference to other radiocommunication services.

ARTICLE  5

Frequency allocations

Section IV  –  Table of Frequency Allocations
(See No. 2.1)

MOD 	ASP/41A15/301

110-255 kHz

| Allocation to services |
| --- |
| Region 1 | Region 2 | Region 3 |
| 130-135.7 FIXED MARITIME MOBILE 5.64 5.67 | 130-135.7 FIXED MARITIME MOBILE 5.64 | 130-135.7 FIXED MARITIME MOBILE RADIONAVIGATION 5.64 |
| 135.7-137.8 FIXED MARITIME MOBILE Amateur ADD 5.A115 5.64 5.67 | 135.7-137.8 FIXED MARITIME MOBILE Amateur ADD 5.A115 5.64 | 135.7-137.8 FIXED MARITIME MOBILE RADIONAVIGATION Amateur ADD 5.A115 5.64 |
| 137.8-148.5 FIXED MARITIME MOBILE 5.64 5.67 | 137.8-160 FIXED MARITIME MOBILE 5.64 | 137.8-160 FIXED MARITIME MOBILE RADIONAVIGATION 5.64 |

ADD	ASP/41A15/302

5.A115	Stations in the amateur service using frequencies in the band 135.7-137.8 kHz shall not exceed a maximum radiated power of 1 W (e.i.r.p.) and shall not cause harmful interference to stations of the radionavigation service operating in countries listed in No. 5.67.

Reasons:	A secondary allocation to the amateur service in the frequency band 135.7-137.8 kHz would harmonize on a worldwide basis the use of this band and satisfy the requirement of the amateur service for a very low frequency allocation.

_______________