Ce-136

Reviewed by T. Nakagawa, JAERI, January 2004

1. Files

ENDF/B-VI:	No data are given.

JENDL-3.3 and JENDL-3.2:

No data are given..

JEFF-3.0 and JEF-2.2:

No data are given.

CENDL-3:	Evaluation was made by Y.L.Han et al. in 2000.

BROND-2:	No data are given.

2. Thermal and resonance region

CENDL-3

No resonance parameters were given.

Cross sections below 100 keV were calculated with a formula of a+bE+C/sqrt(E).

Recommendation/conclusion for the thermal and resonance region

CENDL-3 is tentatively recommended. However, resonance parameters in the energy range from 66 to 876 eV were reported by Vertebny et al. [Ve70]  This set of parameters should be considered. Since the resonance parameters are ignored in CENDL-3, the capture resonance integral is much smaller than recommendation by Mughabghab [Mu81, Mu03].

3. Fast neutron region

(1) Methodology

CENDL-3

Theoretical calculation was performed using the NUNF code. The optical potential parameters were obtained by fitting to the total and non-elastic scattering cross sections and angular distributions of elastic scattering for natural Ce. Direct inelastic was calculated with DWUCK-4.

Emitted particle distributions are given in MF=6. Gamma-ray production data are also given.

(2) Total cross section (MT=1)

See Fig: http://www.nndc.bnl.gov/sg21/fp21/htm/Ce136.htm#mt1

(3) Capture cross section (MT=102)

See Fig: http://www.nndc.bnl.gov/sg21/fp21/htm/Ce136.htm#mt102

Maxwell averaged cross sections were measured by Käppeler et al. [Ka96] at kT=25 keV. Comparison of Maxwell averaged cross sections shows CENDL-3 is smaller than the measured data.

Average cross section (mb) at kT=25 keV

CENDL-3	278

Käppeler et al.	355(21

The shape around 4 MeV may be too large.

(4) Elastic scattering cross section (MT=2)

See Fig: http://www.nndc.bnl.gov/sg21/fp21/htm/Ce136.htm#mt2

(5) Inelastic scattering cross section (MT=4, 51 – 91)

See Fig: http://www.nndc.bnl.gov/sg21/fp21/htm/Ce136.htm#mt4

Discrete levels considered in the evaluations are as follows:

CENDL-3	6 levels up to 1.9785 MeV

The direct inelastic was calculated with DWUCK4 code.

The data of continuum inelastic scattering is zero between threshold (1.99 MeV) and 4.3 MeV. Therefore, the total inelastic has a dip around 4 MeV.

(6) (n,2n) reaction cross section (MT=16)

See Fig: http://www.nndc.bnl.gov/sg21/fp21/htm/Ce136.htm#mt16

Experimental data are reproduced well.

(7) (n,p) reaction cross section (MT=103)

See Fig: http://www.nndc.bnl.gov/sg21/fp21/htm/Ce136.htm#mt103

The resonance-like structure at 4 MeV seems to be strange.

(8) (n,) reaction cross section (MT=107)

See Fig: http://www.nndc.bnl.gov/sg21/fp21/htm/Ce136.htm#mt107

The resonance-like structure is seen at 4 MeV.

(9) Other reactions

The following reaction cross sections are given:

CENDL-3	(n,3n), (n,n), (n,np), (n,d), (n,t), (n,2p)

Recommendation/conclusion for the fast energy region

CENDL-3 is recommended.

References

[Br56]	Brosi A.R. and Ketelle B.H.: Phys. Rev., 103, 917 (1956).

[Ka96]	Käppeler et al.: Phy. Rev., C53, 1397 (1996).

[Ke63]	Keish B.: Phys. Rev., 129, 769 (1963).

[Mu81]	Mughabghab S.F. et al.: Neutron Cross Sections, Vol. 1, part A, Academic press (1981).

[Mu03]	Mughabghab S.F.: “Thermal Neutron Capture Cross Sections Resonance Integrals and g-Factors,” INDC(NDS)-440 (2002)

[Ve70]	Vertebny V.P. et al.: INDC(CCP)-15/U, p.49 (1970).

Table 1  Summary for Resolved and Unresolved Resonance Region: Ce-136

-----------------------------------------------------------------------------------------------------------------

Library	RRP	URP	Remarks

-----------------------------------------------------------------------------------------------------------------

CENDL-3	not given 	not given

-----------------------------------------------------------------------------------------------------------------

Table 2. Thermal Cross Sections and Resonance Integral: Ce-136

Units: barns

-----------------------------------------------------------------------------------------------------------------

Library/Experiment	Total	Elastic	Capture	Res.Integ.

-----------------------------------------------------------------------------------------------------------------

CENDL-3	12.50	5.25	7.25	6.96

Mughabghab et al. [Mu81]			7.3(1.5	58(12

Mughabghab et al. [Mu03]			6.5(1.0*	77(12

-----------------------------------------------------------------------------------------------------------------

*) to ground state.

Table 3. Thermal Capture Cross Sections: Ce-136

Units: barns

-----------------------------------------------------------------------------------------------------------------

Library/Experiment	ground	meta	ratio (M/G)	total

-----------------------------------------------------------------------------------------------------------------

CENDL-3				7.25

Mughabghab et al. [Mu81]	6.3(1.5	0.95(0.25	0.15	7.3(1.5

Mughabghab et al. [Mu03]	6.5(1.0

Brosi and Ketelle [Br56]	6.3		0.1	7.0

Keish [Ke63]			0.15(0.01

-----------------------------------------------------------------------------------------------------------------