POLAR Spacecraft Status As of: Tues June 14,  16:00 EST

(changes from last week in bold border)

| Subsystem/ Component | NOAA-12D AM: 1651=AN STIP data only | NOAA-14J AM: 2039=AN STIP data only | NOAA-15K AM: 1806=AN GAC data only | NOAA-16L PM: 1441=AN GAC&LAC data | NOAA-17M AM: 2225=AN GAC&LAC data | NOAA-N18 OV PM; 14:00=AN APT/HRPT/GAC |
| --- | --- | --- | --- | --- | --- | --- |
| LAUNCHED | 05/14/91 | 12/30/94 | 05/13/98 | 09/21/00 | 6/24/02 | 5/20/05 |
| CNTL OBP | OBP2 | OBP2 OBP1 inoperative | OBP2 | OBP2 | OBP2 | OBP2 |
| BUS | B-BUS XSU-1 | B-BUS XSU2 (XSU1 inop) | B-BUS XSU-1 | B-BUS XSU-1 XSU1 TOAR 444 | B-BUS XSU-1 | B-BUS XSU-1 |
| BUS VETO | NO | NO | NO | NO | NO | NO |
| ADACS X=Yaw Y=Roll Z=Pitch | Nominal Mode RGmode=Monitor Gyro chans=XYZ | Nominal Mode Rgmode=Disabled Gyro chans=XYZ SS check Disabled when mode=YGC | Nominal Mode Rgmode=Monitor Gyro-3 Off 6/26/00 Gyro chans=AAB N2 Low PSI invalid | Nominal Mode Rgmode=Monitor Gyro-3 Off 6/10/04 Gyro chans=AAA | Nominal Mode Rgmode=Monitor Gyro-3 Off 6/10/04 Gyro chans=AAB | Nominal Mode Gyro-A with MIMU Z-wheel -Pitch concerns |
| RXO | PRI BU random enables daily bias+6.5 mS | PRI BU random enables daily bias–7.0 mS | PRI daily bias -8 mS +100 mS 31Au04 | PRI Daily Bias –5.5 mS -100 mS 31Au04 | PRI Daily Bias –3 mS | PRI 23 May |
| CLOCK DIV | 2 | 2 | 2 | 2 | 2 | 2 |
| MIRP | External Synch Rephase Enabled | External Synch Rephase 0730 Daily | External Synch Rephase 0730 daily | External Sync Rephase each orbit | External Sync Rephase Enabled | External Synch Rephase Enabled |
| TIP SIDE | 1 | 1 | 2 (since 4/23/03) 3 Channels inop | 2 since 4/18/05 | 1 Analog telem drifting | 1 |
| DTRs | 3A, 4, 5B Safestate 5B | 1, 2B, 5 Safestate- 1B | 1, 2, 3, 4 Safestate 1B EOT | 1,2,3,4A Safestate 3A 4B STIP only | 1,2,3,4 Safestate=1B DTR2-SSR | 1,2,3,4,5 All solid state digital. Current spikes investigation |
| VTX (APT data) | #1 ON 137.50 MHZ | OFF Since 8/14/02 | #1 ON 137.50 MHZ | INOP OFF since 11/15/00 | #2 ON 137.62 MHZ | #2 ON 137.9125 MHZ |
| BTX | #1 136.77 MHZ | #2 137.77 MHZ | #1 137.35 MHZ | #1 OFF 137.35 MHZ | #2 ON 137.77 MHZ Corrected last week | #2 137.77 MHZ |
| STX #1=1698.0 mhz #2=1702.5 mhz #3=1707.0 mhz #4=2247.5 mhz | 1 – HRPT; 2,3 - Playback | 3 – HRPT 2, 1 – Playback | 2-Omni HRPT Power drop TOAR 446 4-Playback 1,2,3-Degraded | 1 – HRPT; 2– Playback; 4 – Playback 3 low power unused | 3 – HRPT TOAR424 low power 2 & 4 Playback 1-Standby STX-1 output power drop TOAR 443. | 1 - HRPT 2&3 Playback 4-Standby (AIP turned off 9 Jun |
| POWER (Array offset and CANT angle, charge & V/T rates, eclipse states and sun angle) | ArrayOff +50 since 8/31/04 Eclipse season 21Apr-17Aug Sun Angle 33 up to 37 mid-June Batts 1&2=LRC V/T=4 Shunt degraded SA CANT=37 degs | Array Off -55 Since 8/21/03 Eclipse all year Sun angle 50 up trend to 52 Batts 1-3= LRC Batts 1&3V/T=7/11 Batt2 VT=8/11 SS trigger =18.98 Shunt Degraded SA CANT=22 degs | Array Off -45 Since 1/25/01 Eclipse Season started 16 May Sun Angle 28, up- trend to 32 in June Batts 1-3= LRC V/T=7/9 SA CANT=37 degs | Array Off -40 Since 7/16/02 Eclipse all year Sun Angle 56 Steady trend Batts 1-3= LRC V/T=4/8 SA CANT=22 degs | Array Off. –40 Since 1/29/04 Eclipse all year Sun Angle at 71 Uptrend to 72 at the end of May Batts 1-3= LRC V/T= 4/8 SA CANT=37 degs | Array Off. -40 Since 6/6/05 Eclipse all year Batts 1-3=LRC Batts 1-3 V/T=4/8 SA CANT=22 PSSS enabled 30May |
| AVHRR | Nominal | INOP Scan motor stalled 14 Apr 04 | Nominal Rare major scan motor surges. Last Incident 11/18/04 | Operational TCE24 OFF 4/14/04 Elevated scan motor currents. Frequent Image Wave patterns and MIRP rephases Channel 3B only. | Nominal 3A-B switch enabled | Nominal All channels on Channel 3B only 3A-B switch disabled |
| AMSU-A1 |  |  | Operational Ch14 inoperative Ch11 inoperative | Operational Primary PLLO chans 9-14 bias shift. Backup PLLO inop. Channel 9-14 noise worsened recently | OFF/INOP Since 10/30/03 Survival heat on. | Nominal Space view 1 Since 6/7/05 |
| AMSU-A2 |  |  | Nominal | Nominal Space Position-2 | Nominal | Nominal Space view-2 since 6/08/05 |
| AMSU-B |  |  | Operational Bias in All Chans. Motor surges most recent 11/14/04 IPD Reports of degraded data on Chan-3 since 4/30 | Operational Space Position-3 IPD reports channel 8 degradation | Nominal | Replaced by MHS |
| HIRS | ON / INOP Turned on 8/30/04 For power balance Filter Wheel turned OFF 10/17/02. | NOMINAL Operational Occasional loss of Fwheel synch | INPROVED Upgraded to Yellow status 16 May 05 FW Abrupt return to nomial at 09:00Z TOAR 445 open FW mode=Hi Powr FW Heater OFF Frequent Filter | Operational High levels of imagery radiometric noise TOAR 441 open Occasional major FM surges, most recent 12/9/04 | NOMINAL 1 Pixel cross track misalignment . | ON Imagery noise in channels 1-12 under investigation |
| MHS/MIU |  |  |  |  |  | Nominal Final config on 6/4 Now Operational |
| MSU | ON / INOP On For power balance Scan Motor OFF since 3/12/03 | Operational Scan motor and antenna problems |  |  |  |  |
| SSU |  | Nominal |  |  |  |  |
| DCS | Nominal | Nominal | Nominal | Nominal | Nominal | ON All DRU’s on by 30 May DRU-8 commanded off 6/13 capability under investigation |
| SARR |  | Nominal | Operational A-Side, AGC Mode Intermittent failures for 243MHz A&B | Operational Switched back to mode AA 26Apr05 14:10Z A-side, AGC Mode (B-side in FG mode) 243 MHz = INOP. | Nominal A-side All AGC Mode | ON B-Side Since 23 May |
| SARP |  | OFF Power Failure | Nominal RCVR B/W = 2 | Nominal RCVR B/W = 2 | Nominal | ON A-side 23 May All DRU’s on |
| SEM | ON/Nominal Turned on 8/30/04 Elec-CH-HVPS=4 Prot-CH-HVPS=0 | Operational Elec-CH-HVPS=0 Prot-CH-HVPS=0 1 of 4 Tscopes inop | Nominal E-CDEM-HVPS=2 P-CDEM-HVPS=0 | Nominal E-CDEM-HVPS=5 P-CDEM-HVPS=4 | Nominal E-CDEM-HVPS=2 P-CDEM-HVPS=3 | ON Turned on 6 June at 14:05z |
| SBUV |  | Degraded Grate motor sticks Flex memory 3 (giant step) ops suspended 12/2/03 Reduced operations |  | Operational Degraded Ozone data Backup Diffuser inop Primary Diffuser deployment problem TOAR 426 AMSU EMI causing erratic Behavior in PMT cathod, range 3 | Nominal Anode Mode Plan sweep mode Standard Ops Procedure change starting 17 May | ON Turnon completed 27 May Flex memory discrepancies under investigation |
| SADPOS |  |  | N/A | ON Enabled MFactor50% Timer = 12 mins | ON ENABLED Timer = 12mins | ON Enabled |
| THERMAL Heaters, louvers TCE’s | Nominal TCE’s back to nominal configuration following 7/25/04 UVtrip. | Nominal | TCE26 & 15H Telem invalid TOAR 432 HIRS FW Heat tuned ON 17 Apr and OFF on 18 Apr TCE24L&25L (HIRS & AVHRR) failed 5/13/98 RCE thermostat failed 5/13/98 | Nominal TCE24 OFF 4/14 (AVHRR H&L) HIRS Filter heater turned OFF 1/18/05 | TCE3H Batt 2A heater failed ON, turned off 8/26/03 TOAR 428 CLOSED 9/14/04 no corrective action possible. AMSU-A1 survival heaters on 10/29/03 | All TCE’s active |
|  | N12 | N14 | N15 | N16 | N17 | N18 |

COMMENTS/CHANGES:

NOAA-12	As the spacecraft eclipse season approaches its maximum percentage darkness per orbit (expected on or about 20 June)

the battery voltage lows continue to fall on N12, yesterday reaching 19.6 volts.  With a PSSS battery voltage trigger levels on N12 at 18.7 V, EMOSS engineers are concerned that a transmitter inadvertently left on for an extended duration may draw the battery voltage down to this trigger point as it did in July of 2004.  To prevent such an occurrence, engineers have briefed the crews to considered transmitter turnoffs a high priority for N12 and are considering lowering the VT on each battery to 3 (from 4).  Carl Gliniak is EMOSS POC for this subsystem.

NOAA-14:	Spacecraft is operating nominally and power subsystem remains stable and above safe state threshold values as the

percentage darkness time per orbit has now peaked and should stabilize at or slightly below this 20% darkness per orbit value for the remainder of the year.   Otherwise there were no changes to N14 during the past reporting period.

Discussions are ongoing regarding the TBUS replacement of N14 with N18 no changes have yet been implemented.

NOAA-15:	The N15 AMSU’s were all generally stable and nominal during the past week (illustration 1) as was the N15 AVHRR and the HIRS (illustration 2).  N15 continues progressing nominally through its eclipse season (illustration 3) which will soon reach peak darkness per orbit (estimated to be 18 June). No power subsystem reconfigurations are expected.  There has been no change to the STX-2 situation on N15 which experienced a significant drop on 27 May.  The transmitter continues to transmit HRPT data at approximately 5.5 watts down from the previously nominal 7.5 watts.  EMOSS engineers have seen no indication of HRPT imagery degradation as a result of this event nor have any HRPT user complaints been received.

NOAA-16:	The N16 AMSU’s continue performing nominally, from an engineering perspective (illustration 4) although there have

been occasional reports received by EMOSS engineers of degraded products on some channels.  The N16 AVHRR scan motor current continued its slow increase into higher mean values for the eighth week in a row (illustration 5) with synch delta values “pegging out” on nearly every orbit (illustration 6).  Each orbit, over the South Pole, the MIRP rephases because of these high synch deltas thus losing a frame of data as it resets the value.  However, within half a rev, the value is again pegged and requiring reset.  EMOSS analysis of AVHRR imagery (illustration 7) shows the effects of this situation with nearly every GAC image containing a lost frame of data over the South Pole and nearly every HRPT image containing wave patterns.  On the positive side, this frequent rephasing of the MIRP may be the only reason why bar coded imagery has not become prevalent, yet, a situation that may change if the scan motor current trend continues this way much longer.

The N16 HIRS was stable and nominal last week (illustration 8) although some channels have been reported to be experiencing radiometric noise.

BTX-2 remained powered off because of a SOMS identified RF conflict.  EMOSS has requested that the Scheduling group look into the decision making aspect of the SOMS code to determine if this turnoff was correctly chosen.  Will Chadwick is EMOSS POC.

NOAA-17:	The N17 AMSU’s, AVHRR, and HIRS were nominal and stable during the past week (illustration 9 and 10).  There

were no changes to N17 in the past week.

NOAA-18:	Operational responsibility for N18 was passed to NOAA on 9 June at 12:00z with the OV period scheduled to continue

through 3 July 05.  Major operations that occurred on N18 between the previous report and this one are as follows:

6/7/05	23:55	AMSU-A1 to space view-1

6/8/05	01:35	AMSU-A2 to space view-2

6/8/05	13:40	SBUV range-3 to anode

6/8/05	20:25	HIRS scanner park at warm target

6/8/05	22:05	HIRS to full scan mode

6/9/05	12:00	Operational responsibility to NOAA

6/9/05	13:35	HIRS scanner park at space view

6/9/05	15:15	HIRS to full scan mode

6/9/05	20:00	STX-4 turnoff (AIP data)

6/13/05	17:40	DCS DRU-8 turnoff

6/13/05	19:15	SARP bandwidth profile changed from 1 to 2

6/13/05	19:20	SBUV flex memory-1 reload

6/14/05	19:05	SBUV flex memory-1, segment 2, memory test (load 0’s and f’s)

PLAN	6/15/05	12:30	SBUV Flex-2 memory load (with previous flex-1 load)

N18 (cont)

In general the spacecraft is operating nominally (see illustrations 11-19 for selected subsystem analysis graphs).  However, there are several problem areas that are under investigation, some or all of which may (or may not) result in TOARS being generated at a later date.  These areas are as follows:

Excess pitch values (relative to previous spacecraft) and Z-wheel currents (both of which are within spec but outside expected values).  On 7 June a software patch was uploaded that changed a threshold in the rate nulling algorithm.  Additional patches may be required pending the outcome of the investigation into this situation.

DCS DRU-8 inoperability.  DRU-8 was turned off pending additional analysis.

HIRS degraded imagery on channels 1-12.  Tiger teams have been meeting to analyze the situation and determine its cause and resolution.

DDR current spikes.  Not considered a serious problem and all DDR’s appear to be full functional.  However, this situation remains under investigation.

One other area of concern was the SBUV flex memory-1 which was not echoing back all the same words that were being loaded into it (especially segment-2).  A tiger team consisting of EMOSS, Aerospace, NASA and NOAA engineers investigated this situation, ran several tests and with the help of a NOAA DMSP engineer determined the cause to be a “clerical error” in an SBUV spreadsheet that defined the SBUV OV memory loads.  Corrections to the table are a simple matter but SOMS will also be required to have corrections made to it in order to complete the recovery of this situation.  However, the bottom line is that there is no anomaly in the SBUV as was first thought possible.   Jim Walters and Sally House were EMOSS members of this Tiger Team.

An additional attachment to the email that delivered this weekly report is an MS Excel spreadsheet that contains all commands sent to the N18 (but not 28) spacecraft as recorded by the Flight Time Table tool.  This spreadsheet summarizes all Manual, CP, SCT and Scheduled commanding (including NOOP’s) that took place between 20 May 11:48z and 11 June 02:45z.  It also includes the major operations that have occurred since 11 June 02:45 through today, 14 June 19:10z.  This file will allow the user to search and sort on any number of different combinations of data including subsystem, command type, site, rev, time, etc.   (Note the file is rather large, 5100 rows.)  Jeff Devine is EMOSS POC for generating and distributing this file.  It is the combination of all the EMOSS Command Engineer’s work that occurred during the OV period.

Illustration 1:  N15 AMSU’s Analysis:

(Nominal and stable)

Illustration 2:  N15 AVHRR & HIRS Analysis

(Nominal and stable.)

Illustration 3:  N15 Power Analysis

(Nominal and stable as max eclipse approaches.)

Illustration 4:  N16 AMSU’s Analysis

(Nominal, stable)

Illustration 5:  N16 AVHRR Analysis

(Scan motor current continues climbing toward bar code threshold)

Illustration 6:  N16 Synch Delta Analysis

(Very much bar coded imagery performance, without the bar codes, yet)

Illustration 7:  N16 AVHRR Imagery Analysis

(No apparent impact from this situation.)

Illustration 8:  N16 HIRS Health Analysis

(Stable and nominal.)

Illustration 9:  N17 AMSU’s Health Analysis

(Nominal and stable for the two remaining AMSU’s)

Illustration 10:  N17 AVHRR& HIRS Health Analysis

(Nominal and stable)

Illustration 11:  N18 AMSU Analysis

(Nominal and stable)

Illustration 12:  N18 AVHRR Health Analysis

(Nominal and stable)

Illustration 13:  N18 AVHRR Imagery Analysis (HRPT all channels) and Synch Delta Analysis

(Clear, stable and nominal)

Illustration 14:  N18 HIRS Payload Health Analysis

(Nominal and stable from an engineering perspective)

Illustration 15:  N18 HIRS Imagery Analysis.

(Note the various degraded channels)

Illustration 16:  N18 Power Analysis

(Nominal and stable)

Illustration 17:  N18 DDR Currents & STX Power

(DDR’s continue to spike, although less than the previous week.)

N18			vs.				N17

Illustration 18:  N18 Reaction wheel Comparison with N17

(Similar to previous week, still analyzing Z-wheel.)

N18			vs.				N16

Illustration 19:  N18 Gyro Comparison with N16

(Similar to previous week, still analyzing Z-wheel.)

# N17 MEMORY SCRUB REPORT

# Last week.

# POLAR SPACECRAFT TIP CLOCK ERROR

## WEEK ENDING June 10, 2005

| DAY/DATE | NOAA-12 | NOAA-14 | NOAA-15 | NOAA-16 | NOAA-17 | NOAA-18 |
| --- | --- | --- | --- | --- | --- | --- |
| FRI. 06/03 | -743 msec | +193 msec | -183 msec | +106 msec | +051 msec | -102 msec |
| SAT. 06/04 | -743 msec | +193 msec | -185 msec | +105 msec | +052 msec | -101 msec |
| SUN. 06/05 | -749 msec | +193 msec | -187 msec | +105 msec | +051 msec | -099 msec |
| MON. 06/06 | -747 msec | +199 msec | -187 msec | +106 msec | +053 msec | -098 msec |
| TUE. 06/07 | -747 msec | +196 msec | -187 msec | +106 msec | +054 msec | -097 msec |
| WED. 06/08 | -747 msec | +197 msec | -188 msec | +106 msec | +055 msec | -095 msec |
| THU. 06/09 | -748 msec | +200 msec | -189 msec | +110 msec | +056 msec | -094 msec |

EMOSS POC for this chart is JIM SHEPHERD

NOAA-14:  As of 12/23/03 the TIP clock is corrected daily by –7.0 msec to compensate for drift.

NOAA-15:  As of 04/22/03 the TIP clock is corrected daily by –8.0 msec to compensate for drift.

NOAA-16:  As of 12/23/03 the TIP clock is corrected daily by -5.5 msec to compensate for drift.

NOAA-17:  As of 12/23/03 the TIP clock is corrected daily by –3.0 msec to compensate for drift.

NOAA-12:  As of 12/10/03 the TIP clock is corrected daily by +6.5 msec to compensate for drift.

*    A clock jump of +500 milliseconds on 01/31/05 due to fractional second daily ETCUP. A clock

jump of +500 milliseconds on 04/17/05 due to fractional second daily ETCUP. Alternating +/-

500 millisecond clock jumps will ccur at 76-day intervals as long as fractional second daily

ETCUP is utilized to manage clock drift. The next +500 millisecond jump is expected on 07/02/05.

POES Engineering Contact List

Government

Renee Smith-Dearing  NOAA POES Constellation Lead 		301-817-4117

Dong Han:  NOAA, POES Payloads				301-817-4127

Micky Fitzmaurice:  NOAA, POES Bus, IJPS	 	    	301-817-4016

Nicolaie Todirita (Todi): NOAA Ground Systems			301-817-4229

EMOSS-2 Contractor

Jeff Devine: EMOSS POES Lead	 				301-817-4020

Jim Walters:  EMOSS, POES Payload Engineer			301-817-4033

Angelique Riley, EMOSS, POES Comm and DHS			301-817-4028

Carl Gliniak, EMOSS POES Power and Thermal 			301-817-4207

Jim Sheperd, EMOSS POES Attitude Control			301-817-4030

Jon Woodward EMOSS, POES Flight Software C&CS		301-817-4019

Sally House EMOSS POES Payloads 				301-817-4026

William Chadwick EMOSS, POES Comm and DHS			301-817-4015